DEVEXTRN.DOC


				     OS/8 
			       Device Extensions
				 Release Notes














                                  DISCLAIMER

                This document file was created by scanning  the
                original  document and then editing the scanned
                text.  As much as possible, the  original  text
                format  was restored.  Some format changes were
                made to insure this  document  would  print  on
                current laser printers using 60 lines per page.
                The  original  spelling  and  grammar  has been
                preserved.


                1-Nov-1996




						OS/8
					 Device Extensions
					   Release Notes

				       Order No. AA-H565A-TA


















				   ABSTRACT

	 This document describes features of the OS/8 Device Extensions
	 not discussed in the OS/8 Device Extensions User's Guide.


		  OPERATING SYSTEM AND VERSION:	     OS/8 V3D

















     ----------------------------------------------------------------------
     | To order additional copies of this document, contact the Software  |
     | Distribution  Center,  Digital  Equipment  Corporation,  Maynard,  |
     | Massachusetts 01754						  |
     ----------------------------------------------------------------------

	    digital equipment corporation -  maynard. massachusetts




					       First Printing, January 1979



     The information in this document is subject to change without notice
     and should not be construed as a commitment by Digital Equipment
     Corporation.  Digital Equipment Corporation assumes no responsibility
     for any errors that may appear in this document.

     The software described in this document is furnished under a license
     and may only be used or copied in accordance with the terms of such
     license.

     No responsibility is assumed for the use or reliability of software on
     equipment that is not supplied by DIGITAL or its affiliated companies.










	Copyright (c) 1979 by Digital Equipment Corporation









     The postage-prepaid READER'S COMMENTS form on the last page of this
     document requests the user's critical evaluation to assist us in pre
     paring future documentation.


     The following are trademarks of Digital Equipment Corporation:


	      DIGITAL		  DECsystem-10	      MASSBUS
	      DEC		  DECtape	      OMNIBUS
	      PDP		  DIBOL		      OS/8
	      DECUS		  EDUSYSTEM	      PHA
	      UNIBUS		  FLIP CHIP	      RSTS
	      COMPUTER LABS	  FOCAL		      RSX
	      COMTEX		  INDAC		      TYPESET-8
	      DDT		  LAB-8		      TYPESET-11
	      DECCOMM		  DECSYSTEM-20	      TMS-11
	      ASSIST-11		  RTS-8		      ITPS-10
	      VAX		  VMS		      SBI
	      DECnet		  IAS		      



				   CONTENTS



								     Page

     1.0     THE OS/8 DEVICE EXTENSIONS				     1
     2.0     THE RX02 DEVICE					     1
     2.1       RXCOPY						     2
     2.2       Using the RX02 with OS/78			     2
     2.3       RX02 Restrictions under OS/78			     3
     3.0     OS/8 SYSTEM PROGRAMS				     3
     3.1       RESORC						     3
     3.2       BUILD						     3
     3.3       PIP						     3
     3.4       BATCH						     4
     3.5       SET						     4
     4.0     THE VXA0 PSEUDO-DEVICE				     4
     5.0     OS/78 BASIC					     4
     6.0     USING OS/78 ON DECSTATIONS WITH VT100 TERMINALS	     4



				    TABLES


     Table 1   RX02 Device and Handler Information		     1





























				      iii

			 OS/8 EXTENSIONS RELEASE NOTES


     1.0  THE OS/8 DEVICE EXTENSIONS

     The OS/8 Device Extensions support the  following  new  devices  under
     OS/8:   the  KT8A memory management option (limited support), the RL01
     disk  and  controller,  and  the  RX02  double-density  diskette   and
     controller.  For a description of the modules in the Device Extensions
     package, see the OS/8 Device Extensions  User's  Guide  (AA-D319A-TA).		      _____________________________________
     These release notes describe features of the Device Extensions package
     not covered in the User's Guide.			____________

     This manual also  provides  information  on  the  use  of  the  Device
     Extensions under OS/78.



     2.0  THE RX02 DEVICE

     OS/8 software support for the RX02 device is  described  in  the  OS/8								       ____
     Device Extensions User's Guide.     ______________________________

     RX02 handlers are 2-page  handlers.   In  assembly-language  programs,
     make sure you have allowed for this.

     The RX02 handlers can be used only on PDP8/A/E/M omnibus  machines  or
     DECstations.

     Table 1 provides additional  information  on  the  RX02  diskette  and
     device handlers.


				    Table 1
		      RX02 Device and Handler Information

	 -------------------------------------------------------------
	 | Device  Entry   Group   Device  Device  Length   Length   |
	 |  Name   Point   Name     Type    Code   (Octal) (Decimal) |
	 |-----------------------------------------------------------|
	 |  SYS       7     RX8E    RX02     32	     1734     988    |
	 |  RXA0     32     RX02    RX02     32	     1734     988    |
	 |  RXA1     36     RX02    RX02     32	     1734     988    |
	 |-----------------------------------------------------------|
	 |  VT78 2nd Pair Only:					     |
	 |-----------------------------------------------------------|
	 |  RXA2     33     RX0B    RX02     32	     1734     988    |
	 |  RXA3     37     RX0B    RX02     32	     1734     988    |
	 -------------------------------------------------------------









				       1

			 OS/8 EXTENSIONS RELEASE NOTES


     2.1  RXCOPY

     The new version of RXCOPY will operate with  the  new  handlers  only.
     Although RXCOPY does its own I/O, it needs the handler entry points to
     sort out unit numbers.



     2.2  Using RX02 With OS/78

     To place OS/78 V2 on an RX02 double-density diskette for  use  as  the
     system device, use the following sequence of steps.

	  1.  Provide a backup copy of each diskette.

	      a.  Place the OS/8 Device Extension diskette in drive 0 and a
		  blank diskette in drive 1.

		       .DUPLIC RXA1:<RXA0:		       _

		  Label and use the backup copy.  Store the original.

	      b.  Place the OS/8 Device Extension diskette in drive 0.  Use
		  the DUPLICATE command /P option.

		       .DUPLIC RXA1:<RXA0:/P		       _

		  When the READY? message appears, place  OS/78  V2  system
		  diskette  #1 in drive 0 and a blank in drive 1.  Type YES
		  to copy the contents of OS/78 diskette #1 onto the  blank
		  diskette.    When   the  message  IS  MONITOR  REMOUNTED?
		  appears, reinsert the OS/8 Device Extensions diskette  in
		  drive 0 and type YES.

	      c.  Repeat step 2 with OS/78 system diskette #2.

	  2.  Update the OS/8 Device Extensions diskette.

	      a.  Place the OS/8 Device Extensions diskette in drive 0 and
		  the backup copy of OS/78 diskette #1 in drive 1.

	      b.  Run the DEVICE Extensions  batch  file  with  the  SUBMIT 
		  command and the /T option.

		       .SUBMIT OS78.BI/T		       _

	      c.  When the MOUNT message appears, remove OS/78 diskette  #1
		  from  drive  1  and  insert  OS/78 diskette #2.  Type any
		  character to continue.

	      d.  When the second  MOUNT  message  appears,  remove  system
		  diskette  2  and place a blank diskette in drive 1.  Type
		  any character to continue.


				       2

			 OS/8 EXTENSIONS RELEASE NOTES


	      e.  When control returns to  the  Monitor,  the  diskette  in
		  drive  1  is  your  working  copy  of  OS/78 V2 in double
		  density.  Label the diskette in drive 0 the OS/78  master
		  and store it in a safe place.



     2.3  RX02 Restrictions Under OS/78

	  o  The OS/78 Symbiont will not operate in double density.

	  o  If you are using some older OS/8 system programs under  OS/78,
	     they  may  not  operate properly.  The reason for this is that
	     they do not provide for a 2-page system handler.



     3.0  OS/8 SYSTEM PROGRAMS

     The following changes have been made in OS/8 system programs.



     3.1  RESORC

     The RESORC program is now written in MACREL with overlays. This  means
     that it must reside on SYS in order to run.



     3.2 BUILD

     The BUILD program has been modified to write to block  64,  which  has
     been reserved in previous versions.  It will also run now under BATCH.



     3.3  PIP

     If PIP finds a 0 in its device-type table (locations  136xx),  it  now
     assumes  that the device is a diskette and attempts to determine if it
     is single or double density.  Previously,  a  0  in  the  table  would
     simply  cause  PIP  to  return  with  the wrong length for the device.
     Users who write their own handlers must be sure any new device  length
     is  set  in  the  table, since unpredictable results will occur if the
     table is not completed.









				       3

			 OS/8 EXTENSIONS RELEASE NOTES


     3.4  BATCH

     BATCH requires the following patch to prevent wrong Monitor messages.

	  .GET SYS: BATCH
	  .ODT
	  1776/3215 3207
	  ^C
	  .SAVE SYS: BATCH



     3.5  SET

     The Device Extensions package includes a copy of the SET program  with
     a patch for 2-page handlers.  This patch is described in the April/May
     1978 issue of the DIGITAL SOFTWARE NEWS.



     4.0  THE VXA0 PSEUDO-DEVICE

     The pseudo-device VXA0 has been changed to  allow  systems  with  64K,
     96K,  or 128K words of memory to use it.  Each unit of 32K words above
     the   first   32K   is   considered   to   be   one    "platter"    of
     memory -- equivalent  to a platter on a device.  To expand the device,
     use the INSERT command in the BUILD program.  Specify  the  number  of
     "platters" you want to make available by typing

          INSERT VXA0 VXA0=n

     where

	  n=1	    indicates 32K words of memory (1  "platter")  available
		    to the VXA0 in a 64K system

	  n=2	    indicates 64K words available in a 96K system

	  n=3	    indicates 96K words available in a 128K system


     5.0  BASIC

     The BRTS.SV file in the Device Extensions package  is  an  update  for
     OS/8 V3D BASIC.  It is not compatible with the OS/78 commercial BASIC.



     6.0  USING OS/78 ON DECSTATIONS WITH VT100 TERMINALS

     Some DECstations are now being equipped with VT100  terminals.   OS/78
     supports normal scroll mode only at a maximum baud rate of 4800.



				       4

			 OS/8 EXTENSIONS RELEASE NOTES
							OS/8
							Device Extensions
							Release Notes
							AA-H565A-TA

			       READER'S COMMENTS


       NOTE:  This form is for document comments only.  DIGITAL will
	      use comments submitted on this form at the company's
	      discretion.  If you require a written reply and are
	      eligible to receive one under Software Performance
	      Report (SPR) service, submit your comments on an SPR
	      form.


    Did you find this manual understandable, usable, and well-organized?
    Please make suggestions for improvement.
    ______________________________________________________________________
    ______________________________________________________________________
    ______________________________________________________________________
    ______________________________________________________________________
    ______________________________________________________________________
    ______________________________________________________________________
    ______________________________________________________________________
    ______________________________________________________________________
    ______________________________________________________________________

    Did you find errors in this manual?  If so, specify the error and the
    page number.
    ______________________________________________________________________
    ______________________________________________________________________
    ______________________________________________________________________
    ______________________________________________________________________
    ______________________________________________________________________
    ______________________________________________________________________
    ______________________________________________________________________
    ______________________________________________________________________

    Please indicate the type of user/reader that you most nearly represent.

	 []  Assembly language programmer
	 []  Higher-level language programmer
	 []  Occasional programmer (experienced)
	 []  User with little programming experience
	 []  Student programmer
	 []  Other (please specify) _______________________________________


     Name______________________________________Date________________________

     Organization__________________________________________________________

     Street________________________________________________________________

     City__________________________State_____________Zip Code______________
							or
						     Country





















     -------------------------------Fold Here------------------------------

















     -----------------Do Not Tear - Fold Here and Staple-------------------

							  +---------------+
							  |  FIRST CLASS  |
							  | PERMlT NO. 33 |
							  | MAYNARD. MASS.|
							  +---------------+
	BUSINESS REPLY MAIL					   ========
	NO POSTAGE STAMP NECESSARY IF MAILED IN THE UNITED STATES  ========
     ======================================================================
	Postage will be paid by:				   ========
								   ========
			  +-+-+-+-+-+-+-+			   ========
			  |d|i|g|i|t|a|l|			   ========
			  +-+-+-+-+-+-+-+			   ========
								   ========
		      Software Communications			   ========
		      146 Main Street  ML5-5/E39		   ========
		      Maynard, Massachusetts  01754		   ========