HBUPDATE.DOC


				     OS/8
				Handbook Update
			  Order No. DEC-S8-OSHBA-A-DN4
















				  DISCLAIMER

		This document file was created by scanning  the
		original  document and then editing the scanned
		text.  As much as possible, the  original  text
		format  was restored.  Some format changes were
		made to insure this  document  would  print  on
		current laser printers using 60 lines per page.
		The  original  spelling  and  grammar  has been
		preserved.


		1-Dec-1996




						     OS/8
						Handbook Update
					 Order No. DEC-S8-OSHBA-A-DN4

















				   ABSTRACT


	    This document includes all previous corrections to the
	    OS/8 Handbook, and contains the documentation to	    _____________
	    support V3D of OS/8.







	  SUPERSESSION/UPDATE INFORMATION:   This manual updates the
					     OS/8 Handbook for V3D					     _____________
					     of OS/8.


	  OPERATING SYSTEM AND VERSION:	     OS/8 V3D









     ----------------------------------------------------------------------
     | To order additional copies of this document, contact the Software  |
     | Distribution Center, Digital Equipment Corporation, Maynard,	  |
     | Massachusetts 01754						  |
     ----------------------------------------------------------------------

	    digital equipment corporation - maynard. massachusetts





				     First Printing, October 1975
				     Revised:       December 1975
						   September 1977



     The information in this document is subject to change  without  notice
     and  should  not  be  construed as a commitment by Digital Equipment
     Corporation. Digital Equipment Corporation assumes  no  responsibility
     for any errors that may appear in this document.

     The software described in this document is furnished under  a  license
     and  may  be  used or copied only in accordance with the terms of such
     license.

     Digital Equipment Corporation assumes no responsibility for the use or
     reliability  of  its  software  on  equipment  that is not supplied by
     DIGITAL.








	Copyright (C) 1975,1977 by Digital Equipment Corporation








     The postage prepaid READER'S COMMENTS form on the last  page  of  this
     document  requests  the  user's  critical  evaluation  to assist us in
     preparing future documentation.


     The following are trademarks of Digital Equipment Corporation:



		DIGITAL		DECsystem-10	    MASSBUS
		DEC		DECtape		    OMNIBUS
		PDP		DIBOL		    OS/8
		DECUS		EDUSYSTEM	    PHA
		UNIBUS		FLIP CHIP	    RSTS
		COMPUTER LABS	FOCAL		    RSX
		COMTEX		INDAC		    TYPESET-8
		DDT		LAB-8		    TYPESET-10
		DECCOMM		DECSYSTEM-20	    TYPESET-11








				 INTRODUCTION



     This update is a collection of  changes  and  additions  to  the  OS/8								       ____
     Handbook  for use with Version 3D of OS/8. These changes and additions     ________
     are documented herein by Chapter as they appear in the handbook.  This
     update  also  includes  information  on  several  new  or revised OS/8
     utility programs.  These utility programs, included as  Appendixes  to
     the handbook, are:


			   RXCOPY   -    Appendix I
			   SET      -    Appendix J
			   FUTIL    -    Appendix K
			   DUMP	    -    Appendix L
			   RKLFMT   -    Appendix M



































				      iii




						 FRONT MATTER AND CHAPTER 1

						      ADDITIONS AND CHANGES



     Page			    Addition/Correction


     ii		In the second line from the bottom, change "Communications
		Services, Parker Street" to "Software Distribution Center".


     viii	In the first line of the second paragraph, change
		"impossible" to "possible".

		At the end of the second paragraph, add "OS/8 also runs on
		the VT-78."


     1-2	Step 1, change DEC-S8-OSYSB-A-UCI to AL4711C-BA


     1-4	Step 1, change DEC-S8-OSYSB-A-UC2 to AL4712C-BA


     1-5	Step 6, First line of example, change "form" to "from"

		Step 6, change DEC-S8-OSYSB-A-UCI to AL4711C-8A


     1-9	Step 1, change DEC-12-OSYSB-A-ACI to AL-3580C-BM


     1-10	Step 1, change DEC-S8-OSYSB-A-TC1 to AR4585C-BA


     1-15	Step 1, change DEC-S8-OSYSB-A-TC2 to AR4586C-BA

		Step 2, change DEC-S8-OSYSB-A-TC3 to AR4587C-BA


     1-16	Step 4, In the MCPIP: program line 5 is changed, lines 12
		and 13 are deleted, and three lines are appended. The
		complete program reads as follows:

		    *SYS:CCL.SV<CSA0:CCL.SV		    _
		    *SYS:DIRECT.SV<CSA0:DIRECT.SV		    _
		    *SYS:FOTP.SV<CSA0:FOTP.SV		    _
		    *SYS:PIP.SV<CSA0:PIP.SV		    _
		    *SYS:LIB8.RL<CSA0:LIB8.RL		    _
		    *SYS:EDIT.SV<CSA0:EDIT.SV		    _
		    *SYS:PAL8.SV<CSA0:PAL8.SV		    _


				       1



     Page			    Addition/Correction


     1-16 	    *SYS:CREF.SV<CSA0:CREF.SV		    _
     (cont.)	    *SYS:BITMAP.SV<CSA0:BITMAP.SV		    _
		    *SYS:BOOT.SV<CSA0:BOOT.SV		    _
		    *SYS:CAMP.SV<CSA0:CAMP.SV		    _
		    *SYS:FORT.SV<CSA1:FORT.SV		    _
		    *SYS:SABR.SV<CSA1:SABR.SV		    _
		    *SYS:LOADER.SV<CSA1:LOADER.SV		    _
		    *SYS:SRCCOM.SV<CSA1:SRCCOM.SV		    _
		    *SYS:EPIC.SV<CSA1:EPIC.SV		    _
		    *SYS:PIP10.SV<CSA1:PIP10.SV		    _
		    *SYS:RESORC.SV<CSA1:RESORC.SV		    _
		    *SYS:DTCOPY.SV <CSA1:DTCOPY.SV		    _
		    *SYS:TDCOPY.SV<CSA1:TDCOPY.SV		    _
		    *SYS:TDFRMT.SV<CSA1:TDFRMT.SV		    _
		    *SYS:DTFRMT.SV<CSA1:DTFRMT.SV		    _
		    *SYS:LIBSET.SV<CSA1:LIBSET.SV		    _
		    *SYS:RXCOPY.SV<CSA1:RXCOPY.SV		    _
		    *SYS:HELP.SV<CSA1:HELP.SV		    _

		Step 5, change the current Step 5 to Step 6 and insert the
		following as the new Step 5.

		To write SET.SV and HELP.HL files on the system device,
		mount AR4688C-BA in drive 0 and AR4689C-BA in drive 1. Type
		the following command line after the asterisk is printed on
		the terminal.

		    *SYS:SET.SV<CSA0:SET.SV		    _
		    *SYS:HELP.SV<CSA1:HELP.SV		    _

		By typing the command line:

		.R CCL		_

		you can run your programs by using CCL commands.

		Step 6, in the new Step 6 change DEC-S8-OSYSB-A-TC6 to
		AR4690C-B.


    1-17	Step 2, change (DEC-S8-OSYSB-A-PB1) to AK4678C-BA.


    1-19	Change the NOTE to read as follows:


					    NOTE

		    When building from the low-speed reader (KS33), after
		    entering PTR followed by carriage return the system
		    responds with an up-arrow;  the user must respond by
		    typing any character on the terminal and then

				       2



     Page			    Addition/Correction


     1-19	    immediately turn on the reader.  If the reader is not
     (cont.)	    turned on promptly, the system hangs.  Remember to turn
		    off the reader when it reaches the leader/trailer at
		    the end of the tape.

		Step 6, change (DEC-S8-OSYSB-A-PB4) to AK4679C-BA.

		Step 7, change (DECS8-OSYSB-PB5) to AK4680C-BA


     1-20	Step 9, change ABSLDR to EPIC

		Delete the entire section "Loading System Programs from
		Paper Tape" pages 1-20 through 1-25, and replace with the
		following:

		Loading Paper Tape Binary Kit

		Paper tape binary kits for OS/8 V3D are punched using EPIC.
		This use of EPIC simplifies loading these tapes onto SYS:
		All tapes, except those used to build a Monitor and a Sys-
		tem Head and EPIC itself, must be loaded onto SYS: using
		EPIC. The procedure for loading paper tape binary kits is
		described below.

						  NOTE
			Skip Step 1 if EPIC.SV exists in system directory.

		1. Place the EPIC binary tape (AK4667C-BA) in the reader
		and type:

		    .R ABSLDR (CR)		    _
		    *PTR:($)^		    _	    _

		Turn on reader and type any key on keyboard.

						NOTE
			(CR) is carriage return (press RETURN key). ($) is
			escape or altmode, strike ESC key.

		EPIC will be read in by this procedure. If necessary, turn
		off the reader. Save EPIC as a file by typing:

		    .SAVE SYS:EPIC.SV(CR)		    _

		2. Type .R EPIC(CR)			_

		3. To load any paper tape onto SYS:, put the paper tape for
		that file in the reader and type:

		    *SYS:</0/Y($) for the high speed reader or		    _
		    *SYS:</0/Y/L($) for the low speed reader. (Turn on the		    _

				       3



     Page			    Addition/Correction


     1-20		low speed reader, depress CONT on the operator's
     (cont.)		console after the computer halts to allow loading
			the tape in the reader. After the tape has read in,
			the computer halts again. If there are no more
			tapes to that file to be loaded, turn off the reader
			and depress CONT. If these are more tapes to the
			file continue to Step 4.


		4. If the file being created requires more than one tape to
		be input, the message:

		    END OF TAPE ENTER NEXT		    ______________________

		will be displayed on the console terminal and the computer
		will halt with 7777(8) in the AC. Place the next tape of
		the file in the reader, turn it on, and depress CONT.
		Repeat Step 4 until all tapes for the file are loaded.

		If the tapes of a multiple tape file are read out of
		sequence an error message:

		    NEED nnnn FOUND mmmm		    ____________________

		will be output on the console terminal. Check the tapes of
		the file and place the proper tape in the reader, and
		depress CONT on the operators console.

		5. Repeat Steps 3 and 4 to load each tape or set of tapes
		into a file on SYS:

		More information on EPIC can be found in Chapter 2 of the
		OS/8 Handbook (DEC-S8-OSHBA-A-D).

		6. If desired, you can load CCL.SV, EDIT.SV, and BATCH.SV
		(if you have the OS/8 Extension Kit) and then create a
		batch stream to load the desired files onto SYS:

		Create a batch file as follows:

		    .CREATE LOAD.BI(CR)		    _
		    #A(CR)		    _
		    $JOB TO LOAD FILES USING EPIC(CR)
		    .R EPIC(CR)

		    *SYS:</0/Y$(CR)	$=dollar sign key (shift/4) - not
		    *SYS:</0/Y$(CR)	escape or altmode. Add/L before $
					(see example in Step 3 above) if
					reading from low speed reader.
		    *SYS:</0/Y$(CR)	Put in a few of the load commands;
		    .SU LOAD.BI/T(CR)	the more you put in, the fewer
					times the job will re-submit itself.

				       4



     Page			    Addition/Correction


     1-20	    (CTRL/FORM)		(CTRL/FORM) means hold down
     (cont.)	    #E(CR)		CTRL key, depress "L" (FORM) key		    _

		Then run it, using the command:

		    .SU LOAD.BI/T(CR)		    _

		Every time the computer stops, replace the tape in the
		reader with a new one (or next in sequence) and depress
		CONT. Ignore any

		    L/T ERROR		    _________

		messages on console terminal due to running off the end of
		the paper tape.


     1-29	Insert the following table before the section entitled
		"Restarting OS/8":

			Table 1-11A RX01 Floppy Disk Bootstrap

		-----------------------------------------------------------
		Step Octal	Switch Register
		# Values	Setting	And Then
		-----------------------------------------------------------
				012	345	678	91011
		1   0000	000	000	000	000	press EXTD
								 ADDR LOAD
		2   0024	000	000	010	100	press ADDR
								 LOAD
		3   7126	111	001	010	110	lift DEP key
		4   1060	001	000	110	000	lift DEP key
		5   6751	110	111	101	001	lift DEP key
		6   7201	111	010	000	001	lift DEP key
		7   4053	100	000	101	011	lift DEP key
		8   4053	100	000	101	011	lift DEP key
		9   7104	111	001	000	100	lift DEP key
		10  6755	110	111	101	101	lift DEP key
		11  5054	101	000	101	100	lift DEP key
		12  6754	110	111	101	100	lift DEP key
		13  7450	111	100	101	000	lift DEP key
		14  7610	111	110	001	000	lift DEP key
		15  5046	101	000	100	110	lift DEP key
		16  1060	001	000	110	000	lift DEP key
		17  7041	111	000	100	001	lift DEP key
		18  1061	001	000	110	001	lift DEP key
		19  3060	011	000	110	000	lift DEP key
		20  5024	101	000	010	100	lift DEP key
		21  6751	110	111	101	001	lift DEP key
		22  4053	100	000	101	011	lift DEP key
		23  3002	011	000	000	010	lift DEP key

				       5



     Page			    Addition/Correction


     1-29	24  2050	010	000	101	000	lift DEP key
     (cont.)	25  5047	101	000	100	111	lift DEP key
		26  0000	000	000	000	000	lift DEP key
		27  6753	110	111	101	011	lift DEP key
		28  5033	101	000	011	011	lift DEP key
		29  6752	110	111	101	010	lift DEP key
		30  5453	101	100	101	011	lift DEP key
		31  7024	111	000	010	100	lift DEP key
		32  6030	110	000	011	000	lift DEP key
		33  0033	000	000	011	011	press ADDR
								LOAD and
								press CLEAR
								and press
								CONT


     1-31	Add the following to Table 1-12 Permanent Device Names:

		RXAn	Diskette n (floppy), where n is an integer in the
			range of 0-7 inclusive.

		RKBn	DECpack n, where n is an integer in the range 0-1.

		NULL	On input this returns an immediate end-of-file; on
			output this device ignores characters.

		DUMP	Prints contents of device blocks on LPT


     1-32	Add the following to Table 1-13 Assumed Extensions:

						NOTE
		    Refer to Appendix F for a complete list of commonly used
		    extensions.


     1-37	Under the GET Command, add the following insert before the
		last sentence in that paragraph.

		In addition, location 7747 in field 0 is loaded with the
		block number of the first block of the core image file
		(.SV) specified.

		Under the "JOB STATUS WORD," delete "Bits 4-9 Unused and
		reserved for future expansion" and add the following:

		Bit 4=1 A core image file that was generated by LINK
		containing overlays.

		Bit 5=1 This program cannot be run by the R, RUN, or GET
		commands under OS/78.


				       6



     Page			    Addition/Correction


     1-37	Bit 6-9 Unused and reserved for future expansion.
     (cont.)

     1-41	Replace this page with:

		RUN Command
		    The RUN command is of the form:

			.RUN dev file.ex
		    or
			.RU dev file.ex

		The RUN command, like the SAVE command, handles only core-
		image files. The file indicated (file.ex) on the device
		specified (dev) is loaded into core and its core control
		block is moved to the system scratch area. The program is
		started at its starting address. Location 7747 in field 0
		is loaded with the block member of the first block of the
		core image file (.SV).

		The RUN command is equivalent to a GET and a START command.

		If an extension to the file is not specified, the extension
		.SV is automatically added to the file name. For example:

		    .RU DTA1:PROG		    _

		causes the file PROG.SV on DECtape 1 to be loaded and started.

		R Command
		    The R Command is of the form:

				.R file.ex				_
		and is similar to
				.RUN SYS file.ex				_

		This command handles only core image files from the system
		device. The file is loaded and started and location 7747 is
		loaded with the block member of the first block of the core
		image file (.SV). If the file name extension is not
		specified, the extension .SV is automatically added.

		The R command differs from the RUN command in that a core
		control block is not written to the system device. In order
		to save a program which does not have its core control
		block in the usual location on the system device, all the
		optional arguments of the SAVE command must be explicitly
		stated. System programs are most often called using the R
		command, since they need not be resaved.

		To call a program which is to be later updated and saved,
		use of the RUN or GET commands is suggested.

				       7



     Page			    Addition/Correction


     1-41	START Command
     (cont.)	    The START command is of the form:


     1-52	Middle of the page, remove the paragraph that begins "The
		user may write his own CCL commands..." and insert:

		Sophisticated users who wish to add their own CCL commands
		should refer to the OS/8 V3 source listing of
		CCL(DEC-S8-OSYSB-A-LA18).


     1-53	After BACKSPace add
		BASIC
		Delete CORE
		After DIRect add
		DUPlicate
		After MAP add
		MEMory
		Delete RES and replace with
		RESource


     1-55	In Table 1-16 add options

		   -N	NULL
		   -D   DUMP


     1-56	Add the following as the last paragraph under the section
		entitled "INDIRECT COMMANDS":

		A single quote is permitted after file specification; if
		used, it is ignored. A single quote prevents the next
		letter from being considered part of the indirect command
		file name.


     1-57	In the third paragraph, change "64" to "40". In the example
		above the paragraph, change "0102036404000506" to
		"0102034004000506".


     1-58	Before the title "BOOT Command", insert the following:

		BASIC COMMAND
		The BASIC command requests execution of the BASIC editor.

		Format:

		.BASIC


				       8



     Page			    Addition/Correction


     1-58	Example:
     (cont.)
		    .BASIC		    _
		    NEW OR OLD--		    ____________

		For additional information on BASIC, refer to Chapter 6.

		This command runs CCL.SV and BASIC.SV.


     1-59	Add the following to the section entitled "COMPILE Command",
		after ".COM file.ex<file.ex":

		or
		.COM A,B<C,D
		for multiple Input/Output files.

		The COMPILE command produces similar results when chaining
		and specifying either the /T option or the /T/F options.
		For example, both of the following commands produce a RALF
		symbol table only:

		    .COM LPT FL1/T/G		    _
		    .COM LPT FL1/T/F/G		    _


     1-61,62	Delete the CORE command and its description.


     1-64	Before the EDIT command, insert the following:

		DUPLICATE COMMAND
		The DUPLICATE command copies or transfers the entire
		contents of one diskette to another diskette.

		Format:

		    .DUPLICATE outdev:<indev:/options

		In addition to the necessary arguments in the command line,
		DUPLICATE options can be used to affect the DUPLICATE
		operation.

		Example:

		    .DUPLICATE RXA1:<RXA0:		    _

		The contents of input device RXA0 is copied onto output
		device RXA1.

		Changing Devices Before and After Executing the DUPLICATE
		Command - You can only duplicate from RXA0 to RXA1 or RXA1

				       9



     Page			    Addition/Correction


     1-64	to RXA0. Driver RXA2 and RXA3 is not supported by the
     (cont.)	DUPLICATE command. Since the Monitor resides on the system
		device, the system device must remain an line when
		interacting with the Monitor and any OS/78 system programs.

		If you want to transfer the contents of a diskette
		containing only files (one that does not contain a system),
		use the /P option. The /P option pauses before and after its
		execution of the DUPLICATE command. A ready message followed
		by a question mark is displayed. This pause provides time to
		remove the system device and mount a device onto which the
		contents are to be transferred, to or from. To start the
		DUPLICATE operation, type a Y after the question mark and
		press the RETURN key. After the DUPLICATE operation is
		completed, a message is displayed asking if the Monitor is
		remounted. The second pause provides time to remove the new
		device and remount the system device so control can return
		to the Monitor. After remounting the system device, type a
		Y after the question mark and press the RETURN key, to
		return control to the Monitor.

		Example:

		    .DU RXA0:<RXA1:/P		    _
		    READY?Y		    ______
		    IS MONITOR REMOUNTED?Y		    _____________________
		    .		    _

		Performing a Read Check
		To check the integrity of a diskette, use the /R option and
		specify only the input device. By specifying the /R option,
		every block of the specified device is read and checked for
		bad sectors. If bad sectors exist, a message with the
		device, track number and sector number is displayed. If
		none exist, control returns to the Monitor.

		Example:

		    .DU <RXA1:/R		    _
		    INPUT DEV READ ERROR TRACK:nn SEC:nn		    ____________________________________

		Transfer Without Checking for Identical Contents
		To transfer the contents of one device to another without
		performing any checks, use the /N option. By specifying the
		/N option, the contents of the input device is transferred
		or copied to the output device. If /N is not specified and
		the DUPLICATE operation is completed, the contents of the
		output device is compared to that of the input device to
		assure accuracy.

		Check for Identical Contents Without Transferring
		To check the contents of devices to see if they are

				      10



     Page			    Addition/Correction


     1-64	identical without transferring, use the /M option. By
     (cont.)	specifying the /M option the contents of both devices are
		read and checked for a match. If they do match, control
		returns to the Monitor. However, if they differ in any way,
		a message, the device-name, the track number, and the
		sector number of the sectors or blocks that do not match
		are displayed.

		Example:

		    .DU RXA1:<RXA0:/M		    _
		    COMPARE ERROR TRACK nn SECTOR nn		    ________________________________

		This command causes the execution of both the CCL.SV and
		the RXCOPY.SV programs.


     1-65	Add the following to the section entitled "EXECUTE Command",
		after ".EXE file.ex,file.ex":

		or
		.EXE A<B
		to execute file "B" producing file "A".


     1-66	Delete the HELP command description and insert:

		HELP Command
		The HELP command sends information on OS/8 programs to the
		output device, usually the terminal. There is a HELP
		program (HELP.SV) that is executed every time the HELP
		command is used. There is also a HELP file (HELP.HL) that
		contains a list of all the HELP subfiles available and the
		actual HELP text itself. Both the HELP.SV and HELP.HL
		files must be on the system device.

		Format:

		    .HELP outdev:file.ex<argument

		where:

		    argument is usually an OS/8 program or CCL command.

		Example:

		    .HELP RXCOPY or .HELP DUPLICATE		    _		    _

		Note that the default output device is TTY.

		The OS/8 software for the HELP files can be supplied on any


				      11



     Page			    Addition/Correction


     1-66	device. Following is a list of all the arguments that can
     (cont.)	be used with the HELP command.

		ABSLDR	      BASIC	   BCOMP	BRTS	    BOOT
		BUILD	      "NONE"	   CCL		CREF	    DIRECT
		EDIT	      CREATE	   EPIC		FORT	    FRTS
		F4	      FORTRAN	   F4ERR	LIBRA	    LOAD
		LOADER	      MAP	   BITMAP	ODT	    PAL8
		PAL	      PALERR	   PIP		PIP10	    DUPLIC
		RXCOPY	      SABR	   SET		SRCCOM	    COMPAR
		BATCH	      SUBMIT	   TECO		MAKE	    MUNG
		FOTP	      LIST	   COPY		RENAME	    TYPE
		DELETE	      ASSIGN	   DATE		DEASSIG	    GET
		MEMORY	      R		   RUN		SAVE	    START
		SQUISH	      UA	   ZERO

		There is a HELP file which contains all CCL commands. This
		file is displayed by typing the HELP command without any
		arguments as follows:

		    .HELP		    _

		If a HELP file for a specific command is desired, type the
		name of the command for which the information is desired.
		For example,

		    .HELP PAL		    _

		To obtain a list of all legal arguments for HELP, type the
		HELP command followed by an asterisk or type the HELP
		command followed by 'HELP' as follows:

		    .HELP *
		or
		    .HELP HELP

		Note that the HELP.HL file must be on the system device.


     1-68	Both examples of the MAKE Command should specify "MAK" not
		"MA". Also, change "%SUPERCEDING" to "%SUPERSEDING".


     1-70	In the first line of the MUNG command example, change "HX!"
		to "HX1!".

		Before the PAL Command insert the following:

		MEMORY COMMAND
		The MEMORY command is used to find the highest field
		available in hardware or to limit that value in software.


				      12



     Page			    Addition/Correction


     1-70	Format:
     (cont.)
		    .MEMORY n or .MEMORY

		where:

		    n	is an octal number representing the number of
			fields (4K) available to OS/8. It is in the range
			of 0-7.

		Example:

		    .MEMORY 3		    _
	
		    16K MEMORY		    __________

		The following table lists the values of n and their meanings.

		    n	memory

		    O	all available memory
		    1	8K
		    2	12K
		    3	16K
		    4	20K
		    5	24K
		    6	28K
		    7	32K


		To find the amount of memory actually being used by OS/8,
		type the command with no argument.

		    .MEMORY		    _

		    20K/32K MEMORY		    ______________

		In this example, a 32K system has been restricted to only
		20K of available memory. This was done by using a MEMORY 4
		command.

		If all available memory is being used, the total amount of
		memory is printed.

		Example:

		    .MEMORY		    _

		    32K MEMORY		    __________

		This command causes the execution of the CCL.SV program.


				      13



     Page			    Addition/Correction


     1-74	Add the following note to the end of the section "UA, UB,
		UC Commands":

		"The CCL commands UA, UB, and UC are used to remember and
		recall arguments. These arguments are not deleted when the
		system date is changed. Most other CCL commands do not
		remember commands typed at sessions on previous days."


     1-77	In "Table 1-18 CCL Error Messages (Cont.)", change
		"%SUPERCEDING" to "%SUPERSEDING".


     1-79	Delete the /A option from Table 1-19.


     1-81	In Table 1-21, insert a dot (.) in the lefthand column
		("Character") of the first line.


     1-99	In the second paragraph under the /I option, change "-n" to
		"=n". The missing example should be:

		    *IMPORT.PA[23]</I=27

		Delete /L option and its description.


     1-102	Add the following NOTE to the end of Table 1-24:

		"PIP does not ask the question ZERO SYS for a handler that
		is co-resident with the SYS: handler.  For example, if both
		SYS: and LTA0 are LINCtape 0, a request to zero LINCtape 0
		will not produce the question.  This is a potentially
		dangerous command."


     1-120	In the last line of the first paragraph, change "0007" to
		"0006".


     1-122	In Table 1-28, insert a slash (/) in the lefthand column
		opposite the last line.










				      14





								  CHAPTER 2

						      ADDITIONS AND CHANGES



     Page			    Addition/Correction


     2-3	In Table 2-1 Run Time Options, append the following:

                /H  Process the batch input file without echoing and without
		    sending the $JOB and $END batch monitor commands to both
		    the terminal and batch log.


     2-34	In the first paragraph of the section entitled "OS/8 Device
		Handlers", change "Appendix H" to "Appendix G".


     2-36	At the top of the page, change (DEC-S8-OSYSB-A-UC2) to:

                AL-4712C-BA

                After Table 2-7 change (DEC-S8-OSYSB-A-TC4) to:

                AR-4588C-BA


     2-37	After Table 2-8 change (DEC-S8-OSYSB-A-PB2) to:

                AK-4660C-BA and (DEC-S8-OSYSB-A-PB3) to:

                AK-4671C-BA


     2-38	In Table 2-9 after the entry "DF32 disk nonsystem handler"
		add:

                RX01SY disk system handler      RX8E  SYS        RX01SY.BN
                RX01NS disk nonsystem handler   RX01  RXA0,RXA1  RX01NS.BN
                VT50 VT-50 input handler        VT50  LST        VT50.BN
                LQP line printer handler        LQP   LPT        LQP.BN
                Octable block DUMP handler      DUMP  DUMP       DUMP.BN
                RX78B disk nonsystem            RX01  RXA2,RXA3  RX78B.BN
                handler (for VT-78 only)


     2-47	The last example on the page should be:

                    $UNLOAD TC:DTA3



				      15



     Page			    Addition/Correction


     2-48	The first example on the page should be:

		    $UNLOAD TC:DTA0,DTA2


     2-52	After the section entitled "VERSION" add:

		SIZE

		Syntax:$SIZE aname or $ SIZE aname=new value

		aname must be the permanent name of a device currently
		marked as active.

		Example: $SIZE RF08=1777

		changes the length of the RF08 handler to 1777.

		Function: The SIZE command modifies word ten of a handler
		header block. Word ten specifies the size, in blocks, of a
		single platter on a system device.


     2-56	In Table 2-11 after "?PLAT", add:

		?SLOTS	This error indicates you have inserted more than 8
			groups of non-system handlers. Each slot may have
			more than one entry point. To correct, delete
			PNAMES until there are 8 or less non-system
			handlers.


     2-60	In Table 2-12 at the top of the page, change "25-26=unused"
		to 25=RX01 disk; 26=unused.

		Change "31-37=unused by Digital" to:

		31-35 Unused by Digital

		36 Dump Handler

		37 Unused by Digital

		In the section "ENTRY POINT OFFSET", change all occurrences
		of "7-23" to "7-24". In the list of devices, change "RK8
		disk" to "RK8/RK8E disk", and add the following:

		    "RF/DF disk       24"
		    RXA0	      30
		    RXA1	      34



				      16



     Page			    Addition/Correction


     2-60	Also, change "Thus, the user-coded file ...." to "Thus, the
     (cont.)	user-coded file devices should use entry points other than
		7-24,30,34.


     2-61	Add the following information:

		CREATING A SYSTEM HANDLER

		When creating a new system handler, the user must obey the
		following restrictions:

		    (a) The length of a bootstrap must be greater than or
			equal to 21 (octal) locations. A bootstrap shorter
			than 21 locations must be padded, otherwise BUILD
			results are unpredictable.
		    (b) The length of the bootstrap must be less than or
			equal to 177 (octal) locations.
		    (c) If the system handler is a one-page handler, only
			the first 47 (octal) locations of the bootstrap are
			significant. The remaining locations are ignored
			and not written on the system device. Also, no
			handler may have more than 20 (octal) entry points.
		    (d) If a system handler is 2 pages long, relative
			location 12 of the first page must contain a 3. The
			second page loads into location 27600 and is stored
			on block 66 of SYS:


     2-69	Add the following to the NOTE: RALF is not fully supported
		by CREF.


     2-70	In Table 2-14 (CREF Options), change the /E option to /A.


     2-77	After the last paragraph on this page, add the following:


						NOTE
			   If you want the date printed in your directory
			   listings, it must be entered into the system
			   prior to the DIRECT command.


     2-97	Add the following examples to the "FILE ORIENTED TRANSFER
		PROGRAM (FOTP)". These examples will help give the user a
		better understanding of the program.

		Transfer the file X.Y from disk to DECtape:



				      17



     Page			    Addition/Correction


     2-97		*DTA0:<X.Y
     (cont.)
		Transfer the files A, B, C, D and E from SYS: to DTA3:

			*DTA3:<SYS:A,B,C,D,E

		Transfer all FORTRAN source files from one DECtape to
		another, producing a log of those copied:

			*DTA2:<DTA5:*.FT/L

		List all FORTRAN and BASIC files on the line printer in
		order of appearance on DSK:

			*LPT:<*.FT,*.BA

		List all FORTRAN and BASIC files on the line printer
		listing all FORTRAN files before all BASIC files:

			*LPT:<*.FT,*.BA/U

		Copy all files other than .SV and .BN files from DTA3: to
		DSK: then copy all files other than those whose name begins
		with a K from DTA2: to DSK:. Log all files copied:
	
			*DSK:<DTA3:*.SV,*.BN,DTA2:K?????.*/V/L

		Copy the file A.B from DSK: to DTA1: changing its name to
		C.D. Give the new file today's data:

			*DTA1:C.D<A.B/T

		Copy all files from LTA2: which have the extension .PA to
		SYS: changing the extension to .PL allocating storage on
		SYS: without doing pre-deletions:

			*SYS:*.PL<LTA2:*.PA/N

		Find all files on RKA2: with the name FOO and any extension
		but which have today's date, and copy them to SYS:
		changing the file name to WXYZ yet keeping the extension:

			*SYS:WXYZ.*<RKA2:FOO.*/C

		Delete all disk files (except those with today's date)
		which either have the extension .LS, .TM, or .BK and those
		whose file name begins with TMP:

			*DSK:<*.LS,*.TM,*.BK,TMP???.*/D/O

		Delete each .BN file for which there is a corresponding .PA
		file:

				      18



     Page			    Addition/Correction


     2-97		**.BN<*.PA/D
     (cont.)
		Delete all .LS files on DTA3: for which there is a file on
		RKA0: with the same name but an extension of either .PA,
		.RA, or no extension:

			*DTA3:*.LS<RKA0:*.PA,*.RA,*/D

		Delete all files on the disk for which there are already
		copies on one of the four DECtape drives:

			*DSK:<DTA0:*.*,DTA1:*.*,DTA2:*.*,DTA3:*.*/D

		Produce a log of all files on DTA1: that have the file name
		FOO and an extension which is the same as any file on SYS:
		that has a one or two-character file name beginning with a
		"T". Do not perform any transfers or deletions:

			*DTA1:FOO.*<SYS:T?.*/N/D/L

		Change the name of the file DSK:FILE.PA to FILE2.PA:

			*FILE2.PA<FILE.PA/R

		Rename all files on DTA6: with a .PA extension to have a
		.PB extension:

			*DTA6:*.PB<DTA6:*.PA/R

		Change the extension from .RL to .OL of all files on DTA1:
		that correspond to files on DSK: with the same name and
		today's date:

			*DTA1:*.OL<*.RL/C/R


     2-106	In "Table 2-20 FOTP Options (Cont.)", add to the "/R"
		option:

		     (a) The rename option (/R) now looks at the /T switch.
			 If /T is typed then not only is the file renamed,
			 but the new file receives today's date. Without /T,
			 the new name has the same date as the old name.
		     (b) The rename option (/R) now allows you to rename a
			 file to its own name. This was not previously
			 permitted. It is not very useful unless some other
			 switch is included, for example /T.
		     (c) If no output file is specified with /R, then FOTP
			 assumes the same name as the first input file.

		Example: To redate all files on a DECtape to Jan. 1, 1976:


				      19



     Page			    Addition/Correction


     2-106	    .DATE 1/1/76		    _
     (cont.)	    .RENAME DTA0:*.*/T		    _


     2-113	Add the following options to Table 2-22:

		/I   Assume the input device is a cassette drive. An input
		     device must also be specified on the command decoder
		     line, but it is ignored. This option is used when
		     there are no cassette handlers configured into your
		     system. The drive number is specified as an option,
		     e.g., /1 represents drive 1. The /I and /O options
		     must not be used in the same command line.

		/O   Assume the output device is a cassette drive. An
		     output device must also be specified on the command
		     decoder line, but is ignored. This option is used when
		     there are no cassette handlers configured into your
		     system. The drive number is specified as an option. The
		     /I and /O options must not be used in the same command
		     line.


     2-140	In the fourth paragraph change the second sentence to:

		All error messages are of the form:

		      ?XXX

		where XXX is a 3-letter mnemonic which references the list
		of error messages that appears at the end of this chapter.

		After the last sentence on this page, append:

		If TECO runs on a machine with at least 12K of memory, the
		error message and a description of the error message are
		displayed on the terminal.


     2-142	In Table 2-28, under RUBOUT, append:

		If SET TTY SCOPE is typed followed by a carriage return,
		RUBOUT erases the character from the screen of a VT52.


     2-143	In Table 2-28, under CTRL/C, append:

		If CTRL/C is not typed as the first character after an
		asterisk (*) is printed, the ?XAB error message (execution
		aborted) is displayed and control returns to TECO.



				      20



     Page			    Addition/Correction


     2-146	In Table 2-30, under the Y command, append:

		If this command is issued while an output file containing
		text in the buffer is open, an error message is displayed.
		To avoid this situation, use HKY.

		In Table 2-30, under the P command, delete the description
		and replace with:

		Writes the content of the buffer onto the output file then
		clears the buffer and reads the next page of the input file
		into the buffer. A form feed is appended only if one was
		present when the buffer was read in.


     2-152	In Table 2-35 delete ^Rtext1$text2$ and the description.


     2-155	Under COMMAND LOOPS in the sentence "If n is not supplied,
		a value of 4096 is assumed." change "4096" to "infinity".


		Under Q-Registers, in the sentence "In the number storage
		area, each Q-register can store one integer in the range
		-2048<=n<=2047" change the range to:
		
		- 4095<=n<=4095


     2-156	Change Table 2-37 as follows: The last sentence describing
		n%q$ should read "If n is not present, it is assumed to be
		equal to 1."

		Replace the command n%$ with n%q.

		Under the nUq command change the range from "-2049<=n<=2048"
		to:

		"-4095<=n<=4095".


     2-159	In Table 2-39 delete the n-m"A and n-m"B commands and their
		 descriptions.

		Under the n"G command, change the range from
		"- 2048<=n<=2047" to:

		"-4095<=n<=4095"


    2-160	Under the section entitled Numeric Arguments, delete the
		second paragraph and insert the following:

				      21


     Page			    Addition/Correction


     2-160	This leads to an important restriction on the maximum size
    (cont.)	of any numeric argument. Commands which require positive
		arguments must have an argument in the range 0<n<8195,
		since 8195 is the largest number which may be stored in one
		TECO word. Commands which may have positive or negative
		arguments require an argument in the range -4095<n<4095,
		because -4095 is the smallest number which may be stored in
		13 bits using 2's complement notation, while 4095 is the
		largest number which may be stored in this manner.


     2-162	In Table 240, change the ^V character to EO and the
		description to:

		EO is equivalent to the version of TECO which is currently
		being run. This manual describes TECO version 5.


     2-163	In the last line before Table 241, change 4096 to 8192.

		In Table 2-41, under the - operator, change -2=4096 to
		-2=-2.


     2-175	Replace figures 2-5 and 2-6 with the following:

		Figure 2-5:

		     J!1!OUN 0US!
		     !<QNA-32"E 1%S$'!
		     !QNA-13"E OJUSTIFY$'!
		     !1%N$>!
		     !!JUSTIFY!QN-40"G!
		     !60-QN-QS<S $I $S^N$>
		     !0L QS%N$ Q5%S$ OJUSTIFY$'!
		     !60-QN"G 60-QN<S $I $S^N $>''!
		     !LZ-."G0 1$'$$

		Figure 2-6:

		     .R TECO
		     *ERDTA1:MACRO.TE$ Y HXI HK$$
		     *ERDTA1:TEXT.AS$ Y MI$$


     2-178	Replace the example for SUPER TECO with:

		     .GET SYS TECO
		     .ODT
		     2051/7420 7610
		     2134/7450 7410
		     ^C
		     .SAVE SYS STECO

				      22



     Page			    Addition/Correction


     2-178	Replace the current example of STECO (Super TECO) with the
     (cont.)	following example.

		.R STECO
		*ERBBB:$EWDDD:JUNK.$$	(WHERE BBB IS THE DEVICE WITH A LOST
					FILE (EMPTY)). READ FROM BAD DEVICE
					BBB: WRITE A FILE JUNK ON GOOD
					DEVICE DDD:

		*NABCDE$QLT$$		SEARCH FOR NEXT "ABCDE" THEN TYPE
					THE LINE. MULTIPLE SEARCHES MAY
					NEED TO BE MADE.

		*D......		DELETE JUNK CHARACTERS FROM THE BE-
					GINNING OF THE LINE PARTICULARLY A
					^Z.

		*EF$$			CLOSE THE JUNK FILE.

		*EWDEV:FILEN.EX$$	OPEN A NEW FILE ON THE GOOD DEVICE
					WITH THE PROPER FILE NAME.

		*NUVWXYZ$PWEF$$		SEARCH FOR THE END OF THE FILE TEXT
					"UVWXYZ" WRITING TO THE NEW FILE.

		*EX$$			EXIT TO OS/8.

		In the section on "Incompatibilities Between OS/8 TECO and
		DECsystem-10 TECO," change incompatibility #1 to read as
		follows: "The ^R command does not exist on DECsystem-10
		TECO."


     2-179	Step 6 - delete

		Step 7 - delete the word "^V".

		In Table 244, add the commands:

		FS  search for a character string in the current buffer and
		    replace with another string.

		FN  search for a character string in a page of the input
		    file which may not have been read into the buffer, and
		    replace with another string.

		^U  insert the specified character string into the text
		    storage area of the Q-register.


     2-180	In Table 244, under the heading POINTER POSITIONS, change
		the command mL to nL.

				      23



     Page			    Addition/Correction


     2-182,	In the section "Running TECO on the PDP-12" change all
     2-183	references to "^W" to "W"


     2-184	Table 2-45, delete all and replace with: Table 2-45 on next
		3 pages.


		   Table 2-45 Summary of TECO Error Messages

     ----------------------------------------------------------------------
     | Printout |	  Printout	   |	       Meaning		  |
     | Abbrev-	|	  Message	   |				  |
     | iation   |			   |				  |
     |----------|--------------------------|------------------------------|
     |	?ARG	| IMPROPER ARGUMENTS	   | Number missing before comma, |
     |		|			   | or two arguments specified   |
     |		|			   | to D, or three numeric	  |
     |		|			   | arguments			  |
     |		|			   |				  |
     |	?BNI	| NOT AN ITERATION	   | Iteration close (>) without  |
     |		|			   | matching open (<)		  |
     |		|			   |				  |
     |	?CCL	| CCL.SV NOT FOUND OR EG   | CCL not found or EG argument |
     |		| ARGUMENT TOO BIG	   | too long			  |
     |		|			   |				  |
     |	?FER	| FILE ERROR		   | FILE ERROR can mean:	  |
     |		|			   | 1) input file not found on   |
     |		|			   |    "ER" command		  |
     |		|			   | 2) cannot enter output file  |
     |		|			   |    on "EW" or "EB" command	  |
     |		|			   | 3) device specified for file |
     |		|			   |    does not exist		  |
     |		|			   | 4) "EB" command given on	  |
     |		|			   |    non-file structured device|
     |		|			   |				  |
     |	?FUL	| OUTPUT COMMAND WOULD HAVE| Output command would have	  |
     |		|			   | overflowed output file	  |
     |		|			   | (panic mode)		  |
     |		|			   |				  |
     |	?IEC	| ILLEGAL CHARACTER X*	   | E followed by an illegal	  |
     |		| AFTER E		   | character			  |
     |		|			   |				  |
     |	?IFC	| ILLEGAL CHARACTER X*     | F followed by an illegal	  |
     |		| AFTER F		   | character			  |
     |		|			   |				  |
     |	?IFN	| ILLEGAL CHARACTER X***   | Illegal file name in "ER",	  |
     |		| IN FILE NAME		   | "EW" or command		  |
     |		|			   |				  |
     |	?ILL	| ILLEGAL COMMAND X*	   | Illegal command		  |
     ----------------------------------------------------------------------
						(continued on next page)

				      24



     Page			    Addition/Correction


	       Table 2-45 Summary of TECO Error Messages (cont.)

     ----------------------------------------------------------------------
     | Printout |	  Printout	   |	       Meaning		  |
     | Abbrev-	|	  Message	   |				  |
     | iation   |			   |				  |
     |----------|--------------------------|------------------------------|
     |	?INP	| INPUT ERROR		   | Parity error on input file	  |
     |		|			   |				  |
     |	?IQC	| ILLEGAL CHARACTER X*	   | " followed by an illegal	  |
     |		| AFTER ""		   | command			  |
     |		|			   |				  |
     |	?IQN	| ILLEGAL Q REGISTER NAME  | Non-alphanumeric Q-register  |
     |		| X**			   | name			  |
     |		|			   |				  |
     |	?MEM	| STORAGE CAPACITY EXCEEDED| Text buffer overflow	  |
     |		|			   |				  |
     |	?NAC	| NEGATIVE ARGUMENT TO,	   | Negative argument to comma	  |
     |		|			   |				  |
     |	?NAE	| NO ARGUMENT BEFORE =	   | No numeric argument to the   |
     |		|			   | left of an equal sign	  |
     |		|			   |				  |
     |	?NAP	| NEGATIVE OR ZERO ARGUMENT| Negative or zero argument to |
     |		| TO P			   | P				  |
     |		|			   |				  |
     |	?NAQ	| NO ARGUMENT BEFORE QUOTE | No numeric argument to the   |
     |		|			   | left of a quote		  |
     |		|			   |				  |
     |	?NAS	| NEGATIVE OR ZERO ARGUMENT| Negative or zero argument	  |
     |		| TO S			   | with a search		  |
     |		|			   |				  |
     |	?NAU	| NO ARGUMENT BEFORE U	   | No numeric argument to the	  |
     |		|			   | left of a U		  |
     |		|			   |				  |
     |	?NAY	| NUMERIC ARGUMENT TO Y	   | Numeric argument specified   |
     |		|			   | with Y command		  |
     |		|			   |				  |
     |	?NFO	| VERSION NUMBER TO FILE   | Attempt to output without	  |
     |		| FOR OUTPUT		   | opening an output file	  |
     |		|			   |				  |
     |	?NYI	| CASE SUPPORT NOT	   | Case support not implemented |
     |		| IMPLEMENTED		   | (use EO for version)	  |
     |		|			   |				  |
     |	?NYI	| CASE SUPPORT NOT	   | Case support not implemented |
     |		| IMPLEMENTED		   | (use W for watch)		  |
     |		|			   |				  |
     |	?OUT	| OUTPUT ERROR		   | Output file too big or	  |
     |		|			   | output parity error	  |
     ----------------------------------------------------------------------
						(continued on next page)



				      25



     Page			    Addition/Correction


	       Table 2-45 Summary of TECO Error Messages (cont.)

     ----------------------------------------------------------------------
     | Printout |	  Printout	   |	       Meaning		  |
     | Abbrev-	|	  Message	   |				  |
     | iation   |			   |				  |
     |----------|--------------------------|------------------------------|
     |	?PDO	| INTERNAL PUSHDOWN	   | Pushdown overflow (macros	  |
     |		| OVERFLOW		   | and iterations nested too    |
     |		|			   | deeply)			  |
     |		|			   |				  |
     |	?POP	| ATTEMPT TO MOVE POINTER  | Attempt to move pointer	  |
     |		| OFF PAGE		   | outside of text buffer	  |
     |		|			   |				  |
     |	?QMO	| Q REGISTER MEMORY	   | Q-register storage overflow  |
     |		| OVERFLOW		   |				  |
     |		|			   |				  |
     |	?SNI	| NOT IN AN ITERATION	   | Semicolon on command level	  |
     |		|			   |				  |
     |	?SRH	| SEARCH FAILED		   | Failing search at command	  |
     |		|			   | level			  |
     |		|			   |				  |
     |	?STL	| SEARCH STRING TOO LONG   | Search string too large	  |
     |		|			   | (greater than 31 characters) |
     |		|			   |				  |
     |	?UTC	| UNTERMINATED COMMAND	   | Incomplete command (PDL not  |
     |		|			   | empty at end of command	  |
     |		|			   | string)			  |
     |		|			   |				  |
     |	?UTM	| UNTERMINATED MACRO	   | Incomplete command (PDI not  |
     |		|			   | empty at end of macro)	  |
     |		|			   |				  |
     |	?WLO	| CANNOT WRITE OUT ERROR   | Write locked system device   |
     |		| MESSAGE OVERLAY	   |				  |
     |		|			   |				  |
     |	?XAB	|			   | Execution aborted		  |
     |		|			   |				  |
     |	?YCA	| Y COMMAND ABORTED	   | Y (or .) command aborted	  |						   _
     |		|			   | because data would be lost   |
     ----------------------------------------------------------------------


		Add the following information about the DECtape Formatting
		and DECtape Copying Programs at the end of Chapter 2.

		DTFRMT
		This program records the required timing and mark tracks on
		a DECtape mounted on the TC01-TU55 unit or a TC08-TU56
		DECtape unit.

		The program interacts with you via the terminal to obtain
		the necessary data for each set of DECtapes to be formatted.

				      26



     Page			    Addition/Correction


     2-184	As soon as one set of tapes is formatted, the program is
     (cont.)	ready to format another set.

		Two full passes are required to completely format each
		DECtape, and up to eight DECtapes may be formatted at a
		time (assuming that the user has eight tape transports).
		Upon completion of a cycle, new tapes may be mounted and
		formatted as the last, with a minimum of operator-program
		communication.

		PRELIMINARY REQUIREMENTS

		Equipment
		PDP-8, terminal, TC01-TU55 DECtape Control.

		LOADING PROCEDURE

		Load the program into core using the standard Binary Loader.

		USING THE PROGRAM

		Starting Procedure

		a. Key 1000 into the SWITCH REGISTER. Depress LOAD ADDRESS
		   and depress START. "DTA?" is printed on the terminal.

		Mount the DECtapes to be marked onto the tape transports,
		with just enough turns of tape on the right hand reel of
		each transport to provide a grip. Make sure that no two
		tape units are set to the same unit number. Set the RDMK-
		WRTM-NORMAL switch located on the TC01 maintenance control
		panel to the WRTM position, for each transport to be used,
		set the WRITE ENABLED-WRITE LOCK switch to WRITE ENABLED,
		and the REMOTE-OFF-LOCAL switch to REMOTE.


		Operating Procedures
		The user types: R DTFRMT in response to the monitor dot (.).
		The program and operator now converse. The printout "DTA?"
		is asking which DECtape units will be used. The operator
		types a unit number or series of unit numbers,
		corresponding to the DECtape units upon which he has
		mounted tapes. For instance, if the operator has mounted
		tapes on units 2, 5, 7, and 8, he would type 2 5 7 8 (CR)
		(where (CR) signifies a carriage return). Spaces are
		ignored, so it makes no difference if the operator types
		spaces between the unit numbers. Only one specification of
		a unit is significant, i.e., typing 2 2 5 7 7 5 8 2 8
		(CR) has the same effect as typing 2 5 7 8 (CR).

		Once the operator has specified the units he wishes to use,
		the program types "DIRECT?". The operator responds by

				      27



     Page			    Addition/Correction


     2-184	typing MARK (CR) or MARK XXXX (CR). If he types MARK
     (cont.)	(CR) the program assumes 201(8) words, 2702(8) blocks
		(standard PDP-8 format). Otherwise, XXXX is accepted as a
		decimal number of words per block, and must be divisible by
		3. Note that typing MARK 384 (CR) will cause the program
		to generate a standard PDP-10 format DECtape (1102(8)
		blocks of 600(8) words, which is equivalent to 1102(8)
		blocks of 200(8) words, where each word is 36 bits rather
		than 12 bits).

		The program now types "XXXX WORDS, YYYY BLOCKS OK? (YES OR
		NO)." This serves as a final check for block count. XXXX
		and YYYY are octal values representing the final outcome of
		a formula solved by the program, determining the number of
		blocks that may be written on a DECtape knowing the number
		of words. If a NO (CR) answer is given, the program
		reverts to "DIRECT?". Otherwise (if YES (CR)) the tape on
		the first unit specified begins to move.

		Once all of the tapes specified have been marked, the
		printout "SET SWITCH TO NORMAL" appears. Then the operator
		returns the "RDMK-WRTM-NORMAL" switch to NORMAL, and
		strikes the (CR) key on the terminal, starting the second
		pass. Note that during the second pass with multiple
		DECtape units, as soon as one tape stops and the next tape
		starts, the first tape is completed and may be replaced
		with a fresh tape in preparation for recycling.

		The program continues by itself until completed, at which
		time the "DIRECT?" printout occurs. Typing "SAME (CR)"
		repeats the entire process with the original constants.
		The new DECtapes must be mounted and ready to write timing
		and mark tracks before "SAME (CR)" is typed. Also, in
		response to "DIRECT?", typing "RDR (CR)" causes the
		printout of the unit numbers of the DECtapes and the last
		twelve block numbers; "RDF (CR)" causes the printout of
		the unit numbers and the first twelve block numbers; and
		"RESTART (CR)" returns the program to "DTA?". Unit
		numbers are printed as "N000", where N is the unit number
		(0 means DECtape unit 8). Once formatting begins, control
		C will cause the program to restart at "DTA?". If the user
		wishes to return to the monitor another control C may be
		typed at this time.

		Following are several examples of successful operation. The
		underlined portions are printed by the program. ALL
		operator responses should be followed by a carriage return.

		a. Create a standard tape on unit 4.




				      28



     Page			    Addition/Correction


     2-184	    DTA? 4		    ____
     (cont.)	    DIRECT? MARK		    _______
		    0201 WORDS, 2702 BLOCKS.OK? YES OR NO		    _____________________________________
		    YES
		    SET SWITCH TO NORMAL		    ____________________
		    DIRECT?		    _______

		b. Create 16 standard PDP-10 format tapes - eight at a time,
		   on units 1-8.

		    DTA? 12345678		    ____
		    DIRECT? MARK 384		    _______
		    0600 WORDS,1102 BLOCKS OK? YES OR NO		    ____________________________________
		    YES
		    SET SWITCH TO NORMAL (USER TYPES (CR))		    ____________________
		    DIRECT? SAME		    _______
		    SET SWITCH TO NORMAL (USER TYPES (CR))		    ____________________
		    DIRECT?		    _______

		Errors

		    Errors Typed to "DTA?" and "DIRECT?" - Revert back to
		    "DTA?" or "DIRECT?"

		    Error Messages for Response to MARK XXXX-

		    NOT DECIMAL		A character in XXXX is not 0-9.
		    NOT DIVISIBLE BY 3  XXXX cannot be divided evenly by 3.
		    TOO MANY WORDS	The number of words plus 15 exceeds
					7777(8).
		    TOO MANY BLOCKS	The number of blocks generated by
					XXXX exceeds 7777(8).

		    Error Messages for Response to YES (After message -
		    revert back "DTA?")

		    SETUP?		Indicates an error in the DECtape
					setup -

					Unit in WRITE LOCK
					Nonselectable unit
					Switch not in WRTM position

		    Error Messages for Marking and Verifying a Tape

		    XXXX SHOULD BE YYYY BLK ERROR PHASE X
		    XXXX SHOULD BE YYYY DATA ERROR PHASE X
		    END TAPE ERROR PHASE X
		    MARK TRACK ERROR PHASE X
		    PARITY ERROR PHASE X
		    SELECT ERROR PHASE X
		    TIMING ERROR PHASE X

				      29



     Page			    Addition/Correction


     2-184	    LAST INT NOT END ZONE
     (cont.)
		Recovery
		Although error should cause doubt concerning the entire
		process, restarts may be made by phases (except when in
		phase 0). Restart the phase by typing "RETRY (CR)" Type
		"RESTART" to return to "DTA?"

		    PHASE 0:	MARK TRACK WRITE
		    PHASE 1:	WRITING LAST REVERSE BLOCK NUMBER FORWARD
		    PHASE 2:	WRITING BLOCK NUMBERS AND DATA IN REVERSE
		    PHASE 3:	READING AND CHECKING BLOCK NUMBERS AND DATA

		An error that should be considered catastrophic is LAST INT
		NOT END ZONE. This indicates that between the last (or
		first) block number and the end zone, something caused an
		interrupt (DTF).

		The entire program may be restarted at 1000(8) any time.

		DETAILS OF OPERATION AND STORAGE
		The program writes timing and mark tracks on a DECtape,
		then inserts block numbers and parity correct information,
		checking the results of all operations.

		The number of block frames to be written is a function of
		the number of words per block. The formula

				  212080
		blocks per tape = ------ + 2
				  NW+15

		where NW equals the number of words to be written, is used
		by the program to compute the number of blocks, but is
		adjusted by the program to provide the standard PDP-8
		format of 129 (12-bit) words, 1744 blocks, and standard
		PDP-10 format of 128 (36-bit) words, 578 blocks.

		Two full passes are required to mark and verify a tape.

		     Pass 1	  Marks the tape forward, inserts block
				  numbers and parity correct date in
				  reverse.

		     Pass 2	  Reads and checks block numbers and data
				  forward and reverse.

		During the forward direction of the first pass, the TC01 is
		switched into WRITE TIMING AND MARK TRACKS, CONTINUOUS MODE,
		FORWARD. The program manipulates data to be written by
		monitoring the word count register and the DTF, (DECtape
		flag). Initially, ten feet of end-zone code is written, and

				      30



     Page			    Addition/Correction


     2-184	abutting the end zone are about two standard block lengths
     (cont.)	of interblock sync. To the TC01, this interblock sync acts
		as no operation, but guarantees that at turn-around time,
		block 0 is read first (or 2701 if turning out of the
		forward end zone). Now the remainder of the tape is
		written creating block frames. The number of such frames is
		determined by the above formula. Upon completion of the
		block framing; another extended interblock sync zone is
		written as well as ten feet of end zone.

		Pass 1 forward is now complete (timing and mark tracks are 
		written).  The tape is ordered to MOVE in reverse for three 
		seconds, thus moving it out of the end zone and onto the 
		marked section.  The tape is once again moved forward, and 
		the last REVERSE BLOCK NUMBER is written until the forward 
		end zone is sensed.  Now the tape is turned out of the end 
		zone in SEARCH, and the program waits for a block 
		interrupt (first reverse block number).  When the DTF 
		rises, the TC01 is switched into WRITE ALL, CONTINUOUS, 
		REVERSE;  thus the system is synchronized and all block 
		numbers and data are written:  until the forward end zone 
		is sensed.  This completes the marking and blocking of the 
		tape.  Pass 2 in CONTINUOUS MODE checks the data and block 
		numbers to be certain they are correct.  When multiple 
		DECtape units are specified, Pass 1 forward is completed 
		for each tape before Pass 1 reverse is begun. 

		TDFRMT
		The TD8-E DECtape formatter program records the timing and 
		mark tracks on a DECtape mounted on the TU56 DECtape 
		transport.

		The program interacts with the operator via the terminal to 
		obtain the necessary data for each set of DECtapes to be 
		formatted.  As soon as one set of tapes is formatted, the 
		program is ready to format another set.

		Three full passes are required to completely format each 
		DECtape, and up to two DECtapes may be formatted at a time 
		(units 0 and 1).  Upon completion of a cycle, new tapes may 
		be mounted and formatted as the last, with a minimum of 
		operator-program communication.  One tape excluding tape 
		setup time, requires three minutes from start to finish.

		Mount the DECtapes to be marked onto the tape transports 
		with just enough turns of tape on the right hand reel of 
		each transport to provide a grip.  Make sure that no two
		tape units are set to the same unit number.  Set the switch 
		on the TD8-E to WTM position.  For each transport to be 
		used, set the WRITE-ENABLED-WRITE LOCK switch to WRITE 
		ENABLED, and the REMOTE-OFF-LOCAL switch to REMOTE.


				      31



     Page			    Addition/Correction


     2-184	OPERATING PROCEDURES
     (cont.)	The user types .R TDFRMT in response to the monitor dot (.).
		The program and operator now converse.  The printout 
		"UNIT?" is asking which DECtape units will be used. The 
		operator types one or two unit numbers corresponding to the 
		DECtape units upon which he has mounted tapes.  For 
		instance, if the operator has mounted tapes on units 0 and 
		1, he would type a 1.  Spaces are ignored, so it makes no 
		difference if the operator types spaces between the unit 
		numbers.  Only one specification of a unit is significant,
		i.e., typing 000111 has the same effect as typing 01.

		Once the operator has specified the unit(s) he wishes to 
		use, the program types "FORMAT?".  The operator responds by 
		typing MARK or MARK XXXX.  If he types MARK, the program 
		assumes 201 words 2702 blocks (standard PDP-8 format).  
		Otherwise XXXX is accepted as a decimal number of words per 
		block and must be divisible by 3.  Note that typing MARK 
		384 will cause the program to generate standard PDP-10 
		format DECtapes (1102(8) blocks of 600 words, which is 
		equivalent to 1102(8) blocks of 200 words where each word 
		is 36 bits rather than 12 bits).

		The program now types "XXXX WORDS, YYYY BLOCKS OK? (YES OR 
		NO)".  This serves as a final check for block count.  XXXX 
		and YYYY are octal values representing the final outcome of 
		a formula solved by the program, determining the number of 
		blocks that may be written on DECtape knowing the number of 
		words.  If a no answer is given, the program reverts to 
		"FORMAT?".  Otherwise (IF YES), the program types out "SET 
		SWITCH TO WTM".  Then the operator hits carriage return on 
		the teletype and the tape on first unit specified begins to
		move if the switch is set.

		Once all of the tapes specified have been marked, the 
		printout "SET SWITCH TO OFF" appears, then the operator 
		resets the WTM switch to off, and strikes the return key on 
		the terminal starting the second pass.  Note that during 
		the second pass with multiple DECtape units, as soon as one 
		tape stops and the next tape starts, the first tape is com-
		pleted and may be replaced with a fresh tape in preparation 
		for recycling.

		The program continues by itself until completed at which 
		time the "FORMAT" printout occurs.  Typing "SAME<" repeats 
		the entire process with the original constants. The new 
		DECtapes must be mounted and ready to write timing and mark 
		tracks before a carriage return is hit on the teletype 
		after the typing "SET SWITCH TO WTM".  Also, in response 
		to "DIRECT?", typing "RDR" causes the printout of the unit 
		number of the DECtape and the last 22 block numbers;  
		"RDF<" causes the printout of the unit number and the first 

				      32



     Page			    Addition/Correction


     2-184	22 block numbers;  and "RESTART<" returns the program to 
     (cont.)	"UNIT?". Unit numbers are printed as "000N" where N is the 
		unit number.

		Following are several examples of successful operation.  
		The underlined statements are printed by the program.  All 
		operator responses should be followed by a carriage return.

		a. create a standard PDP-8 tape on unit 1

		     UNIT?1		     _____
		     FORMAT?MARK		     _______
		     0201 WORDS, 2702 BLOCKS, OK? (YES OR NO)		     ________________________________________
		     YES
		     SET SWITCH TO WTM		     _________________
		     SET SWITCH TO OFF		     _________________
		     FORMAT?		     _______

		b. create 4 standard PDP-10 format tapes, two at a time on
		   units 0 1

		     UNIT?01		     _____
		     FORMAT?MARK 384		     _______
		     0201 WORDS, 2702 BLOCKS, OK? (YES OR NO)		     ________________________________________
		     YES
		     SET SWITCH TO WTM		     _________________
		     SET SWITCH TO OFF		     _________________
		     FORMAT?SAME		     _______
		     SET SWITCH TO WTM		     _________________
		     SET SWITCH TO OFF		     _________________
		     FORMAT?		     _______


		ERRORS
		Errors typed to "UNIT" and "FORMAT" revert back to "UNIT?"
		or "FORMAT?".

		Error messages for response to MARK XXXX

		NOT DECIMAL		     A CHARACTER IN XXXX IS NOT 0-9
		NOT DIVISIBLE BY 3	     XXXX CANNOT BE DIVIDED EVENLY
					     BY 3
		TOO MANY WORDS		     THE NUMBER OF WORDS PLUS 15
					     EXCEEDS 7777(8).
		TOO MANY BLOCKS		     THE NUMBER OF BLOCKS GENERATED
					     BY XXXX EXCEEDS 7777(8).

		Error messages for response to "SET SWITCH TO WTM".





				      33



     Page			    Addition/Correction


     2-184	    1. SETUP?	        indicates an error in the DECtape
     (cont.)			        setup. One of the units specified 
				        is in write lock position, not 
				        selected, or the write flip-flop is
				        unable to be set, or there may be a 
					timing error. (After message revert 
					back to "UNIT".)

		    2. Switch not set to WTM or single line flag failed
		       to set. Set switch to WTM.

				        This type out says that either the
				        switch on the M868 modules is not 
					set to the WTM position or the 
					timing generator for writing the 
					mark and timing tracks is not 
					setting the single line flag.

		      RECOVERY:

				        If the switch was not set to WTM
				        position set the switch and hit
				        carriage return on the teletype.

				        If the switch was set to WTM 
					position and this type out 
					occurred, try again or examine the
					timing generator circuit.

		Error messages for marking and verifying a tape

		      PC  XXXX MARK TRACK ERROR PHASE Y
		      PC  XXXX BLOCK NUMBER ERROR PHASE Y
		      PC  XXXX DATA ERROR PHASE Y
		      PC  XXXX CHECKSUM ERROR PHASE Y
		      PC  XXXX TIMING ERROR PHASE Y
		      PC  XXXX WRITE ERROR PHASE Y

		XXXX equals the program counter at time of the failure. Y
		equals the pass which it was in.

		Although an error should cause doubt concerning the entire
		process, a restart may be made (except in phase 0) by
		typing "RETRY<'. Retry causes the program to go back to
		phase l, type "RESTART<'' to return to "UNIT?".

		      PHASE 0:	   WRITE TIMING AND MARK TRACK FORWARD
		      PHASE 1:	   READS MARK TRACK REVERSE
		      PHASE 2:	   WRITE DATA, FORWARD BLOCK AND REVERSE
				   BLOCK NUMBERS FORWARD AND WRITES THE
				   CHECKSUMS
		      PHASE 3:	   DISPLAYS BLOCK NUMBERS IN AC REVERSE

				      34



     Page			    Addition/Correction


     2-184	      PHASE 4:	   READS DATA, FORWARD BLOCK AND REVERSE
     (cont.)			   BLOCK NUMBERS FORWARD AND CALCULATES
				   THE CHECKSUM
		      PHASE 5:	   READS REVERSE BLOCK NUMBERS IN REVERSE

		The entire program may be restarted at 0200 any time.

		DETAILS OF OPERATION AND STORAGE
		The program writes timing and mark track on a DECtape
		forward with WTM switch set. Then it reads the mark track
		in the reverse direction with the switch set to off. The
		program checks all of the mark track once it is in sync.
		(see flow figure 1) when it finishes reading the mark track
		reverse, it bounces off the end zone and starts writing
		zeroes to the first block mark. The program is now in sync.
		The program now continues writing forward block numbers,
		reverse checksum, data, checksum, and reverse block numbers
		for the rest of tape. When it sees the end zone, it turns
		around and starts displaying the reverse block number in
		the accumulator until it hits the end zone again. Now the
		tape turns around and starts reading and comparing all
		forward block numbers, reverse checksum, all data, checksum
		and reverse block numbers that was written in Phase 2. This
		comparison is done on all blocks until the end zone is
		reached. The tape turns around in the end zone and starts
		looking for reverse block numbers and comparing them all the
		way down tape to the end zone. The formatting is now
		complete, the tape stops, and "FORMAT" is typed out waiting
		for new directions.

		The number of block frames to be written is a function of
		the number of words per block.

		The formula

		     BLOCKS PER TAPE [(212080)/(NW+15)] +2

		where NW equals the number of words to be written, is used
		by the program to compute the number of blocks, but is
		adjusted by the program to provide the standard PDP-8
		format of 129(10)(12-bit) words, 1474(10) blocks, and
		standard PDP-10 format of 128(10)(36-bit) words, 578(10)
		blocks.

		Theory

		The writing of the mark track is done through AC bits 0,3,6
		and 9. The following description is how the mark track is
		written.

		A. Install the tape with enough turns to create a pull. The
		   reverse end zone requires a sequence of three data words

				      35



     Page			    Addition/Correction


     2-184	   for its pattern.
     (cont.)
		     4044
		     0440
		     4404

		   In the mark track the words appear at 101101101101101
		   (5555(8)). The reverse end zone should cover about 10
		   feet of tape. Write the above three words 4096(10)
		   times.

		B. Write the below three words (see C) or expand code 99
		   times.
	
		C. Expand code, three words of expand code should
		   immediately follow each block,
	
		     0404
		     0404
		     0404

		   In the mark track the words appear as 010101010101
		   (2525(8)).

		D. The forward block mark and reverse guard require three
		   words.

		     0404
		     4004
		     4040
	
		   Which appear on the mark track as 010110011010 (2632(8)).

		E. The lock mark, reverse checksum, reverse final, reverse
		   prefinal consist of six PDP-8 memory words,
	
		     0040
		     0000
		     4000
		     0040
		     0000
		     4000

		   These words appear on the mark track as
		   001000001000001000001000 (10101010(8)).
	
		F. Mark track code for data is generated by

		     4440
		     0044
		     4000


				      36



     Page			    Addition/Correction


     2-184	   These three words appear as 111000111000(7070(8)) and
     (cont.)	   are repeated 41(10) times for a 129 word block.

		G. The prefinal, final, checksum, and reverse lock consist
		   of six PDP-8 words.

		     4440
		     4444
		     4044
		     4440
		     4444
		     4044

		   These words appear on the mark track as
		   111011111011111011111011 (73737373(8)).

		H. The guard and reverse block mark consist of three words

		     4040
		     0440
		     0404

		   which appear as 101001100101 (5145(8)).

		I. Generate 2702(8) block patterns. Repeat C through H.
		   2702(8) times.

     		J. 100 expand codes (see C).

		K. The end zone pattern consist of three words,

		     0400
		     4004
		     0040

		   which appears on the mark track as 010010010010
		   (2222(8)). Repeat these 3 words 4096(10) times. See
		   Figure 2 for a diagram of the mark track and data
		   tracks.


		DTCOPY
		The TC01, TC08, TU-55 Copy Program is controlled through a
		dialog on the terminal. The responses to the questions are
		in the form of octal numbers followed by a carriage return.
		Where more than one answer is required to a question, the
		answers are separated by semicolons. Alphabetic or other
		illegal characters will cause an error message to be
		generated and the question to be repeated. If too many
		digits are typed for the response expected, only the last
		ones typed will be used. If the response was to be either 0
		or 1 (YES or NO), a non-zero final digit will be assumed to

				      37



     Page			    Addition/Correction


     2-184	be 1.
     (cont.)
		Before answering the dialog's questions, the user must
		ensure that all the DECtapes involved are mounted on their
		respective drives. All the drives must be set to REMOTE.
		The input drive may be set to WRITE LOCK or WRITE ENABLE;
		all output drives must be set to WRITE ENABLE. No two
		drives may have the same unit number.

		The user types R DTCOPY in response to the monitor dot (.).
		The program types DECtape COPY V1OA.

		For each set of copies, the dialog is as follows (the
		user's response is underlined; (CR) means carriage return):

		     DECTAPE COPY V1OA
		     FROM UNIT 0			       _

		     TO UNIT 2			     _

		     FIRST BLOCK TO COPY (OCTAL) 0						 _

		     FINAL BLOCK TO COPY (OCTAL) 700						 ___

		     PDP-8 WORDS PER BLOCK 0201

		     VERIFY OUTPUT? (0=YES, 1=NO): 0						   _

		When all specified copies have been finished, the tapes are
		rewound and the dialog	continues:

		     DONE
		     DECTAPE COPY V1OA
		     FROM UNIT

		The user may return to the monitor by typing CTRL/C at
		anytime. (Control characters are not echoed printed.)

		ERROR MESSAGES
	
		ILLEGAL RESPONSE      The user's response to the dialog was
				      not correct; for example, an
				      alphabetic character was typed or
				      carriage return was typed before an
				      octal number was given where one was
				      required. The question will be
				      restated and any previous answer
				      ignored. Nothing should be typed until
				      the terminal has stopped printing.

		SELECT ERROR UNIT n   During attempted data transfer, unit
				      n was not found. The program waits

				      38



     Page			    Addition/Correction


     2-184			      for the user to correct the cause of
     (cont.)			      the error. The user should check to
				      see that:
					1. if unit n is an output drive, it
					   is set to WRITE ENABLE.
					2. unit n is set to REMOTE.
					3. there is only one unit n.
					4. all units are set to numbers
					   appropriate to their TD8E
					   internal wiring.
					When the cause of the error has
					been corrected, the user may type
					CTRL/R to resume transfer or he may
					type CTRL/S to restart the dialog.

		TAPE ERROR BLOCK x UNIT n
					During attempted transfer, a parity
					error or timing error was detected,
					or too great a block number was
					requested near block x on the tape
					on unit n. The tapes are rewound
					and the dialog is automatically
					restarted at DONE, REPEAT (YES=1,
					NO=0).

		VERIFY ERROR BLOCK x UNIT n
					The data on the input tape does not
					match the data which was written on
					block x of the output tape on unit
					n. The user may type CTRL/R to
					ignore the error and continue with
					the transfer, CTRL/T to try the
					last transfer again and continue if
					the error does not recur, or CTRL/S
					to restart the dialog.

		ILLEGAL FORMAT UNIT n
					Either the number of words per
					block on unit n does not agree with
					the number of words per block on
					the input unit or, when the number
					of blocks on the tape was calculated
					from the block length of the input
					tape, the length was found to be
					illegal. The number of blocks is
					only calculated if the whole tape
					copy option is requested. In either
					case, when the error has been
					corrected, the user may type CTRL/R
					to check the formats of all tapes
					again and continue, or CTRL/S to
					restart the dialog.

				      39



     Page			    Addition/Correction


     2-184	TDCOPY
     (cont.)	TD8E Copy is controlled through a dialog on the terminal.
		The response to the questions are in the form of octal
		numbers followed by a carriage return. Where more than one
		answer is required to a question, the answers are separated
		by semicolons. Alphabetic or other illegal characters will
		cause an error message to be generated and the question to
		be repeated. If too many digits are typed for the response
		expected, only the last ones typed will be used. If the
		response was to be either 0 or 1 (YES or NO), a non-zero
		final digit will be assumed to be 1.

		Before answering the dialog's questions, the user must
		ensure that all the DECtapes involved are mounted on their
		respective drives. All the drives must be set to REMOTE. The
		input drive may be set to WRITE LOCK or WRITE ENABLE; all
		output drives must be set to WRITE ENABLE. No two drives may
		have the same unit number.

		The user types R TDCOPY in response to the monitor dot(.).
		The program prints:

		     TD8E COPY V4A
		     HIGHEST FIELD AVAILABLE:

		The user response with the number of the highest field he
		wishes used for buffer space. This response may allow data
		to be preserved in any higher field or may make full use of
		the memory available. This question is asked only once,
		immediately after the program has been loaded. To change
		the response, the program must be executed again. If 4K of
		memory is to be used, the response is 0; if 8K, the
		response is 1, and so forth.

		For each set of copies, the dialog is as follows (the user's
		response is underlined; (CR) means carriage return):

			Dialog				Comments

		FROM UNIT: 0(CR)	     User may specify one unit			   _____
					     number.

		TO UNITS: 1;2;3;4;5;6;7(CR)  User may specify up to 7 unit			  _________________
					     numbers, separated by
					     semicolons.

		FIRST INPUT BLOCK: 100(CR)   User may supply any legal				   _______
					     DECtape block number.

		FIRST OUTPUT BLOCK: 200(CR)  User may supply any legal				    _______
					     DECtape block number.


				      40



     Page			    Addition/Correction


     2-184	NUMBER OF BLOCKS TO COPY: 50(CR)					  ______
     (cont.)				     User may supply appropriate
					     number of blocks.

		VERIFY OUTPUT (YES=1, NO=0): 1(CR)					     _____

		0201 12-BIT WORDS PER BLOCK  Determined by program from
					     tape on input unit.

		The block length of all the specified tapes is checked. If
		any are found to be different from the input tape, the
		ILLEGAL FORMAT UNIT n error message is generated.
	
		When all specified copies have been finished, the tapes are
		rewound and the dialog continues:

		     DONE

		     REPEAT (YES=1,NO=0):

		If there are more tapes to be copied with the same set of
		specifications, they should be placed on the drives before
		typing 1 to repeat the previous operation. If a different
		set of specifications is desired, 0 should be typed to
		restart the dialog.
	
		Occasionally a TD8E drive will not stop fast enough after
		the tapes have been rewound and the end of the tape will
		spin off the reel. If this should happen, the drive may be
		stopped manually by setting it to OFF and stopping the reel
		by hand. This will not affect the validity of the copy. If
		the dialog does not continue properly after one or more
		tapes have spun off, the program may be restarted.

		In response to any question in the dialog, the user may
		type either CTRL/S to restart the dialog at REPEAT (YES=1,
		NO=0) or CTRL/C to exit the monitor. Either CTRL/S or
		CTRL/C may also be typed during a small amount of further
		motion. If CTRL/S is typed during the dialog the response
		to the REPEAT question should be NO; this option is mainly
		for cases where a complete set of specifications is already
		available.

		(CTRL/ characters are typed by holding the CONTROL key
		down while typing the character. The procedure is similar
		to that used with the SHIFT key on a typewriter. CTRL/
		characters are not echoed (printed).)

		A special case of the dialog allows the entire input tape
		to be copied onto the output tape with a minimum of effort.
		This case eliminates the need to specify the starting block
		numbers and number of blocks to copy. In this case, the

				      41



     Page			    Addition/Correction


     2-184	answer to FIRST INPUT BLOCK: is only a carriage return. The
     (cont.)	shortened dialog will be as follows:

		     TD8E COPY
		     FROM UNIT: 0(CR)				_____
		     TO UNITS: 1;2;3;4;5;6;7(CR)			       _________________
		     FIRST INPUT BLOCK: (CR)					____
		     VERIFY OUTPUT (YES=1, NO=0): 1(CR)						  _____
		     0201 12-BIT WORDS PER BLOCK

		The preceding sample dialog will cause the entire tape on
		unit 0 to be copied onto the other 7 tapes and verified.

		ERROR MESSAGES

		ILLEGAL RESPONSE	The user's response to the dialog
					was not correct; for example, an
					alphabetic character was typed or
					carriage return was typed before
					an octal number was given where	one
					was required. The questions will be
					restated and any previous answer
					ignored. Nothing should be typed
					until the terminal has stopped
					printing.

		SELECT ERROR UNIT n	During attempted data transfer,
					unit n was not found. The program
					waits for the user to correct the
					cause of the error. The user should
					check to see that:

					   1. if unit n is an output drive,
					      it is set to WRITE ENABLE.
					   2. unit n is set to REMOTE.
					   3. there is only one unit n.
					   4. all units are set to numbers
					      appropriate to their TD8E
					      internal wiring.

					When the cause of the error has
					been corrected, the user may type
					CTRL/R to resume transfer or he may
					type CTRL/S to restart the dialog.

		TAPE ERROR BLOCK x UNIT n
					During attempted transfer, a parity
					error or timing error was detected,
					or too great a block number was
					requested near block x on the tape
					on unit n. The tapes are rewound
					and the dialog is automatically

				      42



     Page			    Addition/Correction


     2-184				restarted at DONE, REPEAT (YES=1,
     (cont.)				NO=0).

		VERIFY ERROR BLOCK x UNIT n
					The data on the input tape does not
					match the data which was written on
					the block x of the output tape on
					unit n.

					The user may type CTRL/R to ignore
					the error and continue with the
					transfer, CTRL/T to try the last
					transfer again and continue if the
					error does not recur, or CTRL/S to
					restart the dialog.

		ILLEGAL FORMAT UNIT n
					Either the number of words per
					block on unit n does not agree with
					the number of words per block on
					the input unit or, when the number
					of blocks on the tape was calculated
					from the block length of the input
					tape, the length was found to be
					illegal. The number of blocks
					is only calculated if the whole
					tape copy option is requested. In
					either case, when the error has
					been corrected, the user may type
					CTRL/R to check the formats of all
					tapes again and continue, or CTRL/S
					to restart the dialog.

		DETAILS OF OPERATION

		After the answers to the dialog have been stored, the
		following procedure is used:

		     1. The number of words per block is determined from
			the input tape. All output tapes are checked to see
			if they have the same format as the input tape. If
			the shortened dialog option was used, the number of
			blocks on the tape is determined using the formula:

			# of blocks=(636,160/(words per block+17))+2 (octal)

			or

			# of blocks=(212,080/(words per block+15))+2 (decimal)




				      43



     Page			    Addition/Correction


     2-184	     2. The response to the VERIFY question is checked. The
     (cont.)		copying loop is set up to verify or not, as was
			requested.

		     3. The loop is entered which copies the input tape,
			using the same set of specifications for each
			output tape.

			a. The buffers are filled from the input tape.
			b. All output tapes are written with the contents
			   of the buffers.
			c. If verification was requested, a separate set of
			   buffers is filled from the output tape and the
			   two sets of buffers are compared. If there are
			   any discrepancies a VERIFY ERROR has occurred.
			d. If more blocks remain to be copied, the loop is
			   entered again.

		     4. When all the specified blocks have been copied onto
			the output tapes, all the tapes are rewound.

		     5. The REPEAT option is offered.

		The number of fields to be used for buffer space is
		determined immediately after loading. As soon as the
		question has been answered, it is removed from the program.

		If the output tape is to be verified, each available field,
		including that part of field 0 not occupied by the program,
		is divided in half. The lower half is used as the input and
		output buffer; the upper half is used for verification. The
		output tape is read back into the upper half and the two
		halves are compared. If they are not identical a VERIFY
		ERROR has occurred.



















				      44





								  CHAPTER 3

						      ADDITIONS AND CHANGES



     Page			    Addition/Correction

     3-29	End-Of-File paragraph should read:

		End-Of-File
		PAUSE signals the assembler to stop processing the file
		being read. A PAUSE should only be used at the physical end
		of a file and with two or more segments of one program.
		When a PAUSE statement is reached, the remainder of the
		file is ignored and processing continues with the next
		input file. In such a case PAUSE must be present or a PH
		error will occur. The PAUSE pseudo-op is present mainly for
		compatibility with paper tape assemblers, and its use is
		optional.


     3-30	After the TEXT string example change the words "IF option"
		to "/F option".

		The second sentence in the second paragraph under
		"Suppressing the Listing" should read "XLIST may also be
		used with expression as an argument; a listing will be
		inhibited if the expression is not equal to zero, or
		allowed if the expression is equal to zero".


     3-31	Insert the following example just before the section
		entitled "Controlling Binary Output":

		     IFZERO	A<
		     .
		     .
		     (code)
		     .
		     .
		     > ...



     3-41	Under "Memory Reference Instructions" change "JSM" to "JMS".








				      45





								  CHAPTER 5

						      ADDITIONS AND CHANGES



     Page			    Addition/Correction


     5-22	Add the following note on RALF assembly at the end of the
		page:

		"RALF code that includes forward reference to the base page
		should employ pseudo-ops # and ' as the first character of
		the symbol; this permits RALF to generate symbols that do
		not conflict with programmer-generated symbols that are
		also on the base page. The # pseudo-op can also be used
		following FPP memory reference instructions to indicate
		use of the 2-word form of the instruction. Likewise, the '
		pseudo-op indicates use of the single-word direct form of
		the instruction.

































				      46




							          CHAPTER 6

						      ADDITIONS AND CHANGES


     Page			    Addition/Correction


     6-35	Randomize example (bottom of page) is incorrect.

		    1 PRINT "A"

		should be added as the first line.


     6-61	In the paragraph above the section entitled "File 
		Statements" change "PS/8" to "OS/8" and change the order 
		number of the manual to "DEC-S8-OSSMB-A-D".


     6-64	The last sentence in the first paragraph should read: the
		subsequent reading of numbers from the file in line number
		80 shows the use of a dummy argument (C) to compensate for
		the carriage return and line feed since they would otherwise
		be read as numeric data with a value of 0. Line 80 in the
		example should be: 80 INPUT #1:J,C.


     6-66	Add the following option designations (bottom of page):

		/C   In BCOMP, the /C option is used in conjunction with
		     the /K option to create a file that can be chained to
		     from a non-BASIC file. For example:

			.R BCOMP
		  	*EXAM.BA/C/K

		/V   In BCOMP, the /V option is used to obtain the current
		     version number of COMP, BLOAD, and BRTS. For example:

			.R BCOMP
			*EXAM.BA/V

		This causes the system to print at the console the current
		version numbers for BCOMP, BLOAD, and BRTS as part of the
		output of the file being compiled.


    6-69	Change the sentence preceding NOTES to:

		     In general, any departure from these procedures will
		     cause a CX error.

		Add the following to the List of CHAIN restrictions:

				      47



     Page			    Addition/Correction


     6-69	     3.  When chaining BASIC core image files, the program
     (cont.)		 being chained to must be on the system device.
			 This is a restriction of the USR CHAIN function.


     6-76	Under the title THE STRING ACCUMULATOR (SAC), and starting
		on line 4, delete the sentence:

		and the length of the string currently in the SAC is stored
		as a negative number in STRLEN.

		and insert the following:

		The SAC starts at location SAC in BRTS. The SAC is 80 words
		long and contains one 6-bit character per word. The length
		is stored as a negative number in SACLEN.


     6-83	In the middle of the page, delete:

		BRTS maintains links for FGET and FPUT on page 0 of field 0,
		providing convenient access to these frequently used
		routines.

			 Page 0
		       Link Name		 Routine Linked

			FGETL			   FFGET
			FPUTL			   FFPUT

     6-85	and insert the following:

		BRTS contains Page Zero literals used by the FGET and FPUT
		routines. These Page Zero literals can be found in the BRTS
		source listing. Page Zero literals reference the following
		routines. For more information on Page Zero literals, refer
		to the section on BRTS Subroutines.

		       Page Zero Link		 Routine

			  FNEGL			 FFNEG
			  FNORL			 FFNOR
			  FCLR			 FACCLR


		In the middle of the page under the title FLOATING POINT
		OPERATIONS, and in the second paragraph, delete:

		Page 0 links are maintained for negate, normalize, and
		clear.



				      48



     Page			    Addition/Correction


     6-85	      Page 0 Link 		 Routine
     (cont.)
			FNEGL 			 FFNEG
			FNORL 			 FFNOR
			FCLR 			 FACCLR

		At the bottom of the page before the title SUBROUTINE
		ARGPRE, insert the following:

		     Many routines are now addressed with Page Zero literals
		     that can be found in the BRTS source listing. Note that
		     explicit references to Page Zero pointers by name no
		     longer apply. The purpose is to shorten the size of the
		     BRTS symbol table.


     6-90	Towards the bottom half of the page, delete the section
		entitled SUBROUTINE BSW.


     6-108	In the example form for the CHAIN command (Table 6-1) the
		device and file name specification must be enclosed in
		quotation marks as follows:

		     CHAIN "dev:filename.ex"


     6-117	In Table 6-3 Run-Time Diagnostics after the CI diagnostic
		code, insert the following:

		CX Incompatible file extensions were used in BASIC CHAIN
		statement.


     6-118	At the bottom of the page following the first paragraph,
		delete the column entitled "Distributed on:"

		At the bottom of the page following the first paragraph,
		delete:

		     BASIC.BN   Binary for editor
		     BCOMP.BN   Compiler binary
		     BLOAD.BN   Loader binary
		     BRTS.BN    Run-time system binary (any PDP-8 or PDP-12)


     6-119	At the top of the page following BLOAD.SV, insert the
		following:

		     EABRTS.SV   KE8/EAE Version of Run-time System save
				 image


				      49



     Page			    Addition/Correction


     6-119	At the top of the page under the column entitled "Component"
     (cont.)	that describes BRTS.SV, delete:

		    (from BRTS.BN)

		In the middle of the page, delete:

		Making SAVE Images from Binary Files:
		To create SAVE images of each of the OS/8 BASIC binaries,
		perform the following OS/8 commands.

		and insert the following:

		Making SAVE Images from Binary Files:
		To create SAVE images for each of the OS/8 BASIC binaries,
		use the following BUILD procedure for OS/8 BASIC non-EAE.

		In the middle of the page delete:

		     1.  For the editor:

			  .R ABSLDR
			  *DEV:BASIC.BN$
			  .SAVE SYS:BASIC;3011

		and insert the following:

		     1.  For the editor:
	
			  .PAL BASIC
			  .LOAD BASIC
			  .SAVE SYS:BASIC;3211

		Towards the bottom of the page, delete:

		     2. For the compiler:

			  .R ABSLDR
			  *DEV:BCOMP.BN$
			  .SAVE SYS:BCOMP;7000

		and insert the following:

		     2. For the compiler:

			  .PAL BCOMP
			  .LOAD BCOMP
			  .SAVE SYS:BCOMP;7000


		at the bottom of the page, delete:


				      50



     Page			    Addition/Correction


     6-119	     3. For the loader:
     (cont.)
			  .R ABSLDR
			  *DEV:BLOAD.BN$
			  .SAVE SYS:BLOAD;7605

		and insert the following:

		      3. For the loader:

			  .PAL BLOAD
			  .LOAD BLOAD
			  .SAVE SYS:BLOAD;7605

		At the bottom of the page, delete:

		     4. For the run-time system:

			  .R ABSLDR
			  *DEV:BRTS BN$ (without KE8/E EAE option)
			     or
			  *DEV:BRTS.BN,DEV:EAEOVR.BN$
					   (PDP-8/E, PDP-8M or
					   PDP-8F with KE-8E EAE)

		and insert the following:

		     4. For the run-time system:

			  .PAL BRTS/W
			  .LOAD BRTS
			  .SAVE SYS:BRTS 0-6777;7605
			  .SAVE SYS:BASIC.AF 3400-4577;7605
			  .SAVE SYS:BASIC.SF 12000-13177;7605
			  .SAVE SYS:BASIC.FF 13400-14577;7605

		Append the following at the end of the page

		Making SAVE Images from Binary Files:
		To create SAVE images of each of the OS/8 BASIC binaries,
		use the following BUILD procedure for OS/8 BASIC EAE.

		     1. For the editor:

			  .R PAL8
			  *DEV:BASIC.BN<DEV:BASIC.PA
			  .R ABSLDR
			  *DEV:BASIC.BN$
			  .SAVE SYS:BASIC;3211

		     2. For the compiler:


				      51



     Page			    Addition/Correction


     6-119		  .R PAL8
     (cont.)		  *DEV:BCOMP.BN<DEV:BCOMP.PA
			  .R ABSLDR
			  *DEV:BCOMP.BN$
			  .SAVE SYS:BCOMP;7000

		     3. For the loader:

			  .R PAL8
			  *DEV:BLOAD.BN<DEV:BLOAD.PA
			  .R ABSLDR
			  *DEV:BLOAD.BN$
			  .SAVE SYS:BLOAD;7605

		     4. For the run-time system:

			  .R PAL8
			  *DEV:EARBRTS.BN<TTY:,SYS:BRTS.PA/W
			     (pause)
			  EAE=1
			  ^Z
			     (pause)
			  ^Z
			  .R ABSLDR
			  *DEV:EABRTS.BN$
			  .SAVE SYS:BRTS 0-6777;7605
			  .SAVE SYS:BASIC.AF 3400-4577;7605
			  .SAVE SYS:BASIC.SF 12000-13177;7605
			  .SAVE SYS:BASIC.FF 13400-14577;7605


     6-120 	At the top of the page on lines 1,2,3, and 4, append the
		following:

		     ;7605

		In the middle of the page under the column entitled "Name",
		delete all the .03 extensions and replace them with the
		following extension:

		     .PA

		In the middle of the page, following "The OS/8 BASIC
		sources are named as follows": delete "NAME.MM" and the
		sentence "where MM represents the version number."

		At the bottom half of the page change the .03 extensions on
		the input files to .PA.





				      52



     Page			    Addition/Correction


     6-121	At the top of the page, delete:

		To assemble for PDP-12, PDP-8, PDP-8/I or PDP-8/L, or
		PDP-8E without EAE, create a source file named NOEAE.PA
		with EDIT that works as follows:

		     EAE=0
		     PAUSE

		Then

		     .R PAL8
		     *DEV:BRTS.BN<DEV:NOEAE,DEV:BRTS.03/K

		To assemble the run-time system overlay for PDP-8E, PDP-8F
		or PDP-8/M with KE-8/E EAE option, prepare a file called
		EAE.PA that looks as follows:

		     EAE=1
		     PDP8E=1
		     PAUSE

		Then:

		     .R PAL8
		     *DEV:EAEOVR.BN<DEV:EAE,DEV:BRTS.03/K

		and insert the following:

		To assemble for PDP-12, PDP-8, PDP-8/I or PDP-8/L, or
		PDP-8E without EAE, type the following command:

		     .R PAL8
		     *DEV:BRTS.BN<DEV:BRTS.PA/W

		In the example command lines for PILLOW, change the
		extensions ".03" to ".PA".


     6-126	In the list of addresses, change "01566/**** 3541" to
		"01566/**** 3542" and change "01567 /**** 3521"
		to "01567 /**** 3522".


     6-127	In command line 11 (top of page), change "ADH(N)" to
		"ADC(N)".







				      53






								  CHAPTER 7

						      ADDITIONS AND CHANGES


     Page			    Addition/Correction


     7-1	After "Calling and Using the OS/8 FORTRAN Compiler", insert
		the following:

		Before calling the FORTRAN compiler, make sure that LIB8.RL
		is on the system device.


     7-13	In the paragraph "Zero raised to a power..." change the
		sentence "A negative number..." to read as follows:

		A negative number raised to a floating point power causes
		an error message and uses the absolute value; calculation
		continues.


     7-18	Change the example of an implied DO LOOP from
		"WRITE (1,100)I,(A(J,I)J=1,3)" to
		"WRITE (1,100)I,(A(J,I),J=1,3)".


     7-44	In the section on "DECTAPE I/O ROUTINES", add a note that
		the RTAPE and WTAPE are for TC08 DECtapes only.























				      54






								  CHAPTER 8

						      ADDITIONS AND CHANGES


     Page			    Addition/Correction



     8-10	In the paragraph after the example command line, change
		"(terminated by a carriage return)" to "(terminated by a
		carriage return or altmode)".


     8-29	Add the following to Table 8-6:

		EX   The symbol is referenced but not defined.

		ME   Multiple Entry. The symbol is multiply defined.

		MS   Multiple Section. A section is multiply defined.

		*    The symbol is referenced illegally. Generally this
		     symbol is an overlay and is either referenced as data
		     from another overlay (only CALL references are allowed)
		     or called from the same or a higher-number overlay
		     level, violating the overlay rules defined on page 8-22.


     8-37	Add the following restriction to the first paragraph
		(concerning error traceback):

		When a statement is reached through any form of GOTO, the
		line number for error traceback is not reset. Thus, an
		error in such a line will give the number of the last
		executed line in the error traceback.


     8-62	In the section "NCHANL =", change "(8 images)" to
		"(FUNCTN=8)".


     8-66	In the example FORTRAN IV Coding Form, change "TYPE 105,I"
		to "WRITE (4,105)I".


     8-80	In the second paragraph, change "An integer variable which
		... " to "A variable that ...".


     8-81	Change the first two lines of the section "Computed GO TO
		Statement" to read:

				      55



     Page			    Addition/Correction

     8-81	Form GO TO(nl,n2,...., nK),e
     (cont.)
     		     A comma must follow the right parenthesis.


     8-83	Add the following information to the section entitled
		"Arithmetic IF Statement":

		Logical expressions may be used in an arithmetic IF
		statement. In such a case, the logical expression is first
		converted to an integer.


     8-88	At the top of the page in the section on PAUSE STATEMENT,
		under Effect, change the second sentence as follows:

		Execution is suspended until the user types a character on
		the console.


     8-91	Change	"FORMAT (F7.2,3(12,2(13,E9.3)17))" to
			"FORMAT (F7.2,3(I2,2(13,E9.3),17))"


     8-98	In the last example on the page, note that the first
		character output after the colon is a "space".


     8-100	Lower third of page, change "Where a is an integer constant
		or variable name that is ..." to "Where a is an integer
		constant or integer variable..".


     8-106	In the first full paragraph, which begins "A direct access
		WRITE statement ...", add the following sentence before the
		words "For example:": "This means minimum record size is
		one block."

		In the first example, change "WRITE(8)X" to "WRITE(6)X".


     8-107	Change all references (under FORTRAN) to the maximum size
		of ARRAYS from "4096" to "4095".


     8-112	Under the section entitled "THE DATA STATEMENT", change
		"DATA var list1/val list1/var list2/val list2/, ..." to
		"DATA var list1/val list1/,var list2/val list2/, ...".


		Change the second paragraph from the bottom to read:



				      56



     Page			    Addition/Correction


     8-112	Elements in the variable list may be either single
     (cont.)	subscripted or unsubscripted variables, or the name of an
		entire array.


     8-113	Change example line "DATA A(1),A(2),A(3),/3*0./" to
		"DATA A(1),A(2),A(3)/3*0./"


     8-125	The middle paragraph, which begins "PDP-12 users ..."
		should be changed to begin "PDP-8 and PDP-12 users ...".


     8-127	In the example at the top of the page, after "LVL OVLY
		LENGTH", change "0 00 10270" to "0 00 10371 ".


     8-129	After the second sentence, insert the following:

		A minimum of 12K of memory is required for the plotting
		routines.


     8-138	In the description for "L" under the subject CALL PSCALE
		(A,L,N,I), change "greater than or equal to 1" to:

		      ... greater than or equal to 2.


























				      57





							     APPENDICES E-H

						      ADDITIONS AND CHANGES


     Page			    Addition/Correction



     E-10	Insert the following message after the CORE? message:

		     CX BCOMP    Incompatible file extensions were used in
				 BASIC CHAIN statement.


     E-31	After the error message "SL" add the following:

		     ?SLOTS BUILD    More than 8 groups of non-system
				     handlers have been inserted.


     F-1	Add the following to the table:

		.CM Indirect file used by CCL.


     G-4	Insert the following sentence at the end of the paragraph
		in the section entitled "MAGNETIC TAPE".

		Normal use of magnetic tape by OS/8 V3 involves reading and
		writing records of 128 words.

		At the end of page, insert the following information:

		     NULL HANDLER

		The NULL handler is included in the source of RF, the
		nonsystem RF08 handler, only because there was extra room
		there. It has nothing to do with RF08's. These handlers
		share space since there is a limitation on the number of
		handler slots available in OS/8. NULL is very useful when
		debugging a program with voluminous output which you do not
		need. On output, NULL ignores data sent to it. On input,
		NULL returns an immediate end-of-file.



     H-1	In the table under program, change "POTP" to "FOTP".






				      58



     Page			    Addition/Correction


     H-2	Add to the table:

		     HANDLERS   Run RESORC with the /E option.

		     BCOMP 	/V to .R BCOMP

		     BLOAD 	/V to .R BCOMP

		     BRTS 	/V to .R BCOMP












































				      59





								 APPENDIX I

							     RXCOPY PROGRAM

     The RXCOPY program is used to copy or transfer the entire contents and
     system head of one RX floppy disk to another RX floppy disk. This
     program can be used only with RX permanent device names or a user
     defined name that has been assigned to an RX device. Specification of
     filenames in the I/0 specification line results in an error message
     and, therefore, is not permitted.

     The following command and I/0 specification line will load and run
     RXCOPY under OS/8:

	  .R RXCOPY	  _
	  *output dev:<input dev:/options	  _

     Example:

	  .R RXCOPY	  _
	  *RXA1:<SYS:	  _

     When RXCOPY is loaded and the I/O specification line is entered at the
     keyboard, the input device is copied to the output device on a sector
     by sector basis. When the operation is complete, the Monitor dot is
     printed on the screen and the specified output device becomes an exact
     duplicate of the input device.

     Table I-1 lists the options available for use with the RXCOPY program.
     These options modify the RXCOPY operation.


			   Table 1-1  RXCOPY Options
     ----------------------------------------------------------------------
     |  Option  |			Meaning				  |
     |----------|---------------------------------------------------------|
     |	  /P	| Pause and wait for user response before and after 	  |
     |		| execution of RXCOPY program.				  |
     |----------|---------------------------------------------------------|
     |	  /N	| Copy the contents of one device to another but don't 	  |
     |		| check them for identical contents unless otherwise 	  |
     |		| specified.						  |
     |----------|---------------------------------------------------------|
     |	  /M	| Check both devices for identical contents and list the  |
     |		| tracks and sectors that do not match but do not perform |
     |		| a transfer unless otherwise specified.		  |
     |----------|---------------------------------------------------------|
     |	  /R	| Read every block on the specified device and list the   |
     |		| bad tracks and sectors but do not perform a transfer 	  |
     |		| unless otherwise specified.				  |
     |----------|---------------------------------------------------------|
     |	  /V	| Print the current version number of the RXCOPY program. |
     ----------------------------------------------------------------------

				      60



     If no options are specified, RXCOPY assumes both the /N and /M
     options.

     If an error occurs during the execution of RXCOPY, the current job is
     aborted and control returns to the Monitor.

     Table I-2 lists the RXCOPY error messages and their meanings.


		       Table I-2  RXCOPY Error Messages
     ----------------------------------------------------------------------
     |     Message       |		     Meaning			  |
     |-------------------|------------------------------------------------|
     | NO INPUT DEVICE	 | No input device is specified.
     |-------------------|------------------------------------------------|
     | CAN'T LOAD INPUT  | The name of the input device specified in the
     | DEVICE 		 | command line is not a permanent device name.
     |-------------------|------------------------------------------------|
     | CAN'T LOAD OUTPUT | The name of the output device specified in the |
     | DEVICE		 | command line is not a permanent device name.   |
     |-------------------|------------------------------------------------|
     | COMPARE ERROR	 | When using the /M option all the areas that do |
     |			 | not match are printed as COMPARE ERRORS. Since |
     |			 | this is an non-fatal error, the RXCOPY 	  |
     |			 | operation continues.				  |
     |-------------------|------------------------------------------------|
     | INPUT DEVICE READ | Bad input, bad tracks or sectors. Since this   |
     | ERROR		 | is an non-fatal error, the RXCOPY operation 	  |
     |			 | continues.					  |
     |-------------------|------------------------------------------------|	
     | OUTPUT DEVICE 	 | Bad data on output device, tracks and sectors  |
     | READ ERROR	 | bad. Since this is an non-fatal error, the 	  |
     |			 | RXCOPY operation continues.			  |
     |-------------------|------------------------------------------------|
     | OUTPUT DEVICE 	 | Fatal output error. Since this is an non-fatal |
     | WRITE ERROR	 | error, the RXCOPY operation continues.	  |
     ----------------------------------------------------------------------



















				      61





								 APPENDIX J

								SET PROGRAM


     The SET program permits the operating characteristics of OS/8 to be
     modified, according to the attributes that are specified. The SET
     program is used to make frequently-required standard changes to system
     programs, especially I/O handlers. These changes are identified by
     specifying certain attributes in the SET command string which has the
     following format:

	  .R SET	  _
	  #SET device [NO] attribute [argument]	  _

     where:

	  SET		is the operation to be performed.

	  device	indicates the handler of the device you want
			modified.

	  [NO]		indicates that the attribute specified does not
			apply. [NO] cannot be used with every attribute.

	  attribute	is the characteristic to be modified. (See Table
			J-1.)

	  [argument]	is an optional parameter that the user must supply
			for certain SET commands. SET error messages are
			listed in Table J-2.


		       Table J-1  SET Command Attributes
     ----------------------------------------------------------------------
     |	 TTY	| Card   | Mag Tape |    SYS	 |  LPT    |  Any Device  |
     |		| Reader |	    |		 |	   |		  |
     |----------|--------|----------|------------|---------|--------------|
     | ARROW	| CODE n | PARITY x | INIT xxxxx | LA78    | FILES	  |
     | CODE n	|	 | FILES    | OS8	 | LA8A    | DVCODE	  |
     | COL n	|	 |	    | OS78	 | LC	   | LOCATION n=m |
     | ECHO	|	 |	    | 		 | LV8E    | READONLY	  |
     | ESCAPE	|	 |	    | 		 | WIDTH n | VERSION x	  |
     | FILL	|	 |	    |		 |	   | BLOCK b	  |
     | FLAG	|	 |	    |		 | 	   | 		  |
     | HEIGHT m |	 |	    |		 |	   |		  |
     | LC	|	 |	    |		 |	   |		  |
     | PAGE	|	 |	    |		 |	   |		  |
     | PAUSE n	|	 |	    |		 |	   |		  |
     | SCOPE	|	 |	    |		 |	   |		  |
     | TAB	|	 |	    |		 |	   |		  |
     | WIDTH n	|	 |	    |		 |	   |		  |
     ----------------------------------------------------------------------

				      62



			 Table J-2  SET Error Messages
     ----------------------------------------------------------------------
     | ? SYNTAX ERROR							  |
     |	    Incorrect format used in SET command or NO specified when not |
     |	    allowed.							  |
     |									  |
     | ? UNKNOWN ATTRIBUTE FOR DEVICE dev				  |
     |	    An illegal attribute was specified for the given device.	  |
     |									  |
     | ? CAN'T - DEVICE IS RESIDENT					  |
     |	    No modifications are allowed to the system handler.		  |
     |									  |
     | ? CAN'T - OBSOLETE HANDLER					  |
     |	    The handler has an old version number.			  |
     |									  |
     | ? CAN'T - UNKNOWN VERSION OF THIS HANDLER			  |
     |	    The version of the handler is not one recognized, possibly 	  |
     |	    because it is a newer version.				  |
     |									  |
     | ? ILLEGAL WIDTH							  |
     |	    A width of 0 or a width too large was specified, or for the   |
     |	    TTY, a width of 128 or one not a multiple of 8 was specified. |
     |									  |
     | ? NUMBER TOO BIG							  |
     |	    The number specified was out of range.			  |
     |									  |
     | ? CAN'T - DEVICE DOESN'T EXIST					  |
     |	    A nonexistent device was referenced.			  |
     |									  |
     | ? I/O ERROR ON SYS:						  |
     ----------------------------------------------------------------------


     J.1  TERMINAL ATTRIBUTES


     J.1.1  Arrow
     Specifying this attribute causes each control character typed by the
     KL8E handler to be printed in the form:

	   ^x

     where:

	   ^	indicates that a control character is being typed, and
	   x	specifies which control character is being typed (100+code
		for control character).

     Format:

	   .SET TTY [NO] ARROW	   _

     Example:

	   .SET TTY ARROW	   _

				      63



     If a CTRL/E character is typed, by the KL8E handler, an ^E is printed
     on the terminal. Note that ARROW is the default.

     Using this attribute with the NO modifier causes each control
     character typed by the KL8E handler to print with no modification.

     Example:

	  .SET TTY NO ARROW	  _

     Now if a CTRL/E character is typed by the KL8E handler, it will
     actually send a CTRL/E (ASCII code 5) to the terminal. The result is
     that no character is printed.

				     NOTE
	      On some terminals, the arrow (^) is replaced by the
	      circumflex (^).


     J.1.2  CODE n
     where n is an octal number in the range

	   1 <= n <= 77

     This command changes the internal IOT code for keyboard to n. The
     internal device code for the teleprinter is set to n+1. For example,
     if you have a VT05 hooked to your system with device codes of 40 and
     41, you would say SET TTY CODE 40. The NO restriction is not permitted.

     Example:

	   .SET TTY CODE=3	   _


     J.1.3  COLumn n
     Specifying this attribute changes the default number of columns used
     to print the directory (using the DIRECT command) to the decimal
     number you specify as n. The initial default number of columns is
     equal to one and the decimal number you specify should be in the range
     of 1-7.

     Format:

	   .SET TTY COL n	   _

     Example:

	   .SET TTY COL 3	   _

     Note that specification of this attribute does not actually change the
     behavior of the KL8E handler. Also, the NO modifier is not permitted
     to be used with this attribute.




				      64



     J.1.4  ECHO
     Specifying this attribute causes all TTY characters typed at the
     keyboard as input or received on the terminal as output to be printed.
     Specification of this attribute affects the KL8E handler only and not
     character echoing by the keyboard monitor.

     Format:

	   .SET TTY [NO] ECHO	   _

     Example:

	   .SET TTY ECHO	   _


     If it is desired that no character echoing take place, use the NO
     modifier in the command line. By specifying the NO modifier, all TTY
     characters on input or output are not printed and do not appear on the
     terminal screen.

     Example:

	   .SET TTY NO ECHO	   _


     J.1.5  ESCape
     Specifying this attribute causes the escape character (ASCII code 33)
     to print as a control character (see also ARROW attribute).

     Format:

	   .SET TTY [NO] ESC	   _

     Example:

	   .SET TTY ESC	   _

     Specifying the NO modifier, in the command line, causes escape to
     print as a dollar sign ($).

     Example:

	   .SET TTY NO ESC	   _

     Escapes can also be affected by the ARROW attribute. Specifying NO
     ARROW causes escapes to be sent to the terminal with no modification.
     This is useful for sending escape sequences to CRT terminal.


     J.1.6  FILL
     Specifying this attribute causes two fill characters to be typed
     following a tab. This attribute should only be used in conjunction
     with the TAB attribute.



				      65



     Format:

	   .SET TTY [NO] FILL	   _

     To remove these fill characters, use the NO modifier in the command
     line.

     Example:

	   .SET TTY NO FILL	   _


     J.1.7  FLAG
     Specifying this attribute causes the handler to flag lower case
     characters on output by printing them as upper case characters
     preceded by a quote.

     Format:

	   .SET TTY [NO] FLAG	   _

     Example:

	   .SET TTY FLAG	   _

     If it is desired to remove the quote preceding upper case characters,
     use the NO modifier in the command line.

     Example:

	   .SET TTY NO FLAG	   _


     J.1.8  HEIGHT m
     Specifying this attribute changes the number of lines that are printed
     on the terminal between pauses. Twenty-four lines is the default value
     of m.

     Format:

	   .SET TTY HEIGHT m	   _

     Example:

	   .SET TTY HEIGHT 12	   _

     This attribute has no meaning unless the PAUSE attribute is also
     specified.


     J.1.9  LC
     Specifying this attribute causes the KL8E handler to accept lower case
     characters on input.



				      66



     Format:

	   .SET TTY [NO] LC	   _

     Example:

	   .SET TTY LC	   _

     Specifying the NO modifier in the command line causes lower case
     characters on input to be converted to upper case.

     Example:

	   .SET TTY NO LC	   _


     J.1.10  PAGE
     Specifying this attribute adds both the CTRL/S and CTRL/Q features to
     the keyboard monitor.

     Format and example:

	   .SET TTY PAGE	   _

     When used with the NO modifier, this attribute removes the CTRL/S and
     CTRL/Q features.

     Example:

	   .SET TTY NO PAGE	   _

     For more detailed information on the control characters, see the OS/8
     Handbook.

     J.1.11  PAUSE n		   _
     Specifying this attribute sets the pause time between terminal output
     frames to the decimal number you specify as n. The exact time depends
     on the cycle time of your machine.

     Format:

	   .SET TTY PAUSE	   _

     Example:

	   .SET TTY PAUSE 5	   _

     If it is desired that no pause takes place, specify the NO modifier in
     the command line or specify zero as n.

     Example:

	   .SET TTY NO PAUSE	   _
     or
	   .SET TTY PAUSE 0	   _

				      67



     J.1.12  SCOPE
     Specifying this attribute causes characters that are erased via the
     rubout or delete key by the KL8E handler, key board monitor, and
     command decoder to physically disappear from the CRT screen. This
     attribute should not be specified if you do not have a CRT.

     Format and Example:

	   .SET TTY SCOPE	   _


     J.1.13  TAB
     Specifying this attribute causes the handler to print real tabs (ASCII
     code 211). This can only be used if your handler has the TAB feature.

     Format:

	   .SET TTY [NO] TAB	   _

     Example:

	   .SET TTY TAB	   _

     If your handler does not have the TAB feature, use the NO modifier in
     the command line. By specifying the NO modifier, all tabs are
     simulated as spaces.

     Example:

	   .SET TTY NO TAB	   _


     J.1.14  WIDTH n		   _
     Specifying this attribute changes the width of the terminal to the
     decimal number you specify as n. The decimal number you specify should
     be a multiple of eight and in the range of 1-255. However, n must not
     be 128. If your TTY handler does not have the tab feature, the width
     you specified in the command line may not be your final result. The NO
     modifier is not permitted to be used with this attribute. Placing an
     equal sign (=) between the attribute and the decimal number you
     specify is optional.

     Format:

	   .SET TTY WIDTH n	   _

     Example:

	   .SET TTY WIDTH 64	   _



     J.2  CARD READER ATTRIBUTES



				      68



     J.2.1  CODE n
     Specifying this attribute causes the card reader to use the card code
     you specify.

     Format:

	   .SET CDR CODE n	   _

     where:

	   n is a decimal number having a value of either 026 or 029.

     Example:

	   .SET CDR CODE 026	   _

     Note that the NO modifier is not permitted with this attribute.


     J.3  MAGNETIC TAPE ATTRIBUTES

     J.3.1  PARITY x	  	   _
     Specifying this attribute causes the parity check to be either even or
     odd.

     Format:

	   .SET MTxx:PARITY x	   _

     Example:

	   .SET MTA0:PARITY EVEN	   _

     Note that the NO modifier is not permitted with this attribute.


     J.3.2  FILES
     Specifying this attribute causes the handler not to issue an automatic
     rewind when referencing block 0.

     Format:

	   .SET MTxx [NO] FILES	   _

     Example:

	   .SET MTA1:FILE

     If it is desired that the automatic rewind take place when block 0 is
     referenced, use the NO modifier in the command line.

     Example:

	   .SET MTA0:NO FILES	   _


				      69



     J.4  SYSTEM ATTRIBUTES

     J.4.1  INITIAL xxxxx
     Specifying this attribute causes the system device to execute the
     command you specify as when the system is boot strapped. This command
     can contain a maximum of five characters excluding a RETURN key.

     Format:

	   .SET device INIT xxxxx	   _

     Example:

	   .SET SYS INIT HELP	   _

     If xxxxx is not specified, @INIT is assumed, and causes the system to
     execute the command in the file INIT.CM when bootstrapped. Note that
     the INIT.CM file must be created prior to bootstrapping.

     If it is desired that no special commands be executed at system
     bootstrap, use the NO modifier in the command line. By specifying the
     NO modifier, the system prints the monitor dot immediately after
     bootstrapping.

     Example:

	   .SET SYS NO INIT	   _

     If an initial command is specified and the system is bootstrapped,
     anything previously in memory is destroyed.


     J.4.2  OS8
     Specifying this attribute modifies the system handler to be OS/8.

     Format and example:

	   .SET SYS OS8	   _

     Note that the NO modifier is not permitted with this attribute.


     J.4.3  OS78
     Specifying this attribute modifies the system handler to be OS/78.

     Format and example:

	   .SET SYS OS78	   _

     Note that the NO modifier is not permitted with this attribute.






				      70



     J.5  LINE PRINTER ATTRIBUTES

     J.5.1  LA78
     Specifying this attribute modifies the LPSV handler to handle an LA78
     line printer.

     Format and example:

	   .SET LPT LA78	   _


     J.5.2  LA8A
     Specifying this attribute restores the LPSV handler to its original
     state.

     Format and example:

	   .SET LPT LA8A	   _


     J.5.3  LC
     Specifying this attribute causes the handler to print lower case
     characters. This attribute must only be used with line printers that
     have the physical ability to print lower case characters.

     Format:

	   .SET LPT: [NO] LC	   _

     Example:

	   .SET LPT: LC	   _

     Specifying the NO modifier in the command line converts lower case
     characters to upper case prior to printing.

     Example:

	   .SET LPT: NO LC	   _


     J.5.4  LV8E
     Specifying this attribute modifies the LPSV handler to work on an LV8E
     line printer.

     Format:

	   .SET LPT: [NO] LV8E	   _

     Example:

	   .SET LPT: LV8E	   _

     By specifying the NO modifier in the command line, this will work on
     an LP08 and LS8E line printer.

				      71



     Example:

	   .SET LPT: NO LV8E	   _


     J.5.5  WIDTH n
     Specifying this attribute sets the width of the line printer to the
     decimal number you specify as n.

     Format:

	   .SET LPT WIDTH n	   _

     where:

	   n is a decimal number in the range of 1-256

     Example:

	   .SET LPT WIDTH 80	   _

     Note that the NO modifier is not permitted with this attribute.


     1.6  ANY DEVICE ATTRIBUTES

     1.6.1  FILES
     Specifying this attribute causes the handler to handle a file-
     structured device.

     Format:

	   .SET device [NO] FILES	   _

     Example:

	   .SET MTA0: FILES	   _

     If it is desired that the handler handle non-file structured devices,
     use the NO modifier in the command line.

     Example:

	   .SET DTA1: NO FILES	   _

				     NOTE
	   This attribute remains in effect until the next time you
	   bootstrap, at which time the original status is restored.


     J.6.2  DVCode nn
     Specifying this attribute sets the IOT device code used by the handler
     to the decimal number you specify as nn. This number should be in the
     range of 30-77.


				      72



     Format:

	   .SET device DVC nn	   _

     Example:

	   .SET RXA0 DVC 64	   _

     This example could be used if your diskettes were hooked up to the
     non-standard device code of 64. Note that the NO modifier is not
     permitted with this attribute.


     J.6.3  LOCation n=m or LOCation n
     Specifying the first argument changes the contents of the location in
     the handler you specify as n to contain the value you specify as m.
     Both n and m are octal numbers.

     where:

	  n	is an octal number and must be in the range of 0-177 for
		one-page handlers and in the range of 0-377 for two-page
		handlers.
	  m	is an octal number and must be in the range of 0-7777.

     Format:

	   .SET device LOC n=m	   _

     Example:

	   .SET LPT LOC 37-1234	   _

     Specifying the second argument causes the system to print the current
     contents of the location in the handler you specify as n. This is then
     followed by a slash. The user can now enter a new value in that
     location by typing that value followed by a carriage return. If it is
     desired to leave the contents of that location unchanged, the user
     just types a carriage return.

     Format:

	   .SET device LOC n	   _

     Example:

	   .SET PTP LOC 144	   _


     1.6.4  READOnly
     Specifying this attribute causes the device specified to become a
     read-only device. Therefore, any output sent to this device causes an
     error message informing you that the output device is a read-only
     device.


				      73



     Format:

	   .SET device [NO] READO	   _

     Example:

	   .SET TTY READO	   _

     To remove the READONLY attribute, use the NO modifier in the command
     line.

     Example:

	   .SET TTY NO READO	   _

				     NOTE
	      The READONLY attribute remains in effect only until
	      the next time you bootstrap, at which time its original
	      status is restored.


     J.6.5 VERSION x		   _
     Specifying this attribute changes the version number of the handler to
     the letter you specify as x.

     Format:

	   .SET device VERSION x	   _

     Example:

	   .SET TV: VERSION G	   _

     Note that the NO modifier is not permitted with this attribute.


     J.6.6  BLOCK b, LOCation n=m or BLOCK b, LOC n
     Specifying the first attribute changes the contents of the location in
     the handler you specify as n that is located in the block you specify
     as b. The contents of that relative location is changed to the value
     you specify as m.

     where:

	  b	is an octal number
	  n	is an octal number and must be in the range of 0-177 for
		one-page handlers and in the range of 0-377 for two-page
		handlers
	  m	is an octal number and must be in the range of 0-7777.

     Format:

	   .SET device LOC n=m	   _



				      74



     Example:

	   .SET RKB1 LOC 10=2420	   _

     Specifying the second attribute causes the system to print the current
     contents of the location in the handler you specify as n that is
     located in the block you specify as b. This is then followed by a
     slash. The user can now enter a new value in that location by typing
     that value followed by a carriage return. If it is desired to leave
     the contents of that location unchanged, the user types a carriage
     return.

     Format:

	   .SET device LOC n	   _

     Example:

	   .SET LPT LOC 175	   _





































				      75





								 APPENDIX K

								      FUTIL
						  OS/8 FILE UTILITY PROGRAM


     FUTIL was originally developed by Jim Crapuchettes of Menlo Computer
     Associates, Inc., Menlo Park, CA. It is now included within the OS/8
     Extension Kit for the convenience of PDP-8 users.


     K.1  INTRODUCTION


     K.1.1  Description
     FUTIL enables a user to examine and modify the contents of mass
     storage devices. It is the only program currently available that can
     be used to patch programs containing overlays (F4/LOAD outputs). Other
     possible uses include examination and repair of OS/8 directories; bad
     block checking and correction; decimal/octal conversion of double
     precision numbers; output of the Core Control Block (CCB) of ".SV"
     files and the HEADER of ".LD" files; and the creation of special
     directories. Supporting these functions is signed double-precision
     arithmetic expression evaluation that can be used in the command
     syntax whenever a numeric value is needed.

     FUTIL's command set is divided into two groups of commands. The first
     group uses single letters to direct the program in the examination and
     modification of single words on the device specified. The second group
     of commands uses command words to direct the program in the dumping,
     listing, modifying and searching of the device on a block-by-block
     basis. Also included in this group is a series of commands to direct
     the program in some auxiliary functions including setting and
     resetting switches and variables within the program, showing current
     FUTIL parameters.

     Several examples are given in Section K.4. The first two examples,
     especially, are simple and well-documented to acquaint you with the
     features of FUTIL. You may want to look at them at this point to get a
     better understanding of the material that follows.


     K.1.2  Special Characters Used in This Appendix
     To help increase clarity, the characters single quote ('), double
     quote ("), angle brackets (< and >) and square brackets ([ and ])
     have been used to help separate special items from the words around
     them. The single quote character is used to surround a word-type
     command; for example, the 'FORMAT' option 'SET's up the format in
     which output is to be done. The double quote is used to surround an
     item whose actual name is being used; for example, the "RETURN" key is
     the key on the Teletype that has that word printed on it. The angle
     brackets are used to surround the name of a type of item (a syntactical
     type); for example, "<n>" means that a NUMERIC ITEM is to be used. The

				      76



     square brackets are used to surround optional items; for example,
     "w[ord] " would indicate that the characters "ord" may be supplied
     optionally.


     K.1.3  Special Characters Used in FUTIL
     Several characters, when keyed, cause immediate action from the
     program. Typing either CTRL/P (which prints "^P") or CTRL/C (which
     prints "^C") will immediately cause the program to stop whatever it is
     doing. CTRL/P then causes the program to go back to command input mode
     and wait for you, while CTRL/C calls the OS/8 Monitor (as it does with
     most system programs). CTRL/S and CTRL/Q control program execution
     (including all I/O). Typing CTRL/S at any time will cause the program
     to pause and wait for either CTRL/C, CTRL/P or CTRL/Q. Typing CTRL/Q
     will then allow program execution to resume. Any other characters
     entered at this point will be simply ignored. If a CTRL/Q is typed by
     itself at any time, it is simply ignored.

				     NOTE
	      CTRL/S and CTRL/Q are active at all times, not just
	      during console output. The result is that both input
	      from the console and program execution with no con-
	      sole interaction (such as 'SCAN','WORD' and 'STRING'
	      command execution) can and will be paused and re-
	      started with these keys.

     During console terminal input, three other keys can be used to help
     with editing the input string of characters. These keys are RUBOUT,
     CTRL/U (which prints "^U") and CTRL/R (which prints "^R"). The action
     of RUBOUT and CTRL/U is exactly the same as it is for the OS/8 Monitor
     and Command Decoder (including usage of "scope mode" operation to
     change the action of the RUBOUT key from echoing the rubbed out
     characters between back slashes to erasing the characters from the
     screen). The action of CTRL/R is the same as that of the LINE-FEED key
     for the Monitor and Command Decoder.

     For those users with upper-lower case terminals, the program
     translates all lower case characters received from the keyboard to
     upper case. The characters are echoed and handled internally as upper
     case characters. While this makes use easier, it does not allow any
     lower-case characters to be input directly. In those cases where
     lower-case codes are needed in the modification of a file, either use
     the codes directly or use a text editor. Note that this translation
     occurs only on input. Lower case characters in a file will be printed
     to the best ability of the output device. This may produce incorrect
     results on upper-lower case line printers.

     All of the commands are taken in context, that is, many of the
     characters which are used in the single character command set will
     not be considered to be commands if they are included in a line which
     begins with a command word or if they are embedded within expressions.

     The carriage-return ("RETURN") always starts command execution, and is
     the terminator for all word-type command lines.


				      77



     K.1.4  Running FUTIL
     FUTIL is run using the OS/8 Monitor command "R FUTIL" (or "RU
     dev:FUTIL").

     When started, FUTIL is set up to access the system device, the 'ERROR'
     message output mode is set to 'LONG', the access 'MODE' is set to
     'NORMAL' and no file is known. To access some other device, give the
     command 'SET DEVICE dev'. To set the 'ERROR' mode to 'SHORT', give the
     command 'SET ERROR SHORT'. To use some other access mode, give a 'SET
     MODE <mode>' command with a <mode> of 'LOAD', 'OFFSET' or 'SAVE'. When
     in 'OFFSET' mode, the 'OFFSET' to be used can be specified by the
     command 'SET OFFSET nnnn'. Lastly, a file lookup can be performed by
     giving a 'FILE' command (with three default extensions).


     K.1.5  Access Method
     The program accesses the OS/8 device one OS/8 block (256 words) at a
     time. For every location specified, the real block and word are
     determined and compared with the current block in memory. If the
     desired block and current block are not the same, the
     <something-changed> flag is checked to see if anything has been
     changed in the current block. If nothing has been changed, the new
     block is read in. If something has been changed, the current (modified)
     block is first written out and then the new block is read in. This
     action happens correctly even when the access mode is changed because
     it is done at the level of the OS/8 block number right before calling
     the current 'DEVICE' handler. The status of the <something-changed>
     flag can be determined by simply 'SHOW'ing 'ABS', 'REL' or 'ODT'
     locations. If the flag is set, the word "MOD" will be output following
     location information.

     The contents of the OS/8 device are therefore not changed unless the
     block in which changes are made is written out either implicitly, as
     described above, or explicitly, using the 'WRITE' command (which is
     discussed near the end of the section on word-type commands). The
     result is that typing CTRL/C before writing out the current block
     (assuming it has been modified) will return to the Monitor without
     actually modifying the contents of the device itself. Note, also, that
     only one implicit write attempt is ever made by the program. Should an
     error occur when the write is attempted (for example, write-locked
     device), an explicit 'WRITE' command must be given to actually write
     out the block.

     If the words within some blocks are changed accidentally, the
     <something-changed> flag can be reset by using the 'SET' command to
     reset the 'DEVICE' (described further along in this writeup) to the
     same device currently being used. This will reset the
     <something-changed> flag, the current block in memory, and the file
     start block and core control-block/header-block (if they had been set
     by a 'FILE' command). The resetting of the current block in memory
     will cause the next access to the device to read in the block desired.
     The resetting of the file information will require a new 'FILE'
     command to be given to set it back up. If you can't remember what is
     the current setting of the 'DEVICE', use 'SHOW DEVICE' first and then
     'SET' it the same.

				      78



     Files stored on an OS/8 mass-storage device generally fall into one of
     four categories. The program has four corresponding modes for
     accessing the device. The current 'MODE' of the program can be set by
     the 'SET' command or by chaining (as described previously) and
     examined by the 'SHOW' command (to be described later).

     The four categories and their corresponding modes are:

	  1.  General (binary, ASCII and data) files - 'NORMAL' mode
	  2.  Core image (save) files - 'SAVE' mode
	  3.  FORTRAN IV load modules - 'LOAD' mode
	  4.  System overlays - 'OFFSET' mode

     The actual operation of the program for each of these modes is as
     follows:

	 'NORMAL'	The high order 7 bits of the 15 bit address are
			added to the current block number to get the actual
			block number. The low 8 bits of the 15 bit address
			are used to specify the desired word within that
			block.

	 'SAVE'		The file to be examined must be set up by a 'FILE'
			command. "Block" numbers are used to specify an
			overlay number (future MACREL/LINK support) and
			must be exactly zero ("0") for files without
			overlays (generated by the monitor "SAVE" command).
			The core segment data (pages and fields) from the
			file's CCB (core-control-block) is used to
			determine where on the device the desired word is
			to be found. This is done by first determining the
			correct block from the file's CCB and then using
			the low 8 bits of the address to specify the
			desired word within that block. Specifying a
			nonexistent address or overlay for one of the
			single-character (ODT) commands will cause an error.
			Specifying a nonexistent address or overlay for any
			of the word-type commands will cause the program to
			ignore the address and access no data.

	 'LOAD'		The file to be examined must be set up by a 'FILE'
			command. Block number specifications are actually
			taken as FORTRAN IV overlay specifications and must
			be contained within the file. The information from
			the OIT (overlay-information-table) in the header
			block of the file is used to determine where on the
			device the desired word is to be found. Nonexistent
			addresses are handled the same way as for 'SAVE'
			mode.

					NOTE
		Because the "block" part of the location specification
		changes definition depending on the mode in use, it is
 		recommended that the first operation following a switch
		to 'SAVE' or 'LOAD' mode explicitly specify a "block"

				      79



		part of 0. Otherwise a previously specified "block" part
		will be taken to mean a non-existent overlay number,
		causing an error.

	 'OFFSET'	The 12-bit 'OFFSET' (which is set by the 'SET'
			command and examined by the 'SHOW' command) is
			subtracted from the low order 12 bits of the
			address and then the same arithmetic as with the
			'NORMAL' mode is used. This mode is used mostly
			with system overlays whose start block number and
			actual loading address is known. By setting the
			'OFFSET' to the loading address (which can only be
			a 12 bit number), the 12 bit "actual" addresses of
			the overlay can be used.

     The 'SAVE' and 'LOAD' modes are mentioned together throughout this
     appendix as MAPPED modes because their method of address translation
     uses a descriptor block from the file of interest to control access to
     the file in a noncontiguous manner.


				     NOTE
	     For all access modes, the OS/8 "actual" block number
	     for the block to be read is stored (for display) in the
	     computer MQ register (if present). The value is stored
	     before checking if the current block needs to be written.
	     It is particularly useful for following the progress of the
	     'SCAN' command.


     K.1.6  Referencing Words on the Device
     The words on the OS/8 device are referenced by their location> (often
     abbreviated as <l>). This <location> consists of an optional <block>
     or <overlay> number (which must be followed by a "." if present), and
     an <address> or <displacement>. The <block>/<overlay> number is a
     12-bit number which must be in the range 0 thru 7776 (octal), or 4094
     (decimal). Block number 7777 (or 4095, decimal) does not exist under
     OS/8, and the program will ignore this number. The <overlay> number is
     further limited to the number of overlays at a given address. Whenever
     the <block>/<overlay> part of the <location> is not used, the program
     will use the last specified value. The <address>/<displacement> is a
     15 bit number (5 octal digits), but leading 0's need not be specified.
     Thus, the forms and their corresponding examples are as follows:

		Form			Example

	<block>.<displacement>		1201.37524

	<overlay>.<address>		3.57633

	<address>			15721

	<displacement>			223



				      80



				    CAUTION
	    Neither this program nor the OS/8 device handlers gener-
	    ally include checking for legal block numbers! It is
	    simply assumed that all accesses to the device will be
	    done after checking with the directory for legal file
	    start blocks and lengths, which is the normal mode of
	    operation under OS/8. This can have very interesting re-
	    sults with this program; for example, the RK8/E
	    handler, given a block number greater than 6257 (octal)
	    on device RKA0, will simply continue on into device
	    RKB0.

     For the rest of this document, unless otherwise stated, block will
     mean <block> or <overlay> and address will mean <address> or
     <displacement>, depending on usage. Therefore the definition will be:

 	  [block.] address=<location>=<1>

     Since these location references are numeric input, all of the
     characteristics described next can also be used when specifying
     locations.


     K.1.7  Numeric Items (Or Numbers)
     Two "switches" are used by the program to allow the input of either
     octal, decimal or mixed numeric input where ever numeric input is
     used. Each new command line always resets the input mode to octal. The
     character CTRL/D (printed as "^D") switches the input mode for any
     following input to decimal. The character CTRL/K (printed as "^K")
     switches the input mode back to octal. These two switches may be
     located anywhere in numeric input.

     For example, when inputting a string of numbers, the input would be
     alternately decimal and octal if it were

	  ^D100,^K100,^D200,^K200,^D300,K300

     Two other characters, the double quote (") and apostrophe ('), may be
     used for numeric input. The double quote functions the same way in
     this program as it does in PAL8 in that the 8-bit ASCII value of the
     following character is used as a number. As with all character input,
     the special characters described earlier cannot be used. The
     apostrophe functions in a way similar to the way that the "TEXT"
     pseudo-op operates in PAL8 in that the following two characters are
     masked to 6-bits each and packed into a 12-bit word. There must always
     be exactly two characters following the single quote. If it is
     desired to pack one half of the word with a 6-bit 00, use the
     character "@". For example, a string equivalent to the file-name
     "PIP.SV" would be represented by the string

	  'PI,'P@,0,'SV

     Expressions may also be used for numeric input when enclosed in
     parentheses. The parentheses pair "( and )" must surround the
     expression. When this is so, all the options of the 'EVAL' command are

				      81



     available for numeric input. For example, the contents of the switch
     register can be used for a number by the expression "(S)", or the
     current block number +5 could be used by the expression "(B+5)". See
     the discussion of the 'EVAL' command for the other options available.


				     NOTE
	      The opening and closing parentheses must completely
	      surround the expression. Neither digits nor the switch
	      characters may be outside of the parentheses or an error
	      will result. This is required because many of the non
	      alphabetic characters have multiple meanings (com-
	      mands or operators) so the use of the parentheses pair
	      "(...)" provides the necessary context to remove
	      ambiguity


     K.1.8  Errors (And Error Messages)
     Whenever the program recognizes an error of some type, it outputs an
     error message to inform you what went wrong. The message tells both
     what went wrong and where in the command line the error was made.
     Depending on the setting of the 'ERROR' mode switch, either 'SHORT' or
     'LONG' messages are output.

     The error messages have the forms:

	  "?<ee> at <cc><error message>"  	-'LONG'

     or

	  "?<ee> at <cc>"  			-'SHORT'

     where <ee> is the error code, <cc> is the number of the column in the
     command line where the program stopped scanning and <error message> is
     the message itself. There are currently 45 error conditions with
     corresponding codes and messages to assist the user of this program.
     The error codes and their messages can be printed out by the 'SHOW'
     'ERRORS' command. The 'ERROR' mode is set by the 'SET' command.

     The error messages are swapped with the USR, but not in the normal
     manner, allowing write locked startup with the loss of the message
     text (see the section on program execution for more information).


     K.2  SINGLE CHARACTER (ODT-LIKE) COMMANDS
     These commands allow the examination and modification of words on an
     OS/8 device in the same way that ODT allows the examination and
     modification of the memory in the computer.

     In all of the following commands where <n> a numeric item is
     specified, the operation of "closing" the location is to place the
     value of <n> into the word if it is open. If the current location is
     not open, or if <n> is not specified, no change takes place. Refer to
     the "Introduction to Programming" and the OS/8 Handbook section on ODT
     for more information if needed. Note that (as mentioned previously)

				      82



     "[<n>]" with the following commands means that a numeric item may be
     optionally supplied.

	<l>/			Open and output the contents of location
				<l> in the current 'OUTPUT' mode.

	/			Reopen the last location opened by one of
				these commands and output its contents in
				the current 'OUTPUT' mode.

	[<n>]#			Close the current location, reopen it and
				output its contents in 'BCD' (3 digit
				binary coded decimal).

	[<n>]$			Close the current location, reopen it and
	(dollar sign)		output its contents in 'OS/8' ASCII.

	[<n>]%			Close the current location, reopen it and
				output its contents in 'BYTE' octal (8 bits
				with OS/8 packing).

	[<n>]&			Close the current location, reopen it and
				output its contents in 'XS240' format
				packed ASCII.

	[<n>]:			Close the current location, reopen it and
				output its contents in 'SIGNED' decimal.

	[<n>]<			Close the current location, reopen it and
				output its contents in 'OCTAL'.

	[<n>]=			Close the current location, reopen it and
				output its contents in 'UNSIGNED' decimal.

	[<n>]>			Close the current location, reopen it and
				output its contents in 'PDP' (symbolic).

	[<n>]?			Close the current location, reopen it and
				output its contents in 'DIRECTORY' format
				[negated DECIMAL, DATE (see "@" next) and
				PACKED (ASCII)].

	[<n>]@			Close the current location, reopen it and
				output its contents in 'DATE' format:
				dd-mmm-yy 2 digits each for the day and
				year and 3 alphabetic characters for the
				month (except for illegal month numbers,
				which are output as a space and 2 decimal
				digits).

	[<n>][			Close the current location, reopen it and
				output its contents in 'ASCII'.




				      83



	[<n>]\			Close the current location, reopen it and
				output its contents in 'FPP' (symbolic).

	[<n>]]			Close the current location, reopen it and
				output its contents in 'PACKED' ASCII.

	[<n>]$ 			Close the current location, reopen it and
	("ALTMODE" or		type its contents as specified by the
	"ESCAPE" key)		current 'FORMAT'.
	
	[<n>]<cr>		Close the current location.

	[<n>];			Close the current location and open the
				next sequential location. Neither address
				nor contents are output, but one space is
				echoed.


		  				  NOTE
				The ";" command can be used to advance
				through addresses without outputting their
				value in octal when some other format is
				really more helpful. For example, when
				examining a directory, the file name and
				extension can be output using the "]"
				command (PACKED ASCII), the date can be
				output using the "@" command and the file
				length can be output using the ":" command
				and all of this information can be made to
				appear on one line by simply using the ";"
				command to do the incrementing between each
				of the output commands. The result would
				look something like this:

				2.5/ 2317 ]SO;]UR;]CE;]PA;@30-AUG-72;:-0071

     For the following commands, the location of the newly opened word is
     output before the contents are output. This location is composed of
     the 12-bit block number (4 octal digits), a "." for a separator, and
     the 15 bit address (5 octal digits). This is immediately followed by
     "/" to separate the contents from the address.

	[<n>]<line feed>	Close the current location, open and output
				the contents of the next sequential
				location in the current 'OUTPUT' mode.

	[<n>]!			Close the current location, open and output
				the contents of the previous sequential
				location in the current 'OUTPUT' mode.

	[<n>]^ (circumflex	Close current location, open the location
	or up-arrow)		that would have been referenced if the
				contents were a PDP-8 memory reference
				instruction, and output the contents of the
				new location in the current 'OUTPUT' mode.

				      84



				Note: this command works like the stand-
				alone version of ODT, not like the OS/8
				version. Even if bit 3 of the word (the
				indirect bit of a PDP-8 instruction) is a
				1, this command will not do the equivalent
				of an indirect reference.

	[<n>]_ (backarrow	Close the current location, take its
	or underline)	  	contents as an address, open that location
				and print its contents in the current
				'OUTPUT' mode. This operates as an indirect
				address into the current field would. The
				field currently being examined (the high
				octal digit of the 5 digit location) will
				not be changed by this operation.

	<l>+			Open the location <l> locations forward
				from the current location and output its
				contents in the current 'OUTPUT' mode. 15
				bit arithmetic is used and the block part is
				ignored, so this will operate across field
				boundaries, i.e., within a 32K area.

	<l>-			Open the location <l> locations backward
				from the current location and output its
				contents in the current 'OUTPUT' mode. Same
				restrictions as with the '+' command.

     The "current 'OUTPUT' mode" has been mentioned several times above.
     The program will output the contents of a location either as a
     four-digit octal number, or as a four-digit octal number with two
     spaces and the "symbolic" representation ('PDP' or 'FPP') of the word.
     See the 'SET' and 'SHOW' commands as well as the following section.


     K.2.1  "Symbolic" Output Formats
     The "symbolic" typeout is in approximately the format that input to an
     assembler would need to be in order to generate the contents of the
     current location. It is assumed, of course, that these contents are
     either a PDP-8 or an FPP-12/8A instruction, depending on the output
     selected. If the word to be output is not an instruction, as is the
     case for the second word of all 2-word instructions (EAE and FPP), the
     decoding will obviously be meaningless.

     For PDP-8 instructions decoding into mnemonics is done for all memory
     reference instructions, for all legal operate instructions
     (including 8/E EAE instructions except for "SWAB"), for all 8/E
     processor, extended memory and memory parity IOTs, for teletype and
     high-speed paper-tape IOTs, for 8/E redundancy check option IOTs, for
     programmable real-time clock IOTs and for FPP IOTs. There are
     currently a total of 96 IOTs and space has been provided in the
     program for an additional 32 IOT codes and their mnemonics. These can
     be patched directly into the program using itself. The first word of
     each four-word entry is the exact IOT code (for example, 6221 for "CDF
     20"), followed by 3 words containing up to 6 packed ASCII characters

				      85



     padded with trailing 0's. No attempt is made to decode any micro-coded
     IOTs. Either an exact match for the current contents will be found in
     the table or the program will output "IOT nnnn where nnnn is the octal
     typeout of the low 9 bits of the code. The next free location in the
     table (which is in field 1) is pointed to by the contents of location
     10000. The table is terminated by the first 0 for an IOT code,
     so additions must be contiguous and added directly at the current end
     of the table.

     For FPP instructions, the full FPP-8/A instruction set is decoded
     except for "IMUL", which is actually an integer mode "LEA". For the
     data manipulation instructions, the op-code mnemonic is followed by a
     "#" for the long-indexed format, by a "%" for the indirect-indexed
     format and by a space for the base addressing format. For the indirect
     indexed and base addressing formats, the operand address is output as
     "B+nnn", where nnn is the 3 digit octal value of the displacement (3
     or 7 bits) multiplied by 3. These formats are those used by the RALF
     assembler. This is also true for "LEA" instructions (i.e., "LEAI" is
     decoded as "LEA%"). Both jump and load-truth instruction decoding is
     done as a single mnemonic whose last two characters indicate the
     specified condition. All instructions which use 2 words are decoded
     with an "*" in the location in the normal assembler format where the
     value of the second word would go. Index register number and "+" for
     auto-increment (if used) are also shown in the assembler format. Any
     combinations which are not in the FPP-8/A instruction definitions are
     output as "UNUSED".

				     NOTE
	    For both of these output formats, the use of the mapped
	    access modes (and the 'OFFSET' mode for PDP decoding)
	    allow the use of the "actual" addresses when decoding
	    the instruction.


     K.3  WORD-TYPE COMMANDS
     These commands are grouped by function, as follows:

     Group 1:
	  DUMP		type/list out the contents of one or more blocks.
	  LIST		type/list out the contents of one or more locations.
	  MODIFY	modify one or more locations.


     Group 2:
	  WORD		word search
	  STRING	string search
	  SMASK		set up string search mask

     Group 3:
	  SET		set up program switches & variables
	  SHOW		show settings of program switches & variables
	  FILE		look up file(s) on device
	  WRITE		write out current buffer
	  SCAN		scan for bad blocks
	  REWIND	move device to block 1 & reset directory segment

				      86



     Group 4:
	  OPEN		open an output file on a file-structured device
	  CLOSE		close the open output file

     Group 5:
	  IF		cause command skipping based on expression value
	  END		resume command execution after unsatisfied 'IF'
	  COMMENT	pass user commentary to output device
	  EXIT		exit to OS/8 (same as CTRL/C)

     Group 6:
	  EVAL		evaluate a signed, double-precision expression.

     Command words may always be abbreviated to their first two characters,
     as with the Monitor and BUILD, and some of the commands and their
     options may also be abbreviated to only one letter. When this is true,
     the command forms given will include the one-letter form, and the
     option forms will give the one-letter form directly under the full
     word form.

				     NOTE
	     In many cases, two or more words start with the same
	     letter. In these cases, only one of these words may be
	     abbreviated to one letter.

     The descriptions for each command include each of the possible forms
     of the command, with an example of that form following it on the same
     line.


     K.3.1  Output Formats
     The 'FORMAT' option is used to 'SET' up the output format for the "$"
     ('ALTMODE' or 'ESCAPE') command (single-character) described earlier
     and the default format for the 'DUMP', 'LIST' and 'MODIFY' commands
     described below. The syntax of this command is shown with the other
     'SET' commands but is described here to make the descriptions of the
     following three commands more understandable. The <format> may be one
     of the following:

	ASCII		output each word as a single ASCII character.
	A

	PACKED		Output each word as two 6-bit trimmed and packed
	P		ASCII characters. This is the format of PAL8 TEXT
			strings.

	OS		Output each word as 1 or 2 OS/8 packed ASCII
			characters. The even address words output 1
			character and the odd address words output 2
			characters.

	XS240		Output each word as two 6-bit packed ASCII
			characters by adding a space (240 octal) to the
			contents of each 6-bit byte. This is the format of
			PAL12 SIXBIT strings.

				      87



	BYTE		Output each word as 1 or 2 OS/8 packed bytes of 8
			bits each as a 3-digit octal numbers. The even
			address words output 1 number and the odd address
			words output 2 numbers.

	UNSIGNED	Output each word as an unsigned decimal number.
	U

	SIGNED		Output each word as a signed decimal number.
	S

	OCTAL		Output each word as a 4 digit octal number.
	O

	BCD		Output each word as 3 bcd digits. The digits 0
	B		through 9 are followed by ":" (10), ";" (11), "<"
			(12), "=" (13), ">" (14) and "?" (15).

	PDP		Output each word as an octal number, followed by 2
	FPP		spaces and its mnemonic representation, assuming it
			to be a PDP-8 or an FPP-8A instruction. See the
			"symbolic" output description.

	DIRECTORY	Output each word in octal, decimal (signed), date
			(see "@" command) and packed ASCII formats.

     The 'FORMAT' is initialized to 'PACKED' ASCII.

     The output from the 'DUMP' and 'LIST' commands for each of these
     formats is set up as follows:

	  1.  At the beginning of each line the current location is output
	      in <location> format with a 4 digit block number and a 5
	      digit address, both in octal, as

		   <block>.<address>:

	      For example, "1271.17205:"--location 17205(8) relative to
	      block 1271(8).

	  2.  The maximum number of words per line is set up as follows:

	      A.  The four character formats output 16 words per line with
		  no extra characters.
	      B.  The five numeric formats output 8 words per line with 2
		  spaces between each number.
	      C.  The "symbolic" and directory formats output 1 word per
		  line.

     For 'LIST' with A or B, the first line may be shorter than succeeding
     lines to force the second and following address outputs to be even
     multiples of 10 (octal).




				      88




     K.3.1.1  DUMP - The 'DUMP' command is used to output one or more whole
     256 word device blocks in the default or an optionally supplied
     format. This command has the following forms:

	  DUMP [<format>] <block string>

	  DUMP<block string>			DU 100,200-213,250
	  D <block string>			D (B)-(B+10),(S)
	  DUMP <format> <block string>		DU PA 212
	  D <format> <block string>		D OS 514

     where the optional <format> is one of those given for the 'FORMAT'
     option above, and the <block string> is one or more numeric items
     separated by ","s and "-"s. The "-" is used when it is desired to dump
     a group of blocks, and is used as

		    <start block>-<end block>

     the "," is used to separate single blocks or groups of blocks if there
     is more than one per line.

				     NOTE
		 When in a mapped ('SAVE' or 'LOAD') mode, the
		 'DUMP' command cannot dump any block except
		 the block containing location D. To eliminate
		 the confusion that this would produce, the
		 command will simply output an error message
		 reminding the user that the proper command to
		 use in a mapped mode is the 'LIST' command.


     The output from the 'DUMP' command is sent to the 'DDEV' ("dump"
     device), which can be either the console terminal, the line printer,
     or a file. See the 'SET' command for setting the "dump" device and
     output mode.


     K.3.1.2  LIST - The 'LIST' command is used to output the contents of
     one or more words on the device in the default or an optionally
     supplied format. This command has the following forms:

	  LIST [<format>] <location string>
	
	  LIST <location string>		LI 123.200-517,200.0
	  L <location string>			L 312.10-17,100-117,176
	  LIST <format> <location string>	LI UN 200-227
	  L <format> <location string>		L SI 200-277

     where the optional <format> is one of those given for the "FORMAT"
     option above, and the <location string> is one or more <location>s,
     separated by ","s. When it is desired to list a group of words, the
     "-" is used to separate the start and end addresses as

	  [<block>.] <start address>[-<end address>]

				      89



     If the block part is not specified, the last block number specified to
     the program will be used. If an end address is specified, the start
     address is assumed to be in the same field as the end address (i.e.
     the highest octal digit of the 5-digit address), so a maximum of 4096
     words can be specified by each group.

     As with the 'DUMP' command, the output from the 'LIST' command is sent
     to the 'DDEV'. For more information see the last paragraph of the
     'DUMP' command, the 'SET' command, and the miscellaneous information
     section.


     K.3.1.3  MODIFY - The 'MODIFY' command allows a string of locations on
     the device to be changed in an easy way. This is done by specifying
     the format of the input and letting the program do the work of storing
     the data properly. This command has the following forms:

	  MODIFY [<format>] <location string>

	  MODIFY <location string>		MO 200.0-17,35-43
	  M <location string>			M 32745-32777
	  MODIFY <format> <location string>	MO PA 12342-12360
	  M <format> <location string>		M AS 367.7261-7275


     where the <location string> has exactly the same format as for the
     'LIST' command and the <format> options are shown below. If the
     <format> is not specified (as with the first form), the program will
     pick the one of the formats below which corresponds to the current
     setting of the 'FORMAT' option. The corresponding formats are shown
     below.

	  'MODIFY' format	'FORMAT' setting and 'MODIFY' action.

	  ASCII			ASCII one character of input is stored in
	  A			each word to be modified.

	  PACKED		PACKED two characters of input are packed
				as trimmed 6-bit characters, padded with
				trailing 00's. Control characters (those
				with codes less than 240 octal) are packed
				as a 6-bit 77 (flag) and the low-order
				6-bits of the character. Note that this
				means that "@" is packed as a terminator
				(00) and that "?" is not unique.

	OS			OS three characters of input are packed into
				two words to be modified. When using this
				format, the start address must be even and
				the end address must be odd.

	XS240			XS240 a space (240 octal) is subtracted
				from each character and then it is packed
				as 6-bit bytes. Control characters are
				handled as with 'PACKED' format.

				      90



	NUMERIC			SIGNED & UNSIGNED decimal, BCD, OCTAL, BYTE,
	N			PDP, FPP and DIRECTORY formats the input is
				a string of numeric items which are stored
				one per 12 bit word. See the section on
				numeric items. Note that bcd, byte,
				directory and "symbolic" are not included,
				that decimal or octal input are determined
				by the "CTRL"-"D" and "CTRL"-"K" switches
				and that signed numbers must be input
				enclosed in parentheses, e.g., 17, (-10),
				^D200, (-^K312), 40, (-^D35*129).

     For each location or group of locations specified by the <location
     string>, the program will prompt for the input by printing the start
     location in the same format as described under the output format
     options above.

				    CAUTION
		The program always modifies exactly the number
		of words specified by each item in the
		<location string>. If you input extra
		characters for the character formats or extra
		numeric items for the numeric format, they
		will be ignored. If you input not enough
		characters or items, the rest of the words to
		be modified will be set to the 'FILLER' value
		(see the 'SET' command). The program will not
		output any message if either of these things
		takes place. This does, however, make it
		possible to fill from 1 to 16 blocks on a
		device with zero or some other value by
		specifying all the words to be filled in
		'NUMERIC' format and then responding to the
		prompt with a single "(F)" (the value of the
		'FILLER') and "RETURN".

     Input to the program is always terminated by a carriage-return
     ("RETURN"). It is therefore not possible to insert a carriage-return
     into a word using this command. All of the editing keys are available
     for use during input, therefore the CTRL/C, CTRL/Q, CTRL/S, CTRL/R,
     CTRL/P, CTRL/U and "RUBOUT" characters cannot be entered using this
     command either. For all of the character input formats, spaces
     (excluding leading spaces, which are ignored) and tabs in the input
     string are packed as they are seen. For numeric input, spaces are
     ignored and the numeric items must be separated by commas.

     The command can always be aborted by CTRL/P if you change your mind
     before the "RETURN" key is pressed.


     K.3.2  Search Limits:
     There are two search commands in the program, the 'WORD' search and
     the 'STRING' search. They both search from a lower to an upper limit.
     The limits are either the 'LOWER' and 'UPPER' limits set by the 'SET'
     command (the default) or the limits set up by the " 'FROM'<l>" (which

				      91



     overrides the 'LOWER' limit) and/or "'TO'<l>" (which overrides the
     'UPPER' limit) clauses which can optionally follow the command word.
     Leaving out the block parts of either of the two temporary limits will
     cause the program to use the block part of the corresponding default
     limit set by the 'SET' command. When in a mapped ('SAVE' or 'LOAD')
     access mode, searching through non existent locations or overlays will
     never produce a match. Whenever a match is found, the program outputs
     the location where the match occurred, followed by the word or string
     that matched.

				     NOTE
		It is not possible to search through more than
		one overlay per search command. To do so would
		require different and separate handling of the
		"block" and "address" parts of the limits when
		in the mapped modes including the resetting of
		the "address" part. The result is that in the
		mapped modes the "block" parts are used to set
		the overlay to be searched (lower limit only)
		and only the "address" parts are used in the
		determination of the number of words to be
		searched.

     K.3.2.1  WORD (Search) - The 'WORD' search command is used to search
     for a word for words which, masked by the 'MASK' (which is set by the
     'SET' command), will match the search word (also masked). This command
     has five options and therefore has the forms:

	  WORD [UNEQ] [ABS] [MEM] [FROM <l>] [TO <l>] <n>

	  WORD <n>			WO 217
	  W <n>				W (S)
	  WORD UNEQUAL <n>		W UN 0
	  WO U <n>			WO U (C&377)
	  WORD ABSOLUTE <n>		WO AB 7402
	  WA <n>			W A 7000
	  WORD MEMREF <n>		WOR MEM 41
	  WO M <n>			WO M 40
	  WORD FROM <l> <n>		WO FR 213.0 2317
	  W F<l> <n> 			W F 1.35(S)
	  WORD TO <l> <n>		W TO 213.345 1111
	  W T <l> <n>			WORD T 6257.377 7777
	  ... and any combination and order of the above options.

     where <n> is the bit pattern being searched for, 'UNEQUAL' means that
     all words which are not equal to <n> under the mask do match, the
     temporary limits clause is as described above,'ABSOLUTE' means that
     the location where the match occurred is to be output as an absolute
     block number and displacement rather than as a relative location, and
     'MEMREF' means that only words whose high-order octal digit is 0 thru
     5 (i.e. the PDP-8 memory reference op-codes) are allowed to match,
     independent of the setting of the 'MASK'.

     When you want to search for those words which reference a specific
     location, 'SET' the 'MASK' to 377 (octal) and then use the 'MEMREF'

				      92



     option. This will exclude all Operate (op-code 7) and IOT (op-code 6)
     "instructions" from the output and can make it considerably easier to
     find the desired information (e.g. you will not output the location of
     every "CIA",7041 octal, when you are looking for references to
     location 41 octal).


				     NOTE
		'UNEQUAL' has a higher priority than 'MEMREF',
		so first each word is tested under the mask
		for equal/'UNEQUAL' and if the specified
		condition is true, then the word is tested for
		the 'MEMREF' condition.


     K.3.2.2  STRING (Search) - The 'STRING' search command is used to
     search for a string of numbers (bit patterns) under an optional string
     mask. This command has four options and therefore has the forms:

	  STRING [MASKED] [ABS] [FROM <l>] [TO <l>] <numeric string>

	  STRING <numeric string>		ST 4557,0,0
	  STRING MASKED <numeric string>	ST MA 4577,0,1203
	  ST M <numeric string>			ST M 5566,0
	  STRING ABSOLUTE <numeric string>	ST AB 'PI,'P@
	  ST A <numeric string>			ST A "A, "B
	  STRING FROM <[><numeric string>	STR FR 100 1,4000,2
	  STR F <l> <numeric string>		ST F 123.4567 (S),(-S)
	  STRING TO <l> <numeric string>	STR T 7577 'ER, 'RO, 'R@
	  ST F <l> T <l> <numeric string>	ST F 1.0 T 7.0 'FO,'TP
	  ... and any combination and order of the above options.

     where the <numeric string> is simply a string of numeric items
     separated by commas, 'MASKED' specifies that the search is to be done
     under the string mask, 'ABSOLUTE' is as for the 'WORD' search, and the
     temporary limits clause is as described above.

     When the 'MASKED' option is used, each item of the <numeric string> is
     masked by a separate mask word from the string mask. If the string
     mask is shorter than the search string, it is used in a circular
     fashion (the first word follows the last) as many times as necessary
     to mask all of the items of the search string. If the string mask is
     longer than the search string, the extra words are not used. This
     feature allows for very complex searches to be done.

     For example:  Suppose it is desired to find all calls to a certain
     subroutine in a file and also see their arguments. This could be done
     as follows:

	  FILE FUTIL	 		-look up file to be searched
	  FUTIL.SV 6070-6120 ^P	 	-you stop typeout
	  SE MODE SAVE	 		-set access mode to mapped
	  SMASK (-1),0,0	 	-set mask for 2 arguments per call
	  ST M 4547,0,0	 		-search for 4547 and 2 dummies


				      93



     The output will give the address of the subroutine call (which
     requires an exact match due to the mask of 7777) and the contents of
     the two following words (which can be anything, since they are masked
     by 0).

     Using the mask specified above, a search could be made for an exact
     match, 2 "don't care words" and another exact match by simply
     specifying a search string with 4 arguments. The first item of the
     string mask will be used to mask both the first and the last items of
     the search string. This command can be particularly useful when trying
     to find certain kinds of references in programs for which no CREF
     listing (or perhaps no listing at all) is available.


     K.3.2.3  SMASK - The 'SMASK' command is used to set up the string
     mask. It has the following form:

	  SMASK <numeric string> 	SM (-1),0,0,7000,0

     where the <numeric string> is the same as for the 'STRING' search
     command above. The current contents of the string mask may be examined
     by the 'SHOW' command.


     K.3.2.4  SET - The 'SET' command is used to set up various switches
     and variables within the program. It has many options, each of which
     is the name of the switch or variable and is always followed by a word
     or number describing how it is to be set. All items are separated by
     spaces. The command has the following two forms:

	  SET <option(s)>		SE OU PDP ERR LONG MODE SAV
	  S <option(s)>			S LO 100.0 UP 123.377 IDEV LPT

     where the options are as follows:

	  OUTPUT OCTAL			Set the output mode for the
	  OUTPUT O			single-character commands.
	  O 	 PDP			Initialized to 'OCTAL'.
	  O 	 P
	  OUT 	 FPP
	  O 	 F

	  ERROR  SHORT			Set the mode for error message
	  E 	 S			output. The 'SHOW ERRORS' command
	  E 	 LONG			will list all error messages.
	  ERROR  L			Initialized to 'LONG'. Also set to
					'SHORT' by write-locking system
					device.

	  FORMAT <format>		Set output format for 'LIST', 'DUMP',
					etc. The formats have been described
					previously. Initialized to 'PACKED'
					ASCII.



				      94



	  OFFSET <l>			Set the offset to the low 12 bits of
					<l>. Initialized to 0.

	  FILLER <n>			Set the filler to the low 12 bits
					of <n>. Initialized to 0.

	  LOWER	 <l>			Set the lower search limit.
					Initialized to 0.200.

	  UPPER	 <l>			Set the upper search limit.
					Initialized to 0.17577.

	  DEVICE <device name[:]>	Set up the OS/8 device for access.
					The handler is fetched at this
					time. Initialized to "SYS" (device
					01). ":" In <device name [:] > is
					optional. <device name> is an
					assigned or permanent OS/8 mass
					storage device name.

	  DDEV <device name[:]>		Set up the "dump" device.
					Initialized to 'SYS'. See also
					'DMODE' below and 'OPEN' and 'CLOSE'
					commands.

	  MODE 	 NORMAL			Set up the device access mode.
	  MODE	 N			These have been described
	  MODE 	 SAVE			previously. Initialized to 'NORMAL'.
	  MODE	 S
	  MO	 LOAD
	  MO	 L
	  MO	 OFFSET
	  MO	 O

	  DMODE	 NONE			Set up the "dump" output mode.
	  DMODE	 PART			Initialized to "NONE", which sends
	  DMODE	 ALL			all output to console only. 'PART'
					sends 'DUMP', 'LIST' and 'SHOW
					ERRORS' output to the 'DDEV'
					(perhaps to a file). 'ALL' sends all
					output to both the console device
					and to the 'DDEV'. (See section on
					file output.)

	  MASK	 <n> 			Set the 'WORD' search mask to the
	  M	 <n> 			low 12 bits of<n>. Initialized to
	  				7777.

	  TEMP	 <n> 			Set the 'TEMP' storage to the 24-bit
					value of <n>. Value is returned by
					subsequent use of the 'T' in
					expressions.

     As many options as desired may be specified on one command line,
     separated by spaces. In the event of an error, none of the options

				      95



     past the point where the error occurred will have been set. If you
     have any question, use the 'SHOW' command.


     K.3.2.5  SHOW - The 'SHOW' command is used to list the current setting
     of any of the program switches and variables set by the 'SET' command
     and other information. The program outputs either words or numbers to
     best describe the current settings. As with the 'SET' command, as many
     of the options for this command as desired may be specified on a
     single command line, separated by spaces. This command has the form:

	  SHOW <option(s)>		SH BL CCB LOW UP ODT REL ABS

     where the <options> are as follows:

	  BLOCK				Output in octal the start block
	  B				number of the last file specified
					by the last 'FILE' command.

	  CCB				Output the core control block of
	  C				the last file specified by the
					'FILE' command. If the file is not
					a 'SAVE' file, an error will occur.
					The start address of the file is
					output as a 5-digit octal number,
					the job status word (JSW) is output
					in octal, and the core segments are
					output as 5-digit octal addresses.

	  HEADER			Output the header block information
	  H				for the last file specified by the
					last 'FILE' command. If the file is
					not a 'LOAD' file, an error will
					occur. The start address is output
					as a 5-digit octal number, followed
					by the next free address as a 5
					digit octal number, the loader
					version number in octal and a
					message if Extended Precision is
					required. Then, for each level, a
					line is output with the number of
					overlays, the 5 digit start address,
					the relative start block and the
					length of the overlays (in blocks)
					for this level.

	  ABSOLUTE			Output the absolute location of the
	  A				last word accessed on the device in
					<location> format (a 4 digit octal
					block number, a "." and a 5-digit
					octal address) and the word "MOD"
					if the current block has been
					changed (the <something-changed>
					flag is set).


				      96



	  RELATIVE			Output the relative location (what
	  R				you specified) of the last word
					accessed on the device in <l>
					format and the word "MOD" if the
					current block has been changed.

	  ODT				Output the relative location of the
					last word accessed by one of the
					special-character commands in <l>
					format and the word "MOD" if the
					current block has been changed.

	  LOWER				Output the search lower limit in
					<l> format.

	  UPPER				Output the search upper limit in
					<l> format.

	  FILLER			Output the value of the filler in
					octal.

	  MASK				Output the 'WORD' search mask in
	  M				octal.

	  SMASK				Output the current contents of the
					'STRING' search mask as a string of
					octal numbers.

	  OFFSET			Output the value of the offset in
					octal.

	  MODE				Output the name of the current
					setting of the device access mode
					switch ('NORMAL', 'SAVE', 'LOAD' or
					'OFFSET').

	  DEVICE			Output the OS/8 device name and
					number.

	  DDEV				Output the name of the "dump"
					device.

	  OUTPUT			Output the name of the current
	  O				single-character (ODT) command
					'OUTPUT' mode (OCTAL, PDP or FPP).

	  FORMAT			Output the name of the current
	  F				output format.

	  VERSION			Output the current version number
					of FUTIL.

	  ERRORS			Output a complete list of all error
	  E				codes and their corresponding
					messages. Note: This list is output

				      97



					to the 'DDEV' ("dump" device) so
					that it can be output using the
					"LPT" handler for your system. Note
					that Version number is also output
					with errors.


     K.3.2.6  FILE - The 'FILE' command is used to locate files on the OS/8
     device and to set up the start block of a file for the mapped access
     modes, 'SHOW CCB', etc. This command has the forms:

	  FILE <file name string> 	FI FUTIL PIP.SV
	  F <file name string> 		F MICRO.LD

     where the <file name string> is a string of one or more OS/8 file
     names, separated by spaces. Any other characters except "." will be
     taken as part of the file names. The program assumes extensions of
     ".SV", ".LD" and null (in this order) when looking up the file. This
     can lead to a substantial amount of time when a large directory is
     searched three times for a file that does not exist. Specifying an
     extension will cause only one lookup attempt to be made. A null
     extension, if desired, may be specified by making the "." the last
     character of the file name. The program does one (or more) separate
     lookup(s) for each file name specified and outputs either

	  <file name> ssss-eeee oooo (dddd) b.111 dd-mmm-yy
     or
	  <file name> ssss-eeee oooo (dddd) b.111
     or
	  <file name> LOOKUP FAILED

     where "ssss" is the start block of the file in octal, "eeee" is the
     last block of the file in octal, "oooo" is the length of the file in
     octal, "dddd" is the length of the file in decimal, "b.111" is the
     block (segment) and location within that block of the first word of
     the file entry (the first two characters of the name) in the
     directory, and dd-mmm-yy is the file date. If the directory does not
     contain the extra word required for the date or the date word of the
     file is 0, the second form with no date will be output rather than the
     first form. The "LOOKUP FAILED" message means either that the file
     name was not found on the device or that the device is a write-only
     device.

     The actual lookup operation is performed by the OS/8 USR, which is
     swapped as needed (see section on program execution). Since the USR
     keeps track of the current device once the first 'FILE' command is
     given, it will have the wrong directory in memory if the medium (tape
     or disk) is changed on the physical device. This can be solved one of
     three ways:

	  1.  Use the 'REWIND' command to rewind the device being removed
	      and clear the directory segment from the USR.
	  2.  Do a 'SHOW ERRORS' and abort the output when the message
	      output begins. This will have swapped out the USR. If
	      messages are not available, use 1 or 3.

				      98



	  3.  Use EXIT or CTRL/C to return to OS/8 and then directly
	      restart FUTIL with the OS/8 START command. This will have
	      swapped out both error messages and USR from memory.

     Any of these methods should be followed by a 'SET' command to reset
     the 'DEVICE' and the rest of the I/O parameters desired.

     The last file name specified that did not have a LOOKUP FAIL will be
     the file used in the mapped access modes, 'SHOW' 'CCB', etc. The
     program is initialized with no known file, so attempting to access any
     location in a mapped access mode or attempting to 'SHOW' 'CCB' or
     'SHOW' 'HEADER' without giving a valid 'FILE' command will cause an
     error.


     K.3.2.7  WRITE - The 'WRITE' command is used to force the program to
     write out the block currently in memory. It has the form:

	  WRITE [<block>]

     where the optional <block> overrides the default number of the block
     that was read to specify where the current	 block is to be
     written. This obviously dangerous operation does allow a limited
     amount of copying in a special situation, e.g., allowing a directory
     to be backed up by moving a copy to the end of the device (see the
     examples section) or copying a single block from one device to another
     by changing the 'DEVICE' and then doing a 'WRITE' (with or without an
     argument). Again, as stated in the section on accessing the device,
     caution must be used because attempting to write beyond the end of a
     device may not be checked by the handler.


     K.3.2.8  SCAN - The 'SCAN' command is used to do a rapid scan for read
     errors on the current 'DEVICE'. It has the form:

	  SCAN<block string> 		SC 0-6257

     where the <block string> is of the same form as for the 'DUMP'
     command. Each block is simply read. If an error occurs, it is reported
     as:

	  oooo BAD BLOCK

     where "oooo" is the block number in octal, and the scan continues.
     This is the only FUTIL command that will continue on a read error.
     Should the current block have been changed, and any other blocks be
     included in the scan, an implicit write will be attempted by FUTIL. An
     error on this implicit write will be reported and then the command
     will be aborted. This is the only time that this command will attempt
     a write. The command can then be repeated if it is desired and it will
     execute (only one implicit write attempt is ever made by FUTIL).





				      99



				      NOTE
		The OS/8 "actual" block number for the block
		to be read is stored (for display) in the
		computer MQ register (if present). It is
		particularly useful for following the
		progress of this command. The value is stored
		before checking if the current block needs to
		be written.


     K.3.2.9  REWIND - The 'REWIND' command is used to move a tape back to
     block 1 and to reset the USR directory segment. It has the form:

	  REWIND

     and must be terminated by the "RETURN" key. It causes a read of block
     1 of the device and resets the directory segment in the USR (if in
     memory). Any subsequent 'FILE' command will cause the directory to be
     read.


     K.3.3  File Output
     Output to file-structured or non-file-structured "dump" devices is
     provided through two commands, 'OPEN' and 'CLOSE', and two 'SET'
     options,'DDEV' and 'DMODE'. They can be used to simply make fast hard
     copy output from the 'DUMP', 'LIST' and 'SHOW ERRORS' commands, to
     provide a hard copy log of all operations carried out with a video
     terminal, to provide an ASCII file output of some data for later
     processing by another program, etc.

     Output to file-structured and to non-file-structured devices (serial
     devices) is handled in two separate ways. Output to the
     file-structured device is done by first setting the 'DDEV' and 'DMODE'
     and then 'OPEN'ing an output file. No output to the device will be
     done until the file is open (to protect your directories), and then
     output will be done one block at a time. When output to the file is
     complete, 'CLOSE' your file to make it a permanent file (properly
     terminated with a CTRL-Z and padded with nulls).

     Output to a non-file-structured device is done by simply setting the
     'DDEV' and 'DMODE'. Output to the device will be done one line at a
     time, as soon as specified by the 'DMODE', and neither the 'OPEN' nor
     the 'CLOSE' commands are needed. The output is done by padding the
     buffer with nulls after each line is ready and then calling the output
     device handler, so the handler used should ignore nulls (which leaves
     out the "PTR:" handler, for example).


     K.3.3.1  OPEN - The 'OPEN' command is used to open an output file on
     file-structured devices for partial or total output from the program.
     It has the form:

	  OPEN <file name> 		OPEN OUT.DA

     where the <file name> should be a standard OS/8 file name. The

				     100



     extension defaults to ".DU" (for "dump") if none is supplied.


				    WARNING
		FUTIL gives significance only to the
		characters space, carriage-return and "."
		when scanning file names. It is therefore
		the responsibility of the user not to
		include characters that are not legal to
		other OS/8 programs or the files will be
		able to be accessed only through FUTIL or
		the CCL command decoder.

     This command must be given after the "dump" device is 'SET' by the
     'DDEV' option. The output specified by the 'DMODE' will then be sent
     to this file, one block at a time (packed only 8 bits per word), until
     either the 'DMODE' is changed or the file is 'CLOSE'd.

     Files can be opened at will without closing any previous file. This
     gives the user additional flexibility, but at the expense of possibly
     losing an output file if it is not 'CLOSE'd.

     Should an error occur on the output device while doing output, the
     file is simply thrown away (it cannot be 'CLOSE'd).


     K.3.3.2  CLOSE - The 'CLOSE' command is used to close an output file
     previously 'OPEN'ed. It has the form:

	  CLOSE

     and must be on a line by itself. If given with no file open, it is
     simply ignored.


     K.3.4  Batch Operation
     Operation of FUTIL under BATCH allows repeated operations to be done
     without re-entry. All of the operations provided under interactive
     operation are provided except that the "RUBOUT" character is simply
     ignored, input is taken directly from the BATCH stream and console
     output goes to the log output device.

     Four commands have been added specifically to support use of FUTIL
     under BATCH: 'IF','END','COMMENT' and 'EXIT'. These commands are also
     available for interactive use, but are not as important in that mode.


     K.3.4.1  IF - The 'IF' command was implemented specifically to allow
     FUTIL, when operating under BATCH to be sure that the correct
     operations are proceeding before modifying something incorrectly. It
     has the form:

	  IF <expression> 		IF C-3575

     where <expression> is a general expression of the same form as used by

				     101



     the 'EVAL' command. If the expression evaluates to exactly zero (as a
     24-bit integer), command execution will continue as though the command
     had not been seen. If the result is not exactly zero, command skipping
     will begin and will continue until a line containing the single word
     'END' is found. Command execution will then resume.

     This command was set up to test only for zero under the assumption
     that a test is to be made for some exact quantity. However, the
     capabilities of the expression evaluator can be used to generate
     sufficiently complex expressions for other tests. For example:

	  IF 40000000&(......) 		will test for positive
	  IF -(40000000&(...))-1 	will test for negative
	  IF 10000&(-(77770000!(...)))  will test for 12-bit non-zero


     K.3.4.2  END - The 'END' command is used to re-enable command
     execution following an unsatisfied 'IF' command. It has the form:

	  END

     and must be on a single line by itself. When encountered during
     command execution, it is ignored. Note that the 'IF'/'END' commands
     cannot be nested because the first 'END' found will re-enable command
     execution for any number of previous 'IF' commands. For example:

	  IF ...
	  IF ...
	  IF ...
	  END				will terminate all three!


     K.3.4.3  COMMENT - The 'COMMENT' command allows optional comments in
     command input which will simply be ignored during execution. It has
     the forms:

	  COMMENT [<comment>] 		COMMENT THIS IS ONE
	  C [<comment>] 		C

     where [<comment>] is an optional comment. Note that blank lines may
     also be used for formatting of the output log but that they will also
     close any open location.


     K.3.4.4  EXIT - The 'EXIT' command provides a method of return to OS/8
     other than "CTRL/C". It has the form:

	  EXIT

     and the rest of the line is ignored. Exit does not write out the last
     block modified. Use 'WRITE' to make changes permanent.


     K.3.4.5  EVAL - The 'EVAL' command is used to evaluate a parenthesized
     expression of signed double-precision integers. It has the forms:

				     102




	  EVAL <expression> 		EV S*^D4096+D
	  E <expression> 		E B*400+L

     where the <expression> follows the normal rules for arithmetic
     expressions. Legal operators, in their order of precedence are:

	  (		evaluate inner expression
	  /		signed division
	  *		signed multiplication
	  -		subtraction
	  +		addition
	  &		logical product ("and")
	  !		logical sum ("or")
	  )		expression end

     Besides 24 bit numeric input (which can be octal, decimal or mixed
     octal and decimal under the control of the CTRL/D and CTRL/K switches
     and ASCII and packed ASCII using " and ', the following "variables"
     may be used:

	  C		current contents (of location "L").
	  L		current location (15 bit, same value as is output
			by the 'SHOW' 'RELATIVE' command).
	  B		current block number (as for "L").

	  F		contents of 'FILLER' (12 bits).
	  T		contents of 'TEMP' (24 bits).

	  S		contents of the console switch register.

	  R		the remainder of the last division or the high
			product of the last multiplication. 24 bits, the
			sign may not be correct.

	  D		contents of OS/8 Monitor "date" word.


     Overflow on addition, subtraction and multiplication are ignored, but
     trying to divide by 0 will cause an error.

     If no errors occur, the program evaluates the expression and types out
     the results in the form:

	  = oooooooo (sddddddd)

     where "oooooooo" is the double precision result in octal and
     "sddddddd" is the signed double precision result in decimal (the sign
     is either "-" or " ").


     K.4  EXAMPLES
     These examples are to help provide an overview of the use of the
     program and to stimulate the thoughts of the user. Example 3 and those
     that follow are not as well commented as the first two examples since

				     103



     it is intended to show concepts of what can be done with the program
     rather than the mechanics of the operations. Should questions arise on
     the mechanics, it is suggested that the first two examples and the
     discussions of the commands in question be reviewed.

     EXAMPLE 1:

     Assume that you would like to know what CCL remembers of your last
     ".UA" command. The remembrances are stored on block 65 (octal) of the
     system device. As described in the source of CCL, each of the
     remembrances is allocated 40 (octal). or 32 (decimal) words in this
     block, the first four of which contain binary information and the last
     34 of which contain the last input command, stored as packed ASCII
     characters. The lines contain the inputs for the commands as follows:
     TECO and MAKE (line 0), EDIT and CREATE (line 1), COMPILE and EXECUTE
     and PAL (line 2), UA (line 3), UB (line 4), and UC (line 5). Thus, the
     saved ".UA" command can be listed by out putting the contents of the
     4th through 37th words of area 3 in block 65 as packed ASCII
     characters as follows:

	  .R FUTIL <cr>  		-call FUTIL from OS/8

	  EVA 3*40+4<cr>  		-calculate start displacement
	  = 00000144 ( 0000100)  	-of the 3rd "line" (= 144[8])

		Now list the words of this line with the LIST command,
		specifying the output format to be PACKED ASCII characters
		and the words to list to be block 65 locations 144 (from
		above) through 144+33 (the expression for the location of
		the last word of this "line"). FUTIL responds with the start
		location and a line of characters, and the next location
		with a multiple of 10[8] as an address and a line of
		characters.

	  LIST PACKED 65.144-(144+33)<cr>  	-list the words wanted

	  0065.00144: DIR R:FUT???.*/E/R=3
	  0065.00160:	 			-that's it!

				     NOTE
		For the examples above and below, the symbol
		"<cr>" is used to show that you need to
		terminate your command lines with a "carriage
		return". All other lines above are output by
		the program.


     EXAMPLE 2:

     Now assume that you would like to make the simple patch for OS/8
     FORTRAN IV users with an FPP-8/A to use the lockout feature of the
     FPP-8/A, as given in the August 1976 DIGITAL Software News. This
     requires changing the contents of location 15776 of FRTS (the Fortran
     Run Time System) from 400 to 410 (which adds the lockout bit). You
     also want to update the date word of the directory entry for FRTS (the

				     104



     4th word beyond the start of the entry) to show that the file has been
     updated. This is done as follows:

	  .R FUTIL<cr>  		-call it

	  SET MODE SAVE <cr>  		-set FUTIL to a mapped mode
	  FILE FRTS<cr>  		-look up the file to map
	  FRTS.SV 0671-0722 0032 (0026) 1.327 31-DEC-75
					-"1.327" is start of entry!

		Now use "ODT" command "/" to open and change one word.

	  15776/ 0400 410<cr>  		-add LOCKOUT bit

	  SET MODE NORMAL<cr>  		-switch to unmapped

		Now use "ODT" command "/" with an expression to open the
		date word, command "@" to output it in "date" format and
		then put today's date (as an octal value) in its place.

	  1.(327+4)/6375
	  @31-DEC-75 (D)<cr>	 	-change file date to today's date

	  WRITE<cr>	 		-send out this change


				   NOTE
		First the file FRTS.SV is changed, and then
		the OS/8 directory is updated to the current
		date. Changing the address desired from FRTS
		to the directory automatically writes out
		the modified block of FRTS before reading in
		the directory segment that contains the file
		name. However, the changed directory segment
		must be written out explicitly because there
		are no other blocks to examine for this
		example.

EXAMPLE 3:

     While doing a "/S" transfer with PIP, PIP gives a read error in your
     file "SOURCE.PA". Attempting to read it with EDIT causes EDIT to type
     "?0^C" and return to the Monitor. Find out what is wrong as follows:

	  .R FUTIL

	  FI SOURCE.PA  		-look up the file
	  SOURCE.PA 0243-0351 0107 (0071) 2.005 30-AUG-74

	  SE MASK 0 LO 243.0 UP 351.377  -set up mask & limits

	  W UNE 0  			-search the file

	  ?ee AT 08 FATAL READ ERROR	-here is the problem
	  [Note: "ee" may change with version, so is left out.]

				     105



	  SH ABS	 		-find out where it is
	  ABS. LOC = 0271.00000

	  WR	 			-attempt to clear error

	  DU OS (B+L/400)	 	-it worked, now dump it

	  0271.00000:....^P  		-change your mind

	  W UN FR 272.0 0	 	-check the rest of the file

	  ^C	 			-ok, now go fix the source

     This sequence can also be carried out using the SCAN command as
     follows:

	  .R FUTIL
	  F1 SOURCE.PA  		-use CCL to call & lookup

	  SOURCE.PA 0243-0351 0107 (0071) 2.005 30-AUG-74
	  SCAN 243 -351	 		-scan the area

	  0271 BAD BLOCK	 	-here is the problem!

	  271.0/ ?ee AT 07 FATAL READ ERROR	-get block with trouble

	  WR	 			-attempt to clear error

	  DU OS (B+L/400)	 	-it worked, now dump it

	  0271.00000:....^P  		-change your mind

	  ^C	 			-ok, now go fix the source

     If the error had been of some type other than a clearable error, the
     'WR' commend might also have failed.

     EXAMPLE 4:

     After using BUILD to change your system, find out the device number
     for "DTA1 ":

	  .R FUTIL

	  SE DEV DTA1	 		-fetch the device handler
	  SHOW DEV
	  DEVICE = DTA1(06)	 	-number is decimal

     EXAMPLE 5:

     By accident you zero a DECtape directory which contains the only copy
     of a file you need. You have the PIP "/E" listing of the directory but
     only want to re-build it enough to get the wanted file. The name of
     the file is "LOST.FI ":


				     106



	  .R FUTIL

	  SE DEV DTA1	 		-it was here
	  EV ^D5+14+11+10+16+13+8+5	-lengths of all preceding
	  = 00000122 ( 0000082)	  	- files
	  EV ^D730-^K61-^D82-25	 	-rest of DECtape room
	  = 00001076 ( 0000574)

	  1.0/7777 (~3)	 		-now 3 files
	  4/ 7777			-1 extra word per entry
	  0001.00005\0000 'DU	 	-set up a "DUMMY" file
	  0001.00006\7556 'MM	  	-over the old <EMPTY>
	  0001.00007\1752 'Y@
	  0001.00010\3451 0	 	-a null extension
	  0001.00011\6234 (D)	 	-put in today's date
	  0001.00012\4235 (-^D82)	-length
	  0001.00013\5761 'LO	 	-the desired file
	  0001.00014\3341 'ST
	  0001.00015\2371 0

	  0001.00016\1107 'FI	 	-the extension
	  0001.00017\1366 (D)
	  0001.00020\3015 (-^D25)	-its length
	  0001.00021\3415 0	 	-an <EMPTY> to end it
	  0001.00022\2713 (-^D574)	-the rest of the tape

	  WRITE	 			-now write it out
	  ^C	  			-& exit to use it

     The "LINE-FEED" key was used to advance through the words.

     The above example is exactly the same as hand calculating the required
     length of the "DUMMY" file and then doing the following sequence using
     PIP:

	  .R PIP
	  *DTA1 :DUMMY</I= 122	 	-enter the DUMMY file
	  *DTA1 :LOST.FI</I=31	 	-enter the LOST.FI
	  *^C

     Note that the lengths of the files are specified for PIP in octal.

     EXAMPLE 6:

     Search for the end of each page of text in the file "WRITE.UP". Since
     the file is an OS/8 ASCII file, which has two characters packed in the
     low 8 bits of two words and a third character packed in the high 4
     bits of both of the two words, the form-feed character (^L) may be
     packed as the third character in some cases. So it is necessary to
     search both through the low 8 bits of each word and through the high 4
     bits of each pair of words. Do it as follows:





				     107



	  .R FUTIL

	  FI WRITE.UP
	  WRITE.UP 0301-0437 S^P	 -typeout stopped
	  SE MA 377
	  SE LO 301.0 UP 437.377	 -char mask & limits set

	  W A "^L	 		-search for form-feed

	  .......typeout occurs here

	  SMASK 7400,7400	 	-set up string mask
	  ST M A ("^L*20),("^L*400)	-search for 3rd char f-f
	  .......more typeout here  	-only even addresses are real
		  			-parts of form-feed pair!

     In the string search, both the string and the data searched are
     "masked" by the string mask.

     EXAMPLE 7:

     You just assembled and saved PROG.SV but forgot to use the "/P" switch
     to ABSLDR. Fix the CCB (core control block) as follows:

	  .R FUTIL
	  FI PROG.SV
	  PROG.SV 0341-^P		-stop output
	  341.1/6203	 		-the "CDF CIF" part &
	  0341.00002\6400	  	-the address
	  0341.00003\0000 400	 	-change the JSW

	  WR	 			-write the new CCB

	  SHOW CCB	 		-check it this way
	  CCB:
	    SA=06400,JSW=0400
	    CORE^P	 		-ok, output stopped

     EXAMPLE 8:

     The CREF listing file for your source file is about 732 blocks long
     (just over one full DECtape). If you do want to CREF the file onto a
     DECtape, you must do it either with the "/X" (don't process literals)
     switch or else you could use FUTIL to set up the directory with 735
     blocks (by starting at block 2) as follows:

	  .R PIP
	  *DTA1 :</Z	 		-zero the directory
	  *^C

	  .R FUTIL

	  SE DEV DTA1	 		-* * see WARNING below * *
	  1.1/0007 2	 		-change first block number
	  6/6446 (C-5)			-5 more blocks

				     108



	  WR	 			-write it out
	  ^C	 			-now CREF it

WARNING
		Do not copy files onto a device that has been
		fixed this way with FOTP (COPY command) because
		it writes out a directory of six blocks after
		the transfers are finished and this will zap
		blocks 2 through 6 (the first 5 blocks of the
		first file) after the copy is done! PIP and other
		processors do not monkey around with the directory
		and will handle this correctly.

     EXAMPLE 9:

     Something is extremely flaky in your system and you have been losing
     your directory repeatedly. After fixing it up with both PIP and FUTIL,
     you just want to back it up while you generate your output files onto
     another device. Since your system device has a total of 6260 (octal)
     blocks (an RK8E) you back up the directory as follows:

	  .R FUTIL

	1.0/7714 WR 6251	 	-transfer blocks up by
	2.0/7740 WR 6252		-6250 blocks.
	3.0/7770 WR 6253
	4.0/0000 3.2/0000	 	-block 3 was last, so
	^C	  			- all done

     Shortly after this, everything crashes totally, i.e., directory
     smashed, system gone from disk. Rebooting from DECtape you use PIP to
     restore the system area and then use FUTIL to restore the directory:

	  .R FUTIL

	  SET DEV RKA0	 		-load non-system device
	  6251.0/7714 WR 1	 	-transfer by 6250 blocks
	  6252.0/7740 WR 2	 	-the other way
	  6253.0/7770 WR 3	 	-the last one

	  SCAN 0-6250	 		-do a SCAN for good luck


     EXAMPLE 10:

     During a SCAN of a device a bad block is found in an important data
     file and you would like to know just how far the read of that block
     really succeeded (e.g., on a DECtape, the type of error will determine
     whether the read will abort immediately or wait until the end of the
     physical block). The following commands assume that the block number
     is "bbbb" and set the input/output buffer in FUTIL to zeros before
     doing the read:

	  bbbb.0/ ?ee AT 07 FATAL READ ERROR	-do read to set up


				     109



	  MOD NUM 0-377
	  bbbb.00000: 0	 			-set whole buffer to 0

	  SET DEV same	 			-set to device now in use

	  / ?ee AT 01 FATAL READ ERROR	 	-force the read again

	  DUMP OC bbbb	 			-dump & examine the block

     This example makes use of the fact that changing the DEVICE resets the
     status of the buffer without changing its contents. This status
     includes the block number known and the <something-changed> flag.
     Therefore the next access to the block causes the block to be re-read
     without attempting to write it out. Following the second error, as
     much as possible of the block will have been read into memory and can
     now be examined for non-zero values (assuming that the data itself was
     not all zeros). If the read terminated before the end of the block,
     there should be an obvious separation between the zero and non-zero
     values.

     EXAMPLE 11:

     Your system has a line printer which can output 132 characters per
     line and 68 lines per page and you would like to change PAL8 and CREF
     to make use of this to use less paper. Allowing two lines at the
     bottom of the page, the lines per page should be set to 66 (call this
     "nl"). Three changes need to be made to PAL8 to change the global
     number of lines per page (nl), the number of items per column of the
     symbol table (-nl+1) and the number of symbols per page (3*[nl-1]).
     One change needs to be made to CREF to change the number of lines per
     page (m) and three changes need to be made to change the number of
     items per line of cross references. Since CREF uses 10 characters for
     the symbol name and 6 characters per line number, 19 references can
     comfortably fit on one line (19*6+10 = 124). The following changes to
     these two programs will increase the number of lines per page and the
     number of items per line in the cross-reference outputs and then
     update the dates of the two programs in the directory:

	  .R FUTIL FILE PAL8.SV

	  PAL8.SV 0200-0217 0020 (0016) 1.057 03-APR-76
	  SET MODE SAVE
	  1104/ 0070 ^D66  		-global lines per page

	  1256/7711 (-^D65)  		-symbol table column size

	  1273/0245 (3*^D65)  		-symbols per page

	  FILE CREF  			-* * SEE NOTE BELOW * *
	  CREF.SV 0220-0234 0015 (0013) 1.065 18-JAN-74

	  2564/ 7704 (-^D66)	 	-lines per page as above

	  2017/ 1102 1366> TAD 2166	-change instructions here


				     110



	  2132/ 1102 1366> TAD 2166	-and here to get new

	  2166/0077 (-^D19)	  	-references per line

	  SET MODE NORM	 		-reset access mode

	  1.(57+4)/2036 (D)	 	-change dates of PAL8

	  (65+4)/0624 (D)	  	-and CREF.

	  WRITE	 			-output the last changes

     Location 2166 was not used previous to this patch. Note that the first
     reference to the word in CREF will cause the last block that was
     modified in PAL8 to be written out. Similarly, the first reference to
     the directory will cause the last block that was modified in CREF to
     be written out.


				     NOTE
		These patches were empirically determined and
		applied to PAL8 V9H and CREF V3C. They have
		been applied to some other versions of both
		programs but have not been tested with OS/8
		V3D. USE THESE WITH CAUTION!


     K.5  MISCELLANEOUS INFORMATION


     K.5.1  Program Execution and Memory Allocation
     The start address is 06400. When the program is started here, it
     resets the internal CCB buffer, resets the start address to 00200,
     tests the "scope mode" status (changing the action of "RUBOUT" if it
     is set), performs initialization for the extended date format,
     attempts to write out the error messages (resetting the 'ERROR' mode
     control if unsuccessful), tests the "BATCH-in-progress" status
     (changing all console I/O to BATCH I/O if it is set) and jumps to
     00200. If, for some reason, it is desired to manually re-start the
     program after it has been loaded, it can be re-started at 00200.

     The error messages are swapped with the USR, but not in the normal
     manner, allowing write-locked startup with the loss of the
     message text. When the program starts execution, it writes the
     messages onto the system device in the same area used by the USR in
     swapping. Once this has been done, the USR or error messages need only
     be read into memory, as needed. In the case where it is not possible
     to write on the system device, i.e., it is write-locked, the messages
     are discarded, 'SHORT' mode is set permanently and execution continues
     without a hitch. Similarly, should an error occur when reading the
     messages, 'SHORT' mode is set permanently and an error is given to warn
     that this has happened (with no message, of course!).

     The program uses almost all of the available memory in an 8K PDP-8. It
     is allocated as follows:

				     111



	  00000-06237		program proper
	  06240-06577		buffer for arguments
	  06400-06777	 	once only code for chaining
	  06600-07177		"dump" device handler area, 2 pages
	  07277-07577		device handler area, 2 pages
	  10000-11777		USR area & error messages (swapped)
	  12000-12577		CCB/header input and test, file output
	  12600-15700		textstrings, lists
	  15700-16377		string mask, command buffer stack
	  16400-16577		CCB buffer, 1 page
	  16600-17177		"dump" device buffer, 2 pages
	  17200-17577		I/O buffer, 2 pages

     The buffer for arguments in field 0 is defined long enough to store 45
     numeric string items. The string mask buffer, in field 1, is 66 words
     long, and the command buffer, also in field 1, is 140 characters long.
     These lengths were chosen in anticipation of input from console
     devices with up to 132 characters per line. No checking of any kind is
     done to protect against overflow of any of these buffers under the
     assumption that these buffers are large enough for any reasonable
     input to this program, however, the arrangement of the buffers is set
     up in such a way that the most valuable data is the farthest distance
     from a variable buffer.

     The expression evaluation stack buffer uses the area in field 1 from
     the end of the command buffer (approximately location 16130) to the
     beginning of the CCB buffer (location 16377). This should provide
     ample room for any expression able to fit on one line. Again, no
     checking to prevent overflow is done.


     K.6  COMMAND SUMMARY
     SINGLE-CHARACTER commands: ([<n>] = optional <item>)


	[<l>]/  <l>+  <l>-
	[<n>] with     #  $  :  %  &  <  =  >  ?  @  [  \  ]
	$ (ESCAPE)  RETURN;  LINE FEED  !  ^  _

     WORD-TYPE commands: (And modifiers, many of which are optional)

	  ASCII PACKED OS XS240 UNSIGNED SIGNED BCD BYTE OCTAL PDP FPP DIR
	DUMP 	[<format>] <block string>	([<format>] s above)
	LIST 	[<format>] <location string>	([<format>] s above)
	MODIFY 	[<format>] <location string>	([<format>] s below)
	  ASCII PACKED OS XS240 NUMERIC

	WORD	<option(s)> <n>
		UNEQUAL ABSOLUTE MEMREF FROM <l> TO <l>
	STRING	<option(s)> <number string>
		MASKED ABSOLUTE FROM <l> TO <l>
	SMASK	<number string> 	e.g.,1,34,0,7700,0,(-1),377




				     112



	SET	<option>	<setting>
		OUTPUT		OCTAL PDP FPP
		ERROR		LONG SHORT
		FORMAT		<format>
		OFFSET		<l>
		LOWER		<l>
		UPPER		<1>
		DEVICE		<device name[:]>
		DDEV		<device name[:]>
		MODE		NORMAL SAVE LOAD OFFSET
		DMODE		NONE PART ALL
		MASK		<n>
		FILLER		<n>
		TEMP		<n>

	SHOW	<option(s)>
		BLOCK CCB ABSOLUTE RELATIVE ODT LOWER UPPER
		MASK SMASK OFFSET MODE DEVICE OUTPUT FORMAT
		HEADER FILLER VERSION ERRORS DDEV
	FILE	<file name(s)>
	WRITE	[<block>]
	SCAN	<block string>
	REWIND

	OPEN	<file name>
	CLOSE

	IF	<expression>
	END
	COMMENT	[<comment line>]
	EXIT

	EVAL	<expression>		e.g., (1!(S+^D17))*^Kl5+(C&7600)
		!  &  +  -  *  /  (  )  C  L  B  F  T  S  R  D

     Numeric Input:

	^D ^K <digits> "<1 character> '<2 characters>
	(...all eval options...)

     Control Characters:

	^P  ^C  ^U  ^R  RUBOUT  ^S  ^Q


     K.7  SINGLE-CHARACTER COMMAND OUTPUT FORMAT SUMMARY	

	([<n>] = optional numeric item)

     Output in octal or octal & "symbolic" (PDP or FPP):

	<l>/    /	[<n>]"LINE-FEED"	[<n>]!  [<n>]^	[<n>]_
	<l>+   <l>-

     Output in a specified format:

				     113



	[<n>]#		BCD
	[<n>]$	 	OS/8 ASCII
	[<n>]:		SIGNED decimal
	[<n>]%		BYTE octal
	[<n>1&		XS240 format packed ASCII
	[<n>]<		OCTAL
	[<n>]=		UNSIGNED decimal
	[<n>]>		PDP symbolic
	[<n>]?		DIRECTORY
	[<n>]@		DATE format (extended, in alpha)
	[<n>][		ASCII
	[<n>]\		FPP symbolic
	[<n>]]		PACKED ASCII
	[<n>]$  (ESCAPE)   As 'SET' by last "SET FORMAT x"

     no output: [<n>];








































				     114





								 APPENDIX L

							       DUMP PROGRAM


     The DUMP handler is a new OS/8 2-page handler that obtains blocks of
     binary data on file-structured devices and sends them to the LP08 line
     printer to produce a listing. This listing is called a DUMP.

     Format:

	  .COPY DUMP:<dev:filename.ex
     or
	  .R PIP
	  *DUMP:<dev:filename.ex/I

     Example:

	  .COPY DUMP:<SYS:FL2

     After typing the command line followed by a carriage return, type the
     initial block number of the area in the specified file you want
     dumped. This causes block number 0000 of the file to automatically be
     dumped. In addition, it also causes the DUMP routine to skip to the
     block number specified, dump it and any block numbers greater than it.

     Because the DUMP handler contains a routine that interacts with the
     keyboard monitor, you can change the block number previously entered
     by typing a new block number on the keyboard. When a new block number
     is specified, the current block number is completely dumped before the
     new block number takes effect.

     If a carriage return is entered following the command line and no
     block number is supplied, the DUMP handler starts at block number 0000
     of the file and dumps all the remaining block numbers in the specified
     file.

     For each block of data (2 memory pages) sent to the LP08 line printer,
     there is a printed page of data followed by a form feed. If an uneven
     number of pages is sent to the line printer during the DUMP operation,
     the odd numbered page printed on the line printer will show only half
     a block (one memory page) of data.

     If an illegal character (excluding 0-7, carriage return, and CTRL/C)
     is typed while entering the block number, a question mark (?) is
     echoed on the terminal. This causes any digits typed before it to be
     ignored and allows you to type in a new block number. If CTRL/C is
     typed while the DUMP handler is running, control returns to the key
     board monitor.

     In addition to the CCL format shown using the COPY command, there is a
     -D option. When specified, this option forces the output device to be
     DUMP:. This option can be used with any CCL command.

				     115



     FORM FEEDS
     A form feed on the LP08 line printer occurs before block 0 data is
     sent to the handler, and after the handler is called to do a close
     (page count of 0).

     ADDING THE DUMP HANDLER TO YOUR SYSTEM
     The DUMP handler can be added to your system the same way any other
     handler is added which is through the BUILD program. Its group name as
     well as its entry point name is DUMP; and the current version of the
     handler is A. This handler does not directly interact with the
     keyboard monitor but contains a routine that performed that function.
     It is a 2-page handler and has no coresident handler. The keyboard
     monitor runs completely overlapped with the LP08 handler.

     FORMAT OF THE DUMP
     At the top left of every printed page in the DUMP listing is a 4-digit
     octal number. This number is the relative file block number of the
     data that is printed on that page. The first column of 4-digit octal
     numbers represents line numbers. Note that each line number is
     followed by a slash (/) which distinguishes it from the remaining eight
     columns. The remaining eight columns represent the actual data words
     located within a specific block in a file. The next column containing
     16 characters is a representation of the eight data words on that
     line. There are two 6-bit characters packed in one word. That is, each
     data word is represented by two ASCII characters.

     The last column containing 12 characters is another representation of
     the eight data words on that line. There are three 8-bit characters
     packed in two words. That is, every two data words is represented by
     three ASCII characters. Note that some of these spaces in this column
     could represent non-printable characters. Any character that is not
     physically on the line printer can be referred to as a non-printable
     character.

     The following listing is an example of a single printed page from a
     DUMP listing.

   0004
   0000/ 7733 2213 0000 1720 7777 1322 0506 6300 ?[KK@@OP??KREF3@ [   P  R F@
   0001/ 1501 6264 7653 1322 0506 6300 2202 6264 MA24>+KREF3@R824 A4<+R F@  4L
   0002/ 7767 1420 2326 0000 0216 8304 7777 2213 ?7LPSV@@BN3D??RK    V @ D
   0003/ 0502 1404 2326 6354 7737 0425 1520 0000 EBLDSV3,?.DUMP@@ B  V L   P 0
   0004/ 0215 6314 7776 0681 0000 0000 1501 6314 BN3L?>FI@@@@MA3L  L  1    AL<
   0005/ 7777 0662 0000 0000 1501 6314 7777 0664 ??F2@@@@MA3L??F4  2    AL< 4
   0006/ 0000 0000 1501 6314 7777 0425 1520 0000 @@@@MA3L??DUMP@@    AL<   P 0
   0007/ 2001 6304 7761 2425 1520 6200 2001 6314 PA3D?lDUMP2@PA3L  DL   P < LL
   0010/ 7762 0663 0000 0000 1501 6314 7777 0665 ?2F3@@@@MA3L??F5  3    AL< 5
   0011/ 0000 0000 1521 6314 7777 0363 0000 0000 @@C@MA3L??C3@@@@    AL<
   0012/ 1601 6314 7777 0361 0000 0000 1501 6314 MA3L??C1@@@@MA3L AL<	   AL<
   0013/ 7777 0362 0000 0000 1501 6314 7777 0364 ??C2@@@@MA3L??C4 	AL<
   0014/ 0000 0000 1501 6314 7777 2262 0000 0000 @@@@MA3L??R2@@@@    AL< 2
   0015/ 1501 6314 7777 2261 0000 0000 1501 6314 MA3L??R1@@@@MA3L AL< 1	   AL<
   0016/ 7777 2263 0000 0000 1501 6314 7777 0365 ??K3~@@@MA3L??C5  3	AL<
   0017/ 0000 0000 1501 6314 7777 0425 1520 6300 @@@@MA3L??DUMP3@    AL<   P@<
   0020/ 2001 6324 7762 0425 1520 6300 0216 6324 PA3T?2DUMP3@BN3T  TL	P@< T

				     116



   0021/ 7776 2266 8070 1623 0216 6324 7777 0425 ?>RF08NSBN3T??DU    8 C T
   0022/ 1520 6400 0216 6324 7776 0425 1520 0000 MP4@BN3T?>DUMP@@ P = T	   P 0
   0023/ 2320 6334 7774 0425 1520 6500 2001 6334 SV3\?<DUMP5@PA3\ V\L	P@= \L
   0024/ 7762 0425 1520 6600 2001 6354 7761 0425 ?2DUMP6@PA3,?1DU    P =  L
   0025/ 1520 6500 0216 6354 7776 0425 1520 6400 MP6@BN3,?>DUMP4@ P =	   P =
   0026/ 2001 6324 7762 0425 1520 6500 0216 6334 PA3T?2DUMP5@BN3\  TL	P@= \
   0027/ 7776 1501 0363 6500 0216 6354 7735 1501 ?>MAC35@BN3,?]MA  A  @	   ] A
   0030/ 0363 6500 2001 6354 7400 0617 1700 0000 C35@PA3,<@FOO@@@  @	L  @ 0
   0031/ 1320 6354 7775 1501 0363 6500 1520 6354 MP3,?=MAC35@MP3, P < A  @ P <
   0032/ 7744 0000 7252 1501 0363 6500 1423 6354 ?$@@:*MAC35@LS3,    *A  @   <
   0033/ 5654 0000 7271 6300 0001 6264 7653 1322 2,@@:93@PA24>+KR , @9@	 4L+R
   0034/ 0300 6300 0216 6264 7767 3000 0000 0000 EF3@BN24?7X@@@@@ F@  4
   0035/ 1501 6264 7777 7252 7277 7304 7440 5300 MA24??:*:?;D< +@ A4< *	?D  @
   0036/ 7666 1234 4000 7235 7241 2422 7666 1234 >6J\@:]:!TR>6J\  6	!  6
   0037/ 4000 7235 7241 2422 4000 7235 7241 2422 @:]:!TR@:]:!TR	     !     !









































				     117





								 APPENDIX M

					      RKLFMT DISK FORMATTER PROGRAM


     M.1  INTRODUCTION
     This appendix describes the procedure for formatting a RK05 disk using
     the RKLFMT program. The RK8E/RK8L disk formatter program is designed
     to write and check the format of the complete disk cartridge. Only
     standard Digital surface format is available (i.e., sectors numbered
     in the normal numerical sequence 0, 1, 2, 3, 4, 5, etc.). The program
     occupies locations 0000 to 4177 of the current field.

     Restrictions, using this program, are that the RK8L control which can
     control up to 8 drives, will not run with the DW8E bus adapter. This
     is because the RK8L control uses IOT0 for extended drives 4-7 which is
     not available on the DW8E.

     Hardware requirements are as follows:

	  1.  PDP 8/E, 8/F, 8/M or 8/A Computer
	      Other family of 8-compatible computer with necessary DW8E bus
	      adapter for RK8E control only.
	  2.  At least 4K of read/write memory, and at least 8K of memory is
	      needed for operation of the console package.
	  3.  ASR-33 teletype or equivalent
	  4.  RK8E disk control or RK8L disk control
	  5.  RK05J or RK05F disk drive(s)

				     NOTE
		The RK05F drive is considered as two separate
		units. When answering all questions each
		separate unit must be specified: DSK0?,
		DSK1?, DSK2?, etc.


     M.2  RUNNING THE PROGRAM
     To format an RK05, type the following command:

	  .R RKLFMT	   _

     Mount the disk (write enabled), and the instructions in the program
     that follow.

     If the formatter program fails to operate correctly, run the following
     programs:

	  1.  All basic and extended memory diagnostics
	  2.  For the RK8E control, run the RK8E diskless control test and
	      the RK8E drive control test.
	  3.  For the RK8L control, run the RK8L instruction test.



				     118



     M.3  STANDARD TEST PROCEDURES
     To run the formatter program, follow the procedure in Section M.4. The
     following two procedures describe the drive setup procedure for the
     RK05F and the drive cartridge mounting procedure for the RK05J.


     M.3.1 RK05J Drive Cartridge Mounting Procedure
     The following is the correct cartridge mounting procedure for the
     RK05J disk drive. Any deviation encountered during this procedure
     is considered an error condition.

	  a.  Set switch labeled "RUN/LOAD" to the "LOAD" position.
	  b.  Turn AC power on.
	  c.  Verify that light labeled "PWR" is on.
	  d.  Wait for light labeled "LOAD" to come on.
	  e.  Verify that lights labeled "RDY", "ON CYL", "FAULT", "WT",
	      and "RD" are off.
	  f.  Open access door.
	  g.  Insert cartridge.
	  h.  Close access door.
	  i.  Set switch labeled "RUN/LOAD" to the "RUN" position.
	  j.  Wait for lights labeled "RDY" and "ON CYL" to come on.
	  k.  Toggle switch labeled "WT PROT" and verify that the light
	      labeled "WT PROT" goes on and off.
	  l.  Toggle switch labeled "WT PROT" until light labeled "WT PROT"
	      goes off.
	  m.  Verify that lights labeled "FAULT", "WT", "RD", and "LOAD"
	      are off.


     M.3.2  RK05F Drive Setup Procedure
     The following is the correct drive setup procedure for the RK05F disk
     drive. Any deviation encountered during this procedure is considered
     an error condition.

	  a.  Set switch labeled "RUN/LOAD" to the "LOAD" position.
	  b.  Turn AC power on.
	  c.  Verify that light labeled "PWR" is on.
	  d.  Wait for light labeled "LOAD" to come on.
	  e.  Verify that lights labeled "RDY", "ON CYL", "FAULT", "WT",
	      and "RD" are off.
	  f.  Set switch labeled "RUN/LOAD" to the "RUN" position.
	  g.  Wait for lights labeled "RDY" and "ON CYL" to come on.
	  h.  Toggle switch labeled "WT PROT" and verify that the light
	      labeled "WT PROT" goes on and off.
	  i.  Toggle switch labeled "WT PROT" until light labeled "WT PROT"
	      goes off.
	  j.  Verify that lights labeled "FAULT", "WT", "RD", and "LOAD"
	      are off.


     M.4  FORMAT PROGRAM
	  a.  Make all drives ready to be formatted:



				     119



	      For RK05J drives use the RK05 drive mounting procedure
	      (M.3.1).

	      For RK05F drives use the RK05 drive setup procedure (M.3.2).

	  b.  Set switch labeled "RUN/LOAD" to the "LOAD" position on all
	      drives not being formatted.

	      The TTY will type the following program name, information,
	      and question.

		  RK8E/RK8L DISK FORMATTER PROGRAM

	      For all questions answer Y for YES or N for NO.

		  FORMAT DISK 0?

	  c.  If the operator desires to format disk 0, type Y for YES,
	       otherwise, N for NO, on the TTY keyboard. The following
	       question is then typed on the TTY.

		  FORMAT DISK 1?

	  d.  If the operator desires to format disk 1, type Y for YES,
	      otherwise, N for NO, on the TTY keyboard. The following
	      question is then typed on the TTY.

		  FORMAT DISK 2?

	  e.  If the operator desires to format disk 2, type Y for YES,
	      otherwise, N for NO, on the TTY keyboard. The following
	      question is then typed on the TTY.

		  FORMAT DISK 3?

	  f.  If the operator desires to format disk 3, type Y for YES,
	      otherwise, N for NO, on the TTY keyboard. The following
	      question is then typed on the TTY.

		  FORMAT DISK 4?

	  g.  If the operator desires to format disk 4, type Y for YES,
	      otherwise, N for NO, on the TTY keyboard The following
	      question is then typed on the TTY.

		  FORMAT DISK 5?

	  h.  If the operator desires to format disk 5, type Y for YES,
	      otherwise, N for NO, on the TTY keyboard. The following
	      question is then typed on the TTY.

		  FORMAT DISK 6?

	  i.  If the operator desires to format disk 6, type Y for YES,
	      otherwise, N for NO, on the TTY keyboard. The following

				     120



	      question is then typed on the TTY.

		  FORMAT DISK 7?

	  j.  If the operator desires to format disk 7, type Y for YES,
	      otherwise, N for NO, on the TTY keyboard. The following
	      question is then typed on the TTY.

		  ARE YOU SURE?

	  k.  Typing N for NO causes the repetition of all the previous
	      questions. Typing Y for YES, results in execution of the
	      operation selected.

	  l.  Program execution is approx. 80 seconds per disk drive. After
	      all disks selected have been formatted and checked, the TTY
	      types the following pass complete message and question.

		  RK8E/RK8L DISK FORMATTER PASS COMPLETE
		  FORMAT SAME DISK(S) AGAIN?

	  m.  If the operator desires to repeat the operation selected,
	      type Y for YES. Typing N for NO causes the repetition of the
	      initial start-up questions.


     M.5  ERRORS
     When a recoverable error occurs the TTY prints an "ERROR HEADER" and
     error information pertaining to the failure.

     Possible error headers are as follows:

	  DISK DATA ERROR
	  READ STATUS ERROR
	  WRITE STATUS ERROR
	  RECALIBRATE STATUS ERROR

     After the error header mentioned above is typed, the TTY prints some
     of the following error information pertaining to the failure.

	  PC:	Program Location of Failure
	  GD:	Expected Information
	  EX:	Extended Drive Bit
	  CM:	Software Command Register
	  ST:	Contents of Status Register
	  DA:	Software Cylinder, Surface, and Sector Register
	  CA:	Initial Current Address
	  AD:	Address of Data Break
	  DT:	Data Found During Data Break

     After the error information is typed, the TTY types one of the
     following questions asking the error recovery desired.

	  1.  If the error was a recalibrate error, the following question
	      is typed.

				     121



		  TRY TO RECALIBRATE SAME DISK AGAIN?

	      Typing a Y for YES causes the repetition of the recalibrate
	      sequence on the disk in error. Typing N for NO results in
	      progressing to the next available disk.

	  2.  If the error was a write error the following question is
	      typed.	

		  TRY TO FORMAT SAME CYLINDER AGAIN?

	      Typing Y for YES results in a repeat of the write sequence on
	      the current cylinder. Typing N for NO causes progressing to
	      the next sequential cylinder.

	  3.  If the error was a read or check error the following question
	      is typed.

		  TRY TO CHECK SAME CYLINDER AGAIN?

	      Typing a Y for YES causes the repetition in the read and
	      check sequence on the current cylinder. Typing a N for NO
	      results in progressing to the next sequential cylinder.


     M.6  PROGRAM DESCRIPTION
     The formatting is actually a function of the RK8E or RK8L control and
     drive logic. The program writes data on every sector in the "WRITE
     ALL" mode, then checks the data while in the "READ DATA" mode to
     verify that the header words written on every sector are also correct.
     The "READ DATA MODE" automatically performs a check header function.

     The first two words of every sector are set to the absolute disk
     address (i.e. command register bits 9-11 and cylinder, surface, and
     sector bits 0-11, respectively). The remainder of the data area is set
     to all zeros when the data is written. Only the first two words of
     every sector (i.e., the addressing information) are checked when data
     is read in the "READ DATA" mode.


     M.7  CONTROL CHARACTERS
     Control characters are used to give the operator the ability to
     perform the following functions.

				     NOTE
		The program will respond to the control character
		in five seconds or less.


	  CTRL/C	Starts the monitor at location 7600.

	  CTRL/R	Restarts the program.

	  CTRL/E	Continues the program from an error if allowed by
			the diagnostic or from a waiting statement.

				     122



	  CTRL/L	Switches the terminal messages from the display to
			a line printer. To restore the messages on the
			terminal, CTRL/L must be typed again. If no printer
			is available and CTRL/L is typed the result is that
			the console package will wait for CTRL/C or R. The
			CTRL/L sends output to the line printer and the
			program attempts to continue as if a CTRL/E was
			typed in.

	  CTRL/D	Allows you to change the switch register during
			program operation. Typing this character results in
			an interrogation of the switch register question.

	  CTRL/S	Stops program execution and waits in a loop for a
			continue. The only way to continue is to type a
			CTRL/Q, R or C. This is a nonprinting character.

	  CTRL/Q	This causes continuation of a program after a
			CTRL/S is typed. This is a nonprinting character.



     M.8  MISCELLANEOUS


     M.8.1  Waiting Message
     The waiting message allows the operator time to make a decision as to
     what control character to type. This message appears at the end of
     pass message if the halt on pass bit is set. The control characters
     may now be used to perform the needed function.

     The waiting message is printed after an error message if the halt on
     error bit is set. Here again the control characters may be used.

     The waiting message is printed if operator intervention is required.


     M.8.2  End of Pass
     The normal program pass complete as described in Section M.4 is used.


     M.8.3  Errors
     The standard error reports previously described in Section M.5 are
     used.


     M.8.4  Location Changes
     The following locations can be changed to meet the specific need for
     modification of the diagnostic.

	  3637 	Is the location set for the number of filler characters
		after a CRLF set to four (4)




				    123


						   OS/8 Handbook Update
						   DEC-S8-OSHBA-A-DN4


			       READER'S COMMENTS


       NOTE:  This form is for document comments only.  DIGITAL will use
	      comments submitted on this form at the company's discretion.
	      problems with software should be reported on a Software
	      Performance Report (SPR) form. If you require a written reply
	      and are eligible to receive one under Software Performance
	      Report (SPR) service, submit your comments on an SPR form.


    Did you find errors in this manual?  If so, specify by page.
    ______________________________________________________________________
    ______________________________________________________________________
    ______________________________________________________________________
    ______________________________________________________________________
    ______________________________________________________________________

    Did you find this manual understandable, usable, and well-organized?
    Please make suggestions for improvement.
    ______________________________________________________________________
    ______________________________________________________________________
    ______________________________________________________________________
    ______________________________________________________________________
    ______________________________________________________________________

    Is there sufficient documentation on associated system problems
    required for the use of the software described in this manual ? If
    not, what material is missing and where should it be placed?
    ______________________________________________________________________
    ______________________________________________________________________
    ______________________________________________________________________
    ______________________________________________________________________
    ______________________________________________________________________

    Please indicate the type of user/reader that you most nearly represent.

	 []  Assembly language programmer
	 []  Higher-level language programmer
	 []  Occasional programmer (experienced)
	 []  User with little programming experience
	 []  Student programmer
	 []  Other (please specify) _______________________________________


     Name______________________________________Date________________________

     Organization__________________________________________________________

     Street________________________________________________________________

     City__________________________State_____________Zip Code______________
							or
						     Country





















     -------------------------------Fold Here------------------------------

















     -----------------Do Not Tear - Fold Here and Staple-------------------

							  +---------------+
							  |  FIRST CLASS  |
							  | PERMlT NO. 33 |
							  | MAYNARD. MASS.|
							  +---------------+
	BUSINESS REPLY MAIL					   ========
	NO POSTAGE STAMP NECESSARY IF MAILED IN THE UNITED STATES  ========
     ======================================================================
	Postage will be paid by:				   ========
								   ========
			  +-+-+-+-+-+-+-+			   ========
			  |d|i|g|i|t|a|l|			   ========
			  +-+-+-+-+-+-+-+			   ========
								   ========
		      Software Communications			   ========
		      146 Main Street  ML5-5/E39		   ========
		      Maynard, Massachusetts  01754		   ========