MACLNKUM.DOC



				  MACREL/LINK
				 User's Manual

			     Order No. AA-5664B-TA

















                                  DISCLAIMER

                This document file was created by scanning  the
                original  document and then editing the scanned
                text.  As much as possible, the  original  text
                format  was restored.  Some format changes were
                made to insure this  document  would  print  on
                current laser printers using 60 lines per page.
                The  original  spelling  and  grammar  has been
                preserved.


                1-Mar-1997





						 MACREL/LINK
						User's Manual

					    Order No. AA-5664B-TA














				 January 1979


	      This document is the user's manual for MACREL/LINK, 
	      a PDP-8 macro assembly language and linking loader. 
	      The manual completely describes all operating 
	      instructions, language elements, directives and 
	      options. Examples and demonstration programs are 
	      contained throughout the manual.









     SUPERSESSION/UPDATE INFORMATION:	This document completely supersedes
					its predecessor AA-5664A-TA.

     OPERATING SYSTEM AND VERSION:	OS/8 V3D and subsequent versions.

     SOFTWARE AND VERSION:		MACREL Version 2D
					LINK Version 2B
					CREF Version 2A
					OVRDRV Version 2A





     ---------------------------------------------------------------------
     |  To order additional copies of this manual, contact the Software  |
     |  Distribution Center, Digital Equipment Corporation, Maynard,     |
     |  Massachusetts 01754						 |
     ---------------------------------------------------------------------

	    digital equipment corporation - maynard. massachusetts


					       First Printing, October 1977
					       Revised:	       January 1979


     The information in this document is subject to change without notice
     and should not be construed as a commitment by Digital Equipment
     Corporation. Digital Equipment Corporation assumes no responsibility
     for any errors that may appear in this document. 

     The software described in this document is furnished under a license
     and may only be used or copied in accordance with the terms of such
     license.

     No responsibility is assumed for the use or reliability of software on
     equipment that is not supplied by DIGITAL or its affiliated companies.








     Copyright (c) 1977, 1979 by Digital Equipment Corporation







     The postage-prepaid READER'S COMMENTS form on the last page of this
     document requests the user's critical evaluation to assist us in pre-
     paring future documentation.


     The following are trademarks of Digital Equipment Corporation:



	      DIGITAL		  DECsystem-10	      MASSBUS
	      DEC		  DECtape	      OMNIBUS
	      PDP		  DIBOL		      OS/8
	      DECUS		  EDUSYSTEM	      PHA
	      UNIBUS		  FLIP CHIP	      RSTS
	      COMPUTER LABS	  FOCAL		      RSX
	      COMTEX		  INDAC		      TYPESET-8
	      DDT		  LAB-8		      TYPESET-11
	      DECCOMM		  DECSYSTEM-20	      TMS-11
	      ASSIST-11		  RTS-8		      ITPS-10
	      VAX		  VMS		      SBI
	      DECnet		  IAS






				   CONTENTS


								       Page

     PREFACE							       xi

     CHAPTER  1	       INTRODUCTION				       1-1

	      1.1      MACREL FEATURES				       1-1
	      1.1.1	 Relocation				       1-1
	      1.1.2	 Macros					       1-2
	      1.1.3	 Directives				       1-3
	      1.2      OVERVIEW OF ASSEMBLY AND RELOCATABLE LOADING    1-3
	      1.2.1	 Assembling with MACREL			       1-3
	      1.2.2	 Linking with LINK			       1-4
	      1.3      COMPATIBILITY OF MACREL WITH PAL8	       1-4
	      1.3.1	 MACREL: Differences from PAL8		       1-5
	      1.3.1.1	 Dollar Sign ($)			       1-5
	      1.3.1.2	 DTORG					       1-5
	      1.3.1.3	 MACREL and Literals			       1-5
	      1.3.1.4	 PAUSE					       1-5
	      1.3.1.5	 Closing Literal Expressions		       1-5
	      1.3.1.6	 Terminal Support			       1-6
	      1.3.1.7	 PAL8 Run-Time Options			       1-6
	      1.4      ASSEMBLING EXISTING PAL8 PROGRAMS WITH MACREL   1-6
	      1.5      INTRODUCTION TO MACREL RELOCATION	       1-7
	      1.5.1	 Source Modules				       1-7
	      1.5.2	 Program Sections			       1-7
	      1.5.3	 Fundamentals of Relocatable Programming       1-10
	      1.5.4	 Example of Communication Between Program
			 Sections				       1-13
	      1.5.4.1	 A Sample Program			       1-13
	      1.5.4.2	 Program Operation			       1-16
	      1.5.4.3	 Effects of Relocation on the Program	       1-17
	      1.5.4.4	 The Symbol Table			       1-18
	      1.5.5	 Relocation Type			       1-18
	      1.5.5.1	 Absolute Expressions			       1-19
	      1.5.5.2	 Simple Relocation Expressions		       1-19
	      1.5.5.3	 CDF/CIF Relocation Expressions		       1-19
	      1.5.5.4	 .FSECT Relocation Expressions		       1-19
	      1.5.5.5	 Complex Relocation Expressions		       1-19
	      1.6      THE ASSEMBLY PROCESS			       1-20
	      1.6.1	 Pass One -- Symbol Definition Pass	       1-20
	      1.6.2	 Pass Two -- Binary Code Generation Pass       1-21
	      1.6.3	 Pass Three -- Listing Pass		       1-21
	      1.6.4	 Pass Four -- Cross-Reference (KREF) Listing
			 Pass					       1-21
	      1.7      THE LINKING PROCESS			       1-22
	      1.7.1	 Pass One -- Linking			       1-22
	      1.7.2	 Pass Two -- Loading			       1-22


				      iii



			       CONTENTS (Cont.)

								       Page

     CHAPTER  2	       MACREL SOURCE PROGRAM FORMAT		       2-1

	      2.1      MACREL STATEMENTS			       2-1
	      2.1.1	 Labels					       2-1
	      2.1.2	 Instructions, Directives or Data	       2-1
	      2.1.3	 Comments				       2-2
	      2.2      FORMAT EFFECTORS				       2-2
	      2.2.1	 Form Feed				       2-2
	      2.2.2	 Tabulations				       2-2
	      2.2.3	 Statement Terminators			       2-2

     CHAPTER  3        THE PDP-8 MACHINE INSTRUCTION SET	       3-1

	      3.1      MEMORY REFERENCE INSTRUCTIONS		       3-1
	      3.1.1	 Addressing Modes			       3-2
	      3.2      MICROINSTRUCTIONS			       3-3
	      3.2.1	 Operate Microinstructions		       3-3
	      3.2.2	 Input/Output Transfer Microinstructions       3-5
	      3.3      AUTOINDEXING				       3-5
	      3.4      STANDARD INSTRUCTION SET			       3-6
	      3.5      CONSTANTS				       3-10

     CHAPTER  4        EXPRESSIONS AND THEIR COMPONENTS		       4-1

	      4.1      MACREL CHARACTER SET			       4-1
	      4.1.1	 Alphanumeric Characters		       4-1
	      4.1.2	 Special Characters and Operators	       4-1
	      4.2      SYMBOLS					       4-2
	      4.2.1	 Permanent Symbols			       4-3
	      4.2.2	 Program-Defined Symbols		       4-4
	      4.2.3	 Labels					       4-4
	      4.2.4	 Local Symbols				       4-6
	      4.2.5	 Backslash (\) Special Operator		       4-7
	      4.2.6	 Symbols and Relocation			       4-9
	      4.3      DIRECT ASSIGNMENT STATEMENT		       4-9
	      4.4      CURRENT LOCATION COUNTER			       4-11
	      4.5      LITERALS					       4-11
	      4.5.1	 Current Page Literals			       4-11
	      4.5.2	 Page Zero Literals			       4-14
	      4.6      NUMBER REPRESENTATION			       4-15
	      4.6.1	 Uparrow B (^B) -- Binary Representation       4-15
	      4.6.2	 Uparrow D (^D) -- Decimal Representation      4-16
	      4.6.3	 Uparrow O (^O) -- Octal Representation	       4-16
	      4.6.4	 Period (.) -- Decimal Representation	       4-16
	      4.7      ASCII DATA REPRESENTATION		       4-16
	      4.7.1	 Double Quote (") -- ASCII Representation      4-17
	      4.7.2	 Single Quote (') -- ASCII Pair		       4-17
	      4.7.3	 Uparrow Double Quote (^") -- Control
	      		 Character Representation		       4-18
	      4.8      MACREL ARITHMETIC OPERATORS		       4-18
	      4.8.1	 Plus Sign (+) -- Addition		       4-18

				      iv



			       CONTENTS (Cont.)

								       Page

	      4.8.2	 Minus Sign (-) -- Subtraction		       4-19
	      4.8.3	 Uparrow (^) -- Multiplication		       4-19
	      4.8.4	 Percent Sign (%) -- Division		       4-19
	      4.8.5	 Ampersand (&) -- Boolean AND		       4-20
	      4.8.6	 Exclamation Point (') -- Inclusive OR (or
			 Shift)					       4-20
	      4.8.7	 Space ( ) and Tab -- Inclusive OR	       4-20
	      4.9      SPECIAL OPERATORS			       4-21
	      4.9.1	 Memory Reference Instructions		       4-22
	      4.9.2	 I -- Indirect Addressing		       4-23
	      4.9.3	 Z -- Page Zero Addressing		       4-24
	      4.9.4	 CIF and CDF Instructions		       4-24
	      4.9.5	 EDF -- Evaluate Data Field		       4-25
	      4.9.6	 .FLD					       4-26
	      4.9.7	 XEDF					       4-26
	      4.9.8	 .LEVEL					       4-27
	      4.10     EXPRESSION EVALUATION AND SYNTAX		       4-27
	      4.10.1	 Operator Precedence and Order of Evaluation   4-28
	      4.11     USES OF EXPRESSIONS			       4-29
	      4.12     EXPRESSIONS AND RELOCATION		       4-30

	CHAPTER 5      MACREL DIRECTIVES			       5-1

	      5.1      ASSEMBLY LISTING AND BINARY OUTPUT CONTROL
		       DIRECTIVES				       5-1
	      5.1.1	 Assembly Listing Control Directives	       5-2
	      5.1.1.1	 .LIST and .NOLIST			       5-2
	      5.1.1.2	 .TITLE					       5-3
	      5.1.1.3	 .SBTTL					       5-4
	      5.1.1.4	 .LISTWD Special Variable		       5-4
	      5.1.2	 Other PAL8 Directives			       5-5
	      5.1.2.1	 XLIST					       5-5
	      5.1.2.2	 EJECT					       5-5
	      5.1.2.3	 NOPUNCH and ENPUNCH			       5-6
	      5.2      RADIX CONTROL DIRECTIVES			       5-6
	      5.2.1	 .RADIX					       5-6
	      5.2.2	 Other PAL8 Directives			       5-7
	      5.3      DATA STORAGE DIRECTIVES			       5-7
	      5.3.1	 ZBLOCK					       5-7
	      5.3.2	 TEXT					       5-8
	      5.3.2.1	 Simple Form of the TEXT Directive	       5-8
	      5.3.2.2	 Complex Form of the TEXT		       5-10
	      5.3.2.3	 TEXT Options				       5-11
	      5.4      CODE LOCATION DIRECTIVES			       5-13
	      5.4.1	 Asterisk (*)				       5-14
	      5.4.2	 PAGE					       5-16
	      5.4.3	 FIELD					       5-17
	      5.4.3.1	 FIELD Directive in Named Program Sections     5-17
	      5.4.3.2	 FIELD Directive in Unnamed Program Sections   5-18
	      5.4.4	 RELOC					       5-19
	      5.5      CONDITIONAL ASSEMBLY DIRECTIVE		       5-20

				       v



			       CONTENTS (Cont.)

								       Page

	      5.5.1	 Nested Conditional Assembly Directives	       5-23
	      5.5.2	 Other PAL8 Conditional Assembly Directives    5-24
	      5.6      ASSEMBLY CHAINING DIRECTIVES		       5-24
	      5.6.1	 .INCLUDE				       5-24
	      5.6.2	 .CHAIN					       5-25
	      5.7      USER SERVICE ROUTINE (USR) COMMUNICATION
		       DIRECTIVES				       5-26
	      5.7.1	 DEVICE					       5-26
	      5.7.2	 FILENAME				       5-26
	      5.8      LOADING INFORMATION DIRECTIVES		       5-27
	      5.8.1	 .START					       5-27
	      5.8.2	 .JSW					       5-28
	      5.8.3	 .VERSION				       5-29
	      5.9      SYMBOL TABLE MODIFICATION DIRECTIVES	       5-29
	      5.9.1	 EXPUNGE				       5-29
	      5.9.2	 FIXMRI					       5-31
	      5.9.3	 FIXTAB					       5-32
	      5.10     STACK MANIPULATION DIRECTIVES		       5-33
	      5.10.1	 .PUSH					       5-33
	      5.10.2	 .POP					       5-34
	      5.11     ASSEMBLY OPTIONS DIRECTIVES		       5-34
	      5.11.1	 .ENABLE				       5-35
	      5.11.2	 .DISABL				       5-37
	      5.11.3	 .ENABWD Special Variable		       5-37

     CHAPTER  6	       MACRO AND REPEAT DIRECTIVES		       6-1

	      6.1      MACRO DEFINITIONS			       6-3
	      6.1.1	 .MACRO and .ENDM Directives		       6-3
	      6.2      MACRO CALLS				       6-6
	      6.3      MACRO ARGUMENTS				       6-7
	      6.3.1	 Actual Arguments			       6-7
	      6.3.2	 Substrings of the Argument		       6-9
	      6.3.2.1	 .NCHAR Special Operator		       6-10
	      6.3.3	 Symbols and Names in Macros		       6-11
	      6.3.4	 Apostrophe (') Special Operator	       6-12
	      6.4      NESTED MACROS				       6-13
	      6.4.1	 Nested Macro Definitions		       6-13
	      6.4.2	 Nested Macro Calls			       6-14
	      6.4.3	 .MEXIT Directive			       6-15
	      6.4.4	 Concatenation in Nested Macros		       6-16
	      6.5      CONDITIONAL ASSEMBLY DIRECTIVES IN MACROS       6-16
	      6.5.1	 Nested Conditional Source Code in Macros      6-17
	      6.5.2	 .NARGS Special Operator		       6-19
	      6.6      DEFINING AND CALLING REPEAT BLOCKS	       6-19
	      6.6.1	 .REPT and .ENDR Directives		       6-20
	      6.6.2	 Nested Repeats				       6-20

     CHAPTER  7        RELOCATION				       7-1

	      7.1      THE PROGRAM SECTION DIRECTIVES		       7-2

				      vi



			       CONTENTS (Cont.)

								       Page

	      7.1.1	 Unnamed Program Sections		       7-4
	      7.1.2	 .ASECT					       7-4
	      7.1.3	 .RSECT					       7-5
	      7.1.4	 .ZSECT					       7-6
	      7.1.5	 .XSECT					       7-7
	      7.1.6	 .DSECT					       7-9
	      7.1.7	 .FSECT					       7-10
	      7.1.8	 Summary of Relocation Performed by LINK       7-12
	      7.1.9	 .SECT * Directive			       7-13
	      7.2      INTER-MODULE COMMUNICATION DIRECTIVES AND
		       SPECIAL OPERATORS			       7-14
	      7.2.1	 .EXTERNAL				       7-14
	      7.2.2	 .ZTERNAL				       7-15
	      7.2.3	 .GLOBAL and ==				       7-16
	      7.2.4	 .SECREF				       7-17
	      7.2.5	 .ENTRY					       7-17
	      7.2.6	 CDF Special Operator			       7-18
	      7.2.7	 CIF Special Operator			       7-19
	      7.3      HOW TO WRITE RELOCATABLE CODE		       7-21

     CHAPTER  8        USING MACREL AND KREF			       8-1

	      8.1      RUNNING MACREL				       8-1
	      8.1.1	 MACREL Command String			       8-1
	      8.1.2	 MACREL Command String Examples		       8-4
	      8.1.3	 MACREL Terminal Error Messages		       8-5
	      8.1.3.1	 Run-Time Control Commands		       8-5
	      8.1.3.2	 Default Terminal Conditions		       8-6
	      8.1.3.3	 Terminal Message Format		       8-6
	      8.1.4	 Listing Error Messages			       8-7
	      8.1.5	 Program Listing Format			       8-7
	      8.1.5.1	 Line Number Column			       8-8
	      8.1.5.2	 Current Location Counter Value Column	       8-8
	      8.1.5.3	 Absolute Assembled Value Column	       8-9
	      8.1.6	 Symbol Table Format			       8-10
	      8.1.7	 Example Program Listing		       8-11
	      8.1.7.1	 Assembly Listing			       8-11
	      8.1.8	 Symbol Table Listing			       8-14
	      8.2      RUNNING KREF				       8-15
	      8.2.1	 KREF Command String			       8-15
	      8.2.2	 Description and Example of KREF Listing       8-15

     CHAPTER  9        USING LINK				       9-1

	      9.1      RUNNING LINK				       9-1
	      9.1.1	 LINK Command String			       9-1
	      9.1.2	 LINK Command String Example		       9-3
	      9.2      RULES FOR USING OVERLAY OPTIONS		       9-3
	      9.3      LINK LIBRARIES				       9-6
	      9.4      LINK ERROR MESSAGES			       9-7
	      9.5      LINK LOAD MAP DESCRIPTION AND EXAMPLE	       9-11

				      vii



			       CONTENTS (Cont.)

								       Page

     CHAPTER  10       ADVANCED TECHNICAL TOPICS		       10-1

	      10.1     MACREL SYMBOL TABLE SIZE			       10-1
	      10.2     RELOCATABLE BINARY OBJECT MODULE FORMAT	       10-2
	      10.2.1	 LSD Preface				       10-2
	      10.2.2	 LSD Description			       10-3
	      10.2.3	 Text Description			       10-4
	      10.2.3.1	 Flag Field Meaning			       10-5
	      10.2.3.2	 Loader Codes Generated by MACREL	       10-5
	      10.3     LINK PERFORMANCE				       10-8
	      10.3.1	 LINK Processing of Program Section
			 Definitions				       10-8
	      10.4     LINK LIBRARY				       10-8
	      10.5     WRITING AND USING OVERLAYS		       10-9
	      10.5.1	 Writing Overlay Code			       10-10
	      10.5.2	 How Overlays Work			       10-13
	      10.5.3	 Overlay Driver				       10-14
	      10.6     SAVE FILE FORMAT				       10-14
	      10.7     MACRO LIBRARY				       10-17
	      10.8     SETTING THE CURRENT LOCATION COUNTER TO AN
		       UNKNOWN VALUE				       10-18

     APPENDIX A	       ASCII CHARACTER SET			       A-1

     APPENDIX B        MACREL-PAL8 COMPATIBILITY SUMMARY	       B-1

     APPENDIX C        MACREL PERMANENT SYMBOL TABLE		       C-1

     APPENDIX D        MACREL DIAGNOSTIC ERROR MESSAGES		       D-1

     INDEX							   Index-1




				    FIGURES


     FIGURE   1-1      Program Sections and Modules		       1-10
	      1-2      Example of Communication Between Program
		       Sections					       1-13
	      3-1      Memory Reference Instruction Bit Assignments    3-2
	      3-2      Group 1 Operate Microinstruction Bit
		       Assignments				       3-3
	      3-3      Group 2 Operate Microinstruction Bit
		       Assignments				       3-4
	      3-4      Group 3 Operate Microinstruction Bit
		       Assignments				       3-4
	      3-5      Extended Memory Bit Mapping for CDF and
		       CIF Instructions				       3-10
	      4-1      Extended Memory Field Bit Layout for XEDF       4-27

				     viii



			       CONTENTS (Cont.)

								       Page

				FIGURES (Cont.)

	      4-2      BIT Assignments for .LEVEL Special Operator     4-27
	      5-1      Example of TEXT Option Processing	       5-12
	      6-1      Macro Definition and Storage		       6-5
	      6-2      Macro Expansion				       6-7
	      6-3      Example of Nested Conditional Source Code
		       in Macros				       6-18
	      6-4      Example of a Nested Repeat Block		       6-22
	      6-5      Example of the Expansion of a Nested Repeat
		       Block					       6-23
	      8-1      Example Program Listing			       8-11
	      8-2      Example of Symbol Table Listing		       8-14
	      8-3      Example of KREF Listing			       8-16
	      9-1      Example of LINK Load Map			       9-12
	      10-1     Object Module Format			       10-2
	      10-2     LSD Entry Format				       10-4
	      10-3     Flag Words				       10-4
	      10-4     Loader Code				       10-5
	      10-5     Library File Format			       10-9
	      10-6     MACREL/LINK Overlay Structure (numbers in
		       octal)					       10-11
	      10-7     Permissible JMS's Between MAIN and Overlays     10-12
	      10-8     Transfer Vector Table			       10-13
	      10-9     Memory Control Block			       10-15
	      10-10    Memory Segment Double Words		       10-16
	      10-11    Overlay Storage				       10-16



				    TABLES


     TABLE    1-1      Types of Sections			       1-8
	      4-1      Special Characters and Operators		       4-2
	      4-2      Processing of CDF/CIF Expressions	       4-25
	      4-3      Relocation Types Resulting from Addition and
		       Subtraction Operations			       4-30
	      4-4      Relocation Types Resulting from Other
		       Arithmetic Operations			       4-31
	      5-1      .LIST and .NOLIST Options		       5-2
	      5-2      .LISTWD Bit Assignments			       5-5
	      5-3      FIELD Directive Processing for Named Program
		       Sections					       5-18
	      5-4      Conditions for the .IF Conditional Assembly
		       Directive				       5-22
	      5-5      .ENABLE Directive Options		       5-36
	      5-6      .DISABL Directive Options		       5-37
	      5-7      .ENABWD Bit Assignments			       5-39
	      7-1      Types of Program Sections		       7-3
	      7-2      Summary of Program Section Relocation	       7-12

				      ix



			       CONTENTS (Cont.)

								       Page

				TABLES (Cont.)

	      8-1      MACREL Command String Options		       8-2
	      8-2      Terminal/Control Commands		       8-6
	      8-3      MACREL Error Codes			       8-8
	      8-4      Symbol Table Descriptor Codes		       8-10
	      9-1      LINK Control Options			       9-4
	      9-2      LINK Error Messages			       9-7
	      9-3      LINK-Detected System Errors		       9-9
	      10-1     MACREL Symbol Table Size			       10-1
	      10-2     LSD Preface				       10-3
	      10-3     MACREL/LINK Loader Codes			       10-5
	      10-4     Extended MACREL/LINK Loader Codes	       10-7
	      10-5     LINK Symbol Table Size			       10-8
	      A-1      ASCII Character Set			       A-1





































				       x







				    PREFACE



     ASSUMPTIONS REGARDING READER KNOWLEDGE

     To use this manual effectively, you must be familiar both  with  PDP/8
     computer  hardware and with assembly-language programming.  You should
     also be familiar with OS/8 system operation, and its vocabulary.

     The manual provides some tutorial information, but assumes you have  a
     general  background  in  the  above areas.  If necessary, refer to the
     following documents for more information on any of these topics.


     DOCUMENTS REFERENCED IN THE TEXT

     The following documents are referenced in the text:

	  PDP-8/A Minicomputer Handbook	  _____________________________

	  PDP-8/E, PDP 8/M & PDP 8/F Small Computer Handbook	  __________________________________________________

	  OS/8 Handbook	  _____________

	  OS/8 Software Support Manual	  ________________________________

	  OS/78 Handbook	  ______________


     ABOUT THIS MANUAL

     The MACREL/LINK User's Manual describes the MACREL assembler  and  the	 _________________________
     linking  loader  LINK and discusses how to write programs using MACREL
     and how to link the resulting object modules together with LINK.

     If  you  are  an  inexperienced  PDP8  programmer,  read  the   manual
     sequentially, beginning with Chapter 1.

     For the experienced PAL8 assembly language programmer, the manual also
     explains  the  differences  between MACREL and older PDP/8 assemblers.
     Read the manual straight through, and skip over any material  that  is
     obvious (discussion of literals, etc.).  In particular, begin with the
     Introduction, which outlines the new features of MACREL  and  provides
     an  introduction  to  relocation.   This  introduction is necessary to
     understand the rest of the manual.  Chapter 2, Source Program  Format,
     describes  the rules for formatting a MACREL source program, and shows
     some  new  features  in  MACREL  assembly  listings.   Chapter 3,  the
     Instruction  Set, may be skipped.  Chapter 4, Symbols and Expressions,
     contains some new MACREL features plus a discussion of how  relocation
     affects  symbols,  the  current  location  counter,  direct assignment

				      xi



     statements, and expressions.   Chapter 5,  Directives,  describes  the
     general  assembler  directives  (referred  to  as  pseudo-operators in
     PAL8).  Chapter 6 describes macros and how to use  them.   Chapter  7,
     Relocation,  describes  the  relocation  features  and  how  to  write
     relocatable programs.  Chapters 8 and 9 explain how to run MACREL  and
     LINK, respectively.  Chapter 10 discusses certain advanced programming
     techniques. 



     For the Inexperienced PDP-8 Assembly Language Programmer

     If  you  are  unfamiliar  with  assembly  languages,  read  the   book
     "Introduction  to  Programming"  first.  If you are not experienced in
     PAL8 programming, read the manual in two passes. First become familiar
     with  assembly  language  programming  in  absolute  (non-relocatable)
     program sections, and then reread the manual to become  familiar  with
     relocation.   You  can  skim  over  the  relocation  sections  of  the
     introduction (though some of the information is required to understand
     the  rest  of  the  manual),  and read Chapters 2 through 5 carefully,
     writing sample programs to test out the features mentioned.  Skip over
     the  chapters  on  the  macros and relocation and read the chapters on
     running MACREL and LINK so you can get your programs running. Then you
     can read the manual again to learn about relocation and macros. 


     USE OF KEY TERMS

     Some terms are used throughout the  manual  in  a  precise,  technical
     sense.   These  words  include  program section, program, page, field,
     source  module,  source  file,  relocatable  binary  module,  linking,
     absolute,  simply relocatable, and complex relocatable.  Many of these
     are  covered  in  the  introduction.   In   particular,   notice   the
     distinctions among the terms program, program section, and module. The
     word "segment" is also sometimes used, but in a generic,  nontechnical
     way (that is, a segment of code, meaning a block or group of code). 


     DOCUMENT CONVENTIONS

     Examples consist of actual  computer  output  wherever  possible.  Any
     responses  that  you  must enter are printed in red ink to distinguish
     them from computer output. 

     The symbols defined below are used throughout this manual.

     Symbol				Definition     ______				__________

     []		   Brackets  indicate  that  the   enclosed   argument   is
		   optional.

     ||		   Vertical bars indicate that  a  single  choice  must  be
		   made from a list of arguments.



				      xii



     ...	   Ellipsis indicates optional continuation of an  argument
		   list in the form of the last specified argument.

     UPPER-CASE	   Upper-case characters indicate elements of the  language
     CHARACTERS	   that must be used exactly as shown.

     lower-case	   Lower-case characters indicate elements of the  language
     characters	   that are supplied by the programmer.

	    In some instances the symbol (n) is  used  following  a
	    number  to  indicate  the  radix.   For example, 100(8)
	    indicates that 100 is an  octal  value,  while  100(10)
	    indicates a decimal value.

	    (RET) Indicates that you must enter a carriage return.









































				     xiii






				   CHAPTER 1

				 INTRODUCTION


     MACREL (MACro-RELocatable) is a PDP/8 based assembler that allows  you
     to  write  a  program  using  macro  coding  and  relocatable  program
     sections.  Macros are generalized instruction sequences that  can,  if
     desired,  be  modified  by  arguments  (data)  when the macro is used.
     Relocatable program sections allow you the freedom of writing programs
     without regard to the location of the assembled code in PDP/8 memory.

     The MACREL assembler offers a number of new features to you as a PDP/8
     programmer.   These  are outlined below.  The use of these features in
     assembly-language programming requires some reorientation of thinking.
     You should read this chapter carefully.



     1.1  MACREL FEATURES

     The main features of MACREL are  relocation,  macros,  and  supporting
     directives and operators.



     1.1.1  Relocation

     Relocation refers to the automatic adjustment of memory  addresses  at
     program  loading  time  rather  than  at  program assembly time.  This
     allows you to write programs without consideration  of  actual  memory
     addresses.   Relocation occurs in two stages:  first, MACREL assembles
     your source file into a relocatable binary file, second, LINK converts
     your relocatable binary file into an executable memory image file.

     Normally, sections of code begin on page boundaries.  MACREL/LINK  may
     relocate  these  sections  to  some other page, but generally will not
     relocate them to a different place on the page.  You must still  write
     code with respect to page boundaries.

     Relocation provides several advantages particularly when working  with
     large  programs.  You can correct, edit, assemble and list small files
     rather than having to perform all these functions with large, unwieldy
     files.   Then,  when  you  have assembled all the program modules with
     MACREL, you can link them together using LINK, the linking loader.  By
     observing  the simple programming techniques described in this manual,
     you do not have to know  the  location  of  programs  in  memory.   In
     addition, by splitting the program into discrete sections that perform
     specific functions, you produce programs that are faster to debug  and
     easier   to  understand.   Finally,  relocation  makes  it  easier  to
     construct libraries of routines that you  can  incorporate  into  your
     program.

				      1-1

				 INTRODUCTION


     In practice, you code your programs in much the same way as you always
     have.   If,  however,  you  specify  that  a  given program segment is
     relocatable using, for example, the .RSECT directive, LINK will add  a
     fixed number to the addresses shown in the listing causing the program
     to load at  a  different  set  of  locations  in  memory.   LINK  also
     automatically handles any reference from one program section or module
     to another.

     One additional feature that MACREL and LINK provide  is  a  system  of
     overlays.   This  allows you to segment large programs so they can run
     in a small amount of memory.  In practice, the whole overlay procedure
     is almost invisible.  For example, if your program does a branch (JMS)
     to a location that is not in memory, the overlay driver, which is part
     of the MACREL/LINK software package, brings in the appropriate section
     of code, and the instruction performs as if the code had  always  been
     in memory.  Except for your defining the files as overlays, MACREL and
     LINK automatically handle this entire procedure.



     1.1.2  Macros

     The macro feature of MACREL allows you to predefine a generalized  set
     of code and insert this code anywhere in a program simply by using the
     name of the macro.  In addition, the coding  inserted  can  be  varied
     according  to  the  arguments  supplied.   The  following  is a simple
     example of a macro definition:

	     .MACRO  SUB A,    B	   /Subtract A from B
	     CLA
	     TAD  A
	     CIA
	     TAD B
	     .ENDM SUB

     The .MACRO and .ENDM directives tell  MACREL  that  this  is  a  macro
     definition.   In  order to call this macro, you merely need to use its
     name in a statement followed by the two numbers that you want to  use.
     For  example,  if  you  want  to  subtract the contents of N1 from the
     contents of CNTR, you write the following:

	  SUB N1, CNTR

     Then, when the  program  is  assembled,  the  macro  code  appears  as
     follows:

	  CLA
	  TAB N1
	  CIA
	  TAB CNTR

     Note that the arguments shown in the definition have been replaced  by
     the arguments specified in the macro call.


				      1-2

				 INTRODUCTION


     Each time you call this macro, all four instructions will be  inserted
     into  the  code  (the  calling line does not produce any object code).
     Thus, use of a macro will not necessarily result  in  reduced  program
     size  as  does,  for  example, a subroutine that is called repeatedly.
     Rather, the advantages of macros are that they allow you to  predefine
     commonly   used   sequences   of   code,   perform   complicated  text
     manipulation, and write generalized program sections that assemble  in
     different ways according to the needs of a particular program.



     1.1.3  Directives

     In addition to relocation and macro processing,  MACREL  provides  you
     with  a  comprehensive  set  of directives (called pseudo-operators in
     PAL8).  These directives provide for:

	  o   Repeating portions of code or data (.REPT)

	  o   Including  one  source  file  in  the  assembly  of   another
	      (.INCLUDE)

	  o   Conditionally assembling code (.IF)

	  o   Formatting listing files (.LIST)

	  o   Printing titles and subtitles (.TITLE,.SBTTL)

	  o   Manipulating an assembly time stack (.PUSH,.POP)

	  o   Controlling data storage and expression evaluation (.ENABLE)



     1.2  OVERVIEW OF ASSEMBLY AND RELOCATABLE LOADING

     The complete MACREL/LINK cycle consists of the following steps:

	  o   Assembly

	  o   Linking

	  o   Run

     These steps are discussed in the next two sections.



     1.2.1  Assembling with MACREL

     MACREL assembles the source code into the appropriate machine-language
     instructions  and  their  corresponding  addresses.   If  the  code is
     specified as absolute, the addresses are the actual  memory  addresses
     where  the instructions are to be loaded.  If the code is relocatable,

				      1-3

				 INTRODUCTION


     the addresses are relative to the beginning of  the  program  section.
     LINK  alters  these addresses by adding a fixed number to each address
     to determine the actual memory address into which to load the code.

     In addition to processing instruction codes, MACREL provides a  number
     of  directives.  These are instructions to the assembler itself.  They
     specify special assembly processing, such as interpreting  numbers  in
     octal  or  decimal format, formatting assembly listings appropriately,
     or, in some cases, sending special instructions to LINK that allow  it
     to load the code correctly.

     Several of the directives pertain to the creation of macros.  A  macro
     allows  you  to  predefine  a  frequently used sequence of code and to
     include this sequence anywhere in the program by using the name of the
     macro (with appropriate arguments).  When MACREL processes a macro, it
     inserts the predefined code into the assembled program in place of the
     macro  call.  Thus, the effect of macro processing is to create source
     code that is ready to be assembled.  The macro feature behaves  as  if
     there  is  a separate program that you run to process the macros prior
     to assembly.  (In actuality, it's done  in  one  combined  operation.)
     This allows for complex manipulation of text and data.

     Another group of directives pertain to relocation and program modules.
     They  provide  information  to  LINK  that  allows  it to load program
     sections and modules correctly.  Some of  these  directives  tell  the
     assembler  how  to  handle  the  assembled  code and where to load it.
     Other directives allow for communication between different modules  of
     assembled code.



     1.2.2  Linking with LINK

     The output of the MACREL assembler is a relocatable binary  file.   It
     contains  the binary machine-language instructions with their relative
     loading  addresses,  information  about  where  to  load  the  program
     sections, and a list of unresolved symbols (undefined symbols declared
     to be .EXTERNAL).  LINK, in turn, takes the relocatable  binary  files
     from  one or more assembly runs, and creates a memory-image file ready
     to load.  This memory-image file is, in  essence,  an  exact  copy  of
     memory  itself.   You  can  load  and run your program either by using
     LINK's /G  command  string  option  or  by  using  the  OS/8  Keyboard
     Monitor's R command.

     In order to create the memory-image file, LINK resolves all unresolved
     symbols  first.   Then,  LINK  determines  where  to  load the various
     program  sections,  depending  upon  whether  they  are  absolute   or
     relocatable, and creates the memory-image file.



     1.3  COMPATIBILITY OF MACREL WITH PAL8

     With few exceptions, MACREL is  compatible  with  PAL8.   That  is,  a

				      1-4

				 INTRODUCTION


     program  that can be assembled correctly by PAL8 can also be assembled
     correctly by MACREL.   MACREL,  however,  provides  a  number  of  new
     features  (new  directives,  relocation, macros, new operators, etc.),
     and programs using these features cannot be assembled by PAL8.

     The remainder of this section  is  devoted  to  a  discussion  of  the
     differences between MACREL and PAL8.



     1.3.1  MACREL: Differences from PAL8

     The following PAL8 features either are not available in MACREL or  are
     handled somewhat differently.  They are summarized in Appendix B.



     1.3.1.1  Dollar Sign ($) - In PAL8, a dollar sign ($) anywhere (except
     in  a comment or a text string) terminates the assembly.  Since $ is a
     legal element of  a  symbol  name  in  MACREL,  this  feature  is  not
     implemented  in MACREL.  However, to retain PAL8 compatibility, MACREL
     treats a symbol that consists only of one or more dollar signs  as  an
     end-of-program signal.



     1.3.1.2  DTORG - The PAL8 pseudo-operator DTORG is not implemented  in
     MACREL.   Its  sole function is to output a special code to a piece of
     typesetting hardware.  It has no other function.



     1.3.1.3  MACREL and Literals - When a PAL8 program changes the current
     location  counter  to  return  to  a previous page, PAL8 remembers the
     number of literals on that page and does not overwrite them.   MACREL,
     on  the  other  hand will overwrite literals (except on page zero) any
     time you set the current location counter to  a  previous  page.   For
     this reason, you should code straight through.  (See Section 4.4.)



     1.3.1.4  PAUSE - MACREL ignores the PAL8 pseudo-operator PAUSE  (i.e.,
     no undefined symbol error is generated).  PAUSE is used by PAL8 and is
     included in MACREL for compatibility.



     1.3.1.5  Closing  Literal  Expressions  -  PAL8  ignores   the   right
     parenthesis  ())  or right square bracket (]) in a literal expression.
     Therefore, the literal expression includes all code to  the  right  of
     the  parenthesis  or  bracket.   In  MACREL,  the right parenthesis or
     bracket terminates a literal.  This difference is a problem only  when
     you code a literal expression incorrectly.


				      1-5

				 INTRODUCTION


     1.3.1.6  Terminal Support - In PAL8, if the terminal in use  does  not
     support  horizontal  tab  and  line feed, the assembler simulates them
     whenever a listing is  output  to  that  terminal.   MACREL  does  not
     perform these functions.  Either the terminal in use supports tabs and
     line feed, or the OS/8 TTY handler simulates them.



     1.3.1.7  PAL8 Run-Time Options - There are  a  number  of  differences
     between  PAL8  run-time options and MACREL run-time options.  Only two
     of these directly affect program code  generation  and  are  discussed
     here.  The remainder are listed in Appendix B.

     In PAL8, the /B command-string  option  makes  the  exclamation  point
     operator  (!)  a  6-bit  left  shift  instead  of an inclusive OR.  In
     MACREL, the .ENABLE SHIFT directive replaces this option.

     In PAL8, the /F command-string option disables the extra zero fill  in
     TEXT pseudo-ops.  In MACREL, the .DISABLE FILL directive replaces this
     option.



     1.4  ASSEMBLING EXISTING PAL8 PROGRAMS WITH MACREL

     Except for the  few  minor  incompatibilities  mentioned  above,  PAL8
     programs  will  assemble  under  MACREL  as unnamed absolute sections.
     However, we do recommend that you name  them  explicitly  as  absolute
     program  sections  by  inserting  a  line in the following form at the
     beginning of the program.

	  .ASECT name

     The directive .ASECT indicates that this is an absolute  section,  and
     name  is  the name you supply for the section.  MACREL assumes loading
     address of 200 in field zero by default.

     There are four types of files associated with MACREL:

	  Relocatable Binary File (default extension .RB) - the output file
	  used as input to LINK.

	  Listing File (default  extension  .LS) - the  output  file  which
	  contains the assembly listing.

	  KREF File  (default  extension  .KF) - the  file  used  by  KREF,
	  MACREL's cross-reference listing program.

	  Source  File  1,  Source  File   2,   etc.   (default   extension
	  .MA) - your  file(s)  that  contain  the  ASCII source code to be
	  assembled.




				      1-6

				 INTRODUCTION


     1.5  INTRODUCTION TO MACREL RELOCATION

     The remainder of  this  chapter  provides  a  somewhat  more  detailed
     explanation  of  MACREL/LINK  operation.   If  you  are  new  to PDP-8
     assembly language programming you may wish to read Chapters 2  through
     4 before reading this section.



     1.5.1  Source Modules

     A source module is a continuous file taken as a whole.  To illustrate,
     recall  from  Section  1.4 that the input file string (Source File 1),
     (Source File 2), ...  (Source File n) defined a continuous sequence of
     code to MACREL.  That is, after the last character of the last line of
     source file 1, the first character of the first line of source file  2
     was read without a break.  The assembler treats this sequence of files
     as one continuous file.  In addition, any file may  call  other  files
     internally  if  the .INCLUDE or .CHAIN directives have been specified.
     Again, the result is one continuous file.  This  continuous  file,  or
     source  module, is the input to one assembly operation.  The result of
     the assembly is a relocatable binary module  (the  relocatable  binary
     file used as input to LINK) plus the listing and KREF files.

     To summarize  (and  it  is  important  that  these  terms  be  clearly
     understood),  the  input  to  an  assembly  is a source module and the
     output is a relocatable binary  module  (plus  the  listing  and  KREF
     files).

     Note that these modules may not  comprise  the  entire  program.   The
     program  may  consist  of  a  large  number  of  source  modules  that
     communicate among themselves through symbols that have been defined by
     the   .EXTERNAL,   .GLOBAL,   .ENTRY,   and  various  program  section
     directives.   MACREL  assembles  each  source  module  separately  and
     produces  a  corresponding  relocatable  binary  module  that contains
     information for LINK  about  symbols  that  are  defined  as  .GLOBAL,
     .EXTERNAL,  etc.   LINK resolves all these inter-module references and
     determines where to load the program sections.



     1.5.2  Program Sections

     A program section is a segment of code  that  begins  with  a  program
     section (.SECT) directive.  It is loaded by LINK into a contiguous set
     of memory locations.  LINK  may  arbitrarily  load  different  program
     sections  into  discontinuous  areas  of memory.  Thus, if two program
     sections follow each other in the source module, there is no guarantee
     that  LINK  will load them into consecutive areas of memory.  For PAL8
     compatibility, if a sequence of code has no program section  directive
     or  name,  MACREL  defines  it as an absolute program section (.ASECT)
     that loads into  the  absolute  locations  indicated  on  the  program
     listing.  Relocatable program sections, such as .RSECTs, are relocated
     by LINK at link time.  The assembler handles all  communication  among

				      1-7

				 INTRODUCTION


     the  various sections of a source module.  If, for example, you code a
     JMS I (SUBR), where SUBR is a label in another section, the  assembler
     generates  information  to  LINK  identifying  (SUBR)  as a literal in
     another section,  and  the  program  executes  perfectly  even  though
     neither  you  nor the assembler knows at assembly time where in memory
     the sections will actually load.

     There are six types  of  program  sections  described  in  Table  1-1.
     Programs  typically  are  coded  as  any  combination  of  .ASECTs and
     .RSECTs.  You can use .ASECT  for  programs  that  make  reference  to
     absolute  memory  locations  and  .RSECT  for  programs or sections of
     programs that will be relocated.

     The remaining four section types are more specialized.  If you wish to
     use  page  zero  locations,  you may define a .ZSECT that contains the
     page zero table (or other code) referenced.  If you want  to  use  the
     autoindex  registers  (locations  10-17),  define  an  .XSECT with the
     appropriate labels.  If you  have  a  block  of  data  (containing  no
     instructions)  that  can  be  located  anywhere, place it in a .DSECT.
     Finally, if you have a number of small subroutines that  you  wish  to
     load together on a page, define each subroutine as an .FSECT.  Such an
     .FSECT must be shorter than one memory  page  and  LINK  may  load  it
     anywhere on the page.


				   Table 1-1
			       Types of Sections

     ----------------------------------------------------------------------
     |  Type of Section	   |		      Description		  |
     |---------------------|----------------------------------------------|
     |	.ASECT		   |  ABSOLUTE   SECTION - loaded   into   memory |
     |	       or	   |  starting at the absolute address given.	  |
     |	.SECT name, A      |						  |
     |---------------------|----------------------------------------------|
     |	.RSECT		   |  RELOCATABLE    SECTION - may   be   located |
     |	       or	   |  anywhere  except  page  0,  and  is  loaded |
     |	.SECT name, R	   |  starting at the beginning of a page.	  |
     |---------------------|----------------------------------------------|
     |	.ZSECT		   |  PAGE  ZERO  SECTION - will  be  loaded into |
     |	       or	   |  page zero (locations 20-177).		  |
     |	.SECT name, Z      |						  |
     |---------------------|----------------------------------------------|
     |	.XSECT		   |  AUTOINDEX  SECTION - will  be  loaded  into |
     |	       or	   |  locations 10-17 on page zero.		  |
     |	.SECT name, X	   |						  |
     |---------------------|----------------------------------------------|
     |	.DSECT		   |  DATA SECTION - contains  data  and  may  be |
     |	       or	   |  relocated    anywhere,    not   necessarily |
     |	.SECT name, D	   |  starting on a page boundary.   The  section |
     |			   |  may   flow  across  pages  but  not  across |
     |			   |  fields.					  |
     ----------------------------------------------------------------------
						(continued on next page)

				      1-8

				 INTRODUCTION


			       Table 1-1 (Cont.)
			       Types of Sections
     ----------------------------------------------------------------------
     |  Type of Section	   |		      Description		  |
     |---------------------|----------------------------------------------|
     |	.FSECT		   |  FLOATING  SECTION - contains   instructions |
     |	       or	   |  and   may   be   relocated   anywhere  (not |
     |	.SECT name, F	   |  necessarily beginning on a page  boundary). |
     |			   |  It   must,  however,  be  wholly  contained |
     |			   |  within a page.  Several  floating  sections |
     |			   |  may occupy one page.  (It is generally used |
     |			   |  for miscellaneous small subroutines.)	  |
     ----------------------------------------------------------------------

     LINK can load any program section into any field, but you can  specify
     the  memory  field  where a program section is to be loaded by using a
     FIELD directive.  A program section may not  cross  field  boundaries,
     and may not contain more than 4095 words of data.

     You can define a program section using either of two syntaxes:

	  .SECT BPROC.  R

     This line defines a relocatable program section named BPROC.   Another
     example is:

	  .ASECT MAIN

     This uses the alternative form .ASECT rather  than  .SECT  NAME,A  and
     defines an absolute section named MAIN.

     You can explicitly specify the loading address of a program section by
     setting the current location counter with the asterisk directive.

	  *300

     This sets the current  location  counter to  300.   MACREL  assumes  a
     default  loading address of 200 for absolute programs, and 0 (relative
     to the beginning of  the  program  section)  for  relocatable  program
     sections.

     Note that source files,  source  modules,  and  program  sections  are
     completely  different  entities.  Figure 1-1 shows the relationship of
     these terms.  A given program  may  consist  of  a  number  of  source
     modules,  each  of which is associated with one assembly operation.  A
     module may consist of one or more program sections, each of which is a
     logical unit at link time:  that is, it loads into a contiguous set of
     memory locations and  is  identified  by  an  entry  in  a  load  map.
     Physically, a source module may consist of any number of files.

     One file might terminate in the middle of a program  section  and  the
     next  one  complete that program section and go on to others.  This is
     of no concern to the assembler, however, because it treats all  source
     files as one continuous input stream.

				      1-9

				 INTRODUCTION


		      -----------			A program contains
		      |  Final  |			one or more
		      |	Program |			modules.
		      -----------
			   ^
			   |
	  -----------------|.................
	  |		   |		    .
     ------------     ------------     ------------	 A module contains
     | Module 1 |     | Module 2 |.....| Module P |	 one or more
     ------------     ------------     ------------	 sections.
			   ^
			   |
	  -----------------|.................
	  |		   |		    .
     -------------    ------------    -------------	 A section contains
     | Section 1 |    | Section 2 |....| Section M |	 one or more memory
     -------------    -------------    -------------	 locations.
			   ^
			   |
	  -----------------|.................
	  |		   |		    .
     --------------   --------------   --------------	 Memory locations
     | Location 1 |   |	Location 2 |...| Location N |    contain the source
     --------------   --------------   --------------    code.


		   Figure 1-1  Program Sections and Modules


     MACREL handles communication among  program  sections  of  one  source
     module  and  in  general  does  not  require  special coding.  A JMS I
     (SUBR), where SUBR  is  a  subroutine  in  another  section,  executes
     correctly  without  any  special  effort  on your part.  Communication
     between  program  sections  in  different  source  modules,   however,
     requires  that  all  references  to  a  symbol  in  another  module be
     identified by the directives  .EXTERNAL,  .GLOBAL,  .ENTRY,  or  their
     equivalent.   These  directives are necessary because the other module
     is assembled at a different time and hence its symbols are  not  known
     to  MACREL at this assembly time.  For example, a TAD I (B, where B is
     a label in another source module, results in an undefined symbol error
     message,  unless the symbol B is identified in a statement of the form
     .EXTERNAL  B.  Chapter  7   describes   these   module   communication
     directives.



     1.5.3  Fundamentals of Relocatable Programming

     In general, the  techniques  for  programming  a  relocatable  program
     section  are  the same as those for programming individual pages of an
     absolute program section.  Since an .RSECT always  loads  starting  at
     page  boundaries, the effect of relocation is merely to move the whole
     section as a unit by some multiple of 200  (octal)  memory  locations.

				     1-10

				 INTRODUCTION


     Consider the following sequence of code:

		   *200
		   CLA
		   TAD B
		   TAD I BPOINT
		   JMS .+3
	  B,	   7
	  BPOINT,  B

     This would assemble (in an absolute section) as:

	  1		0200		   *200
	  2    00200	7200		   CLA
	  3    00201	1204		   TAD B
	  4    00202	1605		   TAD I BPOINT
	  5    00203	5206		   JMP .+3
	  6    00204	0007	 B,	   7
	  7    00205	0204	 BPOINT,   B


	  SYMBOL TABLE

	  B	    0204
	  BPOINT    0205

     Note that the program ends by adding the value contained at location B
     twice  (once  through  a direct TAD and once through an indirect TAD).
     It then jumps to some code following this, at location 206.

     If this entire piece of code is relocated to start at  location  *400,
     it results in the following:

	  1		0400		   *400
	  2    00400	7200		   CIA
	  3    00401	1204		   TAD B
	  4    00402	1605		   TAD I BPOINT
	  5    00403	5206		   JMP .+3
	  6    00404	0007	  B,	   7
	  7    00405	0404	  BPOINT,  B

     Note that in the code column to the right of the address  column  only
     one  line  of  code has changed from the previous example, namely, the
     indirect address pointer BPOINT.  Everything else is  the  same.   For
     example,  TAD B still has a code value of 1204 (i.e.  two's complement
     add the contents of location 4 on the  current  page).   The  indirect
     address  pointer  BPOINT has been incremented by octal 200, the amount
     of the relocation factor.

     In general, during relocation,  instructions  and  ordinary  data  are
     unchanged.   Twelve-bit  addresses  and  values that are computed from
     them are altered by adding to them  the  address  to  which  they  are
     relocated.


				     1-11

				 INTRODUCTION


     For example, if this segment of code is  made  into  an  .RSECT  named
     FLOAT, the code (including the symbol table) looks like this:

	  1	       0000    .RSECT FLOAT
	  2    ?0000   7200	       CLA
	  3    ?0001   1204	       TAD B
	  4    ?0002   1605	       TAD I BPOINT
	  5    ?0003   5206	       JMP .+3
	  6    ?0004   0007    B,      7
	  7    ?0005   0004 +  BPOINT, B


	  SYMBOL TABLE

	  B	    0004+ FLOAT
	  BPOINT    0005+ FLOAT
	  FLOAT     0006  RSECT

     Compare this example with the one that loads at absolute  address  200
     and notice the following changes:

	  1.  A question mark (?) replaces the field column of the  address
	      to show that LINK may load the program into any field.

	  2.  The address of the first line of code is now  shown  as  0000
	      rather  than  200,  which  is  relative  to  the start of the
	      program section.

	  3.  Each succeeding address is relative in  the  same  way.   The
	      same  idea  also  applies  to  the  12-bit  address stored in
	      BPOINT, which is now 004 rather than 204, because it will  be
	      relocated at link time.

	  4.  The plus sign (+) to the right of  the  code  indicates  that
	      this relocation takes place.

     In the symbol table, FLOAT shows up as the name  of  this  relocatable
     program  section  and has an address of zero relative to the beginning
     of the section.  All other labels in the section,  then,  are  defined
     relative to FLOAT.  thus, BPOINT is 5+FLOAT.  This means that, at link
     time, the label BPOINT will be evaluated by taking 5  and  adding  the
     value  of  FLOAT,  the  memory  address  of  the start of the section.
     BPOINT consists of an absolute part of 5 and a relocatable part FLOAT.
     The  value  of  BPOINT,  therefore,  is the sum of the two parts.  The
     absolute part does not change, but the relocatable part is unknown  at
     assembly  time  and  is  determined by LINK after memory is allocated.
     These effects of relocation are generally not of major concern to  you
     because  MACREL  and  LINK  automatically handle them.  However, it is
     helpful to understand what  is  happening,  and  how  it  affects  the
     program listing.





				     1-12

				 INTRODUCTION


     1.5.4  Example of Communication Between Program Sections

     In general, communication between program  sections  is  the  same  as
     communication  between different pages of an absolute program section.
     For example, in an absolute section, a TAD I (B) executed on one  page
     where  B  is  a  label  on  another page, generates an on-page literal
     containing the address of B on the other page.  In the same way, a TAD
     I  (B)  in  a  relocatable  section,  where  B  is  a label in another
     relocatable section, generates an on-page literal pointer,  and  after
     linking,  that  pointer  contains the actual address of B in the other
     section.



     1.5.4.1  A Sample Program - The example program SKIFOC shown in Figure
     1-2  illustrates  communication between program sections.  The program
     obtains a character stored in a buffer, tests the character to see  if
     it  is  an  octal  digit, and then prints the result of the test.  The
     program consists of three program sections:  .RSECT TESTP, .RSECT SUBS
     and .DSECT DATA.

     .RSECT TESTP is the main section of the program.   It  first  calls  a
     subroutine  SKIFOC in the .RSECT SUBS and then calls PRINT, the second
     subroutine  in  SUBS.   When  both  subroutines  are  complete,  TESTP
     increments  a  pointer to the buffer in .DSECT DATA and then checks to
     see if all the characters in the buffer have been tested.

     .RSECT SUBS has two subroutines:  SKIFOC and PRINT.   SKIFOC  tests  a
     character  from  the  buffer  and then returns to the calling program,
     TESTP, at either of two locations.  PRINT then prints on the terminal,
     either an "N" or an "S" as a result of the test in SKIFOC.

     The .DSECT DATA contains the buffer that stores the  characters  being
     tested.   In  this example there are four characters:  /, 0, 7, and 8.
     The final location in the buffer contains null (binary zero), which is
     used to terminate the test.

     This example is the listing file  of  the  relocatable  binary  module
     produced  by  MACREL.   The assembler adds three columns to the source
     module during assembly.  The first column is the  source  module  line
     number,  the  second  is  the  relative address in the section and the
     third and final column is the code.  Items in the code column that are
     marked by an asterisk (*) will be altered at link time.


      1		  0000		.RSECT TESTP	/TEST SKIFOC ROUTINE
      2		  0000		FIELD 0		/LOAD IN FIELD 0
      3
      4
      5	  00000   4777   START,  JMS I   (SKIFOC)       /CALL SKIFOC,IS IT
							  AN OCTAL DIGIT

	 Figure 1-2  Example of Communication Between Program Sections


				     1-13

				 INTRODUCTION


      6	  00001   1376		 TAD	 ("N-"S)	/NO,SET TO PRINT AN
							  ASCII "N"
      7	  00002   1375		 TAD	 ("S)		/YES,GET AN ASCII
							  "S"
      8	  00003   4774		 JMS I	 (PRINT)	/CALL SUB ROUTINE
							  "PRINT"
      9	  00004   2211		 ISZ	 BLOC		/INCREMENT BUFFER
							  POINTER
     10	  00005   1611		 TAD I	 BLOC		/GET NEXT CHARACTER
     11   00006   7640		 SZA CLA		/IS IT ZERO
     12	  00007   5200		 JMP	 START		/NO, TEST IT
     13	  00010   5773		 JMP I	 (7605)		/YES,RETURN TO
							  KEYBOARD MONITOR
     14
     15	  00011   0000 *  BLOC,	 BUFFER			/STORAGE FOR LOCAL
							  DATA
     16
     17
     18
     19
	  -----
	  00173   7605
	  00174   0021 *
	  00175   0323
	  00176   7773
	  00177   0004 *
     20		  0000		 .RSECT SUBS		/SECTION OF SUB
							  ROUTINES ,SKIFOC
							  & PRINT
     21		  0000		 FIELD 0		/ALSO IN FIELD 0
     22
     23
     24							/STORE LOCAL DATA
							  FOR THIS SECTION
     25
     26	  00000   7520	 NEG0,	 -"0			/MINUS ASCII 0
     27	  00001   7511	 NEG7,	 -"7			/MINUS ASCII 7
     28	  00002   0011 * BLOCAD, BLOC			/THE ADDRESS OF
							  "BLOC"
     29	  00003   0000	 VBLOC,	 0			/ON PAGE STORAGE FOR
							  "BLOC"
     30
     31
     32
     33	  00004   0000   SKIFOC, 0			/ROUTINE TO TEST THE
							  CHARACTER IN BUFFER
     34							/IF IT IS AN OCTAL
							  DIGIT SKIP NEXT
     35							/INSTRUCTION (LINE 6)
							  IN THE CALLING
     36							/PROGRAM
     37	  00005   7200		 CLA			/CLEAR ACCUMULATOR

     Figure 1-2  (Cont.)  Example of Communication Between Program Sections

				     1-14

				 INTRODUCTION


     38	  00006   1602		 TAD I	 BLOCAD		/GET ADDRESS OF
							  BUFFER
     39	  00007   3203		 DCA	 VBLOC		/STORE IT ON PAGE
     40	  00010   1603		 TAD I	 VBLOC		/GET CHARACTER AT
							  THIS ADDRESS
     41	  00011   1200		 TAD	 NEG0		/SUBTRACT ASCII 0
     42	  00012   7710		 SPA CLA		/IS IT > OR =TO 0
     43	  00013   5604		 JMP I	 SKIFOC		/NO, RETURN TO
							  CALLING PROGRAM
     44	  00014   1603		 TAD I	 VBLOC		/YES, GET CHARACTER
							  AND TEST AGAIN
     45	  00015   1201		 TAD	 NEG7		/SUBTRACT ASCII 7
     46	  00016   7750		 SPA SNA CLA		/IS IT < OR= TO 7
     47	  00017   2204		 ISZ	 SKIFOC		/YES, INCREMENT
							  RETURN ADDRESS OF
     48							/CALLING PROGRAM
     49	  00020   5604		 JMP I	 SKIFOC		/NO, RETURN TO
							  CALLING PROGRAM
     50
	  .RSECT TESTP	 /TEST SKIFOC				PAGE 1-1
						FILE 1
     51
     52   00021	  0000	 PRINT,	 0			/A ROUTINE TO PRINT
							  ONE ASCII
							  CHARACTER
     53
     54	  00022	  6046		 TLS			/PRINT THE CHARACTER
     55	  00023	  6041		 TSF			/TEST AND SKIP ON
							  FLAG
     56	  00024	  5223		 JMP	 .-1		/STILL PRINTING ,TRY
							/  AGAIN
     57	  00025	  7200		 CLA
     58	  00026	  5621		 JMP I	 PRINT		/RETURN TO CALLING
							  PROGRAM
     59
     60
     61
     62		  0000		 .DSECT DATA		/DATA SECTION TO
							  STORE THE TEST
     63							/CHARACTERS ,TWO
							  OCTAL DIGITS AND
     64							/TWO THAT ARE NOT
							  OCTAL
     65		  0000		 FIELD 0		/THIS SECTION IS
							  ALSO IN FIELD 0
     66
     67	  00000	  0257	 BUFFER, "/			/NOT-OCTAL
     68	  00001	  0260		 "0			/OCTAL
     69	  00002   0267		 "7			/OCTAL
     70	  00003	  0270		 "8			/NOT-OCTAL
     71	  00004	  0000		 0			/THE .RSECT TESTP
							 TESTS EACH

     Figure 1-2  (Cont.)  Example of Communication Between Program Sections

				     1-15

				 INTRODUCTION


     72							/EACH CHARACTER ,WHEN
							  IT FINDS THE ZERO
     73							/IN THE BUFFER ,IT
							  STOPS TESTING AND
     74							/RETURNS TO MONITOR.
							  (SEE LINES 11 & 13
							/ABOVE)

     Figure 1-2  (Cont.)  Example of Communication Between Program Sections



     1.5.4.2  Program Operation - Program  operation  is  described  below.
     All references are to the line numbers in the listing.

     Because TESTP calls two subroutines, program execution begins at  line
     5,  jumps  to  line 33, continues through line 49, and then returns to
     TESTP.  After the return from the first subroutine, execution jumps to
     line  52,  proceeds  through line 58, and again returns to the calling
     program TESTP.  The second  return  is  to  line  9  and  the  program
     continues through lines 10, 11, 12 and 13.

     Line 5 is the start of the program and calls  the  subroutine  SKIFOC.
     Execution  then  continues  on line 33 which stores the return address
     for SKIFOC.  The subroutine  is  complete  in  lines  37  through  48.
     SKIFOC  gets the address of the buffer (TAD I BLOCAD, line 38), stores
     it at VBLOC (line 39) then gets the contents of that address (line  40
     and  again  line  44)  and checks to see if the character (contents of
     VBLOC) is in the range ASCII 260 to ASCII 267 (lines  41  and  42  and
     again  lines  45  and  46).   If the character is in this range SKIFOC
     increments the return address stored at line 33 and returns  to  TESTP
     at line 7.  If the character is out of range (i.e., not octal), SKIFOC
     does a normal return to TESTP at line 6.

     If the return to TESTP is to line 6, the accumulator  is  loaded  with
     the  literal  at  relative  location 00176 (-5, the difference between
     ASCII N and ASCII S) and then summed with line 7 (ASCII S) to  produce
     the  ASCII  code for N.  If the return is to line 7 the accumulator is
     loaded with only the literal at location 175, the ASCII value of S.

     TESTP now jumps to the subroutine PRINT.  PRINT is located at the 21st
     address  in  the  .RSECT  SUBS (line 52).  This address is stored as a
     literal at address 00174 and marked with an asterisk to show  that  it
     will be relocated at link time.

     PRINT sends the contents of the accumulator to the terminal  and  then
     returns to the calling program.

     TESTP now increments the pointer to the buffer (line 9),  obtains  the
     contents  of  the buffer (line 10), and checks for zero (line 11).  If
     the buffer now has a zero value (end  of  test)  TESTP  exits  to  the
     monitor  (line  13), if the buffer has another character, TESTP starts
     over again (at line 5) with the JMP START instruction on line 12.


				     1-16

				 INTRODUCTION


     When run, the program produces the following output:

	  NSSN
	  .

     This indicates that the  first  and  last  characters  are  not  octal
     digits,  while  the middle two are.  The period is printed by the OS/8
     Keyboard Monitor upon completion.



     1.5.4.3  Effects of Relocation on the Program - Although  this  sample
     program consists of three sections, its construction is identical to a
     program that is located in three pages of one  absolute  section.   In
     fact, you could replace the three sets of program directives and field
     statements by three PAGE directives and  program  operation  would  be
     virtually identical.

     The  following  is  a  brief  review  of  the  program  in  terms   of
     communication   between  program  sections.   (You  can  compare  this
     description with interpage  communication  within  a  single  absolute
     program  section.)  On  line 5, there is an indirect JMS to an address
     (SKIFOC) in another section.   This  is  handled  by  the  literal  at
     address  00177  (below line 19).  This literal shows up in the listing
     as 0004.

     The actual memory address of SKIFOC is entered into this  location  at
     LINK  time.   Because  SKIFOC  is at relative address 4 in the section
     SUBS, the actual value of the literal will be computed as 4 (its place
     in  SUBS)  plus  SUBS  (the  loading  address  of the beginning of the
     section).  The same principle applies to line 8, JMS I  (PRINT,  where
     PRINT  is  another  subroutine in SUBS.  Here the literal is stored in
     address 174, and has the value of 0021*.  This means that  the  actual
     value  will  be  altered to 21 (it's the 21st entry in SUBS) plus SUBS
     (the loading address of the beginning of the section).

     The location BLOC (line 15) contains a pointer to BUFFER in  the  DATA
     section.   Again, it contains the address of the beginning of the DATA
     section at link time.

     When TESTP jumps to SKIFOC and PRINT, it stores the appropriate return
     address  in the entry word of each routine.  The return to the calling
     program (even though it's in another section) is handled  normally  by
     the hardware;  the program uses the usual indirect JMP to the entry.

     On line 28, the section SUBS has a pointer to BLOC in TESTP.  The code
     shows a 0011*.  Again, this is modified at link time by adding 11 (its
     position in TESTP) to the value of TESTP.  Once the address of BLOC is
     known,  the  actual  communication  between  the  sections  is  easily
     initiated.

     Note  that  although  we  used  only  JMS  and  TAD  instructions   to
     communicate   between  sections  in  this  sample  program,  the  same


				     1-17

				 INTRODUCTION


     principles apply to any memory  reference  instructions  used  between
     sections.



     1.5.4.4  The Symbol Table - The symbol table for this example contains
     two  types of entries:  section names and labels.  The numbers next to
     the section names (DATA, SUBS, and TESTP) indicate  the  size  of  the
     sections.   Notice  that  although  TESTP contains fewer lines of code
     than SUBS, TESTP shows up as a larger section (octal 200 as opposed to
     octal  27)  because  it  uses literals, which load from the end of the
     page.  Thus the entire page is effectively used.  (LINK will not  load
     one section into a gap in another.)

     The remaining entries in the symbol table  are  labels,  and  in  each
     case,  the  entry  consists of an octal number that shows the relative
     location in the section, a plus sign, and the name of the  section  in
     which they appear.

     / A PROGRAM TO TEST "SKIFOC"
     SYMBOL TABLE

     BLOC      0011+ TESTP
     BLOCAD    0002+ SUBS
     BUFFER    0000+ DATA
     DATA      0006  DSECT
     NEG0      0000+ SUBS
     NEG7      0001+ SUBS
     PRINT     0021+ SUBS
     SKIFOC    0004+ SUBS
     START     0000+ TESTP
     SUBS      0027  RSECT
     TESTP     0200  RSECT
     VBLOC     0003+ SUBS

     The symbolic name of the section has a value equal to  the  amount  of
     its  relocation  offset calculated at LINK time.  Thus, if TESTP loads
     into location 200, its value at link time will be 200, and BLOC (shown
     as 0011+ TESTP) will have a value of 11 + TESTP, or 211.  That is, the
     location BLOC has an actual memory address of 211.  The same principle
     applies to all other labels in the symbol table.



     1.5.5  Relocation Type

     Absolute program sections  may  only  contain  expression  and  symbol
     values  that are known at assembly time.  Relocatable program sections
     may contain expression and symbol values  that  are  known  either  at
     assembly  time  or  at  LINK time.  There are five types of relocation
     associated with them:

	  o   Absolute


				     1-18

				 INTRODUCTION


	  o   Simple Relocation

	  o   CDF/CIF Relocation

	  o   .FSECT Relocation

	  o   Complex Relocation



     1.5.5.1  Absolute Expressions - An absolute expression is evaluated as
     a  fixed  12-bit  number during assembly.  For example, the expression
     N= "A+1 causes "A+1 to be evaluated and the result assigned to N.   N,
     then, has a value of 301 (ASCII A) + 1 or an absolute value of 302.



     1.5.5.2  Simple   Relocation   Expressions - A    simple    relocation
     expression consists of an absolute part plus one relocatable part that
     must be evaluated at link time.  A  label  in  an  .RSECT  is  a  good
     example.  If the following example is part of a relocatable section:

		 .RSECT ANA
		 CLA
		 TAD    B
		 TAD    C
	 LOOP,   TAD    A
		 .
		 .
		 .

     ANA has an absolute  part  of  zero  and  a  relocatable  part  to  be
     evaluated at link time.  LOOP has an absolute part of 3 (location 0003
     in .RSECT ANA) and a relocatable part of ANA.  Thus  LOOP  appears  in
     the symbol table as 0003 + ANA.



     1.5.5.3  CDF/CIF Relocation Expressions - An expression is  considered
     CDF/CIF  relocatable  whenever it uses a value that results from using
     either the CDF or CIF special operators (see Section 4.9.4).



     1.5.5.4  .FSECT Relocation Expressions - An expression  is  considered
     .FSECT  relocatable  whenever  it  uses  a  value  that results from a
     relocatable expression  residing  in  an  .FSECT,  .XSECT,  or  .ZSECT
     program section (see Section 7.1).



     1.5.5.5  Complex Relocation Expressions -  An  expression  is  complex
     relocatable  when  it  cannot be reduced during assembly to one of the
     relocation types described in the preceding  sections.   For  example,

				     1-19

				 INTRODUCTION


     continuing with the previous program segment, suppose the code LOOP %4
     appeared as follows:

		.RSECT ANA
		CLA
		TAD    B
		TAD    C
	 LOOP,  TAD    A
		.
		.
		.
	 A,	LOOP %4
		.
		.
		.

     The expression at location A is complex relocatable because its  value
     is  0003  +  ANA  divided by 4, which MACREL cannot reduce to a simple
     relocation expression at assembly time.  The entire  expression,  LOOP
     %4 is passed on intact for LINK to evaluate.

     An expression need not look complicated  to  be  complex  relocatable.
     For example, B=LOOP+ANA is a complex relocatable expression because it
     cannot be evaluated at assembly time to an absolute  portion  and  one
     relocatable   part.   Here,  B  would  evaluate  to  3+<2^ANA>  (i.e.,
     3+ANA+ANA) and twice ANA is not one relocatable part.   On  the  other
     hand,  B=LOOP-ANA is not a complex relocatable expression;  in fact, B
     evaluates to the absolute quantity 3 (3+ANA-ANA).

     In general, complex CDF/CIF and .FSECT relocatable expressions  should
     be  of  little  concern  unless  you  have unusual code constructions.
     Relocation is covered in greater detail in Chapter 7.



     1.6  THE ASSEMBLY PROCESS

     The MACREL assembler performs a maximum of  four  passes  through  the
     source  module.   The  number of passes is determined by the number of
     output files in the file-specification  line.   (Pass  one  is  always
     run -- providing  an  input  file is specified.) See Section 1.4 for a
     list of the file types.



     1.6.1  Pass One -- Symbol Definition Pass

     On its first pass, MACREL constructs the  symbol  table.   The  symbol
     table  contains  both  permanent  symbols and program-defined symbols.
     Each symbol stored is identified according to type, whether or not  it
     is  defined,  and  (if  defined) its value.  Additional codes indicate
     whether it has been declared as .EXTERNAL, .GLOBAL, .ENTRY,  etc.   If
     the  symbol is a macro name, the entire text of the macro is stored in
     the symbol table area as well.  Because source code lines are read and

				     1-20

				 INTRODUCTION


     immediately processed (i.e., not retained in memory), the symbol table
     requires a large number of memory locations.  Thus,  a  large  program
     being assembled on a machine with insufficient memory could exceed the
     available symbol table space.

     In addition to creating the symbol table, the assembler  performs  its
     normal  algorithm  of  processing expressions, directives, etc.  Thus,
     most error messages of a syntax nature  are  generated  on  pass  one.
     However,  no  undefined  symbol error messages are printed on pass one
     since the symbol table is not complete until the end of the pass.



     1.6.2  Pass Two -- Binary Code Generation Pass

     If you specify  an  output  file  (relocatable  binary  file,  default
     extension  .RB),  the assembler starts generating binary code.  MACREL
     reads a line of source code, looks up any symbols in the symbol table,
     evaluates  expressions,  and writes the resultant code into the output
     file.  In the case of directives, it performs the action specified  by
     the directive.

     If you do not specify any output files, the assembler  performs  error
     checking on pass one, and then returns to the OS/8 Keyboard Monitor.

     On this second pass, all symbols must be defined;   any  undefined  or
     illegally redefined symbol produces an error message.

     At the end of the pass, all  symbols  that  have  been  defined  by  a
     declaration  such  as .ENTRY, .EXTERNAL, .GLOBAL and the like, or that
     are the names of sections are written out in a block  of  code.   This
     block  of  code, called the Loader Symbol Dictionary (LSD), is used by
     LINK to define all global symbols.  In addition to global symbols, the
     LSD contains the size of each section in the module, which  LINK  uses
     to determine loading addresses.



     1.6.3  Pass Three -- Listing Pass

     If you specify the second  output  file  (the  listing  file,  default
     extension  .LS), MACREL performs pass three.  This pass is essentially
     the same as pass two  but  instead  of  writing  binary  code,  MACREL
     produces  the  listing  file.   At  the  end  of the listing file, the
     assembler outputs the symbol table as part of the listing.



     1.6.4  Pass Four -- Cross-Reference (KREF) Listing Pass

     If you specify the third output file (the KREF file, default extension
     .KF),   MACREL   makes   a   fourth  pass  to  create  the  KREF  file
     (cross-reference listing).  Note that this is  different  from  PAL8's
     CREF   file.   The  KREF  listing  tabulates  program-defined  symbols

				     1-21

				 INTRODUCTION


     alphabetically and, after each symbol, the line numbers of every  line
     that references that symbol.



     1.7  THE LINKING PROCESS

     The output of one assembly operation is a relocatable binary module in
     file  form.   LINK  takes  up  to  128  such files, combines them, and
     prepares a memory-image file that is ready to load  into  memory.   If
     desired,  LINK  also  loads  the file into memory and starts it.  LINK
     performs this operation in two passes.



     1.7.1  Pass One -- Linking

     On the first pass, LINK creates a Global Symbol Table (GST), which  is
     a  combination  of  all  the  Loader  Symbol  Dictionaries (LSDs).  In
     particular, LINK searches through the LSDs of the input files  looking
     for  unresolved  references.  For every symbol in a source module that
     is defined by an .EXTERNAL or .ZTERNAL directive, LINK searches  other
     modules  for  .GLOBAL  or  .ENTRY declarations of the same symbol.  As
     each match is made,  the  symbol  is  defined  and  the  reference  is
     satisfied.  This process is called linking.

     LINK continues this process until all .EXTERNAL or .ZTERNAL references
     are  resolved.  Normally, this will occur by the end of pass one.  If,
     however, reference is made to programs  on  a  library  file,  several
     passes  may  be  required  to resolve all references.  This is because
     LINK is more selective when referring to a library file.   It  selects
     only  modules  from the file that are actually referenced, rather than
     loading  everything.   However,  one  library  program  may  reference
     another one, and so on in turn, and a number of passes may be required
     to resolve all references.

     At the end of this process (logical pass one) LINK will have  resolved
     all  references unless there is an error.  The resulting Global Symbol
     Table (GST) is then used for pass two.



     1.7.2  Pass Two -- Loading

     Having defined all symbols, LINK allocates memory.  All of the section
     references  in  the  table  are  sorted,  primarily by the size of the
     program section.  Memory is allocated, working from the  beginning  of
     the  table  (largest  section) to the end.  LINK performs an algorithm
     that ensures that sections are allocated correctly.   In  some  cases,
     this  may mean a considerable change from the original "largest first"
     order.  The result is that, at the end of this operation, all sections
     have  been  allocated memory space.  In particular, the actual loading
     addresses of section names are determined.  For example, up until now,


				     1-22

				 INTRODUCTION


     in  the  section  .RSECT  MAIN,  MAIN had a value (address) of 0+MAIN.
     Now, MAIN will be given an actual numerical value.

     Having allocated memory, LINK writes the  memory-image  file  (default
     extension .SV).  LINK also reads the relocatable binary modules again,
     but this time, as each undefined symbol in the file is referenced,  it
     looks  up  the  symbol  in  the Global Symbol Table, adds the absolute
     part, and inserts the correct value.  This is the relocation  function
     of LINK.  For example:

			 .RSECT  MAIN
		 MPTR,   NUM1
			  .
			  .
			  .
			 TAD I MPTR
			  .
			  .
			  .
			 .RSECT  MATH
			 CLA
			 TAD A
			 JMP .+4
		 NUM1,	  0
			  .
			  .
			  .


     The line MPTR, NUM1 in the .RSECT MAIN contains a  12-bit  pointer  to
     NUM1  in .RSECT MATH.  Prior to this time, this pointer word contained
     the simply-relocatable value MATH+3.  Now, if  the  section  MATH  has
     been  determined to load at location 4200 (i.e., MATH=4200), when LINK
     reads the MATH+3 reference in the relocatable binary module, it  looks
     up  MATH  in  the  table,  adds  3, and stores the value 4203 into the
     memory-image file.  LINK continues in this way until the  entire  file
     has  been  written.  The memory-image file contains both addresses and
     the code to be loaded into those addresses.

     You can load the memory-image file into memory using either  the  OS/8
     Keyboard Monitor's R command, or LINK's /G command string option.














				     1-23







				   CHAPTER 2

			 MACREL SOURCE PROGRAM FORMAT



     2.1  MACREL STATEMENTS

     Source programs are usually prepared on the console terminal (using an
     OS/8  editor)  as a sequence of statements.  Each statement is written
     on a single line and is terminated by  typing  the  RETURN  key.   The
     MACREL  line  buffer  can  store 128 characters including the carriage
     return.  There are three types of elements in a MACREL statement  line
     that  are identified by the order of their appearance in the statement
     and by the separating (or delimiting) character following or preceding
     the element.  These are:

	  1.  Label,

	  2.  Instruction, directive, or data

	  3.  Comment

     A statement must contain at  least  one  of  these  elements  and  may
     contain  some  combination  of  them.   Any combination must be in the
     order given and they may be separated from each other by any number of
     spaces   or   tabs.    The  assembler  interprets  and  processes  the
     statements, generating one or more binary instructions or data  words,
     or performing an assembly process.



     2.1.1  Labels

     A label is the symbolic name created to identify  the  location  of  a
     statement in the program.  If present, the label is written first in a
     statement.  It must be a legal symbol name  and  be  terminated  by  a
     comma  or  colon.   Furthermore,  there  must be no intervening spaces
     between any of the characters and the comma, or colon.



     2.1.2  Instructions, Directives or Data

     An instruction may be one or more of the mnemonic machine instructions
     explained in Chapter 3.

     Directives are direct instructions to the MACREL assembler to  perform
     certain functions.  Since directives are instructions to the assembler
     itself they generally do not create code.


				      2-1

			 MACREL SOURCE PROGRAM FORMAT


     If this element of the statement contains only an  expression,  it  is
     evaluated by MACREL and stored in memory as data.



     2.1.3  Comments

     You may add notes or comments to a statement by separating these  from
     the  remainder of the line with a forward slash (/).  Such comments do
     not affect assembly processing or program execution but are useful  in
     the  program  listing  for later analysis or debugging.  The assembler
     ignores everything from the slash to the next carriage return.

     It is also possible to have only a carriage return  on  a  line.  This
     causes  a  blank  line  in  the assembly listing.  No error message is
     given.



     2.2  FORMAT EFFECTORS

     You can use the characters described below to control the format of an
     assembly  listing.   They allow a neat readable listing to be produced
     by providing a means of spacing through the program.



     2.2.1  Form Feed

     The form feed code causes the assembler to output blank lines in order
     to  skip  to  a  new  page  in  the output listing;  this is useful in
     creating a page-by-page listing.  The form feed is generated by typing
     a CTRL/L on the console terminal.



     2.2.2  Tabulations

     Tabulations are used in the body  of  a  source  program  to  separate
     fields into columns.  For example, a line written:

	  GO,TAD TOTAL/MAIN LOOP

     is much easier to read if tabs are inserted to form:

	  GO,	 TAD TOTAL	 /MAIN LOOP



     2.2.3  Statement Terminators

     You can use the RETURN key to terminate a statement  and  to  cause  a
     carriage  return/line  feed  combination to occur in the listing.  The
     semicolon (;) may also be  used  as  a  statement  terminator  and  is

				      2-2

			 MACREL SOURCE PROGRAM FORMAT


     considered  identical  to  a  carriage  return except that it will not
     terminate a comment.  For example in the following line:

	  TAD A  /THIS IS A COMMENT;    TAD B

     the entire expression between the slash and  the  carriage  return  is
     considered  a  comment.   Thus, in this case the assembler ignores the
     TAD B.















































				      2-3







				   CHAPTER 3

		       THE PDP-8 MACHINE INSTRUCTION SET



     This  chapter  describes  the  three  general  classes   of   computer
     instructions and the way in which they are used in programs.

     The first class of instruction operates upon data that  is  stored  in
     some  memory  location  and  must  tell the computer where the data is
     located in memory so that the computer can  find  it.   This  type  of
     instruction  is  said to reference a location in memory; therefore, it
     is called a memory reference instruction (MRI).

     When speaking of memory locations, it is very important that you  make
     a clear distinction between the address of a location and the contents
     of that location.  A memory reference instruction refers to a location
     via  a  12-bit address.  The instruction causes the computer to act on
     the contents of that location.  However, although  the  address  of  a
     specific  location  in  memory  remains  the same, the contents of the
     location are subject  to  change.   In  summary,  a  memory  reference
     instruction uses a 12-bit address value to refer to a memory location,
     and it operates on the 12-bit binary number stored in  the  referenced
     memory location.

     The  second   class   of   instruction   consists   of   the   operate
     microinstructions,  which  perform  a  variety  of  program operations
     without any need for reference to a memory location.  Instructions  of
     this  type  are  used  to perform the following operations:  clear the
     accumulator, test for negative accumulator,  halt  program  execution,
     etc..   Many  of  these  operate  microinstructions  can  be  combined
     (microprogrammed)  to  increase  the  operating  efficiency   of   the
     computer.

     The third class of instruction consists of the  input/output  transfer
     (IOT) instructions.  These instructions perform or aid in the transfer
     of information between a peripheral device and the computer memory.



     3.1  MEMORY REFERENCE INSTRUCTIONS

     Memory reference instructions take the form shown in Figure 3-1.

     Bits 0 through 2 contain the operation code of the instruction  to  be
     performed.   Bit 3 tells the computer if the addressing mode is direct
     or  indirect.   Bit  4  tells  the  computer  if  the  instruction  is
     referencing the current page or page zero.  This leaves bits 5 through
     11 (seven bits) to specify an address.  In these seven bits, 200 octal
     (128  decimal)  locations  can  be  specified;  the page bit increases

				      3-1

		       THE PDP-8 MACHINE INSTRUCTION SET


     accessible locations to 400 octal or  256  decimal.   A  list  of  the
     memory  reference  instructions and their codes is given at the end of
     the chapter.


		 0   1   2   3   4   5   6   7   8   9  10  11
	       -------------------------------------------------
	       | OPERATION |   |   |			       |
	       |  CODE 7   |   |   |	       ADDRESS	       |
	       |	   |   |   |			       |
	       ----|---|---|---|---|---|---|---|---|---|---|---|
			     ^	 ^
	INDIRECT ADDRESSING -|   |
	MEMORY PAGE -------------|

	    Figure 3-1 Memory Reference Instruction Bit Assignments


     In MACREL a  memory  reference  instruction  must  be  followed  by  a
     space(s)  or  tab(s),  an  optional  I or Z designation, and any valid
     expression.



     3.1.1  Addressing Modes

     The PDP-8 has two addressing modes, direct and indirect.  Consider the
     following:

	  TAD 40

     This is a direct address statement, where 40  is  interpreted  as  the
     location  on  page  zero  containing  the  quantity to be added to the
     accumulator.  References to locations on the  current  page  and  page
     zero  may  be  done directly.  For compatibility with older paper-tape
     assemblers the symbol Z is also accepted as a way of indicating a page
     zero reference, as follows:

	  TAD Z 40

     This is an  optional  notation,  not  differing  in  effect  from  the
     previous  example.   Thus,  if location 40 contains 0432, then 0432 is
     added to the accumulator.  When the symbol I appears  in  a  statement
     between  a memory reference instruction and an operand, the operand is
     interpreted as the address (or location) containing the address of the
     operand  to  be  used  in  the  current  statement.   Now consider the
     following:

	  TAD I 40

     This is an indirect address statement, where the contents 40  is  used
     as  the address of the location containing the quantity to be added to
     the accumulator.  Thus, if location 40 contains 0432, and location 432
     contains 0456, then 456 is added to the accumulator.

				      3-2

		       THE PDP-8 MACHINE INSTRUCTION SET


				     NOTE

		   Because   the   letters    I    and    Z
		   indicate  indirect  addressing,   and  a
		   page  zero  reference  respectively, you
		   cannot use them to name a variable.



     3.2  MICROINSTRUCTIONS

     Microinstructions  are  divided  into   two   groups:    operate   and
     Input/Output     Transfer     (IOT)     microinstructions.     Operate
     microinstructions are further subdivided into three groups:   Group  1
     Group  2,  and  Group  3.   Instructions  in  these  groups  cannot be
     intermixed.



     3.2.1  Operate Microinstructions

     Group  1  microinstructions  perform  clear,  complement,  rotate  and
     increment operations, and are designated by the presence of a 0 in bit
     3 of the machine instruction word, as shown in Figure 3-2.


		 0   1   2   3   4   5   6   7   8   9  10  11
	       -------------------------------------------------
	       |	   |   |   |   |   |   |   |   |   |   |
	       | 1   1   1 | 0 |CLA|CLL|CMA|CML|   |   |BSW|IAC|	
	       |	   |   |   |   |   |   |   |   |   |   |
	       ----|---|---|---|---|---|---|---|---|---|---|---|
						 ^   ^   ^
	ROTATE AC AND L RIGHT -------------------|   |   |
	ROTATE AC AND L LEFT ------------------------|   |
	ROTATE 1 POSITION IF A 0, 2 POSITIONS IF A 1 ----|
	(BSW IF BITS 8, 9 ARE 0)

	LOGICAL SEQUENCE:  1 - CLA, CLL    2 - CMA, CML
			   3 - IAC	   4 - RAR, RAL, RTR, RTL, BSW

	 Figure 3-2  Group 1 Operate Microinstruction Bit Assignments


     Group 2 microinstructions check the contents of  the  accumulator  and
     link  and,  based  on  the  check,  continue  on  to  or skip the next
     instruction.  Group 2 microinstructions are identified by the presence
     of a 1 in bit 3 and a 0 in bit 11 of the machine instruction word. See
     Figure 3-3.






				      3-3

		       THE PDP-8 MACHINE INSTRUCTION SET


		 0   1   2   3   4   5   6   7   8   9  10  11
	       -------------------------------------------------
	       |	   |   |   |   |   |   |   |   |   |   |
	       | 1   1   1 | 1 |CLA|SMA|SZA|SNL|   |OSR|HLT| 0 |
	       |	   |   |   |   |   |   |   |   |   |   |
	       ----|---|---|---|---|---|---|---|---|---|---|---|
						 ^
     REVERSE SKIP SENSING OF BITS 5, 6, 7 IF SET-|

	LOGICAL SEQUENCE:  1 (BIT 8 IS 0) - SMA OR SZA OR SNL
			     (BIT 8 IS 1) - SPA AND SNA AND SZL
			   2 - CLA
			   3 - OSR, HLT

	 Figure 3-3  Group 2 Operate Microinstruction Bit Assignments


     Group 3  microinstructions  reference  the  multiplier  quotient  (MQ)
     register.   They  are  differentiated from Group 2 instructions by the
     presence of a 1 in bits 3 and 11;   the  other  bits  are  part  of  a
     hardware arithmetic option.  Figure 3-4 shows these bit assignments.


		 0   1   2   3   4   5   6   7   8   9  10  11
	       -------------------------------------------------
	       | OPERATION |   |   |   |   |   |	   |   |
	       |  CODE 7   |   |CLA|MQA|   |MQL|	   |   |
	       |	   |   |   |   |   |   |	   |   |
	       ----|---|---|---|---|---|---|---|---|---|---|---|
			     ^		\_/     \_________/  ^
	CONTAINS 1 TO	     |		\_________________/  |
	SPECIFY GROUP 3 -----|			 ^	     |
	KE8-E EXTENDED ARITHMETIC ELEMENT -------|	     |
	CONTAINS A 1 TO SPECIFY GROUP 3 ---------------------|

	 Figure 3-4  Group 3 Operate Microinstruction Bit Assignments


     You cannot combine Group 1 and Group 2 microinstructions because bit 3
     determines  either  one  or  the other.  Within Group 2, there are two
     groups of skip instructions, the OR group and the AND group.

	  OR Group			AND Group	  ________			_________

	    SMA				   SPA
	    SZA				   SNA
	    SNL				   SZL

     The OR group is designated by a 0 in bit 8 and the AND group by a 1 in
     bit 8.  You cannot combine OR and AND group instructions because bit 8
     determines either one or the other.

     If you combine legal skip instructions, it is important  to  note  the
     conditions under which a skip may occur.

				      3-4

		       THE PDP-8 MACHINE INSTRUCTION SET


	  1.  OR Group-If you combine  these  skips  in  a  statement,  the
	      inclusive  OR  of  the  conditions  determines the skip.  For
	      example:

		   SZA SNL

	      The next statement is skipped  if  the  accumulator  contains
	      0000 or the link is a 1 or both.

	  2.  AND Group-If you combine these  skips  in  a  statement,  the
	      logical  AND  of  the  conditions  determines  the skip.  For
	      example:

		   SNA SZL

	      The next statement is skipped only if the accumulator differs
	      from 0000 and if the link is 0.


				     NOTE

		   If you specify an illegal combination of
		   microinstructions,  the  assembler  will
		   simply perform an inclusive  OR  between
		   them.    For   example,   CLL   SKP   is
		   interpreted as SPA  because  MACREL  ORs
		   7100  (CLL)  with  7410 (SKP) to produce
		   7510 (SPA).



     3.2.2  Input/Output Transfer Microinstructions

     These microinstructions initiate operation of peripheral equipment and
     effect  an  information transfer between the central processor and the
     Input/Output device.  (See Standard Instruction Set, Section 3.4.)



     3.3  AUTOINDEXING

     Interpage references are often necessary for obtaining  operands  when
     processing large amounts of data.  The PDP-8 computers have facilities
     to ease the addressing of this data.  When you indirectly address  one
     of  the  absolute  locations from 10 to 17 (octal) the contents of the
     location is incremented before it is  used  as  an  address,  and  the
     incremented  number  is  left  in  the  location.   This allows you to
     address  consecutive  memory  locations  using  a  minimum  number  of
     statements.   It must be remembered that initially these locations (10
     to 17 on page 0) must be set  to  one  less  than  the  first  desired
     address.  Because of their characteristics, these locations are called
     autoindex registers.  No incrementation takes place when locations  10
     to  17  are addressed directly.  For example, if the instruction to be
     executed next is in location 300 and the data to be referenced  is  on

				      3-5

		       THE PDP-8 MACHINE INSTRUCTION SET


     the page starting at location 5000, you can use autoindex register  10
     to address the data as follows:

	  0276	     1377	TAD C4777     /=5000-1
	  0277	     3010	DCA 10	      /SET UP AUTO INDEX
	  0300	     1410       TAD I10	      /INCREMENT TO 5000
	  .	     .		.	      /BEFORE USE AS AN
	  .	     .		.	       ADDRESS
	  .	     .		.
	  0377	     4777	C4777,4777

     When the instruction in location  300 is  executed,  the  contents  of
     location  10  will be incremented to 5000 and the contents of location
     5000 added to the contents of the accumulator.  When  the  instruction
     TAD  I  10  is  executed  again, the contents of location 5001 will be
     added to the accumulator and so on.



     3.4  STANDARD INSTRUCTION SET

     The following are  the  most  commonly  used  elements  of  the  PDP-8
     instruction set and are found in the permanent symbol table within the
     PAL8 Assembler.  For additional information on these instructions  and
     for  a description of the symbols used when programming other optional
     devices, see The Small Computer Handbook, or the PDP-8A  Miniprocessor		  ___________________________	      _____________________
     User's  Manual  (available  from  the  DIGITAL  Software  Distribution     ______________
     Center).


     ----------------------------------------------------------------------
     | Mnemonic       Code		    Operation		  Cycles  |
     |									  |
     |   Memory Reference Instructions					  |
     |									  |
     |   AND	      0000	 Logical AND			    2	  |
     |	 TAD	      1000	 Two's complement add		    2	  |
     |	 ISZ	      2000	 Increment and skip if zero	    2	  |
     |	 DCA	      3000	 Deposit and clear AC		    2	  |
     |	 JMS	      4000	 Jump to subroutine		    2	  |
     |	 JMP	      5000	 Jump				    1	  |
     |	 IOT	      6000	 In/Out transfer		    -	  |
     |	 OPR	      7000	 Operate			    1	  |
     ----------------------------------------------------------------------











				      3-6

		       THE PDP-8 MACHINE INSTRUCTION SET


     ----------------------------------------------------------------------
     | Mnemonic       Code		    Operation		 SEQUENCE |
     |									  |
     |   Group 1 Operate Microinstructions (1 cycle)			  |
     |									  |
     |	 NOP	      7000	 No operation			    -	  |
     |	 IAC	      7001	 Increment AC			    3	  |
     |	*BSW	      7002	 Byte swap			    4	  |
     |	 RAL	      7004	 Rotate AC and link left one	    4	  |
     |	 RTL	      7006	 Rotate AC and link left two	    4	  |
     |	 RAR	      7010	 Rotate AC and link right one	    4	  |
     |	 RTR	      7012	 Rotate AC and link right two	    4	  |
     |	 CML	      7020	 Complement the link		    2	  |
     |	 CMA	      7040	 Complement the AC		    2	  |
     |	 CLL	      7100	 Clear link			    1	  |
     |	 CLA	      7200	 Clear AC			    1	  |
     ----------------------------------------------------------------------
	 * PDP-8/A,E,F,M and VT78 only

     ----------------------------------------------------------------------
     | Mnemonic       Code		    Operation		 SEQUENCE |
     |									  |
     |   Group 2 Operate Microinstructions (1 cycle)			  |
     |									  |
     |	 HLT	      7402	 Halts the computer		    3	  |
     |	 OSR	      7404	 Inclusive OR SR with AC	    3	  |
     |	 SKP	      7410	 Skip unconditionally		    1	  |
     |	 SNL	      7420	 Skip on non zero link		    1     |
     |	 SZL	      7430	 Skip on zero link		    1	  |
     |	 SZA	      7440	 Skip on zero AC		    1	  |
     |	 SNA	      7450	 Skip on non zero AC		    1	  |
     |	 SMA	      7500	 Skip on minus AC		    1	  |
     |	 SPA	      7510	 Skip on positive AC (zero is	    1	  |
     |				 positive)				  |
     |									  |
     |  *Group 3 Operate Microinstructions				  |
     |									  |
     |	 MQA	      7501	 Multiplier Quotient OR into AC	    2	  |
     |	 MQL	      7421	 Load Multiplier Quotient	    2	  |
     |	 SWP	      7521	 Swap AC and Multiplier Quotient    3	  |
     |	 CLA	      7601	 Clear AC			    1	  |
     |	 NOP	      7401	 No operation			    -	  |
     |	 CAM	      7621	 Clear AC and MQ		    3	  |
     |	 SWP	      7521	 Swap AC and MQ			    3	  |
     |	 ACL	      7701	 Load MQ into AC		    3	  |
     |	 CLA SWP      7721	 Load MQ into AC and clear MQ	    3	  |
     ----------------------------------------------------------------------
	* If MQ is available in hardware.







				      3-7

		       THE PDP-8 MACHINE INSTRUCTION SET


     ----------------------------------------------------------------------
     | Mnemonic       Code		    Operation			  |
     |									  |
     |   Combined Operate Microinstructions				  |
     |									  |
     |	 CIA	      7041	 Complement and increment AC		  |
     |	 STL	      7120	 Set link to 1				  |
     |	 GLK	      7204	 Get link (put link in AC, bit 11)	  |
     |	 STA	      7240	 Set AC to -1				  |
     |	 LAS	      7604	 Load AC with SR			  |
     |									  |
     |   Internal IOT Microinstructions					  |
     |									  |
     |	 SKON	      6000	 Skip with interrupts on and turn	  |
     |				 them off				  |
     |	 ION	      6001	 Turn interrupt processor on		  |
     |	 IOF	      6002	 Turn interrupt processor off		  |
     |	 GTF	      6004	 Get flags				  |
     |	 RTF	      6005	 Restore flag, ION			  |
     |	 SGT	      6006	 Skip if "Greater Than" flag is set	  |
     |	 CAF	      6007	 Clear all flags			  |
     |									  |
     |   Keyboard/Reader (1 cycle)					  |
     |									  |
     |	 KCF	      6030	 Clear keyboard flags			  |
     |	 KSF	      6031	 Skip on keyboard/reader flag		  |
     |	 KCC	      6032	 Clear keyboard/reader flag and		  |
     |				 AC;  set reader run			  |
     |	 KRS	      6034	 Read keyboard/reader buffer		  |
     |				 (static)				  |
     |	 KIE	      6035	 Set/clear interrupt enable		  |
     |	 KRB	      6036	 Clear AC, read keyboard buffer		  |
     |				 (dynamic), clear keyboard flags	  |
     |									  |
     |   Teleprinter/Punch (1 cycle)					  |
     |									  |
     |	 TFL	      6040	 Set teleprinter flag			  |
     |	 TSF	      6041	 Skip on teleprinter/punch flag		  |
     |	 TCF	      6042	 Clear teleprinter/punch flag		  |
     |	 TPC	      6044	 Load teleprinter/punch and print	  |
     |	 TSK	      6045	 Skip on keyboard or teleprinter flag	  |
     |	 TLS	      6046	 Load teleprinter/punch, print,		  |
     |				 and clear teleprinter/punch flag	  |
     ----------------------------------------------------------------------











				      3-8

		       THE PDP-8 MACHINE INSTRUCTION SET


     ----------------------------------------------------------------------
     | Mnemonic       Code		    Operation			  |
     |									  |
     |   High Speed Perforated Tape Reader				  |
     |									  |
     |	 RPE	      6010	 Set Reader/Punch interrupt enable	  |
     |	 RSF	      6011	 Skip if reader flag=1			  |
     |	 RRB	      6012	 Read reader buffer and clear flag	  |
     |	 RFC	      6014	 Clear flag and buffer and fetch	  |
     |				 character				  |
     |									  |
     |   High Speed Perforated Tape Punch				  |
     |									  |
     |	 PCE	      6020	 Clear Reader/Punch interrupt enable	  |
     |	 PSF	      6021	 Skip if punch flag=1			  |
     |	 PCF	      6022	 Clear flag and buffer			  |
     |	 PPC	      6024	 Load buffer and punch character	  |
     |	 PLS	      6026	 Clear flag and buffer, load buffer	  |
     |				 and punch character			  |
     |									  |
     |   Memory Extension						  |
     |									  |
     |	*CDF	      62nl	 Change to Data Field n (n=00 to 07)	  |
     |		      62n5	 Change to Data field n (n=10 to 17)	  |
     |		      63nl	 Change to Data Field n (n=20 to 27)	  |
     |		      63n5	 Change to Data Field n (n=30 to 37)	  |
     |	*CIF	      62n2	 Change to Instruction Field n		  |
     |				 (n=00 to 07)				  |
     |		      62n6	 Change to Instruction Field n		  |
     |				 (n=10 to 17)				  |
     |		      63n2	 Change to Instruction Field n		  |
     |				 (n=20 to 27)				  |
     |		      63n6	 Change to Instruction Field n		  |
     |				 (n=30 to 37)				  |
     |	*CDI	      62n3	 Change to Data and Instruction Fields n  |
     |				 (n=00 to 07)				  |
     |		      62n7	 Change to Data and Instruction Fields n  |
     |				 (n=10 to 17)				  |
     |		      63n3	 Change to Data and Instruction Fields n  |
     |				 (n=20 to 27)				  |
     |		      63n7	 Change to Data and Instruction Fields n  |
     |				 (n=30 to 37)				  |
     |	 RDF	      6214	 Read Data Field			  |
     |	 RIF	      6224	 Read Instruction Field			  |
     |	 RIB	      6234	 Read Interrupt Buffer			  |
     |	 RMF	      6244	 Restore Memory Field			  |
     ----------------------------------------------------------------------
	* See Figure 3-5 for mapping of extended memory bits into the
	instruction word.






				      3-9

		       THE PDP-8 MACHINE INSTRUCTION SET


			Field Number (0-37) = abcde

		      bit 0		      bit 11
		CDF	| 110 | 01a | cde | b01 |
			-------------------------

		CIF	| 110 | 01a | cde | b10 |
			-------------------------

	    CDF CIF	| 110 | 01a | cde | b11 |
			-------------------------

      Figure 3-5  Extended Memory Bit Mapping for CDF and CIF Instructions



     3.5  CONSTANTS

     Occasionally you may find it convenient to load the accumulator with a
     constant  produced by combinations of microinstructions, or to produce
     a combination of microinstructions by loading a constant.  Some common
     examples follow:

	  Constant	Instruction	  ________	___________

	       0	CLA
	       1	CLA IAC
	       2	CLA CLL CML RTL
	       3*	CLA CLL CML IAC RAL
	       4*	CLA CLL IAC RTL
	       6*	CLA CLL CML IAC RTL
	     100*	CLA IAC BSW
	    2000	CLA CLL CML RTR
	    3777	CLA CLL CMA RAR
	    4000	CLA CLL CML RAR
	    5777	CLA CLL CMA RTR
	    6000*	CLA CLL CML IAC RTR
	    7775	CLA CLL CMA RTL
	    7776	CLA CLL CMA RAL
	    7777	STA (=CLA CMA)

     *  Do not  use  these  instructions  in  software  that  runs  on  old
     (non-Omnibus) PDP-8 computers.












				     3-10







				   CHAPTER 4

		       EXPRESSIONS AND THEIR COMPONENTS


     This  chapter  discusses  MACREL  expressions   and   their   symbolic
     components.    Some   parts  of  this  chapter  refer  to  symbols  or
     expressions in relocatable code.  You should, therefore,  be  familiar
     with Chapter 1 before proceeding with this chapter.

     Often a major element of a MACREL  statement  is  an  expression.   An
     expression may be composed from one or more of the following
     components:

	  o  Symbols
	  o  Operators
	  o  Special Operators
	  o  Numbers

     Naturally,  there  are specific  rules  for  the  combination  of  the
     elements  of statements and expressions.  This chapter describes these
     elements and the rules for their valid combination.



     4.1  MACREL CHARACTER SET



     4.1.1  Alphanumeric Characters

     MACREL accepts as input all of the upper case alphabetic characters  A
     through  Z,  the  numeric  characters  0 through 9, and the characters
     dollar sign ($) and period (.).

     Lower case alphabetic characters are permitted within a symbol and are
     treated   as  the  corresponding  upper  case  character.   The  first
     character of a symbol may  not be  a  digit,  and  only  the  first  6
     characters (not counting an initial $) of a symbol are significant.



     4.1.2  Special Characters and Operators

     MACREL also accepts as input certain special characters and operators,
     which  are  listed  alphabetically  in  Table  4-1  below.  All of the
     special  characters  and  operators  are  explained  and   their   use
     illustrated in various sections of this manual.




				      4-1

		       EXPRESSIONS AND THEIR COMPONENTS


				   Table 4-1
		       Special Characters and Operators

     ----------------------------------------------------------------------
     |	    Name	  | Symbol |	     Name		 | Symbol |
     |--------------------------------------------------------------------|
     |  Angle Brackets	  |  < >   |  I				 |   I	  |
     |  Ampersand	  |   &	   |  Left Right Parenthesis	 |   ()   |
     |  Apostrophe	  |   '	   |  Left/Right Square Brackets |   []   |
     |  Asterisk	  |   *	   |  Minus Sign		 |   -	  |
     |  Back Slash	  |   \	   |  Percent Sign		 |   %	  |
     |  Colon		  |   :	   |  Period			 |   .	  |
     |  Comma		  |   ,	   |  Plus Sign			 |   +	  |
     |  Dollar Sign	  |   $	   |  Semicolon			 |   ;	  |
     |  Double Quotes	  |   "	   |  Up Arrow			 |   ^	  |
     |  Exclamation Point |   !	   |  Up Arrow Double Quote	 |   ^"	  |
     |  Equal Sign	  |   =	   |  Z				 |   Z	  |
     |  Forward Slash	  |   /	   |				 |	  |
     ----------------------------------------------------------------------

     Both the space and tab are legal input to MACREL also and their use is
     described in Chapter 2.



     4.2  SYMBOLS

     A symbol in MACREL is a valid combination of letters, digits, and  the
     characters period (.) and dollar sign ($).  The symbol must begin with
     either a letter, a period, or a dollar sign.   If  it  begins  with  a
     dollar sign the second character must not be a digit.

     A symbol may consist of any number of characters, but only  the  first
     six  are  significant.   (If  the  first character is a dollar sign, a
     total of seven characters are significant.) The  remaining  characters
     are merely scanned for valid characters and ignored.  Thus, the symbol
     NEW.VALUE is exactly equivalent to NEW.VA.  If the last character in a
     symbol  is  a  dollar  sign,  that  symbol is considered to be a local
     symbol (see Section 4.2.4).  A symbol is terminated by  any  character
     other  than  those mentioned.  Thus, in the expression NEW+1, the plus
     sign (+) terminates the symbol NEW.

     Normally symbols in MACREL are unique.  A macro name, for example, may
     not  be  used  as  an  ordinary  symbol.   The  one exception is local
     symbols, which need not be unique, in different local symbol blocks.

     The following are valid symbol names:

	  DATA1
	  $POINTR
	  .LONGER	 only .LONGE is significant
	  .A....
	  NEW.VL
	  .A.1.3

				      4-2

		       EXPRESSIONS AND THEIR COMPONENTS


	  GET$		 local symbol
	  HYPOTENUSE	 only HYPOTE is significant

     The following are not valid symbol names:

	  NU MER	 symbols cannot contain embedded spaces
	  1STNUM	 symbols cannot begin with a digit
	  $3BUF		 a digit may not follow an initial dollar sign
	  R:03		 invalid character


				     NOTE

		   Though legal,  you  should  avoid  using
		   symbols  starting  with  period  (.)  or
		   global symbols that  begin  with  dollar
		   sign  ($), as they may be used by future
		   system  software  released  by   DIGITAL
		   EQUIPMENT CORP.


     Internally, symbol definitions are stored in  the  assembler's  symbol
     table.   Thus,  with  the  exception  of  a  few  symbols  defined  by
     directives, symbols are evaluated  during  the  assembly  process  and
     converted   to   12-bit   values.   LINK  completes  this  process  of
     evaluation, especially in the case of relocatable symbols.



     4.2.1  Permanent Symbols

     A number of  symbols  are  reserved  for  use  as  machine-instruction
     mnemonics,  directives,  and  special  operators.   These  symbols are
     maintained in the permanent symbol table.  If you attempt to  redefine
     any  of  these  through  use of a comma (,), colon (:), or equals sign
     (=), an  error  message  is  produced.   For  example,  the  statement
     AND=7000 will produce an error message.

     For compatibility with PAL8, the old pseudo-op PAUSE is reserved as  a
     permanent symbol, but is otherwise ignored.

     Assembler command string options  allow  you  to  add  or  delete  the
     PDP-8/E  symbols  and  the  extended arithmetic instruction mnemonics.
     Another run-time option deletes certain redundant PAL8 pseudo-ops from
     the symbol table.

     The entire permanent symbol table, including those symbols altered  by
     command string options, is listed in Appendix C.

     You can also alter the permanent symbol table by  using  the  EXPUNGE,
     FIXMRI, and FIXTAB directives (see Section 5.9).




				      4-3

		       EXPRESSIONS AND THEIR COMPONENTS


     4.2.2  Program-Defined Symbols

     You must define any symbol that is not a permanent symbol by  entering
     the  symbol name as the first item (excluding any spaces or tabs) on a
     line, followed immediately by a comma (,), colon (:), or  equals  sign
     (=).  If you refer to a symbol that is not defined in this way, and is
     not declared as  .EXTERNAL,  an  undefined  symbol  error  message  is
     printed.  For example, the code DCA ALPHA+5 causes an error message if
     ALPHA is not defined.  A symbol defined with a comma or a colon  is  a
     label  and  a  symbol defined by the equal sign is a directly assigned
     symbol.  Both labels  and  directly  assigned  symbols  are  discussed
     below.

     In addition to these familiar ways  of  defining  symbols,  there  are
     three  other  special  ways  of  defining  symbols.  The first is by a
     program section name.  The name of a program section is  defined  when
     you  use  it  following  some  form of program section directive.  For
     example:

	  .RSECT GVALUE
     or
	  .SECT DATA1, D

     define sections with names of GVALUE and DATA1 respectively.  You  can
     use these symbols in expressions, but they cannot be redefined.

     Two other ways of defining symbols relate to macros.  A macro name  is
     a  symbol  that  stands  for  a  sequence of code, and use of the name
     causes that sequence of code to be inserted into the program.  Thus, a
     macro  name  is  an entirely different entity from an ordinary symbol.
     However, the use of symbols as dummy arguments in a  macro  definition
     does  not  define  them.  Both of these special cases are discussed in
     detail in Chapter 6.



     4.2.3  Labels

     A  label  is  a  program-defined  symbol  terminated  by  a  comma  or
     optionally,  by a colon (for local symbol blocks).  The comma or colon
     must immediately follow the symbol name.  The label must be the  first
     entry  on  a  line  (excluding spaces and tabs, and except for another
     label) and generally is placed at the left margin.

     A label is used to identify an address in memory.  It is assigned  the
     value  of  the  current  location counter.  The following two lines of
     code:

		   *400
	  STRT,	   TAD 20

     are equivalent to:



				      4-4

		       EXPRESSIONS AND THEIR COMPONENTS


		   *400
	  STRT	  =.
		   TAD 20

     Both examples create an entry in the symbol table  with  the  name  of
     STRT  and  a  value  of  400  relative to the beginning of the current
     program section.  Further, they both result in a line of code  with  a
     relative  location  of  400  and value of 1020.  (See Sections 4.4 and
     4.3.)

     Since a label is a symbol and has as its value an address, it is  also
     called  a  symbolic  address.   In  programming  it  is  important  to
     distinguish the address from the contents of that  address.   Although
     for  expediency  you  might  write a line of code and a comment in the
     form:

	  TAD	   BUFSZE   /ADD BUFSZE, THE LENGTH
			    /OF THE BUFFER.

     remember that you are not actually adding BUFSZE  (since  that  is  an
     address)  but  rather  the  contents  of  BUFSZE.  This distinction is
     especially important in  expressions  involving  indirect  addressing,
     literals, and computed addresses.

     You cannot use a label to redefine a symbol;  you must  use  a  direct
     assignment statement instead.  In the following code:

		   *600
	  INIT,	   TAD B
		   .
		   .
		   .
	  INIT,	   NOP

     the second use of  INIT  will  result  in  a  redefined  symbol  error
     message.  The same error message results if you attempt to use a label
     to redefine a symbol  already  defined  through  a  direct  assignment
     statement.

     More than one label, however, may have  the  same  value.   Thus,  the
     code:

		   *300
	  NAME1,
	  NAME2,
	  NAME3,   0

     is perfectly legal, and results in NAME1, NAME2, and NAME3 all  having
     a value of 300.  The following line:

	  NAME1, NAME2, NAME3, 0

     is also legal, and also results in the three labels having a value  of
     300.

				      4-5

		       EXPRESSIONS AND THEIR COMPONENTS


     4.2.4  Local Symbols

     The local symbol feature of MACREL allows  you  to  use  a  convenient
     symbol  name  in one segment of a program, and then, without conflict,
     use the same symbol name in another segment.  You  designate  a  local
     symbol  by using a dollar sign ($) as the last character.  Thus, DATA$
     is a local symbol.

     Local symbols are defined only within a local symbol block.   A  local
     symbol  block  extends from one label defined with a comma to the next
     label defined with a comma, or as far  as  the  next  program  section
     directive,  or  PAGE  directive,  or as far as the end of the program,
     whichever comes first.  Any labels inside the local symbol block  must
     be  defined  using  a  colon  (:)  rather  than  a  comma.  A colon is
     equivalent to a comma, except that it does not  cause  termination  of
     the local symbol block.

     The following is an example of a  local  symbol  block  (the  code  is
     hypothetical):

		   .
		   .
		   .
	  INR,	   DCA		NEW
		   TAD		COUNT$
		   CIA
	  LOOP$:   TAD		OFFSET
		   ISZ		BCNT$
		   JMP		LOOP$

		   JMP		: NEXT
	  /DATA
	  BCNT$:   0
	  COUNT$:  0
	  NEXT,    0

     Notice that the local symbol block starts with  the  first  use  of  a
     label  with a comma (INR,) and terminates with the next use of a label
     with a comma (NEXT,).  All labels inside the local symbol  block  must
     be defined with a colon.

     If you refer to a local symbol outside its block and fail to define it
     as a local symbol in a new local symbol block, the assembler prints an
     undefined-symbol error message.  Local symbols do not  appear  in  the
     symbol  table  but can be included in the cross-reference listing.  In
     effect, they are invisible to the  program  outside  their  own  local
     symbol block.

     You can also define local symbols with a direct assignment  statement.
     The  equals sign of the direct assignment statement does not terminate
     the local symbol block;  only a label with a  comma  or  a  new  .SECT
     Directive or the end of the program delimit the local symbol block.



				      4-6

		       EXPRESSIONS AND THEIR COMPONENTS


     A local symbol may also consist of one to four decimal digits followed
     by  a  dollar sign.  For example, 3$ or 1234$, are both local symbols.
     The value of the digits must be  less  than  4096  (decimal)  and  may
     include  leading zeros which are not significant.  The value may be an
     expression enclosed in angle brackets.  Thus, if A=3 then

	  <A+3>$

     represents the symbol 6$.



     4.2.5  Backslash (\) Special Operator

     You can insert numeric characters  that  represent  the  value  of  an
     expression  into  a  symbol  name  by  using the backslash (\) special
     operator.  If MACREL encounters a backslash within a symbol  name,  it
     evaluates the term to the right of the backslash and inserts its value
     into the symbol name.  For example:

	  DATA\NUMB

     If the value of the symbol NUMB is 2, this  construction  generates  a
     symbol  DATA2  that  is exactly identical to a symbol DATA2 written in
     the program source.  Moreover it can be referenced as DATA2  by  other
     segments  of  programs.   Similarly,  if  NUMB  has a value of 12, the
     symbol will be DATAl2.

     The following code:

		   AP=0
	  N\AP,	   AP+"0
		   AP=AP+1
	  N\AP,	   AP+"0
		   AP=AP+1
	  N\AP,	   AP+"0

     produces three labels with the following contents:  N0, which contains
     ASCII 0;  N1, which contains ASCII 1;  and N2, which contains ASCII 2.

     In evaluating symbols with a backslash, the assembler uses the current
     radix.  If the radix is changed to 2, as in the following example:

		   N=7
		   .RADIX 2
		   TAD B\N
		   .
		   .
		   .
	  B1,	   0
	  B10,	   0
	  B11,	   0
	  B100,	   0
	  B101,	   0

				      4-7

		       EXPRESSIONS AND THEIR COMPONENTS


	  B110,	   0
	  B111,	   0

     the assembler will evaluate the symbol N in TAD B\N as a binary  value
     (.RADIX 2), and the instruction causes the program to load the current
     contents of Blll.

     In evaluating the number following the backslash,  leading  zeros  are
     ignored.  Thus, N\0001 is evaluated as N1.  Also, if the number to the
     right of the backslash contains more than six significant digits, only
     the  least significant (rightmost) six are used.  This situation might
     occur, for example, if the current radix were 2 (binary).

     You may use the backslash  construction  anywhere  in  a  program  and
     should  find  it  particularly  valuable  in  creating  symbols within
     macros.

     Notice that all evaluation of  the backslash  construction  occurs  at
     assembly  time.   In  the  example shown above, the value of N must be
     absolute.

     The backslash must be within the symbol and  must  be  followed  by  a
     term.  An expression can be used after the backslash if it is enclosed
     in angle brackets.  Thus,

	  A\B+C

     is not a legal symbol whereas,

	  A\<B+C>

     is.  The expression B+C could also be assigned  a  name  by  a  direct
     assignment.  Thus,

	  N=B+C

	  A\N

     produces a legal symbol.

     The backslash may be embedded in a  symbol.   Thus  if  C=3  then  the
     following code

	  AB\<C+2>D

     represents the symbol AB5D.

     The backslash may be nested without limit.  For example,

	  A\B\C

     is identical to:

	  A\<B\C>.

				      4-8

		       EXPRESSIONS AND THEIR COMPONENTS


     4.2.6  Symbols and Relocation

     One function that MACREL and LINK perform (as a unit) is the reduction
     of  symbols  to  12-bit  (or in the case of addresses, 17-bit) numeric
     values.  Although the function of the assembler is to  reduce  symbols
     to numerical values, at the end of the assembly operation many symbols
     are not yet evaluated.  In fact, the assembler cannot evaluate symbols
     that  are  to  be  relocated, because the amount by which they will be
     relocated is determined by the loading address of the beginning of the
     program section.  This address cannot be known until LINK runs.

     For this reason, the assembler stores symbols as an absolute part  and
     a  relocatable part.  The complete value of the symbol is not known at
     assembly time.  MACREL passes any expression that is more  complicated
     than this to LINK for resolution.  For example, a symbol that requires
     two relocatable parts to evaluate is complex relocatable.

     Symbols can be classified into  five  groups:   absolute  (relocatable
     part  is  zero),  relocatable  (absolute  plus  one relocatable part),
     complex relocatable (neither of the above),  CDF/CIF  Relocatable  and
     .FSECT  Relocatable.   Up  to  now,  the examples in this chapter have
     assumed that the program is one absolute section, and the symbols  are
     all  absolute.   Any  label, however, that is defined in a relocatable
     section will be simply relocatable.  If the example  used  in  Section
     4.2.3 appeared in a relocatable section named RELOK, as:

		  .RSECT RELOK
		  *400
	  STRT,   TAD 20

     then the label  STRT  will  have  an  absolute  value  of  400  and  a
     relocatable  part  of  RELOK.  STRT will appear in the symbol table as
     00400+RELOK.  (Note that the assembler directive RELOC cannot be  used
     as a program section name.)

     In practice, you will adjust to this difference quickly and there will
     be little change in the way that you write code.



     4.3  DIRECT ASSIGNMENT STATEMENT

     A direct assignment statement  assigns  a  value  to  a  symbol.   The
     statement has two forms.  The first form is:

	  Symbol=Expression

     There must not be any space between the symbol  and  the  equal  sign.
     The direct assignment statement defines the symbol as having the value
     of the expression on the right.  For example, DATA=7 causes DATA to be
     assigned  a  value  of 7.  Notice that this is different from a label,
     which defines the symbol as having the value of the current address.



				      4-9

		       EXPRESSIONS AND THEIR COMPONENTS


     The second form of the direct assignment is:

	  Global Symbol==Expression

     Here, the double equals sign must immediately follow the  symbol,  and
     there  must be no space between the two equal signs.  This form of the
     direct assignment statement is the same as that of  the  single  equal
     sign, but in addition it defines the symbol as being a global symbol.
     Thus,

	  BUFSZE==100

     is exactly the same as:

	  .GLOBAL BUFSZE
	  BUFSZE=100

     Use of the .GLOBAL directive is discussed in Chapter 7.

     When used in any program section, the expression to  the  right  of  a
     direct assignment statement can be any legal expression that is either
     simply relocatable or absolute.  Thus,

	  XVALUE=2^<BCNT+4>-2

     is a perfectly legal statement provided that BCNT is  defined  in  the
     current  source  module  and is absolute.  One forward reference to an
     undefined symbol is allowed,  but  more  than  one  is  illegal.   For
     example,

	  A=B
	   .
	   .
	   .
	  B=3

     is a legal sequence of code, because although B is  unknown  when  the
     assembler  reaches  A=B,  it  is known when the assembler reaches B=3.
     This is one forward reference.  However,

	  A=B
	   .
	   .
	   .
	  B=C
	   .
	   .
	   .
	  C=3

     is not a  legal  sequence  of  code  because  there  are  two  forward
     references:  A cannot be known until B is known, and B cannot be known
     until C is known.  This structure may cause your program  to  assemble
     incorrectly.

				     4-10

		       EXPRESSIONS AND THEIR COMPONENTS


     You can use a direct assignment statement  to  redefine  a  previously
     defined  symbol,  but  not  to  redefine  a macro name, a directive, a
     machine-instruction mnemonic, or any other permanent symbol.  Use of a
     direct  assignment  statement  to  redefine any of these results in an
     error message.

     In relocatable program sections, some care is required in the  use  of
     direct assignment statements.  For example,

	  XVALUE=2^<BCNT+4>-2

     will produce a COMPLEX-RELOCATABLE ERROR message if BCNT is a label in
     a  relocatable section, because the value of the expression containing
     BCNT cannot be determined until link time, though XVALUE needs a value
     at assembly time.

     A direct assignment statement assigns to the symbol to the left of the
     equals  sign  all  the characteristics of the expression on the right:
     its absolute part and its relocatable part.  An assembly error results
     if  the  expression  to  the  right  of  the  equal sign is not simply
     relocatable, and the symbol to the left of the equal  sign  is  not  a
     global or external symbol.



     4.4  CURRENT LOCATION COUNTER

     The assembler  maintains  an  internal  register  called  the  current
     location  counter,  which  contains  the address of the next available
     location.  As each instruction or data word is assigned, the  counter,
     is  increased  by  one.   To  set  this  counter, use the asterisk (*)
     directive (see Section 5.5).

     To obtain the value of the current location counter,  use  the  period
     (.) operator.  You can use this permanent symbol in expressions in the
     same way as any other symbol.  Because it is a symbol, you cannot  use
     it  next  to  another  symbol  (including an instruction mnemonic);  a
     space  or  other  character  must  intervene.   For  example,  in  the
     statement  DCA.+3,  the  assembler would assume you are referring to a
     symbol DCA., and are trying to add 3 to it.

     The period always has the value of the current location counter.  Like
     other permanent symbols, it cannot be redefined by a direct assignment
     statement.  Because it has the value of the current location  counter,
     the  period  itself is often called the current location counter.  One
     of its common uses is demonstrated by a statement of the form:

	  JMP .+3

     This means, jump to the current location plus three.   This  statement
     implies  that you will not at some time insert additional code between
     JMP .+3 and  the  location  jumped  to.   If  future  insertion  is  a
     possibility, it is better to jump to a local symbol.


				     4-11

		       EXPRESSIONS AND THEIR COMPONENTS


     4.5  LITERALS

     Literals are expressions, which are defined  by  parentheses  (current
     page  literals),  or  square  brackets (page zero literals).  They are
     evaluated and assigned locations by the assembler.



     4.5.1  Current Page Literals

     Parentheses () define a current page literal.  The  assembler  assigns
     them  a  location  beginning  at  the  highest location on the current
     page and works downward.  For example,  in  an  absolute  section  the
     following code,

	  *400
	  TAD (-4)
	  JMS I (DECODE)
	   .
	   .
	   .

     results in two literals being generated, and if DECODE is a  label  at
     address 600, the assembly listing appears as,

	  1		0400		   *400
	  2    00400	1377		   TAD (-4)
	  3    00401	4776		   JMS I (DECODE)
	       -----
	       00576	0600
	       00577	7774

     The literals are listed after the five hyphens in a  program  listing.
     The  TAD (-4) line results in generating a literal at address 577 (the
     top of  the  page)  that  contains  a  minus  four  (7774).   The  TAD
     instruction   addresses  this  location.   The  JMS  I  (DECODE)  line
     generates a pointer (stored at location 576) to DECODE (which  has  an
     address  0600).   The JMS instruction uses location 576 as an indirect
     pointer to location 0600.

     In evaluating a literal, the assembler first evaluates the  expression
     contained  within  the  parentheses  and then stores this value in the
     location that it allocates.  The right parenthesis is  optional,  and,
     if  omitted,  the  assembler  evaluates  the entire line as far as the
     carriage return or semicolon,  and  assigns  that  expression  to  the
     literal.   The  assembler  then  refers to the literal in terms of its
     address.  Thus, the left parenthesis of a literal can be thought of as
     meaning  "the  address where the following expression is stored".  For
     example, the TAD (-4) in the previous example means:  "Perform a two's
     complement add of the contents of the address where a -4 is stored".

     Literals may also be  nested.   In  evaluating  nested  literals,  the
     assembler  first evaluates the expression in the innermost parentheses
     and assigns it  a  storage  location.   It  then  evaluates  the  next

				     4-12

		       EXPRESSIONS AND THEIR COMPONENTS


     innermost  parenthesis and assigns it a location.  It proceeds in this
     manner  until  all  the  literals  have  been  evaluated.   Thus,  the
     assembler  will generate a number of storage words equal to the number
     of left parentheses.  The following is an example of  nested  literals
     and the resulting code:

	  1		0200		   *200
	  2    00200	0000	 A1,	   0
	  3    00201	1376	 ENTRY,    TAD (DCA (A1))
	       -----
	       00376	3377
	       00377	0200

     The top literal (address 377) contains the evaluation of the innermost
     parentheses,  the  address  of  A1.   The  next  literal (address 376)
     contains the value of the code generated by DCA (A1).   The  TAD  then
     addresses this value.

     When computing literals, the  assembler  keeps  track  of  the  values
     stored  on  the  current page and does not store more than one literal
     with the same value.  The assembler works on the assumption  that  the
     values stored in literal locations are unchangeable.  For example, the
     DCA (7 line of code in the following example:

	  CLA
	  DCA (7)
	  TAD (7)

     will overwrite the 7 stored in the literal location, so that  the  TAD
     (7) line will no longer load the AC with a 7, as was intended.

     The assembler will not create two literals with the same  value.   For
     example:

	  1
	  2    00200	1377	 A,	TAD	(3+5)
	  3    00201	1376	 B,	TAB	(4000)
	  4    00202	0377	 C,	AND	(10)
	       -----
	       00376	4000
	       00377	0010

     The assembler refers both literals (3+5) and  (10)  to  location  377.
     This  is called literal sharing.  This literal sharing takes place for
     simple relocation literals only if both  the  absolute  part  and  the
     relocatable part are the same.

     Literals that to the assembler are different cannot be shared, even if
     after evaluation by LINK they prove to have the same value.

     Literals cannot be  complex  relocatable  and  should  not  appear  in
     .XSECTs  or  .DSECTs.   In a named program section you should use page
     zero for literals rather than the current page.


				     4-13

		       EXPRESSIONS AND THEIR COMPONENTS


     The literal pool cannot contain more  than  100(8)  literals.   MACREL
     stores literals in memory as follows:

	  o  In  an  unnamed  absolute  program  section  (.ASECT),  MACREL
	     assigns current page literals to locations in descending order
	     beginning at the end  of  the  page.   It  assigns  page  zero
	     literals  to  locations  in  page  zero  in  descending  order
	     beginning at location 177.

	  o  In a named absolute program section  (.ASECT)  or  relocatable
	     program section (.RSECT), MACREL assigns current page literals
	     to locations in descending order beginning at the end  of  the
	     page.  It assigns page zero literals to locations in a special
	     page zero (.ZSECT) literal program section in increasing order
	     starting  at  the  beginning  of the program section.  (MACREL
	     creates names for these literal page zero program sections  by
	     using the name of the program section where a literal is first
	     referenced prefixed with a dollar sign ($).)

	  o  In a floating program section (.FSECT), MACREL assigns current
	     page literals to locations in ascending order beginning at the
	     end of the .FSECT.  It assigns page zero  .FSECT  literals  in
	     the same way that it assigns page zero .RSECT literals.

     If you put too  many  words  of  code  in  a  memory  page  containing
     literals, the code will begin to overwrite the existing literals.  The
     assembler will print  an  appropriate  error  message  for  each  such
     occurrence.


				   CAUTION

		   One  situation   where   the   assembler
		   overwrites   literals  without  printing
		   error messages is  when  you  reset  the
		   current  location  counter to a previous
		   page containing literals  by  using  the
		   Asterisk  (*), PAGE or FIELD directives.
		   The assembler does not retain the number
		   of  literals  stored  on  the previously
		   assembled page and it begins storing any
		   new  literals  at  the  top of the page,
		   thus overwriting any previous  literals.
		   To  avoid  this problem, you should code
		   straight through, rather than return  to
		   a previous page.



     4.5.2  Page Zero Literals

     Page zero literals are defined by square  brackets  ([]).   The  right
     square  bracket  is optional in the same way as the right parenthesis.
     Moreover, the assembler treats page zero literals in the same  way  as

				     4-14

		       EXPRESSIONS AND THEIR COMPONENTS


     current  page  literals, except that it stores them on page zero, thus
     making them  available  to  all  pages  in  the  current  field.   The
     following two lines of code,

	  TAD (4)
	  TAD [4]

     each generates a literal, one on the current  page  and  one  on  page
     zero.  It may be to your advantage to use page zero literals (if there
     is room on page zero) when certain literals  are  used  frequently  on
     many pages.  Like other literals, the assembler does not keep track of
     page zero literals when you leave the current program section, or  the
     current  field  in  an  unnamed  program  section.   Therefore,  it is
     possible to overwrite page zero literals  if  you  leave  the  current
     program section and then return to it.



     4.6  NUMBER REPRESENTATION

     Numbers are handled in 12-bit, two's complement  arithmetic.   If  the
     current radix is octal, -1 and 7777 both define the same number.

     A sequence of digits delimited by a nondigit character forms a number.
     A  plus  or  minus sign may precede the number.  Numbers are initially
     treated as octal, but you can change this with  the  .RADIX  directive
     (see Section 5.2.1).

     You can also enter a single number in a radix other than  the  current
     radix by using the following temporary radix control operators.

	  o  Uparrow B (^B)
	  o  Uparrow D (^D)
	  o  Uparrow O (^O)
	  o  Period (.)

     These operators temporarily supersede or override the radix  currently
     in effect.



     4.6.1  Uparrow B (^B) -- Binary Representation

				     NOTE

		   Some terminals substitute the circumflex
		   (^) for the uparrow (^).					|


     Uparrow B (^B) defines a following sequence of digits as binary.   For
     example,

	  ^B101111001110


				     4-15

		       EXPRESSIONS AND THEIR COMPONENTS


     defines the number 5716  (octal).   No  space  is  allowed  after  the
     uparrow or after the B.



     4.6.2  Uparrow D (^D) -- Decimal Representation

     Uparrow D (^D) defines a following sequence of digits as decimal.  For
     example,

	  TAD (-^D40

     causes the assembler to generate a literal with the decimal  value  of
     -40 stored in it, and then to TAD the literal.  Note that the notation
     TAD (^D-40 is illegal since the uparrow must be  immediately  followed
     by a sequence of digits.



     4.6.3  Uparrow O (^O) -- Octal Representation

     Uparrow O (^O) defines a following sequence of digits as octal.   This
     would  be used if the current radix had been changed from its original
     setting of octal to some other radix.  The following code line,

	  ^O5555

     causes the octal number 5555 to be loaded into  memory  regardless  of
     the  current  radix  in  effect.   The  digits  8 and 9 are of course,
     illegal within the digit string.



     4.6.4  Period (.) -- Decimal Representation

     A period at the end of a sequence of digits is another way of defining
     the  digits as decimal.  There must be no space between the digits and
     the period.  For example,

	  913.

     defines the number  913  (decimal).   The  period  must  be  the  last
     character  of  the  number - it cannot be embedded in a number.  It is
     illegal to use  the  period  if  any  other  temporary  radix  control
     operator precedes the digit string.  Thus, ^0345.  is illegal.



     4.7  ASCII DATA REPRESENTATION

     There are a number of ways to enter ASCII codes  in  a  program.   The
     simplest  is  to enter the octal number value of the code itself.  For
     example, in 8-bit ASCII,  215  represents  a  carriage  return.   (See
     Appendix E for a complete chart of ASCII codes.)

				     4-16

		       EXPRESSIONS AND THEIR COMPONENTS


     Another way is to use the TEXT directive discussed in  Section  5.3.2.
     For example,

	  TEXT "ERR:  IMPROPER SYNTAX"

     causes the assembler to generate and to store the ASCII characters for
     this error message.

     The following ASCII conversion operators allow  you  three  additional
     ways of specifying ASCII characters:

	  o  Double quote (")
	  o  Single quote (')
	  o  Uparrow double quote (^")



     4.7.1  Double Quote (") -- ASCII Representation

     The double quote operator causes the character that follows it  to  be
     interpreted  as  an  ASCII  character  and  converts  it  to  a 12-bit
     expression value.  The  .ENABLE  directive's  text  options  determine
     whether  the  character  is  converted  to a 7-bit or 8-bit value (see
     Section 5.11.1).  Only one character may follow the double quote.  For
     example, a "A will generate a code of 301.

     You should use this form of ASCII  representation  only  for  printing
     characters.  For control characters, use the uparrow double quote (^")
     construction  described  in  Section  4.7.3.   You  can  enter   other
     nonprinting   characters  as  their  numeric  values.   The  following
     characters are not allowed and will result in an error message:

	  o  Carriage Return -- indicates end of line
	  o  Line Feed -- also indicates end of line
	  o  Form Feed
	  o  Control Z -- indicates end of file
	  o  Null



     4.7.2  Single Quote (') -- ASCII Pair

     The single quote  operator  causes  the  next  two  characters  to  be
     interpreted  as 6-bit ASCII codes, and combined into one 12-bit value.
     Thus:

	  'AZ

     causes the assembler to generate the 6-bit code for A (01) and combine
     it  with  the  6-bit  code for Z (32), giving 0132 (octal).  The 6-bit
     code for a character is the low order 6 bits of the character's  ASCII
     code.



				     4-17

		       EXPRESSIONS AND THEIR COMPONENTS


     4.7.3  Uparrow Double Quote (^") -- Control Character Representation

     The use of the double quote operator  to  convert  control  characters
     presents some problems.  First since these are nonprinting characters,
     it is impossible from looking at the program listing to determine what
     the  character  is.   Second, it is impossible to enter several of the
     control characters into the file, since they have special  meaning  to
     OS/8  programs.   For  example,  CTRL/C  means  return to the Keyboard
     Monitor, and its use in a file causes an exit  from  the  file  and  a
     return to the monitor.

     The uparrow double quote operator generates ASCII  codes  for  control
     characters.   The  .ENABLE  directive's text options determine whether
     the character is converted to a 7-bit  or  8-bit  value  (see  Section
     5.11.1).  For example,

	  ^"C

     This construction generates the ASCII code for a control C (203).



     4.8  MACREL ARITHMETIC OPERATORS

     An arithmetic operator is a symbol or  code  that  indicates  that  an
     action  or  operation  is  to  be  performed  on a term or terms in an
     arithmetic  expression.   There  are  seven  arithmetic  operators  in
     MACREL:

	  +		  Addition
	  -		  Subtraction or negation
	  ^		  Multiplication
	  %		  Division
	  !		  Boolean Inclusive OR
	  &		  Boolean AND
	  Space or Tab	  Inclusive OR (except in MRI instructions)

     The operators + and - are used as unary operators to act on  a  single
     term,  and  are  also used as binary operators to act on more than one
     term.  The remaining five characters in  the  above  list  are  binary
     operators.

     Binary operators perform operations involving two numbers or  symbols.
     They  combine an expression to the left of the operator with a term to
     the right of the operator.  All operations are  performed  in  12-bit,
     two's complement arithmetic, which is explained in detail in Chapter 1
     of Introduction To Programming.	___________________________



     4.8.1  Plus Sign (+) -- Addition

     The term A+B causes B to be added to A in two's complement arithmetic.
     No check is made for arithmetic overflow;  thus (in octal),

				     4-18

		       EXPRESSIONS AND THEIR COMPONENTS


	  7755+33

     will yield a result of 10.

     The plus sign may be used freely before a term.  Its use  as  a  unary
     operator  does not change the sign of the term.  For instance "+-1" is
     valid and evaluates as 7777 (octal).



     4.8.2  Minus Sign (-) -- Subtraction

     The term A-B causes B to be subtracted  from  A  in  two's  complement
     arithmetic.  Again, no check is made for arithmetic overflow.

     As a unary operator, the minus sign negates any term that follows  it.
     Both the plus and minus signs act as unary operators before any binary
     operations are done, and both may be used in any combination before  a
     term.   For example, --+-4 is valid and evaluates as -4 or 7774 octal.
     If an expression precedes a sequence of  plus  and  minus  signs,  the
     first  sign  is  a  binary  operator and the remaining signs are unary
     operators.  Thus A---B is the same as A-B.


				     NOTE

		   Extra spaces before unary  operator  are
		   interpreted  as  inclusive  OR's and are
		   not permitted.  Thus, A  -B  means  A!-B
		   and is not the same as A-B.



     4.8.3  Uparrow (^) -- Multiplication

     The expression A^B causes A to be multiplied  by  B  through  repeated
     addition.   All  12 bits are treated as magnitude and no check is made
     for overflow.  For example (in octal),

	  1234^10

     produces a result of 2340.  Also,

	  -1^2

     produces a result of 7776.



     4.8.4  Percent Sign (%) -- Division

     The term A%B causes A to be divided by B through repeated subtraction.
     The  number of full subtractions that were able to be performed is the
     quotient.  The remainder is not saved.  All 12 bits of each number are

				     4-19

		       EXPRESSIONS AND THEIR COMPONENTS


     considered  as  magnitude.   Division by zero causes an error message,
     the result arbitrarily to be considered zero.  For example:

	  723%10

     yields 72.  Also (in decimal),

	  .RADIX 10
	  -10%10

     gives 408 (603 octal) because -10 would be  treated  as  decimal  4086
     (7766 octal).



     4.8.5  Ampersand (&) -- Boolean AND

     The term A&B causes the assembler to perform a bit-by-bit Boolean  AND
     between A and B.  For example (in octal),

	  7436&1743

     produces a result of 1402.



     4.8.6  Exclamation Point (!) -- Inclusive OR (or Shift)

     The term A!B causes the assembler  to  perform  a  bit-by-bit  Boolean
     inclusive OR between A and B.  For example (in octal),

	  1234!4444

     produces 5674.

     If you use the SHIFT option of the .ENABLE directive  it  changes  the
     meaning  of  its  exclamation  point operator.  The expression A!B now
     means, shift A six bits to the left and inclusive OR the  result  with
     B.   The  left  six  bits  of  A  are  lost.   For example (in octal),

	  7711!2077

     produces a result of (1100 OR 2077), or 3177.

     This option is useful for manipulating 6-bit values.  For example,  If
     A=21 and B=47, then A!B=2147 (SHIFT enabled).



     4.8.7  Space ( ) and Tab -- Inclusive OR

     The space (or optionally, tab) provides another way of  indicating  an
     inclusive  OR between two symbols or numbers.  The primary use of this
     form of the inclusive OR is in specifying microprogrammed instructions

				     4-20

		       EXPRESSIONS AND THEIR COMPONENTS


     though  you  may,  in  fact,  use it for any valid OR expression.  The
     following is an example of its use for microprogrammed instructions:

	  CLA CLL IAC

     Here, the spaces cause  the  assembler  to  perform  an  inclusive  OR
     between  the permanent symbols CLA (7200), CLL (7100), and IAC (7001).
     The result is  7301  (all  numbers  in  octal).   The  assembler  thus
     produces  a  code  word  of  7301,  which  when  executed  clears  the
     accumulator, clears the link,  and  increments  the  accumulator.   In
     other  words, the instruction clears the link and sets the accumulator
     to 0001.

     It is your responsibility to ensure that the  instruction  codes  that
     you OR together are compatible.  For example, MACREL will OR the codes
     SNA(7450),CLA(7200) and CLL(7100) to produce 7750, which  is  SPA  SNA
     CLA  and  not the intended instruction.  You must also be careful when
     embedding spaces near other operators.  For example in  the  code  TAD
     (3+6 a space inadvertently placed before the plus sign yields a result
     of octal 7 instead of the intended octal 11.


				     NOTE

		   Since space and tab are  operators,  you
		   cannot  use  them  as  format  effectors
		   within a term to improve readability.


     The current programming convention is that  you  use  the  exclamation
     point  construction of the inclusive OR for actual logical operations,
     and the space construction for loading the  various  components  of  a
     word of code.

     If the SHIFT option of the .ENABLE directive  is  not  in  force  (the
     default  condition)  space  and  !  are  normally  equivalent with one
     exception:  You must use the exclamation point  (!)  form  of  the  OR
     operator  if  a  left  angle bracket (<) immediately follows it.  This
     prevents an ambiguous  condition  with  certain  conditional  assembly
     directives.



     4.9  SPECIAL OPERATORS

     In addition to unary and binary  operators,  there  are  a  number  of
     special  operators.   Special  operators  are  permanent  symbols that
     return  values.   They  may  appear   anywhere   in   an   expression.
     Other  special  operators  that  pertain  to  macros  are discussed in
     Chapter 6.





				     4-21

		       EXPRESSIONS AND THEIR COMPONENTS


     4.9.1  Memory Reference Instructions

     The assembler processes the  memory  reference  instruction  mnemonics
     AND,  TAD,  ISZ,  DCA, JMP, and JMS differently from the other machine
     instructions.  The assembler treats an expression that  follows  other
     machine-instructions mnemonics as a value to be ORed with the value of
     the particular instruction.  It treats the expression that  follows  a
     memory reference instruction mnemonic as an address.  It then performs
     the necessary computations  for  the  address.   Specifically  if  the
     assembler  recognizes a symbol as being a memory reference instruction
     that is followed by an expression (N),  the  assembler  evaluates  the
     expression N and does the following (all numbers in octal):

	  1.  If N is absolute and addresses page 0, the assembler OR's the
	      value  of the memory reference instruction (MRI) with N.  For
	      example, TAD 10 will produce  1010.   (TAD  has  a  value  of
	      1000.)  The result is absolute.  If N is relative to a .ZSECT
	      in the same source module (or includes a Z component) then  N
	      is  added  to the MRI.  The relocatable part of the result is
	      then the same as the relocatable part of N.

	  2.  If N addresses the current page  (other  than  page  0),  the
	      assembler  sets  the  current  page bit and OR's the MRI with
	      bits 5 through 11 of the absolute part of N.  An  instruction
	      DCA  P,  where  P  has  a  value of 4013 on the current page,
	      generates the code 3213.  The 3 indicates a DCA  instruction,
	      the  2  shows that the current page bit is set, and the 13 is
	      the address on the current  page.   If  the  current  program
	      section is an .FSECT, .XSECT, or .ZSECT, the result is .FSECT
	      relocatable (see 7.1.7).  Otherwise the result is absolute.

	  3.  If N addresses some other page than the current page  in  the
	      same  program  section, or page zero, the assembler generates
	      an on-page reference to the address of N.   Specifically,  it
	      treats  MRI N as if it were MRI I (N) by setting the indirect
	      bit and creating an on-page reference much  like  a  literal.
	      If  the  current  program  section  is  an .FSECT, .XSECT, or
	      .ZSECT,  the  result  is  .FSECT  relocatable  (see   7.1.7).
	      Otherwise,  the result is absolute.  If N already contains an
	      I component, then an illegal reference is generated.


				     NOTE

		   In  the  last  example,  the   assembler
		   indicates that it has created an on-page
		   reference  (link),   by   including   an
		   apostrophe  (') to the right of the code
		   column in the listing.  You  might  want
		   to consider this linkage as an error and
		   use MRI I (N), the literal construction;
		   this  implies  that  N  is off-page, and
		   does  not  leave  it  as  an   assembler
		   decision.    If   error   print-out   is

				     4-22

		       EXPRESSIONS AND THEIR COMPONENTS


		   specified  as  a  control  option   (see
		   Chapter  8) the assembler will treat the
		   linkage as  an  error,  print  an  error
		   message, and continue the assembly.


     In evaluating a memory reference instruction, the assembler looks  for
     an expression following the instruction to represent the address.  For
     example,

	  TAD DATA+1^2 SYM

     will cause the assembler to add 1 to  DATA,  multiply  by  2,  OR  the
     result  with  SYM, and take this result as the address of the TAD.  To
     modify the result of the MR instruction in  some  way,  rearrange  the
     order of the expression, or use angle brackets.  For example,

	  <TAD B>+N

     will cause the assembler to first evaluate TAD  B  and  then  add  the
     value of N to it.  For example,

	  TAD DCA A AND B

     means:

	  TAD <DCA A!<AND B>>

     In addition to the six memory reference instructions  AND,  TAD,  ISZ,
     DCA,   JMP   and  JMS,  you  can  define  your  own  memory  reference
     instructions by using the FIXMRI directive (see Section 5.9).



     4.9.2  I -- Indirect Addressing

     The special operator I indicates indirect addressing.   It  is  always
     specified with a memory reference instruction in the form:

	  MRI I n

     where:

	  n		 is some expression

	  I		 indicates  that  n  is  not  the  address  of  the
			 operand,  but  is  the location whose contents are
			 the address of the operand.

     When n is indirectly addressed it must be on the current page or page
     0.   If  it  is  not,  the  assembler  prints  an error message.  The
     assembler sets the indirect address bit when  creating  an  off  page
     reference,  but in this case the bit has already been set by the I in
     the instruction.

				     4-23

		       EXPRESSIONS AND THEIR COMPONENTS


     Although  placing  the  I  immediately  after  the  memory   reference
     instruction  is  the  preferred  format,  the  I  may  actually appear
     anywhere in an expression following the memory reference  instruction.
     For example,

	  DCA B+2 I

     will have the same effect as the following:

	  DCA I B+2

     I is a permanent symbol and cannot be used as a program symbol.



     4.9.3  Z -- Page Zero Addressing

     In a memory reference instruction of the following format:

	  MRI Z n

     where:

	  n		 is an expression

	  Z		 indicates page zero addressing.

     In effect, the Z is ignored because the  value  of  n  determines  the
     actual  address.   However,  if n is an absolute address other than on
     page zero the assembler will print  an  error  message  Z  INCORRECTLY
     SPECIFIED.   Thus,  use  of  the  Z  makes it obvious that a page zero
     reference is intended, and should an error be made  (for  example,  if
     you  change the value of a variable and forgot that it was a page zero
     reference), MACREL generates an error message.  If n is external, then
     this instruction acts as if n had been declared .ZTERNAL.



     4.9.4  CIF and CDF Instructions

     The assembler treats the CIF and CDF instruction mnemonics as  special
     operators  when  not used in absolute program sections.  Both have the
     same format and MACREL processes them identically.  The format is,

	  CIF n or CDF n

     where:

	  n    is a term.

     The relocation type of n that results, depends on the relocation  type
     of the arguments in the term.



				     4-24

		       EXPRESSIONS AND THEIR COMPONENTS


     Table 4-2 lists the relocation type and gives the assembly process for
     each type.


				   Table 4-2
		       Processing of CDF/CIF Expressions

     ----------------------------------------------------------------------
     |	       CDF/CIF		|	    Operation			  |
     |     Relocation Type	|	(values are octal)		  |
     |--------------------------|-----------------------------------------|
     |	     Absolute		|  OR the value of the  symbol  with  CIF |
     |				|  (6202).   For  example,  "CIF 30" will |
     |				|  produce 6232.			  |
     |				|					  |
     |				|  OR the value of the  symbol  with  CDF |
     |				|  (6201).   For  example,  "CDF 30" will |
     |				|  produce 6231.			  |
     |				|					  |
     |       Relocatable	|  Instruct LINK to find the field of the |
     |				|  symbol  N  and map it into bits 5-9 of |
     |				|  CIF (6202).  See Figure 3-5.		  |
     |				|					  |
     |				|  Instruct LINK to find the field of the |
     |				|  symbol  N  and map it into bits 5-9 of |
     |				|  CDF (6201).  See Figure 3-5.		  |
     ----------------------------------------------------------------------

     CDF and CIF can be combined in a line of the form:

	  CDF CIF N

     The order of CDF and CIF is not significant.  The result is  the  same
     as  in Table 4-2 except that the value 6203 (rather than 6201 or 6202)
     is used.  If N is not absolute, then the result is complex relocatable
     (actually  CDF-relocatable).   This  is  because  the result is of the
     form:  constant + field of section.



     4.9.5  EDF -- Evaluate Data Field

     The EDF (evaluate data field) special operator allows  you  to  obtain
     the field of any symbol.  The format is:

	  EDF sym

     where:  sym    is a relocatable symbol.

     This instruction causes LINK to determine the field of the symbol  and
     to  map  it  into  bits  5-9 of the current location value (see Figure
     3-4).  For example, if LPOINT is a symbol in a section that LINK loads
     into field 7,


				     4-25

		       EXPRESSIONS AND THEIR COMPONENTS


	  EDF LPOINT

     will store 0070 (octal) in memory at the current location.

     You can use EDF in any expression.  If  the  relocation  type  of  the
     argument is either absolute or CDF/CIF relocatable, then EDF N has the
     same value as N.  If relocation type of the  argument  is  complex  or
     .FSECT relocatable, the result is complex relocatable.

     You can evaluate the field that the current (relocatable) section  has
     been loaded into by using the following construction:

	  EDF  .

     You can use this construction because the current location counter  in
     a  relocatable  section  is  always  relative  to  the current program
     section.

     If the current section is  not  known  to  be  relocatable,  EDF  .FLD
     evaluates to the current field in bits 5-9.  The .FLD special operator
     is discussed in Section 4.9.6.



     4.9.6  .FLD

     The .FLD special operator returns a 12-bit expression value  in  which
     bits  5-9  specify  the number of the current field.  Figure 3-5 shows
     the mapping of these bits.  If .FLD  occurs  in  an  absolute  program
     section,  the  result  is  absolute.  Otherwise, the result is CDF/CIF
     relocatable with a zero absolute part (see Section 4.9.4).



     4.9.7  XEDF

     XEDF is a special operator that you can  use  when  forming  an  RTS/8
     Device  Handler  Function  Control Word (see RTS/8 User's Manual).  It						  ___________________     
     returns a 12-bit expression value that is  the number  of  the  memory
     field where a symbol resides.
     The form is:

	  XEDF sym

     where:  sym    is a relocatable symbol

     The field value is mapped into bits 6-10 as shown in Figure 4-1.   The
     result of this expression is complex relocatable.







				     4-26

		       EXPRESSIONS AND THEIR COMPONENTS


			Field Number (0-37) = abcde

			bit 0			bit 11
			   | 000 | 000 | cde | ba0 |
			   -------------------------

	     Figure 4-1 Extended Memory Field Bit Layout for XEDF



     4.9.8  .LEVEL

     The .LEVEL special operator returns a 12-bit expression value at  LINK
     time  that  contains  the  overlay  and  level  numbers of the current
     program section.  You can use this operator in an expression or as  an
     argument  to  a  global symbol assignment statement.  Figure 4-2 shows
     the bit assignments.  The value of this special  operator  is  complex
     relocatable at assembly time.


			 |0------>| LEVEL | OVERLAY |
			 |--------|-------|---------|
			0	4 5     7 8	     11

	    Figure 4-2 BIT Assignments for .LEVEL Special Operator

     Example:

	      TAD LVL
		.
		.
		.

	  LVL,  .LEVEL

     At program execution time the code in this example causes the  overlay
     and level values of the current program section to be added to the AC.



     4.10  EXPRESSION EVALUATION AND SYNTAX

     Expressions consist of valid  combinations  of  terms  and  operators.
     Terms  may  include numbers, ASCII codes, symbols, machine instruction
     mnemonics, the current location counter, literals,  other  expressions
     enclosed  in  angle  brackets  (<>),  and  special  operators  or some
     combination of the above.

     Note that expressions consist of terms separated by  binary  operators
     (the final separating operator is the space).  Any unary operators are
     assumed to belong to the term to which they  apply,  and  any  special
     operators  that  take  an  entire expression (such as memory reference
     instructions)  are  shown  as   terms.    The   following   expression
     illustrates this:

				     4-27

		       EXPRESSIONS AND THEIR COMPONENTS


	  DATA-.+(ALPHA+1)%10.!<EDF X1> TAD I DATA+6

     This expression evaluates as:

	  <DATA>-<.>+<(ALPHA+1)>%<10.>!<EDF X1>!<TAD I DATA+6>

     That is, the terms in angle brackets are evaluated first, and then the
     binary  operations  performed  from  left  to  right.   Note  that the
     parentheses denote the address of a literal.



     4.10.1  Operator Precedence and Order of Evaluation

     MACREL uses the following sequence to evaluate expressions:

	  1.  Evaluate any  special  radix  control  and  ASCII  conversion
	      operators.

	  2.  Evaluate any unary operators.

	  3.  Evaluate terms that require further processing.

	  4.  Perform binary operations between terms, evaluating them from
	      left to right.

     For example, the following expression,

	  <ISZ> M-<ALPHA+4>+TAD I M N

     contains four terms:

	  <ISZ>
	  <M>
	  <ALPHA+4>
	  <TAD I M N>

     MACREL evaluates each term separately  before  performing  the  binary
     operations.

     If, however, the initial set of angle brackets is removed, as follows:

	  ISZ  M-<ALPHA+4>+<TAD I M N>

     then the resulting expression contains  only  one  term,  because  the
     memory  reference  instruction ISZ takes as its argument an expression
     that goes to the end of the line.  In other words, the entire line  is
     an argument to ISZ.

     In the expression,

	  A-+B+--C+^B1101+89.+"A



				     4-28

		       EXPRESSIONS AND THEIR COMPONENTS


     the terms are as follows:

	  <A>
	  <+B>
	  <--C>
	  <^B1101>
	  <89.>
	  <"A>

     Note the special operators in this example that indicate binary  (^B),
     decimal  (.),  and  ASCII  (")  are  not  unary  operators, but are an
     integral part of the term they modify.  The + before the <B>  and  the
     -- before the <C>, however, are unary operators.

     MACREL uses the three rules stated at the beginning of this section to
     evaluate each term in sequence, until it reduces each term to a 12-bit
     number.

     There is no precedence among the binary operators.  You can use angle
     brackets freely to indicate order of operations.  For example,

	  A ^<B+C>

     will cause MACREL to compute the sum of B+C first, then multiply A  by
     this result.  In other words, the angle brackets alter the normal left
     to right evaluation of A^B+C.



     4.11  USES OF EXPRESSIONS

     An expression may consist of only a single number or symbol, or it may
     be a complex construction.  After evaluation, if the expression is the
     only element on the line (except for a label or comments), the  12-bit
     value  is  loaded  into the current location, and the current location
     counter is incremented by one.

     Notice that the assembler does  not  distinguish  machine  instruction
     mnemonics  (except  for  memory  reference instructions, CIF, and CDF)
     from other symbols.  A CLA, for example, is a  permanent  symbol  that
     has  a  value  of  7200.   The  assembler  loads  the  next expression
     regardless of whether it is an instruction or a data item.

     In addition to this loading  function,  expressions  may  be  used  in
     direct  assignment  statements  and  in  certain  directives.   In the
     following direct assignment statement,

	  SYM=EXPR

     MACREL evaluates the expression EXPR and assigns  this  value  to  the
     symbol SYM.  This operation is performed at assembly time;  no code is
     generated.



				     4-29

		       EXPRESSIONS AND THEIR COMPONENTS


     Expressions used in directives are  discussed  under  the  appropriate
     directives.



     4.12  EXPRESSIONS AND RELOCATION

     In an absolute program all expressions are absolute.   That  is,  they
     evaluate  to  a 12-bit number.  However, in a program with relocatable
     sections, expressions may be simply relocatable,  complex  relocatable
     CDF/CIF relocatable, or .FSECT relocatable (see Section 1.5.5).

     A number of MACREL directives take an expression value as an argument.
     For some of these directives, there are restrictions on the relocation
     types allowed for these expressions.  Tables 4-3 and 4-4 show you  the
     relocation  types  that  result  when   using the arithmetic operators
     described in Section 4.8.


				   Table 4-3
      Relocation Types Resulting from Addition and Subtraction Operations

       --------------------------------------------------------------------
      /		   |				Right Operand		  |
     /		   |------------------------------------------------------|
     |	Left	   | Absolute | Simple   | Complex  | CDF/CIF  | .FSECT	  |
     |	Operand	   |	      |Relocation|Relocation|Relocation|Relocation|
     |-------------|----------|----------|----------|----------|----------|
     | Absolute    | Absolute | Simple   | Complex  | Complex  | .FSECT	  |
     |		   |	      |		 |	    |	       |	  |
     | Simple	   | Simple   | Complex  | Complex  | Complex  | Complex  |
     | Relocation  |	      |(see note)|	    |	       |	  |
     |		   |	      |		 |	    |	       |	  |
     | Complex	   | Complex  | Complex  | Complex  | Complex  | Complex  |
     | Relocation  |	      |		 |	    |	       |	  |
     |		   |	      |		 |	    |	       |	  |
     | CDF/CIF	   | Complex  | Complex  | Complex  | Complex  | Complex  |
     | Relocation  |	      |		 |	    |	       |	  |
     |		   |	      |		 |	    |	       |	  |
     | .FSECT	   | .FSECT   |	Complex  | Complex  | Complex  | Complex  |
     | Relocation  |	      |		 |	    |	       |	  |
     ----------------------------------------------------------------------

     Note:  If the relocatable part of each operand value is the same,  the
     result is absolute.










				     4-30

		       EXPRESSIONS AND THEIR COMPONENTS


				   Table 4-4
	  Relocation Types Resulting from Other Arithmetic Operations

	      ------------------------------------------------------
	     /			|	 Right Operand		   |
	    /			|----------------------------------|
	   /			|	       |   Simple, Complex |
	   | Left		|   Absolute   |   CDF/CIF, .FSECT |
	   | Operand		|	       |   Relocation	   |
	   |--------------------|--------------|-------------------|
	   | Absolute		|   Absolute   |   Complex	   |
	   |--------------------|--------------|-------------------|
	   | Simple		|	       |		   |
	   | Complex,		|	       |		   |
	   | CDF/CIF,		|   Complex    |   Complex	   |
	   | .FSECT		|	       |		   |
	   | Relocation		|	       |		   |
	   ---------------------------------------------------------





































				     4-31







				   CHAPTER 5

			       MACREL DIRECTIVES


     Directives are direct instructions to the MACREL assembler to  perform
     certain   functions.   Because  directives  are  instructions  to  the
     assembler itself, in general  they  do  not  create  code.   In  PAL8,
     directives are called pseudo-operators.

     Do not confuse operators,  expressions  and  directives.   Expressions
     consist of terms and operators.  Any number of terms and operators may
     be present in an expression.  The special operator EDF,  for  example,
     can appear anywhere in the expression, as in the following:

	  TAD EDF DATA+OFS+5.

     Directives, on the other hand, may not  be  embedded  in  expressions;
     they  must  be  the  only  entry  on the line, with the exception of a
     label, a comment, or with some  directives,  a  following  expression.
     Although  labels  are permitted with directives, in most cases they do
     not make sense, as for example:

	  "STRT, .RADIX 10".

     Note that  a  period  (.)  generally  precedes  the  names  of  MACREL
     directives but not the older PAL8 pseudo-operators.  The two forms are
     not interchangeable.

     The directives are grouped according to their function in the assembly
     or  linking process.  Each group, and the directives within the group,
     is discussed in a separate section in this chapter.



     5.1  ASSEMBLY LISTING AND BINARY OUTPUT CONTROL DIRECTIVES

     The following seven directives control the  assembly  listing  or  the
     binary output:

	  o  .NOLIST
	  o  .LIST
	  o  .TITLE
	  o  .SBTTL
	  o  XLIST
	  o  EJECT
	  o  NOPUNCH and ENPUNCH





				      5-1

			       MACREL DIRECTIVES


     5.1.1  Assembly Listing Control Directives



     5.1.1.1  .LIST  and  .NOLIST - These  directives  enable  (.LIST)  and
     disable (.NOLIST) the printing of portions of an assembly listing.

     The form of the directive is:

	    .LIST
		      [option,...]
	    .NOLIST

     where:

	  option    is one of the options shown in Table 5-1.   If  you  do
		    not  specify  any  options,  the  directives  enable or
		    disable listing output.
	

				   Table 5-1
			   .LIST and .NOLIST Options

	   ---------------------------------------------------------
	   | Option  |		      Description		   |
	   |---------|---------------------------------------------|
	   | BE	     | Binary expansion lines			   |
	   | CND     | Unsatisfied conditionals			   |
	   | LN	     | Count unlisted line numbers		   |
	   | MC	     | Macro calls				   |
	   | ME	     | Macro expansions (all lines)		   |
	   | MEB     | Macro expansions (lines that generate code) |
	   | ST      | Symbol table				   |
	   | TOC     | Table of contents			   |
	   ---------------------------------------------------------

     You can dynamically alter  listing  conditions  at  assembly  time  by
     changing  the  value  of  the  .LISTWD  special  variable (see Section
     5.1.1.4).

     .LIST followed  by  any sequence  of  these  options  turns  them  on.
     .NOLIST  followed  by  any sequence of the options turns them off.  At
     the beginning of each assembly  pass  the  following  default  listing
     options are in effect:

	  BE - on
	  CND - on
	  MC - on
	  ME - off
	  MEB - off
	  ST - on
	  TOC - on



				      5-2

			       MACREL DIRECTIVES


     For example:

	  .NOLIST  CND,  ME

     at the beginning of a program prevents  any  unsatisfied  conditionals
     and macro expansions from being listed.

     If you use a .LIST or .NOLIST directive in the middle of a program, it
     will  enable  or  disable the options specified from that point of the
     code on until MACREL encounters the next .LIST or  .NOLIST  directive.
     For  example,  if  you  specify  .NOLIST ME for a certain section of a
     program, that section will have no macro expansions listed.

     You can use the directives without arguments to eliminate  repetitious
     sections  of  code  from  a  listing.  For example, if you have a long
     series of text items that you do not  wish  to  print,  code  them  as
     follows:

		   .
		   .
		   .
		  JMP NEND
		  .NOLIST
	  TABLE,  TEXT "CLA"
		  TEXT "NOP"
		   .
		   .
		   .
		  TEXT "BSW"
		  .LIST
	  N1,     CLA
		   .
		   .
		   .

     None of the TEXT items will print on the listing.

     Note that if you turn on the listing  of  macro  expansions  (ME)  all
     lines  inside  macro expansions will be listed regardless of the state
     of the MEB list option.

     If you turn on the listing of macro  expansion  binaries  (MEB)  only,
     then  only  lines inside macro expansions that generate binary will be
     listed.

     In the case of lines  containing  multiple  statements  (separated  by
     semicolons),  the  line  will  be  listed  if  and  only  if the first
     statement on the line satisfies all listing requirements.



     5.1.1.2  .TITLE - The .TITLE directive defines a title for a  program.
     The title prints as the top line of every page of the listing after it
     is used at the beginning of a program section.   If  it  is  also  the

				      5-3

			       MACREL DIRECTIVES


     first line of a physical page, it appears as the heading of that page.
     No page ejection (execution of a form feed) takes place.

     The form of the directive is:

	  .TITLE text

     where:

	  text	    is a sequence of up to 40 ASCII characters including  a
		    single   space   that   must   follow   the  directive.
		    Additional characters  are  ignored.   Tabs  should  be
		    voided in the text.

     An example of the directive is:

	  .TITLE FLOATING-POINT ARITHMETIC PACKAGE



     5.1.1.3  .SBTTL - The .SBTTL directive defines a subtitle to appear as
     the  second line of the header for each page.  The subtitle appears on
     the first page following each use of the directive.

     The form of the directive is:

	  .SBTTL text

     where:

	  text	    is a sequence of up to 40  ASCII  characters  including
		    the  single  space  that  must  follow  the  directive.
		    Additional characters are ignored.   You  should  avoid
		    using tabs in the text (but they may precede it).

     An example of the directive is:

	  .SBTTL MULTIPLY

     The following heading illustrates the use of both  .TITLE  and  .SBTTL
     directives:

	  FLOATING-POINT ARITHMETIC PACKAGE
	  MULTIPLY



     5.1.1.4  .LISTWD Special Variable - .LISTWD is an assembler-maintained
     variable  that  you can examine and modify to alter the options of the
     .LIST and .NOLIST directives at assembly time.  The variable  contains
     a  12-bit  number  the  bits of which control these options (see Table
     5-2).  The following is an example of how you can use .LISTWD:



				      5-4

			       MACREL DIRECTIVES


	    .
	    .
	    .
	 TEMP = .LISTWD		    /SAVE CURRENT LISTING OPTIONS
	 .LISTWD = NEW		    /SET NEW LISTING OPTIONS
	    .
	    .
	    .
	 .LISTWD = TEMP		    /RESTORE OLD LISTING OPTIONS


				   Table 5-2
			    .LISTWD Bit Assignments

	----------------------------------------------------------------
	|   Bit    |		Meaning when set to 1		       |
	|----------|---------------------------------------------------|
	|    0	   | Disable listing output			       |
	|    1	   | Do not list unsatisfied conditional code	       |
	|    2	   | Do not list binary extensions		       |
	|    3	   | Do not list macro expansions		       |
	|    4	   | Do not list macro expansions that generate binary |
	|    5	   | Do not list macro calls			       |
	|    6	   | Do not list macro definitions		       |
	----------------------------------------------------------------


     5.1.2  Other PAL8 Directives

     Four PAL8 directives are maintained in MACREL, to keep the  assemblers
     compatible.  These are XLIST, EJECT, ENPUNCH, and NOPUNCH.



     5.1.2.1  XLIST - The directive XLIST turns  off  the  listing  on  its
     first  use, and turns it back on on its second use.  XLIST may also be
     used with an expression in the form:

	  XLIST exp

     where:

	  exp	    is an expression.  The expression must be absolute.  If
		    the  expression  evaluates  to  0,  the listing will be
		    turned off;  otherwise it will be turned on.

     The XLIST directive itself does not appear in the listing.



     5.1.2.2  EJECT - The EJECT directive causes the listing to jump to the
     next page.  Additionally, if a string of characters follows the EJECT,
     the first 40 (decimal) characters will be placed in the top line  (the
     .TITLE line) of the heading.

				      5-5

			       MACREL DIRECTIVES


     5.1.2.3  NOPUNCH and  ENPUNCH  -  The  directive  NOPUNCH  causes  the
     assembler to cease binary output, but continue assembling code.  It is
     ignored except during the second  assembly  pass  through  the  source
     module.

     ENPUNCH causes the assembler to resume binary  output  after  NOPUNCH,
     and  is  ignored  except during pass 2.  Use these two directives when
     several programs share the same data on page 0.  This  avoids  loading
     page  0  more  than  once.   The same result is achieved with the PNCH
     option of the .ENABL and .DISABL directives.



     5.2  RADIX CONTROL DIRECTIVES

     MACREL maintains a  current  radix  according  to  which  numbers  are
     interpreted.   Unless  the  radix  is changed, MACREL assumes it to be
     octal.  To change the radix use the .RADIX directive.



     5.2.1  .RADIX

     The .RADIX directive alters the current radix.

     The form of the directive is:

	  .RADIX exp

     where:

	  exp	    is any valid expression that specifies the radix.   The
		    expression  exp must be absolute, and must have a value
		    between 2 and 10, inclusive.  Any  constants  appearing
		    in exp are evaluated in the decimal radix.

     For example:

	  .RADIX 10

     sets the current radix to 10 regardless of the previous radix.

     In addition to the current radix, you may temporarily set a radix  for
     an  individual  number  by using the temporary radix control operators
     described in Section 4.6.

     If you wish to determine the current radix simply write the characters
     10  in  your  program.   For  example, to equate the symbol R with the
     current radix, write:

	  R=10

     Thus, if the current radix is decimal, the number 10 would be input as
     a decimal number and R would be assigned a value of decimal 10.

				      5-6

			       MACREL DIRECTIVES


     Remember that numbers are always stored  internally  in  binary  form.
     The  effect of a .RADIX directive is to interpret a sequence of digits
     in the source module.



     5.2.2  Other PAL8 Directives

     PAL8 provides two directives:  DECIMAL and OCTAL, which in MACREL  are
     replaced   by   the  .RADIX  directive.   Both  directives  are  still
     acceptable to MACREL, but for simplicity, it is recommended  that  you
     replace  them  with  the  .RADIX  directive.   This is accomplished as
     follows:

	  PAL8 Directive      MACREL Equivalent	  ______________      _________________

	     DECIMAL		   .RADIX 10
	     OCTAL		   .RADIX 8

     Unlike .RADIX, OCTAL and DECIMAL do not take an expression.



     5.3  DATA STORAGE DIRECTIVES

     MACREL provides four directives to control data storage.  These are:

	  o  .REPT
	  o  .ENDR
	  o  ZBLOCK
	  o  TEXT

     .REPT and .ENDR are macro directives and are discussed in Section 6.6.
     ZBLOCK and TEXT are discussed in this section.  Because options of the
     .ENABL and DISABL directives affect TEXT  additional  details  on  the
     TEXT directive are included in Section 5.11.1 and 5.11.2.



     5.3.1  ZBLOCK

     ZBLOCK stores a specified value in a selected block of memory.

     The form of the directive is:

	  ZBLOCK n,m

     where:

	  n	    is an absolute  expression  value  that  specifies  the
		    number  of  words  in  the  block.   The  value of this
		    expression must be known on pass 1.



				      5-7

			       MACREL DIRECTIVES


	  m	    is an expression value  that  specifies  the  value  to
		    store  in  each word.  The expression cannot be complex
		    relocatable.

     Examples:

	  *300
	  ZBLOCK 7, HLT

     In this example, seven words,  each  containing  HLT  (7402)  will  be
     stored in locations 300 through 306, inclusive.

     In this example, if DATA is defined as being .EXTERNAL to the  present
     module (.EXTERNAL DATA), the directive:

	  ZBLOCK 5, DATA

     causes MACREL to generate five words of code, each of which contains a
     reference  to  DATA  in  the  other module.  LINK fills in the correct
     addresses at link time.

				    CAUTION

		   Avoid having assembly passes one and two
		   generate   different  lengths  of  code.
		   This results in an assembly error.   For
		   example, the following code:

			ZBLOCK N
			N=N+10

		   causes  such   an   error,   because   N
		   initially  has  a  value  of  0 which is
		   changed  by  the   "N=N+10"   statement.
		   However,

			N=1
			ZBLOCK  N
			N=N+10

		   assembles correctly because N gets reset
		   to 1 on each pass.



     5.3.2  TEXT

     There are two forms of the  TEXT  directive;   a  simple  form  and  a
     complex form.



     5.3.2.1  Simple Form of the TEXT Directive - The simple  form  of  the
     TEXT directive is:

				      5-8

			       MACREL DIRECTIVES


	  TEXT "text string"

     where:

	  text string    is a sequence of graphic characters including  the
			 space  character.   You  must  enclose  the string
			 within a pair of graphic characters such as double
			 quotes ("").

     The  directive  is  followed  first  by  a  printing  character  as  a
     delimiter,  then the text string, and finally the same delimiter.  The
     double quote (") is recommended as a delimiter.  Left or  right  angle
     brackets  (<>)  and  nonprinting  characters  may  not  be used as the
     delimiter.  If you have to use double quote (") as part  of  the  text
     string,  use  the  construction  "".  Thus, two double quotes in a row
     signify one double quote in the text string.  No other  delimiter  has
     this characteristic.

     When you use the directive in this form, the  assembler  converts  the
     characters to their 6-bit ASCII codes and packs them two characters to
     a word (i.e., six bits per character) and adds at least one  character
     code  of zero at the end.  For example, if the text string contains an
     odd number of characters, the assembler adds a character code of  zero
     to the binary code produced, and if the text string has an even number
     of characters, a full word of zeros is stored.  Thus,

	  *300
	  TEXT "ERR"

     causes the following binary code to be generated:

	  00300	  0522	  (E R)
	  00301   2200	  (R zero-fill)

     Similarly, the TEXT message:

	  *300
	  TEXT "USER""S NO."

     contains an even number  of  characters  (since  the  two  consecutive
     double  quotes signify one double quote (") character) that results in
     the following code:

	  00300	  2523	  (U S)
	  00301	  0522	  (E R)
	  00302	  4223	  (" S)
	  00303	  4016	  (Space N)
	  00304	  1756	  (O .)
	  00305   0000    (Zero-fill word)

     Certain options of the .ENABLE directive (see  Section  5.1.1)  affect
     the  way that MACREL processes text strings.  The ASCII packing option
     causes  TEXT  to  generate  one  8-bit  ASCII  character   per   word.
     Additionally, if the 7BIT option is specified in addition to the ASCII

				      5-9

			       MACREL DIRECTIVES


     option, the TEXT directive generates one 7-bit ASCII  code  per  word.
     The  OS/8  packing  option causes TEXT to generate OS/8 packing (three
     characters in two words).   Also,  the  FILL  option  of  the  .DISABL
     directive  inhibits TEXT from producing an extra all-zero word, if the
     number of characters is even.

     You should include only printing characters  in  text  strings.   This
     avoids  editing  problems  and confusion when the listing is read.  At
     any rate, the following characters are illegal within text strings and
     cause error messages:

	  o  Carriage Return
	  o  Line Feed
	  o  Form Feed
	  o  Control Z
	  o  Null

     But while these characters are not allowed in text  strings,  you  can
     include  their  functions  in  text  strings by using the format shown
     below.



     5.3.2.2  Complex Form of the TEXT - The TEXT directive also allows you
     to  enter  special codes such as line feed and carriage return as part
     of the text string by using the ASCII  value  rather  than  the  ASCII
     character.  For example, the following statements,

	  .ENABLE ASCII
	  TEXT "ID" <215> <212>

     cause the assembler to use ASCII packing (one 8-bit  code  per  word),
     and to generate five words, as follows:

	  0311    I
	  0304    D
	  0215    Carriage return
	  0212    Line feed
	  0000    Zero-fill word

     The general form of the TEXT directive is:

	  TEXT item ...

     where:

	  item		 is either a text  string  with  delimiters  or  an
			 expression   contained   within   angle  brackets.
			 Spaces are optional between items.  Any left angle
			 bracket   must   ultimately  be  followed  by  its
			 corresponding right angle bracket.

     Expressions within angle brackets must be absolute.  Processing is  as
     follows:

				     5-10

			       MACREL DIRECTIVES


	  o  The expression is evaluated.

	  o  MACREL takes the low order seven bits and constructs the
	     proper code.

	  o  MACREL checks for .ENABLE directive options.

	  o  For the 8BIT option, MACREL sets the high order bit to 1.


				     NOTE

		   If the  SIXBIT  option  of  the  .ENABLE
		   directive   (default)   is   in  effect.
		   MACREL cannot construct the proper  code
		   for  nonprinting  characters,  which are
		   undefined in 6-bit ASCII.



     5.3.2.3  TEXT Options - In evaluating a sequence of text  strings  the
     assembler  treats  the  sequence  as  if  it  were one continuous text
     string.   For  example,  under  the  SIXBIT  option  of  the   .ENABLE
     directive, the statement,

	  TEXT "A" "B"

     causes the A and B to be packed in  the  same  word.   When  the  FILL
     option  is  in effect, the assembler evaluates the entire sequence and
     then, at the end, adds a zero fill if one is not  present.   That  is,
     the zero fill is not added to each item in the sequence.

     Figure 5-1 shows examples of  how  MACREL  processes  text  under  the
     various  options  of  the TEXT directive.  The example uses the source
     line:

	  TEXT "VER" <C> <212> "NO.  " <260+VDIGIT> "."

     with the five  option  combinations  shown.   You  might  employ  this
     statement  to  store  data  that  your  program would use to print the
     following message:

	  VER
	  NO.  3.

     In the example, VDIGIT contains the one-digit version number.  C has a
     value (7015) that will generate the code for a carriage return.  (This
     is to demonstrate the expression  evaluation  described  above.)  Note
     that  the  first  three .ENABLE lines establish the default conditions
     (i.e., initial) MACREL conditions.  The expression <212> prints a line
     feed.  Notice also that the first example does not produce the desired
     result because the carriage return and line feed have been changed  to
     the 6-bit codes for M and J respectively.


				     5-11

			       MACREL DIRECTIVES


				     NOTE

		   You can use the forward slash  character
		   (/)  as a string delimiter for the first
		   item of the text directive.  This is the
		   only  place  it  is  not  treated as the
		   beginning of a comment.


     VDIGIT=3
     C=7015
     .ENABLE 8BIT
     .ENABLE SIXBIT
     .ENABLE: FILL
     TEXT "VER" <C> <212> "NO. " <260+VDIGIT> "."
     .ENABLE ASCII
     TEXT "VER" <C> <212> "NO. " <260+VDIGIT> "."
     .ENABLE ASCII
     .ENABLE 7BIT
     TEXT "VER" <C> <212> "NO. " <260+VDIGIT> "."
     .ENABLE OS8
     TEXT "VER" <C> <212> "NO. " <260+VDIGIT> "."
     .ENABLE OS8
     .ENABLE 8BIT
     .DISABLE FILL
     TEXT "VER" <C> <212> "NO. " <260+VDIGIT> "."

				       MACREL-V2D THU 10-JAN-79
						      FILE # 1
	1		     / QTEXTK ---FIX
	2	     0003    VDIGIT=3
	3	     7015    C=7015
	4		     .ENABLE 8BIT
	5		     .ENABLE SIXBIT
	6		     .ENABLE FILL
	7    00200   2605 TEXT "VER" <C> <212> "NO. " <260+VDIGIT> "."
	     00201   2215
	     00202   1216
	     00203   1756
	     00204   4063
	     00205   5600 .FILL
	8		     .ENABLE ASCII
	9    00206   0326    TEXT "VER" <C> <212> "NO. " <260+VDIGIT> "."
	     00207   0305
	     00210   0322
	     00211   0215
	     00212   0212
	     00213   0316
	     00214   0317
	     00215   0256
	     00216   0240
	     00217   0263

		 Figure 5-1 Example of TEXT Option Processing

				     5-12

			       MACREL DIRECTIVES


	     00220   0256
	     00221   0000
	10		     .ENABLE ASCII
	11		     .ENABLE 7BIT
	12   00222   0126    TEXT "VER" <C> <212> "NO. " <260+VDIGIT> "."
	     00223   0105
	     00224   0122
	     00225   0015
	     00226   0012
	     00227   0116
	     00230   0117
	     00231   0056
	     00232   0040
	     00233   0063
	     00234   0056
	     00235   0000
	13		     .ENABLE OS8
	14   00236   2526    TEXT "VER" <C> <212> "NO. " <260+VDIGIT> "."
	     00237   1105
	     00240   2015
	     00241   7012
	     00242   1117
	     00243   0056
	     00244   0063
	     00245   0056
	     00246   0000
	     00247   0000
	15		     .ENABLE OS8
	16		     .ENABLE 8BIT
	17		     .DISABLE FILL
	18   00250   6726    TEXT "VER" <C> <212> "NO. " <260+VDIGIT> "."
	     00251   1305
	     00252   6215
	     00253   7212
	     00254   5317
	     00255   0256
	     00256   0263
	     00257   0256

	     Figure 5-1 (Cont.) Example of TEXT Option Processing



     5.4  CODE LOCATION DIRECTIVES

     The following directives affect the location of code:

	  o  Asterisk (*)
	  o  PAGE
	  o  FIELD
	  o  RELOC




				     5-13

			       MACREL DIRECTIVES


				     NOTE

		   See also the program section  directives
		   described in Section 7.1.



     5.4.1 Asterisk (*)

     The asterisk (*) directive sets the  current  location  counter.   The
     form of the directive is:

	  *exp

     where:

	  exp		 is an expression.

     In an absolute program section, the expression exp  must  be  absolute
     and  any  symbols must have been previously defined within the current
     source module.  The current location counter then is set to the  value
     of the expression.  For example (in octal),

	  N=7
	  *N^200
	  CLA

     sets the current location counter to  1600,  and  therefore,  the  CLA
     (7200) will load at address 1600.

     In relocatable program section, the  expression  (exp)  should  be  an
     absolute or a simple relocation expression.  For example,

	  .RSECT WPROC
	  *400

     sets the current location counter to 400 plus WPROC where WPROC is the
     address  of the beginning of the program section.  Thus, the assembler
     skips the first 400 words in the program section.


				   CAUTION

		   It is legal to set the current  location
		   counter   to  an  unknown  value  (i.e.,
		   complex   relocatable   expression    or
		   external symbol).  This can be dangerous
		   and requires care in  use  (see  Section
		   10.8).


     It is illegal to set the current location counter out of  the  current
     program section.


				     5-14

			       MACREL DIRECTIVES


     You can use the asterisk directive to skip over the next five words by
     using the construction:

	  *.+5

     Note that you can set the current location counter downward, but  this
     may produce unsatisfactory results.  For example:

	  *.-20

     is a valid statement  provided  the  value  in  the  current  location
     counter  is  20  or  greater.   But  this statement causes the next 20
     instructions to overwrite 20 previously  assembled  instructions.   In
     addition,  if  this  statement  sets the current location counter to a
     previous page, any address literals on that page may be overwritten.

     You can also change the current location through  the  PAGE  directive
     and  through  the  FIELD  directive  (see  Sections  5.4.2  and  5.4.3
     respectively).

     In absolute programs, the current location  counter  (.)  has  as  its
     value a 12-bit absolute number.

     In relocatable sections, it has an absolute  part  and  a  relocatable
     part.   The  relocatable  part  is  relative  to  the beginning of the
     section.


				     NOTE

		   Because the asterisk is a directive,  it
		   cannot be embedded in an expression.


     To  see  the  results  of  using  the  current  location  counter   in
     relocatable expressions, study the following example:

	  .RSECT    LEW
		    .+3
	  A,	    .-LEW
		    .+A

     This source program segment generates the following code:

	  1.  The line .+3 evaluates (at  assembly  time)  as  the  current
	      location  (0  plus  LEW)  plus 3, or 3 plus LEW.  (LEW is the
	      loading address of the  beginning  of  this  section,  to  be
	      determined by LINK).

	  2.  The label A in the third line is defined as 1 plus LEW.   (It
	      is  the  first  location  after  zero.)  The current location
	      counter also has this value, so subtracting  LEW  results  in
	      <1+LEW>-<0+LEW>, or absolute 1.


				     5-15

			       MACREL DIRECTIVES


	  3.  The fourth line .+A evaluates as the current location (2+LEW)
	      plus  A  (1+LEW),  or 3+2^LEW.  This is a complex relocatable
	      expression and is passed on as global arithmetic for LINK.


				    CAUTION

		   Avoid having assembly pass one  generate
		   a   different   origin   for  code  from
		   assembly pass two.  This will happen  if
		   the  expression  following  the asterisk
		   evaluates  to  different  values  on the
		   different  passes and causes an assembly
		   error.



     5.4.2  PAGE

     The PAGE directive followed by an argument is used to set the  current
     location  counter to the beginning of the specified page.  If the PAGE
     directive is used without an argument, it causes the  program  counter
     to skip to the beginning of the next page.  If the current location is
     already the beginning of a memory page, MACREL ignores  the  directive
     and does not skip to the next page.

     The form of the directive is:

	  PAGE exp

     where:

	  exp		 is an expression.  The expression must be  in  the
			 range 0 to 37, inclusive.

     When PAGE is used with an expression, the current location counter  is
     set to the beginning of the page indicated.  For example, if the radix
     is octal, the following two directives perform a similar function:

	  PAGE E
	  *200^E

     If E=4, either expression will set the  current  location  counter  to
     1000 (octal).

     In a relocatable program section, the directive sets the absolute part
     of  the  location  counter as just described.  The relocatable part is
     relative to the beginning of the program section.

     The value of exp must be known on pass 1.

     The PAGE directive, when used without arguments, provides a convenient
     means  of  defining  pages in the program;  namely if code is inserted


				     5-16

			       MACREL DIRECTIVES


     into an earlier part of the program section, you need  not  alter  all
     succeeding PAGE or Asterisk directives in that program section.


				    CAUTION

		   Avoid having assembly pass one  generate
		   a   different   origin   for  code  from
		   assembly pass two.  This will happen  if
		   the  expression  following  the asterisk
		   evaluates to  different  values  on  the
		   different  passes and causes an assembly
		   error.


     You will find the directive useful at the end of a page to make MACREL
     list  the  current  page literals on the same physical listing page as
     the code.



     5.4.3  FIELD

     The FIELD directive restricts the field into which the current program
     section   is   to  be  loaded.   The  FIELD  directive  acts  somewhat
     differently in named and unnamed program sections.   You  should  name
     all  sections,  to  maintain  a  consistent  approach  to  coding your
     programs.



     5.4.3.1   FIELD  Directive  in  Named  Program  Sections - The   FIELD
     directive is specified in the form:

	  FIELD exp

     where:

	  exp		 is an expression.  The processing depends  on  the
			 relocation  type  of  expression  as  described in
			 Table 5-3.

     You can use the FIELD directive anywhere in  the  program  section  to
     which  it  applies.   It does not change the current location counter.
     When the expression (exp) is absolute the field digits  (0-37)  appear
     in  the  field  column  of the assembly listing.  When exp is a simple
     relocation expression,  the  directive  instructs  LINK  to  load  the
     program  section  into  the  same field (whatever it might be) as exp.
     The field column of the listing has a question mark (?) to  show  that
     the value is unknown at assembly time.





				     5-17

			       MACREL DIRECTIVES


				   Table 5-3
	     FIELD Directive Processing for Named Program Sections

     ----------------------------------------------------------------------
     | Relocation     |							  |
     | Type of Ex-    |			    Processing			  |
     | pression	      |							  |
     |----------------|---------------------------------------------------|
     | Absolute	      | Restricts this program section to load  in  field |
     |		      |	exp.   (exp  must  have a value between 0 and 37, |
     |		      |	inclusive;   otherwise,  an  error   message   is |
     |		      |	produced.)					  |
     |----------------|---------------------------------------------------|
     | Simple	      |	Restricts this program section  to  load  in  the |
     | Relocatable    |	same  field  as the field of the relocatable part |
     |		      |	of the  expression.   For  example,  FIELD  SUBR, |
     |		      |	where  SUBR is a symbol in a relocatable section, |
     |		      |	causes the current program section to  be  loaded |
     |		      |	to  the  same  field  as the program section that |
     |		      |	contains SUBR.					  |
     |----------------|---------------------------------------------------|
     | Complex-	      | Not allowed.					  |
     | Relocatable    |							  |
     |----------------|---------------------------------------------------|
     | .CDF/CIF	      | Not allowed.					  |
     |----------------|---------------------------------------------------|
     | .FSECT	      | Not allowed.					  |
     ---------------------------------------------------------------------|



     5.4.3.2  FIELD Directive in  Unnamed  Program  Sections - To  maintain
     PAL8 compatibility, MACREL treats unnamed program sections as absolute
     program sections (see Section 7.1.1).  (This  means  that  no  program
     section  directives  have  appeared  prior to this in the program.) It
     processes the FIELD directive the same way that PAL8 does.

     The form of the directive is:

	  FIELD exp

     where:

	  exp		 is an expression.  The expression must be absolute
			 and in the range 0 to 37 inclusive.

     The directive creates a new unnamed program section, causes it  to  be
     loaded  into  field  specified  by  exp  and sets the current location
     counter to 200.  Thus, any code that follows will be loaded into  that
     field  starting  at  location  200.   Note  that, since FIELD sets the
     current location counter to 200, any asterisk directives should follow
     FIELD  rather  than  precede  it.  For example, if you want to set the
     current location counter to 400, the construction,


				     5-18

			       MACREL DIRECTIVES


	  *400
	  FIELD 1

     does not produce the desired result (the current location counter will
     be  set  to 200).  A program with no program section directives and no
     FIELD directives loads into field 0.



     5.4.4  RELOC

     The RELOC directive allows you  to  create  a  segment  of  code  that
     executes  in a set of memory locations that are different from the set
     of memory locations where LINK loads them.

     The form of the directive is:

	  RELOC exp
	  code
	    .
	    .
	    .
	  RELOC

     where:

	  exp		 is an  expression  that  specifies  the  beginning
			 address  of the area in memory where the code will
			 be executed.  All symbols in the  expression  must
			 be defined previously in the source module.  In an
			 absolute program section, the expression  must  be
			 absolute.    In   a   relocatable   section,   the
			 expression must be relative to the current program
			 section.    The  expression  may  not  be  complex
			 relocatable.  Thus, in a relocatable section  OVR,
			 the directive:

			      RELOC 4000

			 would be interpreted as RELOC 4000+OVR.

	  code		 is one or more lines of code to be relocated.

	  RELOC		 terminates the relocation  sequence  and  restores
			 MACREL   to   its   ordinary   mode   of   address
			 calculation.

     It is your program's  responsibility  to  dynamically  move  the  code
     affected  by this directive to the area of memory that begins with the
     address specified by the value of the expression (exp).

     The following example illustrates the use of the RELOC directive.



				     5-19

			       MACREL DIRECTIVES


		  0400		  *400
		  2000		  RELOC 2000
	  02000*  1377	  CODE,	  TAD (CODE
	  02001*  3005		  DCA 5
	  02177*  2000
				  PAGE
		  0600		  RELOC

     The location  marked  CODE  is  loaded  into  location  400,  but  the
     assembler  treats  it  as  if it were loading into location 2000.  The
     asterisks after the location values indicate that the virtual and  the
     actual  location  counters differ for that line of code.  RELOC on the
     last line sets the  virtual  location  counter  equal  to  the  actual
     location counter and terminates the relocation section.


				    CAUTION

		   Be sure that all literals that apply  to
		   the  RELOC  segment  reside  within that
		   segment.



     5.5  CONDITIONAL ASSEMBLY DIRECTIVE

     This section describes the .IF conditional assembly directive and  the
     logical  conditions  that  complete  the directive.  The .IF directive
     replaces  the  conditional  assembly  pseudo-operators  of  the   PAL8
     assembler.

     The .IF conditional assembly directive allows you to create  different
     binary   object   modules  depending  on  the  conditions  of  certain
     variables.  For example, the code,

	  .IF EQ LRGMEM <TAD MEM
		 DCA MEMP>

     causes the two lines TAD MEM and DCA  MEMP  to  be  assembled  if  the
     variable LRGMEM equals 0, and ignored if LRGMEM does not equal 0.  The
     use  of  conditional  code   is   particularly   useful   in   writing
     general-purpose  programs  that  are to be assembled in different ways
     depending on local parameters.


				    CAUTION

		   Do  not  write   a   program   so   that
		   conditional  code  assembles differently
		   on each pass.  This  may  result  in  an
		   assembly  error.   For  example,  in the
		   previous  code,  if  you  define  LRGMEM
		   after  this  point  in  the program, the
		   conditional might expand differently  on

				     5-20

			       MACREL DIRECTIVES


		   the  second  pass than on the first.  In
		   general, you must  perform  calculations
		   that alter symbol definitions before the
		   symbol is used  as  the  argument  of  a
		   conditional.


     The form of the directive is:

	  .IF  cond   exp  <source code
		     source code
		       .
		       .
		       .
		     source code>

     where:

	  cond		 is one of the logical  condition  codes  shown  in
			 Table 5-4.

	  exp		 is an expression suitable to the condition.

	  <source code>  is any number of lines  of  source  code  enclosed
			 within   angle  brackets  (<>).   The  left  angle
			 bracket (<) must  be  on  the  same  line  as  the
			 directive itself.


				    NOTES

	  1.  When you specify one of the condition codes in  Table  5-4,
	      only  the  first two characters are significant, except for
	      REL, which requires three characters.  Two letters  may  be
	      used,  or  (when  appropriate)  the  full word.  Additional
	      letters or numbers after the significant ones are  ignored.
	      Thus,  EQUAL  may  be used instead of EQ.  For BL only, the
	      letter B may be used alone.

	  2.  The BL (blank) condition is normally used to test  for  the
	      presence  of  one of the actual arguments of a macro to see
	      if it is used in a given macro call (see Chapter  6).   For
	      example, the macro:

		   .MACRO ADDNBS   A, B, C, D
			 CLA
			 TAD A
		   .IF NB B <TAD B>
		   .IF NB C <TAD C>
		   .IF NB D <TAD D>
		   .ENDM




				     5-21

			       MACREL DIRECTIVES


				   Table 5-4
	     Conditions for the .IF Conditional Assembly Directive
			(Grouped in Complementary Pairs)

     ----------------------------------------------------------------------
     | Condition |		 |					  |
     |   Code	 | Argument Type |	Assemble <Source Code> If:	  |
     |-----------|---------------|----------------------------------------|
     |   EQ	 | Expression	 | Expression=0				  |
     |   NE	 | Expression	 | Expression 0				  |
     |-----------|---------------|----------------------------------------|
     |   LT	 | Expression	 | Expression<0				  |
     |   GE	 | Expression	 | Expression 0				  |
     |-----------|---------------|----------------------------------------|
     |   GT	 | expression	 | Expression>0				  |
     |   LE	 | Expression	 | Expression 0				  |
     |-----------|---------------|----------------------------------------|
     |   DF	 | Symbol	 | Symbol is defined with a value	  |
     |   NDF	 | Symbol	 | Symbol is not defined		  |
     |-----------|---------------|----------------------------------------|
     |   BL	 | STRING	 | Argument is blank (null) (see text)	  |
     |   NB	 | STRING	 | Argument is not blank (see text)	  |
     |-----------|---------------|----------------------------------------|
     |   ABS	 | Expression	 | Expression is absolute		  |
     |   REL	 | Expression	 | Expression is relocatable (includ-	  |
     |		 |		 | ing complex-relocatable)		  |
     |-----------|---------------|----------------------------------------|
     |   IDN	 | STRING,STRING | Two strings are identical		  |	
     |   DIF	 | STRING,STRING | Two strings are different.		  |
     ----------------------------------------------------------------------


	      can be used to add between one and four  values.   The  .IF
	      directive  with the condition NB (not blank) is used to see
	      if a given argument is  specified  in  a  particular  macro
	      call.   If  the  argument B, for example, was not used in a
	      specific call, it will have a  value  of  null  inside  the
	      macro.   Then  the  conditional  code  TAD  B  will  not be
	      assembled.

	  3.  Note that BL and NB  refer  to  the  logical  condition  of
	      being.  They do not refer to the ASCII space character.

	  4.  The  ABS  condition  means  that  the  expression  has   no
	      relocatable part.  For example, the statement:

		   .IF ABS . <TAD A>

	      causes the TAD A to assemble if it is used in an .ASECT and
	      to  be  ignored  if  it  is  used in an .RSECT, because the
	      current location counter always has the attributes  of  the
	      current section.



				     5-22

			       MACREL DIRECTIVES


	  5.  The IDN and DIF condition options allow you  to  perform  a
	      character   by  character  comparison  of  two  ASCII  text
	      strings.  The left argument string cannot contain  a  comma
	      (,).  The right argument string cannot contain a left angle
	      bracket (<).  All other ASCII  characters  including  space
	      can be used.

     The following example shows a block of conditionally assembled code:

	  MUSER=0
	  .IF NDF MUSER <A=A+4
		    TAD (A)
		    DCA MUN>

     The condition used here is NDF  (not  defined).   Because  the  symbol
     MUSER  is,  in  fact,  defined, the condition is false;  therefore the
     code enclosed within angle brackets is not  assembled.   A  symbol  is
     defined  by  being  used as a label, in a direct assignment statement,
     or as a program section or macro name.   All  permanent  symbols  are,
     of  course,  defined.  For the purpose of this condition, an .EXTERNAL
     symbol is undefined, because it is not known at the time  of  assembly
     of this source module.



     5.5.1  Nested Conditional Assembly Directives

     Conditional assembly directives may also  be  nested.   A  maximum  of
     4095  levels  is  allowed.   The  general  form  of nested conditional
     statements is:

	  .IF cond.1 arg.l <code code----code
	  .IF cond.2 arg.2 <code---code>>

     The angle brackets are treated as pairs.   If  the  condition  in  the
     first  .IF  is  true, all of the code contained within the outside set
     of angle brackets, including a test of the second  .IF  directive,  is
     assembled.   If  it  is  false  all code within the outer set of angle
     brackets  is  ignored,  regardless  of  the  condition  of  the  inner
     conditional.   If  the  first  conditional is true, the assembler then
     checks the condition of the second conditional statement.

     If the second conditional is false,  the  code  contained  within  the
     inner  set  of  angle  brackets  is  ignored,  but  all  other code is
     assembled.

     The code in the following example  determines  if  the  symbol  NEWAVG
     has been defined, and if it is different from the symbol OLDAVG.

	  .IF DF NEWAVG <.IF NE NEWAVG-OLDAVG<TAD NEWAVG;DCA OLDAVG>>

     This statement first checks  whether  NEWAVG  has  been  defined.   If
     NEWAVG  is  defined, the code contained in the outer angle brackets is
     assembled.  The code within the  outer  brackets  is  the  second  .IF

				     5-23

			       MACREL DIRECTIVES


     directive,  IF  NE NEWAVG-OLDAVG.  If NEWAVG and OLDAVG are different,
     the condition is true and the code contained  in  the  inner  brackets
     is  assembled.   This  inner  code deposits the value of NEWAVG in the
     location formerly occupied by the value of OLDAVG.



     5.5.2  Other PAL8 Conditional Assembly Directives

     For compatibility with  PAL8,  MACREL  allows  you  to  use  the  PAL8
     conditional   pseudo-operators.    Each   is  equivalent  to  the  .IF
     directive plus the suitable condition.   The  PAL8  directives  behave
     in  all  ways  like  the equivalent .IF directives.  The following are
     the  PAL8  directives  and  their  exact  equivalents  using  the  .IF
     directive:

	  PAL8 Pseudo-Operator	     Equivalent MACREL .IF Directive	  ____________________	     _______________________________

	      IFDEF				 .IF DF
	      IFNDEF				 .IF NDF
	      IFZERO				 .IF EQ
	      IFNZRO				 .IF NE



     5.6  ASSEMBLY CHAINING DIRECTIVES

     MACREL allows a source file to include  another  source  file  without
     specifying  the  file in the assembler's command string.  This feature
     is  particularly  useful   for   referencing   subroutine   or   macro
     libraries.  There are two directives for this function.

	  .INCLUDE and .CHAIN.



     5.6.1 .INCLUDE

     The .INCLUDE directive includes another  source  file  in  the  source
     code  stream.   After  executing  an  .INCLUDE directive, MACREL takes
     the next statement to be assembled from  the  file  specified  in  the
     directive,  assembles  all  the  statements in that file, then returns
     to the current file and continues with the assembly.

     The form of the directive is:

	  .INCLUDE file specification

     where:

	  file specification
			 is the  file  specification  of  the  source  file
			 that  you  wish  to  assemble.   The  file  cannot
			 reside  on  a  non-file  structured  device.   The

				     5-24

			       MACREL DIRECTIVES


			 default  device  is  DSK:.   The default file name
			 extension is .MA or if  not  found,  null.   Refer
			 the   OS/8  Handbook  for  a  discussion  of  file			       ______________
			 specifications.

     For example, the statement,

	  .INCLUDE DTA1:LIBRAR.MA

     includes the entire  source  file  LIBRAR.MA  located  on  DECtape  1.
     Similarly,

	  .INCLUDE SUBR.PA

     includes all of the file SUBR.PA located on DSK:.

     .INCLUDE directives may be  nested.   One  file  may  include  another
     file  which  may,  in  turn, include a third file, and so on.  Nesting
     results in control eventually passing  back  to  the  original  source
     file.



     5.6.2 .CHAIN

     The .CHAIN  directive  causes  the  assembler  to  close  the  present
     source  code  file  and  to  continue  assembling from the source file
     specified in  the  directive.   Unlike  the  .INCLUDE  directive,  the
     assembler  does  not  return  to  the  old  source  file,  during this
     assembly pass.

     The form of the directive is:

	  .CHAIN file specification

     where:

	  file specification
			 is the  file  specification  of  the  source  file
			 that  you  wish  to  assemble.   The  file  cannot
			 reside  on  a  non-file  structured  device.   The
			 default  device  is  DSK:.   The default file name
			 extension is .MA, or if not  found,  null.   Refer
			 to  the  OS/8  Handbook  for  a discussion of file				  ______________
			 specifications.

     Assuming that DSK is a file oriented device, the directive:

	  .CHAIN NPART2.MA

     causes the assembler to  disregard  the  remainder  (if  any)  of  the
     present  source  file  and to start assembling from the file NPART2.MA
     on DSK.


				     5-25

			       MACREL DIRECTIVES


     One file may ".CHAIN" to another file which  may,  in  turn,  ".CHAIN"
     to  a  third file.  In this case, assembly will terminate with the end
     of the last file.  .CHAIN directives and .INCLUDE  directives  can  be
     intermixed.



     5.7  USER SERVICE ROUTINE (USR) COMMUNICATION DIRECTIVES

     The User Service Routine (USR), is an OS/8 system routine  that  opens
     and  closes  files,  loads  device handlers, chains programs and calls
     the Command Decoder.

     Several of the USR functions  take  device  names  or  file  names  as
     arguments.   To  simplify  the  task  of  generating  these arguments,
     MACREL incorporates the DEVICE and FILENAME directives to  create  the
     6-bit  ASCII  characters  for  the  device name or the file name.  You
     can use these character strings as part of the coding for  a  call  to
     the  USR  or  for any other coding that requires a 6-bit packed device
     or file name.  Note that these directives do  not  perform  any  other
     function  (call  the  USR,  etc.).   They merely insert the 6-bit text
     for device and file name  at  the  current  location.   The  assembler
     checks to make sure that all characters are letters or numbers.

     The OS/8 Software Support Manual describes how to use the  DEVICE  and	 ____________________________
     FILENAME directives in calls to the User Service Routine.



     5.7.1  DEVICE

     The DEVICE directive creates the 6-bit ASCII codes for  a  4-character
     OS/8 device name and packs them into two words.

     The form of the directive is:

	  DEVICE dev

     where:

	  dev		 is the device name.  You can specify from  one  to
			 four  alphanumeric  characters;   other characters
			 are illegal.

     The directive always generates two 12-bit  words  of  data  regardless
     of  the  number  of  characters  in  its  argument.   If  the argument
     contains  fewer  than  four  characters,   the   remaining   character
     positions are packed with binary zeroes.



     5.7.2  FILENAME



				     5-26

			       MACREL DIRECTIVES


     The  FILENAME  directive  creates  the  6-bit  ASCII  codes  for   the
     characters of an OS/8 file name and extension.

     The form of the directive is:

	  FILENAME filename.ex

     where:

	  file name	 is the name of the file.   You  can  specify  from
			 one to six characters.

	  .ex		 is the file name extension.  This  consists  of  a
			 period followed by two characters.

     The directive always generates  four  12-bit  words:   three  for  the
     file  name  and one for the extension (the period for the extension is
     implied).  If the file name contains less  than  six  characters,  the
     remaining  character  positions  are packed with binary zeros.  If the
     extension is missing, the extension word is packed with binary zeros.



     5.8  LOADING INFORMATION DIRECTIVES

     MACREL  provides  following   directives   that   supply   information
     directly to LINK.  These are:

	  o  .START
	  o  .JSW
	  o  .VERSION



     5.8.1  .START

     The .START directive specifies the program's starting address  in  the
     relocatable  binary  module  rather than at LINK time.  LINK, in turn,
     inserts  this  starting  address  into  the  memory  image  file  (.SV
     extension).   You  can  specify  the  .START  directive  in one of two
     forms:  with two  arguments  or  with  only  one  argument.   Each  is
     interpreted differently.

     The 2-argument form of the directive is:

	  .START m, n

     where:

	  m		 is an  absolute  expression  value  in  the  range
			 0-7777   (octal)   that   specifies  the  starting
			 address within a memory field.



				     5-27

			       MACREL DIRECTIVES


	  n		 is an  absolute  expression  value  in  the  range
			 0-37 (octal) that specifies the memory field.

     For example, the coding,

	  .START 2000, 4

     specifies that the program is to start in field 4 at address 2000.

     The 1-argument form of the directive is:

	  .START m

     where:

	  m		 is  an  expression.    The   expression   may   be
			 absolute  or  relocatable.   If  m is absolute, it
			 defines the starting address,  and  the  field  is
			 the  same  field  as  the current program section.
			 If m is relocatable,  the  absolute  part  of  the
			 expression  defines  the starting address, and the
			 field  is  the   same   as   the   field   of  the
			 relocatable part of the symbol.

     For example, the coding,

	  .RSECT MAIN
	  .START 200

     causes the program to start at address 200  in  the  same  field  that
     section  MAIN  loads into.  Similarly, if WPROC is the name of another
     relocatable program section, the coding,

	  .RSECT SUBR
	  .START WPROC+4000

     causes the program to start at address 4000 plus the  value  of  WPROC
     in the same field that WPROC loads into.



     5.8.2  .JSW

     The .JSW directive sets the Job Status Word (JSW) in  the  relocatable
     binary  module.   LINK,  in  turn,  inserts  this word into the memory
     image file (.SV extension) which it creates.

     The form of the directive is:

	  .JSW n

     where:

	  n	 is an absolute expression.

				     5-28

			       MACREL DIRECTIVES


     The  JSW  is  a  12-bit  word,  in  which  different  bits   represent
     different  instructions  to  the system program that loads the program
     into memory.  For example if bit 0 is set, this indicates that no part
     of  the  program  loads  into  locations 00000 to 01777.  Refer to the
     OS/8 Software Support Manual for more information on  the  Job  Status     ____________________________
     Word and its bit assignments.



     5.8.3  .VERSION

     The .VERSION directive inserts a version number  in  the  range  0  to
     7777 (octal) into the relocatable binary module.

     The form of the directive is:

	  .VERSION n

     where:

	  n		 is an absolute expression.

     At present this information is not used, but it may be  referenced  by
     a user program, or by future DIGITAL EQUIPMENT CORPORATION software.



     5.9  SYMBOL TABLE MODIFICATION DIRECTIVES

     MACREL provides  the  following  directives  that  modify  the  symbol
     table.  They are:

	  o  EXPUNGE
	  o  FIXMRI
	  o  FIXTAB

     With these directives you can eliminate unneeded symbols, add  certain
     standard symbols, or define your own special symbols.


				     NOTE

		   Certain MACREL  command  string  options
		   affect  the  Permanent Symbol Table (see
		   Table 8.1).



     5.9.1  EXPUNGE

     The EXPUNGE directive deletes certain symbols and macro names from the
     symbol  table.   The  directive  has two forms:  without arguments and
     with arguments.


				     5-29

			       MACREL DIRECTIVES


     The form of the directive without arguments is:

	  EXPUNGE

     This form is generally used at the beginning of the program.   EXPUNGE
     causes all regular permanent and program-defined symbols to be deleted
     from the symbol table.  Macro names, directive  keywords  and  keyword
     arguments,  program  section  names, special symbols, and symbols that
     have been named by a  declaration  directive  are  not  deleted.   The
     deletion  occurs  at  the  current  point  in  the assembly.  After an
     EXPUNGE, symbols may then be  selectively  redefined.   The  directive
     functions only on assembly pass one.

     The form of the directive with arguments is:

	  EXPUNGE symbol,...

     where:

	  symbol	 is a symbol name.

     The directive causes MACREL to delete each  symbol  that  you  specify
     from  the  symbol  table  at  the  current point in the assembly.  For
     example,

	  EXPUNGE RSF, RRB, RFC

     deletes the machine instruction mnemonics for  the  high-speed  reader
     from the permanent symbol table.

     You can use the EXPUNGE directive to delete program symbols, permanent
     symbols, or macro names.  It does not delete a directive name, special
     symbol, or a symbol named with a declaration directive.  An attempt to
     delete  these  causes an error message.  It is legal, incidentally, to
     include a nonexistent symbol in the list.  Use this feature if you are
     uncertain whether the symbol exists.

     You can also use the EXPUNGE directive with a list to delete  a  macro
     name  and  its associated text from the symbol table area.  This space
     is reclaimed, allowing more space in the symbol table area  for  other
     functions.

     There are three general reasons to perform an EXPUNGE with a permanent
     or program-defined symbol:

	  1.  To delete a symbol to gain space in the symbol table.

	  2.  To redefine a symbol (EXPUNGE should occur before  the  first
	      use of the symbol).

	  3.  To use the symbol, delete it, and then redefine  it  (perhaps
	      several  times).  For example, you might have a subroutine in
	      another file that happens to use the  same  symbol  or  label
	      that the main program uses.

				     5-30

			       MACREL DIRECTIVES


     The EXPUNGE without arguments works only on pass one.   This  prevents
     deleting  symbols  that  you have redefined.  The purpose of the first
     pass is to create the symbol table;   if  the  assembler  performed  a
     general EXPUNGE at the beginning of the second pass, it is effectively
     set back to pass one  again.   The  assembler  normally  performs  the
     EXPUNGE with arguments directive on assembly pass 1 only.

     To have the EXPUNGE with arguments act on all passes, use the  EXPUNGE
     option of the .ENABLE directive in the form:

	  .ENABLE EXPUNGE

     Note that the EXPUNGE option of the  .ENABLE  directive  is  different
     from  the EXPUNGE directive.  The option allows you to use the EXPUNGE
     directive with arguments in much  the  same  way  as  EXPUNGE  without
     arguments.  For example, in the code,

	  EXPUNGE   HLT
		   .
		   .
		   .
		  TAD HLT
		   .
		   .
		   .
	  HLT,	    7000

     the pass-one-only EXPUNGE allows the symbol HLT to be used  before  it
     is defined.


				     NOTE

		   If the all-pass EXPUNGE  were  used,  an
		   undefined  symbol  error  would occur on
		   pass 2.


     Use the .DISABL directive in the form:

	  .DISABL EXPUNGE

     to return the EXPUNGE with arguments to its former status.



     5.9.2  FIXMRI

     The  FIXMRI  directive  defines  a  symbol  as  a   memory   reference
     instruction.  The form of the directive is:

	  FIXMRI sym=exp



				     5-31

			       MACREL DIRECTIVES


     where:

	  sym		 is a symbol name

	  exp		 is an absolute expression.

     For example,

	  FIXMRI   TAD=1000

     redefines TAD to its normal value.  Use the directive to respecify the
     memory reference instructions after deleting the Permanent Symbol
     Table.



     5.9.3  FIXTAB

     The FIXTAB directive defines permanent symbols.   It  has  two  forms:
     without arguments and with arguments.

     The form of the directive without arguments is:

	  FIXTAB

     It causes all previously defined symbols to  be  marked  as  permanent
     symbols.   Use the FIXTAB directive to redefine permanent symbols that
     have been removed with the EXPUNGE directive.  An  example  of such  a
     redefinition  would  be to create a file named PERMSY.MA that contains
     the desired symbols,

	  CLA=7200
	  NOP=7000
	  HLT=7402
	  SNA=7450
	   .
	   .
	   .
	  FIXMRI AND=0000
	  FIXMRI TAD=1000
	  FIXMRI ISZ=2000
	   .
	   .
	   .

     then insert the following code at the beginning of the source file:

	  EXPUNGE
	  .INCLUDE PERMSY.MA
	  FIXTAB

     This deletes the old permanent symbols and establishes the symbols  in
     the file as the new permanent symbols.


				     5-32

			       MACREL DIRECTIVES


     The form of the directive with arguments is:

	  FIXTAB symbol,...

     where:

	  symbol	 is a symbol name.

     The directive causes the symbols named in the argument to be marked as
     permanent symbols.  Thus,

	  SET1=	  CLA IAC    /SET AC=1
	  SGT0=	  SPA SNA    /SKIP IF AC GREATER THAN 0
	  FIXTAB  SET1, SGT0

     defines SET1 and SGT0 as permanent symbols having  the  values  shown.
     Using  FIXTAB  this way prevents SET1 and SGT0 from being accidentally
     redefined.


				     NOTE

		   You  can  also  define  macro  names  as
		   permanent symbols.



     5.10  STACK MANIPULATION DIRECTIVES

     The stack manipulation directives, .PUSH and .POP, insert one or  more
     numbers  into a pushdown stack (.PUSH) and retrieve them on a last in,
     first out basis (.POP).  Thus the first number pushed onto  the  stack
     is  the last number popped off the stack.  The stack has a capacity of
     about 25 numbers.

     The stack is used at assembly time and is not available to the program
     at execution time.



     5.10.1  .PUSH

     The .PUSH directive inserts one or more symbol values into the stack.

     The form of the directive is:

	  .PUSH sym,...

     where:

	  sym		 is a symbol name the value of which may be  either
			 absolute or simply relocatable.



				     5-33

			       MACREL DIRECTIVES


     For example, if the current radix is octal,

		  *300
	  LOC,
	  N=1O
	  .PUSH N
	  .PUSH LOC

     causes the following numbers to be inserted  into  the  stack  (bottom
     first):  10, 300.

     If the stack size is exceeded (too many numbers  are  pushed),  MACREL
     prints a STACK OVERFLOW error message.



     5.10.2  .POP

     The .POP directive retrieves one or more numbers from the stack.

     The form of the directive is:

	  .POP sym,...

     where:

	  sym		 is the name of the symbol whose value you wish  to
			 retrieve.

     Note that you must specify a list of arguments in  the  reverse  order
     from  that  specified by the .PUSH directive, because MACREL retrieves
     the numbers in last in, first out order.  Thus, if the statement

	  .POP DATA, Q,

     were to follow the statement shown in Section  5.10.1,  the  following
     values would result:

	  DATA    300
	  Q	  10

     If you .POP more values than you .PUSH, an error message results.



     5.11  ASSEMBLY OPTIONS DIRECTIVES

     The assembly options directives allow you  to  enable  and  disable  a
     variety  of assembly features.  (Some of these features are handled in
     PAL8 as run-time options.)





				     5-34

			       MACREL DIRECTIVES


     5.11.1  .ENABLE

     The .ENABLE directive activates the options described in Table 5.5.

     The form of the directive is:

	  .ENABLE option, ...

     where:

	  option	 is one or more nonconflicting  options  listed  in
			 Table 5-5.


				     NOTE

		   You can dynamically alter these  options
		   at  assembly  time by changing the value
		   of the  .ENABWD  special  variable  (see
		   Section 5.11.3).

     If you specify  the  FILL  option,  the  TEXT  directive  will  always
     generate  at  least  one  character consisting of all zeros.  In ASCII
     packing, this means always adding a word  of  all  zeros.   In  SIXBIT
     packing,  this  means  adding  a  word  of  all zeros if the number of
     characters is even.  In OS8 packing, this means adding a word  of  all
     zeros  if  the  number  of  characters  is evenly divisible by 3.  The
     unused character positions for both SIXBIT and OS8 options are  padded
     with binary zeros.  For more information about the TEXT directive, see
     Section 5.3.2.

     For more information about the  SHIFT  and  OR  options,  see  Section
     4.8.6.   For  more  information  about the EXPUNGE option, see Section
     5.9.1.  (Notice that the option and the directive are different.)

     The PUNCH option causes the assembler to resume binary  output  if  it
     has  been  discontinued  by  either  a  .DISABLE  PUNCH directive or a
     NOPUNCH directive.


				    CAUTION

		   MACREL binary  should  not  be  directly
		   output  to  paper  tape  since  it  will
		   create an output file that is in a  form
		   that  LINK  cannot use.  This is because
		   MACREL expects that the output device is
		   a  random  access  device  and  does not
		   build the file sequentially.






				     5-35

			       MACREL DIRECTIVES


				   Table 5-5
			   .ENABLE Directive Options

     ----------------------------------------------------------------------
     | Option	|			   Action			  |
     |----------|---------------------------------------------------------|
     |   ASCII	| Causes the TEXT directive to generate one character per |
     |		| word.   (The  bit length depends on whether the 7BIT or |
     |		| the 8BIT option is in effect.)			  |
     |		|							  |
     | * SIXBIT | Causes the TEXT directive to  generate  two  characters |
     |		| per word (six bits each) using the sixbit ASCII code.	  |
     |		|							  |
     |   OS8	| Causes the TEXT directive to generate three  characters |
     |		| in two words.  Always produces an even number of words. |
     |		| (The bit length depends on whether the 7BIT or the 8BIT |
     |		| option is in effect.)					  |
     |		|							  |
     |   COS	| Causes  the  TEXT  directive  to  generate  two   6-bit |
     |		| characters  per word packed according to the excess 237 |
     |		| encoding scheme.  (Refer to the COS-310 User's Manual.) |
     |		|							  |
     |	 7BIT	| Causes double quote ("), uparrow double quote (^"), and |
     |		| TEXT  directive (unless SIXBIT packing is in effect) to |
     |		| produce 7-bit ASCII codes.				  |
     |		|							  |
     | * 8BIT	| Causes double quote ("), uparrow double quote (^"), and |
     |		| TEXT  directive (unless SIXBIT packing is in effect) to |
     |		| produce 8-bit ASCII codes (high-order bit is always 1). |
     |		|							  |
     | * EXPUNGE| Causes the EXPUNGE directive with no arguments to  work |
     |		| on all assembly passes.				  |
     |		|							  |
     | * FILL	| Causes the TEXT directive  to  generate  at  least  one |
     |		| character  containing  all zeros at the end of the text |
     |		| string.						  |
     |		|							  |
     | * OR	| Causes the exclamation point (!) operator to perform  a |
     |		| logical OR.						  |
     |		|							  |
     |   PERM	| Causes  the  cross-reference  program  (KREF)  and  the |
     |		| symbol table to include all permanent symbols.	  |
     |		|							  |
     |   PUNCH	| Causes the assembler to resume output of the relocatable|
     |		| binary file, if it has been discontinued.  Acts only on |
     |		| pass two.						  |
     |		|							  |
     |   SHIFT	| Causes the exclamation point (!) operator to mean shift |
     |		| six bits to the left then perform a logical OR.	  |
     ----------------------------------------------------------------------
     * = Default condition.

     The following example illustrates OS8 packing.  The 8-bit ASCII  codes
     for A, B, C (i.e., 301, 302, 303) are represented as follows:

				     5-36

			       MACREL DIRECTIVES


	  First Word	 110 0	      11 000 001
			 Left half    ASCII A
			 of ASCII C

	  Second Word	 001 1	      11 000 010
			 Right half   ASCII B
			 of ASCII C

     The first word in octal is 6301 and the second word is 1702.



     5.11.2  .DISABL

     The .DISABL directive disables the options shown  in  Table  5-6  that
     were  enabled by the .ENABLE directive, or were the default conditions
     of the assembler.

     The form of the directive is:

	  .DISABL option,...

     where:

	  option,...	 is one or more options shown in Table 5-6 below.


				   Table 5-6
			  .DISABL Directive Options

     ----------------------------------------------------------------------
     |  Option	 |	      Action (with .DISABL Directive)		  |
     |-----------|--------------------------------------------------------|
     |  FILL	 |  Disables the zero-fill action of the TEXT  directive. |
     |		 |  TEXT will then not add any extra words of zero.	  |
     |-----------|--------------------------------------------------------|
     |  EXPUNGE	 |  Causes the EXPUNGE directive with arguments  to  work |
     |		 |  only on assembly pass 1.				  |
     |-----------|--------------------------------------------------------|
     |  PERM	 |  Disables the listing  of  permanent  symbols  in  the |
     |		 |  symbol table and cross-reference listing.		  |
     |-----------|--------------------------------------------------------|
     |  PUNCH	 |  Causes the assembler to cease output  of  relocatable |
     |		 |  binary  file  only,  MACREL  continues  the assembly. |
     |		 |  Acts only on assembly pass 2.			  |
     ----------------------------------------------------------------------



     5.11.3  .ENABWD Special Variable

     .ENABWD is an assembler-maintained variable that you can  examine  and
     modify to alter the options of the .ENABLE directive at assembly time.
     The variable contains a 12-bit number the bits of which control  these

				     5-37

			       MACREL DIRECTIVES


     options  (see Table 5-7).  The following example shows how you can use
     .ENABWD in a macro to create a table of 8-bit ASCII characters  padded
     with spaces.

	  .MACRO ENTRY ARG
	  .DSECT TABLE
	  .PUSH .ENABWD
	  .ENABLE ASCII, 8-BIT
	  .DISABLE FILL
	  TEXT <ARG>
	  L=8-.NCHARS ARG
	  .IF LT L <.ERROR "TOO MANY CHARS"
	  .IF NE L <
	  .REPT
	  240
	  .ENDR
	  >
	  .POP .ENABWD
	  .SECT *
	  .ENDM ENTRY



































				     5-38

			       MACREL DIRECTIVES


				   Table 5-7
			    .ENABWD Bit Assignments

     ----------------------------------------------------------------------
     |  Bit    | Value	  |		      Meaning			  |
     |---------|----------|-----------------------------------------------|
     |	       |   0	  |  Enable zero fill.				  |
     |	 0     |----------|-----------------------------------------------|
     |	       |   1	  |  Disable zero fill.				  |
     |---------|----------|-----------------------------------------------|
     |	       |   0	  |  Interpret ! operator as OR.		  |
     |	 1     |----------|-----------------------------------------------|
     |	       |   1	  |  Interpret ! operator as 6- bit left  shift,  |
     |	       |	  |  then OR.					  |
     |---------|----------|-----------------------------------------------|
     |	       |   0	  |  Do EXPUNGE (with arguments) on pass 1 only.  |
     |	 2     |----------|-----------------------------------------------|
     |	       |   1	  |  Do EXPUNGE (with arguments) on all  passes.  |
     |---------|----------|-----------------------------------------------|
     |	       |   0	  |  Do  not  cross-reference  (KREF)  permanent  |
     |	       |	  |  symbols.					  |
     |	 3     |----------|-----------------------------------------------|
     |	       |   1	  |  Do   cross-reference    (KREF)    permanent  |
     |	       |	  |  symbols.					  |
     |---------|----------|-----------------------------------------------|
     |	       |   0	  |  Enable 8-bit ASCII.			  |
     |	 4     |----------|-----------------------------------------------|
     |	       |   1	  |  Enable 7-bit ASCII.			  |
     |---------|----------|-----------------------------------------------|
     |	       |   00	  |  Enable SIXBIT packing.			  |
     |	       |----------|-----------------------------------------------|
     |	       |   01	  |  Enable ASCII packing.			  |
     |	10,11  |----------|-----------------------------------------------|
     |	       |   10	  |  Enable OS/8 packing.			  |
     |	       |----------|-----------------------------------------------|
     |	       |   11	  |  Enable COS packing.			  |
     ----------------------------------------------------------------------


















				     5-39







				   CHAPTER 6

			  MACRO AND REPEAT DIRECTIVES


     Macros are a programming tool that allow you to simplify and customize
     assembly language programs.  They allow you to define generalized code
     sequences, data structures, listing conventions,  program  structures,
     assembly  controls  and  so  on,  and  then customize each of these as
     required.

     For instance, you can use a single symbol to represent any sequence of
     assembly language statements.  This allows you to replace similar (not
     necessarily identical) code sequences by a macro definition.  You  can
     call  the  macro  wherever  desired in the program to insert the code.
     For example,

     Suppose your program includes many code sequences of the form:

	  CDF 10
	  MRI
	  CDF 00

     (Where MRI is a memory reference instruction.)

     The macro definition,

	  .MACRO INST A
	  CDF 10
	  A
	  CDF 00
	  .ENDM INST

     can be called with any MRI, anywhere in the program.  Thus,

	  INST "TAD I DATALOC"

     expands to:

	  CDF 10
	  TAD I DATALOC
	  CDF 00

     while

	  INST "ISZ COUNT"

     expands to:




				      6-1

			  MACRO AND REPEAT DIRECTIVES


	  CDF 10
	  ISZ COUNT
	  CDF 00

     As another example of macro utility consider the difficulty of passing
     data to the following subroutine:

	    (Main Program)
	  *400
	  SONG,	   CLA CLL
		   TAD    SWEHRT
		   DCA    .+3
		   TAD    CHI
		   JMS I  30
		   0000
		   DCA    VERSE
		   .
		   .
		   .
	  VERSE,   0000
	  SWEHRT,  40
	  CHI,     26
	  *30;     6000

	    (Subroutine)

	  *6000
	  CHORD,   0000
		   CIA
		   DCA    SIGMA
		   TAD I  CHORD
		   ISZ    SIGMA
		   JMP    .-2
		   ISZ    CHORD
		   JMP I  CHORD
	  SIGMA,   0000

     Note that in using this subroutine, the main program  includes  almost
     as  many instructions to initialize the subroutine as there are in the
     subroutine itself.  The example at the end of Section  6.1.1  shows  a
     macro definition that simplifies and customizes this subroutine.

     Much of the flexibility of MACREL derives from the  many  features  of
     macros, which include:

	  o  Multiple arguments (maximum of 8)

	  o  Nesting of macro definitions

	  o  Null arguments

	  o  Repeat ranges

	  o  Nested repeats

				      6-2

			  MACRO AND REPEAT DIRECTIVES



	  o  Nested macro calls

	  o  Conditional macros

	  o  Argument substring selection

     Since macros expand to the complete text sequence when called, you can
     include all MACREL directives in the body of the macro text to control
     assembly of program sections.



     6.1  MACRO DEFINITIONS

     Define a macro by following the .MACRO directive with the name of  the
     macro,   any  dummy  arguments  that  are  needed,  the  text,  and  a
     terminator.  The text is the source  code  that  you  want  MACREL  to
     assemble  at the point in the program where you insert the macro call.
     You can include dummy arguments in the macro to indicate that you want
     to pass actual arguments at calling time.



     6.1.1  .MACRO and .ENDM Directives

     The .MACRO directive is the first item in  the  macro  definition  and
     always  begins  the  first  line of the macro.  The second line of the
     definition, and as many lines thereafter as are needed, is  the  text,
     or  body, of the macro.  The final line of the macro definition is the
     macro terminator.

     The form of the macro definition is:

	  .MACRO name [arg,...] [/comments]
	  text
	  text
	  .
	  .
	  .
	  text
	  .ENDM name

     where:

	  .MACRO	      is the macro directive

	  name		      is the name you choose to identify the macro.
			      Any  unique  legal  symbol up to six printing
			      characters (excluding permanent symbols)  may
			      be  used.   The  macro name is separated from
			      the dummy arguments, if any are used, by  any
			      sequence of spaces or tabs.


				      6-3

			  MACRO AND REPEAT DIRECTIVES


	  arg,		      is a dummy argument.  You can use  from  zero
			      to  eight legal symbols as dummy arguments to
			      be replaced at  call  time  with  the  actual
			      arguments   passed   with  the  call.   These
			      symbols can appear elsewhere in  the  program
			      without  conflict  of definition.  If you use
			      more  than  one   dummy   argument   in   the
			      definition  you  must  separate  them  with a
			      legal separator, such as a comma,  space,  or
			      tab.  The dummy arguments are optional;  many
			      small macros will not require them.

	  /comments	      is a string of text that you can  include  as
			      comments   after  the  last  dummy  argument.
			      Always start a comment with a slash (/).

	  text		      is the text that will  be  assembled  in  the
	  text		      program  each  time  the  macro expands.  The
	  .		      macro expands whenever you call it by name.
	  .
	  .
	  text

	  .ENDM [name]	      The   .ENDM    directive    terminates    the
			      definition.     The    assembler    continues
			      processing   the    code    following    this
			      terminator.

			      Using  the  macro  name   after   the   .ENDM
			      directive  is  optional but is recommended to
			      help you keep track of which macro  is  being
			      terminated.   The  name  you  use must be the
			      name you used in  the  .MACRO  directive that
			      begins the definition.

     Each macro definition must precede any use (call) of the macro in the
     source  module.   It  is  usually  good  practice  to group all macro
     definitions at the start of the source module in which they are used.

     The following is an example  of  a  macro  definition.   It  uses  the
     routine  that  multiplies  two  numbers (used at the beginning of this
     chapter).

	  .MACRO	 CHORD   A,B
	  CLA CLL
	  TAD	   A
	  CIA
	  DCA	   SIGMA
	  TAD	   B
	  ISZ	   SIGMA
	  JMP	   .-2
	  DCA	   VERSE
	  .ENDM	   CHORD


				      6-4

			  MACRO AND REPEAT DIRECTIVES


     The name of this macro is CHORD and its dummy arguments are A  and  B.
     When CHORD is called, it expands as shown in Figure 6-2.

     Figure 6-1 illustrates macro  definition  and  storage.   It  shows  a
     simplified  line  diagram of the process used by the MACREL assembler,
     when the macro is defined.  The macro is defined at the start of  each
     assembly pass.

     This scanning is indicated in the figure  by  the  top  block  in  the
     source  module  column.   The  assembler  scans  each line and defines
     symbols.  When the .MACRO directive is the first item in  a  statement
     line,  the  assembler  defines  the macro name in the symbol table and
     then transfers control to the macro processor, a software component of
     the  complete  MACREL  assembler.   The macro processor now stores the
     text following the directive in macro space, which  is  a  section  of
     resident  memory  reserved  for  the storage of current assembly macro
     definitions.  In the above example, the macro processor stores all the
     text  after the name CHORD up to the .ENDM terminator.  When the macro
     processor scans the .ENDM directive, control  returns  to  the  MACREL
     assembler and macro storage ceases.  The .ENDM directive instructs the
     assembler to return to  scanning  statement  lines  and  continue  the
     assembly.   The  body  of the macro stored in the macro space is still
     text at this time;  that is, it is unassembled ASCII characters.   The
     text  will  not be interpreted as instructions or data until the macro
     is called.

     ----------------------------------------------------------------------
     |				   ASSEMBLER				  |
     |				   SCAN (Pass One)			  |			     __________
     |			     |						  |
     |	    -----------------|---					  |
     |      | SOURCE	     V	|					  |			     |
     |	    | MODULE	     |	|					  |
     |	    |		     |	|					  |
     |	    |		     |	|					  |
     |	    |		     V	|					  |			     |
     |	    |----------------|--|	      ...................	  |
     |	    | MACRO	     |--------------->|			|	  |
     |	    | DEFINITION	|	      |   Definition    |	  |
     |	    |			|	      | stored in MACRO	|	  |
     |	    |			|	      |	 SPACE for use	|	  |
     |	    |			|	      |	  at call time	|	  |
     |	    |		     |<---------------|			|	  |
     |	    |-------------------|	      |.................|	  |
     |	    | MODULE	     V	|					  |			     |
     |	    | CONTINUES	     |	|					  |
     |	    |		     |	|					  |
     |	    |		     |	|					  |
     |	    |		     V	|					  |			     |
     |	    ---------------------					  |
     |									  |
     ----------------------------------------------------------------------

		   Figure 6-1  Macro Definition and Storage

				      6-5

			  MACRO AND REPEAT DIRECTIVES


     6.2  MACRO CALLS

     You can call a macro by entering the name of the macro along with  the
     actual arguments to be used at the point in the program where you want
     MACREL to expand the code.

     The form of the macro call is:

	  name [argl,...,arg8]

     where:

	  name		 is the name that you  assign  to  the  macro  when
			 defining it.

	  argl,...,arg8  are the actual arguments that  replace  the  dummy
			 arguments  used  in the definition.  These are the
			 arguments that are evaluated in the macro when the
			 macro code is assembled.

     If, in the previous example, the number 40 is to be multiplied by  26,
     the call to the macro would be:

	  CHORD  (26, (40

     CHORD is the name of the macro, and the two actual arguments  are  (26
     and (40.

     During assembly, MACREL recognizes the call  and  expands  the  macro.
     The  assembler  scans  each  statement  line  and, while continuing to
     define symbols, looks up already defined symbols in the symbol  table,
     interprets  the  statements,  and generates the object code.  When the
     assembler reads a macro call, control transfers to the macro processor
     which  then suspends assembly, reads the macro text into the main line
     of the program section, and assembles  the  text  to  generate  object
     code.

     This transfer is shown in the simplified line diagram in Figure 6-2 in
     which  the  macro call CHORD with the arguments (26 and (40 is read by
     the assembler, processed by the macro processor, and expanded into the
     complete macro as defined.  Note that the actual arguments (26 and (40
     replace the dummy arguments A and B and that the expanded macro,  with
     all  of  its instructions, is placed in the source module at the point
     of the call.  The locations following  the  call  (labeled  SIGMA  and
     VERSE) now follow the expanded macro.  This expansion takes place each
     time the macro is called and if, each time it is called, the real  (or
     actual)  arguments  are  new,  the  macro  expands  with new arguments
     replacing the dummy arguments in each call.







				      6-6

			  MACRO AND REPEAT DIRECTIVES


     ----------------------------------------------------------------------
     |							source module	  |
     |		original				as seen by MACREL |
     |							assembler	  |
     |		source						.	  |
     |								.	  |
     |		module						.	  |
     |		  .				     -------------------- |
     |		  .				     |  CLA CLL		| |	
     |		  .				     |			| |
     |		  .				     |  TAD	(26	| |
     |		  .				     |			| |
     |		  .				     |  CIA		| |
     |		  .				     |			| |
     |		  .				     |  DCA	SIGMA	| |
     |	   ..................			     |			| |
     |	   | CHORD (26, (40 |--- macro processor --->|	TAD	(40	| |
     |	   ..................			     |			| |
     |	SIGMA, 0000				     |	ISZ	SIGMA	| |
     |						     |			| |
     |	VERSE, 0000				     |  JMP	.-2	| |
     |						     |			| |
     |						     |  DCA	VERSE	| |
     |						     -------------------- |
     |						  SIGMA, 0000		  |
     |									  |
     |						  VERSE, 0000		  |
     ----------------------------------------------------------------------

			  Figure 6-2  Macro Expansion



     6.3  MACRO ARGUMENTS

     A macro definition may contain from zero  to  eight  dummy  arguments.
     The  call to a macro may pass up to eight associated actual arguments.
     There is a strict positional relationship between the dummy  arguments
     and  the  actual  arguments.   The  first actual argument replaces the
     first dummy argument, the second replaces the second and so on.   This
     positional  relationship  continues  for  all  of the actual arguments
     passed to the macro.  If, when calling the macro,  you  wish  to  pass
     fewer  actual  arguments  than  the  definition  requires,  the  macro
     processor will interpret as null arguments any comma that occupies the
     position of a dummy argument in the definition.



     6.3.1  Actual Arguments

     From zero to eight actual arguments may be passed to a  macro.   These
     actual  arguments  are text strings that are separated from each other
     by either, (1) tabs and/or spaces or (2) a comma.  The  comma  may  be
     surrounded by spaces or tabs.

				      6-7

			  MACRO AND REPEAT DIRECTIVES


     The first actual argument is separated from  the  macro  name  by  any
     number of spaces or tabs.  For example,

	  MACNAM    A,B,C,D

     or to improve readability,

	  MACNAM  A ,  B ,  C ,  D

     or you can eliminate the commas to give the appearance  of  a  machine
     instruction with operands.  For example,

	  DSZ  I  A

     might be a call to a macro with two arguments.

     Each actual argument is pure text and may contain any character except
     comma or space.  For example,

	  BAR NONE, A, >

     is a macro call with three arguments, NONE , A , and >.

     If  you  use  a  macro  call  to  end  a  conditional  statement,  the
     terminating  right  angle  bracket  of  the conditional statement must
     appear on the next line.  For example,

	  .IF DF X < BAR NONE,A>

     includes a macro call with the actual arguments "NONE" and "A>"

     But

	  .IF  .DF X <
		     BAR NONE A
			       >

     has the two actual arguments NONE and A.

     If spaces, tabs, or commas are to appear in  a  actual  argument,  you
     must enclose them in double quotes (").  For example,

	  STAN A,B

     is a macro call with the two arguments A and B, whereas,

	  STAN "A,B"

     has only one actual argument, the three character string (A,B).

     If you want to use a double quote as  part  of  the  actual  argument,
     insert two double quotes.  Thus,

	  TYPE "HE SAID ""HELLO"" TO THE MAN."

				      6-8

			  MACRO AND REPEAT DIRECTIVES


     has as its actual argument the character string:

	  HE SAID "HELLO" TO THE MAN.

     You can also use a  pair  of  angle  brackets  to  enclose  an  actual
     argument.  For example:

	  TYPE <HE SAID "HELLO" TO THE MAN>

     An actual argument that begins with a left angle  bracket  extends  to
     the  matching  right angle bracket.  If angle brackets are used within
     the text string they must be paired.

     An actual argument may begin with a backslash (\).  The term following
     the  backslash  is  evaluated  by MACREL and the representation of the
     resulting value (in the current  radix,  and  without  leading  zeros)
     becomes the actual argument.  For example in the call:

	  MACIN  A, \CLA , B

     the second argument is the four-character string 7200.

     If there are  more  actual  arguments  than  are  specified  by  dummy
     arguments,  the  excess  actual  arguments  are ignored.  If there are
     fewer actual arguments than dummy arguments, MACREL assumes that  each
     unspecified actual argument that remains is a null string.



     6.3.2  Substrings of the Argument

     You can define macros that use  substrings  of  the  actual  arguments
     passed.

     The form is:

	  dummy argument  [low:high]

     where:

	  dummy argument is the name of the dummy  argument  in  the  macro
			 definition  for  which you wish to use a substring
			 of the actual argument.

	  [		 delimits the beginning of the range specification.

	  low		 is an expression value that specifies the  ordinal
			 position  of  the first character that you want in
			 the substring.

	  :		 separates the low value from the high value.

	  high		 is an expression value that specifies the  ordinal
			 position  of  the  last character that you want in

				      6-9

			  MACRO AND REPEAT DIRECTIVES


			 the  substring.   If  the  value  is   zero,   all
			 characters  to the end of the argument string will
			 be accepted.  If you do not specify  a  value  for
			 high, the value of low is assumed.

	  ]		 delimits the end of the range specification.

     Both high and low may be  either  variables  or  expressions.   MACREL
     evaluates  variables when the macro expands.  It evaluates expressions
     at macro definition time.  To allow MACREL  to  differentiate  between
     the two, you must begin an expression with a digit.  For example:

	  DARG[0+FOO-BAR:0+BAR-FOO]

     In a macro with A as a dummy argument, any  occurrence  of  A  in  the
     definition  expands  to  the actual argument when the macro is called.
     But if, in the text of the definition, the dummy argument is  followed
     by  a  left  square  bracket,  only  selected characters in the actual
     argument are used.  For example, A[3]  expands  with  only  the  third
     character  of  the  actual  argument;   A[3:6]  expands with the third
     through the sixth characters of the actual argument.  For example:

	  .MACRO CLEAR R,E,G
	  .IF IDN    R[1],$<CLA CLL>
	  .ENDM CLEAR

     The macro expands when called.  If the first character in  the  actual
     argument passed is a dollar sign ($), the code CLA CLL is assembled.

     The  following  example   illustrates   the   utility   of   substring
     specification.

	  .MACRO PRINT V
	  TEXT " THEE LOVES V[1:N]"
	  .ENDM PRINT

     In this example, you supply a value to N inside the brackets, and call
     the macro

	  N=4
	  PRINT HEROS

     The result is that four  of  the  five  characters  (i.e.   HERO)  are
     accepted as the actual argument.



     6.3.2.1  .NCHAR Special Operator - The .NCHAR special operator returns
     a  12-bit  expression   value  that is the number of characters in the
     string identified by its argument.  .NCHAR must  always  be  the  last
     element in the expression.

     The form of the operator is:


				     6-10

			  MACRO AND REPEAT DIRECTIVES


	  .NCHAR erg

     where:

	  erg		 is any text string.


     You can define a macro to use a substring of the argument depending on
     the number of characters passed in the actual argument.  For example:

	  .MACRO PRINT A
	  L=.NCHAR A
	  IF EQ L-4<
	  .DISABL FILL
	  TEXT "THEE LOVES A[1:4]
	  .ENABLE FILL
	  >
	  .ENDM PRINT



     6.3.3  Symbols and Names in Macros

     You must exercise care when choosing macro names, dummy arguments, and
     actual  arguments.  In most situations common sense and a knowledge of
     assembly language are reliable guides.  For example:

	  .MACRO INSTR X,Y
	  X!Y
	  .ENDM INSTR

     The call to the macro is:

	  INSTR CLA,CLL

     In this call, machine instructions are passed   as  actual  arguments.
     While  using a macro may not be an efficient way to clear the link and
     accumulator there is nothing wrong with the call.   However,  if  some
     other  instructions,  say TAD and JMP, are used in the call, something
     else will happen.  For example:

	  INSTR TAD,JMP

     Now, because of the  exclamation  point  (!)  operator  in  the  macro
     definition,  MACREL  does an inclusive OR of the instructions, and the
     object code that results makes no sense.

     Macros expand  with  actual  arguments  exactly  replacing  the  dummy
     argument.   It  is  your  responsibility  to  assure  that  the actual
     arguments,  when  expanded,  are  legal  within  the  sense   of   the
     definition.   Actual  arguments  may  include  any  printing character
     except comma,  space,  and  tab.   They  can  be  included  in  quoted
     arguments (see Section 6.3.4).


				     6-11

			  MACRO AND REPEAT DIRECTIVES


     Dummy arguments are replaced when the macro expands so you can use any
     legal  symbol  as  a  dummy  argument.   Each macro is itself unique,
     therefore, the repeated use of the same symbol as a dummy argument in
     other macros creates no conflict.  When choosing names for macros you
     cannot use any symbol in the permanent symbol table as a macro name.
     For example:

	  .MACRO  JMP    K,L,H
	  ISZ     K
	  JMP     L
	  JMP     H
	  .ENDM   JMP

     Conceptually, the name JMP is appropriate as the name of a macro  that
     jumps to some selected location.  When the macro is called:

	  JMP    A+1,FOX,TABLE

     MACREL does not know if the word JMP is a  machine  instruction  or  a
     macro call.

     The Permanent symbol JMP could be expunged first or the macro could be
     named JUMP and be defined in the same way.  The call then becomes:

	  JUMP  A+1,FOX,TABLE

     and without conflict, the macro expands to:

	  ISZ A+1
	  JMP FOX
	  JMP TABLE

     This call retains the descriptive macro  name  but  prevents  assembly
     errors.

     Long or complex macro definitions sometime require labels, or tags, to
     identify  specific locations within them.  You can use the same labels
     in different macros, so long as you  create  unique  labels  for  each
     expansion (see Section 4.2.4).



     6.3.4  Apostrophe (') Special Operator

     The apostrophe is a special operator in the  macro  definition.   When
     you use it between two or more dummy arguments in the body of a macro,
     the apostrophe causes the concatenation of the  arguments.   Thus  the
     apostrophe  combines the two dummy arguments and their actual argument
     replacements into a single character string.

     The macro is written in the standard manner, with the  directive,  the
     name, and the dummy arguments.  Concatenation is indicated in the body
     of the macro.  For example:


				     6-12

			  MACRO AND REPEAT DIRECTIVES


	  .MACRO CONCAT A,B    /defines a macro which concatenates
	  A'B		       /the two symbols A and B into one
	  .ENDM CONCAT	       /symbol AB

     The macro definition,

	  .MACRO  ZEB TABLE,SUB
	  TAD	  TABLE'SUB
	  .ENDM . ZED
		.
		.
		.

     when called,

	  ZED	 DATA, X

     expands to,

	  TAD,   DATAX

     which at run time adds to the accumulator the data located at address
     DATAX.

     Use the apostrophe (') only  inside  a  macro  definition  immediately
     following  a  symbol  name.   (A'B  is  legal even if A is not a dummy
     argument.) When used in this manner the apostrophe is  not  stored  in
     macro  space.  Any other use of the apostrophe inside a macro will not
     cause concatenation and it is stored in macro space as an  apostrophe.
     Thus, if a macro includes the code,

	  TAD ('PQ)

     the apostrophe does not concatenate (it does not follow a symbol)  and
     it  is  stored  in  macro space for creation of a two character, 6-bit
     literal at expansion time.



     6.4  NESTED MACROS

     This section discusses nesting of macro definitions and  macro  calls.
     It  also  covers  the  .MEXIT  directive  and  concatenation in nested
     macros.



     6.4.1  Nested Macro Definitions

     You can nest macro definitions to no  more  than  eight  levels.   The
     actual  level  is  determined by the complexity of the macros.  Macros
     defined with  the  .INCLUDE  or  .CHAIN  directives  as  part  of  the
     definition  restrict  the  depth  to  which  the macros may be nested.
     Because  the  .INCLUDE  directive  can  itself be nested, the depth is

				     6-13

			  MACRO AND REPEAT DIRECTIVES


     further restricted by each level of nesting in the .INCLUDE directive.
     If,  for  instance,  you  nest  one  macro  definition  containing the
     .INCLUDE directive, and it contains another nested .INCLUDE, the total
     depth  is  three nests.  The first nest for the macro, the second nest
     for the first .INCLUDE and the third for the nested .INCLUDE.  Most of
     the macro definitions you write will not be complex enough, or contain
     enough nests to exceed the capacity of macro space  or  of  the  macro
     nesting stack.  For example:

	  .MACRO SETCLA	   /define a macro SETCLA with no argument
	  .MACRO INSTR	   /define a second macro INSTR nested
			   /within, SETCLA
	  CLA		   /the single instruction CLA which is
			   /the complete definition of the macro
			   /named INSTR
	  .ENDM INSTR	   /end second Level macro INSTR
	  .ENDM SETCLA	   /end first level macro, SETCLA

     The macro call,

	  SETCLA

     expands to:

	  .MACRO INSTR
	  CLA
	  .ENDM INSTR

     which is the expansion of the first level macro

     In other words, the program now includes a macro definition  with  the
     name INSTR.  When you call the macro,

	  INSTR

     it expands to the single instruction:

	  CLA

     which is the expansion of the second level macro.



     6.4.2  Nested Macro Calls

     You can nest macro calls in a way that is similar to  the  nesting  of
     macro definitions.  For example:

	  .MACRO  TOP    RED
	  BOTTOM  RED
	  .ENDM   TOP
	     .
	     .
	     .

				     6-14

			  MACRO AND REPEAT DIRECTIVES


	  .MACRO BOTTOM  HED
	  TEXT "HED"
	  .ENDM   BOTTOM

     The macro TOP contains a call  to  the  macro  BOTTOM;   when  TOP  is
     called:

	  TOP    STRING

     This is the macro call with the actual argument STRING.

     It expands to:

	  BOTTOM STRING

     The actual argument STRING replaces the dummy argument RED in the  top
     macro  but  the  word BOTTOM is, itself, a macro call.  It now has the
     actual argument STRING and it expands to:

	  TEXT   "STRING"

     The expansion with the actual  argument  STRING  replacing  the  dummy
     argument HED of the bottom macro.

     The macro definitions written so far are  terminated  with  the  .ENDM
     directive,  but  the .MEXIT directive, described below, is also useful
     in some macros using the conditional assembly directives.



     6.4.3  .MEXIT Directive

     The example of nested macro definitions diagrammed  in  Section  6.4.1
     had  each macro terminated explicitly with the .ENDM directive and the
     name of  the  macro.   The  .ENDM  directive  is  a  MACREL  assembler
     instruction  that  terminates  macro storage and returns MACREL to the
     previous assembly.

     In nested macros,  .ENDM  still  terminates  macro  storage,  but  the
     previous  assembly  is  another  macro  definition.  Therefore, MACREL
     first stops and then returns to storing macros.

     The .MEXIT directive is an assembler directive that  instructs  MACREL
     to stop assembling the macro - not to stop storing it.

     The form of the directive is:

	  .MEXIT

     The directive resides in macro storage space along with the rest of
     the macro text.  When you call the macro, MACREL reads the directive
     as it assembles code.  When .MEXIT is read, MACREL stops assembly of
     the current macro and returns to assembling the previous code, which
     could be a macro at a higher nesting level.

				     6-15

			  MACRO AND REPEAT DIRECTIVES


     The following is an example of .MEXIT in conditional code:

	     .MACRO JUMP A,B
	     MESG B
	     TAD (MESG'A)
	     DCA ADDR$
	     SKP
     ADDR$,  0
	     TYPE
     MONIT,  JMP I (7605)
	     .ENDM JUMP

	     .MACRO MESG B
	     .IF BL B <.MEXIT>
	     TEXT / B /
	     .ENDM MESG

     In the case of nested macros, the final level of the macro  is  always
     terminated  with  the  .ENDM  directive.   You  can use the macro name
     optionally with the .ENDM directive.


     6.4.4  Concatenation in Nested Macros

     When you use the  apostrophe  (')  concatenation  operator  in  nested
     macros,  the  concatenation of the symbols differs from that described
     in Section 6.3.4.  Each  level  of  nested  macro  requires  an  extra
     apostrophe.

     For example, you might wish to use TAD ALPHA'BETA in  a  nested  macro
     named VALUE.  If VALUE is nested to the third level, three apostrophes
     are needed, ALPHA'''BETA.  MACREL interprets one apostrophe  for  each
     level.   A  second level nested macro would require two apostrophes to
     concatenate symbols, a third level nest requires three apostrophes,  a
     fourth level requires four, and so on.



     6.5  CONDITIONAL ASSEMBLY DIRECTIVES IN MACROS

     The conditional assembly directives were discussed in Section 5.5.  In
     Section  6.3  conditional  assembly  was  shown as part of the example
     illustrating selected substrings of arguments.  From  these  examples,
     you  can  understand  that  any  .IF  directive can be used in a macro
     definition.

     Two of the .IF directives (.IF BL and .IF NB) are normally  used  only
     within macro definitions.  You can use them to test the macro call for
     actual non-null arguments.  A conditional block of  source  code  with
     the  .IF  BL  directive  is  assembled  if a specified argument is not
     passed with the call.  The .IF  NB  directive  allows  assembly  if  a
     specified argument is passed.



				     6-16

			  MACRO AND REPEAT DIRECTIVES


     In the following example, a macro named  CHANGE  calls  another  macro
     named  JUMP with different actual arguments being passed, depending on
     whether or not a non-null argument has been passed to CHANGE.

	     .MACRO CHANGE XYZ

	     .IF BL XYZ<JUMP 1
			     .MEXIT>

	     .IF NB XYZ<JUMP 2
			     .MEXIT>
	     .ENDM CHANGE

     Only the two directives .IF BL and .IF NB are used  in  this  example,
     but all of the other conditionals are legal.  For example, if you have
     to determine if the symbol  NEWAVG  is  defined,  you  could  use  the
     following:

	  .IF DF NEWAVG <.......>

     or, if you wanted to determine if NEWAVG is both defined and equal  to
     some other value, you could use the following:

	  .IF BD NEWAVG    <.IF  EQ  NEWAVG-OLDAVG<......>>

     The next example shows how you can write both of the conditionals as a
     macro:

	  .MACRO SCRTCH

	  .IF DF NEWAVG<

		  .IF EQ NEWAVG-OLDAVG<TAD NEWAVG

		  .MEXIT >>
		  .TAD OLDAVG
		  .ENDM SCRTCH

     When you use a conditional statement in a macro definition, the  first
     left  angle  bracket (<) that encloses the conditional code must be on
     the same line as the .IF directive.  The right angle bracket (>)  must
     be  on the last line that contains conditional code.  This is shown in
     the example above.



     6.5.1  Nested Conditional Source Code in Macros

     Nesting conditional statements in  macros  simplifies  the  coding  of
     complex  program  sections.  The macro CHANGE shown above is rewritten
     in Figure 6-3 to show how you can use  nested  conditional  macros  to
     determine  if  arguments  have  been passed to it and if so, how many.
     The example uses the special  operator  .NARGS  described  in  Section


				     6-17

			  MACRO AND REPEAT DIRECTIVES


     6.5.2,  which  returns  the  number of arguments passed with the macro
     call.

	     .MACRO CHANGE A,B,C

	     X=.NARGS	     /FIND OUT HOW MANY ARGUMENTS PASSED

	     .IF EQ X<JUMP 0	     /IF NONE CALL JUMP AND PRINT
			     .MEXIT>	      /FIRST MESSAGE

	     .IF NE X<X=X-1		      /IF ANY SUBTRACT 1 AND CHECK
		     .IF EQ X<JUMP 1	      /FOR ZERO -CALL JUMP -PRINT
				     .MEXIT>>	      /MESSAGE AND EXIT

	     X=X-1				      /TRY AGAIN

	     .IF EQ X<JUMP 2
			     .MEXIT>

	     X=X-1				     /AND AGAIN

	     .IF EQ X<JUMP 3
			     .MEXIT>

	     .IF NE X<JUMP 4			     /IF STILL ARGUMENTS
			     .MEXIT>		     /PRINT DUMMY MESSAGE
	     .ENDM CHANGE			     /AND EXIT
	     .MACRO MESG B
	     TEXT "B"
	     .ENDM MESG

	     .MACRO JUMP A   /THIS MACRO CONCATENATES THE ACTUAL ARGUMENT
			     /WITH MESG STORES THE ADDRESS OF MESG AND
			     /THEN CALLS THE MACRO TYPE TO COMPLETE THE
			     /ROUTINE.
	     TAD     (MESG'A)
	     DCA     ADDR$
	     SKP
     ADDR$:  0
	     TYPE	     /  THE CALL TO THE MACRO TYPE
     MONIT,  JMP I   (7605)
	     .ENDM JUMP
     /THIS IS A MACRO TO TYPE A STRING OF CHARACTERS ON A SINGLE LINE AT
     /THE TERMINAL.THE ACCUMULATOR HOLDS THE ADDRESS OF THE CHARACTER
     /STRING (FROM DCA ADDR$ IN THE MACRO JUMP) WHICH MUST BE IN THE
     /CURRENT FIELD.AT THE COMPLETION OF THE MACRO THE ACCUMULATOR EQUALS
     /0000.THE STRING FORMAT IS 6-BIT ASCII CHARACTERS TERMINATED BY NULL
     /(00) WHERE THE FIRST CHARACTER IS THE LEFT HALF OF A 12-BIT WORD.
     /***   NOTE   ***   WILL NOT PRINT CR OR LF CHARACTERS   ***

        Figure 6-3  Example of Nested Conditional Source Code in Macros




				     6-18

			  MACRO AND REPEAT DIRECTIVES


	     .MACRO  TYPE
	     CLL	     /START WITH LEFT HALF
     LOOP$:  TAD I  ADDR$    /GET WORD FROM STRING
	      SNL	     /LINK INDICATES HALF
	      BSW	     /LEFT HALF
	      AND   (77)     /MASK SIX BIT BYTE	       0-37    40-77
	      SNA	     /IS IT NULL
	      JMP   MONIT    /YES/ RETURN TO MONITOR
	      TAD   (240)    /NO -CONVERT TO ASCII   240-277   300-337
	      AND   (77)			      40-77	 0-37
	      TAD   (240)			     300-337   240-277
	      TLS	     /SEND TO TERMINAL
	      TSF	     /WAIT UNTIL PRINTED
              JMP   .-1
	      CML	     /SWITCH TO OTHER HALF
	      SNL CLA	     /IS IT LEFT HALF
	      ISZ   ADDR$    /YES-NEXT WORD
	      JMP   LOOP$    /NO-SAME WORD
	     .ENDM TYPE


     .RSECT  CONDIT
	     .LIST ME
	     CHANGE

     .DSECT ERRMSG
     MESG0,  MESG "NO ARGUMENTS PASSED"
     MESG1,  MESG "ONE ARGUMENT PASSED"
     MESG2,  MESG "TWO ARGUMENTS PASSED"
     MESG3,  MESG "THREE ARGUMENTS PASSED"
     MESG4,  MESG "TOO MANY ARGUMENTS PASSED ,DUMMY"

     Figure 6-3 (cont.) Example of Nested Conditional Source Code in Macros



     6.5.2  .NARGS Special Operator

     The .NARGS special operator returns a 12-bit value that is the  number
     of  actual  arguments  passed in a macro call.  This operator is legal
     only when used in a macro definition.  In Figure 6-3, the symbol X  is
     directly assigned the quantity returned by .NARGS, that is, the number
     of arguments  passed.   This  count  includes  specified  null  actual
     arguments.



     6.6  DEFINING AND CALLING REPEAT BLOCKS

     MACREL provides a special directive that  lets  you  repeat  the  same
     sequence of code a number of times.  The repeat block defined with the
     .REPT directive expands immediately and the code is repeated  as  many
     times as called for by the argument of the directive.


				     6-19

			  MACRO AND REPEAT DIRECTIVES


     6.6.1  .REPT and .ENDR Directives

     The general form of the repeat directive includes the  directive,  the
     argument  to  the  macro, and, on the next line, the body (or text) of
     the  directive.   The  repeat  block  is  terminated  with  the  .ENDR
     directive.

     The form of the directives is:

	  .REPT   argument
	  text
	    .
	    .
	    .
	    .
	  text
	  .ENDR

     where:

	  .REPT	      is an assembly directive informing the assembler that
		      the following code is to be repeated.

          argument    is the number of times the code is  to  be  repeated.
		      The argument may be any expression value in the range
		      of 0 to 7777 (octal).

	  text
	    .	      is the body of the macro that is to be repeated, this
	    .	      is  stored  as text  in  the  symbol  table  and is
	    .	      expanded as written.
            .
	  text

	  .ENDR	      is the terminating directive of the repeat macro.  It
		      halts  the  storage  of  text  in  the  symbol table.
		      Processing  of  the  program   continues   with   the
		      statement  line  following  the .ENDR directive.  All
		      repeat blocks  must  be  terminated  with  the  .ENDR
		      directive.

	  For example:

		      A=3

		      TAD COUNT

		      CIA

		      .REPT A

		      IAC

		      .ENDR

				     6-20

			  MACRO AND REPEAT DIRECTIVES


		      DCA NOACC

     When MACREL expands this macro, it repeats the instruction IAC as many
     times as specified by the current value of A.  If the value of A is 3,
     IAC will occur three times as shown below:

		 TAD	 COUNT

		 CIA

		 IAC

		 IAC

		 IAC

		 DCA	 NOACC

     Upon execution of the expanded and assembled code, the value of  COUNT
     is  brought  into  the  accumulator, complemented, and incremented and
     then incremented three more times before  being  deposited  in  NOACC.
     Neither  the  .REPT  nor  the  .ENDR directive appears in the expanded
     macro text.   The  text  of  the  repeat  is  stored  in  macro  space
     temporarily and is deleted from these after assembly.



     6.6.2  Nested Repeats

     You can nest repeat blocks to  any  level.   The  only  limit  is  the
     capacity of the assembler's internal stack.

     The example in Figure 6-4 shows a repeat block with a range  of  three
     nested  inside  a  repeat block with a range of two.  Figure 6-5 shows
     how MACREL expands the nested repeat block.




















				     6-21

			  MACRO AND REPEAT DIRECTIVES


		   ------------------------------------
		   |          .REPT	2	      |
		   |				      |
		   |          RAR		      |  OUTER NEST
		   |				      |
		   |	      IAC		      |
		   |				      |
		   |     --------------------         |
		   |     |	.REPT	3   |  INNER  |
		   |     |		    |	NEST  |
		   |     |	RAL	    |	      |
		   |     |		    |	      |
		   |     |	RTL	    |	      |
		   |     |		    |	      |
		   |     |	.ENDR	    |	      |
		   |     --------------------         |
		   |	      IAC		      |
		   |				      |
		   |	      .ENDR		      |
		   ------------------------------------

	         Figure 6-4  Example of a Nested Repeat Block

































				     6-22

			  MACRO AND REPEAT DIRECTIVES


		   ------------------------------------
		   |         RAR		      |
		   |				      |   1st repeat of
		   |	     IAC		      |   outer nest
		   |				      |
		   |     -----------		      |
		   |     |   RAL   |   1st repeat     |
		   |	 |	   |   of inner	      |
		   |	 |   RTL   |   nest	      |
		   |     -----------		      |
		   |     -----------		      |
		   |     |   RAL   |   2nd repeat     |
		   |	 |	   |   of inner	      |
		   |	 |   RTL   |   nest	      |
		   |     -----------		      |
		   |     -----------		      |
		   |     |   RAL   |   3rd repeat     |
		   |	 |	   |   of inner	      |
		   |	 |   RTL   |   nest	      |
		   |     -----------		      |
		   |         IAC		      |
		   ------------------------------------

		   ------------------------------------
		   |         RAR		      |
		   |				      |   2nd repeat of
		   |	     IAC		      |   outer nest
		   |				      |
		   |     -----------		      |
		   |     |   RAL   |   1st repeat     |
		   |	 |	   |   of inner	      |
		   |	 |   RTL   |   nest	      |
		   |     -----------		      |
		   |     -----------		      |
		   |     |   RAL   |   2nd repeat     |
		   |	 |	   |   of inner	      |
		   |	 |   RTL   |   nest	      |
		   |     -----------		      |
		   |     -----------		      |
		   |     |   RAL   |   3rd repeat     |
		   |	 |	   |   of inner	      |
		   |	 |   RTL   |   nest	      |
		   |     -----------		      |
		   |         IAC		      |
		   ------------------------------------

         Figure 6-5  Example of the Expansion of a Nested Repeat Block


     The .MEXIT directive treats the body of a repeat range as if it were a
     macro body.




				     6-23







				   CHAPTER 7

				  RELOCATION



				     NOTE

		   This chapter is a  logical  continuation
		   of  "Introduction to MACREL Relocation,"
		   Section 1.5 in Chapter 1.  Although that
		   section  was  presented earlier in order
		   to facilitate understanding the rest  of
		   the  manual, it may be considered as the
		   first section of this chapter.  You  may
		   find  it  helpful to review that section
		   before continuing with this chapter.  In
		   addition,    reviewing    "The    MACREL
		   Assembler," Section 1.6 and  "LINK,  the
		   Linking  Loader,"  Section  1.7  will be
		   helpful in understanding  relocation  as
		   discussed in this Chapter.


     You can use the relocation features that MACREL and  LINK  provide  at
     two  levels.   On the first level, you can write a relocatable program
     that is wholly contained in one  source  module.   The  advantages  of
     writing  a  relocatable  rather than an absolute program at this level
     are as follows:

	  1.  LINK performs the job of allocating memory.

	  2.  Programs are loaded  more  efficiently.   For  example,  LINK
	      automatically groups .DSECTS and .FSECTS in an efficient way.

	  3.  If desired, LINK provides an output of a  load  map,  showing
	      where each section is loaded.  This can speed up debugging.

	  4.  The use of segmentation  (grouping  code  that  performs  one
	      function  in  one  program section) makes for clearer, better
	      designed programs which may be easily modified, if necessary.

	  5.  Programs sometimes become larger than  expected,  and  coding
	      programs  as relocatable from the beginning allows them to be
	      easily broken into modules later on.  Also, you may  wish  to
	      employ a routine from a different module later on.

     On a second level, you may wish to write code that employs two or more
     modules  that  communicate with each other.  The additional advantages
     of using this approach are the following:


				      7-1

				  RELOCATION


	  1.  You can work with smaller blocks of  code  so  that  you  can
	      perform  the  whole  process  of  coding, debugging, editing,
	      reassembling, and listing with files of manageable size.

	  2.  LINK performs all operations  of  linking  the  two  modules,
	      therefore  eliminating  another  difficult and time-consuming
	      affair.

	  3.  You can create libraries of  commonly  used  subroutines  and
	      include  them  as  part  of the current program by specifying
	      their file name in the list of input  files  to  LINK.   This
	      eliminates  copying  subroutines  into the source program and
	      makes for smaller source listings.  It  also  simplifies  the
	      problems  of program development as more and more subroutines
	      become written.

	  4.  Overlays may be defined at link time.

	  5.  The added structural advantage  of  defining  specific  entry
	      points  that  are used in communication between modules makes
	      for more logical design of programs.

     The remainder of this chapter discusses the following subjects:

	  o  Program section directives

	  o  Inter-module communication

	  o  Relocatable code

	  o  Overlays



     7.1  THE PROGRAM SECTION DIRECTIVES

     The program section directives allow you to divide your  program  into
     absolute and relocatable parts.  If you do not put any program section
     directives in a program,  MACREL  treats the  program  as  an  unnamed
     absolute  program section (.ASECT) that begins at location 200.  Every
     FIELD directive in a  program  like  this  implicitly  defines  a  new
     unnamed  absolute  program  section.  MACREL assigns a default name to
     each unnamed program section.

     The types of program sections are summarized in  Table  7-1,  and  are
     described  in  more  detail in the paragraphs that follow.  No program
     section may extend across field boundaries (this limits a  section  to
     no  more  than  4095  locations).   A program section extends until it
     reaches the end of the field, until a new program section is  defined,
     or until the source module ends.





				      7-2

				  RELOCATION


				   Table 7-1
			   Types of Program Sections

     ----------------------------------------------------------------------
     | Section	|	 Description	     |    Loading Restriction	  |
     |----------|----------------------------|----------------------------|
     | .ASECT	|  ABSOLUTE      SECTION-    |  Extends from  its  lowest |
     |		|  Where  code   or  data    |  address  to  its  highest |
     |		|  must  be  located   at    |  address, inclusive.	  |
     |		|  specific addresses.       |				  |
     |		|			     |  If  no  field   statement |
     |		|			     |  is    specified,    loads |
     |		|			     |  into  field  0,  but  can |
     |		|			     |  not use location 7777.	  |
     |----------|----------------------------|----------------------------|
     | .RSECT	|  RELOCATABLE	  SECTION-   |  May  be  loaded  anywhere |
     |		|  General     programming   |  in memory, except page 0. |
     |		|  use.			     |  Starts  to  load  on  the |
     |		|			     |  beginning of a page.	  |
     |----------|----------------------------|----------------------------|
     | .ZSECT	|  PAGE    ZERO   SECTION-   |  May  be  loaded  anywhere |
     |		|  Used  for any page zero   |  inside     page     zero, |
     |		|  code.   Generally field   |  locations 20-177.	  |
     |		|  restricted  to the same   |				  |
     |		|  field as the .RSECT  to   |				  |
     |		|  which   it  relates  or   |				  |
     |		|  vice versa.		     |				  |
     |----------|----------------------------|----------------------------|
     | .XSECT	|  AUTOINDEX      SECTION-   |	May  be  loaded  anywhere |
     |		|  Used  for   code   that   |	inside  locations  10-17, |
     |		|  employs  the  autoindex   |	the autoindex registers.  |
     |		|  registers.    Generally   |				  |
     |		|  field   restricted   to   |				  |
     |		|  the  same  field as the   |				  |
     |		|  RSECT   to   which   it   |				  |
     |		|  relates or vice versa.    |				  |
     |----------|----------------------------|----------------------------|
     | .DSECT	|  DATA  SECTION- Contains   |	May  be  loaded  anywhere |
     |		|  relocatable data.  (May   |	in  memory.    May   flow |
     |		|  not   be    used    for   |	across pages.		  |
     |		|  instructions).	     |				  |
     |----------|----------------------------|----------------------------|
     | .FSECT	|  FLOATING      SECTION-    |	May  be  loaded  anywhere |
     |		|  Contains  instructions.   |	in      memory       (not |
     |		|  Generally   used    for   |	necessarily  beginning on |
     |		|  short  subroutines,  so   |	page boundary), but  must |
     |		|  that   several  may  be   |	be  wholly located within |
     |		|  loaded  onto  the  same   |	one page.		  |
     |		|  page.		     |				  |
     ----------------------------------------------------------------------





				      7-3

				  RELOCATION


     7.1.1  Unnamed Program Sections

     MACREL treats all source program statements, up to the  first  program
     section  directive  that  it  finds,  as  an  unnamed absolute program
     section (.ASECT).  This allows you to assemble PAL8  programs  without
     inserting  program  section  directives.  MACREL also assumes that all
     statements up to the first FIELD  directive  that  it  finds  will  be
     loaded  starting  at location 200 of field zero.  Upon finding a FIELD
     directive, it terminates  assembly  in  the  current  unnamed  program
     section  and  begins  assembling the code into another unnamed program
     section.

     MACREL assigns a special default name to each unnamed absolute program
     section and inserts this name into the symbol table.

     These names have the form:

	  FLD:n

     where:

	  n    is either the number of  the  field  specified  in  a  FIELD
	       directive  argument,  or  zero,  if  no  FIELD directive was
	       specified.

     MACREL loads page zero literals  that  occur  in  an  unnamed  program
     section in descending order beginning at location 177.



     7.1.2  .ASECT

     The .ASECT directive  defines  an  absolute  (nonrelocatable)  program
     section that is very similar to a PAL8 program.  Inside an .ASECT, you
     can define code that loads into the autoindex registers,  or  anywhere
     in memory.

     The form directive is:

	  .ASECT name
	       or
	  .SECT name, A

     where:

	  name	    is a legal symbol that identifies this program section.

     For example, an .ASECT named MAIN is specified in the form:

	  .ASECT MAIN
	  *600
	  .

     600 indicates the address at which the program loads.

				      7-4

				  RELOCATION


     If you do not set the current location counter with the  asterisk  (*)
     directive, loading will begin at location 200.



     7.1.3  .RSECT

     The .RSECT directive defines a general  relocatable  program  section.
     LINK will load a program section defined by this directive anywhere in
     memory  except  page  zero.   You  can  specify   additional   loading
     restrictions  by  using  the  FIELD  directive  and  the  PAGE and LOC
     keywords.

     The form of the directive is:

	  .RSECT name
	       or     [,PAGE n] [,LOC=n] [,LEVEL=n] [,OVERLAY=n] [,ROOT]
	  .SECT name R

     where:

	  name	    is the name of a  legal  symbol  that  identifies  this
		    program section.

	  PAGE=n    specifies the memory page where  loading  begins.   The
		    expression  value  n  must be in the range 1-37 and may
		    not be complex relocatable.

	  LOC=n	    specifies the memory  location  where  loading  begins.
		    The expression value n may not be complex relocatable.

	  LEVEL=n   declares that this program section  is  in  an  overlay
		    (see  Section  10.5).   The  value  of the expression n
		    specifies the overlay level and must be  in  the  range
		    0-7.   This  option  allows  you to avoid specifying an
		    overlay level at LINK execution time (see Section 9.1).

	  OVERLAY=n declares that this program section  is  in  an  overlay
		    (see  Section  10.5).   The  value  of the expression n
		    specifies the overlay number and must be in  the  range
		    0-17(octal).    This   option   allows   you  to  avoid
		    specifying an overlay/number  at  LINK  execution  time
		    (see Section 9.1).

	  ROOT	    specifies  that  this  program  section  is  the   main
		    (nonoverlay)   part   of   the  program  (identical  to
		    LEVEL=0).


				     NOTE

		   Do not use the LOC or  PAGE  options  if
		   you use the FIELD directive.


				      7-5

				  RELOCATION


     7.1.4  .ZSECT

     The .ZSECT directive defines a special  relocatable  program  section.
     LINK  will  load  a  program  section defined by a .ZSECT in locations
     20-177 of page zero in any memory field.  You can  specify  additional
     loading restrictions by using the LOC keyword or the FIELD directive.

     The form of the .ZSECT directive is:

	  .ZSECT name
	       or      [,LOC=n] [,LEVEL=n] [,OVERLAY=n] [,ROOT]
	  .SECT name, Z

     where:

	  name	    is a legal symbol that identifies this program section.

	  LOC=n     specifies the memory location within  page  zero  where
		    loading  begins.  The expression value n must be in the
		    range:  20-177, and may not be complex relocatable.  Do
		    not use this option if you use a FIELD directive.

          LEVEL=n   declares that this program section  is  in  an  overlay
		    (see  Section  10.5).   The  value  of the expression n
		    specifies the overlay level and must be  in  the  range
		    0-7.   This  option  allows  you to avoid specifying an
		    overlay level at LINK execution time (see Section 9.1).

          OVERLAY=n declares that this program section  is  in  an  overlay
		    (see  Section  10.5).   The  value  of the expression n
		    specifies the overlay number and must be in  the  range
		    0-17(octal).    This   option   allows   you  to  avoid
		    specifying an overlay/number  at  LINK  execution  time
		    (see Section 9.1).

	  ROOT	    specifies  that  this  program  section  is  the   main
		    (nonoverlay)   part   of   the  program  (identical  to
		    LEVEL=0).

     Since more than one program section may load into page  zero,  if  you
     define  the  loading  address  of  each  as  the same value, they will
     overlay each other.  If you define the  loading  address  of  each  as
     different values, they will load into consecutive locations.  If there
     is insufficient space, LINK will generate an error message.

     All values in a .ZSECT are .FSECT  relocatable  (see  Section  7.1.6).
     Normally,  .ZSECTs  are  used in conjunction with the .RSECTs to which
     they are related.  If only one .RSECT uses a .ZSECT, you may  wish  to
     give  them  both the same name with a Z appended to the .ZSECT's name.
     You would normally restrict them to the same field by  using  a  FIELD
     directive.   If  you know the field they will be loaded, you can use a
     statement in both program sections of the form:

	  FIELD PFIELD

				      7-6

				  RELOCATION


     PFIELD  must  be  a  variable  that  is  defined   in   the   program.
     Alternatively you could code it as:

	  .ZSECT SORTZ
	  FIELD SORT
	  BUFADD,  0
	  NEWV,    0
	  LAST,    0
	  /
	  .RSECT SORT
	  STRT,    CLA
		   TAD Z LAST
		   DCA Z NEWV

     Here, .RSECT SORT is not field restricted;  it can be loaded into  any
     field.   However,  the .ZSECT it references is restricted to load into
     the same field as SORT.  Other sections can reference this  page  zero
     section  as well.  Again, you will want either to restrict them to the
     same field, or to set up the necessary CDF construction to access  the
     .ZSECTs  field.   If you have used many locations on page zero, it may
     be better to restrict the .RSECT, to the field of the .ZSECT.

     Except for naming the .RSECTs and .ZSECTs and performing the necessary
     field   restrictions,   the   techniques  for  programming  page  zero
     references are the same as those in PAL8.

     MACREL automatically creates a special .ZSECT for any program  section
     that  includes  page  zero literals.  MACREL assigns a special name to
     this literal .ZSECT that is the name of the program section  with  the
     page  zero  literals  prefixed  by a dollar sign ($).  For instance an
     .RSECT named SPEC has an associated literal .ZSECT, restricted to  the
     same  field,  named  $SPEC.  MACREL adds the dollar sign to identify a
     literal .ZSECT.

     Within the literal .ZSECT, the literals are allocated from the  bottom
     location  upward.   The  first  page  zero  literal  in .RSECT SPEC is
     located at location zero relative to  $SPEC;   the  second  page  zero
     literal is at $SPEC+1 and so on.

     This normal allocation for literal .ZSECTs  is  reversed  for  unnamed
     .ASECTs  only.   This retains compatibility of the literal allocations
     between MACREL and the PAL8 assembler.



     7.1.5  .XSECT

     The .XSECT directive defines a special  relocatable  program  section.
     LINK  will  load  a  program  section  defined  by  an .XSECT into the
     autoindex registers at locations 10-17 in  page  zero  of  any  memory
     field.   You  can specify additional loading restrictions by using the
     FIELD directive or the LOC keyword.

     The form of the directive is:

				      7-7

				  RELOCATION


	  .XSECT name
	       or      [,LOC=n] [,LEVEL=n] [,OVERLAY=n] [,ROOT]
	  .SECT name, X

     where:

	  name	    is a legal symbol that identifies this program section.

	  LOC=n	    specifies the memory location within  page  zero  where
		    loading  begins.  The expression value n must be in the
		    range:  10-17, and may not be complex relocatable.  You
		    cannot use this option if you use the FIELD directive.

	  LEVEL=n   declares that this program section  is  in  an  overlay
		    (see  Section  10.5).   The  value  of the expression n
		    specifies the overlay level and must be  in  the  range
		    0-7.   This  option  allows  you to avoid specifying an
		    overlay level at LINK execution time (see Section 9.1).

	  OVERLAY=n declares that this program section  is  in  an  overlay
		    (see  Section  10.5).   The  value  of the expression n
		    specifies the overlay number and must be in  the  range
		    0-17(octal).    This   option   allows   you  to  avoid
		    specifying an overlay/number  at  LINK  execution  time
		    (see Section 9.1).

	  ROOT	    specifies  that  this  program  section  is  the   main
		    (nonoverlay)   part   of   the  program  (identical  to
		    LEVEL=0).

     All values in an .XSECT are .FSECT relocatable (see Section 7.1.6).

     The following example shows how two  .RSECTs  reference  two  one-word
     .XSECTs:

	  .XSECT XA1
	  FIELD    0
	  XA1,     0
	  /
	  .RSECT INIT
	  FIELD    0
	  FIRST,   TAD (BUFFER)
		   DCA XA1
		   .
		   .
		   .
	  .XSECT XA2
	  FIELD    0
	  XA2,     0
	  /
	  .RSECT MOVE
	  FIELD    0
		   .
		   .

				      7-8

				  RELOCATION


		   .
		   TAD I XA2
		   SNA
		   JMP DONE
		   DCA I XA1
		   JMP .-4
		   .
		   .
		   .

     The routine moves data from one location to another, and when it reads
     a zero, jumps out of the loop.  The two .XSECTs could also be combined
     into a single one.  Both .XSECTs load somewhere  between  10  and  17,
     inclusive, in field zero as determined by LINK.



     7.1.6  .DSECT

     The .DSECT directive  defines  a  relocatable  program  data  section.
     .DSECTs  are  used  to  store  data.   They  cannot  be  used to store
     instructions, because LINK does not necessarily relocate them to begin
     on  page  boundaries,  and  this would alter the code in unpredictable
     ways.  Although .DSECTs may flow across page boundaries, they may  not
     flow  across  field  boundaries.   You  can specify additional loading
     restrictions by using the FIELD directive or the PAGE or LOC keywords.

     The form of the directive is:

	  .DSECT name
	       or      [,PAGE=n] [,LOC=n] [,LEVEL=n] [,OVERLAY=n] [,ROOT]
	  .SECT name, D

     where:

	  name	    is a legal symbol that identifies the program section.

	  PAGE=n    specifies the memory page where  loading  begins.   The
		    expression  value  n must be in the range 0-37 and must
		    not be complex relocatable.

	  LOC=n	    specifies the memory where loading begins.

	  LEVEL=n   declares that this program section  is  in  an  overlay
		    (see  Section  10.5).   The  value  of the expression n
		    specifies the overlay level and must be  in  the  range
		    0-7.   This  option  allows  you to avoid specifying an
		    overlay level at LINK execution time (see Section 9.1).

	  OVERLAY=n declares that this program section  is  in  an  overlay
		    (see  Section  10.5).   The  value  of the expression n
		    specifies the overlay number and must be in  the  range
		    0-17(octal).    This   option   allows   you  to  avoid


				      7-9

				  RELOCATION


		    specifying an overlay/number  at  LINK  execution  time
		    (see Section 9.1).

	  ROOT	    specifies  that  this  program  section  is  the   main
		    (nonoverlay)   part   of   the  program  (identical  to
		    LEVEL=0).


				     NOTE

		   Do not use the LOC or  PAGE  options  if
		   you use the FIELD directive.


     By defining blocks of data as .DSECTs, you allow LINK to  combine  the
     program sections in an efficient way.  Thus, if you change the size of
     a  table,  and  it  no  longer  fits  in  its  former  location,  LINK
     automatically finds a new spot of the right size.

     The following sample of code shows how you  can  use  a  .DSECT  in  a
     program:

	  .RSECT ERROR
	  FIELD 2
	    .
	    .
	    .
	  TAD COUNT		   /Get the item number in table
	  TAD (TABLE)		   /Get the table starting address
	  DCA TPOINT		   /Store it in a pointer
	  TAD I TPOINT		   /Now set the value at that address
          .DSECT
	  FIELD 2
	  TABLE,    ZBLOCK 100

     The .DSECT can be loaded anywhere in the field without  affecting  its
     capability to store data.



     7.1.7  .FSECT

     The .FSECT directive defines a special  relocatable  program  section.
     LINK  will  load  a  program  section defined by an .FSECT anywhere in
     memory except page 0.  You can specify additional loading restrictions
     by  using  the FIELD directive or the PAGE or LOC keywords.  An .FSECT
     may load anywhere in memory, but must be wholly contained  within  the
     page  in  which it loads.  Thus, if a loading address is specified, it
     must not cause the section to flow across page boundaries.

     The form of the directive is:




				     7-10

				  RELOCATION


	  .FSECT name
		or     [,PAGE=n] [,LEVEL=n] [,OVERLAY=n] [,ROOT]
	  .SECT name, F

     where:

	  name	    is a legal symbol that identifies this program section.

	  PAGE=n    specifies the memory page where  loading  begins.   The
		    expression  value  n  must  be in the range:  0-37, and
		    must not be complex relocatable.  If n is  relocatable,
		    the program section must load into the same page as the
		    relocatable part of n.

	  LEVEL=n   declares that this program  section  is  in an  overlay
		    (see  Section  10.5).   The  value  of the expression n
		    specifies the overlay level and must be  in  the  range
		    0-7.   This  option  allows  you to avoid specifying an
		    overlay level at LINK execution time (see Section 9.1).

          OVERLAY=n declares that this program section  is  in  an  overlay
		    (see  Section  10.5).   The  value  of the expression n
		    specifies the overlay number and must be in  the  range
		    0-17(octal).    This   option   allows   you  to  avoid
		    specifying an overlay/number  at  LINK  execution  time
		    (see Section 9.1).

	  ROOT	    specifies  that  this  program  section  is  the   main
		    (nonoverlay)   part   of   the  program  (identical  to
		    LEVEL=0).


				     NOTE

		   Do not use the LOC or  PAGE  options  if
		   you use the FIELD directive.


     .FSECTs  contain  instructions  and  are  generally  used  for   short
     subroutines  or macros.  Unlike .RSECTs, .FSECTs need not be loaded at
     the beginning of a page thus LINK will combine them onto the same page
     or insert them into available spaces in memory.

     .FSECTs are used primarily to create libraries of  short  subroutines.
     If,  for  example,  you  define  each routine in a floating point math
     package library as an .FSECT, and then reference them  in  a  program,
     LINK automatically loads only the subroutines referenced.  It does not
     load the entire math package.  This saves memory space.

     .FSECTs  employ  a  special  type  of  relocation,  known  as   .FSECT
     relocation.  The following example illustrates this:




				     7-11

				  RELOCATION


	       .FSECT	FPTST
	  0    PTST,	0
	  1		CLA
	  2		TAD A
          3		SZA
	  4		JMP PASS1
	  5		JMP PASS2
	  6    A,	0
			.
			.
			.

     If this program section happened to load at the beginning of  a  page,
     the  TAD  A  instruction  on line 2 would be assembled as 1206;  i.e.,
     two's complement add relative location 06 (the A) on the current page.
     But  if  the  .FSECT  did  not  load  at the beginning of the page and
     instead loaded at location 20 on the  current  page,  location  06  is
     incorrect.   The  address  bits  of the TAD A must be changed, because
     1206  would  address  a   location   entirely   outside   the   .FSECT.
     Consequently,  in relocating an .FSECT, LINK adjusts the 7-bit address
     portion of a  memory  reference  instruction  by  the  amount  of  the
     relocation  relative to the beginning of the page, 20 in this example.
     Thus, the TAD A would be loaded  as  1226.   This  process  is  .FSECT
     relocation.



     7.1.8  Summary of Relocation Performed by LINK

     Table 7-2  summarizes the relocation of different sections.


				   Table 7-2
		     Summary of Program Section Relocation

       ------------------------------------------------------------------
       |  Source Code Line    |	   ASECT    |    RSECT    |    ZSECT    |
       |----------------------|-------------|-------------|-------------|
       |  Absolute expression |	   none	    |    none	  |    none     |
       |  (e.g., 7777 or HLT) |		    |		  |	        |
       |		      |		    |		  |	        |
       |  Memory reference    |	   none	    |    none	  |   "FSECT"   |
       |  instruction:	      |		    |		  | relocation  |
       |  TAD A, where A      |		    |		  |	        |
       |  is on page	      |		    |		  |	        |
       |		      |		    |		  |	        |
       |  12-bit address,     | abs. part + | abs. part + | abs. part + |
       |  pointer	      | reloc. part | reloc. part | reloc. part |
       |		      |		    |		  |	        |
       |  Simply-relocatable  | abs. part + | abs. part + | abs. part + |
       |  expression reloc.   | part reloc. | part reloc. | part reloc. |
       ------------------------------------------------------------------



				     7-12

				  RELOCATION


			       Table 7-2 (Cont.)
		     Summary of Program Section Relocation

       ------------------------------------------------------------------
       |  Source Code Line    |	   XSECT    |	 DSECT	  |    FSECT    |
       |----------------------|-------------|-------------|-------------|
       |  Absolute expression |	   none	    |    none	  |    none     |
       |  (e.g., 7777 or HLT) |		    |		  |	        |
       |		      |		    |		  |	        |
       |  Memory reference    |	  "FSECT"   |	 none	  |   "FSECT"   |
       |  instruction:	      |	relocation  |		  | relocation  |
       |  TAD A, where A      |		    |		  |	        |
       |  is on page	      |		    |		  |	        |
       |		      |		    |		  |	        |
       |  12-bit address,     | abs. part + | abs. part + | abs. part + |
       |  pointer	      | reloc. part | reloc. part | reloc. part |
       |		      |		    |		  |	        |
       |  Simply-relocatable  | abs. part + | abs. part + | abs. part + |
       |  expression reloc.   | part reloc. | part reloc. | part reloc. |
       ------------------------------------------------------------------



     7.1.9  .SECT * Directive

     The .SECT * directive returns program assembly control to the previous
     program  section.   The  directive  is  used  in  the  body of a macro
     definition.  Two SECT * directives in succession are not allowed.

     The form of the directive is:

	  .SECT *

     This directive is particularly useful in macros  that  change  program
     sections to set up data tables.  For example:

	  .MACRO DATA A,B,C
	  .DSECT DATUM
	  *A
	  B
	  TEXT "C"
	  .SECT *
	  .ENDM DATA

     When the macro expands, it changes program section to the .DSECT DATUM
     and  then  sets  the  current location counter to the value of A (*A).
     The macro stores B and the text string  C  and  then  returns  to  the
     program  section (.SECT *) in which the macro was called.  The program
     section that called the macro could be an .RSECT, as shown below.






				     7-13

				  RELOCATION


	  .RSECT CODE
	  TAD (20)
	  DCA TEMP
	  DATA 100,-5, "GOOD"
	  HLT

     Note that the HLT instruction resides in relative location  2  of  the
     .RSECT CODE, not in .DSECT DATUM.



     7.2  INTER-MODULE COMMUNICATION DIRECTIVES AND SPECIAL OPERATORS

     The  preceding  sections  have  discussed  relocatable  programs  that
     consist  of  only  one source module.  This section describes programs
     that contain more than one source module.

     When a program consists of more than one source module,  you  can  use
     the   following   directives   and   special   operators   to  control
     intermodule communication:

	  o  .EXTERNAL

	  o  .ZTERNAL

	  o  .GLOBAL

	  o  .SECREF

	  o  .ENTRY

	  o  CDF and CIF



     7.2.1  .EXTERNAL

     The .EXTERNAL directive declares a symbol as being defined outside the
     current module.

     The form of the directive is:

	  .EXTERNAL sym,...

     where:

	  sym	    is a symbol name.

     If you do not explicitly declare an external symbol, MACREL  generates
     an error message.

     The following examples show how you can use the .EXTERNAL directive.



				     7-14

				  RELOCATION


	  .EXTERNAL EVAL, WPROC
		   .
		   .
		   .
		   TAD TEMP
		   SNA
		   JMS EVAL
		   JMP WPROC

     In this example, the directive causes the program to jump to addresses
     EVAL  and  WPROC in another module.  EVAL and WPROC must be labels and
     be declared with a .ENTRY directive, in the other module.

     You  can  also  use  the  .EXTERNAL  directive  to  declare  a  symbol
     referenced  by  an  AND,  TAD,  ISZ, DCA, JMS or JMP instruction.  For
     example:

	  .EXTERNAL BUFSZE
		   TAD I (BUFSZE)

     MACREL generates a current-page literal that, after linking,  contains
     the  actual memory address of the location BUFSZE (assuming you define
     BUFSZE and declare it as .GLOBAL in another  source  module).   Hence,
     except  for  declaring .EXTERNAL, treat externally defined symbols the
     same way as symbols inside the current module.  You  must  handle  any
     differences   in  field  between  the  two  modules  by  using  a  CDF
     instruction  or  by  field  restricting  the  current  section.    For
     example:

	  .EXTERNAL BUFSZE
	  FIELD BUFSZE
		   TAD I (BUFSZE)



     7.2.2  .ZTERNAL

     The .ZTERNAL directive defines a symbol as being external and  located
     on page zero.

     The form of the directive is:

	  .ZTERNAL sym,...

     where:

	  sym	    is a symbol name.

     .ZTERN is best understood when compared with the .EXTERNAL  directive.
     For example:

	  .EXTERNAL B
		    TAD B


				     7-15

				  RELOCATION


     Here the assembler assumes that B is on a page  other  than  zero  and
     generates a pointer to B.


				     NOTE

		   This pointer is called a link.  This  is
		   an   on-page   pointer  to  an  off-page
		   location, it has nothing to do with  the
		   linking function of MACREL/LINK.


     However, if you have a data item on page zero, do not generate a  link
     and  eliminate  the  advantage  of  having the data item on page zero.
     Consequently, you should use,

	  .ZTERNAL B
		   TAD B

     This instructs the assembler that B, in addition to being external, is
     located on page zero, so it does not generate a link unnecessarily.

     Again, like .EXTERNAL, the symbol must  be  declared  as  .GLOBAL  and
     defined  in  another source module.  Additionally, if the symbol, when
     defined, is not located on page zero, LINK generates an error message.

     An alternative way of eliminating the extraneous link is  to  use  the
     following construction:

	  .EXTERNAL B
		   TAD Z B

     In this example, the special operator Z instructs MACREL that this  is
     a  page  zero  reference.   This  code  performs  the same function as
     .ZTERNAL.  The .EXTERNAL directive, however, must be used,  since  the
     special operator Z itself does not declare the symbol to be external.



     7.2.3  .GLOBAL and ==

     The .GLOBAL directive declares  to  MACREL  and  LINK  that  a  symbol
     defined in the current module may be referenced by other modules.

     The form of the directive is:

	  .GLOBAL sym,...

     where:

	  sym	    is a symbol name.

     For example:


				     7-16

				  RELOCATION


	  .GLOBAL A1, B1
	  A1, 0
	  B1=20

     The code declares A1 and B1 as global  symbols  and  defines  them  as
     well,  A1  through  a  label,  and  B1  through  a  direct  assignment
     statement.

     You can use the double equal signs (==) as an alternate way to declare
     a global symbol and assign it a value.  For example:

	  CSIZE== 7

     This is equivalent to the code:

	  .GLOBAL CSIZE
	  CSIZE=7

     Only one symbol per line may be declared and assigned in this way.

     Declaring a symbol as .GLOBAL when it is not used in  another  program
     is  permissible.  (When coding the program, you might not know whether
     a given symbol will be used by another module or not.) If a symbol  is
     declared as .GLOBAL, however, and is not defined in the current source
     module, MACREL generates an error message.

     In general, labels that you define as .GLOBAL should not  be  used  as
     operands  for JMS or JMP instructions from another module.  You should
     use the directive .ENTRY to define these symbols.



     7.2.4  .SECREF

     The .SECREF (secondary reference) directive defines a  symbol  in  the
     same  way  as  the  .EXTERNAL directive, except that the symbol can be
     undefined at LINK time without causing a library search to resolve it.
     If  LINK  encounters  a  second  reference to the symbol, it will then
     perform a library search for the symbol.

     The form of the directive is:

	  .SECREF sym,...

     where:

	  sym       is a symbol name.



     7.2.5  .ENTRY

     The .ENTRY directive defines an entry point into  the  current  module
     from  another  module.  The directive specifies the symbolic addresses

				     7-17

				  RELOCATION


     to which other modules can transfer program control via a JMP or JMS.

     The form of the directive is:

	  .ENTRY sym,...

     where:

	  sym       is a symbol name.

     For example:

	  .RSECT GETVAL
	  .FIELD   0
	  .ENTRY   GETVAL, STVAL
	  GETVAL,  0
		   CLA
		   TAD OFFSET
		   SZA
		   JMP I GETVAL
	  STVAL,   DCA VAL
		   TAD (-10)
		   .
		   .
		   .

     Here, GETVAL is an entry point for a JMS and STVAL is an  entry  point
     for  a JMP.  GETVAL and STVAL must be declared .EXTERNAL in the source
     module containing the  JMP  and  JMS.   All  symbols  that  have  been
     declared  as  .ENTRY  will  appear as an entry in the load map listing
     produced by LINK (see Section 9.5).

     Internally, MACREL processes .GLOBAL and  .ENTRY  declarations  almost
     identically.   In  fact,  you  can use .GLOBAL declarations instead of
     .ENTRY declarations.  However, a JMS or JMP  to  an  overlay  may  not
     behave correctly if you use the .GLOBAL declaration.  In practice, use
     .ENTRY for all JMS and JMP entries, and .GLOBAL for all others.



     7.2.6  CDF Special Operator

     The CDF special operator described in Section 4.9.4 changes  the  data
     field.   In  programming  inter-module  communication, not knowing the
     field into which LINK will load the current section  and  not  knowing
     the  field of the referenced modules are often problems.  You can find
     the field of the current section with RDF (Read  Data  Field)  or  RIF
     (Read  Instruction  Field)  instructions.  You can find the field of a
     referenced module with the CDF instruction.   For  instance:   If  you
     need  to  get  data from a section named DATA1 in an unknown field use
     CDF DATA1 to change the data-field  register  to  the  field  of  that
     section as shown in the following example:



				     7-18

				  RELOCATION


	  .EXTERNAL DATAl, DATA7
	  CDF DATA1
	  TAD I (DATA7)
	  DCA TEMP
	  CDF .FLD

     Here, the CDF DATA1 changes the data field to the field of DATA1 TAD I
     (DATA7)  gets  the  value  stored in DATA7 (a label inside the program
     section DATA1), DCA TEMP stores it on the current page in the  current
     field.   The  CDF  .FLD (change data field to the field of the current
     program section) returns the program to the current field.

     LINK performs the evaluation of  the  CDF.   When  LINK  processes  a
     program  section  containing  CDF  N  where N is a simple relocatable
     expression, it takes the field of N and OR's it into bits 5-9 of  the
     absolute part 6201 already generated by MACREL.



     7.2.7  CIF Special Operator

     MACREL and LINK handle the CIF special operator in the same  way  that
     they  handle  the  CDF  special operator, except that the field of the
     relocatable part is ORed with 6202 instead of 6201.  CDF and  CIF  may
     be  combined in one expression CIF CDF N, in which case the field of N
     will be ORed with 6203.

     You can JMS to an unknown field by using a CIF.  For example:

	  .EXTERNAL  IN
		   CDF .FLD
		   CIF IN
		   JMS I (IN)
		   .
		   .
		   .

     Here .EXTERNAL defines IN as being in another module.  CDF  .FLD  sets
     the data field to the current field and provides a return path for the
     subroutine IN in the other module.  CIF IN sets the instruction  field
     to  the  same  field  as IN.  (The CIF instruction is effective on the
     first jump instruction that follows it.) The line JMS I (IN) calls the
     subroutine  IN with a 17-bit address (the 12-bit address plus the five
     field bits).

     The subroutine IN in another module might look like this:


	  .RSECT   ALPHA
	  .ENTRY   IN
	  IN,	   0
		   DCA ACTEMP
		   TAD (CIF CDF)
		   RDF

				     7-19

				  RELOCATION


		   DCA EXIT
		   CDF .FLD	   /Optional.  See text.
		   .		   /Subroutine Performs its Processing
		   .
		   .
		   .
	  EXIT,    0
		   JMP I IN

     .RSECT ALPHA names the program section and .ENTRY IN declares IN as an
     entry  point.   IN,  0  contains  the return address for the JMS.  DCA
     ACTEMP saves the value of the accumulator.  TAD (CIF CDF) and the next
     instruction  RDF  load  the  accumulator with 6203 (combined CIF CDF),
     then OR's the field bits of the calling program into  bits  5-9.  This
     complete  instruction  sequence  is  deposited at location EXIT by the
     next line of code DCA EXIT.  In this location the combined instruction
     is  the  last instruction before the subroutine returns to the calling
     program.  The instruction CDF .FLD is necessary only if the subroutine
     performs  some indirect AND, TAD, ISZ, or DCA instruction into its own
     field.

     The subroutine, having done all  its  bookkeeping,  now  performs  its
     intended  processing.   When  this is complete, it JMPs to EXIT.  This
     sets the data field and instruction  field  to  that  of  the  calling
     program.   The  last instruction, JMP I IN, acts like a 17-bit jump to
     the location following the original call.

     If you wish to pass an argument to the subroutine (e.g.,  the  address
     of  data  in  a different field) add two words to the call so that the
     instruction sequence becomes:

	  .EXTERNAL IN, DATA
		   CDF.FLD
		   CIF IN
		   JMS I (IN)
		   CDF DATA
		   DATA
		   .
		   .
		   .

     Here, the CDF DATA stores a preformed CDF instruction, with the  field
     of DATA.  The next line stores the 12-bit address of DATA.

     Somewhere in the subroutine, you might execute the following  code  to
     access the data:

		   .
		   .
		   .
		   TAD I IN
		   DCA DATAF
		   ISZ IN
		   TAD I IN

				     7-20

				  RELOCATION


		   DCA DATAP
		   ISZ IN
	  DATAF,   0
		   TAD I DATAP
		   .
		   .
		   .
	  DATAP,   0
		   .
		   .
		   .

     In this routine, the optional  CDF  .FLD  used  previously  should  be
     omitted because this code requires that the data field register be set
     to the field of the calling program.  The TAD I IN gets the  preformed
     CDF  instruction  from  the  calling  program.  DCA DATAF stores it in
     DATAF, where it will be executed shortly.  ISZ  IN  increments  IN  to
     point  to  the  next  argument.   TAD  I IN and DCA DATAP get the next
     argument, the location of DATA, and store it as  a  pointer.   ISZ  IN
     increments  IN  to  the  correct return address when the subroutine is
     exited.  The program then executes the preformed CDF  at  DATAF,  thus
     changing  the  data  field  to that of DATA.  The TAD I DATAP gets the
     contents of the first word of data, and processing continues.



     7.3  HOW TO WRITE RELOCATABLE CODE

     In general,  all  the  elements  of  relocatable  programs  have  been
     defined.  The rest is a matter of developing the effective techniques.

     You should first create a logical design for the program.  Segments of
     code  that  perform  a  discrete  function  should  reside in the same
     program section, or be coded as  a  separate  source  module.   If you
     choose  the latter, you should determine which symbols are to be known
     by more than one source module.  You should define  these  symbols  as
     .GLOBAL, .ENTRY, .EXTERNAL, or .ZTERNAL.

     Most source code typically consists of .RSECTs.  If page zero code  is
     desired,  you  must specify the necessary .ZSECTs and .XSECTs.  Blocks
     of data may be defined as .DSECTs.  Small subroutines should either be
     grouped together as .RSECTs, or specified individually as .FSECTs.  If
     you have to reference an absolute memory location, make that reference
     to a label defined inside an .ASECT.

     In writing the actual code, make no assumptions about where LINK  will
     load  a  program  section.   Instead specifically define any necessary
     linkage for fields.  If one program section references another, either
     restrict them to the same field, or provide the necessary field change
     linkage (see Sections 7.2.5 and 7.2.6).

     If you reference page zero extensively, you  should  restrict  .XSECTs
     and  .ZSECTs  to load into the same field as the associated .RSECT, or


				     7-21

				  RELOCATION


     you should restrict the .RSECT to load into the .XSECT's  or  .ZSECT's
     field.

     In general, use customary  assembly  language  programming  techniques
     with relocation.  Do avoid using any construction that addresses as an
     absolute location, unless that location is contained within an .ASECT.

     Remember, LINK does not load a program section into a gap  in  another
     program  section.   It also does not load a program section so that it
     extends across field boundaries.  Therefore, no program section may be
     larger than a field.












































				     7-22







				   CHAPTER 8

			     USING MACREL AND KREF


     This  chapter  describes  the  operating  procedures  for  the  MACREL
     assembler  and  the  KREF  cross-reference  utility  program.   Before
     running these programs, be sure that you are using OS/8 Version 3D (or
     a  later version), and that the files MACREL.SV, MACOVR.SV, MACERR.SV,
     and KREF.SV reside on the system device (SYS:).  If you are unfamiliar
     with OS/8 file specifications, refer to the appropriate section of the
     OS/8 Handbook.     _____________



     8.1  RUNNING MACREL


     8.1.1  MACREL Command String

     You can use either the OS/8 Keyboard Monitor R command or the OS/8 CCL
     command  MAC  (described  in  the  OS/8  Handbook)  to  run the MACREL					______________
     assembler.  Enter the following command immediately to  the  right  of
     the  Keyboard  Monitor's  period  (.) prompting symbol to begin MACREL
     operation:

	  .R MACREL (RET)

     OS/8 responds by invoking the Command Decoder which in  turn  displays
     its  asterisk (*) prompting symbol at the left margin of the terminal.
     Respond to the asterisk by entering a MACREL I/O specification  string
     in the form:

	  [binary] [,listing] [,kref]<source,...[/option,...] (RET)

     where:

	  binary    is the output file specification  for  the  relocatable
		    binary  file  of  your assembled program.  This will be
		    the input file to LINK.  The default  device  is  DSK:.
		    The  default  file  name  extension  is .RB.  Omit this
		    specification if you do not want MACREL to create  this
		    file.  (You must, however, enter the comma delimiter if
		    you want a listing or a KREF file.) Omitting this  file
		    causes MACREL to skip pass 2.

	  listing   is the output file  specification  for  the  file  that
		    contains  the  assembly  listing  of your program.  The
		    default  device  is  DSK:.   The  default   file   name
		    extension  is  .LS.   Omit this specification if you do
		    not want  MACREL  to  create  this  file.   (You  must,

				      8-1

			     USING MACREL AND KREF


		    however,  enter  the comma delimiter if you want a KREF
		    file.) Omitting this file causes MACREL to skip pass 3.

	  kref	    is the output file specification  for  the  KREF  file.
		    This is a specially formatted file that serves as input
		    to  the  cross-reference  listing  program  KREF.   The
		    default   device   is  DSK:.   The  default  file  name
		    extension is .KF.  Omit this specification  if  you  do
		    not  want  MACREL  to  create this file.  Omitting this
		    file causes MACREL  to  skip  pass  4  (unless  /C  was
		    specified).

	  <	    is a delimiter.  The Command  Decoder  interprets  file
		    specifications  to  the  left as output files, and file
		    specifications to the right as input files.

	  source    is the input  file  specification  for  your  program's
		    source   file.    You   can   enter  up  to  nine  file
		    specifications for source  files.   Each  specification
		    must  be  separated  from  the  next with a comma.  The
		    default device  for  the  first file  specification  is
		    DSK:.   For  the  remaining  file  specifications,  the
		    default device is the name of the device  contained  in
		    the  preceding  file  specification.   The default file
		    name extension is .MA.

	  /option   is zero or more of the options described in Table  8-1.
		    You can enter them in any order.


				   Table 8-1
			 MACREL Command String Options

     ----------------------------------------------------------------------
     | Option	  |			   Meaning			  |
     |------------|-------------------------------------------------------|
     | /A	  | Delete PDP-8/E instructions.  The  PDP-8/E  has  some |
     |		  | instructions  not  available  on  older PDP-8's.  You |
     |		  | should delete these if your system is not a  PDP-8/E, |
     |		  | /F, /M, /A, or VT78.  This option provides more space |
     |		  | for the symbol table.  (See Appendix C.)		  |
     |------------|-------------------------------------------------------|
     | /B	  | Print the name of the listing file as a block  letter |
     |		  | heading on the first page of the listing.		  |
     |------------|-------------------------------------------------------|
     | /C	  | Chain to the cross-reference listing program  KREF.SV |
     |		  | to  produce  a  cross-reference  listing.  If no kref |
     |		  | file was specified, KREF.TM is  assumed  by  default. |
     |		  | The KREF listing file has the same name as the MACREL |
     |		  | listing  file,  but  the  extension  is  one  greater |
     |		  | (lexicographically).  That is, if the listing file is |
     |		  | FOO.LS, then the kref listing file will be FOO.LT.	  |
     ----------------------------------------------------------------------
						(continued on next page)

				      8-2

			     USING MACREL AND KREF

			       Table 8-1 (Cont.)
			MACREL Command String options
     ----------------------------------------------------------------------
     | Option	  |			   Meaning			  |
     |------------|-------------------------------------------------------|
     | /E	  | Output error message if linkages are generated.	  |
     |------------|-------------------------------------------------------|
     | /G	  | Chain to LINK after assembly and then run the program |
     |		  | after linking.					  |
     |------------|-------------------------------------------------------|
     | /J	  | Do not list conditional code that was not  assembled. |
     |------------|-------------------------------------------------------|
     | /K	  | Include  local  symbols  in  cross-reference   (KREF) |
     |		  | listing.						  |
     |------------|-------------------------------------------------------|
     | /L	  | Chain to LINK after assembly.			  |
     |------------|-------------------------------------------------------|
     | /M	  | Include all permanent symbols in the  cross-reference |
     |		  | symbol table.					  |
     |------------|-------------------------------------------------------|
     | /N	  | List only the symbol table, do not list the assembled |
     |		  | program section (does not override .LIST directive).  |
     |------------|-------------------------------------------------------|
     | /O	  | Omit macro feature.  This provides more space in  the |
     |		  |symbol table for PAL8 programs.			  |
     |------------|-------------------------------------------------------|
     | /P	  | Reset line numbers to 1 for each page in the listing. |
     |------------|-------------------------------------------------------|
     | /Q	  | Add  EAE  symbols.   If  the  computer  includes  the |
     |		  | Extended  Arithmetic Element, these symbols should be |
     |		  | added to the permanent symbol table.   (See  Appendix |
     |		  | C.)							  |
     |------------|-------------------------------------------------------|
     | /R	  | Remove  redundant  (PAL8)   pseudo-operators.    This |
     |		  | provides more symbol table space for programs that do |
     |		  | not use PAL8 pseudo-operators.  (See Appendix C.)	  |
     |------------|-------------------------------------------------------|
     | /S	  | Do not print the symbol table in  the  listing  (does |
     |		  | not override .LIST directive).			  |
     |------------|-------------------------------------------------------|
     | /X	  | Print complete error message  i.e.,  the  two  letter |
     |		  | error code plus the complete descriptive message.	  |
     |------------|-------------------------------------------------------|
     | /Y	  | Eliminate resident overlays.  This causes  MACREL  to |
     |		  | run  slower,  but  provides  additional  symbol table |
     |		  | space.						  |
     |------------|-------------------------------------------------------|
     | /Z	  | Eliminate  BATCH.   If  you  are  not   using   BATCH |
     |		  | facilities  this  option  provides  additional symbol |
     |		  | table space.					  |
     |------------|-------------------------------------------------------|
     | = nnn	  | Set the line  length  of  the  listing.   The  number |
     |		  | replacing nnn must be in octal and less than or equal |
     |		  | to the maximum column width of your printer.	  |
     ----------------------------------------------------------------------

				      8-3

			     USING MACREL AND KREF


     8.1.2  MACREL Command String Examples

	  1.  *TASK<RXA1:TEST

	      This line stores the file TASK.RB  on  DSK:   after  assembly
	      from the file TEST that resides on floppy disk unit 1.

	  2.  *SYS:TEST.RB,TEST.LS<SYS:TEST,MA

	      The listing file TEST.LS is stored on DSK:  and there  is  no
	      print-out of the file.


	  3.  *SYS:TEST.RB,TTY:TEST.LS<SYS:TEST.MA

	      In this example the listing file is printed or  displayed  at
	      the  system  terminal,  but there is no file stored for later
	      retrieval.  If the system terminal is a video terminal, there
	      is no hard-copy of the listing.

	  4.  *SYS:TEST1.RB,LPT:TEST2.LS<SYS:TEST0.MA

	      This time the listing is printed on the line printer  and  no
	      file is stored.

	  5.  *SYS:TEST.RB,TEST1.LS,RKA1:REFER.KF<SYS:MACR5.MA

	      This example assembles a source file named MACR5.MA from  the
	      system  device;   stores a relocatable binary file TEST and a
	      listing file TEST1 on the system device, and creates  a  KREF
	      file REFER that is stored on the second disk RKA1.

	  6.  *SYS:MACT1.RB<TESTl,TEST2

	      MACREL searches DSK:  for both input files with  .MA  as  the
	      extension.

	  7.  *DSK:MACINN.RB,LPT:MACT.LS<SYS:TENT.MA,RXA0:MAHAT.MA,TENT1

	      The relocatable binary file MACINN is output to the disk, and
	      the  listing  file  MACT is printed on the line printer.  The
	      input for MACREL is the file TENT.MA on the system device and
	      the files MAHAT.MA and TENT1, with the default extension .MA,
	      on the floppy disk RXA0.

	  8.  *RKA0:TEST,LPT:<PTR:

	      A program section on paper tape is assembled  and  output  to
	      RKA0:  as TEST.RB.  The program listing is output to the line
	      printer.  The paper tape must be reloaded for each pass.

	  9.  You can use  any  number  of  non-conflicting  options  in  a
	      command string.  For example:


				      8-4

			     USING MACREL AND KREF


		   *SYS:BAT,LPT:BATT<SYS:BUNT.MA/B/E/G/N/O/Q/R/Z=120

	      The source file BUNT with the extension .MA residing  on  the
	      system device is assembled and output on the system device in
	      the file BAT.RB, and the  80  (120(8))  column  line  printer
	      outputs  the  file  BATT.LS with the heading in block letters
	      (/B).  The listing file print-out does not show the assembled
	      program  but  only  the  symbol  table (/N).  As there are no
	      macros in the source, the  /0  option  was  selected  and  /R
	      removes  the redundant directives to gain symbol table space.
	      Similarly, BATCH was eliminated (/Z).  The extra space in the
	      symbol  table  was used to include the EAE instructions.  The
	      /E option conflicts with the /N option and no error  messages
	      are  listed  with  the  /N  option  in force.  Finally the /G
	      option passes the file BAT.RB to LINK and the program is  run
	      after linking.

	  10.  *DSK:TIDE.RB,TTY:TIME.LS<SYS:GRAND.MA/A/B/E/J/L/M/Q/R=110

	      A PDP-8/I with a TTY terminal and  a  single  disk  is  being
	      used.   The file GRAND.MA is assembled and output to the disk
	      in the file TIDE.RB and a listing file TIME.LS is  output  to
	      the TTY.

	      The 72 character length TTY prints a block letter heading  on
	      the  listing  which  includes  the  error  codes but does not
	      include  conditional  code  which  was  not  assembled.   All
	      permanent symbols are cross-referenced.  Redundant directives
	      are removed from the symbol  table.   Because  this  computer
	      system  includes  the  Extended  Arithmetic  Element,  the MQ
	      instructions are added to the symbol table and because it  is
	      not  a PDP-8/E, instructions not available on the PDP-8/I are
	      removed from the symbol table.  Finally, the file is  chained
	      to LINK.



     8.1.3  MACREL Terminal Error Messages

     During assembly, MACREL will send any error messages to the  terminal.
     If  you are using BATCH, and you did not specify the /Z command string
     option, these messages will be sent to  the  BATCH  log  file.   These
     messages  can  be either in an abbreviated form or in an extended form
     depending on whether you select the /X command string option  or  not.
     You  can  also  change the message form by using the run-time commands
     described below.



     8.1.3.1  Run-Time Control Commands - While MACREL is running, you  can
     type commands shown in Table 8-2 to control the way MACREL sends error
     messages to the terminal.  Unless otherwise  specified  below,  MACREL
     will not echo these commands on the terminal.


				      8-5

			     USING MACREL AND KREF


				   Table 8-2
			   Terminal/Control Commands

     ----------------------------------------------------------------------
     |     Command     |		     Meaning			  |
     |-----------------|--------------------------------------------------|
     |	   E	       | Switch to extended form printout		  |
     |-----------------|--------------------------------------------------|
     |	   L	       | Switch to abbreviated form printout		  |
     |-----------------|--------------------------------------------------|
     |	   CTRL/O      | Turn echo off.  This echoes as ^O followed by  a |
     |		       | carriage-return  linefeed.   While  echo is off, |
     |		       | all characters output to the terminal are  lost. |
     |		       | Echo is turned back on by striking any character |
     |		       | other  than  CTRL/O.  (The character struck will |
     |		       | also have its usual effect.)			  |
     |-----------------|--------------------------------------------------|
     |	   CTRL/S      | Enter  hold  screen  mode.   If  a  message  was |
     |		       | printing,  MACREL  stops what it was doing until |
     |		       | you leave this mode.  To leave this  mode,  type |
     |		       | any character other than CTRL/S.  (The character |
     |		       | struck will also have its usual effect.)	  |
     |-----------------|--------------------------------------------------|
     |	   CTRL/C      | Abort assembly and return to OS/8.  An ^C may or |
     |		       | may not be printed.				  |
     ----------------------------------------------------------------------



     8.1.3.2  Default Terminal Conditions - When MACREL begins running,  it
     operates under the following default printout conditions.

	  1.  Abbreviated printout is on.

	  2.  Hold-screen mode is off.

	  3.  Echo is on if no listing file is specified, otherwise  it  is
	      off.



     8.1.3.3  Terminal Message Format -  The  error  messages  that  MACREL
     prints  on  the  terminal  consist of four or five fields depending on
     whether you selected the abbreviated or extended printout  form.   The
     following  paragraphs describe each field in the order (left to right)
     that they appear on the terminal.

	  1.  Error Code

	      A two letter code that identifies the error type  (see  Table
	      8-3)

	  2.  Error Description


				      8-6

			     USING MACREL AND KREF


	      A brief text message that describes the error condition.

	  3.  Error Location

	      This field starts with an at-sign (@).  This is  followed  by
	      the  value of the current location counter at the point where
	      the error occurred.  This value  is  given  symbolically,  if
	      possible,  in  the  form  TAG+nnnn  where TAG is the previous
	      label and nnnn is the difference between the current  address
	      and  the  address of the label.  If no label has yet occurred
	      within the current section, then the TAG+ is omitted and nnnn
	      represents  the  current  location  counter.   The  label  is
	      printed as ASCII characters with no space-fill.  nnnn  is  an
	      octal  number with leading zeroes suppressed.  If the line in
	      error has a label, then the +nnnn is omitted.

	  4.  Program Section Name

	      The name of the  section  in  which  the  error  occurred  is
	      printed  preceded by the word SECT.  This field is omitted if
	      the program section (SECT) where error occurred is  the  same
	      as that of the previous error.

	  5.  Error Line

	      If you select the extended error printout form  (see  below),
	      the  line in which the error occurs is printed in this field.
	      Tabs  occurring  within  the  line  are  converted   to   the
	      appropriate number of spaces.

	      The assembler prints these messages on the pass in which they
	      are  detected.  Unless the error is serious enough to warrant
	      repetition, the  error  message  is  printed  only  once  per
	      assembly, not once each pass.



     8.1.4  Listing Error Messages

     In addition to the  messages  printed  at the  terminal,  MACREL  also
     prints  diagnostic  error messages on the program listing.  Appendix D
     lists these messages and their meanings.



     8.1.5  Program Listing Format

     The program listing is an output file that shows the  results  of  the
     assembly  operation.   A  program listing consists of two major parts:
     the statements  that  you  entered  into  the  source  file,  and  the
     assembled results that MACREL produces for each statement.

     The following paragraphs  describe  the  format  and  meaning  of  the
     information  generated  by  MACREL.   Figure 8-1 shows a printout of a

				      8-7

			     USING MACREL AND KREF


				   Table 8-3
			      MACREL Error Codes
		----------------------------------------------
		|     Code     |	   Meaning	     |
		|--------------|-----------------------------|
		|      CF      |  KREF not found	     |
		|      DE      |  Device Error		     |
		|      DF      |  Device Full		     |
		|      DV      |  Divide by 0		     |
		|      IC      |  Illegal Character	     |
		|      ID      |  Illegal Redefinition	     |
		|      IE      |  Illegal Equate	     |
		|      II      |  Illegal Indirect	     |
		|      IP      |  Illegal Pseudo-op	     |
		|      IR      |  Invalid Reference	     |
		|      IZ      |  Illegal Page 0 Reference   |
		|      LD      |  LINK not found	     |
		|      LG      |  Link Generated	     |
		|      IM      |  Illegal Macro		     |
		|      NE      |  Number Error		     |
		|      PE      |  Page Exceeded		     |
		|      PH      |  Phase Error		     |
		|      RD      |  Redefinition		     |
		|      RE      |  Relocation Error	     |
		|      SE      |  Symbol Table Exceeded	     |
		|      SY      |  Syntax Error		     |
		|      UO      |  Undefined Loading Address  |
		|      US      |  Undefined Symbol	     |
		|      XS      |  LSD overflow		     |
		|      ZE      |  Page 0 Exceeded	     |
		----------------------------------------------


     sample program listing.  The columns of  information  discussed  below
     are identified by circled reference numbers.



     8.1.5.1  Line Number Column - The line  number  column  is  the  first
     (leftmost)   column   of   the   assembly   listing  (see  Figure  8-1
     reference 1).  It consists of an  ascending  sequence  of  consecutive
     decimal  numbers.  MACREL assigns a line number to each line contained
     in the source file.  This includes lines of text that  are  suppressed
     in  a  particular  assembly  listing by the listing control directives
     (see Section 5.1), lines affected  by  the  .IF  conditional  assembly
     directive,  and  blank  lines.  MACREL does not assign line numbers to
     lines in a macro expansion.



     8.1.5.2  Current Location Counter Value Column - The current  location
     counter  value  is  the  second column of the assembly listing (Figure
     8-1, reference 2 ).  It consists of one or more consecutive groups  of
     four to six digit octal numbers in ascending order.

				      8-8

			     USING MACREL AND KREF


     In absolute program sections, this value is the actual memory  address
     where LINK will store instructions and data.

     In relocatable program sections, this value is the address relative to
     the   beginning   of   the  program  section  where  LINK  will  store
     instructions and data.  LINK determines the absolute address as  shown
     on  the  load map.  A question mark (?) preceding the relative address
     value means that the program section is not restricted to  load  in  a
     particular  memory  field.   An  asterisk  (*)  following the relative
     address value means that the instruction code in  the  column  to  the
     right was processed by a RELOC directive.  The address value itself is
     that of the relocated code.

     MACREL sets the least significant four digits of the current  location
     value  to  ????  to  show that the address value cannot be known until
     LINK time.  This happens whenever you use the asterisk  (*)  directive
     to  change  the  current  location  counter  value  to  the value of a
     currently undefined external symbol, or to  the  value  of  a  complex
     relocatable expression (see Section 10.8).  The current location value
     remains at ???? until MACREL detects a known current location  counter
     value.



     8.1.5.3  Absolute Assembled Value  Column  -  The  absolute  assembled
     value  column is the third column of the assembly listing (Figure 8-1,
     reference 3 ).  It consists of a four digit octal number that  is  the
     assembled value of either an instruction or data.

     If there is an entry in the preceding current location  value  column,
     it is the absolute part of the value that will be stored.

     The value in this column can also  be  the  result  of  an  expression
     associated with directives that don't generate storage values.

     If four asterisks (****) appear in the column, the  value  is  complex
     relocatable.   Several  special  symbols  may  follow  entries in this
     column:

	Symbol				      Meaning	______				      _______

	  ' (apostrophe) Link generated for a symbol on this line.

	  (space)	 Value is absolute.

	  +		 Value requires simple relocation relative  to  the
			 current program section.

	  -		 Value requires .FSECT relocation.

	  *		 None  of  the  above.    Value   may   either   be
			 relocatable  to  another  program  section  or  be
			 CDF/CIF relocatable.


				      8-9

			     USING MACREL AND KREF


     8.1.6  Symbol Table Format

     The symbol table listing immediately  follows  the  assembly  listing.
     This  is  a  list of all user-defined symbols in the module along with
     their values.  (You can also list the permanent symbols by  using  the
     command string options shown in Table 8-1.)

     The listing consists of two columns of information (see  Figure  8-1).
     The  first  column contains a list of the symbols in alphabetic order.
     The second column contains the absolute  value  associated  with  each
     symbol.  MACREL may also precede and follow a symbol value with one or
     more of the identifying codes shown in Table 8-4.


				   Table 8-4
			Symbol Table Descriptor Codes

		  ---------------------------------------------------------
		  |  Code  |		Meaning				  |
     -------------|--------|----------------------------------------------|
     |		  |   E    |  Symbol is an entry point.			  |
     |		  |	   |						  |
     |		  |   G	   |  Symbol is global.				  |
     |		  |	   |						  |
     |  Precedes  |   M	   |  Symbol is a macro name.			  |
     |		  |	   |						  |
     |	Symbol	  |   X	   |  Symbol is external, value is ****.	  |
     |		  |	   |						  |
     |	Value	  |   Y	   |  Symbol is a secondary reference (.SECREF),  |
     |		  |        |  value is ****.				  |
     |		  |	   |						  |
     |		  |   Z    |  Symbol is ZTERNAL, value is 0***.		  |
     |============|========|==============================================|
     |		  | ASECT  |  Symbol is .ASECT name.			  |
     |		  |	   |						  |
     |		  | DSECT  |  Symbol is .DSECT name.			  |
     |		  |	   |						  |
     |	Follows	  | FSECT  |  Symbol is .FSECT name.			  |
     |		  |	   |						  |
     |	Symbol	  | RSECT  |  Symbol is .RSECT name.			  |
     |		  |	   |						  |
     |	Value	  | XSECT  |  Symbol is .XSECT name.			  |
     |		  |	   |						  |
     |		  | ZSECT  |  Symbol is .ZSECT name.			  |
     |		  |	   |						  |
     |		  | + name |  Relocatable part of symbol value.   Symbol  |
     |		  |        |  will be relocated relative to the value of  |
     |		  |	   |  name.					  |
     |		  |	   |						  |
     |		  | <----  |  Undefined symbol				  |
     ----------------------------------------------------------------------




				     8-10

			     USING MACREL AND KREF


     8.1.7  Example Program Listing

     The typing routine that was used as an example in Chapter 6  is  again
     used  as an example.  It is slightly changed to illustrate the listing
     of a program section assembled by  MACREL  and linked  and  loaded  by
     LINK.



     8.1.7.1  Assembly  Listing -  The  listing  starts  with  the  program
     section  exactly  as  written.   The  first 42 lines include the macro
     definitions for the three macros MESG, JUMP and TYPE.  The macro  JUMP
     includes  the  nested  macro  call  TYPE.  Except for the decimal line
     numbers added by the assembler, this portion of  the  listing  is  the
     same  as  a  copy  of  the  source  file you request with the OS/8 CCL
     commands TYPE or LIST.  The addition of the line  numbers  during  the
     assembly  makes  easier  working with the source file, if you retain a
     copy of the listing for subsequent editing.


     LISTING AND SYMBOL TABLE EXAMPLE   MACREL-V2D THU 10-JAN-79
						       FILE  1
       (1)
       /	
      /
     1	.TITLE LISTING AND SYMBOL TABLE EXAMPLE
     2	.SBTTL DO NOT COLLECTY 200$
     3
     4
     5
     6				   .MACRO MESG A
     7				   TEXT "A"
     8				   .ENDM MESG
     9
     10
     11				   .MACRO JUMP A
     12				   .ENTRY  MONIT
     13				   TAD	   (MESG'A)
     14				   DCA	   ADDR$
     15				   SKP
     16			   ADDR$:  0
     17				   TYPE
     18			   MONIT,  JMP I   (7605)
     19				   .ENDM JUMP
     20
     21
     22
     23
     24				   .MACRO  TYPE
     25				   CLL		   /START WITH LEFT HALF
     26			   LOOP$:  TAD I   ADDR$   /GET WORD FROM STRING
     27				   SNL		   /LINK INDICATES HALF

		      Figure 8-1 Example Program Listing

				     8-11

			     USING MACREL AND KREF


     28				   BSW		   /LEFT HALF
     29				   AND	   (77     /MASK SIX BIT BYTE
     30				   SNA		   /IS IT NULL
     31				   JMP	   MONIT   /YES/ RETURN TO MONITOR
     32				   TAD	   (240	   /NO -CONVERT TO ASCII
     33				   AND	   (77
     34				   TAD	   (240
     35				   TLS		   /SEND TO TERMINAL.
     36				   TSF		   /WAIT UNTIL PRINTED
     37				   JMP	   .-1
     38				   CML		   /SWITCH TO OTHER HALF
     39				   SNL CLA	   /IS IT LEFT HALF
     40				   ISZ	   ADDR$   /YES-NEXT WORD
     41				   JMP	   LOOP$   /NO-SAME WORD
     42				   .ENDM   TYPE
     43		   (3)
     44		    |
     45		    V		    |
     46	    (2)	   0000	   .RSECT TYPE2
     47	     |			   JUMP    1
	     V			   .ENTRY  MONIT	     |
	   ?0000   1377		   TAD     (MESG1)
	   ?0001   3203		   DCA	   ADDR$
	   ?0002   7410		   SKP
	   ?0003   0000	   ADDR$:  0
				   TYPE
	   ?0004   7100		   CLL		   /START WITH LEFT HALF
	   ?0005   1603    LOOP$:  TAD I   ADDR$   /GET WORD FROM STRING
	   ?0006   7420		   SNL		   /LINK INDICATES HALF
	   ?0007   7002		   BSW		   /LEFT HALF
	   ?0010   0376		   AND	  (77	   /MASK SIX BIT BYTE
	   ?0011   7450		   SNA		   /IS IT NULL
	   ?0012   5225		   JMP	   MONIT   /YES/ RETURN TO MONITOR
	   ?0013   1375		   TAD	   (240	   /NO -CONVERT TO ASCII
	   ?0014   0376		   AND	   (77
	   ?0015   1375		   TAD	   (240
	   ?0016   6046		   TLS		   /SEND TO TERMINAL
	   ?0017   6041		   TSF		   /WAIT UNTIL PRINTED
	   ?0020   5217		   JMP	   .-1
	   ?0021   7020		   CML		   /SWITCH TO OTHER HALF
	   ?0022   7620		   SNL CLA	   /IS IT LEFT HALF
	   ?0023   2203		   ISZ     ADDR$   /YES--NEXT WORD
	   ?0024   5205		   JMP	   LOOP$   /NO-SAME WORD
	   ?0025   5774	   MONIT,  JMP I   (7605)
     48
     49
	   ?0174   7605
	   ?0175   0240
	   ?0176   0077
	   ?0177   0000	*
     50		   0000	   .DSECT ERRMSG
     51

		  Figure 8-1 (Cont.) Example Program Listing

				     8-12

			     USING MACREL AND KREF


     52			   MESG1, MESG"PROG ERR -GO TO JAIL,DO NOT PASS GO"
	   ?0000   2022		  TEXT "PROG ERR -GO TO JAIL,DO NOT PASS GO"
	   ?0001   1707
	   ?0002   4005
	   ?0003   2222
	   ?0004   4055
	   ?0005   0717
	   ?0006   4024
	   ?0007   1740
	   ?0010   1201
	   ?0011   1114
	   ?0012   5404
	   ?0013   1740
	   ?0014   1617
	   ?0015   2440
	   ?0016   2001
	   ?0017   2323
	   ?0020   4007
	   ?0021   1700

		  Figure 8-1 (Cont.) Example Program Listing


     Line 47 of this listing is the complete program;  the single statement
     which is a call to the macro JUMP 1.  The macro expansion follows JUMP
     1.  MACREL now adds two columns to the listing:  the first  column  is
     the relative core location of the instruction in octal, and the second
     column is the octal value of the instruction.  The field number of the
     core  address  is  represented  by a question mark because at assembly
     time MACREL has no way of knowing which field LINK will  use  for  the
     various program sections.

     Following the macro call JUMP, the macro is expanded.  The first  line
     in  the macro is .ENTRY MONIT, which is stored in the Symbol Table and
     as a declaration directive, is not given a memory location.  The first
     location  is  assigned  to the second line in the macro (TAD (MESG1)).
     The expansion of JUMP continues until the macro call  TYPE,  following
     location  ?0003.   TYPE needs no memory location because it is a macro
     call.  Now the macro TYPE is expanded up to  and including  the  final
     instruction  JMP  LOOP$  after which MACREL continues the expansion of
     the macro JUMP.  The last instruction MONIT, JMP I (7605) is stored at
     location ?0025.

     The listing continues, after the  blank  lines  48 and  49,  with  the
     program  section's literals.  They are stored beginning at the highest
     location  on  the  memory  page  beginning  with  the  first   literal
     encountered  in  the  section.  At location ?0000 in .RSECT TYPE2, the
     literal (MESG1), is stored at location ?0177 the highest  location  on
     the  page.   The  value of the literal is listed in the second column.
     The value of (MESG1) is its address;  the asterisk indicates  that  it
     is  relocatable.  The next literal encountered is 77, followed by 240.
     The final literal is the address 7605 stored at location ?0174.



				     8-13

			     USING MACREL AND KREF


     The listing continues at line 50 with a statement that defines  .DSECT
     ERRMSG.   Line  52  contains the label MESG1 and the call to the macro
     MESG following this is the expansion of the macro MESG with the actual
     argument.   Because this is a .DSECT, assembly starts at the beginning
     of a new memory page and successive locations are used for the text of
     the message, which is stored in six-bit ASCII.



     8.1.8  Symbol Table Listing

     The final part of MACREL's listing output is the  Symbol  Table.   The
     symbol  table  listing  shows  where  the  various labels and names of
     globals, program sections and macros are defined.  Figure 8-2 contains
     the symbol table listing for the program shown in Figure 8-1.

     All symbols, labels,  macros,  program  sections,  globals  and  entry
     points  are  identified by name and listed alphabetically in the first
     column.  The second column gives either the location relative  to  the
     beginning of the program section (for labels and entry points), or the
     first free location after the program section for  individual  program
     sections.

     The first symbol in the table  is  the  label  ADDR$  which  is  three
     locations  after  the beginning of .RSECT TYPE2.  The second symbol is
     the .DSECT name ERRMSG.  The first free location after the section  is
     location  0022.   The macros JUMP,MESG, and TYPE are identified by the
     letter M before the second column.  It shows  no  locations  allocated
     for the macro definitions.  (The definitions are temporarily stored in
     space reserved for macros during assembly.)


     LISTING AND SYMBOL TABLE EXAMPL   MACREL-V2D  THU  10-JAN-79
     SYMBOL TABLE

     ADDR$     0003+ TYPE2
     ERRMSG    0022  DSECT
     FLD: 0    0200  ASECT
     JUMP    M 0000
     LOOP:$    0005+ TYPE2
     MESG    M 0000
     MESG1     0000+ ERRMSG
     MONIT   E 0025+ TYPE2
     TYPE    M 0000
     TYPE2     0200  RSECT

		  Figure 8-2 Example of Symbol Table Listing


     The entry MONIT is listed  with  the  identifying  letter  E  and  its
     location  (25 locations after the start of the program section TYPE2).
     The symbol table is an aid to finding the  various  program  sections,
     macros,  globals,  and  labels,  in the program, but it lists only the
     defining location of a particular name in the  program  section.   The

				     8-14

			     USING MACREL AND KREF


     KREF  cross  reference listing, described below, lists all occurrences
     of program symbols.



     8.2  RUNNING KREF



     8.2.1  KREF Command String

     The KREF program produces  a  complete  cross-reference  listing  that
     shows  the location of every symbol used in the program.  KREF uses as
     its input file the KREF file (.KF extension) created by  MACREL.   You
     can  use  either  the  OS/8 Keyboard Monitor R command or the OS/8 CCL
     command KREF (described in the OS/8 Handbook) to run KREF.  Enter  the				    _____________
     following  command  immediately to the right of the Keyboard Monitor's
     period (.) prompting symbol to begin KREF operation.

	  .R KREF (RET)

     OS/8 responds by invoking the Command Decoder which in  turn  displays
     its  asterisk (*) prompting symbol at the left margin of the terminal.
     Respond to the asterisk by entering a KREF I/O specification  line  in
     the form:

	  output<input (RET)

     where:

	  output    is   the   output   file    specification    for    the
		    cross-reference  listing.   The  default  device is the
		    line printer (LPT:).  The default file  name  extension
		    is .LT.

	  <	    is a delimiter that separates input file specifications
		    from output file specifications.

	  input	    is the input  file  specification  for  the  KREF  file
		    output  by  MACREL.   The  default device is DSK:.  The
		    default file name extension is .KF.



     8.2.2  Description and Example of KREF Listing

     Figure 8-3 is an example cross-reference file for the program  section
     shown in Figure 8-1.







				     8-15

			     USING MACREL AND KREF


		      ADDR$   47     47#     47      47
		      ERRMSG  50
		      LOOP$   47#    47
		      MESG1   47     52#
		      MONIT   47     47	     47#
		      TYPE2   46
		      L174+   47
		      L175+   47     47
		      L176+   47     47
		      L177+   47
		      V0+     47     50#
		      V77     47     47	     50#
		      V240    47     47	     50#
		      V7605   47     50#

		      Figure 8-3 Example of KREF Listing


     KREF lists the symbols alphanumerically in the first column.  The next
     column  contains  the  line  number of the listing where the symbol is
     used for the first time.  Each column after that is the line number of
     another  occurrence of the same symbol.  A number sign (#) following a
     line number entry indicates the line where the symbol is defined.   To
     illustrate:   the symbol MESGl is first used in line 47 of the listing
     but is not defined until line 52 of the listing.  Because the  program
     section  used  in the example is a single statement program consisting
     of only a macro call (JUMP l on line 47) most of the  symbols  in  the
     program  are  inside  the  macro and are shown at line 47.  The symbol
     ADDR$, for instance, is shown to have four occurrences in the program,
     all on line 47 where it is also defined.

     If you examine the listing you will see the four  occurrences  of  the
     symbol  at  locations  l, 3, 5 and 23 relative to the beginning of the
     .RSECT TYPE2, the symbol is defined at location 3.  Following the  six
     symbols  used in the program, the KREF list shows the location, on the
     memory page, of the literals followed by a plus sign to indicate  that
     they  have  been  relocated  by  LINK.   Again  the  columns after the
     literals show where they occur in the program, but the point at  which
     they  are  defined  is shown in the next part of the list, the literal
     values.  The values of the literals are listed next, preceded  by  the
     letter  V.  All of these values are shown as being defined at line 50,
     the first line in the listing that follows the literal table.













				   8-16







				   CHAPTER 9

				  USING LINK


     This chapter describes the operating procedures for the linking loader
     program  LINK.   Before  running LINK, be sure that you are using OS/8
     Version 3D (or a later version), and that the file LINK.SV resides  on
     the system device (SYS:).  The file OVRDRV.RB must be available if you
     use overlays.  If you are unfamiliar with  OS/8  file  specifications,
     refer to the appropriate section of the OS/8 Handbook.					     _____________

     Once a program or program section is assembled  by  MACREL,  you  must
     call  LINK  to  complete  the  programming  task.   LINK  converts the
     relocatable binary file(s) created by MACREL into an executable memory
     image  file  that  can  be  either  memory  resident  or in an overlay
     structure.  LINK provides the following features:

	  o  Adjustment of address dependent  locations  to  correspond  to
	     the relocation of program sections.

	  o  Resolution of all global references within object modules.

	  o  Creation of an overlay structure including the overlay
	     driver.

	  o  Search of libraries for unresolved external symbols.

	  o  Creation  of  the  memory  image  file  with  the  linked  and
	     relocated object code and the memory control block.

     LINK performs these tasks during two passes over the  specified  input
     object  modules.   In the first pass LINK constructs the Global Symbol
     Table, allocates the named program sections to  memory,  and  searches
     and  links  the  library  files.   During the second pass LINK creates
     overlays, sets up the overlay driver, creates  the  memory  image  and
     load map files.



     9.1  RUNNING LINK



     9.1.1  LINK Command String

     You can use either the OS/8 Keyboard Monitor R command or the OS/8 CCL
     command  LINK (described in the OS/8 Handbook) to run LINK.  Enter the				     _____________
     following command immediately to the right of the  Keyboard  Monitor's
     period (.) prompting symbol to begin LINK operation.


				      9-1

				  USING LINK


	  .R LINK (RET)

     OS/8 responds by invoking the Command Decoder which in  turn  displays
     its asterisk (*) prompting symbol at the left margin of the terminal.

     Respond to the asterisk by entering a LINK I/O specification string in
     the form:

	  [save] [,load map]<file-l[/options,...,file-9/options terminator]

     where:

	  save		 is the output file specification  for  either  the
			 executable  memory  image  save file or the ABSLDR
			 binary file.  The default  device  is  DSK:.   The
			 default file name extension is .SV for a save file
			 and  .BN  for  a  binary  file.   If  no  file  is
			 specified, LINK performs all other required  tasks
			 but  does  not  create a save or binary file.  You
			 must, however, enter the comma  delimiter  if  you
			 are going to specify a load map file.

	  load map	 is the file specification for the load  map  file.
			 The default device is DSK:.  The default file name
			 extension is  .MP.   If  you  do  not  enter  this
			 specification, LINK will not produce a load map.

	  <		 is a delimiter.  The  Command  Decoder  interprets
			 file  specifications  to the left as output files,
			 and those to the right as input files.

	  file-l/options is  the   input   file   specification   for   the
			 relocatable binary file produced by MACREL and its
			 associated LINK control options (Table 9-1).   You
			 can  use  any  combination  of compatible options.
			 You   can   enter   up   to    nine    file/option
			 specifications  on a line.  You must separate each
			 specification with a comma.  The default file name
			 extension  is  .RB.   The  default  device for the
			 first  file  specification  is  DSK:.    For   the
			 remaining  file specifications, the default device
			 is  the  name  of  the  device  contained  in  the
			 preceding  file  specification.   The default file
			 name extension is .MA.

	  options	 is one or more of the options listed in Table 9-1.

	  terminator	 is either  a  specification  or  line  terminator.
			 ALTMODE  terminates  the  specification string and
			 signals LINK to begin.  If you want to enter  more
			 than   nine   file/option  specifications,  use  a
			 carriage return to terminate each line except  the
			 last.   Use  ALTMODE  to  terminate the last line.


				      9-2

				  USING LINK


			 LINK will not accept  more  than  128  file/option
			 specifications.



     9.1.2  LINK Command String Example

     Example:

	  .R LINK
	  *NAME.SV,LPT:<MAIN.RB,OVRDRV.RB/S/K=7
	  *LIB.RB/L/O
	  *SUB1.RB,SUB2/C
	  *SUB3,SUB4/O
	  *SUB5$

     The first line of the example establishes an image  (save)  file  with
     the  designation  NAME  and specifies a load map that is output to the
     line printer.  The input files consist of the program module  MAIN.RB,
     a relocatable binary file assembled by MACREL, and the file OVRDRV.RB.
     This last file is a special file that must be assembled by MACREL  and
     then included in the input specification for any program that includes
     overlays.  The overlay driver (OVRDRV.MA) is a source program designed
     to control the overlay structure;  it is un-assembled so that internal
     parameters can be  changed,  as  necessary,  to  fit  your  particular
     overlay  requirements.   This  program should be edited, if necessary,
     assembled by MACREL, and then explicitly specified to  the  LINK  each
     time  a  final program (that includes overlays) is linked.  Details on
     OVRDRV.MA can be found in Section 10.5.  OVRDRV.RB,  the  final  input
     file  on  the  first  line  of  the example is followed by the control
     options.  The /S option generates a request to  LINK  for  a  starting
     address  while  the /K=7 sets the virtual core size to the upper limit
     of field 7.  The second command line has  only  one  input  file,  the
     library file LIB.RB;  library files must be indicated by the /L option
     when you write the specification line.  The /O option  on  the  second
     line and again on the fourth line closes the current overlay level and
     opens the next overlay level.  On line two, it closes the  main  level
     and  opens  level one.  The overlays are listed beginning on the third
     line.  The /C option closes the current overlay  and  opens  the  next
     overlay.   Notice  particularly  the  difference between the /O and /C
     options;  /O closes the current overlay level and opens the next level
     while /C closes the current overlay and opens the next overlay.

     Table 9-1 gives all of the options that are used with LINK.



     9.2  RULES FOR USING OVERLAY OPTIONS

     The control options /O and /C open one overlay or level (/O) and close
     the  next overlay or level (/C).  The internal operation of LINK takes
     care of the overlays and the overlay driver in a  transparent  manner.
     In  order  to  use  the  overlay  feature of LINK, you must specify an
     overlay structure either in your source program  with  the  LEVEL  and

				      9-3

				  USING LINK


				   Table 9-1
			     LINK Control Options

     ----------------------------------------------------------------------
     | Option	  |			 Function			  |
     |------------|-------------------------------------------------------|
     |	 /B	  | Create an ABSLDR binary (.BN) file rather than a  .SV |
     |		  | file.						  |
     |		  |							  |
     |	 /C	  | Close current overlay, open next overlay.		  |
     |		  |							  |
     |	 /F	  | Disable LINK overlay  error  checking.   JMS  is  now |
     |		  | possible to anywhere in the program to any overlay or |
     |		  | level, but it is now your  responsibility  to  insure |
     |		  | return paths to the calling routine.		  |
     |		  |							  |
     |   /G	  | Start the program when linking is complete, the image |
     |		  | (.SV  file  extension)  must  be  on SYS:  if you use |
     |		  | overlays.  A .BN file can reside on any device.	  |
     |		  |							  |
     |	 /H	  | Initialize empty memory image locations  to  the  HLT |
     |		  | instruction (7402) instead of zero.			  |
     |		  |							  |
     |	 /J	  | Initialize empty memory image locations  to  the  JMP |
     |		  | instruction.					  |
     |		  |							  |
     |	 /K	  | Set virtual memory size  as  specified  by  low-order |
     |		  | bits  of  =m (where:  m is a value between 0 and 37). |
     |		  | Default is current OS/8 system memory size.		  |
     |		  |							  |
     |	 /L	  | This line specifies library files only.		  |
     |		  |							  |
     |	 /M	  | Permit program sections to load the top page  of  all |
     |		  | fields  other  than  0  or 1.  If not specified, LINK |
     |		  | reserves the top page of every field for OS/8.	  |
     |		  |							  |
     |	 /N	  | Null module.  Set aside a  double  memory  page  that |
     |		  | begins  with  the  17-bit  address  specified  by  =m |
     |		  | (where:  m is a value between 0  and  377777).   This |
     |		  | double page will not be loaded.  A double page is two |
     |		  | consecutive  pages  whose  starting  address   is   a |
     |		  | multiple of 400(8).					  |
     |		  |							  |
     |	 /O	  | Close current overlay level, open next overlay level. |
     |		  |							  |
     |	 /R	  | Reserve field specified by =m (where  m  is  a  value |
     |		  | between  0  and  37).   LINK  will not load into this |
     |		  | field.						  |
     |		  |							  |
     |	 /S	  | Ask  for  starting  address  or  begin   at   address |
     |		  | specified  by  =m.   You  can  respond with either an |
     |		  | absolute address in octal or a global name.		  |
     ----------------------------------------------------------------------
						  (continued on next page)

				      9-4

				  USING LINK


			       Table 9-1 (Cont.)
			     LINK Control Options

     ----------------------------------------------------------------------
     | Option	  |			 Function			  |
     |------------|-------------------------------------------------------|
     |	 /T	  | If running under  BATCH,  output  error  messages  to |
     |		  | terminal instead of BATCH log.			  |
     |		  |							  |
     |	 /V	  | Print LINK's current version number.		  |
     |		  |							  |
     |	 /W	  | Ask for status word or use value specified by =m.  If |
     |		  | not requested, LINK generates a job status word.	  |
     |		  |							  |
     |	 /X	  | Perform special RTS/8 (V3) processing on  the  object |
     |		  | module.						  |
     |		  |							  |
     |	 /Y	  | If available, use 7600-7777 of memory fields 2  to  7 |
     |		  | for Symbol Table storage.				  |
     |		  |							  |
     | /0,1,...,7 | Reserve the referenced memory field.  This field will |
     |		  | not be loaded.					  |
     |		  |							  |
     |	 /8	  | Do not load locations 0-1777 of field 0.		  |
     |		  |							  |
     |	 /9	  | Do not load locations 0-1777 of field 1.		  |
     |		  |							  |
     |	 =	  | Defines values for various options (see K, M, S, N, R |
     |		  | and W above).					  |
     ----------------------------------------------------------------------

				    WARNING

		   Do not use /R, /S, /M and /W options  on
		   the  same  line with each other, or with
		   the /K and /N options.  The  /K  and  /N
		   options  override  the /M, /R, /S and /W
		   options.

     OVERLAY  options  of  the program section directives, or at link time.
     This allows LINK to modify the program module structure to produce the
     desired  overlays  at  run  time.  You must include the overlay driver
     (OVRDRV.RB) in the input file specifications for the main level (level
     0).  LINK allows up to eight levels of overlays, level 0 through level
     7.   Level 0 always contains the mainline program, the overlay driver,
     and the library;  it is always memory resident.  Levels  1  to  7  may
     each have up to 16 overlays, only one of which may be core resident at
     any one time.

     When referencing overlayed portions of code, there are only four basic
     rules that must be observed, as shown below:

	  1.  Branches (JMP or JMS) to an  overlay  must  be  to  an  entry
	      point.

				      9-5

				  USING LINK


	  2.  Entry points in an overlay cannot  be  used  for  referencing
	      data within the overlay.

	  3.  Calls from an overlay may be to entries in the same  overlay,
	      the root segment, or an overlay with a higher level number.

	  4.  Subroutines in the root segments  that  are  called  from  an
	      overlay  should  observe  rule  3 as if such subroutines were
	      part of the overlay section that called them.

     Note that the /F control option supersedes rules 3  and  4.   You  can
     make  calls  to an entry at any level, but you must provide the proper
     return path.  Use this control option with extreme care.  For example,
     a  JMS  instruction  might  replace  the  current overlay with another
     overlay and thus remove the return point for the subroutine.

     If an object module is overlayed, LINK will  set  bit  4  of  the  Job
     Status Word for that module to inform system software that there is an
     overlay present in the module.



     9.3  LINK LIBRARIES

     A LINK Library file consists of a set of  concatenated  MACREL  object
     modules which you must specify with the /L option to the specification
     line which includes the library files as input.  After processing  all
     non-library  files,  LINK  searches  the library files for any, as yet
     unresolved, external symbols.  Modules can appear in any order in  the
     library file and LINK continues to search through the files to resolve
     any missing external  symbols.   Each  time  an  undefined  symbol  is
     defined, LINK adds the definition to the Global Symbol Table.  Because
     LINK allows backward references in a  library,  the  search  continues
     until  all  symbols have been defined.  This could require many passes
     through a library, thereby increasing LINK's execution time.

     Library files are typically collections of utility routines  that  you
     have  created  to be used in many different programs.  This collection
     of individual files can be concatenated with PIP and the PIP option /I
     and then included as a library for LINK.  If a library is specified to
     LINK, any referenced entry causes LINK to search the library and  link
     only the individual piece being referenced.

     The following example shows how  you  can  concatenate  library  files
     using OS/8 utility program PIP.

				     NOTE

		   A library file cannot  be  greater  than
		   255(10) blocks.


	  .R PIP
	  *CONCAT.RB<LIB1.RB,LIB2.RB,.../I

				      9-6

				  USING LINK


     If more than 9 are being concatenated together:

	  *CONCAT.RB<CONCAT.RB,LIB10.RB,.../I

     You need not  always  specify  a  library.   A  default  library  file
     LNKLIB.RB,  which you can create, is always the last library file that
     LINK searches (if it exists) to resolve any undefined symbols  in  the
     program module.



     9.4  LINK ERROR MESSAGES

     Most program errors in MACREL/LINK occur in the assembly of the source
     files.   MACREL  reports then when it assembles the object module (see
     Appendix D).  LINK generates  error  messages  to  indicate  incorrect
     specifications,  bad  overlay structure, or other errors particular to
     LINK.  These errors are listed in Table 9-2.  System  errors  reported
     by  LINK  are  listed in Table 9-3.  Unless indicated by the asterisk,
     all errors reported  by  LINK  are  fatal  errors  and  result  in  an
     immediate return to the Keyboard Monitor.


				   Table 9-2
			      LINK Error Messages

     ----------------------------------------------------------------------
     |      Error Message      |	       Meaning			  |
     |-------------------------|------------------------------------------|
     | BAD CORE SPECIFICATION  | * Memory specified as less  than  8K  or |
     |			       |   greater than 32K.			  |
     |			       |					  |
     | BAD ENTRY NAME	       | * Name given for starting address is not |
     |			       |   in global symbol table.		  |
     |			       |					  |
     | BAD INPUT LINE	       | * Bad data input for job status word  or |
     |			       |   starting address.			  |
     |			       |					  |
     | DS XXXXXX	       | * The  global  symbol  XXXXXX  has  been |
     |			       |   defined more than once.  LINK uses the |
     |			       |   first occurrence of the symbol.	  |
     |			       |					  |
     | ENTER ERROR	       |   An error was encountered while opening |
     |			       |   one of the output files.		  |
     |			       |					  |
     | IMAG OVERFLOW	       |   Not enough room on output  device  for |
     |			       |   memory image file.			  |
     |			       |					  |
     | LINKER I/O ERROR	       |   Device handler error.		  |
     ----------------------------------------------------------------------
	  Note:  * means error is not fatal.
						  (continued on next page)



				      9-7

				  USING LINK


			       Table 9-2 (Cont.)
			      LINK Error Messages

     ----------------------------------------------------------------------
     |      Error Message      |	       Meaning			  |
     |-------------------------|------------------------------------------|
     | NO ROOM		       | * No  room,  program  will  not  fit  in |
     | XXXXXX		       |   memory.   XXXXXX  is  the  name of the |
     |			       |   program section causing  error.   LINK |
     |			       |   will output a load map before returning|
     |			       |   to the Keyboard Monitor.		  |
     |			       |					  |
     | NO SECT		       |   No program sections in program.	  |
     |			       |					  |
     | NULL OUT OF CORE RANGE  | * Null  module  specification  was   not |
     |			       |   within allowable memory size.	  |
     |			       |					  |
     | OVERLAY-LEVEL           | * Overlay-level error.  Overlay level is |
     |			       |   lower than allowed.			  |
     |			       |					  |
     | PAGE 0 REF NOT ON PAGE 0| * Page zero reference failed  to  be  on |
     |			       |   page zero at load time.		  |
     |			       |					  |
     | SECT OVERFLOW	       |   Program section table  overflow.   Too |
     |			       |   many sections in program.		  |
     |			       |					  |
     | SYM OVERFLOW	       |   Symbol table overflow. Too many global |
     |			       |   symbols.				  |
     |			       |					  |
     | TOO BIG		       |   The memory image requires more  memory |
     |			       |   than has been specified.		  |
     |			       |					  |
     | TOO MANY INPUT FILES    | * More than 128 input  files  have  been |
     |			       |   specified.				  |
     |			       |					  |
     | TOO MANY LEVELS	       | * More  than  seven  levels  have   been |
     |			       |   specified.				  |
     |			       |					  |
     | TOO MANY OVERLAYS       | * More than 16 overlays per  level  have |
     |			       |   been defined.			  |
     |			       |					  |
     | TOO MANY XFER VECTORS   | * More than  511  transfer  vectors  for |
     |			       |   overlays are needed for program.	  |
     |			       |					  |
     | US XXXXXX	       | * The symbol XXXXXX is not defined.	  |
     ----------------------------------------------------------------------
	  Note:  * means error is not fatal.








				      9-8

				  USING LINK


				   Table 9-3
			  LINK-Detected System Errors

     ----------------------------------------------------------------------
     |		Message        |		   Meaning		  |
     |-------------------------|------------------------------------------|
     | ABSLDR.SV NOT ON SYS:   |					  |
     | WHEN 'G' OPTION	       |					  |
     | SPECIFIED	       |					  |
     |			       |					  |
     | ATTEMPT TO ALLOCATE     |					  |
     | NON-EXISTENT MEMORY     |					  |
     |			       |					  |
     | ATTEMPT TO DIVIDE BY 0  |					  |
     | IN .RB FILE LOAD IMAGE  |					  |
     |			       |					  |
     | ATTEMPT TO READ/WRITE   | Check  I/O  specification in the command |
     | DEVICE 0		       | string.				  |
     |			       |					  |
     | BAD LOADER CODE IN .RB  |					  |
     | FILE LOAD IMAGE	       |					  |
     |			       |					  |
     | BAD SYMBOL TYPE	       |					  |
     |			       |					  |
     | CORE IMAGE DEVICE NOT   | Check  I/O  specification   in   command |
     | FILE ORIENTED	       | string.				  |
     |			       |					  |
     | CORE IMAGE OF 'MAIN'    |					  |
     | HAS TOO MANY 'PIECES'   |					  |
     |			       |					  |
     | CLOSED LOOP SECT	       | Two or more program sections  restricted |
     | RESTRICTION	       | to load in the same field.		  |
     |			       |					  |
     | ERROR CLOSING CORE      | Bad device,  device  medium,  or  system |
     | IMAGE FILE	       | error.					  |
     |			       |					  |
     | ERROR CLOSING MAP FILE  | Bad device,  device  medium,  or  system |
     |			       | error.					  |
     |			       |					  |
     | ERROR READING FROM      | Bad  device  medium,  or  system  error. |
     | SCRATCH BLOCKS ON SYS:  |					  |
     |			       |					  |
     | ERROR WRITING TO        | Bad device,  device  medium,  or  system |
     | SCRATCH BLOCKS ON SYS:  | error.					  |
     |			       |					  |
     | FAILURE FETCHING DEVICE | Check  I/O  specification   in   command |
     | HANDLER		       | string.				  |
     |			       |					  |
     | FSECT WON'T FIT ON ONE  | Check assembly listing.		  |
     | PAGE		       |					  |
     ----------------------------------------------------------------------
						  (continued on next page)



				      9-9

				  USING LINK


			       Table 9-3 (Cont.)
			  LINK-Detected System Errors

     ----------------------------------------------------------------------
     |		Message        |		   Meaning		  |
     |-------------------------|------------------------------------------|
     | LIBRARY 'PIECE' TABLE   |					  |
     | FULL		       |					  |
     |			       |					  |
     | LINK INPUT FILE NOT IN  | Check  I/O  specification   in   command |
     | .RB FORMAT	       | string.				  |
     |			       |					  |
     | LOADER SYMBOL	       | Source file too big.  Divide it into two |
     | DICTIONARY TOO BIG      | modules, reassemble and relink.	  |
     |			       |					  |
     | LSD REF.  DOES NOT      |					  |
     | REFERENCE A GLOBAL      |					  |
     | SYMBOL IN .RB FILE LOAD |					  |
     | IMAGE		       |					  |
     |			       |					  |
     | OVERLAY DRIVER FATAL    | LINK's internal  overlay  driver  failed |
     | ERROR		       | because  it read a bad record from SYS:, |
     |			       | LINK.SV  not  on  SYS:,  or  wrong  OS/8 |
     |			       | Monitor version (must be V3D or later).  |
     |			       |					  |
     | OVERLAY DRIVER SYMBOLS  |					  |
     | NOT FOUND WHEN OVERLAYS |					  |
     | WERE SPECIFIED	       |					  |
     |			       |					  |
     | PUSH DOWN LIST OVERFLOW |					  |
     |			       |					  |
     | PUSH DOWN LIST	       |					  |
     | UNDERFLOW	       |					  |
     |			       |					  |
     | REFERENCE TO NON-       |					  |
     | EXISTENT SYMBOL IN .RB  |					  |
     | FILE LOAD IMAGE	       |					  |
     |			       |					  |
     | SECT NOT RESTRICTED TO  |					  |
     | A SECT, GLOBAL, OR      |					  |
     | ENTRY SYMBOL	       |					  |
     |			       |					  |
     | SECT RESTRICTED TO NON- | Check assembly listing.		  |
     | EXISTENT MEMORY	       |					  |
     |			       |					  |
     | SECT RESTRICTED TO      | Check assembly listing.		  |
     | UNKNOWN ADDRESS	       |					  |
     |			       |					  |
     | SECT RESTRICTED TO      | Check assembly listing.		  |
     | UNKNOWN FIELD	       |					  |
     ----------------------------------------------------------------------
						 (continued on next page)



				     9-10

				  USING LINK


			       Table 9-3 (Cont.)
			  LINK-Detected System Errors

     ----------------------------------------------------------------------
     |		Message        |		   Meaning		  |
     |-------------------------|------------------------------------------|
     | SYMBOL FORWARD	       | Check assembly listing.		  |
     | REFERENCE TO UNKNOWN    |					  |
     | SYMBOL		       |					  |
     |			       |					  |
     | TOO MANY 'HOLES' IN     |					  |
     | MEMORY DURING SECT      |					  |
     | ALLOCATION	       |					  |
     |			       |					  |
     | UNKNOWN LEVEL FOR       |					  |
     | CURRENT SECT	       |					  |
     |			       |					  |
     | 7 BIT RELOCATION ON NON |					  |
     | RELOCATABLE DATA IN .RB |					  |
     | FILE LOAD IMAGE	       |					  |
     ----------------------------------------------------------------------



     9.5  LINK LOAD MAP DESCRIPTION AND EXAMPLE

     If you enter a second output  file  specification  to  LINK,  it  will
     generate  a  load  map  with the default extension .MP.  This load map
     file includes the starting point  in  memory  and  the  size  of  each
     program section in the modules being linked.  Each entry point and its
     address is listed in the map in columns following the section in which
     it appears.

     The typing routine that was used in Chapter 6 and again in  Chapter  8
     was  assembled  by  MACREL and then linked by LINK, the following load
     map was generated from that program section by LINK.


	  OS/8      LINK    V 2B   LOAD  MAP	    10-JAN-79
	  SECTION   ADDR    SIZE   ENTRY    ADDR    ENTRY    ADDR

	  ERRMSG    00000   0022
	  TYPE2     00200   0200   MONIT    00225

	  PROGRAM ENTRY:   00200
	  JOB STATUS WORD:  0000

     The source module was written with two sections, A .DSECT named ERRMSG
     which  is  22  locations  long  and an .RSECT named TYPE2 which is 200
     locations long.  Because no field restriction or starting address were
     included in the source program module, LINK assumed a starting address
     (PROGRAM ENTRY:) of 200 in field 0.  One entry  was  included  in  the
     module  at  location  00225 in the section TYPE2.  The default section
     for any unnamed absolute sections is at location  00200  in  field  0.

				     9-11

				  USING LINK


     Any  unnamed  absolute  section  that  is not field restricted will be
     given the name FLD:  0 and this appears in  the  load  map.   In  this
     example  all  program  sections were named and therefore the length of
     the default section is 0000.

     The final item in the map is the Job Status Word.  In this example, it
     was  not  required.   This example does not include overlays, but when
     overlays are part of the object  modules  that  are  linked  they  are
     entered into the load map file following the listing of the sections.

     If a program was written with several overlays, assigned to two levels
     by  the  specifications,  the  load map would show the location of the
     overlays, their length, and any entry points in the  overlay.   Figure
     9-1 shows a sample of such a load map.

	      OS/8      LINK  V 2B  LOAD MAP	     10-JAN-79


	      SECTION   ADDR  SIZE     ENTRY   ADDR   ENTRY   ADDR

	      MAIN	00200 2332       A1    00200    B1    01000
					 B2    01400
	      ORWELL    02600 0534      COS    02600   SIN    2654

	      OVERLAY   LEVEL 1  OVERLAY 0

	      SUB1      03400 356
	      SUB2	04000 200

	      OVERLAY   LEVEL 1  OVERLAY 1

	      SUB3	03400 200   X1 03552
	      SUB4	03600 1000

	      OVERLAY   LEVEL 2  OVERLAY 0

	      SUB5	04600 234   X2   04717   X3   05000G

	      PROGRAM ENTRY:  00200

	      JOB STATUS WORD:  0200

		      Figure 9-1 Example of LINK Load Map

     The first line of the load map identifies the version  of  LINK  being
     used  and the date.  The second line contains the headings for each of
     the columns described below.  Next the map lists each program section,
     its  address,  and  size.   The  entry  points  are listed by name and
     address in the columns beside the program section name in  which  they
     are  located.   The  section MAIN has two entry points:  A1 at address
     00200 and B1 at address 01000.  The section  named  ORWELL  has  three
     entries, B1,COS, and SIN.  Overlay 0 - level 1 has two overlays:  SUB1
     which is 356 locations long and begins at  location  03400,  and  SUB2
     beginning at 04000 with a length of 200 locations.

				     9-12

				  USING LINK


     SUB3, overlay 1 - level 1, has an entry point  named  X1  at  location
     03552.   Another entry point named X2 is in SUBS, overlay 0 - level 2.
     SUB5 is 234 locations long and begins at  location  04600,  the  entry
     point  X2  is  at  location  04717 and global symbol X3 is at location
     05000.  The G following the address signifies that the  global  symbol
     is  in  an  overlay  and  not  an entry point.  There are no undefined
     symbols in the example.  Both global, absolute and  undefined  symbols
     will  appear  in  the  load  map,  if they appear in the modules being
     linked.














































				     9-13









				  CHAPTER 10

			   ADVANCED TECHNICAL TOPICS


     This chapter presents some advanced concepts of MACREL/LINK  that  may
     be  useful  to  the  experienced programmer.  You should be thoroughly
     familiar with all of the material in  the  preceding  chapters  before
     reading  this  chapter.   A  full  knowledge  of  the  OS/8  system is
     necessary for understanding some of the concepts in this chapter.



     10.1  MACREL SYMBOL TABLE SIZE

     MACREL requires at least 12K words of memory and runs under  OS/8  V3D
     (or  a later version).  MACREL uses the memory between 12K and 32K for
     additional symbol table space.  Table 10-1 shows the approximate  size
     of the symbol table with different memory sizes.


				  Table 10-1
			   MACREL Symbol Table Size

		     -------------------------------------
		     | Memory Size  |  Number of Symbols |
		     |--------------|--------------------|
		     |	    12K	    |	      576	 |
		     |	    16K	    |	     1088	 |
		     |	    20K	    |	     1600	 |
		     |	    24K	    |	     2112	 |
		     |	    28K	    |	     2624	 |
		     |	    32K	    |	     3136	 |
		     -------------------------------------

     Notes:

	  1.  If MACROs are not used, more symbols may be used.

	  2.  Current permanent symbol  table  is  about  110  symbols,  so
	      deduct  this number from values shown above to get final size
	      of your symbol table.

	  3.  The table will be diminished by about 192 symbols if BATCH is
	      running.   For example, in 12K, only about 448 symbols may be
	      used when running under BATCH.

	  4.  The table will be  diminished  by  approximately  96  symbols
	      unless you use the /Y command string option.

				     10-1

			   ADVANCED TECHNICAL TOPICS


     10.2  RELOCATABLE BINARY OBJECT MODULE FORMAT

     A relocatable object module (Figure 10-1) is the primary unit of input
     to LINK.  It is the output of a single MACREL assembly and consists of
     a Loader Symbol Dictionary (LSD) followed by text.  These are arranged
     into  OS/8  file blocks consisting of 256 words.  The first block of a
     module contains the  LSD  Preface.   If  necessary,  the  LSD  Preface
     extends into the second block. The LSD itself follows the LSD Preface.
     It requires one or more blocks.  Each subsequent block containing  the
     LSD has a header word only.

     Header words:

     Each block in the object module file begins with a header word.

     Bit 0:    0 if LSD block
	       1 if text block

     Bits 1-11 are reserved for future use.

     The first word of the file is the file ID.  It must contain the  value
     2202.   This is the six-bit code for the characters RB that identifies
     this file as a relocatable binary file.  LINK checks  for  this  value
     and generates a fatal error if not found.


    ------------------------------------------------------------------------
    | HEADER WORD | HEADER WORD | HEADER WORD || HEADER WORD | HEADER WORD |
    |-------------|-------------|-------------||-------------|-------------|
    |   FILE ID   |		|	      ||	     |		   |
    |-------------|		|	      ||	     |		   |
    | LSD PREFACE |	LSD	|     LSD     ||    TEXT     |	  TEXT	   |
    |-------------|		|	      ||	     |		   |
    |     LSD     |		|	      ||	     |		   |
    ------------------------------------------------------------------------

		       Figure 10-1 Object Module Format



     10.2.1  LSD Preface

     The LSD preface begins at word two and, although unlikely, could  span
     blocks (skipping header words).

     The LSD preface, described in Table 10-2, consists  of  zero  or  more
     preface  items  terminated by a word of zeroes.  The actual LSD begins
     immediately after this word.

     Each preface item begins with a negative count that is the  length  of
     the  preface  item.   The  count  includes its own location.  The word
     following the count is the item title.  This title is  a  number  that
     signifies  the  type of information that follows it.  For example, the
     number 1 might say that an absolute starting address follows.

				     10-2

			   ADVANCED TECHNICAL TOPICS


     LINK generates an  error  if  it  encounters  a  count  word  that  is
     positive.


				  Table 10-2
				  LSD Preface

     ----------------------------------------------------------------------
     | Count  | Code |			Description			  |
     |--------|------|----------------------------------------------------|
     |	 0    |   -  | End of Preface					  |
     |	-4    |	  1  | Absolute starting address (15 bits)		  |
     |	-4    |   2  | Symbolic starting address (LSD, offset)		  |
     |	-4    |   3  | Creation date					  |	
     |	-4    |   4  | RB Spec level number (level, sublevel)		  |
     |	-7    |   5  | RB author name (3 words 6-bit, 2 words version	  |
     |	      |	     | number)						  |
     |	-3    |   6  | Page number for start of loader map		  |
     |	-3    |   7  | Output width for loader map			  |	
     |	-3    |  10  | Number of lines/page for loader map		  |
     | varies |  11  | Title to appear at top of loader map		  |	
     |  -3    |  12  | Job status word					  |
     |  -3    |  13  | Version number					  |
     ----------------------------------------------------------------------



     10.2.2  LSD Description

     The LSD consists of 0 to 377 entries  that  can  flow  across  blocks.
     Each  entry is either four, five or six words depending on the type of
     symbol (see Figure 10-2).  An LSD is terminated by a  single  word  of
     zeros  and  is  immediately followed by the text, starting at the next
     block.

     The first three words of an LSD entry comprise the symbol name,  which
     is one to six alphanumeric characters stored in 6-bit ASCII.

     The format of word four depends on the symbol type, which  is  defined
     in  bits  8 through 11.  For type 0 or 1 symbols, bits 0 through 7 are
     zero.  For all remaining  nonprogram  section  type  symbols,  bits  0
     through 7 contain an address reference pointer.  For an .ASECT, bits 3
     through 5 contain the field restriction,  and  the  remaining  bits  0
     through  2  and  6  through  7  are unused.  For the remaining program
     section types, bits 0 through 2 contain the type of  restriction  that
     is in word 6 of the entry, as follows:

	  1 = absolute field
	  2 = 12-bit absolute origin
	  3 = same page as reference pointer
	  4 = same field as reference pointer
	  0 = no restriction



				     10-3

			   ADVANCED TECHNICAL TOPICS


	  ---------------------	 /
	1 |    S    |    Y    |  | TYPE CODES	     MEANING	      ENTRY
	  |	    |	      |  |   WORD 4			     LENGTH
	2 |    M    |    B    |	 |  BITS 8-11
	  |	    |	      |  |
	3 |    O    |    L    |	 |    0		FIELD			4
	  |---------|---------|	 |    1		SECONDARY REFERENCE	4
	  |	    |	      |	 |    2		ASECT			6
	  |   FLD   |  TYPE   |	 |    3		RSECT			6
	4 |   SPEC  |	      |	<     4		FSECT			6
	  |  (0-7)  |  (8-11) |	 |    5		DSECT			6
	  |	    |	      |	 |    6-7	UNUSED			-
	  |-------------------|	 |    10	XSECT			6
	5 | VALUE, RELOCATION |	 |    11	ZSECT			6
	  |	OR LENGTH     |	 |    12-13	UNUSED			-
	  |-------------------|	 |    14	ENTRY POINT		5
	  |		      |  |    15	GLOBAL SYMBOL		5
	6 |   ORIGIN SPEC.    |	 |    16	EXTERN			4
	  |		      |  |    17	ZTERN (External Page 0)	4
	  ---------------------	 \

			 Figure 10-2 LSD Entry Format



     The fifth word contains the length of a program section if the  symbol
     is a program section name, otherwise it has an offset or a value.

     The sixth word of the LSD entry contains origin restrictions.  For  an
     .ASECT, it is the absolute origin, for other program section types, it
     depends on the contents of bit 0 through 2 of word 4.



     10.2.3  Text Description

     The text is divided into segments.  Each segment contains a flag  word
     followed  by one to six entries.  An entry may be one or more words in
     length.  In the event a segment overflows a block, the  current  entry
     is  completed  in the next block.  There are no other entries for that
     segment and the remaining flag fields are ignored.

     The flag word is made up of six, two-bit  flag  fields,  as  shown  in
     Figure 10-3.  Each field corresponds to an entry.


	 -------------------------------------------------------------
	 | FIELD 0 | FIELD 1 | FIELD 2 | FIELD 3 | FIELD 4 | FIELD 5 |
	 -------------------------------------------------------------
	0	  2	    4	      6		8	 10        12

			    Figure 10-3 Flag Words



				     10-4

			   ADVANCED TECHNICAL TOPICS


     10.2.3.1  Flag Field Meaning - The words in the flag field are defined
     as follows:

       Word				 Meaning       ____				 _______

	 0     No relocation.  The entry loads as it is.

	 1     12-bit relocation.  The base address of the current  program
	       section is added to the entry.

	 2     7-bit relocation.  Assume the entry is  a  memory  reference
	       instruction  and add the low order seven bits of the current
	       program section's address.

	 3     Special loader code entry.  Each special loader code has two
	       fields (See Figure 10-4):

	       a.  Bits 0-3 contain the loader instruction (see Tables 10-2
	           and 10-3).

	       b.  Bits 4-11 contain an LSD reference.


		    --------------------------------------
		    |    LOADER   |    LSD REFERENCE     |
		    | INSTRUCTION | EXTENDED LOADER CODE |
		    --------------------------------------
		     0		   4

			    Figure 10-4 Loader Code



     10.2.3.2  Loader Codes Generated  by  MACREL - Tables  10-3  and  10-4
     define  the  codes  generated by MACREL that instruct LINK how to load
     your program.


				  Table 10-3	
			   MACREL/LINK Loader Codes

     ----------------------------------------------------------------------
     |  Code  |				Meaning				  |
     |--------|-----------------------------------------------------------|
     |	0     |	The LSD reference  field  contains  an  extended  loader  |
     |	      |	instruction.  See Extended Loader Code.			  |
     |	      |								  |
     |	1     | 12-bit relocation - the  next  word  is  data,  add  the  |
     |	      |	value of the LSD word that is referenced.		  |
     |	      |								  |
     |	2     | The next word is data - add the field of  the  LSD  word  |
     |	      |	that is referenced after shifting left 3 places.	  |
     ----------------------------------------------------------------------
						 (continued on next page)

				     10-5

			   ADVANCED TECHNICAL TOPICS


			      Table 10-3 (Cont.)
			   MACREL/LINK Loader Codes

     ----------------------------------------------------------------------
     |  Code  |				Meaning				  |
     |--------|-----------------------------------------------------------|
     |	3     | Load a ZBLOCK.  The LSD  reference  field  contains  the  |
     |	      |	length  of  the  block  in  one's  complement.  The next  |
     |	      |	word contains the  value  that  is  to  be  loaded  into  |
     |	      |	each word of the block.					  |
     |	      |								  |
     |	4     | Begin  (or  continue)  loading  data  for  the   program  |
     |	      |	section specified by the LSD reference.			  |
     |	      |								  |
     |	5     | The next word is data.  Add the value of  the  LSD  word  |
     |	      |	that is referenced, then:				  |
     |	      |								  |
     |	      |	a.  Verify that  the  LSD  reference  is  in  the  range  |
     |	      |	    0-177.						  |
     |	      |								  |
     |	      |	b.  Verify that the sum of the low  order  bits  of  the  |
     |	      |	    data  word  plus  the  value of the LSD reference is  |
     |	      |	    in the range 0-177.					  |
     |	      |								  |
     |	      |     If either condition  fails,  produce  error  message  |
     |	      |	    indicating Page 0 reference is not on Page 0.	  |
     |	      |								  |
     |	      |				  NOTE				  |
     |	      |								  |
     |	      |		The following instruction codes (6 to 12)	  |
     |	      |		require  the  use of a first in, last out	  |
     |	      |		stack.						  |
     |	      |								  |
     |	6     | The next word is a  12-bit  constant.   Add  it  to  the  |
     |	      |	value  of  the  LSD reference, and push results onto the  |
     |	      |	stack.							  |
     |	      |								  |
     |	7     | The  LSD   field,   contains   an   8-bit   non-negative  |
     |	      |	constant.  Push it onto the stack.			  |
     |	      |								  |
     |	10    | Push the instruction field of  the  LSD  reference  onto  |
     |	      |	the stack.						  |
     |	      |								  |
     |	11    | Pop a value off the stack.  The result is the new  value  |
     |	      |	of  the  LSD  reference.   The LSD reference should be a  |
     |	      |	global symbol, a SECT name is a system error.		  |
     |	      |								  |
     |	12    |	Push the value of the LSD reference onto the stack.	  |
     |	      |								  |
     |  13-17 | Not used						  |
     ----------------------------------------------------------------------




				     10-6

			   ADVANCED TECHNICAL TOPICS


				  Table 10-4
		       Extended MACREL/LINK Loader Codes

     ----------------------------------------------------------------------
     |	 Code   |			 Meaning			  |
     |----------|---------------------------------------------------------|
     |	   0	|  End of text						  |
     |		|							  |
     |	   1	|  The next word is a 12-bit  origin.   This  origin  is  |
     |		|  relative to the base of the current program section.	  |
     |		|							  |
     |	   2	|  Pop a word from the stack, then load it.		  |
     |		|							  |
     |	   3	|  The next word is a 12-bit constant, push it onto  the  |
     |		|  stack.						  |
     |		|							  |
     |	   4	|  Negate the top of the stack.				  |
     |		|							  |
     |		|							  |
     |		|			  NOTE				  |
     |		|							  |
     |		|	Extended  Codes  5-12  represent  binary	  |
     |		|	operations  to be applied to the top two	  |
     |		|	entries on the stack.  The two words are	  |
     |		|	popped  off  the  stack, the first being	  |
     |		|	the second argument to the operator  and	  |
     |		|	the  result  is  pushed  back  onto  the	  |
     |		|	stack.						  |
     |		|							  |
     |		|							  |
     |	   5	|  Add							  |
     |		|							  |
     |	   6	|  Subtract						  |
     |		|							  |
     |	   7	|  Multiply						  |
     |		|							  |
     |	   10	|  Divide						  |
     |		|							  |
     |	   11	|  Inclusive or						  |
     |		|							  |
     |	   12	|  And							  |
     |		|							  |
     |	   13	|  Left Shift						  |
     |		|							  |
     |	   14	|  Push current  program  section's  level  and  overlay  |
     |		|  numbers onto the stack (see Section 4.9.8).		  |
     |		|							  |
     |	   15	|  Next word is absolute origin				  |
     |		|							  |
     |	   16	|  Switch top two entries on stack			  |
     |		|							  |
     |	   17	|  Pop a word from stack, make it new origin		  |
     ----------------------------------------------------------------------


				     10-7

			   ADVANCED TECHNICAL TOPICS


     10.3  LINK PERFORMANCE

     LINK requires at least 12K words of memory, and runs  under  OS/8  V3D
     (or  a  later  version).  LINK uses the memory between 12K and 32K for
     additional symbol table space.  The approximate  size  of  the  symbol
     table with different memories is shown in Table 10-5.


				  Table 10-5
			    LINK Symbol Table Size

		----------------------------------------------
		| Memory Size     | Number of Global Symbols |
		| 12K		  |	       256	     |
		| 16K		  |	       512	     |
		| 20K		  |	       768	     |
		| 24K		  |	       1024	     |
		| 28K		  |	       1536	     |
		| 32K		  |	       2048	     |
		----------------------------------------------
     LINK's symbol table will be diminished by about 192 symbols  if  BATCH
     is  running.   For example, if BATCH is running in 12K of memory, only
     about 64 GLOBAL symbols may be used.



     10.3.1  LINK Processing of Program Section Definitions

     LINK normally expects that all object modules  have  program  sections
     that are uniquely named.  It will, however, process like-named program
     sections (and library pieces) from different object modules if, on the
     first encounter of the program section name, the section is completely
     defined with all of its characteristics (type, field or page
     restrictions, size).

     On subsequent encounters in other object modules LINK checks,  and  if
     necessary, increases the size characteristic of the program section or
     library piece.

     LINK assumes that  a  like-named  program  section  or  library  piece
     overlays  if  the  first  definition  of  the program section or piece
     contains the maximum size  of  the  same  name  program  section.   If
     subsequent  definitions  contain  a  larger  size characteristic, LINK
     performs a rudimentary  concatenation,  but  only  if  the  subsequent
     definition  resides  at  an address higher than the highest address of
     the smaller same name program section or piece.  This cannot  be  done
     for  .ASECTs  because LINK does not check for the lowest address of an
     .ASECT.



     10.4  LINK LIBRARY

     A LINK library is a file that is a  concatenation  of  the  individual

				     10-8

			   ADVANCED TECHNICAL TOPICS


     relocatable  binary  files output by MACREL.  The OS/8 utility program
     PIP (with the /I option) performs the concatenation.  The file  cannot
     be  greater than 255(10) blocks.  The library file (.RB extension) may
     be composed of several pieces, each of which is one  of  the  original
     files  used  to  build the library.  Each piece in the library has its
     own LSD and text (see Figure 10-5).


			   CONCATENATED LIBRARY FILE
	-------------------------------------------   ---------
	| PIECE | PIECE | PIECE | PIECE | PIECE  /.../  PIECE |  LIBR.RB
	-----------------------------------------   -----------
	    ^
	    |		--------------
	    ----------->| LSD | TEXT |
			--------------
			ANY ONE PIECE

			Figure 10-5 Library File Format


     Library files must be specified to  LINK  explicitly.   LINK  searches
     them  for  missing  global symbols and entry names.  LINK searches the
     default library LNKLIB.RB (if it exists) last to resolve any undefined
     symbols that remain.

     These files are processed after all non-library modules and then  only
     if  there  are  undefined  symbols.   Library  files  are  searched as
     follows:

	  1.  If no undefined symbols remain to be defined, LINK terminates
	      the library.

	  2.  LINK reads the next LSD from the library file and searches it
	      for  undefined  symbols.   If it can resolve any, it adds the
	      LSD to the Global Symbol Table.

	  3.  Because backward references are allowed,  LINK  searches  the
	      library  file  repeatedly.  LINK terminates the search when a
	      pass through the  library  fails  to  resolve  any  undefined
	      symbols.   This search method allows modules to appear in any
	      order in the library file.   You  can  significantly  shorten
	      LINK   execution  time  if  your  modules  have  no  backward
	      references.



     10.5  WRITING AND USING OVERLAYS

     Overlays are pieces of the  program  module  that  reside  on  a  file
     structured  device  such as disk or DECtape.  The overlay driver reads
     them into memory for execution  as  they  are  needed.   The  previous
     contents,  of  the  memory  where the overlay is loaded, are lost.  An
     existing overlay is not copied back onto the device when a new overlay

				     10-9

			   ADVANCED TECHNICAL TOPICS


     is brought in.  Thus, the overlay is always brought into memory in the
     same condition in which it was assembled and linked.

     Overlays are defined either by command string options to  LINK  or  by
     MACREL's  LEVEL and OVERLAY options to the program section directives.
     Once you have defined them, they are relatively  invisible.   Assuming
     SUBR resides in an overlay, the code:

	  .EXTERNAL SUBR
	  CIF SUBR
	  JMS I (SUBR

     causes the program to bring in the overlay and perform the JMS to  it.
     This  is  handled  automatically  by  the  overlay  driver, which is a
     program section loaded by LINK to swap overlays in and out of the main
     program  (see Section 10.5.3).  The JMS, of course, stores the correct
     return address of the calling  program  in  the  entry  point  of  the
     overlay.

     Figure 10-6 shows the overlay structure of  MACREL/LINK.   When  using
     overlays,  memory  is  divided  into  a main (or root) program segment
     (MAIN), which is always in memory, and up  to  seven  different  areas
     called  levels.   The  different  levels  are  loaded into consecutive
     memory areas (barring user-established loading restrictions) with MAIN
     starting  at  an  address  supplied  by  you.   Thus, Level 7 (if any)
     normally occupies the highest area in memory.

     The levels are not associated with fields, and are not fixed in  size.
     Main  (implied  level 0) and the other levels may be of any size.  The
     size of each level, except MAIN, is the size of  the  largest  overlay
     for that level, but cannot be larger than one field.

     For each level, you can define up to 16 (decimal) overlays.  Only  one
     of  these  overlays  may  be in memory at a given time.  Notice that a
     given overlay has both a level number and an overlay number.  A  given
     overlay will only be used at the level for which it is defined.  Thus,
     a Level 3 overlay will not be used in a Level 4 memory area.  The code
     however,  may be loaded twice, once as Level 3 and once as Level 4, as
     long as there are no conflicting GLOBAL or ENTRY addresses.   Further,
     if  you are going to use LINK's command string options to do this, two
     copies of the code must exist and be in separate modules.  If  instead
     you  use  the  OVERLAY  and  LEVEL  options  of  the  program  section
     directives, the separate copies and modules are not necessary.



     10.5.1  Writing Overlay Code

     In writing overlays, you must define all entry points  in  the  called
     overlay  as  .ENTRY  and  in  the calling overlay (or main program) as
     .EXTERNAL.

     You should use the CIF/CDF instruction (see Sections 7.2.5 and  7.2.6)
     to change the fields of the calling and called overlays.

				     10-10

			   ADVANCED TECHNICAL TOPICS


					           ----------------
					           |  OVERLAY 17  |
					         ---------------- |
				                 |  OVERLAY 17  | |
				               ---------------- | |
				               |  OVERLAY 17  | | |
				             ---------------- | | |
				             |  OVERLAY 17  | | | |
				           ---------------- | | | |
				           |  OVERLAY 17  | | | | |
				         ---------------- | | | | |
				         |  OVERLAY 17  | | | | | |
				       ---------------- | | | | | |
				       |  OVERLAY 17  | | | | | | |
				       |--------------| | | | | | |
				       |  OVERLAY 16  | | | | | | |
				       |--------------| | | | | | |
				       |  OVERLAY 15  | | | | | | |
				       |--------------| | | | | | |
				       |      .       | | | | | | |
				       |      .       | | | | | | |
				       |      .       | | | | | | |
				       |--------------| | | | | | |
				       |  OVERLAY 10  | | | | | | |
     -----------------		       |--------------| | | | | | |
     |    LEVEL 7    | HIGH MEMORY     |  OVERLAY 7   | | | | | | |
     |---------------|		       |--------------| | | | | | |
     |    LEVEL 6    |		       |  OVERLAY 6   | | | | | | | LEVEL 7
     |---------------|		       |--------------| | | | | |--
     |	  LEVEL 5    |		       |  OVERLAY 5   | | | | | | LEVEL 6
     |---------------|		       |--------------| | | | |--
     |	  LEVEL 4    |		       |  OVERLAY 4   | | | | | LEVEL 5
     |---------------|		       |--------------| | | |--
     |	  LEVEL 3    |		       |  OVERLAY 3   | | | | LEVEL 4
     |---------------|		       |--------------| | |--
     |	  LEVEL 2    |		       |  OVERLAY 2   | | | LEVEL 3
     |---------------|		       |--------------| |--
     |    LEVEL 1    |		       |  OVERLAY 1   | | LEVEL 2
     |---------------|		       |--------------|--
     |     MAIN      | LOW MEMORY      |  OVERLAY 0   | LEVEL 1
     -----------------		       ----------------
      INTERNAL MEMORY		       EXTERNAL STORAGE

         Figure 10-6 MACREL/LINK Overlay Structure (numbers in octal)


     The restrictions on calling overlays are illustrated in  Figure  10-7.
     JMS's are allowed in either direction between MAIN and any overlay.

     Any overlay may call any other overlay having a higher  level  number.
     However, an overlay may not call an overlay with a lower level number.
     For example, an overlay at Level 7 cannot call any other  overlay,  it
     can only call the main program.
		

				     10-11

			   ADVANCED TECHNICAL TOPICS


		      ALLOWED			  NOT ALLOWED
			      -------------------
			      |     LEVEL 7	|
			      |-----------------|
		      --------|			|----
		      |	  --->|     LEVEL 6     |   |
		      |	  |   |-----------------|   |
		      |	  |   |     LEVEL 5	|<---
		      |	  |   |-----------------|
		      |	  ----|			|
		      |	  --->|     LEVEL 4     |----
		      |	  |   |-----------------|   |
		      |	  ----|     LEVEL 3     |   |
		      |	      |-----------------|   |
		      |	  --->|     LEVEL 2     |   |
		      |	  |   |-----------------|   |
		      |	  |   |     LEVEL 1     |<---
		      |	  |   |-----------------|
		      |   ----|			|
		      ------->|      MAIN       |
			      -------------------

	    Figure 10-7 Permissible JMS's Between MAIN and Overlays


     These restrictions protect the return path to the calling  level.   If
     any overlay could call any other overlay, there is a strong likelihood
     that some of the  return  locations  would  be  overwritten  producing
     erratic results when the program is run.

     Since you may not know the memory  field  or  level  of  a  particular
     routine  in  an  overlay structure, you should adhere to the following
     rules for communicating between overlays.

	  1.  Do not use CDF,  TAD,  ISZ,  DCA,  or  AND  with  a  symbolic
	      argument   that   is   defined  as  an  entry  point  (.ENTRY
	      directive).

	  2.  Do use CDF, TAD, ISZ, DCA,  and  AND  only  with  a  symbolic
	      argument,  that is, a program section name or a global symbol
	      (.GLOBAL directive).

	  3.  Do use CIF, JMP, or JMS only with a symbolic argument that is
	      defined  as an entry point.  Do not use program section names
	      or global symbols.

     The  following  example  shows  a  generalized  coding  sequence  that
     guarantees access to an overlay that is not in memory.







				     10-12

			   ADVANCED TECHNICAL TOPICS


	    "MAIN" or Other Overlay			Overlay 5, Level 3

	  .EXTERNAL SUBR				    .ENTRY SUBR
	  CDF .FLD					    SUBR 0
	  CIF SUBR					      .
	  JMS I (SUBR					      .
	      .						      .
	      .						      .
	  other code					    JMP I SUBR
	      .							.
	      .							.
	  CDF TABLE	   accesses a				.
	  TAD I (TABLE	   table once			    TABLE,  val1
			   overlay is				    val2
			   in memory.				    val3
								     .
								     .

     You should fully debug your code as  MAIN  before  placing  it  in  an
     overlay.   This is because the OS/8 octal debugging program (ODT) does
     not allow you to put breakpoints in overlays, thus making debugging in
     an overlay system very difficult.

     Other than these restrictions, there is no difference between  writing
     overlays and writing other subroutines.



     10.5.2  How Overlays Work

     When you perform a JMS to an entry point in a  module  that  has  been
     defined  as an overlay, the JMS is not to the module directly but to a
     table called the transfer vector table in the  overlay  driver.   Each
     transfer  vector  in  the  table  (corresponding  to  one entry in one
     overlay) consists of four words, as shown in Figure 10-8.


			-------------------------------------
		WORD 1  |	       ISZ "FLAG"	    |
			|-----------------------------------|
		WORD 2	|	       JMS I "POINTER"	    |
			|-----------------------------------|
			|   |2     4|5           8|9      11|
			|-----------------------------------|
		WORD 3	|   | LEVEL | OVERLAY NO. |  FIELD  |
			|-----------------------------------|
		WORD 4  |   MEMORY ADDRESS FOR THAT ENTRY   |
			-------------------------------------

		       Figure 10-8 Transfer Vector Table


     For example, if you code a JMS to an  entry  labelled  IN  in  another
     module,  the  actual  JMS will be to word 1 of the transfer vector for

				     10-13

			   ADVANCED TECHNICAL TOPICS


     that particular entry.  This stores the return address in word one and
     performs   the   following   instruction:    JMS  I  'POINTER'.   This
     instruction causes the program to jump to  the  overlay  driver.   The
     driver  picks  up  the  following  word  containing the overlay level,
     overlay number, and field and checks to see  if  that  overlay  is  in
     core.   If  it  is  not, the overlay driver brings it in.  The overlay
     driver then stores the correct return address at the entry  point  and
     performs a JMP to the entry point plus one.  The exit from the overlay
     is made, without going through the transfer vector again.

     If you write a JMP, the ISZ 'FLAG' instruction is executed.  This sets
     a  flag  that  tells  the overlay driver to perform a JMP instead of a
     JMS.  Control then returns to the address of the entry point,  instead
     of the entry point address plus one.

     In practice, this is handled automatically and is  invisible  to  you.
     You code JMS I (IN) and execution begins at the code starting at IN as
     if the module had always been in memory.



     10.5.3  Overlay Driver

     The overlay driver module (OVRDRV.MA Version 2A) is a program that you
     must  LINK into your program, if you are using LINK's overlay feature.
     It is supplied as source module so that, if desired,  you  can  modify
     the  size  of  the  transfer  vector  table  (designated TRANVC in the
     module).  There will be a 4-word entry in the table for  every  .ENTRY
     specified   in  your  program  that  is not in level 0.  Initially the
     TRANVC table is set up to  hold  24  (decimal)  vectors  but  you  can
     increase  the  table  size  to hold 511 (decimal) vectors which is the
     maximum supported  by  LINK.   If  your  program  requires  more  than
     twenty-four  vectors, LINK will automatically increase the size of the
     table (up to 511) as required.



     10.6  SAVE FILE FORMAT

     The save file (.SV extension)  is  LINK's  primary  output  file.   It
     begins with the Memory Control Block illustrated in Figure 10-9.














				     10-14

			   ADVANCED TECHNICAL TOPICS


     Location		    Contents		       Notes

		      MEMORY CONTROL BLOCK
	    ---------------------------------------
	0   | MINUS THE NUMBER OF MEMORY SEGMENTS |
	    |-------------------------------------|    62N3 WHERE N IS THE
	1   |	   CDF CIF (STARTING FIELD)	  |<-- STARTING FIELD
	    |-------------------------------------|
	2   |	       STARTING ADDRESS		  |
	    |-------------------------------------|
	3   |	       JOB STATUS WORD		  |
	    |-------------------------------------|---
        4   |					  |  | MEMORY SEGMENT
	    |-------------------------------------|  |CONTROL DOUBLE WORDS
	95  |					  |  |
            |-------------------------------------|---
	96  |					  |    OVERLAY STORAGE
	    |					  |    INFORMATION
	    |-------------------------------------|
	127 |					  |
	    ~					  ~    REMAINDER OF BLOCK
	377 |					  |    IS UNUSED
        (8) ---------------------------------------

		       Figure 10-9 Memory Control Block


     The Memory Control Block consists of 256 words and has  the  following
     format:

       Word			     Contents       ____			     ________

	  0	     Two's complement number of memory segments
	  1	     Starting Field
	  2	     Starting Address
	  3	     Job Status Word
       4- 95	     Memory Segment Control Double Words
      96-127	     Overlay storage information
     128-255	     Empty

     The format of the Job Status Word (word 3) is as follows:

     Bit Condition			   Meaning     _____________			   _______

       Bit 0 = 1    File does not load into locations 0 to 1777 in field 0.

       Bit 1 = 1    File does not load into locations 0 to 1777 in field 1.

       Bit 2 = 1    Program must be reloaded before it can be restarted.

       Bit 3 = 1    Program never uses above 8K.  This is used  when  BATCH
		    processing is active.

       Bit 4 = 1    Program contains overlays created by LINK.

				     10-15

			   ADVANCED TECHNICAL TOPICS


       Bit 10 = 1   Locations 0 to 1777 in field 0 need not be	  preserved
		    when the Command Decoder is called.

       Bit 11 = 1   Locations 0 to 1777 in field 1 need  not  be  preserved
		    when the USR is called.

     If the object module is overlayed, LINK will automatically set  bit  4
     (0200) of the object module's Job Status Word to indicate the presence
     of overlays to system software.

     The Memory Segment Doublewords (words 4-95) control  the  reading  and
     writing  of  the associated areas of memory.  The format of each entry
     is shown in Figure 10-10:


     Location		   Contents			Notes
	   -------------------------------------------
	1  |		MEMORY ORIGIN		     |	MULTIPLE OF 400(8)
	   |-----------------------------------------|
	   |  |  NUMBER OF PAGES  |  FIELD  |	     |  BITS 0 AND 9-11
	2  |  |	TO LOAD		  | TO LOAD |        |	ARE ZERO
           -------------------------------------------
            0  1		 5 6	   8 9	   11

		   Figure 10-10 Memory Segment Double Words


     The memory loading address must be a multiple  of  400  (octal).   The
     Memory  Segment Control Doublewords are sorted within the header block
     in order of decreasing field and increasing  origin  within  the  same
     field.   There can be no more than 31 (decimal) Memory Segment Control
     Doublewords in any Memory Control Block.

     The Memory Control Block for the program at the time it is loaded into
     memory  is  always  saved  in words 200 (octal) through 377 (octal) of
     block 37 (octal) (one of the system  scratch  blocks)  on  the  system
     device.   There  are  no  memory  segment  double  words for overlays,
     because they are loaded at run time not load time.

     The overlay storage information (words 96-127) has a 4 word entry  for
     each  level  including  level 0 (MAIN).  The format is shown in Figure
     10-11:

			----------------------------------		
		WORD 1	|    NO. OF OVERLAYS IN LEVEL    |
			|--------------------------------|
		     2	|0	 4|       |6	 8|	 |
			| ADDRESS |       |  FLD  |	 |
			|--------------------------------|
		     3  |    RELATIVE STARTING BLOCK     |
			|--------------------------------|
		     4	|	LENGTH (IN PAGES)	 |
			----------------------------------		
			 Figure 10-11 Overlay Storage

				     10-16

			   ADVANCED TECHNICAL TOPICS


     10.7  MACRO LIBRARY

     Commonly used macros may be called  by  any  source  module  if  their
     definitions  reside  in  a  macro library file on DSK:.  The following
     paragraphs describe how you can create this library file.

     Create a file on DSK:, called MACLIB.MA, with the following code.

     .IF NDF .MCALL <

     .MACRO .MCALL A,B,C,D,E,F,G,H

     XLIST

     .IF NB A <$A=1>	     /conditional assembly that concatenates a
     .IF NB B <$B=1>	     /dollar sign($) with the name of your macro
     .IF NB C <$C=l>	     /passed as an actual argument to .MCALL.  Your
     .IF NB D <$D=1>	     /macro name passed with the call to .MCALL is
     .IF NB E <$E=1>	     /thus defined and satisfies the conditional
     .IF NB F <$F=1>	     /assembly (.IF DF) which is Part of Your
     .IF NB G <$G=1>	     /macro definition,
     .IF NB H <$H=1>
     .INCLUDE MACLIB.MA
     XLIST
     .ENDM .MCALL >
	    .
	    .
	    .
     .IF DF $YOUR0<
     .MACRO YOUR0 A,B,...H
	    .
	    .
	    .
     .ENDM YOUR0	     /YOUR0 through YOURnn, are the names of the
     EXPUNGE $YOUR0>	     /macro YOU define.  UP to eight macros can be
     .IF DF $YOUR1<	     /defined with each .MCALL
     .MACRO YOUR1 A,B,...H
	    .
	    .
	    .
     .ENDM YOUR1
     EXPUNGE $YOUR1>
	    .
	    .
	    .
     .IF DF $YOURnn<
     .MACRO YOURnn A,B,...H
	    .
	    .
	    .
     .ENDM YOURnn
     EXPUNGE $YOURnn >



				     10-17

			   ADVANCED TECHNICAL TOPICS


     The source module, which is to use one or more of the  macros  in  the
     library, must include the following code near its beginning:

     .NOLIST LN			   /do not list xlisted lines
     XLIST			   /turn listing off
     .INCLUDE MACLIB.MA		   /define the macro .MCALL which is
				   /contained in MACLIB.MA
     XLIST			   /turn listing back on
     .MCALL YOUR0,YOUR1....YOUR7   /call .MCALL and selectively define
				   /macros in MACLIB.MA

     The .INCLUDE MACLIB.MA causes the file MACLIB.MA to be read.   Because
     .MCALL  is, at this point undefined, the macro is processed and .MCALL
     is now defined.

     To define macros in the library, call the macro .MCALL with the  names
     of  your  macros as arguments.  For each macro named, .MCALL creates a
     symbol with the macro name preceded  by  a  dollar  sign  ($).   Thus,
     .MCALL YOUR creates the symbol $YOUR.

     Each macro definition in MACLIB.MA is surrounded by a conditional test
     that  determines whether a symbol (the concatenation of $ and YOUR) is
     defined.  If defined, the condition is satisfied,  and  the  macro  is
     defined, then the created symbol is expunged from the symbol table.



     10.8  SETTING THE CURRENT LOCATION COUNTER TO AN UNKNOWN VALUE

     The Asterisk (*) directive (described in Section  5.4.1),  unlike  its
     counterpart  in  the  PAL8  assembler,  allows  you to set the current
     location counter to a value that is not known at assembly time.   This
     can  be  a  value  that  is  either  an  external  symbol or a complex
     relocatable expression.  This  feature  permits  you  to  modify  data
     values  in  a  table that exists in another assembly module.  You must
     specify any symbol (external or internal), whether used by  itself  or
     in  a  complex  relocatable expression, as an absolute offset from the
     beginning of the program section in which it resides.  There  are  two
     ways to do this:

	  1.  Specify the symbol as a global symbol with an absolute value.
	      For example:

	      Module 1			Module 2

		     TAB1==10		       .EXTERNAL TAB1
		     .DSECT TABLE	       .DSECT TABLE
		TAB, ZBLOCK 10		       *TAB1
		     ZBLOCK 20			 .
		       .			 .
		       .			 .

	  2.  Specify the symbol as a relocatable value and  calculate  the
	      absolute  offset  of  the  symbol  from  the beginning of the

				     10-18

			   ADVANCED TECHNICAL TOPICS


	      program section by subtracting the relocatable  part  of  the
	      symbol from its absolute part.  For example:

	      Module 1			Module 2
		     .DSECT TABLE	       .EXTERNAL TAB1
		     .GLOBAL TAB1	       .DSECT TABLE
		TAB, ZBLOCK 10		       *TAB1-TABLE
	       TAB1, ZBLOCK 20			 .
		       .			 .
		       .			 .

     During pass 1 LINK resolves all relocatable symbols to their  absolute
     values.   During  pass  2,  LINK  creates the save image and loads the
     code.

     In the first example, if LINK begins the  .DSECT  TABLE  at  2000,  it
     assigns  TABLE the value 2000.  TAB1 already has the value 10 that was
     calculated by MACREL.  When LINK encounters *TAB1, it  calculates  the
     absolute address of TAB1 by adding the value of TAB1 (10) to the value
     of TABLE (2000), giving the result 2010.

     In the second example, if LINK begins the .DSECT  TABLE  at  2000,  it
     assigns  TABLE  the  value 2000 and TAB1 the value 2010 (2000 plus the
     offset 10).  When LINK encounters the  expression  *TAB1-TABLE  during
     pass 2, it calculates the absolute value of TAB1 as follows:

	  1.  It subtracts the value of TABLE (2000) from  TAB1  (2010)  to
	      obtain the absolute offset of TAB1 (10) from the beginning of
	      the program section.

	  2.  It then adds the calculated absolute  offset  value  of  TAB1
	      (10)  to  the  value  of TABLE  (2000) to obtain the absolute
	      value of TAB1 (2010).

     Note that if the example did not use the expression  TAB1-TABLE,  LINK
     would  calculate the value of TAB1 incorrectly as 4010 (that is, value
     of TAB1 (2010) plus TABLE (2000)).

     Program sections that use the Asterisk (*) directive in this way  must
     not  contain  memory reference instructions, labels, or the period (.)
     special operator.  MACREL performs the following operations:

	  1.  MACREL generates codes to LINK  that  instruct  it  to  begin
	      loading at the address specified by the directive.

	  2.  It proceeds with assembly using this  value  until  it  finds
	      another  Asterisk  directive  that  has  a known value for an
	      argument.  For each unknown value, MACREL prints ???? in  the
	      current   location  counter  value  column  of  the  assembly
	      listing.

	  3.  MACREL outputs codes to LINK  that  instruct  it  to  compute
	      where the subsequent data items are to be loaded.


				     10-19

			   ADVANCED TECHNICAL TOPICS


     You must specify the actual length of  the  program  section  at  LINK
     execution  time  by  including  an  identically  named program section
     definition that specifies the actual length of all the pieces  of  the
     entire section as shown in the previous examples (Module 1).



















































				     10-20








				  APPENDIX A

			      ASCII CHARACTER SET



				   Table A-1
			      ASCII Character Set

     ----------------------------------------------------------------------
     | 7-bit  |		  |						  |
     | Octal  |		  |						  |
     | Code   |	Character |		    Remarks			  |
     |--------------------------------------------------------------------|
     |  000   |    NUL	  |  Null, tape feed, CONTROL/SHIFT/P.		  |
     |	001   |    SOH	  |  Start of heading; also SOM, start		  |
     |	      |		  |  of message, CONTROL/A.			  |
     |	002   |    STX	  |  Start of text; also EOA, end of		  |
     |	      |		  |  address, CONTROL/B.			  |
     |	003   |    ETX	  |  End of text; also EOM, end of		  |
     |	      |		  |  message, CONTROL/C.			  |
     |	004   |    EOT	  |  End of transmission (END); shuts		  |
     |	      |		  |  off TWX machines, CONTROL/D.		  |
     |	005   |    ENQ	  |  Enquiry (ENQRY); also WRU,			  |
     |	      |		  |  CONTROL/E.					  |
     |	006   |    ACK	  |  Acknowledge; also RU, CONTROL/F.		  |
     |	007   |    BEL	  |  Rings the bell. CONTROL/G.			  |
     |	010   |    BS	  |  Backspace; also FEO, format		  |
     |	      |		  |  effector; backspaces some			  |
     |	      |		  |  machines, CONTROL/H.			  |
     |	011   |    HT	  |  Horizontal tab. CONTROL/I.			  |
     |	012   |    LF	  |  Line feed or Line space (new line);	  |
     |	      |		  |  advances paper to next line,		  |
     |	      |		  |  duplicated by CONTROL/J.			  |
     |	013   |    VT	  |  Vertical tab (VTAB). CONTROL/K.		  |
     |	014   |    FF	  |  Form Feed to top of next page		  |
     |	      |		  |  (PAGE). CONTROL/L.				  |
     |	015   |    CR	  |  Carriage return to beginning of		  |
     |	      |		  |  line; duplicated by CONTROL/M.		  |
     |	016   |    SO	  |  Shift out; changes ribbon color to		  |
     |	      |		  |  red. CONTROL/N.				  |
     |	017   |    SI	  |  Shift in; changes ribbon color to		  |
     |	      |		  |  black. CONTROL/D.				  |
     |	020   |    DLE	  |  Data link escape. CONTROL/B (DC0).		  |
     |	021   |    DC1	  |  Device control 1, turns transmitter	  |
     |	      |		  |  (READER) on, CONTROL/Q (X ON).		  |
     |	022   |    DC2	  |  Device control 2, turns punch or		  |
     |	      |		  |  auxiliary on. CONTROL/R (TAPE, AUX		  |
     |	      |		  |  ON).					  |
     ----------------------------------------------------------------------
     	      		  			 (continued on next page)

				      A-1

			      ASCII CHARACTER SET


			       Table A-1 (Cont.)
			      ASCII Character Set

     ----------------------------------------------------------------------
     | 7-bit  |		  |						  |
     | Octal  |		  |						  |
     | Code   |	Character |		    Remarks			  |
     |--------------------------------------------------------------------|
     |	023   |    DC3	  |  Device control 3, turns transmitter	  |
     |	      |		  |  (READER) off, CONTROL/S (X OFF).		  |
     |	024   |    DC4	  |  Device control 4, turns punch or		  |
     |	      |		  |  auxiliary off. CONTROL/T (AUX		  |
     |	      |		  |  OFF).					  |
     |	025   |    NAK	  |  Negative acknowledge; also ERR,		  |
     |	      |		  |  ERROR. CONTROL/U.				  |
     |	026   |    SYN	  |  Synchronous file (SYNC). CONTROL/V.	  |
     |	027   |    ETB	  |  End of transmission block; also		  |
     |	      |		  |  LEM, logical end of medium.		  |
     |	      |		  |  CONTROL/W.					  |
     |	030   |    CAN	  |  Cancel (CANCL). CONTROL/X.			  |
     |	031   |    EM	  |  End of medium. CONTROL/Y.			  |
     |	032   |    SUB	  |  Substitute. CONTROL/Z.			  |
     |	033   |    ESC	  |  Escape. CONTROL/SHIFT/K.			  |
     |	034   |    FS	  |  File separator. CONTROL/SHIFT/L.		  |
     |	035   |    GS	  |  Group separator. CONTROL/SHIFT/M.		  |
     |	036   |    RS	  |  Record separator. CONTROL/SHIFT/N.		  |
     |	037   |    US	  |  Unit separator. CONTROL/SHIFT/O.		  |
     |	040   |    SP	  |  Space.					  |
     |	041   |    !	  |						  |
     |	042   |    "	  |						  |
     |	043   |    #	  |						  |
     |	044   |    $	  |						  |
     |	045   |    %	  |						  |
     |	046   |    &	  |						  |
     |	047   |    '	  |  Accent acute or apostrophe.		  |
     |	050   |    (	  |						  |
     |	051   |    )	  |						  |
     |	052   |    *	  |						  |
     |	053   |    +	  |						  |
     |	054   |    ,	  |						  |
     |	055   |    -	  |						  |
     |	056   |    .	  |						  |
     |	057   |    /	  |						  |
     |	060   |    0	  |						  |
     |	061   |    1	  |						  |
     |	062   |    2	  |						  |
     |	063   |    3	  |						  |
     |	064   |    4	  |						  |
     |	065   |    5	  |						  |
     |	066   |    6	  |						  |
     |	067   |    7	  |						  |
     |	070   |    8	  |						  |
     ----------------------------------------------------------------------
     	      		  			 (continued on next page)

				      A-2

			      ASCII CHARACTER SET


			       Table A-1 (Cont.)
			      ASCII Character Set

     ----------------------------------------------------------------------
     | 7-bit  |		  |						  |
     | Octal  |		  |						  |
     | Code   |	Character |		    Remarks			  |
     |--------------------------------------------------------------------|
     |	071   |    9	  |						  |
     |	072   |    :	  |						  |
     |	073   |    ;	  |						  |
     |	074   |    <	  |						  |
     |	075   |    =	  |						  |
     |	076   |    >	  |						  |
     |	077   |    ?	  |						  |
     |	100   |    @	  |						  |
     |	101   |    A	  |						  |
     |	102   |    B	  |						  |
     |	103   |    C	  |						  |
     |	104   |    D	  |						  |
     |	105   |    E	  |						  |
     |	106   |    F	  |						  |
     |	107   |    G	  |						  |
     |	110   |    H	  |						  |
     |	111   |    I	  |						  |
     |	112   |    J	  |						  |
     |	113   |    K	  |						  |
     |	114   |    L	  |						  |
     |	115   |    M	  |						  |
     |	116   |    N	  |						  |
     |	117   |    O	  |						  |
     |	120   |    P	  |						  |
     |	121   |    Q	  |						  |
     |	122   |    R	  |						  |
     |	123   |    S	  |						  |
     |	124   |    T	  |						  |
     |	125   |    U	  |						  |
     |	126   |    V	  |						  |
     |	127   |    W	  |						  |
     |	130   |    X	  |						  |
     |	131   |    Y	  |						  |
     |	132   |    Z	  |						  |
     |	133   |    [	  |  SHIFT/K.					  |
     |	134   |    \	  |  SHIFT/L.					  |
     |	135   |    ]	  |  SHIFT/M.					  |
     |	136   |    ^	  |  *						  |
     |	137   |    _	  |  **						  |
     |	140   |    `	  |  Accent grave.				  |
     |	141   |    a	  |						  |
     |	142   |    b	  |						  |
     |	143   |    c	  |						  |
     |	144   |    d	  |						  |
     ----------------------------------------------------------------------
     	      		  			 (continued on next page)

				      A-3

			      ASCII CHARACTER SET


			       Table A-1 (Cont.)
			      ASCII Character Set

     ----------------------------------------------------------------------
     | 7-bit  |		  |						  |
     | Octal  |		  |						  |
     | Code   |	Character |		    Remarks			  |
     |--------------------------------------------------------------------|
     |	145   |    e	  |						  |
     |	146   |    f	  |						  |
     |	147   |    g	  |						  |
     |	150   |    h	  |						  |
     |	151   |    i	  |						  |
     |	152   |    j	  |						  |
     |	153   |    k	  |						  |
     |	154   |    l	  |						  |
     |	155   |    m	  |						  |
     |	156   |    n	  |						  |
     |	157   |    o	  |						  |
     |	160   |    P	  |						  |
     |	161   |    q	  |						  |
     |	162   |    r	  |						  |
     |	163   |    s	  |						  |
     |	164   |    t	  |						  |
     |	165   |    u	  |						  |
     |	166   |    v	  |						  |
     |	167   |    w	  |						  |
     |	170   |    x	  |						  |
     |	171   |    y	  |						  |
     |	172   |    z	  |						  |
     |	173   |    {	  |						  |
     |	174   |    |	  |						  |
     |	175   |    }	  |  This code generated by ALTMODE		  |
     |	176   |    ~	  |  This code generated by PREFIX key if present |
     |	      |		  |						  |
     |	177   |    DEL	  |  DELETE, RUBOUT.				  |
     ----------------------------------------------------------------------
     *  ^ appears as +on some machines.
     
     **  _ (underscore) appears as <- on some machines.















				      A-4







				  APPENDIX B

		       MACREL-PAL8 COMPATIBILITY SUMMARY



     PAL8 Features Incompatible with MACREL:

	  o  Dollar Sign ($) is treated differently.

	  o  DTORG is not implemented.

	  o  MACREL does not remember current page literals if you set  the
	     current location counter to an off page address and back.

	  o  No special terminal support  (listing  assumes  output  device
	     supports tab and form feed).

	  o  Right parenthesis ()) is not ignored. This ends  current  page
	     literal.

	  o  Right square bracket (]) is not ignored. This ends  page  zero
	     literal.

	  o  No  /B  or  /F  switches.  These  are  replaced   by   .ENABLE
	     conditions.

	  o  No /D switch.

	  o  No /H switch.

	  o  No /X switch (unnecessary).

	  o  No /T switch.

	  o  CIF and  CDF  will  behave  differently  if  used  in  unusual
	     circumstances;   for  example,  CDF+A  or TAD CDF may assemble
	     differently under MACREL.

	  o  A program section cannot contain 4096 words of code.












				      B-1

		       MACREL-PAL8 COMPATIBILITY SUMMARY


     MACREL Features Incompatible with PAL8:

     The following directives are incompatible with PAL8.

	  .ASECT			     .LEVEL
	  .CHAIN			     .LIST
	  .DISABL			     .LISTWD
	  .DSECT			     .MACRO
	  EDF				     .MEXIT
	  .ENABLE			     .NARGS
	  .ENABWD			     .NCHAR
	  .ENDM				     .NOLIST
	  .ENDR				     .POP
	  .ENTRY			     .PUSH
	  EXPUNGE			     .RADIX
	  .EXTERNAL			     .REPT
	  .FLD				     .RSECT
	  .FSECT			     .SBTTL
	  .GLOBAL			     .SECT
	  .IF				     .SECT *
	  .INCLUDE			     .START
	  .JSW				     .TITLE
	  .VERSION			     .ZSECT
	  .XSECT			     .ZTERNAL

     The following features are incompatible with PAL8.

	  Local Symbols			     Dot (as radix override)
	  Uparrow B			     Dot and dollar sign in symbols
	  Uparrow D			     Keyword PAGE and LOC
	  Uparrow O			     Double equal sign
	  KREF

     The following control options are incompatible with PAL8.

	  /A   /M   /Q   /X
	  /B   /O   /R   = nnn
	  /L   /P   /Z

     Overlays,  LINK  libraries,  and  all   LINK   control   options   are
     incompatible with PAL8 and ABSLDR.














				      B-2







				  APPENDIX C

			 MACREL PERMANENT SYMBOL TABLE


	Mnemonic       Octal
	 Symbol        Code			Operation	________       _____			_________

     Memory Reference Instructions

	  AND Y	       0000 	 Logical AND between Y and AC

	  TAD Y	       1000 	 Two's complement Add Y to AC

	  ISZ Y	       2000 	 Increment Y and skip if zero

	  DCA Y	       3000 	 Deposit at Y and clear AC

	  JMS Y	       4000 	 Jump to subroutine at Y

	  JMP Y	       5000 	 Jump to Y

     Operate Microinstructions

	  NOP	       7000 	 No operation. Causes a 1 cycle 
				 program delay.

	  IAC	       7001 	 Increment AC. The content of
				 the AC is incremented by one in
				 two's complement arithmetic.

	  RAL	       7004	 Rotate AC and L left. The con-
				 tent of the AC and the L are
				 rotated left one place.

	  RTL	       7006 	 Rotate two places to the left.
				 Equivalent to two successive
				 RAL operations.

	  RAR	       7010 	 Rotate AC and L right. The con-
				 tent of the AC and L are rotated
				 right one place.

	  RTR	       7012 	 Rotate two places to the right.
				 Equivalent to two successive
				 RAR operations.

	  CML	       7020 	 Complement L.




				      C-1

			 MACREL PERMANENT SYMBOL TABLE


	Mnemonic       Octal
	 Symbol        Code			Operation	________       _____			_________

	  CMA	       7040 	 Complement AC. The content of
				 the AC is set to the one's com-
				 plement of its current content.

	  CIA	       7041 	 Complement and increment ac-
				 cumulator. Used to form two's
				 complement.

	  CLL	       7100	 Clear L.

	  STL	       7120	 Set link. The L is set to contain
				 a binary 1.

	  CLA          7200	 Clear AC. To be used alone or in
				 OPR 1 combinations.

	  STA	       7240	Set AC to -1 (7777)

	  HLT	       7402	 Halt. Stops the program after
				 completion of the cycle in process.
				 If this instruction is com-
				 bined with others in the OPR 2
				 group, the other operations are
				 completed before the end of the
				 cycle.

	  OSR	       7404	 OR with switch register. The OR
				 function is performed between
				 the content of the SR and the
				 content of the AC, with the re-
				 sult left in the AC.

	  SKP	       7410	 Skip, unconditional. The next in-
				 struction is skipped.

	  SNL	       7420	 Skip if L is not = 0.

	  SZL	       7430	 Skip if L = 0.

	  SZA	       7440	 Skip if AC = 0.

	  SNA	       7450	 Skip if AC is not = 0.

	  SMA	       7500	 Skip on minus AC. If the content
				 of the AC is a negative number,
				 the next instruction is skipped.

	  SPA	       7510	 Skip on positive AC. If the con-
				 tent of the AC is a positive num-
				 ber, including zero, the next in-
				 struction is skipped.

				      C-2

			 MACREL PERMANENT SYMBOL TABLE


	Mnemonic       Octal
	 Symbol        Code			Operation	________       _____			_________


	  LAS	       7604	 Load AC with SR.

     Programmed Data Transfer Instructions

	  ION 	       6001	 Turn on interrupt.

	  IOF 	       6002	 Turn off interrupt.

     Teletype Keyboard/Reader

	  KSF	       6031	 Skip on keyboard flag.

	  KCC	       6032	 Clear keyboard flag, and AC, advance
				 reader.

	  KRS	       6034	 Read keyboard buffer static.

	  KRB	       6036	 Read keyboard buffer, clear flag.

     Teletype Teleprinter/Punch

	  TSF	       6041 	 Skip on teleprinter flag.

	  TCF	       6042 	 Clear teleprinter flag.

	  TPC	       6044 	 Load teleprinter and print.

	  TLS	       6046 	 Load teleprinter flag.

     Memory Extension

	  CDF	       62N1 	 Change to data field n (n=0 to 7).

	  CIF	       62N2 	 Change to instruction field N (N=0 to 7).

	  RDF	       6214 	 Read data field.

	  RIF	       6224 	 Read instruction field.

	  RIB	       6234 	 Read interrupt buffer.

	  RMF	       6244 	 Restore memory field.

     Extended Arithmetic Element

	  SCA	       7441 	 Step counter "OR" with AC.

	  SCL	       7403 	 Step counter load from memory.

	  MUY	       7405 	 Multiply.

				      C-3

			 MACREL PERMANENT SYMBOL TABLE


	Mnemonic       Octal
	 Symbol        Code			Operation	________       _____			_________


	  DVI	       7407 	 Divide.

	  NMI	       7411 	 Normalize.

	  SHL	       7413 	 Shift left.

	  ASR	       7415 	 Arithmetic shift right.

	  LSR	       7417 	 Logical shift right.

     The eight permanent symbols used with the EAE are  added  to  MACREL's
     Permanent Symbol Table by the /Q command string option.

     Permanent symbols shown  below  are  included  in  MACREL's  Permanent
     Symbol  Table. All of these permanent symbols are used in newer models
     of the PDP8 including PDP8/A, /E, /F, /M.  For  older  models  of  the
     PDP8,  they  can  be deleted from the Permanent Symbol Table by the /A
     command string option.

     Additional Microinstructions

	  BSW	       7002 	 Byte swap.

	  MQL	       7421 	 Load multiplier quotient.

	  MQA	       7501 	 Multiplier quotient OR into accumulator.

	  SWP	       7521 	 Swap accumulator and multiplier
				 quotient.

	  CAM	       7621	 Clear accumulator and multiplier
				 quotient (CLA MQL).

	  ACL	       7701	 Clear accumulator, load multiplier.

     Programmed Data Transfer Instructions

	  SKON	       6000	 Skip if interrupt on, IOF.

	  SRQ	       6003	 Skip if interrupt request.

	  GTF	       6004	 Get flags.

	  RTF	       6005	 Restore flag, ION.

	  SGT	       6006	 Skip if "greater than" flag is set.

	  CAF	       6007	 Clear all flags.



				      C-4

			 MACREL PERMANENT SYMBOL TABLE


	Mnemonic       Octal
	 Symbol        Code			Operation	________       _____			_________


     Reader/Punch Instructions

	  RPE	       6010	 Set reader/punch interrupt enable.

	  RSF	       6011	 Skip on reader flag.

	  RRB	       6012	 Read reader buffer.

	  RFC	       6014	 Reader fetch character.

	  PCE	       6020	 Clear reader/punch interrupt enable.

	  PSF	       6021	 Skip on punch flag.

	  PCF	       6022	 Clear punch flag.

	  PPC	       6024	 Load punch buffer and punch character.

	  PLS	       6026	 Load punch buffer sequence.

     Teletype Keyboard/Reader Instructions

	  KCF 	       6030 	 Clear keyboard flag.

	  KIE 	       6035 	 Set/clear interrupt enable.

     Teletype Teleprinter/Punch Instructions

  	  TFL	       6040	 Set teleprinter flag.

	  TSK	       6045	 Skip on printer or keyboard flag.

	  SPF	       6040	 Set teleprinter flag.

	  SPI	       6045	 Skip on printer or keyboard flag.

     All of the MACREL directives are  included  in  the  Permanent  Symbol
     Table. These directives are listed below.

	  .CHAIN	.LISTWD
	  DEVICE	.MACRO
	  .DISABLE	.MEXIT
	  EDF		.NARGS
	  EJECT		.NCHAR
	  .ENABLE	.NOLIST
	  .ENABWD	PAGE
	  .ENTRY	.POP
	  EXPUNGE	.PUSH
	  .EXTERNAL	.RADIX
	  FIELD		.RELOC

				      C-5

			 MACREL PERMANENT SYMBOL TABLE


	Mnemonic       Octal
	 Symbol        Code			Operation	________       _____			_________


	  FILENAME	.REPT
	  FIXMRI	.SBTTL
	  FIXTAB	.SECT
	  .FLD		.TITLE
	  .GLOBAL	TEXT
	  I		XLIST
	  .IF		Z
	  .INCLUDE	ZBLOCK
	  .LEVEL	.ZTERNAL

     There are 19 MACREL directives that you can eliminate from the  Symbol
     Table  with  the  /R  command  string  option.  The use of this option
     restricts the flexibility of MACREL but does not eliminate  its  MACRO
     features. These redundant symbols are listed below.

	  .ASECT
	  DECIMA
	  .DSECT
	  ENPUNCH
	  .FSECT
	  IFDEF
	  IFNDEF
	  IFNZRO
	  IFZERO
	  .JSW
	  .LIST
	  NOPUNCH
	  OCTAL
	  PAUSE
	  .RSECT
	  .START
	  .VERSION
	  .XSECT
	  .ZSECT

     The following additional symbols are deleted by the /R option:

	  GLK  7204
	  IOT  6000
	  OPR  7000











				      C-6







				  APPENDIX D

		       MACREL DIAGNOSTIC ERROR MESSAGES


     BE - INTERNAL STACK OVERFLOW (passes 1 and 2)

     BE - INTERNAL STACK UNDERFLOW (passes 1 and 2)

     DF - NO ROOM FOR OUTPUT

	  Meaning:  The output device became filled up. (passes 1 and 2)

	  Action:  The output file is closed. Assembly continues as if  end
	  of input file was encountered.

     DV - DIVIDE BY 0

     FA - FATAL MACRO ERROR
	  (passes 1 and 2)

     IC - BAD CHARACTER WHILE LOOKING FOR TASK NAME
	  (pass 1)

     IC - BAD CHAR, "x", AFTER ^

	  Meaning:  An invalid character occurred after  an  up-arrow.  The
	  only characters which may follow an up-arrow in an expression are
	  ", O, D, and R.  (pass 1)

	  Action:  The up-arrow is ignored.

     IC - BAD SUBSTRING?

     IC - CAN'T PERFORM INCLUDE CHARACTER ? AFTER LOGICAL END OF PSEUDO-OP

     IC - CHARACTER "x" AFTER LOGICAL END OF DIRECTIVE

	  Meaning:  The assembler found a legal  directive  on  this  line.
	  After  the  assembler  found  the  directive  to be completed, it
	  encountered the extraneous character "x" on the line. (pass 1)

	  Action:  The extra character is ignored.

     IC - EXTRA CHARS AFTER INCLUDE







				      D-1

		       MACREL DIAGNOSTIC ERROR MESSAGES


     IC - EXTRA RIGHT ANGLE BRACKET IGNORED

	  Meaning:  A   right   angle   bracket   (>)  was encountered with
	  no matching left angle bracket (<). (pass 1)

	  Action:  The right angle bracket character  is  ignored  and  the
	  assembly continues.

     IC - EXTRANEOUS CHARACTER ? AFTER END OF MACRO DIRECTIVE, MACRO #

     IC - ILLEGAL CHARACTER

     IC - ILLEGAL CHARACTER IN EXPUNGE

     IC - ILLEGAL CHARACTER IN FIXTAB

     IC - ILLEGAL CHARACTER ? IN .PUSH

     IC - ILLEGAL CHARACTER "x" AFTER INCLUDE

	  Meaning:  One or more characters (x) occurred after  an  .INCLUDE
	  directive but before the end of that statement. (pass 1)

	  Action:  The offending characters are ignored.

     IC - MISSING ANGLE BRACKET IN TEXT

	  Meaning:  Within a TEXT directive,  a  sub-item  was  begun  that
	  started with a left angle bracket (<), however, no matching right
	  angle bracket (>) was found. (pass 1)

	  Action:  The directive is aborted.

     IC - MISSING = AFTER FIXMRI

	  Meaning:  No equal sign was found after the symbol following  the
	  word  FIXMRI  in  a  FIXMRI  directive. The FIXMRI directive must
	  have the form:

	       FIXMRI symbol=expression

	  There may be spaces or  tabs  separating  the  4  parts  of  this
	  directive. (pass 1)

	  Action:  The character which was not an equal  sign  is  ignored,
	  and the scan continues to look for an equal sign.

     IC - MISSING = AFTER KEYWORD

     IC - NO DIGIT AFTER D, ^O, OR ^B





				      D-2

		       MACREL DIAGNOSTIC ERROR MESSAGES


     IC - NO MATCHING CLOSE ANGLE BRACKET (ONE ASSUMED)

	  Meaning:   While  parsing  an  expression,  a  subexpression  was
	  encountered  that  began  with  a  left  angle  bracket  (<). The
	  expression scan ended upon encountering a character that  is  not
	  legal  within  an  expression  and this character was not a right
	  (close) angle bracket (>). (pass 1)

	  Action:  MACREL assumes that a right angle  bracket  was  omitted
	  and the parse continues.

     IC - NO MATCHING >

     IC - NON-ALPHABETIC WHILE LOOKING FOR SYMBOL

	  Meaning:  A non-alphabetic  character  was  encountered  after  a
	  FIXMRI  directive.  The  argument  to  the  FIXMRI directive must
	  begin with a valid symbol. (pass 1)

	  Action:  The directive is aborted.

     IC - UNEXPECTED CHARACTER "x" WHILE LOOKING FOR EXPRESSION

	  Meaning:  The character "x" was encountered while  the  assembler
	  was  looking  for  an  expression.  This is not a legal character
	  which can appear at this place in the expression. (pass 1)

	  Action:  The character is ignored.

     IC - UNPRINTABLE CHARACTER <nnnn> BOUNDING TEXT MESSAGE

	  Meaning:  A non-printing character (other than space or tab)  was
	  encountered  as the delimiting character within a TEXT directive.
	  The octal ASCII representation for this character is nnnn.  (pass
	  1)

	  Action:  The character is ignored and the scan continues to  look
	  for a proper delimiter.

     IC - $ NOT ALLOWED IN DEVICE OR FILENAME

	  Meaning:  A dollar sign ($) character appeared  within  the  name
	  argument or a DEVICE or FILENAME directive. (pass 1)

	  Action:  The character is ignored.

     ID - MACRO name ALREADY IN USE

	  Meaning:  The name of a  macro  in  a  .MACRO  directive  already
	  exists,  but  not as macro. If this is desired, the previous name
	  should have first been EXPUNGEd. (pass 1)

	  Action:  The symbol is redefined to  be  a  macro.  Unpredictable 
	  results may occur.

				      D-3

		       MACREL DIAGNOSTIC ERROR MESSAGES


     ID - REDEFINED TAG, name

	  Meaning:  A symbol was defined by using it as a tag  (label)  and
	  it  had  a  prior value that is different from the current value.
	  (pass 1)

	  Action:   The  symbol  is  given  the  new  value  and   assembly
	  continues.

     IO - CAN'T DO INCLUDE FROM NON-FILE-STRUCTURED DEVICE

     IO - CHAIN ERROR
	  (passes 1 and 2)

     IO - DEVICE # DOES NOT EXIST

     IO - ENTER ERROR
	  (passes 1 and 2)

     IO - ERROR CLOSING FILE
	  (passes 1 and 2)

     IO - ERROR FETCHING HANDLER
	  (passes 1 and 2)

     IO - ERROR LOADING HANDLER
	  (passes 1 and 2)

     IO - ERROR READING FILE
	  (passes 1 and 2)

     IO - INPUT ERROR
	  (passes 1 and 2)

     IO - OUTPUT ERROR
	  (passes 1 and 2)

     IO - OVERLAY BAD

	  Meaning:  MACREL attempted to read in an overlay  and  either  an
	  I/O  error  was encountered while trying to read the file, or the
	  file was successfully read but contained bad contents,  i.e.  was
	  an invalid core image. (passes 1 and 2)

	  Action:  The pass is aborted.










				      D-4

		       MACREL DIAGNOSTIC ERROR MESSAGES


     IP - BAD TYPE OF SYMBOL

	  Meaning:  A symbol was encountered in an expression which had  an
	  erroneous  type.  For example, it was a macro name or the name of
	  a system directive. (pass 1)

	  Example:  TAD PAGE

	  Action:  The value of the symbol is treated as an absolute 0.

     IR - ILLEGAL REFERENCE

     LG - LINK GENERATED

	  Meaning:  The  user  specified  that  the  assembler  is  not  to
	  generate links. (pass 1)

	  Action:  A link is generated anyhow. The  program  will  probably
	  run.

     ME - MEXIT WHILE NOT IN MACRO

     NE - BAD DIGIT, "n", IN NUMBER FOR CURRENT RADIX

	  Meaning:  The digit specified is greater than  or  equal  to  the
	  current  radix.  For  example,  the  digit "8" would produce this
	  error if the current radix were octal. (pass 1)

	  Action:  The digit is allowed. For example,  the  string  473  in
	  base 5 would assemble as 4 times 25 plus 7 times 5 plus 3.

     NE - CONFLICTING RADIX OVERRIDE

	  Meaning:  A number was proceeded by  a  temporary  radix  control
	  operator  (^P, ^D, or ^B) and also was followed by the period (.)
	  decimal radix operator. For example:  TAD ^O345.+1. (pass 1)

	  Action:  The number is interpreted in the decimal radix.

     NE - NO DIGIT AFTER ^D, ^O, OR ^B

	  Meaning:  Within an expression, one of the local radix operators,
	  ^D,  ^O,  or  ^B  occurred  but was not followed immediately by a
	  digit.  These  operators  must   be   followed   by   a   number.
	  Intermediate spaces or tabs are not permitted. (pass 1)

	  Action:  The character which was not  a  digit  is  ignored.  The
	  scan  continues  to look for the number associated with the local
	  radix override.






				      D-5

		       MACREL DIAGNOSTIC ERROR MESSAGES


     NE - RADIX OUT OF RANGE

	  Meaning:  The (decimal)  value  of  the  expression  following  a
	  .RADIX  command  was  negative,  0,  1, or greater than 10. These
	  values are not permitted. The specified radix must be  between  2
	  and 10 inclusive. (pass 1)

	  Action:  The argument to the .RADIX directive is assumed to be 8,
	  i.e. the current radix is set to octal.

     NF - FILE # NOT FOUND OR DEVICE WRITE ONLY
	  (passes 1 and 2)

     NI - NOT YET IMPLEMENTED

	  Meaning:  The user attempted to use some feature that is not  yet
	  working in this release of MACREL. (pass 1)

	  Action:  The current statement is skipped.

     NI - UNIMPLEMENTED DIRECTIVE
	  (pass 1)

     NI - UNIMPLEMENTED PSEUDO-OP

     PE - TOO MANY LITERALS
	  (pass 2)

     PH - END OF FILE REACHED BEFORE END OF .REPT

	  Meaning:  The end of the  input  file  was  found  and  no  .ENDR
	  directive  was  encountered  to  close the repeat sequence (.REPT
	  directive).

	  Action:  The pass is aborted.

     PH - MACRO # DOES NOT TERMINATE (.ENDM ASSUMED)

     PH - NO TEXT AFTER MACRO DIRECTIVE, MACRO #

     PH - NO TEXT AFTER .REPT

     PH - PHASE ERROR

	  Meaning:  The end of the input file was encountered when  it  was
	  not  expected.  The  assembler  was  still  in  the  middle  of a
	  conditional  or  macro  definition  which  had  not   terminated.
	  (passes 1 and 2)

	  Action:   The   assembly   concludes   normally,   assuming   the
	  conditional or macro definition had ended.




				      D-6

		       MACREL DIAGNOSTIC ERROR MESSAGES


     RD - GLOBAL REDEFINED TO NON-GLOBAL

	  Meaning:  A global symbol or  entry  point  was  redefined  in  a
	  direct  assignment  expression  that  used  a  single equal sign.
	  (pass 1)

	  Action:  The new value for the symbol is retained and the  symbol
	  remains a global.

     RD - REDEFINITION OF SECT NAME name

	  Meaning:  A program section directive was encountered whose  name
	  was  already  the  name of another program section of a different
	  type.

	  Action:  ^^The new section type is used. This will cause errors to
	  be generated in the relocatable binary file.

     RD - REDEFINITION OF SYMBOL, name

	  Meaning:  A known symbol was given  a  new  type  in  a  .GLOBAL,
	  .EXTERNAL, .ENTRY, or .ZTERN directive. (pass 1)

	  Action:  The new type is accepted. The  relocatable  binary  will
	  probably be bad.

     RD - SYMBOL # BEING REDEFINED TO MACRO NAME

     RE - RELOCATION ERROR

	  Meaning:  An illegal operation was specified such that the result
	  was not simply relocatable. (pass 1)

	  Action:  The result of the expression is assumed to  be  absolute
	  0.

     SE - NO ROOM IN FREESPACE FOR MACRO name
	  (passes 1 and 2)

     SE - RAN OUT OF ROOM IN FREESPACE

	  Meaning:  The assembler ran out of free room.  This  is  probably
	  because  there  were  too many symbols used in the source program
	  and the symbol table got filled up. It could also mean  that  the
	  user  had too much text in macro definitions and that this filled
	  up freespace. (passes 1 and 2)

	  Solution:  Reduce the number of symbols in the  program,  shorten
	  the  length  of  the macros, or break up the program into several
	  source modules.

	  Action:  The pass is aborted.

     SE - TOO MANY LEVELS OF MACRO (OR REPT)

				      D-7

		       MACREL DIAGNOSTIC ERROR MESSAGES


     SE - TOO MANY LSD ENTRIES
	  (passes 1 and 2)

     SY - A DIGIT MAY NOT FOLLOW A DOLLAR IN A SYMBOL

	  Meaning:  A symbol (identifier) was encountered that began with a
	  dollar  sign  and was followed by a digit. This is not permitted.
	  If a symbol begins with a dollar sign, the next character must be
	  a letter or period or a dollar sign. (pass 1)

	  Action:  An erroneous symbol name is generated.

     SY - BAD ARGUMENT TO DIRECTIVE

	  Meaning:  The argument to a PAGE directive was  not  absolute  or
	  relative to the current SECT or it had an absolute part which was
	  greater than 37 octal. (pass 1)

	  Action:  The low order  5  bits  of  the  absolute  part  of  the
	  argument are used.

     SY - BAD DEVICE NAME name

	  Meaning:  Device name  greater  than  4  characters  or  no  name
	  specified  in  the  DEVICE  directive.  This  error  will also be
	  generated if an extension was erroneously specified, e.g.  DEVICE
	  FILE.XX. (pass 1)

	  Action:  If extra characters were specified, or if  an  extension
	  was  specified,  these  characters  are  lost.  If  no  name  was
	  specified, two words of 0 will be assembled.

     SY - BAD MACRO NAME

	  Meaning:  The  character  after  a  .MACRO  directive  (excluding
	  spaces  and  tabs)  was not alphabetic. A valid symbol must occur
	  at this place. (pass 1)

	  Action:  The invalid character  is  ignored,  and  the  assembler
	  continues to search the line for the macro name.

     SY - BAD SECT NAME

     SY - BAD TERM AFTER

     SY - CAN'T RESTRICT A-SECT









				      D-8

		       MACREL DIAGNOSTIC ERROR MESSAGES


     SY - DANGLING OPERATOR

	  Meaning:  An expression ended with an operator (other than  space
	  or tab). (pass 1)

	  Action:  The operator is ignored and the value of the  expression
	  is  determined  solely  by  the  portion  of  the expression that
	  occurred prior to the operator causing the error. (pass 1)

     SY - DEVICE NAME name TOO LARGE

	  Meaning:  The device mnemonic specified in a .INCLUDE  or  .CHAIN
	  directive consisted of more than 4 characters. (pass 1)

	  Action:  Characters following the fourth character are ignored.

     SY - END OF LINE ENCOUNTERED BEFORE END OF ' OR " OPERATOR

	  Meaning:  The " operator  must  be  followed  by  a  legal  ASCII
	  character  before  the  end  of  the  line  is encountered. The '
	  operator must be followed by two legal SIXBIT  characters  before
	  the  end  of  the  line  is  encountered.  Similarly  for  the ^"
	  command. This error  can  also  occur  if  no  character  at  all
	  follows an up-arrow. (pass 1)

	  Action:   The  statement  is  aborted.  Invalid  binary  will  be
	  generated.

     SY - EXTRA RIGHT ANGLE BRACKET IGNORED

     SY - IFDEF NOT FOLLOWED BY A SYMBOL

	  Meaning:  The IFDEF or  .IF  DF  directive  was  not  immediately
	  followed  by  a  symbol.  (Such  a  symbol  would  begin  with an
	  alphabetic character.) The same error message  is  generated  for
	  the IFNDEF and .IF ND directives. (pass 1)

	  Action:  The directive is aborted.

     SY - ILLEGAL ARGUMENT erg

     SY - IMPROPER EXTENSION

	  Meaning:  The file name specified in a FILENAME  directive  began
	  with  a period, or contained two periods. A period indicates that
	  an extension follows. A file name may have  only  one  extension.
	  The name (preceding the extension) may not be omitted. (pass 1)

	  Action:  MACREL generates an erroneous file name.






				      D-9

		       MACREL DIAGNOSTIC ERROR MESSAGES


     SY - IMPROPER LOCAL SYMBOL

	  Meaning:

	      1. A symbol was found that ended with a dollar sign ($),  but
		 this $ was past character 6 in the symbol.

	      2. A symbol ending with a $ was encountered before the  first
		 occurrence  of  a  tag  (terminated  by  a comma) within a
		 SECT. (pass 1)

	  Action:  An unpredictable name  is  generated  and  the  assembly
	  continues.

     SY - INVALID ARG # .PUSH OR .POP

     SY - MISSING DEVICE OR FILENAME

	  Meaning:  No name appeared after a DEVICE or FILENAME  directive.
	  The name must start with a letter. (pass 1)

	  Action:  The directive is aborted.

     SY - MISSING NUMERIC ARGUMENT

	  Meaning:  A statement ended  with  one  of  the  temporary  radix
	  control operators, O, D, ^B. (pass 1)

	  Action:  The statement is aborted.

     SY - MISSING SECT NAME

	  Meaning:  No name was specified in a program  section  directive.
	  (pass 1)

	  Action:  The character after the .SECT directive (which  was  not
	  an  alphabetic  character) is ignored and the assembler continues
	  to scan for the section name.

     SY - MISSING TEXT ITEM

	  Action:  The directive is aborted. (pass 1)

     SY - NAME OF FILE OR DEVICE TOO LONG

	  Meaning:  The filename specified with the FILENAME directive  had
	  more  than  6  characters,  or  the  extension  had  more  than 2
	  characters,  or  the  device  name  specified  with  the   DEVICE
	  directive contained more than 4 characters. (pass 1)

	  Action:  The extra characters are ignored.

     SY - NAME # ON .ENDM DOES NOT MATCH NAME ON .MACRO


				     D-10

		       MACREL DIAGNOSTIC ERROR MESSAGES


     SY - NO COMMA AFTER SECT NAME

     SY - NO COMMA OR SYMBOL AFTER DECLARATION

	  Meaning:

	      1. No symbol was specified as  an  argument  to  a  directive
		 (.EXTERN, .ZTERN, .ENTRY, .GLOBAL).

	      2. The character after a comma within a declaration list  was
		 not a letter (after ignoring spaces and tabs). (pass 1)

	  Action:  The  character  found  is  ignored,  and  the  assembler
	  continues to look for a proper identifier.

     SY - NO PREVIOUS SECT

     SY - QUOTED ARGUMENT MISSING FINAL "

     SY - SECT name HAS UNKNOWN TYPE "x"

     SY - TASK NAME HAS IMPROPER TYPE (pass 1)

     SY - UNKNOWN ENABLE CONDITION

	  Meaning:  The keyword following a .ENABLE directive was  not  one 
	  of the permissible names. (pass 1)

	  Action:  The directive is aborted.

     SY - UNKNOWN IF CONDITION

     SY - UNKNOWN LIST CONDITION

     SY - UNKNOWN TYPE OF SECT

	  Meaning:  In a .SECT directive, the  character  after  the  comma
	  following  the  SECT  keyword  was  not a legal section type. The
	  permissible types are A, F, D, R, X, and Z. This error  may  also
	  occur if no section type is specified after the comma. (pass 1)

	  Action:  The SECT is assumed by default to be an .RSECT.

     SY - VACUOUS EXPRESSION

	  Meaning:  An expression was required in the current context,  but 
	  none was found. (pass 1)

	  Action:  Assembly continues  assuming  an  expression  was  found
	  whose value was 0 (absolute).





				     D-11

		       MACREL DIAGNOSTIC ERROR MESSAGES


     SY - Z IMPROPERLY SPECIFIED

	  Meaning:  The Z  operator  occurred  within  a  memory  reference
	  instruction  whose  direct operand did not refer to page 0. (pass
	  1)

	  Action:  The Z is ignored.

     SY - 4096 OPEN ANGLE BRACKETS

	  Meaning:  A directive or expression contained more than 4095 left
	  angle brackets (<). (pass 1)

	  Action:  The statement is aborted.

     SY - 4096 NESTED TRUE CONDITIONALS

	  Meaning:  More than 4095 conditionals were nested within side  of
	  each other and all the conditions were true.

	  Action:  The pass is aborted.

	  The user must revise the program to use fewer nested  conditional
	  expressions. (pass 1)

     UO - BAD ORIGIN

	  Meaning:  The expression after  an  asterisk  directive  was  not
	  absolute or relative to the current SECT. (pass 1)

	  Action:  Assembly continues assuming the current location counter
	  value  referred  to the absolute part of the specified expression
	  (within the  current  SECT).  The  relocatable  portion  of  that
	  expression is ignored.

     US - SYMBOL NOT FOUND
	  (pass 2)

     XX - UNKNOWN ERROR

     %0 - ZERO DIVIDE














				     D-12




				     INDEX


     /0-9 LINK command string option,	  Assembly, 1-3, 1-20
	9-5				    chaining directives, 5-24
     7BIT .ENABLE directive option,	    format effectors, 2-2
	5-36				    listing control directives, 5-2
     8BIT .ENABLE directive option,	    listing format, 8-7
	5-36				    MACREL passes 1 thru 4, 1-20,
					       1-22
					    option directives, 5-34
					    operating procedures, 8-1
     /A MACREL command string option,	    PAL8 programs, 1-4, 1-6
	8-2				  Assigning symbol values, 4-6, 4-9
     ABS .IF directive condition, 5-22	  Asterisk (*), 4-1
     ABSLDR binary file, 9-2		    directive, 1-9, 4-11, 5-14,
     Absolute assembled value (program	       10-18
       listing), 8-9			    symbol in program listing, 8-9
     Absolute expressions, 1-19		  Autoindex register, 3-5
     Absolute program section, 1-8,	    program section, 1-8,
	 7-4
       asterisk directive in, 5-14
       default name, 7-4
       literals, 4-14			  /B,
       named, 4-14			    LINK command string option, 9-4
       unnamed, 4-14			    MACREL command string option,
     Absolute relocation, 1-19		       8-2
     Absolute symbols, 4-9		    PAL8 command string option, 1-6
     Actual macro arguments, 6-7	  Backslash (\) special operator,
     Addition operator (+), 4-18	     4-1, 4-7
     ALTMODE (ESC) command terminator,	  Bars, vertical (metasymbol), xii
	9-2				  BATCH, 8-3
     Ampersand (&) operator, 4-1, 4-20	  BE .LIST directive option, 5-2
     AND Boolean operator (&), 4-20	  Binary code generation, 1-21
     Angle brackets (<>),		  Binary expression operations,
       in conditional macros, 6-17	     4-28
       in expressions, 4-1, 4-27	  Binary file,
     Apostrophe, 4-1			    ABSLDR, 9-2
       program listing, 8-99		    relocatable, 1-4, 1-6, 8-1
       concatenation operator, 6-12	  Binary radix control, 4-15
     Arguments,				  BL .IF directive condition, 5-22
       macro, 6-7			  .BN filename extension, 9-2
       substrings in macros, 6-9	  Boolean operators, 4-20
     Arithmetic operators, 4-18		  Brackets,
       relocation types for, 4-31	    angle (<>), 4-1, 4-27, 6-17
     ASCII,				    square,
       character set, A-1		      enclosing literals, 4-1,
       data representation, 4-16		4-12, 1-5
       .ENABLE directive option, 5-36	      metasymbol, xii
     .ASECT directive, 1-8, 7-4
       in named and unnamed program
	   sections, 4-14
       in PAL8 programs, 1-6


				    Index-1

				  INDEX (Cont.)


     /C,				  Conditional source code in
       LINK command string option, 9-4      macros, 6-16
       MACREL command string option,      Constants generated by micro-
	  8-2				    instruction combinations, 3-10
     Calls,				  Control character representation,
       macro, 6-6			    4-18
       repeat blocks, 6-20		  Control commands for MACREL
     CDF instruction, 3-10		    error messages, 8-5
       (special operator), 4-24,	  Control options (LINK), 9-4
	 7-18				  COS .ENABLE directive option, 5-36
       in expressions, 1-19		  CREF file PAL8, 1-21
       in overlays, 10-10		  Cross-reference (KREF program),
       relocation, 1-19			    1-21, 8-15
     CDF/CIF,				  CTRL/C control character, 8-6
       relocatable symbols, 4-9		  CTRL/L control character, 2-2
       relocation expressions, 1-19,	  CTRL/O control character, 8-6
	  1-19				  CTRL/S control character, 8-6
     .CHAIN directive, 5-25		  Current location counter, 4-11,
     Change Data Field - see CDF	      5-14, 10-15
     Change Instruction Field -		    in expressions, 4-27
       see CIF				    PAGE directive, 5-16
     Character set, 4-1, A-1		    program listing, 8-9
     Characters,			    setting to unknown values, 5-14
       in symbols, 4-2			  Current page literals, 4-12, 4-12
       in text strings, 4-16, 5-10
       special, 4-1
       uppercase/lowercase (metasymbol),
	  xii				  Data,
     CIF instructions, 3-10		    program section, 1-8, 7-9
       (special operator), 4-24,	    statement format, 2-1
	  7-19				    storage directives, 5-7
       in overlays, 10-10		  Decimal radix control, 4-16
     CND .LIST directive option, 5-2	  DECIMAL PAL8 directive, 5-7
     Code Location Directives, 5-13	  Default filename extensions, 1-6,
     Coding procedures, 7-21		     8-1, 8-15, 9-2
     Colon, 4-1, 4-4, 4-6		  Default terminal conditions
     Comma, 4-1, 4-3			    (MACREL), 8-6
     Command string,			  DEVICE directive, 5-26
       KREF, 8-15			  Devices,
       LINK, 9-1			    KREF default, 8-15
       MACREL, 8-1			    LINK default, 9-2
       PAL8 /B and /F options, 1-6	    MACREL default, 8-1
     Comment statement format, 2-1	  DF .IF directive condition, 5-22
     Communicating between modules,	  Diagnostic messages (MACREL), D-1
	1-7, 7-14			  DIF .IF directive condition, 5-22
     Complex relocation 1-19		  Direct assignment statement, 4-6,
     Concatenating,			     4-9
       in nested macros, 6-16		  Directives, 1-3, 2-1, 5-1
       macro arguments, 6-12		    .ASECT, 1-6, 7-4
     Conditional Assembly Directives,	    Asterisk (*), 1-9, 4-11, 5-14,
	  5-20				       10-15
       in macros, 6-16			    .CHAIN, 5-25
       nested, 5-23			    DECIMAL, 5-7


				    Index-2

				  INDEX (Cont.)


     Directives (cont.)			  Double equal sign (==), 4-9
       DEVICE, 5-26			  Double quote ("), 4-1
       .DISABL, 5-36			    ASCII conversion operator, 4-16
       .DSECT, 7-9			    TEXT directive, 5-8
       EJECT, 5-5			  .DSECT directive, 1-8, 7-9
       .ENABLE, 5-35			  DTORG PAL8 pseudo-operator, 1-5
       .ENDM, 6-3			  Dummy arguments in macros, 6-3
       .ENDR, 6-20			  Dynamic code relocation, 5-19
       ENPUNCH, 5-6
       .ENTRY, 7-17
       EXPUNGE, 5-6
       .EXTERNAL, 7-14			  E MACREL terminal control command,
       FIELD, 5-17			    8-6
       FILENAME, 5-26			  /E MACREL command string option,
       FIXMRI, 5-31			  8-3
       FIXTAB, 5-32			  EDF special operator, 4-25
       .FSECT, 7-10			  EJECT PAL8 directive, 5-5
       .GLOBAL, 7-16			  Ellipsis (metasymbol), xii
       .IF, 5-20			  .ENABLE directive, 5-35
       IFDEF, 5-24			    and TEXT directive, 5-10
       IFNDEF, 5-24			  .ENABWD special variable, 5-37
       IFNZRO, 5-24			  .ENDM directive, 6-3
       IFZERO, 5-24			  .ENDR directive, 6-20
       .INCLUDE, 5-24			  ENPUNCH PAL8 directive, 5-6
       .JSW, 5-28			  Entry point definition, 7-17
       .MACRO, 6-3			  .ENTRY directive, 7-17
       .MEXIT, 6-15			  EQ .IF directive condition, 5-22
       NOPUNCH, 5-6			  Equal sign (=), 4-1
       OCTAL, 5-7			    direct assignment statement, 4-9
       PAGE, 5-16			    LINK command string option, 9-4
       .POP, 5-34			  Error messages,
       .PUSH, 5-33			    assembly, 1-20
       .RADIX, 5-6			    diagnostic, D-1
       RELOC, 5-19			    format, 8-6
       .REPT, 6-20			    LINK, 9-7
       .RSECT, 7-5			    MACREL runtime control, 8-5, 8-8
       .SECREF, 7-17			  ESC (ALTMODE) LINK command
       .SECT, 1-7			    terminator, 9-2
       .SECT *, 7-13			  Evaluate Data Field - see EDF
       .START, 5-27			  Evaluation - see expression
       TEXT, 5-8 to 5-13		    evaluation
       .VERSION, 5-29			  Exclamation point operator (!),
       XLIST, 5-5			    4-1, 4-20
       .XSECT, 7-7			  Expressions, 4-1
       ZBLOCK, 5-7			    absolute, 1-19
       .ZSECT, 7-6			    evaluation, 4-27
       .ZTERNAL, 4-24, 7-15		    .FSECT relocation, 1-19
     .DISABL directive, 5-37		    literal, 4-12, 4-12
     Division operator (%), 4-19	    Memory Reference Instructions,
     Document conventions, xii		      3-6, 4-22
     Dollar sign ($),			    operator precedence, 4-28
       in local symbols, 4-6		    relocation, 1-19, 4-30
       PAL8 terminator, 1-5, 4-1	    simple relocation, 1-19


				    Index-3

				  INDEX (Cont.)


     Expressions (cont.)		  .FSECT directive, 1-9, 7-10
       terms, 4-27			    literals, 4-14
       uses of, 4-30			    relocatable symbols, 4-9
     EXPUNGE directive, 5-29		    relocation, 7-11
     EXPUNGE,				    expressions, 1-19
       .ENABLE directive option, 5-36     /FY MACREL command string  5-28
       .DISABL directive option, 5-37       option, 8-3
     .EXTERNAL directive, 7-14

					  /G,
					    LINK command string option, 9-4
     /F,				    MACREL command string option,
       LINK command string option, 9-4	       8-2
       PAL8 command string option 1-6     GE .IF directive condition, 5-22
     Field - see memory field		  .GLOBAL directive, 7-16
     FIELD directive, 5-17		  Global symbol assignment, 4-10
       in unnamed absolute program	  Global Symbol Table, 1-22, 9-6
	 sections, 7-4			  GST - see Global Symbol Table
     File,				  GT .IF directive condition, 5-22
       binary, 8-2
       KREF, 1-6, 8-2
       listing, 1-6, 8-1
       load map, 9-2			  /H LINK command string option, 9-4
       macro library, 10-17		  Horizontal tab, 2-2
       memory-image, 1-23, 9-2		    in expressions, 4-21
       relocatable binary, 1-4, 1-6,	    inclusive OR operator, 4-20
	  8-1, 10-2			   PAL8 use, 1-6
       save, 1-23, 9-2, 10-2
       source, 1-7, 1-9, 8-2
     FILENAME directive, 5-26
     Filename default extensions, 1-6,    I special operator, 4-1, 4-23
       8-1, 8-15, 9-2			  IDN .IF directive condition, 5-22
     FILL,				  .IF directive, 5-20
       .ENABLE directive option, 5-36       in macros, 6-16
       .DISABL directive option, 5-37     IFDEF PAL8 directive, 5-24
     FIXMRI directive, 5-31		  IFNDEF PAL8 directive, 5-24
     FIXTAB directive, 5-32		  IFNZRO PAL8 directive, 5-24
     .FLD special operator, 4-26, 7-19    IFZERO PAL8 directive, 5-24
     FLD:n default program section	  .INCLUDE directive, 5-25
	name, 7-4			  Inclusive OR operator, 4-20
     Floating program section, 1-9,	  Indirect addressing, 4-23
	 7-10				  Input/Output Transfer
       literals, 4-14			      Instructions, 3-1, 3-5
     Form feed format effector, 2-2	    internal, 3-8
     Format of,				    keyboard/reader, 3-8
       Memory Control Block, 10-16	    memory extension, 3-9
       PDP8 machine instructions, 3-1	    paper tape reader/punch, 3-9
       program listing, 8-7		    teleprinter/punch, 3-8
       relocatable binary (.RB) file,	  Instruction set, PDP/8, 3-1
	 10-2				    statement format, 2-1
       save (.SV) file, 10-14		  Intermodule communication, 1-7
       Symbol Table, 8-10		  directives, 7-14
     Forward slash (/) symbol, 4-1, 2-2     in overlays, 10-10


				    Index-4

				  INDEX (Cont.)


     IOT - see Input/Output Transfer      LINK (cont.),
       Instructions			    loader codes, 10-5
					    operating procedures, 9-1
					    overlay option rules, 9-3
					    pass 1, 1-22
     /J,				    pass 2, 1-22
       LINK command string option, 9-4      symbol resolution, 1-22
       MACREL command string option,	    system files, 9-1
	 8-2				  LINK.SV system file, 9-1
     .JSW (Job Status Word) directive,    Linking, 1-4, 1-22
					  .LIST directive, 5-2
					  Listing file, 1-6
					    MACREL, 8-1
     /K,				    KREF, 8-15
       LINK command string option, 9-4      LINK, 9-2
       MACREL command string option,	    pass 3, 1-21
	 8-2				  .LISTWD special variable, 5-4
     .KF filename extension, 1-6, 8-2,    Literals, 4-12
       8-15				    closing PAL8 expressions, 1-5
     KREF,				    current page, 4-12
       command string, 8-15		    evaluation, 4-12
       example listing, 8-16		    pool size, 4-14
       file, 1-6, 8-2			    page zero, 7-4
       listing example, 8-16		    overwriting, 1-5, 4-14
       operating procedures, 8-15	    storage of, 4-13
       KREF.SV system file, 8-1		  LN .LIST directive option, 5-2
       KREF.TM default filename, 8-2      Load map, 9-11
					    file, 9-2
					  Loading address (program section),
					    1-9, 10-16
     L MACREL terminal control command,   Loading Information Directives,
       8-5				    5-27
     /L MACREL command string option,     Loading (LINK pass 2), 1-22
       8-3				  LOC keyword, 7-5 to 7-11
     Labels, 2-1, 4-4			  Local symbols, 4-6
     LE .IF directive condition, 5-22     Location counter, 4-11, 5-14,
     Left shift operator (!), 4-20	      10-15
     LEVEL keyword, 7-5 to 7-11, 10-10      PAGE directive, 5-16
     .LEVEL special operator, 4-27	    program listing, 8-9
     Levels (overlay), 10-9		    setting to unknown values, 5-14
     Library file,			  Lowercase characters,
       LINK, 1-22, 9-6, 10-8		    in symbols, 4-1
       macro, 10-17			    metasymbology, xii
     Line buffer size(MACREL), 2-1	  .LS filename extension, 1-6, 8-2
     Line feed character, (PAL8), 1-5     LSD - see Loader Symbol Dictionary
     Line number (program listing), 8-8   LST - see Loader Symbol Table
     LINK,				  LT .IF directive condition, 5-22
       command string, 9-1		  .LT filename extension, 8-15
	 example, 9-2
	 options, 9-3
       error messages, 9-7
       features, 1-2
       library file, 1-22, 9-6, 10-8
       load map, 9-11

				    Index-5

				 INDEX (Cont.)


     /M,				  Macros (cont.)
       LINK, command string option,	    names, 6-10
	 9-4				    nesting, 6-14
       MACREL command string option,	    symbols in, 6-10
	 8-3				  .MACRO directive, 6-3
     .MA filename extension, 1-6,	  MC .LIST directive option, 5-2
       8-2, 9-2				  ME .LIST directive option, 5-2
     MACERR.SV system file, 8-1	 	  MEB .LIST directive option, 5-2
     Machine instruction set, 3-6	  Memory,
     MACOVR.SV system file, 8-1		    allocation (LINK pass 2), 1-22
     MACREL,				    field loading restrictions,
       arithmetic operators, 4-18	    5-17
       assembly of PAL8 programs, 1-6       loading address, 10-16
       character set, 4-1		    symbol table requirements, 10-1
       command string 8-1		    virtual size option, 9-4
       comments, 2-1, 2-2		  Memory Control Block format,
       compatibility with PAL8, 1-4	    10-16
       data, 2-1			  Memory extension, 3-9
       diagnostic messages, D-1		  Memory image file, 1-23, 9-2
       directives, 2-1, 5-1		  Memory Reference Instructions,
       error messages, 8-5		    3-1, 3-6, 4-22
       features, 1-1			  Memory Segment Doublewords, 10-16
       instructions, 2-1		  Messages - see error and
       labels, 2-1			    diagnostic messages
       line buffer size, 2-1		  Metasymbology, xii
       listing example, 8-11		  .MEXIT directive, 6-15
       literals, 1-5			  Microinstructions,
       loader codes, 10-5		    generating constants from, 3-10
       operating procedures, 8-1	    operate, 3-1, 3-3
       PAL8 compatability summary, B-1    Minus sign (-), 4-1
       passes 1 thru 4, 1-20		    subtraction operator, 4-19
       Permanent Symbol Table, C-1	    program listing, 8-9
       relocation, 1-1			  Modules,
       source program format, 2-1	    source, 1-7, 1-9
       statement format, 2-1		  MRI - see Memory Reference
       symbol table sizes, 10-1		  Instruction
       system files, 8-1		  Multiplication operator (^), 4-19
       terminal message codes, 8-8
     MACREL.SV system file, 8-1
     Macros, 1-2
       argument substrings, 6-9	   	  /N,
       argument concatenation, 6-12	    LINK command string option,
       arguments, 6-3, 6-7		      9-4, 9-5
       calls, 6-6			    MACREL command string option,
       concatenation in nested, 6-16	      8-3
       conditional assembly directives    Named absolute program section,
	  in, 6-16			       4-14
       conditional source code in,	    FIELD directive in, 5-18
	  6-16				  .NARGS special operator, 6-17,
       definitions, 6-3			     6-19
       directives, 6-1			  NB .IF directive condition, 5-22
       expansion, 6-6, 6-10		  .NCHAR special operator, 6-10
       library file, 10-17		  NDF .IF directive condition, 5-22
       name deletion, 5-30		  NE .IF directive condition, 5-22

				    Index-6

				 INDEX (Cont.)


     Nesting,				  PAGE keyword, 7-5 to 7-11
       literals, 4-12			  Page zero,
       macros, 6-14			    addressing special operator
	  concatenation in, 6-16	       (Z), 4-24
       repeat blocks, 6-21		    literals, 4-12
     .NOLIST directive, 5-2		    program section, 1-7, 7-5
     NOPUNCH PAL8 directive, 5-6	  PAL8,
     Number representation, 4-15	    .ASECT directive in programs,
     Numeric characters in symbols,	       1-5
       4-6				    /B command string option, 1-6
					    closing literal expressions,
					       1-5
					    compatibility with MACREL, 1-4,
     /O,				       B-1
       LINK command string option, 9-4	    CREF file, 1-21
       MACREL command string option,	    DECIMAL directive, 5-7
	  8-3				    dollar sign ($) terminator, 1-5
     Object module, 1-23, 9-2, 10-2	    DTORG pseudo-operator, 1-5
     OCTAL PAL8 directive, 5-7		    EJECT directive, 5-5
     Octal radix control, 4-16		    ENPUNCH directive, 5-6
     Operate microinstructions, 3-1,	    /F command string option, 1-6
	3-3, 3-7			    horizontal tab use, 1-6
     Operating procedures,		    IFDEF directive, 5-24
       KREF, 8-15			    IFNDEF directive, 5-24
       LINK, 9-1			    IFNZRO directive, 5-24
       MACREL, 8-1			    IFZERO directive, 5-24
     Operators,				    line feed support, 1-6
       arithmetic, 4-18			    literals, 1-5
       Boolean, 4-20			    NOPUNCH directive, 5-6
       expression precedence, 4-28	    OCTAL directive, 5-7
       special, 4-1, 4-21		    PAUSE pseudo-operator, 1-5, 4-3
     options - see run time, command	    program assembly, 7-4
	  string,			    run time options, 1-6
       LINK, MACREL, KREF, etc.		    terminal support, 1-6
     OR Boolean operator, 4-20		    XLIST directive, 5-5
     OR .ENABLE directive option, 5-36    Parenthesis ( () ), 4-1
     OS/8,				    current page literals 4-12
       .ENABLE directive option, 5-36       right, 1-5
       Keyboard Monitor R command,	  PAUSE PAL8 pseudo-operator, 1-5,
	  1-23, 8-1, 9-1		    4-3
     Overlay driver, 10-14		  PDP-8 machine instruction set,
     OVERLAY keyword, 7-5 to 7-11,	    3-1, 3-6
       10-10				  Percent sign (%) division
     Overlays,				  operator, 4-1, 4-19
       introduction, 1-2,		  Period (.),
       rules for creating, 9-3, 10-9	    current location counter, 4-11
     OVRDRV.MA system file, 9-3, 10-14      decimal radix control, 4-16
     OVRDRV.RB system file, 9-1		    in directive names, 5-1
					    special operator, 4-1, 4-11
					  PERM,
					    .ENABLE directive option, 5-36
     /P MACREL command string option,       .DISABL directive option, 5-37
       8-3				  Permanent Symbol Table, 4-3,
     PAGE directive, 5-16		    6-10, A-1

				    Index-7

				 INDEX (Cont.)


     PIP (library file creation), 9-6	  Relocatable (cont.)
     Plus sign (+),			    program section, 1-7, 7-5 to
       addition operator, 4-1, 4-18	       7-11
       in program listing, 8-9		    symbols, 4-9
     .POP directive, 5-34		  Relocation, 1-1, 1-6, 7-1
     Program,				    arithmetic expressions, 4-30
       design, 7-21			    dynamic, 5-19
       listing, format, 8-7		    CDF and CIF instructions, 4-24
       format effectors, 2-2		    FIELD directive, 5-18
       subtitle, 5-4			    .FSECT, 7-10
       title, 5-3			    programming, 1-10
     Program section, 1-7		    summary of types, 7-12
       absolute, 4-14			    symbol, 4-9
       communication, 1-13		    types, 1-18
       directives, 7-1			  Repeat directives, 6-1
       loading address, 1-9		  Repeat blocks,
       size, 1-9, 7-2			    defining and calling, 6-20
     Programming fundamentals, 1-10	    nested, 6-21
     PUNCH,			         .REPT directive, 6-20
       .ENABLE directive option, 5-36     RET (carriage return), xii
       .DISABL directive option, 5-37	  RETURN key, 2-1
     .PUSH directive, 5-33		  Right parenthesis ()), 1-5
					  Right square bracket, 1-5
					  ROOT keyword, 7-5 to 7-11
     /Q MACREL command string option,	  Root segment, 10-9
       8-3				  .RSECT directive, 1-8, 7-5
     Question mark (?) in program	  RTS/8 device handler function
       listings, 8-9			    control word, 4-26
     Quote,				  Run time options (PAL8), 1-6
       double ("), 4-17, 5-8		
       single ('), 4-17			

					  /S,
					    LINK command string option, 9-4
      R OS/8 Keyboard Monitor command,      MACREL command string option,
	1-23, 8-1, 9-1			       8-3
      /R,				  Save file, 9-2
	LINK command string option, 9-4     format, 10-14
	MACREL command string option,     .SBTTL directive, 5-4
	   8-3				  Secondary reference to symbols,
      Radix control,			    7-17
	directives, 5-6			  .SECREF directive, 7-17
	operators, 4-15			  .SECT directive, 1-7, 7-2
      .RB,				  .SECT * directive, 7-13
	file format, 10-2		  Semicolon (;), 4-1
	filename extension, 1-6, 8-2,       statement terminator, 2-2
	   10-8				  SHIFT .ENABLE directive option,
      Redefining symbols, 4-10		    5-36
      REL .IF directive condition, 5-22   Simple relocation, 1-19
      RELOC directive, 5-19		  Single equal sign (=), 4-9
      Relocatable,			  Single quote (') ASCII conversion
	binary file, 1-4, 1-6, 8-1,	    operator, 4-17
	   10-2				  SIXBIT .ENABLE directive option,
	coding procedures, 7-21	  	    5-36

				    Index-8

				 INDEX (Cont.)


     Size of program sections, 1-9	  ST .LIST directive option, 5-2
     Slash symbol,			  Stack Manipulation Directives,
       back (\), 4-7			    5-33
       forward (/), 2-2			  .START directive, 5-27
     Source files and modules, 1-7,	  Statement,
       1-9				    direct assignment, 4-9
     Source program format, 2-1		    format, 2-1
     Space,				    labels, 4-4
       in expressions, 4-20		  Substrings of macro arguments,
       in program listing, 8-9		    6-9
       inclusive OR operator, 4-20	  Subtitle directive, 5-4
     Special characters and operators,    Subtraction operator (-), 4-19
	  4-1				  .SV file, 1-23
       Ampersand (&), 4-1, 4-20		  .SV filename extension, 9-2
       Apostrophe ('), 6-12		  Symbol conventions in this
       Backslash (\), 4-7		    manual, xii
       CIF and CDF, 4-24, 7-19		  Symbol definition (assembly
       Dollar sign ($), 1-5, 4-1, 4-6	    pass 1), 1-20
       Double equal sign (==), 4-9	  Symbol Dictionary, 10-2
       Double quote ("), 4-1, 4-17,	  Symbol table, 1-22
	  5-8				    descriptor codes, 8-10
       EDF, 4-25			    format, 8-10
       Exclamation point operator (!)	    modification directives, 5-29
	  4-1, 4-20			    permanent, 4-3, 6-10, A-1
       Equal sign (=), 4-1, 4-9		    sizes, 10-1
       .FLD, 4-26, 7-19			  Symbols, 4-2
       Forward slash (/), 2-2		    assigning values to, 4-6, 4-9
       I, 4-23				    characters in, 4-1
       .LEVEL, 4-27			    defining, 4-3
       Memory Reference Instructions,	    deleting, 4-1, 5-30
	  3-6, 4-22			    external, 7-14, 7-15
       Minus sign (-), 4-1, 4-19	    global, 4-10, 7-16
       .NARGS, 6-17, 6-19		    in macros, 6-10
       .NCHAR, 6-10			    legal characters, 4-2
       Percent sign (%), 4-1, 4-19	    LINK resolution of, 1-22
       Period (.), 4-1, 4-11, 4-16,	    local, 4-6
	  5-1			    	    name modification, 4-6
       Plus sign (+), 4-1, 4-18, 8-9	    permanent, 4-3
       Single quote ('), 4-17		    redifinition, 4-10
       Uparrow (^), 4-1, 4-19		    relocation, 4-9
       Uparrow B (^B), 4-15		    secondary reference, 7-17
       Uparrow D (^D), 4-16		  Syntax (expression), 4-27
       Uparrow double quote (^"), 4-1,    System files, 8-1, 9-1, 9-3
	  4-18				
       Uparrow O (^O), 4-16		
       XEDF, 4-26			
       Z, 4-1, 4-24			  /T LINK command string option,
     Special variables,			    9-5
       .ENABWD, 5-37			  Tab - see horizontal tab or
       .LISTWD, 5-4			    vertical tab
      Square brackets,			  Terminal conditions (MACREL
	in literals, 4-1, 4-12		    default), 8-6
	metasymbol, xii
	right, 1-5

				    Index-9

				 INDEX (Cont.)


     Terminator,			  /W LINK command string option,
       MACREL statements, 2-2	    	    9-5
       macros, 6-3
     Terms (expression), 4-27
     TEXT directive, 5-8 to 5-13	
     .TITLE directive, 5-3		  /X,
     TOC .LIST directive option, 5-2	    LINK command string option, 9-5
					    MACREL command string option,
					       8-3
     Unnamed program sections, 4-14,	    XEDF special operator, 4-26
	  7-2				    XLIST PAL8 directive, 5-5
       default name, 7-4		    .XSECT directive, 1-8, 7-7
       FIELD directive in, 5-18
     Uparrow, 4-1
     Uparrow (^) multiplication		
       operator, 4-1, 4-19		  /Y LINK command string option,
     Uparrow B (^B) binary radix	    9-5
       control operator, 4-15
     Uparrow D (^D) decimal radix
       control operator, 4-16
     Uparrow double quote (^n) control	  Z special operator, 4-1, 4-24
       character representation, 4-1,     /Z MACREL command string option,
	  4-18				    8-3
     Uparrow O (^O) octal radix		  ZBLOCK directive, 5-7
       control operator, 4-16		  .ZSECT directive, 1-8, 7-6
     Uppercase character		  .ZTERNAL directive, 4-24, 7-15
       as metasymbols, xii
       in symbols, 4-1
     User Service Routine (USR)
       Communication Directives, 5-26



     /V LINK command string option,
       9-5
     .VERSION directive, 5-29
     Vertical bars, xii
     Virtual memory size option, 9-4

















				   Index-10


     :							      MACREL/LINK
     :							      Release Notes
     :							      AA-5663B-TA
     :
     :
     :			       READER'S COMMENTS
     :
     :
     :
     :	 NOTE:  This form is for document comments only.  DIGITAL will
     :		use comments submitted on this form at the company's
     :		discretion.  If you require a written reply and are
     :		eligible to receive one under Software Performance
     :		Report (SPR) service, submit your comments on an SPR
     :		form.
     :
     :
     :	Did you find this manual understandable, usable, and well-organized?
     :	Please make suggestions for improvement.
     :  ___________________________________________________________________
     :  ___________________________________________________________________
     :  ___________________________________________________________________
     :  ___________________________________________________________________
     :  ___________________________________________________________________
     :  ___________________________________________________________________
     :  ___________________________________________________________________
     :  ___________________________________________________________________
     :
     :	Did you find errors in this manual? If so, specify the error and the
     :	page number.
     :  ___________________________________________________________________
     :  ___________________________________________________________________
     :  ___________________________________________________________________
     :  ___________________________________________________________________
     :  ___________________________________________________________________
     :  ___________________________________________________________________
     :  ___________________________________________________________________
     :  ___________________________________________________________________
     :
     :	Please indicate the type of reader that you most nearly represent.
     :
     :	      [] Assembly language programmer
     :	      [] Higher-level language programmer
     :	      [] Occasional programmer (experienced)
     :	      [] User with little programming experience
     :	      [] Student programmer
     :	      [] Other (please specify)___________________________________
     :
     :
     :	Name____________________________________ Date______________________
     :
     :	Organization_______________________________________________________
     :
     :	Street_____________________________________________________________
     :
     :	City_________________________ State__________ Zip Code_____________
     :							or
     :						      Country



















     ----------------------------- Fold Here ------------------------------




















     ----------------- Do Not Tear - Fold Here and Staple -----------------


							 ------------------
							 |   FIRST CLASS  |
							 |  PERMIT NO. 33 |
							 | MAYNARD, MASS. |
							 ------------------
     BUSINESS REPLY MAIL					 ==========
     NO POSTAGE STAMP NECESSARY IF MAILED IN THE UNITED STATES	 ==========
     ======================================================================
     Postage will be paid by:					 ==========
								 ==========
			      ---------------			 ==========
			      |D|I|G|I|T|A|L|			 ==========
			      ---------------			 ==========
								 ==========
			  Software Documentation		 ==========
			146 Main Street ML5-5/E39		 ==========
		       Maynard, Massachusetts 01754		 ==========