MMV12.DOC




		    Master Menu Software Installation Guide


				  Version 1.2











                                  DISCLAIMER

                This document file was created by scanning  the
                original  document and then editing the scanned
                text.  As much as possible, the  original  text
                format  was restored.  Some format changes were
                made to insure this  document  would  print  on
                current laser printers using 60 lines per page.
                The  original  spelling  and  grammar  has been
                preserved.

		Figures of the  DECmate  hardware  showing  the 
		keyboard,   floppy   drives,   etc.  cannot  be 
		reproduced with the  ASCII  character  set  and
		are not included in this document.

                1-Oct-1996























		DECmate (TM)

	        ___________________________________________________________


		Master Menu Software
		Installation Guide			        Version 1.2





     Master Menu Software Installation Guide
     AA-HV22A-TV

     May, 1986



     The information in this document is subject to change without notice
     and should not be construed as a commitment by Digital Equipment
     Corporation.  Digital Equipment Corporation assumes no responsibility
     for any errors that may appear in this document.

     The software described in this document is furnished under a license
     and may be used or copied only in accordance with the terms of such
     license.

     Digital Equipment Corporation assumes no responsibility for the use or
     reliability of its software on equipment that is not supplied by
     DIGITAL or its affiliated companies.


     Copyright (C) 1986 by Digital Equipment Corporation. All Rights
			   Reserved.


     The following are trademarks of Digital Equipment Corporation:

	 digital(TM)	  MASSBUS	  RSX
	 ALL-IN-1	  DIBOL		  RT
	 DEC		  PDP		  UNIBUS
	 DECmate	  P/OS		  VAX
	 DECspell	  Professional	  VMS
	 DECUS		  Rainbow	  VT
	 DECwriter	  RSTS		  Work Processor


     CP/M is a trademark of Digital Research Inc.
     MS is a trademark of Microsoft Corporation.


     A NOTE ON PRODUCTION:  This document was prepared on a DECmate II
     using DECmate/WPS version 2.2 software, and printed on the LN03 laser
     printer.  Text was printed using the Compugraphic CG Times font
     cartridge (LN03XX-CB).  Heading and titles were printed using the CG
     Triumvirale font cartridge (LN03XX-CJ).  The book was sent for
     publication from the LN03 without enhancement or alteration except for
     the addition of line art.


			 DIGITAL EQUIPMENT CORPORATION
			    Merrimack, New Hampshire




				      ii



     CONTENTS

     ______________________________________________________________________


     Preface

	New Features for Version 1.2  v
	Intended Audience  v
	    How to Use This Book  v
	Conventions  vi
	Reference Manuals  vii



      1  Introduction

	 Difference Between DECmate II and DECmate III Plus
	 Diskette Drive Operations  1-1
	     Conventions Used to Describe Diskette Drive Operations  1-2
	 Special Function Keys  1-3
	 Required Software  1-3
	 Handling Diskettes  1-4



      2  Installing Master Menu

	 Installing Master Menu  2-1



      3  Backup Diskette to Diskette With Master Menu

	 Backup Installation Software  3-1
	 D - Backup Diskette to Diskette  3-1



     Figures

	1-1   RX50 Diskette Drive Doors on DECmate II System  1-2
	1-2   RX33 Diskette Drive Doors on DECmate III Plus System  1-2
	1-3   CANCEL and MAIN SCREEN Keys on the DECmate Keyboard  1-3
	2-1   Master Menu Install Menu  2-2
	3-1   Hard Disk Services Menu  3-2
	3-2   Fixed Menu Screen in Master Menu  3-4









				      iii



     PREFACE

     ___________________________________________________________________







     Product		DECmate Master Menu Install


     Version		1.2


     The Master Menu Installation Guide describes how to install Master
     Menu on a DECmate system with a hard disk drive.

     NOTE: Master Menu Install version 1.2 uses one diskette drive to
	   install Master Menu software.  The installation procedure
	   described in this book replaces the one described in chapter 3
	   of the Master Menu User's Guide under Section "INST - Install
	   Master Menu."

     NOTE: If you have the DECmate III Plus system, you cannot use the COPY
	   option to make a backup copy of Master Menu Install diskettes A
	   and B.  Refer to Chapter 2 in this manual for instructions on
	   installing Master Menu.  Refer to Chapter 3 for instructions on
	   making backup copies using a single diskette drive.

	   The COPY option is described in the Master Menu User's Guide in
	   Chapter 2 and in Chapter 3 under the section "COPY - Make Copies
	   of the Installation Diskettes.  The COPY option requires two
	   diskette drives."





















				      iv



     PREFACE

     ___________________________________________________________________


     New Features for Version 1.2

     Master Menu version 1.2 has a new option in the Hard Disk Services
     menu. The D (Backup diskette to diskette) option makes backup copies
     of software in Master Menu using a single diskette drive.  This option
     is described in Chapter 3, "Diskette to Diskette With Master Menu."


     Intended Audience

     This book is written for first-time users and experienced users who
     want to install Master Menu on a DECmate system.  The book covers both
     first-time installation and updates to existing Master Menu software.


     How to Use This Book

     This book is organized into the following chapters:

	 o  Chapter 1 describes the necessary hardware and software.

	 o  Chapter 2 explains how to install Master Menu.

	 o  Chapter 3 explains how to make backup copies using the Master
	    Menu D option (backup diskette to diskette).


























				       v



     PREFACE

     ___________________________________________________________________


     Conventions

     The following conventions are used throughout this book:

     Press	   Means to press a specific key once. For examples, press
		   RETURN means press the RETURN key once.


     Enter	   Means to enter or type text from the keyboard. For
		   example, enter the date and press RETURN.


     ALL CAPS	   Indicates the function or edit key to press.
		   For example, press ADVANCE means you press the ADVANCE
		   key located on the Edit keypad.


     Gold XXX	   Press the Gold key on the edit keypad, followed by
		   another key.  For example, press Gold MENU means press
		   the Gold key, followed by the M (MENU) key on the main
		   keyboard.

						    ___
     Rubout Key    Refer to the key marked with an < X | symbol:						    ___

		   The RUBOUT key, also marked WORD CHAR, erases text to
		   the left of the cursor.


     < > key	   The key in the lower right corner of the Edit keypad,
		   labeled with < >, and also marked ENTER.


     {     }	   The braces enclose areas of the screen with inverted
		   video.


     -------	   A box is used to enclose the text displayed on a menu
     |     |	   screen.
     |     |
     -------










				      vi



     PREFACE

     ___________________________________________________________________


     Reference Manuals

     This book assumes your DECmate system is correctly set up and that you
     have formatted your hard disk. Consult the following manuals for
     specific information:


	 DECmate II

	 o  DECmate II Installation Guide

	 o  DECmate II Hard Disk Subsystem Documentation

	 o  DECmate II Owner's Manual


	 DECmate III Plus

	 o  DECmate III Plus System Kit

     The DECmate Master Menu Software Installation Guide only describes how
     to install Master Menu software on a hard disk.  You should refer to
     the Master Menu User's Guide for instructions on how to use Master
     Menu with your DECmate system.



























				      vii



     INTRODUCTION

     ______________________________________________________________________


     The DECmate Master Menu Software installation Guide explains how to
     install Master Menu software on a DECmate system with a hard disk.  The
     instructions in this book can be used on the following DECmate
     systems:

	 o  DECmate II

	    DECmate II system, including monitor, keyboard, system unit
	    with dual diskette drives, and the DECmate II hard disk
	    subsystem installed.

	 o  DECmate III Plus

	    DECmate III Plus system, including monitor, keyboard, and
	    system unit with one diskette drive and one hard disk.

     Master Menu is installed using only one diskette drive.  This is the
     default diskette drive on the DECmate system.  On a DECmate II this is
     the uppermost drive;  on a DECmate III Plus this is the only diskette
     drive.  Throughout this book, the default diskette drive is called
     drive 0.

     Other operating systems, such as CP/M and MS-DOS, use letters instead
     of numbers for device assignments.  For example, the default diskette
     drive is always assigned the letter A.  Other documentation may refer
     to the default diskette drive as drive 0/A or just drive A.



     Difference Between DECmate II and DECmate III Plus
     Diskette Drive Operations


     The main difference between DECmate II and DECmate III Plus hardware
     is the diskette drive used on each system:

	 o  The DECmate II uses an RX50 dual diskette drive.  There are two
	    diskette drive doors.  The hard disk subsystem is optional.

	 o  The DECmate III Plus uses an RX33 diskette drive.  There is one
	    diskette drive with a lock.  The RD31 hard disk comes with the
	    system.

     Figure 1-1 shows a DECmate II system with RX50 dual diskette drive and
     the hard disk subsystem installed.  Note that the RX50 diskette drives
     are opened by pressing on the top or bottom of the diskette drive
     doors.




				      1-1



     INTRODUCTION

     ______________________________________________________________________




	Figure 1-1 not included in this document.

							ASD-522

     Figure 1-1  RX50 Diskette Drive Doors on DECmate II System


     Figure 1-2 shows a DECmate III Plus system with the RX33 diskette
     drive and the RD31 hard disk.  Note that the RX33 diskette drive is
     opened by turning a lock.




	Figure 1-2 not included in this document.

							ASD-871

     Figure 1-2  RX33 Diskette Drive Lock on DECmate III Plus System



     Conventions Used to Describe Diskette Drive Operations

     This book uses the term diskette drive door to refer to both the
     diskette drive door on the RX50 and the lock on the RX33.  When you
     are instructed to open the diskette drive door, follow the correct
     procedure for your system:

     DECmate II		Press the top of the diskette drive door. The door
			springs open.

     DECmate III Plus	Turn the diskette lock up.

     When you are instructed to close the diskette drive door, follow the
     correct procedure for your system:

     DECmate II		Press the bottom of the diskette drive until it
			closes.

     DECmate III Plus	Turn the diskette lock down.  You must have a
			diskette in the drive before you turn down the
			lock.






				      1-2



     INTRODUCTION

     ______________________________________________________________________


     Special Function Keys

     Figure 1-3 shows the DECmate keyboard with two function keys
     highlighted.




	Figure 1-3 not included in this document.

							ASD-232

     Figure 1-3  CANCEL and MAIN SCREEN Keys on the DECmate Keyboard


     The two keys shaded on the DECmate keyboard (CANCEL and MAIN SCREEN)
     in Figure 1-3 are keys Master Menu uses that may not be familiar to
     you:

     CANCEL	The CANCEL key (F8) lets you cancel an operation, function,
		utility, or menu screen.

     MAIN	The MAIN SCREEN key (F9) allows you to display the previous
     SCREEN	menu screen after you complete an operation.

     For a complete discussion of all the other keys on the DECmate
     keyboard, refer to the DECmate Owner's Manual for your system.



     Required Software

     You need the following software to install Master Menu on a formatted
     hard disk:

	 o  Master Menu Install diskette A

	 o  Master Menu Install diskette B

     After you install Master Menu, on the hard disk, you can install the
     following software:

	 o  DECmate WPS (Word Processing System). version 2.2 or higher.
	    Refer to the book Installation Guide for WPS and DECspell (1)
	    for instructions on installing DECmate WPS on the hard disk.

     ______________________________________________________________________
     (1) DECmate/DECspell software uses the Houghton Mifflin dictionary,
     copyrighted by Houghton Mifflin Company, Boston, Massachusetts.


				      1-3



     INTRODUCTION

     ______________________________________________________________________


     Handling Diskettes

     Follow these precautions when you handle diskettes:

	 o  Handle diskettes carefully, holding them on the edges or
	    corners, much as you would a stereo record.

	 o  NEVER touch the read/write openings with your fingers.

	 o  Keep diskettes in their paper envelopes when they are not in
	    use.

	 o  Do not attempt to clean diskettes by wiping them with a cloth.
	    You will ruin the magnetic surface.

	 o  Write on labels before you affix them to a diskette. If you
	    must write on a label already on a diskette use a felt-tip pen.
	    Do not use ballpoint pens, and never use a pencil.

	 o  Keep diskettes away from direct sunlight or high temperatures.
	    Store them in a cool, dry place.

	 o  Keep diskettes away from the video monitor, magnets, tools,
	    phone, or electric motors.



























				      1-4



     2

     ______________________________________________________________________


     INSTALLING MASTER MENU

     Once you have formatted your hard disk, use the following procedure to
     install Master Menu on the hard disk using Master Menu Install
     diskettes A and B.  This procedure differs from the one described in
     the Master Menu User's Guide because you must use the original
     (master) copy of the Master Menu Install diskettes.  You cannot make
     backup copies until Master Menu has been installed.

     Refer to Chapter 3, "Backup Diskette to Diskette With Master Menu,"
     for instructions on making backup copies of original (master) software
     after you install Master Menu.



     INSTALLING MASTER MENU

	 1  If necessary, turn the DECmate system OFF.  Open the diskette
	    drive door(s) and make sure all drive(s) are empty.

	 2  Press the system unit power switch to the ON (1) position.

	 3  Immediately insert the Master Menu Install diskette A into drive
	    0.  If your diskette drive has a colored bar on the drive, make
	    sure the arrow on the diskette lines up with the colored bar
	    Close the diskette drive door.

	    OR

	    If you already have Master Menu, you can start up the new
	    Master Menu Install diskette A from the existing Master Menu by
	    pressing SET-UP and then REMOVE.  Insert Master Menu Install
	    diskette A into drive 0, and close the door.  Press DO.

	    NOTE:  If you do not insert the DECmate Master Menu Install
		   diskette A immediately, the system will boot the startup
		   volume of Master Menu that is already established on
		   your hard disk (if one exists).  If this should happen,
		   either turn off the system and repeat from step 2, or
		   press SET-UP, press REMOVE, insert the Master Menu
		   Install diskette A into drive 0, close the drive door
		   and press DO.

	    The software takes a minute or two to load.  The Master Menu
	    Install Diskette Menu, similar to the one shown in Figure 2-1,
	    appears on the screen.  If you have a DECmate II, the COPY
	    option appears on the screen.




				      2-1



     INSTALLING MASTER MENU

     ______________________________________________________________________


     ----------------------------------------------------------------------
     |{	    	     DECmate Master Menu Install diskette		 }|
     |	Version 1.2				Panel Code Rom Level: xxx |
     |						Internal Data Level: xxxx |
     |									  |
     |									  |
     |{ INST }	Install Master Menu					  |
     |									  |
     |	SMPW	Set Master password
     |									  |
     |	PSWD	List volume passwords
     |									  |
     |	MBB	Mark a bad block
     |									  |
     |	QUIT	Leave this program and go to SETUP to reboot
     |									  |
     |									  |
     |									  |
     |									  |
     |									  |
     |									  |
     |	Select an item using arrow keys or type its tag, then press DO.	  |
     |									  |
     |									  |
     ----------------------------------------------------------------------

     Figure 2-1  Master Menu Install Menu
	

	 4  Use the ^ (UP ARROW) or v (DOWN ARROW) keys to move the		    |		    |
	    highlight to the INST option (Install Master Menu). Press DO.

	    OR

	    Enter INST and press DO.

	    If you already have Master Menu on your system, the following
	    message appears:

	    ---------------------------------------------------------------
	    |								  |
	    | Saving your old menu items.				  |
	    |								  |
	    ---------------------------------------------------------------

	    Master Menu is installed with the volume name MENU.  If you
	    already have a volume named MENU on your hard disk, and if this
	    volume does not contain the Master Menu system (it is possible
	    that another application is named MENU), the following message
	    appears:

				      2-2



     INSTALLING MASTER MENU

     ______________________________________________________________________


	    ---------------------------------------------------------------
	    |								  |
	    | Volume named MENU is not a Master Menu volume.		  |
	    |								  |
	    | If you proceed, the contents of this volume will be erased. |
	    |								  |
	    | To proceed, press DO. To abort, press CANCEL.		  |
	    |								  |
	    ---------------------------------------------------------------

	    If you want to continue with the installation (in other words,
	    you do not need the contents of the volume named MENU), press
	    DO. Proceed to the next step.

	    OR

	    If you do not want to continue with the installation (in other
	    words, you want to keep the contents of the volume named MENU),
	    press CANCEL and the Master Menu Install menu appears. Use ^ or								       |
	    v to highlight QUIT and press DO.  Press REMOVE, located on the	    |
	    Arrow Keypad.  Open drive door 0 and remove Master Menu
	    diskette A.  Press DO to restart the DECmate system.  If you
	    want to keep a volume currently named MENU, use the Rename
	    function (in CP/M or MS-DOS) change the volume name to another
	    name.  You must rename the volume before you install Master
	    Menu.

	 5  Follow the prompts on the screen and remove Master Menu Install
	    diskette A from drive 0.  Place the diskette in its protective
	    envelope.

	 6  Insert Master Menu Install diskette B into drive 0, and close
	    the door.  When you are ready, press DO.  The screen displays a
	    row of dots that turn into asterisks (*) during installation.

	 7  When the installation is complete, you are prompted to remove
	    Master Menu Install diskette B from drive 0.  Take the diskette
	    out, and place it in its protective envelope.

	 8  Replace Master Menu Install diskette A in drive 0, and press DO.
	    If you had menu items that were saved, the following message
	    appears:

	     --------------------------------------------------------------
	     |								  |
	     | Restoring your old menu items.				  |
	     |								  |
	     --------------------------------------------------------------



				      2-3



     INSTALLING MASTER MENU

     ______________________________________________________________________


	 9  You are prompted to press the MAIN SCREEN key to redisplay the
	    Install Menu.  Press MAIN SCREEN.  This key is Function Key 9
	    (F9), located in the uppermost row of gray function keys.

	10  When the Master Menu Install Diskette Menu appears,
	    installation is complete.  Do not select any other options
	    except QUIT until you make a backup copy of the Master Menu
	    Installation diskettes A and B, as described in the next
	    section.

	11  Use the ^ or v keys to select QUIT and press DO.		    |    |

	    OR

	    Enter QUIT and press DO.

	    The DECmate Set Up Screen appears.

	12  Press REMOVE, located on the Arrow Keypad.  Open drive door 0,
	    and remove Master Menu diskette A.  Press DO.  The DECmate
	    system starts itself and displays the Master Menu Date/Time
	    screen.

     Once you have installed Master Menu on the hard disk, you should make
     backup copies of the installation diskettes, as described in the next
     chapter.  When you complete the backup, store the original (master)
     copies and use the backup copies and repeat steps 1 to 3 to redisplay
     the Master Menu Install Menu.  You can then select and use other menu
     items (Set Master password, List volume passwords, Mark a bad block)
     as described in the Master Menu User's Guide.





















				      2-4



     3

     ______________________________________________________________________


     BACKUP DISKETTE TO DISKETTE WITH MASTER MENU

     The D Option (Backup diskette to diskette) is a new Master Menu
     utility that makes backup copies of diskettes.  The D option is found
     in the Hard Disk Services menu, as shown in Figure 3-1.

     The D option transfers a complete copy from one diskette to another
     diskette using a single diskette drive (drive 0). The D option is
     similar to backup in WPS, and can be used to make working copies of
     any diskette, including WPS document diskettes.  Use the D option to
     make backup copies of software installation diskettes, or to make
     copies of other diskettes from Master Menu.

     The other backup utility in Master Menu (B -- Backup Volume(s) to
     diskettes) transfers the contents of a hard disk volume onto a
     diskette in drive 0.  The B option is used primarily for backups of
     hard disk volumes.  Unlike the D option, the B option does not make
     workable copies.  For example, WPS cannot read data from diskettes
     backed up with the B option;  you must use the R (Restore a volume
     from diskette) Option in Master Menu before WPS can read the data.
     Consult Chapter 7, "Hard Disk Services," in the Master Menu User's
     Guide for instructions on using the B and R options in Master Menu.



     Backup Installation Diskettes

     After you install Master Menu you should make backup copies of the
     original Master Menu Install diskettes A and B.  Once this procedure
     is complete, do not use the original diskettes for installation:
     always use backup copies. Store the original diskettes in a safe
     place.

     At the same time, you should also make backup copies of the WPS
     Install, WPS System, and WPS Utility diskettes, and any other software
     you plan to install on the hard disk.  Do this before you install the
     software.  The original Master Menu Install diskettes A and B are the
     only software that cannot be backed up before installation.

     Use blank diskettes for backups, or use diskettes you are sure you do
     not want to keep.  Remember that the contents of these diskettes will
     be erased and replaced when you make backups.



     D - Backup Diskette to Diskette

     The D Option involves four basic steps:



				      3-1



     BACKUP DISKETTE TO DISKETTE WITH MASTER MENU

     ______________________________________________________________________


	 o  Insert the diskette to be copied in drive 0.

	 o  Copy the contents of the diskette into a temporary storage area
	    on the hard disk.

	 o  Remove the diskette to be copied and insert a blank diskette to
	    receive the copy.

	 o  Copy the contents of the temporary storage area on the hard
	    disk onto the blank diskette.

     You need at least one area of 400K bytes free space on your hard disk
     for the temporary storage area.  The 400K bytes must be contiguous, or
     one complete block of space.  If you have 400K bytes free space, but
     the largest area is less than 400K, the space is not contiguous and
     the D option will not work.  Compress space on the hard disk, or erase
     a volume you do not want, to create enough contiguous free space and
     retry the D option.



     ----------------------------------------------------------------------
     |{			      Hard Disk Services			 }|
     |	Screen 1 of 2        Monday 11/10/86 0:00:00	       Version 1.2|
     |									  |
     |		     {L}-- List directory of volumes			  |
     |									  |
     |		      A -- Allocate a new volume			  |
     |									  |
     |		      E -- Erase an existing volume			  |
     |									  |
     |		      B -- Backup Volume(s) to diskettes		  |
     |									  |
     |	  	      D -- Backup diskette to diskette			  |
     |									  |
     |		      R -- Restore a volume from diskettes		  |
     |									  |
     |		      Q -- Return to Master Menu			  |
     |									  |
     |									  |
     |									  |
     |									  |
     |									  |
     |	Select an item using arrow keys or type its tag; then press DO.   |
     |	      Press NEXT SCREEN for more items.				  |
     ----------------------------------------------------------------------

     Figure 3-1  The D Option in the Hard Disk Services Menu



				      3-2



     BACKUP DISKETTE TO DISKETTE WITH MASTER MENU

     ______________________________________________________________________


     The following procedure describes how to make backup copies from
     diskette to diskette using the D option in Master Menu's Hard Disk
     Services menu.

	 1  If necessary, turn the DECmate system OFF.  Open the diskette
	    drive door(s) and make sure all drive(s) are empty.  Press the
	    system unit power switch to the ON (|) position.  Master Menu
	    starts tip and the Date/Time screen appears.  Enter the date
	    and press RETURN.  Entering the time is optional.  Press RETURN
	    to skip entering the time.

	    OR

	    If the DECmate system is on, recall Master Menu.  From WPS Main
	    Menu press F (Finish);  from drive E in CP/M or MS-DOS, enter
	    MENU and press RETURN.

	 2  If you installed Master Menu for the first time the Fixed Menu
	    screen appears, similar to the one shown in Figure 3-2.

	    If you already have Master Menu installed, you also may have
	    other menu items.  Press NEXT SCREEN until the Fixed Menu
	    screen appears.

	 3  Use the ^ or v keys to highlight HD (Hard Disk Services) and		    |	 |
	    press DO or RETURN.

	    OR

	    Enter HD and press DO or RETURN.  The Hard Disk Services Menu
	    appears, similar to the one shown in Figure 3-1.

	 4  Use the ^ or v keys to select D (Backup diskette to diskette)		    |	 |
	    and press DO or RETURN.

	    OR

	    Enter D and press DO.  The following prompt appears:

	    ---------------------------------------------------------------
	    |								  |
	    | Place the diskette to be backed up in drive 0.		  |
	    |								  |
	    | The contents of this diskette will be copied into a	  |
	    | temporary storage area on the hard disk.			  |
	    |								  |
	    | Press DO to proceed or CANCEL to quit.			  |
	    |								  |
	    ---------------------------------------------------------------


				      3-3



     BACKUP DISKETTE TO DISKETTE WITH MASTER MENU

     ______________________________________________________________________


     ----------------------------------------------------------------------
     |{									 }|
     |{  d i g i t a l	      DECmate Master Menu			 }|
     |{									 }|
     |Screen  2 of  2	        Monday 11/10/86 0:00:00     Version 1.2	  |
     |--------------------------------------------------------------------|
     |									  |
     | {HD } DECmate Hard Disk Services				 	  |
     |									  |
     |	 MM   DECmate Menu Maintenance Utility				  |
     |									  |
     |	 DAT  Set System Date and Time					  |
     |									  |
     |	 SDF  Select New Date Format					  |
     |									  |
     |	 F    Finish Using the system					  |
     |									  |
     |									  |
     |									  |
     |--------------------------------------------------------------------|
     |									  |
     | Select an item using arrow keys or type its tag; then press DO.	  |
     |	       Press NEXT SCREEN for more items.			  |
     |									  |
     ----------------------------------------------------------------------

     Figure 3-2  Fixed Menu Screen in Master Menu


	    Proceed to step 5.

	    OR

	    If your hard disk does not have enough free space for the
	    temporary storage area, a message similar to the one below
	    appears instead:

	    ---------------------------------------------------------------
	    |								  |
	    | There is not enough contiguous free space on your hard disk.|
	    |								  |
	    | The minimum amount of free space required to perform a	  |
	    | diskette backup is 400K.					  |
	    |								  |
	    | Press CANCEL to return to Hard Disk Services.		  |
	    |								  |
	    ---------------------------------------------------------------




				      3-4



     BACKUP DISKETTE TO DISKETTE WITH MASTER MENU

     ______________________________________________________________________


	    Press CANCEL to recall the Hard Disk Services menu.  You must
	    create 400K bytes of contiguous free space before you can use
	    the D option.  Use the X (Compress) utility to compress space
	    on your hard disk, or E (Erase) to erase a volume you no longer
	    need. When you have enough free space, repeat steps 1 to 4.

	 5  Place the diskette you want to copy into drive O and close the
	    drive door.  Press DO.  While the diskette is being copied, a
	    row of dots turns to asterisks.

	    When the copy is complete, a second prompt appears:

	    ---------------------------------------------------------------
	    |								  |
	    | Place the diskette to be OVERWRITTEN in drive 0.		  |
	    |								  |
	    | The contents of the previous diskette will be copied from	  |
	    | the hard disk onto this diskette.				  |
	    |								  |
	    | Press DO to proceed or CANCEL to quit.			  |
	    |								  |
	    ---------------------------------------------------------------

	 6  Open the door on drive 0 and remove the diskette.  Insert a
	    blank diskette, or a diskette you no longer need, into drive O
	    and close the door.  Press DO.  While the diskette is being
	    copied, a row of dots turns to asterisks.

	    When the copy is complete, the last message appears:
	
	    ---------------------------------------------------------------
	    |								  |
	    | The backup was successful.				  |
	    |								  |
	    | Remove the diskette from drive 0.				  |
	    |								  |
	    | Press RETURN to make another backup of this diskette.	  |
	    |								  |
	    | Press DO to backup a different diskette.			  |
	    |								  |
	    | Press CANCEL to quit.					  |
	    |								  |
	    ---------------------------------------------------------------

	 7  You can make another copy of the same diskette by pressing
	    RETURN.  The prompt in step 5 appears.  Repeat step 6 as often
	    as required to make additional copies of the same diskette.

	    OR


				      3-5



     BACKUP DISKETTE TO DISKETTE WITH MASTER MENU

     ______________________________________________________________________


	    You can make a backup copy of a new diskette by pressing DO.
	    Repeat steps 4 to 6.

	    OR

	    Press CANCEL.  This is the function key 8 (F8), located in the
	    uppermost row of gray function keys.  The Hard Disk Services
	    Menu appears.

	 8  Use the ^ or v keys to select Q (Return to Master Menu) and		    |	 |
	    press DO.

	    OR

	    Enter Q and press DO.

	    Master Menu displays either the Fixed Menu screen or Screen 1
	    of the menu selections.

































				      3-6