OS8CKTIG.DOC



			       OS/8 Combined Kit

			       Information Guide
















				  DISCLAIMER

		This document file was created by scanning  the
		original  document and then editing the scanned
		text.  As much as possible, the  original  text
		format  was restored.  Some format changes were
		made to insure this  document  would  print  on
		current laser printers using 60 lines per page.
		The  original  spelling  and  grammar  has been
		preserved.


		1-Nov-1996



						       OS/8 COMBINED KIT
							  INFORMATION
							     GUIDE

						     Order No. AA-J016B-TA















				 January 1980

	  This Guide describes the contents of the OS/8 Combined Kit
	  and how to get the system on line.













	 SUPERSESSION/UPDATE INFORMATION:    This manual supersedes the
					     previous edition, Order No.
					     AA-J016A-TA.


	 OPERATING SYSTEM AND VERSION:       OS/8 V3D






     ---------------------------------------------------------------------
     | To order additional copies of this document, contact the Software |
     | Distribution Center, Digital Equipment Corporation, Maynard,      |
     | Massachusetts 01754						 |
     ---------------------------------------------------------------------

	    digital equipment corporation - maynard. massachusetts



					   First Printing, August 1979
					   Revised:       January 1980



     The information in this document is subject to change without notice
     and should not be construed as a commitment by Digital Equipment
     Corporation. Digital Equipment Corporation assumes no responsibility
     for any errors that may appear in this document.

     The software described in this document is furnished under a license
     and may only be used or copied in accordance with the terms of such
     license.

     No responsibility is assumed for the use or reliability of software on
     equipment that is not supplied by DIGITAL or its affiliated companies.







	Copyright (c) 1979, 1980 by Digital Equipment Corporation







     The postage-prepaid READER'S COMMENTS form on the last page of this
     document requests the user's critical evaluation to assist us in pre-
     paring future documentation.


     The following are trademarks of Digital Equipment Corporation:



	      DIGITAL		  DECsystem-10	     MASSBUS
	      DEC		  DECtape	     OMNIBUS
	      PDP		  DIBOL		     OS/8
	      DECUS		  EDUSYSTEM	     PHA
	      UNIBUS		  FLIP CHIP	     RSTS
	      COMPUTER LABS	  FOCAL		     RSX
	      COMTEX		  INDAC		     TYPESET-8
	      DDT		  LAB-8		     TYPESET-11
	      DECCOMM		  DECSYSTEM-20	     TMS-11
	      ASSIST-MM		  RTS-8		     ITPS-10
	      VAX		  VMS		     SBI
	      DECnet		  IAS		     PDT
	      DATATRIEVE	  TRAX





				   CONTENTS

								     Page

	    1.0    INTRODUCTION					      1
	    2.0    OVERVIEW					      1
	    3.0    DOCUMENTATION				      1
	    4.0    DISTRIBUTION					      3
	    5.0    GETTING ON LINE				      3
	    5.1      General Bootstrap Procedures		      3
	    5.1.1    Operating a Hardware Bootstrap		      3
	    5.1.2    Entering a Bootstrap Manually		      4
	    5.2      RK05 Cartridge Disk Pack			      6
	    5.2.1    Loading Procedure				      6
	    5.2.2    Hardware Bootstrap Procedure		      6
	    5.2.3    Manual Bootstrap Procedure			      6
	    5.3      RL01 Cartridge Disk Pack			      7
	    5.3.1    Loading Procedure				      7
	    5.3.2    Hardware Bootstrap Procedure		      8
	    5.3.3    Manual Bootstrap Procedure			      8
	    5.4      RX01 and RX02 Diskettes			      9
	    5.4.1    Loading Procedure				      9
	    5.4.2    Hardware Bootstrap Procedure		     10
	    5.4.3    Manual Bootstrap Procedure			     11
	    5.5      DECtape (12K TD8E)				     12
	    5.5.1    Loading Procedure				     13
	    5.5.2    Hardware Bootstrap Procedure		     13
	    5.5.3    Manual Bootstrap Procedure			     13
	    5.6      Running the System				     14
	    6.0    VERSION CODES				     15
	    7.0    OBTAINING VERSION CODES FROM OS/8 MODULES	     17




				    FIGURES


     Figure 1      Loading the RK05 Disk			      6
	    2      Loading the RL01 Disk Pack			      7
	    3      Loading the RX01 and RX02 Diskette		     10




				    TABLES


     Table  1      Manual Bootstrap Procedure			      5
	    2      RK8E (RK05) Bootstrap Program		      6
	    3      RL01 Bootstrap Program			      9
	    4      RX01 Bootstrap Program			     11
	    5      RX02 Bootstrap Program			     12

				      iii




			       CONTENTS (Cont.)




				TABLES (Cont.)
								     Page

     Table  6      TD8E DECtape Bootstrap Program		     14
	    7      File and Media Duplication Utility Programs       15
	    8      OS/8 Combined Kit Modules and Version Codes       15
	    9      Obtaining OS/8 Module Version Codes		     17











































				      iv



     1.0  INTRODUCTION

     This document briefly describes  the  OS/8  Combined  Kit,  lists  the
     manuals  and  software contained in the kit, and provides instructions
     for getting the system on line.



     2.0  OVERVIEW

     The OS/8 Combined Kit  is  an  operating  system/software  development
     package  for  PDP-8  computers.   As  the  name  implies, the kit is a
     combination of OS/8 software products.  It includes the  software  and
     documentation contained in the following kits:

	  o  OS/8, Version 3D,  Operating  System  (described  in  Software
	     Product Description (S.P.D.  4.1.11)

	  o  OS/8, Version 3D, Extension (S.P.D.  4.5.8)

	  o  OS/8, Version 3D, Device Extensions for RL01, RX02,  and  KT8A
	     (S.P.D.  4.12.0)

	  o  OS/8, Version 3D, FORTRAN IV (S.P.D.  4.10.7)

     In addition, the kit's modules  have  been  updated  with  the  binary
     patches  described  in  the OS/8 Device Extensions User's Guide and in				 ___________________________________
     the issues of the Digital Software News (through June 1979).		       _____________________



     3.0  DOCUMENTATION

     The documents contained in the OS/8 Combined Kit are as follows. The
     titles are presented in alphabetical order.

	     OS/8 COMBINED KIT INFORMATION GUIDE - AA-J016B-TA
		     Describes the kit's contents and how to get the system
		     on line.

	     OS/8 COMBINED KIT - V3D SPD 4.4.2
		     Describes the  OS/8   Combined   Kit,   its   options,
		     licenses,   support   category   and  other  pertinent
		     information.

	     OS/8 DEVICE EXTENSION RELEASE NOTES - AA-H565A-TA
		     Contains supplemental information on the  features  of
		     the  OS/8  Device  Extensions Kit not discussed in the
		     DEVICE EXTENSIONS USER'S GUIDE.

	     OS/8 DEVICE EXTENSIONS USER'S GUIDE - AA-D319A-TA
		     Describes the RL01 and  RX02  disks,  their  bootstrap
		     procedures,  and  the  software  support  for the KT8A
		     (128K) Memory Management option.


				       1



	     OS/8 ERROR MESSAGES - AA-H610A-TA
		     Describes the error messages  generated  by  the  OS/8
		     Monitor and its system programs.

	     OS/8 FORTRAN IV SOFTWARE SUPPORT MANUAL - DEC-S8-LFSSA-A-D
		     Describes internal features of OS/8  FORTRAN  IV  that
		     may be useful to the advanced user.

	     OS/8 LANGUAGE REFERENCE MANUAL - AA-H609A-TA
		     Describes the languages  supported  by  OS/8:   BASIC,
		     FORTRAN IV, PAL8, FORTRAN II, FLAP/RALF, and SABR.

	     OS/8 MARK SENSE BATCH USER'S MANUAL - DEC-S8-OBUGA-A-D
		     Describes the use and  operation  of  the  Mark  Sense
		     Batch  (MSBATCH)  OS/8  system  program.   It includes
		     step-by-step procedures  for  preparing  programs  for
		     submission to MSBATCH.

	     OS/8 SOFTWARE SUPPORT MANUAL - DEC-S8-OSSMB-A-D
		     Describes internal system features that may be  useful
		     to the advanced user.

	     OS/8 SYSTEM GENERATION NOTES - AA-H606A-TA
		     Describes PDP-8/E bootstrap procedures  for  LINCtape,
		     DECtape  (TC08  and TD8E), and disk (DF32, RF08, RK08,
		     RK8E, and RX01), as well as  procedures  for  building
		     the system from paper tape and DECassette (TA8E).

	     OS/8 SYSTEM REFERENCE MANUAL - AA-H607A-TA
		     Describes  the  OS/8  system   conventions,   keyboard
		     commands and utility programs.

	     OS/8 TECO REFERENCE MANUAL - AA-H608A-TA
		     Describes the Text Editing and Correcting program  for
		     OS/8 users.

	     OS/8 V3D SYSTEM RELEASE NOTES - DEC-S8-OSRNA-B-D
		     Describes the differences between version V3D of  OS/8
		     and previous versions, as well as corrections to known
		     software problems.

	     TECO POCKET GUIDE - AV-D530A-TK
		     Contains  a  guick-reference  summary  of  OS/8   TECO
		     commands.












				       2



     4.0  DISTRIBUTION

     The Combined Kit is distributed on the following media:

	  o  One RK05 cartridge disk

	  o  One RL01 cartridge disk pack

	  o  Six RX01 (single density) diskettes

	  o  Three RX02 (double density) diskettes

	  o  Three DECtapes (12K TD8E system)



     5.0  GETTING ON LINE

     To use OS/8, you must load a bootstrap program into memory and run it.
     The  bootstrap  program  loads  the OS/8 monitor from its distribution
     medium and initializes its operation.  Each  type  of  storage  device
     (for  example,  RL01  disk,  DECtape,  etc.)  has a separate bootstrap
     program.

     Your system may have either an internal hardware bootstrap loader or a
     programmer's  console.   (Some hardware configurations have both.) The
     hardware bootstrap  loader  loads  and  starts  an  internally  stored
     bootstrap  program  under the control of a switch located on the front
     of the processor.  The programmer's console has switches that let  you
     manually enter the bootstrap program into memory and start it.

     The following paragraphs tell you how to load the system medium and to
     initialize  (bootstrap)  it.   You  will  also  find  these  bootstrap
     procedures in the OS/8 System Generation Manual and in the OS/8 Device		       _____________________________		___________
     Extensions User's Guide.     _______________________



     5.1  General Bootstrap Procedures

     This section tells you how to use the hardware  bootstrap  loader  and
     how to manually enter and initialize a bootstrap from the programmer's
     console.  The remaining sections of this document provide loading  and
     bootstrap procedures for the OS/8 Combined Kit distribution media.



     5.1.1  Operating a Hardware Bootstrap - If your system has a  hardware
     bootstrap loader and the processor is a:

	PDP-8/A   1.  Load the distribution medium  into  its  device  (see
		      Sections 5.2 through 5.5).




				       3



		  2.  Run the bootstrap loader:

		      o  Press the BOOT button twice  on  the  programmer's
			 console.

						 or

		      o  Raise and lower the BOOT switch on the  operator's
			 panel.

	PDP-8/E   1.  Load the distribution medium into its device (see
		      Sections 5.2 through 5.5).

		  2.  Lower and raise the HALT switch.

		  3.  Lower and raise the SW switch.

     This procedure will have no effect if there is no  hardware  bootstrap
     loader  in  the system for the device that runs your OS/8 distribution
     medium.



     5.1.2  Entering a Bootstrap Manually - If your system has no  hardware
     bootstrap loader for your distribution medium, you must load and start
     the bootstrap, using the programmer's console as follows:

	  1.  Load the distribution medium into its  device  (see  Sections
	      5.2 through 5.5).

	  2.  Use the steps in Table 1 to manually load  and  initiate  the
	      appropriate bootstrap program (see Sections 5.2 through 5.5).
























				       4


				    Table 1
			  Manual Bootstrap Procedure

     ----------------------------------------------------------------------
     |      |		  |		 Processor			  |
     | Step | Function    |-----------------------------------------------|
     |      |		  |	 PDP-8/A      |		PDP-8/E		  |
     |------|-------------|-------------------|---------------------------|
     |  1   | Halt the    | Press HLT/SS      | Lower and raise the HALT  |
     |      | processor   |		      | switch			  |
     |      |		  |		      |				  |
     |  2   | Display     | a. Press MD       | Rotate selector switch    |
     |      | program     |		      | to MD			  |
     |      | data to be  | b. Press DISP     |				  |
     |      | entered     |		      |				  |
     |      |		  |		      |				  |
     |  3   | Select mem- | a. Press 0	      | a. Lower switches 6, 7, 8 |
     |      | ory field 0 |		      |				  |
     |      |		  | b.  Press LXA     | b. Press EXTD ADDR LOAD   |
     |      |		  |		      |				  |
     |  4   | Select      | Using the numeric | Using the numeric	  |
     |      | bootstrap   | keys:	      | switches:		  |
     |      | loading     |		      |				  |
     |      | address     | a. Enter the      | a. Enter the binary equiv-|
     |      |		  | first (lowest)    |    alent of the first     |
     |      |		  | bootstrap	      |    (lowest) address	  |
     |      |		  | address	      |				  |
     |      |		  |		      | b. Press ADDR LOAD	  |
     |      |		  | b. Press LA       |				  |
     |      |		  |		      |				  |
     |  5   | Enter each  | Using the numeric | Using the numeric	  |
     |      | instruction | keys:	      | switches:		  |
     |      | in the pro- |		      |				  |
     |      | gram into   | a. Enter the      | a. Enter the binary equiv-|
     |      | memory      |    first	      |    alent of the first     |
     |      |		  |    instruction    |    instruction		  |
     |      |		  |		      |				  |
     |      |		  | b. Press D NEXT   | b. Raise and lower DEP    |
     |      |		  |		      |				  |
     |      |		  | Repeat above for  | Repeat 1 & 2 for suc-     |
     |      |		  | succeeding	      | ceeding instructions      |
     |      |		  | instructions      |				  |
     |      |		  |		      |				  |
     |  6   | Select      | Using the numeric | Using the numeric	  |
     |      | bootstrap   | keys:	      | switches:		  |
     |      | starting    |		      |				  |
     |      | address     | a. Enter the      | a. Enter the binary equiv-|
     |      |		  |    starting       |    alent of the starting  |
     |      |		  |    address	      |    address		  |
     |      |		  |		      |				  |
     |      |		  | b. Press LA       | b. Press ADDR LOAD	  |
     |      |		  |		      |				  |
     |  7   | Begin       | a. Press INIT     | a. Press CLEAR		  |
     |      | bootstrap   |		      |				  |
     |      | operation   | b. Press RUN      | b. Press CONT		  |
     ----------------------------------------------------------------------

				       5



     5.2  RK05 Cartridge Disk Pack


     5.2.1  Loading Procedure - If your OS/8 Combined  Kit  medium  is  the
     RK05 disk cartridge, insert the disk into the drive as shown in Figure
     1.  DIGITAL suggests that you write-protect the distribution medium by
     pressing the WTPROT switch.  If there is more than one RK05 disk drive
     on your system, insert the disk pack into the drive marked "0".


     ----------------------------------------------------------------------
     |									  |
     |		RK05 picture not included here.				  |
     |									  |
     |									  |
     | 1.  Switch power on.						  |
     |									  |
     | 2.  Set RUN/LOAD switch (3) to LOAD;LOAD indicator light (4) will  |
     |     be lit.							  |
     |									  |
     | 3.  Open access door (1), insert RK05 disk cartridge (2); close    |
     |     access door.							  |
     |									  |
     | 4.  Set RUN/LOAD switch to RUN; the LOAD indicator light will go   |
     |     out.								  |
     |									  |
     | 5.  READY indicator light (5) will go on when it is ready for      |
     |     access.							  |
     ----------------------------------------------------------------------

			Figure 1  Loading the RK05 Disk



     5.2.2  Hardware Bootstrap Procedure - If your system  has  a  hardware
     bootstrap  loader  for  the  RK05  (RK8E controller) disk, perform the
     steps in Section 5.1.1.  This procedure will have no effect  if  there
     is no hardware bootstrap loader for the RK8E on your system.



     5.2.3  Manual Bootstrap Procedure - If your system has a  programmer's
     console,  use  its switches as described in Section 5.1.2 to enter and
     initialize the RK8E bootstrap program listed in Table 2.


				    Table 2
			 RK8E (RK05) Bootstrap Program

					     Address      Instruction					     _______      ___________
	Loading and starting address ------->  30	     6743
					       31	     5031




				       6



     5.3  RL01 Cartridge Disk Pack



     5.3.1  Loading Procedure - If your OS/8 Combined  Kit  medium  is  the
     RL01  Cartridge  Disk  Pack,  load the disk into its drive as shown in
     Figure 2.  DIGITAL suggests that you protect the  distribution  medium
     by  pressing the WRITE PROTECT button (when illuminated, protect is in
     effect).  If there is more than one RL01 drive on  your  system,  load
     the pack into the drive marked "0".



     ----------------------------------------------------------------------
     |									  |
     | TO READY DRIVE:							  |
     |									  |
     | Raise cartridge access door, and load RL01K disk cartridge.	  |
     |									  |
     | Depress load switch.  Note that spindle motor starts turning.      |
     |									  |
     | After 30 seconds, UNIT SELECT/READY indicator should light,	  |
     | indicating drive is ready to read or write.			  |
     |									  |
     | If write protection is desired, depress WRITE PROTECT switch       |
     | (WRITE PROTECT indicator).					  |
     |--------------------------------------------------------------------|
     |									  |
     |									  |
     |									  |
     |	  RL01 picture not included here				  |
     |									  |
     |									  |
     ----------------------------------------------------------------------
						(continued on next page)

		     Figure 2  Loading the RL01 Disk Pack



















				       7




     ----------------------------------------------------------------------
     |					|				  |
     | DRIVE INDICATORS:		| TO LOAD RL01K CARTRIDGE:	  |
     |					|				  |
     | LOAD:				| Support cartridge "A" with left |
     | When lit, indicates that		| hand holding protection cover	  |
     | cartridge may be loaded or that  | "B".				  |
     | spindle is stopped.		|				  |
     |					| Push handle slide "C" to left   |
     | UNIT SELECT/READY:		| with thumb of right hand.       |
     | Indicates logical drive address. |				  |
     | When lit, indicates drive is     | Raise cover handle "D" to full  |
     | ready to read, write or receive  | upright position, releasing     |
     | controller commands.		| protection cover "B".		  |
     |					|				  |
     | FAULT:				| Lift cartridge "A" from	  |
     | When lit, indicates a drive      | protection cover "B" and	  |
     | error condition.  If this	| carefully seat it on drive      |
     | condition persists, seek		| spindle with handle recess      |
     | assistance.			| facing rear of drive.		  |
     |					|				  |
     | WRITE PROTECT:			| Carefully rotate top cover      |
     | When lit, indicates that		| handle "D" a few degrees	  |
     | cartridge currently mounted is   | clockwise and counterclockwise  |
     | write protected.			| to ensure firm seating.	  |
     |					|				  |
     |					| Gently lower top cover handle   |
     |					| "D" to horizontal position to   |
     |					| engage cartridge on drive       |
     |					| spindle.			  |
     |					|				  |
     |					| Place protection cover "B" on   |
     |					| top of cartridge		  |
     ----------------------------------------------------------------------

		 Figure 2  Loading the RL01 Disk Pack (cont.)



     5.3.2  Hardware Bootstrap Procedure - If your system  has  a  hardware
     bootstrap  loader  for  the  RL01  disk,  perform the steps in Section
     5.1.1.  This procedure will have no effect if  there  is  no  hardware
     bootstrap loader for the RL01 on your system.



     5.3.3  Manual Bootstrap Procedure - If your system has a  programmer's
     console,  use  its switches as described in Section 5.1.2 to enter and
     initialize the RL01 bootstrap program listed in Table 3.






				       8



				    Table 3
			    RL01 Bootstrap Program


				       Address		Instruction				       _______		___________

	Loading and starting address--->0001		   6600
					0002		   7201
					0003		   4027
					0004		   1004
					0005		   4027
					0006		   6615
					0007		   7002
					0010		   7012
					0011		   6615
					0012		   0025
					0013		   7004
					0014		   6603
					0015		   7325
					0016		   4027
					0017		   7332
					0020		   6605
					0021		   1026
					0022		   6607
					0023		   7327
					0024		   4027
					0025		   0377
					0026		   7600
					0027		   0000
					0030		   6604
					0031		   6601
					0032		   5031
					0033		   6617
					0034		   5427
					0035		   5001



     5.4  RX01 and RX02 Diskettes



     5.4.1  Loading Procedure - If  your OS/8  Combined  Kit  medium  is  a
     single-density  (RX01)  diskette  or a double-density (RX02) diskette,
     refer to Figure 3 and perform the procedures listed below to load  the
     diskette into the drive.


				    CAUTION

		    You can insert a single-density diskette
		    into  either  an  RX01 or an RX02 drive.
		    You can insert a double-density diskette
		    into an RX02 drive only.


				       9




			RX02 picture not included here


				   Figure 3
		      Loading the RX01 and RX02 Diskette


     Ordinarily you should load the diskette that contains the monitor  and
     system programs (system diskette) into drive 0, which is the left-hand
     slot.  You can use drive 1 (right-hand slot), if necessary, as long as
     there is no diskette in drive 0 when you start the bootstrap program.

	  1.  Select a diskette from the kit.  If you have an RX01 kit, use
	      diskette 1, 2, or 3.  If you have an RX02 kit, use diskette 1
	      or  2.   (The  other  diskette(s)  in  the  kit  contain  the
	      remaining OS/8 modules.)

	  2.  Open the drive's door:

	      a.  Notice that the door latch is embedded in the  horizontal
		  bar that is part of the door assembly.

	      b.  Compress the latch between the thumb  and  index  finger.
		  The  door  is  spring-loaded and will open when the latch
		  disengages.

	  3.  Grasping the diskette by its top (label) edge, remove it from
	      its  protective  storage  jacket.   (This  is  not  the black
	      protective  cover  in  which  the  diskette  is   permanently
	      sealed.)


				    CAUTION

		    Do not touch the exposed portions of the
		    diskette  that show through the slots in
		    the protective cover.


	  4.  Insert  the  diskette  label-side  up  (the  seams   of   the
	      protective  cover  are  down) into the horizontal slot in the
	      drive.

	  5.  Close the door.  (It will automatically lock when you push it
	      down.)



     5.4.2  Hardware Bootstrap Procedure - If your system  has  a  hardware
     bootstrap  loader  for the RX01 or RX02 diskette, perform the steps in
     Section 5.1.1.  This procedure will have no  effect  if  there  is  no
     hardware bootstrap loader for the RX01 or RX02 on your system.



				      10



     5.4.3  Manual Bootstrap Procedure - If your system has a  programmer's
     console,  use  its switches as described in Section 5.1.2 to enter and
     initialize the RX01 or RX02 bootstrap program listed in Tables  4  and
     5, respectively.


				    Table 4
			    RX01 Bootstrap Program


			Address		  Instruction			_______		  ___________

     Loading address---->0024		     7126
			 0025		     1060
			 0026		     6751
			 0027		     7201
			 0030		     4053
			 0031		     4053
			 0032		     7104
     Starting address--->0033		     6755
			 0034		     5054
			 0035		     6754
			 0036		     7450
			 0037		     7610
			 0040		     5046
			 0041		     1060
			 0042		     7041
			 0043		     1061
			 0044		     3060
			 0045		     5024
			 0046		     6751
			 0047		     4053
			 0050		     3002
			 0051		     2050
			 0052		     5047
			 0053		     0000
			 0054		     6753
			 0055		     5033
			 0056		     6752
			 0057		     5453
			 0060		     7024
			 0061		     6030














				      11




				    Table 5
			    RX02 Bootstrap Program


			Address		  Instruction			_______		  ___________

     Loading address --->0020		     1061
			 0021		     1046
			 0022		     0060
			 0023		     3061
			 0024		     7327
			 0025		     1061
			 0026		     6751
			 0027		     7301
			 0030		     4053
			 0031		     4053
			 0032		     7004
    Starting address---->0033		     6755
			 0034		     5054
			 0035		     6754
			 0036		     7450
			 0037		     5020
			 0040		     1061
			 0041		     6751
			 0042		     1061
			 0043		     0046
			 0044		     1032
			 0045		     3060
			 0046		     0360
			 0047		     4053
			 0050		     3002
			 0051		     2050
			 0052		     5047
			 0053		     0000
			 0054		     6753
			 0055		     5033
			 0056		     6752
			 0057		     5453
			 0060		     0420
			 0061		     0020



     5.5  DECtape (12K TD8E)

     The DECtape bootstrap procedures described below apply  to  CPUs  that
     have  a  TD8E Simple DECtape control and at least 12K words of memory.
     The system on the DECtape distribution medium cannot  be  bootstrapped
     in an 8K TD8E ROM environment.






				      12



     5.5.1  Loading  Procedure - If  your  OS/8  Combined  Kit  medium   is
     DECtape, mount the tape as follows:

	  1.  Select either tape 1  or  tape  2  from  the  kit.   (Tape  3
	      contains the remaining OS/8 modules.)

	  2.  Remove the tape from its protective canister.

	  3.  Remove the plastic seal from the end of the tape.

	  4.  Mount the tape (label-side out) on one of the left-hand  hubs
	      of  the  DECtape  transport.  You can use either the right or
	      the left drive.  (If your system has more  than  one  DECtape
	      transport,  you must use the transport that is wired for TD8E
	      units 0 and 1.)

	  5.  Unwrap a  few  turns  of  tape,  pass  it  over  the  drive's
	      read/write head (dull side toward the head), and wind it onto
	      the takeup reel on the right-hand hub.

	  6.  Wind several more turns of tape onto the takeup reel so  that
	      the tape is not slack.

	  7.  Press the REMOTE/LOCAL switch to LOCAL.

	  8.  Wind more tape onto the takeup reel by  momentarily  pressing
	      the  forward/reverse  switch  (marked  with  left  and  right
	      arrows) toward the right arrow.

	  9.  Rotate the numbered thumbwheel switch to 0.

	 10.  Press the REMOTE/LOCAL switch to REMOTE.

	 11.  Press the WRITE ENABLE/WRITE LOCK switch  to  WRITE  LOCK  to
	      protect the distribution medium.



     5.5.2  Hardware Bootstrap Procedure - If your system  has  a  hardware
     bootstrap  loader  for  the  TD8E, perform the steps in Section 5.1.1.
     This procedure will have no effect if there is no  hardware  bootstrap
     loader for the TD8E on your system.



     5.5.3  Manual Bootstrap Procedure - If your system has a  programmer's
     console,  use  its switches as described in Section 5.1.2 to enter and
     initialize the TD8E bootstrap program listed in Table 6.








				      13



				    Table 6
			TD8E DECtape Bootstrap Program


				    Address	     Instruction				    _______	     ___________

     Loading and starting address--->7300		1312
				     7301		4312
				     7302		4312
				     7303		6773
				     7304		5303
				     7305		6777
				     7306		3726
				     7307		2326
				     7310		5303
				     7311		5732
				     7312		2000
				     7313		1300
				     7314		6774
				     7315		6771
				     7316		5315
				     7317		6776
				     7320		0331
				     7321		1327
				     7322		7640
				     7323		5315
				     7324		2321
				     7325		5712
				     7326		7354
				     7327		7756
				     7330		7747
				     7331		0077
				     7332		7400



     5.6  Running the System

     After you load and  run  a  bootstrap,  the  Keyboard  Monitor  should
     identify itself by displaying its prompting symbol, a period (.).  The
     system is waiting for you to enter one of the OS/8 commands  described
     in the OS/8 System Reference Manual.  If there is no response from the	    ____________________________
     system, repeat the bootstrap procedure.  If there is still no response
     from the system, call your local DIGITAL sales office for assistance.

     When you have determined that OS/8 is running, DIGITAL  suggests  that
     you  make  one  or  more working copies of the distribution medium for
     daily use.  You can make copies by using one of the file  manipulation
     utility  programs  listed  in Table 7 and described in the OS/8 System								___________
     Reference Manual.     ________________






				      14



				    Table 7
		  File and Media Duplication Utility Programs

     ----------------------------------------------------------------------
     | Program | CCL Command |			  Use			  |
     |---------|-------------|--------------------------------------------|
     |  FOTP   |    COPY     | Copies   files   between   file-structured |
     |	       |	     | devices.   (You  must  use  PIP  with /Z/Y |
     |	       |	     | first to create a new directory and put  a |
     |	       |	     | system head on the new media.)		  |
     |	       |	     |						  |
     |  PIP    |    ZERO     | Copies   files   between   file-structured |
     |	       |	     | devices,  formats  a  directory  area on a |
     |	       |	     | device (/Z option),  copies  system  heads |
     |	       |	     | between    file-structured   devices   (/Y |
     |	       |	     | option).  (You must use /Z/Y first  before |
     |	       |	     | copying   the  system  files  to  the  new |
     |	       |	     | media.)					  |
     |	       |	     |						  |
     |  RKCOPY |    None     | Duplicates RK05 cartridge disks		  |
     |	       |	     |						  |
     |  RXCOPY |  DUPLICATE  | Duplicates RX01 and RX02 floppy diskettes  |
     ----------------------------------------------------------------------



     6.0  VERSION CODES

     Many of the version codes for the OS/8  system  modules  have  changed
     because  of the binary patches that have been added (see Section 2.0).
     Table 8 lists the version code for each module in the kit.


				    Table 8
		  OS/8 Combined Kit Modules and Version Codes

     ----------------------------------------------------------------------
     |	      Module	     | Version ||	 Module		| Version |
     |-----------------------|---------||-----------------------|---------|
     | Keyboard Monitor      |   3T    || FORTRAN II		|	  |
     |		CCL overlay  |   3A    ||	 RWTAPE.RL      |   2     |
     |		CD	     |   5A    ||	 SQRT.RL	|   4     |
     |		ODT	     |   6     ||	 TRIG.RL	|   6     |
     |		USR	     |   4A    ||	 UTILITY.RL	|   10    |
     |			     |	       ||			|	  |
     | Utilities	     |	       || FORTRAN IV		|	  |
     |		ABSLDR.SV    |   6B    ||	 FRTS.SV	|   5A    |
     |		BATCH.SV     |   8A    ||	 F4.SV		|   4B    |
     |		BITMAP.SV    |   4A    ||	 PASS2.SV	|   4A    |
     |		BOOT.SV      |   5A    ||	 PASS2O.SV	|   4A    |
     |		BUILD.SV     |   7A    ||	 PASS3.SV	|   4A    |
     |		CAMP.SV      |   5A    ||	 LIBRA.SV	|   24A   |
     |		CCL.SV	     |   3A    ||	 LOAD.SV	|   24A   |
     ----------------------------------------------------------------------
						 (continued on next page)

				      15



				Table 8 (Cont.)
		  OS/8 Combined Kit Modules and Version Codes

     ----------------------------------------------------------------------
     |	      Module	     | Version ||	 Module		| Version |
     |-----------------------|---------||-----------------------|---------|
     | Utilities (cont.)     |	       || FORTRAN IV (cont.)    |	  |
     |		CREF.SV      |   5B    ||	 RALF.SV	|   62A   |
     |		DIRECT.SV    |   6A    ||			|	  |
     |		EDIT.SV      |   12D   || Handlers		|	  |
     |		EPIC.SV      |   5A    ||	 ASR33.BN	|   A     |
     |		FUTIL.SV     |   8B    ||	 BAT.BN		|   B     |
     |		FOTP.SV      |   9B    ||	 CR8E.BN	|   C     |
     |		FOTP.SV      |   9B    ||	 CR8E.BN	|   C     |
     |		HELP.SV      |   2A    ||	 CSA.BN		|   A     |
     |		MCPIP.SV     |   6B    ||	 CSB.BN		|   A     |
     |		MSBAT.SV     |   3B    ||	 CSC.BN		|   A     |
     |		GENIOX.S     |   7A    ||	 CSD.BN		|   A     |
     |		PAL8.SV      |   13A   ||	 DF32NS.BN	|   A     |
     |		PIP.SV       |   14A   ||	 DF32SY.BN	|   B     |
     |		PIP10.SV     |   3B    ||	 DUMP.BN	|   C     |
     |		RESORC.SV    |   5A    ||	 KL8E.BN	|   E     |
     |		SET.SV       |   2A    ||	 LINCNS.BN	|   A     |
     |		SRCCOM.SV    |   4A    ||	 LINCSY.BN	|   B     |
     |		TECO.SV      |   5.08  ||	 LPSV.BN	|   C     |
     |		TDINIT.SV    |   7A    ||	 LQP.BN		|   A     |
     |			     |	       ||	 LSPT.BN	|   A     |
     | Formatters and Copiers|	       ||	 L645.BN	|   A     |
     |		DTCOPY.SV    |   10A   ||	 PT8E.BN	|   A     |
     |		DTFRMT.SV    |   4A    ||	 RF08NS.BN	|   A     |
     |		RKLFMT.SV    |   D     ||	 RF08SY.BN	|   B     |
     |		RLFRMT.SV    |   1A    ||	 RK08NS.BN	|   A     |
     |		RXCOPY.SV    |   4B    ||	 RK08SY.BN	|   D     |
     |		TDCOPY.SV    |   4A    ||	 RK8ENS.BN	|   A     |
     |		TDFRMT.SV    |   4A    ||	 RK8ESY.BN	|   C     |
     |			     |	       ||	 RLSY.BN	|   A     |
     | Languages	     |	       ||	 RL0.BN		|   A     |
     |		BASIC	     |	       ||	 RL1.BN		|   A     |
     |		BASIC.SV     |   5B    ||	 RL2.BN		|   A     |
     |		BCOMP.SV     |   5A    ||	 RL3.BN		|   A     |
     |		BLOAD.SV     |   5B    ||	 RLC.BN		|   A     |
     |		BRTS.SV      |   5C    ||	 ROMSY.BN	|   A     |
     |		EABRTS.SV    |   5A    ||	 RXNS.BN	|   N     |
     |			     |	       ||	 RXSY1.BN	|   M     |
     | FORTRAN II	     |	       ||	 RXSY2.BN	|   M     |
     |		FORT.SV      |   5A    ||	 RX78C.BN	|   N     |
     |		LOADER.SV    |   4A    ||	 TC08NS.BN	|   A     |
     |		LIBSET.SV    |   3A    ||	 TC08SY.BN	|   B     |
     |		SABR.SV      |   18A   ||	 TD8EA.BN	|   D     |
     |		LIB8.RL      |	       ||	 TD8EB.BN	|   D     |
     |		ATAN.RL      |   11    ||	 TD8EC.BN	|   D     |
     |		FLOAT.RL     |   5     ||	 TD8ED.BN	|   D     |
     |		INTEGR.RL    |   5     ||	 TD8ESY.BN	|   A     |
     ----------------------------------------------------------------------
						 (continued on next page)

				      16




				Table 8 (Cont.)
		  OS/8 Combined Kit Modules and Version Codes

     ----------------------------------------------------------------------
     |	      Module	     | Version ||	 Module		| Version |
     |-----------------------|---------||-----------------------|---------|
     | FORTRAN II (cont.)    |	       || Handlers (cont.)      |	  |
     |		IOH.RL       |   10    ||	 TM8E.BN	|   F     |
     |		IOPEN.RL     |   21    ||	 VR12.BN	|   A     |
     |		IPOWER.RL    |   2     ||	 VT50.BN	|   A     |
     |		POWERS.RL    |   5     ||	 VXNS.BN	|   A     |
     |			     |	       ||	 VXSY.BN	|   A     |
     ----------------------------------------------------------------------



     7.0  OBTAINING VERSION CODES FROM OS/8 MODULES

     You can obtain version codes from OS/8 system modules in several ways.
     Many  of  the  programs  allow  you  to enter an option to the Command
     Decoder.  Other programs display their version codes when  they  begin
     operation.   To  get the version codes of device handlers, you can use
     either the BUILD or ODT programs.

     Table 9 lists the modules and the methods for obtaining their  version
     codes.   Additional  information about some of the methods is given in
     the notes that follow.


				    Table 9
		      Obtaining OS/8 Module Version Codes

     ----------------------------------------------------------------------
     |	       Module	     |		       Method			  |
     |-----------------------|--------------------------------------------|
     | ABSLDR		     | Examine location 12200 with ODT (Note 1)   |
     |			     |						  |
     | BASIC.SV		     | Type .EXECUT prog.BA/V			  |
     | BAT		     | Type .RESORC/E (Note 2)			  |
     | BATCH		     | Type /V after BATCH's *			  |
     | BCOMP		     | Type .EXECUT prog.BA/V			  |
     | BITMAP		     | See heading in output listing		  |
     | BLOAD		     | Type .EXECUTE prog.BA/V			  |
     | BOOT		     | Type VERS after Boot's /			  |
     | BRTS		     | Type .EXECUT prog.BA/V			  |
     | BUILD		     | Type VE after BUILD's $			  |
     |			     |						  |
     | CAMP		     | Type VE after CAMP.s #			  |
     | CCL		     | Type VER after Monitor's .		  |
     | CD		     | FUTIL 51.0 (Note 3)			  |
     | CREF		     | See heading in output listing		  |
     ----------------------------------------------------------------------
						(continued on next page)


				      17



				Table 9 (Cont.)
		      Obtaining OS/8 Module Version Codes

     ----------------------------------------------------------------------
     |	       Module	     |			 Method			  |
     |-----------------------|--------------------------------------------|
     | DIRECT		     | Type /W after DIRECT's *			  |
     | DTCOPY		     | See heading in output listing		  |
     | DTFRMT		     | See heading in output listing		  |
     |			     |						  |
     | EABRTS		     | Examine locations 1115 and 1116 with ODT   |
     |			     |   (Note 1)				  |
     | EDIT		     | Type # after EDIT's #			  |
     | EPIC		     | ODT locations 352 and 353 (Note 1)	  |
     |			     |						  |
     | FORT		     | Type /V after FORT's * or examine location |
     |			     |   0342 with ODT (Note 1)			  |
     | FOTP		     | Type /W after FOTP's *			  |
     | FRTS		     | Type /V after FRTS's * or examine locations|
     |			     |   5533 and 5534 with ODT (Note 1)	  |
     | F4		     | See heading in output listing or examine	  |
     |			     |   location 0113 with ODT (Note 1)	  |
     | FUTIL		     | Type SH VERS after FUTIL's *		  |
     |			     |						  |
     | KBM (Keyboard Monitor)| Type VER after Monitor's prompt.		  |
     | KL8E		     | Type RESORC/E (Note 2)			  |
     |			     |						  |
     | LIBRA		     | Examine locations 4404 and 4405 with ODT   |
     |			     |   (Note 1)				  |
     | LIBSET		     | Examine location 12753 with ODT (Note 1)   |
     | LOADER		     | Examine location 17374 with ODT (Note 1)   |
     | LOAD		     | Examine location 12073 and 17074 with ODT  |
     |			     |   (Note 1)				  |
     | LPSV		     | Type RESORC/E (Note 2)			  |
     | LQP		     | Type RESORC/E (Note 2)			  |
     | LINCSY		     | Examine location 207 with ODT (Note 4)     |
     |			     |						  |
     | MCPIP		     | Type /V after MCPIP			  |
     | MSBAT		     | Type /V after MSBAT'			  |
     |			     |						  |
     | ODT		     | FUTIL 60.0 (Note 3)			  |
     | PAL8		     | See heading in output listing		  |
     | PASS2		     | See heading in F4 output listing		  |
     | PASS2O		     | See heading in F4 output listing		  |
     | PASS3		     | See heading in F4 output listing		  |
     | PIP		     | Type /V after PIP's *			  |
     | PIP10		     | See directory listing or examine location  |
     |			     |   4320 with ODT (Note 1)			  |
     |			     |						  |
     | RALF		     | See heading in F4 output listing		  |
     | RESORC		     | Type RESORC/V				  |
     | RF08NS		     | Type RESORC/E (Note 2)			  |
     | RF08SY		     | Examine location 207 with ODT (Note 4)     |
     ----------------------------------------------------------------------
						(continued on next page)

				      18



				Table 9 (Cont.)
		      Obtaining OS/8 Module Version Codes

     ----------------------------------------------------------------------
     |	       Module	     |			 Method			  |
     |-----------------------|--------------------------------------------|
     | RK08NS		     | Type RESORC/E (Note 2)			  |
     | RK08SY		     | Examine location 207 with ODT (Note 4)     |
     | RK8ENS		     | Type RESORC/E (Note 2)			  |
     | RK8ESY		     | Type RESORC/E (Note 2)			  |
     | RKLFMT		     | Examine location 0000 with ODT (Note 1)    |
     | RLFRMT		     | See startup dialog			  |
     | RLSY		     | Type RESORC/E (Note 2)			  |
     | RL0		     | Type RESORC/E (Note 2)			  |
     | RL1		     | Type RESORC/E (Note 2)			  |
     | RL2		     | Type RESORC/E (Note 2)			  |
     | RL3		     | Type RESORC/E (Note 2)			  |
     | RLC		     | Type RESORC/E (Note 2)			  |
     | ROMMSY		     | Type RESORC/E (Note 2)			  |
     | RXNS		     | Examine location 206 with ODT (Note 4)     |
     | RXSY1		     | Examine location 206 with ODT (Note 4)     |
     | RXSY2		     | Examine location 206 with ODT (Note 4)     |
     | RX28C		     | Examine location 206 with ODT (Note 4)     |
     | RX78C		     | Type RESORC/E (Note 2) or examine location |
     |			     |   0572 with ODT (Note 4)			  |
     | RXCOPY		     | Type /V after RXCOPY's *			  |
     |			     |						  |
     | SABR		     | Examine location 206 with ODT (Note 1)     |
     | SET		     | Type VERS after SET's #			  |
     | SRCCOM		     | See output listing			  |
     |			     |						  |
     | TC08SY		     | Examine location 206 with ODT (Note 4)     |
     | TD8ESY		     | Type RESORC/E (Note 2) or examine location |
     |			     |   0207 with ODT (Note 4)			  |
     | TDCOPY		     | See startup dialog or examine locations    |
     |			     |   0074 and 0075 with ODT (Note 1)	  |
     | TDFRMT		     | Examine location 206 with ODT (Note 1)     |
     | TDINIT		     | See startup dialog or examine locations    |
     |			     |   1420 and 1421 with ODT (Note 1)	  |
     | TDROM		     | None					  |
     | TD12K		     | None					  |
     | TD8EA		     | Type RESORC/E (Note 2)			  |
     | TECO		     | Type EO= after TECO's $			  |
     |			     |						  |
     | VXNS		     | Type RESORC/E (Note 2)			  |
     | VXSY		     | Type RESORC/E (Note 2)			  |
     ----------------------------------------------------------------------









				      19



     NOTES:

	  1.  Load the program with  the  GET  command,  then  use  ODT  to
	  examine the contents of the specified location.

	       .GET SYS:prog.ex  <RETURN>
	       .ODT  <RETURN>
	       aaaaa/cccc  <RETURN>

	  where:

	       prog.ex    is the name of the program

	       aaaaa      is  the  memory  location   that   contains   the
			  version code

	       nnnn       is an  octal  number  that  is  the  6-bit  ASCII
			  equivalent  of  the  version  code.  The left two
			  digits represent the  first  character,  and  the
			  right    two    digits   represent   the   second
			  character.

	  Example:

	       To obtain the version code for the ABSLDR program, type:

	       .GET SYS: ABSLDR
	       .ODT
	       12200/6602

	       The value 6602 is the  version  code  in  6-bit  ASCII.   It
	       translates into the characters 6B as follows:

			66 02			__ __
			|   |
			V   V
			6   B

	  2.  Use the RESORC CCL command with the /E  option  to  list  the
	      active  handlers  in the current system head.  If the handler
	      is not in the system head, you must:

		   a.  Run the BUILD program  (see  OS/8  System  Reference
		       Manual).

			 o  Load it into BUILD with the LOAD command.

			 o  Make it active with the INSERT command

			 o  Insert it into the system head  with  the  BOOT
			    command.

		   b.  Use the RESORC/E command to get  a  listing  of  the
		       system's handlers.


				      20



	  3.  To obtain some program version codes, you must run the  FUTIL
	      program as follows:

		   .R FUTIL  <RETURN>
		   bbbb.ddd/nnnn  <RETURN>

	      where:

		   bbbb       is the block number on the system device

		   ddd	is the displacement into the block where  the
			      version code resides.


		   nnnn       is an octal number that is  the  6-bit  ASCII
			      equivalent of the version code.  The left two
			      digits represent the first character, and the
			      right   two   digits   represent  the  second
			      character.  (See the example in Note 1.)

     4.  To obtain   some  handler  version  codes,  you  must  use  ODT  as
	 follows:

	      .LOAD filnam.BN  <RETURN>
	      .ODT  <RETURN>
	      aaaaa/nnnn  <RETURN>

	 where:

	      filnam.BN   is the filename of the handler

	      aaaaa       is  the  memory  location   that   contains   the
			  version code

	      nnnn	is an  octal  number  that  is  the  6-bit  ASCII
			  equivalent  of  the  version  code.  The left two
			  digits represent the  first  character,  and  the
			  right    two    digits   represent   the   second
			  character.  (See the example in Note 1.)

















				      21


					       OS/8 Combined Kit
					       Information Guide
					       DEC-S8-OSRNA-B-D



			       READER'S COMMENTS


      NOTE:  This form is for document comments only.  DIGITAL will 
	     use comments submitted on this form at the company's 
	     discretion. If you require a written reply and are
	     eligible to receive one under Software Performance
	     Report (SPR) service, submit your comments on an SPR 
	     form.


    Did you find this manual understandable, usable, and well-organized?
    Please make suggestions for improvement.
    ______________________________________________________________________
    ______________________________________________________________________
    ______________________________________________________________________
    ______________________________________________________________________
    ______________________________________________________________________
    ______________________________________________________________________
    ______________________________________________________________________


    Did you find errors in this manual?  If so, specify the error and the
    page number.
    ______________________________________________________________________
    ______________________________________________________________________
    ______________________________________________________________________
    ______________________________________________________________________
    ______________________________________________________________________
    ______________________________________________________________________
    ______________________________________________________________________


    Please indicate the type of user/reader that you most nearly represent.

	 []  Assembly language programmer
	 []  Higher-level language programmer
	 []  Occasional programmer (experienced)
	 []  User with little programming experience
	 []  Student programmer
	 []  Non-programmer interested in computer concepts and capabilities


     Name______________________________________Date________________________

     Organization__________________________________________________________

     Street________________________________________________________________

     City__________________________State_____________Zip Code______________
							or
						     Country



     +-+-+-+-+-+-+-+					  +---------------+
     |d|i|g|i|t|a|l|					  |  FIRST CLASS  |
     +-+-+-+-+-+-+-+					  | PERMlT NO. 33 |
							  | MAYNARD. MASS.|
							  +---------------+
								   ========
								   ========
		------------------------------------------	   ========
		|	  BUSINESS REPLY MAIL		 |	   ========
		| FIRST CLASS PERMIT NO.33 MAYNARD MASS. |	   ========
		------------------------------------------	   ========
								   ========
		POSTAGE WILL BE PAID BY ADDRESSEE		   ========
								   ========
								   ========
								   ========
		RT/C SOFTWARE PUBLICATIONS  ML 5-5/E45		   ========
		DIGITAL EQUIPMNT CORPORATION			   ========
		146 MAIN STREET					   ========
		MAYNARD, MASSACHUSETTS  01754			   ========








     -----------------Do Not Tear - Fold Here and Staple-------------------