Programming the DECMATE II for the RD51D Disk Subsystem




			        Revision 1


				16-March-83


				John Elkins
			      Robert F. Morse





		   		Table Of Contents



	Section    						     Page
	
	   1.	INTRODUCTION					       1
		  Bad block mapping				       2
		  Error retries					       2

	   2.	SYSTEM CONTROL DATA ON DISK			       3
		  Block 1: Disk geometry and bad block map	       4
		  Blocks 13..15: Disk directory			       5

	   3.	6120 INSTRUCTIONS AND FLAGS			       6
		  Instructions					       6
		  Flags						       6
		  Interrupts					       7
		  Command execution				       7
		  Power-on reset				       8

	   4.	CONTROLLER COMMANDS				       9
		  Command errors				      10
		  Command error codes				      11
	
	   5.	COMMAND DETAILS
		  Mount volume					      12
		  Get volume data				      13
		  Update volume data				      14
		  Read disk directories				      15
		  Dismount volume				      16
		  Set block					      17
		  Fill buffer					      18
		  Write						      19
		  Read						      20
		  Empty buffer					      21
		  Get error					      22
		  Test error					      23
		  Get status					      24
		  Execute self-test				      25
		  Set retry-count				      26
		  Set normal mode				      27
		  Set special mode				      28
		  Set format sequence				      29
		  Set physical address				      30
		  Restore					      31
		  Format					      32


	APPENDIX A.  OPERATING SYSTEM CONSIDERATIONS		      A1

	APPENDIX B.  CHANGES TO RD51 PROGRAMMING SPECIFICATIONS       B1


	-----------------------------------------------------------------
	Programming the DECMATE II for the RD5lD Disk Subsystem
	Revision 1, 16-March-83					  Page i
	-----------------------------------------------------------------







	    Programming the DECMATE II for the RD51D Disk Subsystem	    _______________________________________________________



	1. INTRODUCTION        _______________


	The RD51D Disk Subsystem consists of a controller and one or  two					       __________
	Winchester disk units.  Each unit has up to eight heads and up to			_____				  _____
	4096 cylinders.  Each cylinder-head (track) has 16 sectors of 512	     _________			     _____	   _______
	bytes each.

	Each physical unit contains up to 60 logical volumes.  Disk  data						     _______
	are  addressed in units of 512-byte (or 256-word) blocks relative							  ______
	to the beginning of a volume (the first  block  is  numbered  0).
	Each  block  is stored in one physical sector (the terms are used 
	interchangably in this document).

	Volumes are created on a disk by entering their descriptions in a
	disk  directory which is written in a fixed location on the disk.	______________
	Each volume's entry  in  the  directory  has  an  eight-character
	volume name, separate 16-bit passwords for read and write access,
	a physical disk starting block, a block  count  which  determines
	the  volume's  size,  a system format indicator (e.g., WPS, CP/M,
	COS-310, OS/8), and additional operating-system dependent data.

	The controller allows access to a volume  via  a  path  called  a 
	logical  device.  The  controller supports 16 such devices, which	_______________
	are designated by numbers from  0  through  15.  To  access  disk
	data  it  is  first necessary to associate a volume with a device
	number by issuing  a  MOUNT  VOLUME  command.  The  eight  device
	numbers  0  through  7  are  for  use  by  operating  systems and
	application programs.  Devices 8  through  15  are  reserved  for
	special functions.

	Once a volume is mounted, its blocks can be read and written.  To
	read  a  block,  use  the SET BLOCK command to specify the device
	number and block number.  Then issue the READ  command  and  wait
	for the "done" flag.  Then use an EMPTY BUFFER command to get the
	block image from the controller's buffer.
	
	To write disk data, issue SET BLOCK to specify device  and  block
	number.  Then  use a FILL BUFFER command to send the block's data
	to the controller's buffer and issue a WRITE command.

	For all normal volumes, only those blocks within the  volume  can
	be  accessed, and volume spaces do not overlap (i.e. a particular
	physical block can be assigned to only  one  volume).  Access  to



	-----------------------------------------------------------------
	Programming the DECMATE II for the RD5lD Disk Subsystem
	Revision 1, 16-March-83					  Page 1
	-----------------------------------------------------------------



	the entire  disk  for  volume  directory  maintenance  is  via  a
	pseudo-volume  called  the "master volume", which maps the entire
	physical disk as a volume such that  volume  block  0  refers  to
	physical  block  0.  The  master  volumes  for  units 0 and 1 are
	permanently mounted on devices 8 and 9, respectively.

	A 6120 program uses six IOT instructions to send commands to  the
	controller,  exchange  data  with it, and test its status.  These
	commands are discussed in section 3, below.  Section 2  describes
	the principal data structures on the disk and in the controller's
	local storage which are necessary to understand the operation  of
	the   various   controller  commands.  Section  4  describes  the
	controller commands in detail.


	Bad block mapping	_________________

	The controller automatically resolves  references  to  physically
	defective blocks.  The disk control block (permanently written on
	block 1 of each disk) contains a  list  of  physically  defective
	blocks  and  the  location  of  a replacement block for each one.
	This list is read  into  the  controller's  storage  whenever  an
	EXECUTE  SELF-TEST  command  is  executed  to create a "bad block
	map".

	There is a value in each sector header that indicates  whether  a
	block  is  a  bad  block.  If a block is bad or if a block is not
	found or if a sector header  contains  a  CRC  error,  the  block
	number  is  looked  up in the bad-block map.  If the block is not
	found in the bad-block map, retries will continue.  If the  block
	is  found,  the block number of the corresponding good block will
	be substituted for the bad block number and  the  read  or  write
	will be retried.


	Error retries	_____________

	Retries consist of  the  following:  If  the  DAA  state  machine
	detects  an  error in a block, the controller firmware determines
	whether the error is  retryable.  There  are  two  categories  of
	retryable errors:

	    Category 1 errors consist of data or header  CRC  errors  and
	    header  found but no data found.  These errors are retried by
	    staying on track and  continuing  to  attempt  the  operation
	    until  either the error goes away or the retry-count (see SET
	    RETRY-COUNT) has been satisfied.

	    Category 2 errors consist of header-not-found  errors.  These
	    errors  are  retried  by  restoring  the  unit  to  track  0,
	    reseeking, and trying again until either the error goes  away
	    or the retry-count has been satisfied.



	-----------------------------------------------------------------
	Programming the DECMATE II for the RD5lD Disk Subsystem
	Revision 1, 16-March-83					  Page 2
	-----------------------------------------------------------------



	2.  SYSTEM CONTROL DATA ON DISK        _______________________________


	The first 64 blocks of a disk contain  special  information  that
	the disk controller firmware requires for operation.

	     Blocks	Usage             ______     _____

	     0		System boot block.  This block  is  read  by  the
			DECmate   II  ROM  bootstrap  code  to  determine 
			whether there is valid firmware in blocks 16..47.

	     1		Disk geometry and bad block map.

	     2..12	    (Reserved)

	     13..15 	Disk directory.  Each block contains a header and
			twenty 24-byte directory entries.

	     16..47 	DECmate II firmware.

	     48..63 	Alternates for bad sectors.

	These blocks constitute a volume whose name is always "FIRMWARE".
	This volume is created by the utility program which formats a new
	disk unit, and can  be  mounted  by  programs  which  update  the
	firmware   or  directory  contents.  (The  contents  of  the disk 
	directory can be read more easily  and  safely  by  a  READ  DISK
	DIRECTORIES command.)


























	-----------------------------------------------------------------
	Programming the DECMATE II for the RD5lD Disk Subsystem
	Revision 1, 16-March-83					  Page 3
	----------------------------------------------------------------- 



	Block 1:  Disk geometry and bad-block map	_________________________________________

	This block contains information about the unit geometry  and  bad
	block  mapping.  Its contents are read by the controller into its
	local RAM storage during an EXECUTE SELF TEST command  (which  is
	automatically performed upon a power-on reset).

	Since the controller is designed to operate with a wide range  of
	Winchester units, it must accomodate varying numbers of cylinders
	and heads.  Therefore this geometry information is recorded in  a
	"disk  control block" at a fixed location on the disk that may be
	accessed without prior knowldege of  the  unit's  geometry.  (All
	units are assumed to have 16 blocks of 512 bytes on each track).

	Occasionally a unit will have bad spots that make  it  impossible
	to  reliably  read  or  write some blocks.  When these blocks are
	discovered, their numbers are recorded in a  "bad-block  map"  in
	the  disk  control  block  and they are physically formatted with
	"bad block" flags.  Subsequent references to such  a  block  will
	cause  it  them  to  be  looked  up  in  the bad-block map, which
	contains the location of an alternate  block  to  be  used  as  a
	replacement for the original block.

	The disk control block is physical block 1 and looks like this:

	    Bytes	Contents	    _____	________

	    0..7 	Literal ASCII value "DRIVEHDR"

	    8..15 	Disk name (ASCII)

	    16..19 	Disk password (binary)

	    20..31 	    Reserved

	    32..33 	16-bit number of  cylinders  on  the  unit  (low,
			high).

	    34		Number of heads on the unit (1..8).

	    35..63	    Reserved

	    64..191	Bad block map.  Provision is made to map up to 16
			bad  blocks.  The  map  contains  16 entries of 8
			bytes each.  The first four  bytes  identify  the
			bad block, as follows:
			    0:	low-order cylinder number
			    1:	high-order cylinder number
			    2:	head number
			    3:	sector number
			The next four  bytes  identify  (using  the  same
			format) the replacement block.



	-----------------------------------------------------------------
	Programming the DECMATE II for the RD5lD Disk Subsystem
	Revision 1, 16-March-83					  Page 4
	----------------------------------------------------------------- 



	Blocks 13..15:  Disk directory	______________________________

	Each disk contains up to 60 logical volumes allocated by  a  user
	through  the  use of a special disk utility program.  Each volume
	has a name, read and write passwords, a number of  blocks  (which
	is always a multiple of 16), and a physical starting point.

	The disk directory occupies three blocks and each block  contains 
	directory  entries  for  20  volumes.  Each block is formatted as 
	follows:

	    Bytes	Contents	    _____	________

	    0..11	Literal ASCII value "DIRECTORY   "

	    12..31 	    (reserved)

	    32..511 	Twenty entries of 24 bytes each

	Each directory entry contains information  as  described  in  the
	following  table.  Note  that  bits  within a byte are numbered 7
	through 0, left to right. Bit 0 is the least-significant bit.

	    Bytes	Contents	    _____	________

	    0..7 	Volume name (ASCII)

	    8..9 	Password for reading (binary)

	    10..11 	Password for writing (binary)

	    12..13	Physical starting  block,  divided  by  16  (low-
			order byte first)

	    14..15	Number  of  blocks  in  volume,  divided  by   16
			(low-order byte first)

	    16		<4> "1" = active volume entry; "0" = unused entry
			<2> "1"  marks  the  "startup  volume"  which  is
			mounted by the MOUNT STARTUP VOLUME command
			<1>  "1"  indicates  that  the  volume  has  been
			modified  by one or more WRITE commands (this bit
			should be cleared by a utility which has  made  a
			backup copy)

	    17..23 	7 bytes of operating system data (see Appendix A)









	-----------------------------------------------------------------
	Programming the DECMATE II for the RD5lD Disk Subsystem
	Revision 1, 16-March-83					  Page 5
	----------------------------------------------------------------- 



	3. 6120 INSTRUCTIONS AND FLAGS	______________________________


	Instructions	____________

	Six instructions are used to program the RD51D controller.  There 
	is one instruction to send a command (RDSC), one to transfer data
	(RDTD), one to control interrupts (RDWE), and three to  test  and
	reset  the  flags.  All  of  the  instructions clear the AC after
	execution except for an RDTD when the direction of data  transfer
	is  "in"  to  the 6120.  Table 1 lists the instructions and their
	octal values.


	_________________________________________________________________


	    Octal   Mnemonic	Description	    _____   ________    ___________

	    6700     --		     (reserved, effect TBS)
	    6701    RDSR	Skip on DATA REQUEST flag; clear flag.
	    6702    RDSC	Send command (in AC) to controller.
	    6703    RDSD	Skip on DONE flag; clear flag.
	    6704    RDTD	Transfer data to/from AC <0:11>.
	    6705    RDWE	Write interrupt-enable mask from AC <11>.
	    6706    RDSE	Skip on ERROR flag; clear flag.
	    6707     --		     (reserved, effect TBS)

			Table 1. 6120 Instructions for RD51D

	_________________________________________________________________



	Flags	_____

	Three flags are used to synchronize the 6120 and the  controller. 
	They are:

	-- DONE, 	  which is set at the  completion  of  a  command
			  (and     causes    an    interrupt    if    the
			  interrupt-enable mask has been set).
	-- ERROR, 	  which is set simultaneously with  DONE  if  the
		     	  command ended with an error condition.
	-- DATA REQUEST,  which is set for each word to be transferred to
			  or  from the controller for commands which have
			  associated data transfers.

	Each flag has an associated "skip" instruction  which  tests  the
	flag  and,  if the flag is set, skips the next instruction in the 
	program and clears the flag.  A 6120  CAF  instruction  does  not								      ___
	affect the flags.



	-----------------------------------------------------------------
	Programming the DECMATE II for the RD5lD Disk Subsystem
	Revision 1, 16-March-83					  Page 6
	----------------------------------------------------------------- 



	Interrupts	__________

	The RDWE instruction stores the low-order-bit of the  AC  in  the
	controller's  interrupt-enable  mask.  A "one" enables interrupts
	so that the assertion of the DONE  flag  generates  an  interrupt
	request.  This  mask  is cleared to "zero" uponpower-on reset.  A
	6120 CAF instruction does not affect the interrupt mask.


	Command execution	_________________

	A program executes an RD51D command as follows:

		-- Issue a command. 
		-- Transfer zero or more words of data. 
		-- Wait for done flag. 
		-- Test error flag.

	To issue a command, the program loads the  AC  with  the  desired
	command word and executes an RDSC instruction to send the command
	to the controller.  The AC is cleared by this instruction.

	Each command may  be  followed  by  a  number  of  data  transfer
	requests  (which may  be  zero).  The  command  descriptions  (in
	section 4) show for each command the number and direction of such
	transfers.  If the number is not zero, the program transfers each
	word by waiting until the DATA REQUEST flag  is  set  (using  the
	RDSR  instruction)  and  then  issuing  an  RDTD  instruction  to
	transfer one word of data.  If the  transfer  direction  is  "in"
	from  the controller to the 6120, the RDTD clears the AC and then
	loads it with the incoming word.  If the  transfer  direction  is
	"out" to the controller from the 6120, the program must place the
	outgoing data in the AC  before  issuing  the  RDTD.  The  AC  is
	cleared by an RDTD for outgoing data.

	The program uses the RDSD instruction to test the DONE flag which
	indicates  the  completion  of a command.  If the RD51D interrupt
	enable mask is set, assertion of the DONE flag will also  request
	an  interrupt.  In  this  case,  the  interrupt service code must
	issue an RDSD to clear  the  flag  and  turn  off  the  interrupt
	request.

	After the DONE flag has been detected and  cleared,  the  program
	may  use  the  RDSE instruction to test and clear the ERROR flag.
	The GET ERROR command can be issued to determine the nature of an
	error.

	Once a command has been issued to  the  controller,  the  program
	must  monitor the DATA REQUEST and DONE flags and satisfy them as
	described above before attempting another command.  There  is  no
	way  to  prematurely  terminate  a  command  except by a power-on
	reset.  Note that the CAF instruction has no effect on the  RD51D
	controller.


	-----------------------------------------------------------------
	Programming the DECMATE II for the RD5lD Disk Subsystem
	Revision 1, 16-March-83					  Page 7
	----------------------------------------------------------------- 



 	Power-on reset	______________

	A power-on reset causes the controller to execute the  equivalent
	of  an EXECUTE SELF-TEST command and to set the DONE and possibly
	the ERROR flags to reflect the outcome of  this  operation.  Note
	that this operation may require 20 seconds or more to complete if
	the disk unit must spin up to speed from rest.
















































	-----------------------------------------------------------------
	Programming the DECMATE II for the RD5lD Disk Subsystem
	Revision 1, 16-March-83					  Page 8
	----------------------------------------------------------------- 



	4. CONTROLLER COMMANDS	______________________


	This section describes the commands which  are  executed  by  the
	controller.  These are listed below in Table 2.


	_________________________________________________________________


							  Octal
	     Command Name		 In/out   Words	   code	    ____________		 ______   _____   _____

		Normal commands		_______________


	     MOUNT VOLUME		 Out	      9   0000
	     GET VOLUME DATA		 In	     24   0030
	     UPDATE VOLUME DATA		 Out	     25   0006
	     READ DISK DIRECTORIES	 In	 n * 24   0033
	     DISMOUNT VOLUME		 Out	      1   0005

	     SET BLOCK			 Out	      3   0001
	     FILL BUFFER (8-bit)	 Out	    512   0102
	     FILL BUFFER (12-bit)	 Out	    256   0002
	     WRITE			 -	      -   0003
	     READ			 -	      -	  0004
	     EMPTY BUFFER (8-bit)	 In	    512   0125
	     EMPTY BUFFER (12-bit)	 In	    256   0025

	     GET ERROR		 	 In	      1	  0027
	     TEST ERROR			 -	      -   0021
	     GET STATUS			 In	      5   0026

	     EXECUTE SELF-TEST		 -	      -   0011
	     SET RETRY COUNT		 Out	      1   0013
	     SET NORMAL MODE		 -	      -   0020
	     SET SPECIAL MODE		 -	      -	  0007
	     SET FORMAT SEQUENCE	 Out	     16	  0015

		Special commands		________________

	     SET PHYSICAL ADDRESS	 Out	      4   0014
	     RESTORE			 -	      -   0016
	     FORMAT			 -	      -   0017

			      Table 2.  Command Summary.


	_________________________________________________________________





	-----------------------------------------------------------------
	Programming the DECMATE II for the RD5lD Disk Subsystem
	Revision 1, 16-March-83					  Page 9
	----------------------------------------------------------------- 



 	There are two classes of commands:  normal  and  special.  Normal
	commands  are  used by operating systems and application programs
	to read and write the various volumes on a disk.  As long as  the
	FIRMWARE  volume  is not mounted, none of the normal commands can
	compromise the volume structure of the disk, and only  blocks  in
	volumes  which are mounted can be read and written.  Only devices
	0 through 7 may be used in normal mode. 

	System utility programs which create and delete volumes and  make
	backup  copies  can  use  the master volumes which are mounted on
	devices 8 and 9 to obtain write access to the  volume  directory.
	These  devices can only be used when the controller is in special
	mode.

	Special commands are used only to physically format  a  disk  and
	write   its  disk  control  block.  They  allow  device-dependent
	addressing by physical unit, cylinder, head, and sector  and  for
	execution of the FORMAT and RESTORE commands.  These commands can
	only be executed after  a  SET  SPECIAL  MODE  command  has  been
	issued.  The controller is set to normal mode by a power-on reset
	and by SET NORMAL MODE and EXECUTE SELF-TEST commands.


	Command errors	______________

	Execution of a command sets or clears the ERROR flag and  puts  a
	value  in  the error register in the controller which can be read
	by a GET ERROR command.  The  detailed  command  descriptions  in
	this  section list the error codes which can be generated by each
	command.  There is a group of codes which can result from  actual
	read  or write access to a disk; these are denoted by the summary
	code DIO in the command  descriptions.  These  codes  (in  octal)
	are:

	     0001  Invalid cylinder number (too high for disk)
	     0005  Data CRC error
	     0006  Header CRC error
	     0007  Header not found (format error, or bad block  with  no
			alternate assigned in bad-block map)
	     0014  DAA failed to complete (controller hardware error)
	     0015  DAA failed to start (controller hardware error)
	     0016  Invalid head number (too high for disk)
	     0020  Invalid unit--not ready or not installed
	     0021  Seek incomplete (disk hardware error)
	     0032  No data found after header (format error)
	
	An RDSC instruction which sends an invalid command  code  to  the
	controller  yields  an error code of 0011.  Table 3 lists all the
	error codes.






	-----------------------------------------------------------------
	Programming the DECMATE II for the RD5lD Disk Subsystem
	Revision 1, 16-March-83					  Page 10
	----------------------------------------------------------------- 



	_________________________________________________________________

	    Octal 
	     code  Meaning	    _____  _______

	    0000   No error
	    0001   Invalid cylinder number	
	    0002   Invalid block number
	    0003     (not used)
	    0004     (not used)
	    0005   Data CRC error
	    0006   ID (header) CRC error
	    0007   ID not found

	    0010   Write fault
	    0011   Illegal command code
	    0012   Unable to find cylinder 0
	    0013   (not used)
	    0014   DAA state machine failed to complete in 2 revolutions
	    0015   DAA state machine failed to respond to abort command
	    0016   Invalid head selected
	    0017   No units in system

	    0020   Invalid unit--not ready or not installed
	    0021   Seek incomplete
	    0022   Invalid device number
	    0023   Volume name not found in directory
	    0024   Device has no volume mounted
	    0025   Read or write access denied
	    0026   Special mode required
	    0027   RAM failure during self-test

	    0030   Bad format command 
	    0031   No index found during FORMAT command 
	    0032   Time-out (found header but no data) 
	    0033   DAA failed self-diagnosis 
	    0034   Invalid volume directory 
	    0035   Invalid disk control block
	    0036     (not used)
	    0037     (not used)

			    Table 3. Command Error Codes.


	_________________________________________________________________










	-----------------------------------------------------------------
	Programming the DECMATE II for the RD5lD Disk Subsystem
	Revision 1, 16-March-83					  Page 11
	----------------------------------------------------------------- 



	MOUNT VOLUME 					     MOUNT VOLUME	____________					     ____________


	This command associates a volume with a device number so that its
	contents can be read and written.  A MOUNT VOLUME command must be
	issued once before the first SET BLOCK, READ or WRITE command for
	that   device.   Each   volume  in  the  disk  directory  has  an
	8-character name.  In addition, one volume may be marked  with  a
	special  flag  as the "startup volume".  In this command, you may
	specify the volume you want either by name or by asking  for  the
	startup volume.

	Command code:  0000

	Data words:  9 out

		 Word	  Bits  Contents		 ____	  ____  ________

		    1    <4:4>  Read access allowed if "1"
			 <5:5>  Write access allowed if "1"
			 <6:6>  "0" for unit 0; "1" for unit 1
			 <7:7>  "0" for mount by name; "1" to  mount  the
				     startup volume
			<8:11> 	Device number by which to refer  to  this
				     volume (0..15)
		 2..9   <4:11>  8-character volume name

	Error codes:

	     0022  Invalid device number
	     0023  Volume name not found in directory
	     0026  Special mode required for devices 8..15
	     0034  Invalid volume directory
	     DIO   Disk read errors

	Notes:

	     1.  Execution of this command sets the device number to  the
	         number  specified in word 1 and sets the block number to
		 0.

	     2.  This command destroys the contents of the block buffer.

	     3.  Do not attempt to mount a volume  on  devices  8  or  9;
		 these  are  reserved  for  the master volumes (which are
		 automatically mounted at the conclusion of  a  self-test
		 command).








	-----------------------------------------------------------------
	Programming the DECMATE II for the RD5lD Disk Subsystem
	Revision 1, 16-March-83					  Page 12
	----------------------------------------------------------------- 



	GET VOLUME DATA 				  GET VOLUME DATA	_______________					  _______________


	This command returns the contents of the directory entry for  the
	volume  mounted  on  the device referenced in the most recent SET
	BLOCK command.

	Command code:  0030

	Data words:  24 in

		 Word	  Bits  Contents		 ____	  ____  ________

		 1..8   <4:11>  Volume name
		9..10   <4:11>  Read password
	       11..12   <4:11>  Write password
	       13..14   <4:11>  Starting physical block  number,  divided
				     by 16  (low-order 8 bits in first
				     word)
	       15..16   <4:11>  Number of blocks in volume, divided by 16
				     (low-order 8 bits in first word)
		   17	   <4>  "1" indicates read access permitted
			   <5>  "1" indicates write access permitted
			   <6>  "0" for unit 0; "1" for unit 1
			   <7>  "1" if a volume is mounted on this device
			   <9>  "1" if this is the "startup" volume
			  <10>  "1" if this volume has been modified by a
				     WRITE command
	       18..24   <4:11>  OS-dependent data (see Appendix A)

	Error codes:  none

	Notes:

	     1.  If bit 7 of word 17 is "0", no volume is mounted on  the
		 device and the rest of the data returned by this command 
		 is invalid.


















	-----------------------------------------------------------------
	Programming the DECMATE II for the RD5lD Disk Subsystem
	Revision 1, 16-March-83					  Page 13
	----------------------------------------------------------------- 



	UPDATE VOLUME DATA 			       UPDATE VOLUME DATA	__________________			       __________________


	This command replaces the contents of the directory entry for the 
	volume  mounted  on the specified device (except for the physical 
	size and location of the volume).  It can be used, in conjunction 
	with  GET  VOLUME DATA, to rename a volume, change its passwords, 
	alter the "startup" and "modified" flags, and change its OS data.

	Command code:  0006

	Data words:  25 out

		 Word     Bits  Contents

		    1   <8:11>  Device upon which the volume is presently
				     mounted (0..7) 
		 2..9   <4:11>  Volume name
	       10..11   <4:11>  Read password
	       12..13   <4:11>  Write password
	       14..17 		  (ignored)
		   18	   <4>  "1" indicates read access permitted
			   <5>  "1" indicates write access permitted
			 <6:7>    (ignored)
			   <9>  "1" if this is the "startup" volume
			  <10>  "1" if this volume has been modified by a
				  WRITE command
	       19..25   <4:11>  OS-dependent data (see Appendix A)

	Error codes:
	     0022  Invalid device number
	     0024  Device has no volume mounted
	     DIO   Disk I/O errors

	Notes:

	     1.  The arrangement of the 24 words to  be  written  to  the
		 volume's  directory  entry is the same as those returned
		 by GET VOLUME DATA.  Thus  these  two  commands  can  be
		 conveniently  used  to selectively alter a volume's data
		 by getting it with GET VOLUME DATA, making  the  desired
		 alterations,  and  then  rewriting it with UPDATE VOLUME
		 DATA (remembering to precede the  data  for  the  latter
		 with the device number).

	     2.  The new data is  both  written  to  the  permanent  disk
		 directory  and  stored in the controller's device table,
		 making any changes immediately effective.  For  example,
		 if  the  update  alters  the  read or write access bits,
		 these will govern subsequent attempts to use the  volume
		 until it is dismounted and remounted (these bits are not
		 written in the disk directory).

	     3.  This command destroys the contents of the block buffer.

	-----------------------------------------------------------------
	Programming the DECMATE II for the RD5lD Disk Subsystem
	Revision 1, 16-March-83					  Page 14
	----------------------------------------------------------------- 


	
	READ DISK DIRECTORIES 			    READ DISK DIRECTORIES	_____________________			    _____________________


	This command reads the directories of all the disks available  to
	the controller and returns the contents of each 24-byte directory
	entry which represents a volume on a  disk.  Unused  entries  are
	not  returned.  The  number of transfer requests will be 24 times
	the number of volumes defined in the available directories.

	Command code:  0033

	Data words:  n * 24 in

		 Word 	  Bits  Contents		 ____	  ____  ________

		 1..8   <4:11>  Volume name
		9..10   <4:11>  Read password
	       11..12   <4:11>  Write password
	       13..14   <4:11>  Starting physical block  number,  divided
				     by  16  (low-order  8  bits in first
				     word)
	       15..16   <4:11>  Number of blocks in volume, divided by 16
				     (low-order  8  bits  in  first word)
		   17	   <6>	"0" for unit 0; "1" for unit 1
			   <7>  "1" if an active directory entry  (should
				     never be "0")
			   <9>  "1" if this is the "startup"
			  <10>  "1" if this volume has been modified by a
				     WRITE command
	       18..24   <4:11>  OS-dependent data (see Appendix A)

	Error codes:

	     0034  Invalid volume directory
	     DIO   Disk read errors

	Notes:

	     1.  This command destroys the contents of the block buffer.
















	-----------------------------------------------------------------
	Programming the DECMATE II for the RD5lD Disk Subsystem
	Revision 1, 16-March-83					  Page 15
	----------------------------------------------------------------- 



	DISMOUNT VOLUME 				  DISMOUNT VOLUME	_______________					  _______________


	This command reverses the effect of a  MOUNT  VOLUME  command  by
	breaking  the  association  between a device number and a volume.
	After execution of this command,  subsequent  references  to  the
	device number will be rejected.
		
	Command code:  0005

	Data words:  1 out

		 Word     Bits  Contents		 ____	  ____  ________

		    1   <8:11>  Device number from which volume is to  be
				    dismounted (0..15)

	Error codes:

	     0022  Invalid device number 
	     0026  Special mode required for devices 8..15

	Notes:

	     1.  Issuing DISMOUNT VOLUME invalidates  the  stored  device
		 and  block  numbers  in the controller.  A new SET BLOCK
		 must precede the next READ or WRITE.

	     2.  No error occurs if no volume was mounted on the device.

	     3.  The master volumes on devices 8 and 9  should  never  be
		 dismounted.  (An  EXECUTE  SELF-TEST  will remount them,
		 but will dismount the volumes on all other devices.)






















	-----------------------------------------------------------------
	Programming the DECMATE II for the RD5lD Disk Subsystem
	Revision 1, 16-March-83					  Page 16
	----------------------------------------------------------------- 



	SET BLOCK 						SET BLOCK	_________						_________


	This command establishes  the  device  and  block  number  for  a
	subsequent READ or WRITE operation.

	Command code:  0001

	Data words:  3 out

		 Word     Bits  Contents		 ____	  ____  ________

		    1   <8:11>  Device number (0..15)
		    2   <0:11>  Low-order 12 bits of block number
		    3   <4:11>  High-order 8 bits of block number

	Error codes:

	     0002  Invalid block number (too high for volume)
	     0022  Invalid device number
	     0024  Device has no volume mounted
	     0026  Special mode required for devices 8..15

































	-----------------------------------------------------------------
	Programming the DECMATE II for the RD5lD Disk Subsystem
	Revision 1, 16-March-83					  Page 17
	----------------------------------------------------------------- 



	FILL BUFFER 					      FILL BUFFER	___________					      ___________


	This command transfers a block of  data  from  the  6120  to  the
	controller's  block buffer.  It is used prior to a WRITE command.
	If the command qualifier is "1" (8-bit mode) then there  will  be
	512 transfer requests, each for a byte of data from AC<4:11>.  If	
	the command qualifier is "0" (12-bit mode) then there will be 256	
	transfers, each for a word of data from AC<0:11>.

	Command code:  0002 (12-bit)
		       0102 (8-bit)

	Data words:  256 out (12-bit)
		     512 out (8-bit)

	Error codes:  none






































	-----------------------------------------------------------------
	Programming the DECMATE II for the RD5lD Disk Subsystem
	Revision 1, 16-March-83					  Page 18
	----------------------------------------------------------------- 



	WRITE 							    WRITE	_____							    _____


	This command writes the contents of the block buffer to the disk. 
	This  command  normally  should  be  preceeded  by  a FILL BUFFER
	command and a SET BLOCK  command  or  (in  special  mode)  a  SET
	PHYSICAL ADDRESS command.

	Command code:  0003

	Data words:  none

	Notes:

	     1.  If the "modified" flag in the volume's directory data is 
		 "0",  execution  of a WRITE sets that bit to "1" in both
		 the device table and the on-disk  directory.  (This  bit
		 can be cleared by using the UPDATE VOLUME DATA command.)

	Error codes:

	     0025  Write access denied  (i.e. the volume was mounted with 
			a  "0"  in  AC<5> of word 1 of the command's data 
			words).
	     DIO   Disk write errors






























	-----------------------------------------------------------------
	Programming the DECMATE II for the RD5lD Disk Subsystem
	Revision 1, 16-March-83					  Page 19
	----------------------------------------------------------------- 



	READ 							     READ	____							     ____


	This command reads the selected block  from  the  disk  into  the
	controller's  block buffer.  A subsequent EMPTY BUFFER command is
	needed to bring the data back  to  the  6120.  Note  that  before
	issuing  this  command, the 6120 program should issue a SET BLOCK
	command or (in special mode) a SET PHYSICAL ADDRESS command.

	Command code:  0004

	Data words:  none

	Error codes:

	     0025  Read access denied (i.e. the volume was  mounted  with
			a  "0"  in  AC<4> of word 1 of the command's data
			words).
	     DIO   Disk read errors




































	-----------------------------------------------------------------
	Programming the DECMATE II for the RD5lD Disk Subsystem
	Revision 1, 16-March-83					  Page 20
	----------------------------------------------------------------- 



	EMPTY BUFFER 					     EMPTY BUFFER	____________					     ____________


	This command transfers the contents  of  the  controller's  block
	buffer to the 6120.  If the command qualifier is "1" (8-bit mode)
	then there will be 512 data transfers, each for a  byte  of  data
	into  AC<4:11> (AC<0:3> is cleared).  If the command qualifier is
	"0" (12-bit mode) then there will be 256 transfers,  each  for  a
	word of data into AC<0:11>.

	Command code:  0025 (12-bit)
		       0125 (8-bit)

	Data words:  256 in (12-bit)
		     512 in (8-bit)

	Error codes:  none

	Notes:

	     1.  This  command  does  not  alter  the  contents  of   the
		 controller's block buffer.

































	----------------------------------------------------------------- 
	Programming the DECMATE II for the RD5lD Disk Subsystem
	Revision 1, 16-March-83					  Page 21
	----------------------------------------------------------------- 



	GET ERROR 						GET ERROR	_________						_________


	This command returns the error code   set  by  the  last  command
	executed  (other  than GET ERROR).  This command may be issued at
	any time after the completion of another command,  regardless  of
	whether  or not the error flag was set.  A returned value of zero
	indicates that there was no  error.  Execution  of  this  command
	does  not  clear  the error register.  Table 3 lists the possible 
	error code values.

	Command code:  0027		

	Data words:  1 in

		 Word     Bits  Contents

		    1   <0:11>  Error code from previous command

	Error codes:

	     (any; see description above)

































	-----------------------------------------------------------------
	Programming the DECMATE II for the RD5lD Disk Subsystem
	Revision 1, 16-March-83					  Page 22
	----------------------------------------------------------------- 



	TEST ERROR 					       TEST ERROR	__________					       __________


	This command sets or clears  the  ERROR  flag  according  to  the
	current  value  in the controller's error register.  If the value
	is not zero, the ERROR flag is  set;  otherwise  it  is  cleared.
	Execution of this command does not alter the error register.

	Command code:  0021

	Data words:  none

	Error codes:

	     (any; see description above)








































	-----------------------------------------------------------------
	Programming the DECMATE II for the RD5lD Disk Subsystem
	Revision 1, 16-March-83					  Page 23
	----------------------------------------------------------------- 



	GET STATUS 					       GET STATUS	__________					       __________


	This command returns the current mechanical status of  the  last-
	selected  unit  and  the  physical cylinder, head and sector last
	addressed.

	Command code:  0026

	Data words:  5 in

		 Word	  Bits  Contents

		    1    <4:4>  Index pulse (transient)
			 <5:5>  "1" if unit is at physical cylinder zero
			 <6:6>  "1" if a write fault occurred on the last 
				     disk operation
			 <7:7>  "1" if selected unit is ready
			 <8:8>       (undefined)
			 <9:9>  "1" if seek complete (from unit)
		       <10:10>  "1" if unit 1  is  selected  (acknowledge
				     signal from unit)
		       <11:11>  "1" if unit 0  is  selected  (acknowledge
				     signal from unit)
		    2   <0:11>  Cylinder number 
		    3   <9:11>  Head number 
		    4   <8:11>  Sector number 
		    5   <0:11>  Controller program version number

	Error codes:  none

























	-----------------------------------------------------------------
	Programming the DECMATE II for the RD5lD Disk Subsystem
	Revision 1, 16-March-83					  Page 24
	----------------------------------------------------------------- 



	EXECUTE SELF-TEST 				EXECUTE SELF-TEST	_________________				_________________


	This command causes the controller to execute its self-test  code
	and  reset  its  internal data.  It dismounts all mounted volumes
	and sets the controller to "normal" command mode.  It  reads  the
	disk  control  blocks  (block  1)  from  each  available  disk to
	establish their geometries and store their  bad-block  maps,  and
	mounts the master volumes on devices 8 and 9.

	Command code:  0011

	Data words:  none

	Error codes:

	     0017  No units are attached to the controller
	     0027  RAM failure during self-test 
	     0033  DAA failed its self-test 
	     0035  Invalid device control block 
	     DIO   Disk read error (on device control block)

	Notes:

	     1.  Since self-test  dismounts  all  volumes,  no  reads  or
		 writes  can  be performed (except to the master volumes) 
		 until one  of  the  MOUNT  commands  has  been  executed
		 successfully after this command.

	     2.  This command is executed automatically upon  a  power-on
		 reset.
























	-----------------------------------------------------------------
	Programming the DECMATE II for the RD5lD Disk Subsystem
	Revision 1, 16-March-83					  Page 25
	----------------------------------------------------------------- 



	SET RETRY-COUNT 				  SET RETRY-COUNT	_______________					  _______________


	The disk controller will retry read and write errors by restoring
	seeking  to cylinder 0) and re-seeking and reading/writing again.
	It will do  this  <retry-count>  times.  The  default  value  for
	<retry-count>  is  1.  This   command   alters   the   value   of
	<retry-count>; the  new value remains effective until another SET
	RETRY-COUNT or an EXECUTE SELF-TEST command is executed.

	Command code:  0013

	Data words:  1 out

		 Word     Bits  Contents		 ____	  ____	________

		    1   <4.11>  Number of retries to attempt

	Error codes:  none




































	-----------------------------------------------------------------
	Programming the DECMATE II for the RD5lD Disk Subsystem
	Revision 1, 16-March-83					  Page 26
	----------------------------------------------------------------- 



	SET NORMAL MODE 				 SET NORMAL MODE	_______________					 _______________


	This command  places  the  controller  in  "normal"  mode,  which
	disallows  execution  of  all  of  the  "special  mode" commands.
	Special mode can only be reestablished by the  SET  SPECIAL  MODE
	command.

	Command code:  0020

	Data words:  none

	Error codes:  none










































	-----------------------------------------------------------------
	Programming the DECMATE II for the RD5lD Disk Subsystem
	Revision 1, 16-March-83					  Page 27
	----------------------------------------------------------------- 



	SET SPECIAL MODE 				 SET SPECIAL MODE	________________				 ________________


	This command enables the execution  of  "special"  disk  commands
	listed in Table 2 and the use of devices 8 through 15.

	Command code:  0007

	Data words:  none

	Error codes:  none












































	-----------------------------------------------------------------
	Programming the DECMATE II for the RD5lD Disk Subsystem
	Revision 1, 16-March-83					  Page 28
	----------------------------------------------------------------- 



	SET FORMAT SEQUENCE			      SET FORMAT SEQUENCE	___________________			      ___________________


	This command specifies the order in which the sixteen sectors  on
	a  track  are  numbered  when the track is formatted, and must be
	issued  before  issuing  a  FORMAT  command.  Sixteen  words  are
	transmitted to the controller, each containing a sector number in
	bits  8:11.  Each  number from 0 through 15 must be sent once and
	only once.  The sequence can be set up to effect an  interleaving
	scheme  to  match  the  speed  of  the  disk  to the speed of the
	programs which use it.

	A physically defective sector is permanently marked as such by  a
	value of 255 (decimal) in the word in the pattern list containing
	its sector number.  The controller will record this in the sector
	header  on  the  disk  track.  When  a  block  so marked is later
	accessed, the controller  will  note  the  flag  and  search  the
	bad-block map for the identity of a substitute block.

	Command code:  0015

	Data words:  16 out

		 Word     Bits  Contents		 ____	  ____	________

		1..16   <4:11>  Sector number 0..15, or  255  for  a  bad
				     sector

	 Error codes:  none


























	-----------------------------------------------------------------
	Programming the DECMATE II for the RD5lD Disk Subsystem
	Revision 1, 16-March-83					  Page 29
	----------------------------------------------------------------- 



	SET PHYSICAL ADDRESS 			     SET PHYSICAL ADDRESS	____________________			     ____________________


	This command selects the unit, cylinder, head and  sector  to  be
	used for subsequent READ, WRITE, RESTORE, or FORMAT commands.

	Command code:  0014

	Data words:  4 out

		  Word	   Bits  Contents		  ____	   ____	 ________

		     1  <11:11>  "0" = select unit 0
				 "1" = select unit 1
		     2	 <0:11>	 Cylinder number, 0 4095 (subject to  the
				      physical limits of the unit!)
		     3   <9:11>  Head number, 0..7
		     4   <8:11>  Sector number, 0..15

	Error codes:

	     0026  Special mode required

	Notes:

	     1.  This command merely stores the cylinder  value; it  does
		 not perform a physical disk seek.

	     2.  The cylinder number must be in the  range  zero  through
		 one  less  than  the number of physical cylinders in the
		 unit.  This is not checked in this command, but will  be
		 checked  when  an  actual disk operation attempts to use
		 the cylinder value.

	     3.  The head number must be in the range  zero  through  one
		 less  than the number of heads in the unit.  This is not
		 checked in this command, but will  be  checked  when  an
		 actual disk operation attempts to use the head value.

















	-----------------------------------------------------------------
	Programming the DECMATE II for the RD5lD Disk Subsystem
	Revision 1, 16-March-83					  Page 30
	----------------------------------------------------------------- 



	RESTORE 						  RESTORE	_______							  _______


	This command moves the heads of the previously selected unit (see
	SET  PHYSICAL ADDRESS command) to cylinder 0 (the outside edge of
	the disk).  The command will complete within 1.2 seconds.

	Command code:  0016

	Data words:  none

	Error codes:

	     0012  Unable to find cylinder 0 (disk hardware error)
	     0020  Unit not installed
	     0026  Special mode required







































	-----------------------------------------------------------------
	Programming the DECMATE II for the RD5lD Disk Subsystem
	Revision 1, 16-March-83					  Page 31
	----------------------------------------------------------------- 



	FORMAT 							   FORMAT	______							   ______


	This command  writes  sector  format  information  on  the  track
	designated  by  the  preceding SET PHYSICAL ADDRESS command.  The
	sectors are numbered in the sequence specified by  the  preceding
	SET FORMAT SEQUENCE command.	

	Command code:  0017

	Data words:  none
	
	Error codes:

	     0026  Special mode required 
	     0030  Bad format command 
	     0031  No index found 
	     DIO   Disk I/O errors

	Notes:

	     1.  Formatting destroys the contents  of  the  track.  After 
		 formatting,  each  sector  contains  512 bytes of binary 
		 zeros.

	     2.  A SET FORMAT SEQUENCE command must be issued before  the
		 first use of the FORMAT command, but that pattern is not
		 altered by  FORMAT  and  remains  valid  for  subsequent
		 FORMAT commands.


























	-----------------------------------------------------------------
	Programming the DECMATE II for the RD5lD Disk Subsystem
	Revision 1, 16-March-83					  Page 32
	----------------------------------------------------------------- 



	Appendix A.  OPERATING SYSTEM CONSIDERATIONS	____________________________________________


	The last seven bytes (offset 17  through  23)  of  each  volume's
	24-byte  directory  entry  contain  data  specific  to  the  file
	structure of the  volume.  The  first  byte  indicates  the  file
	structure of the volume, as follows:

	     Bytes    Bits      Contents	     _____  _________	________

		17  X... ....	Bootable-system  flag  A  "1"   marks   a
				    volume  whose  block  0  contains  an 
				    executable bootstrap loader.

		17  .XXX XXXX 	File structure (values in octal): 
				    010  WPS-8 
				    011  OS-8
				    012  COS 310 
				    100  CP/M

	Bytes 18..23 for the various file structures are TBS.


	Operating system bootstrapping	______________________________

	A logical volume may contain an operating  system  which  can  be
	bootstrapped  into  an  empty  machine.  Such  a volume is marked
	"bootable" (as shown above) and has a 256-word  bootstrap  loader
	in  its  block  0.  By convention, such a system is loaded by the
	following command sequence:

	    -- Execute self-test to dismount all volumes.
	    -- Mount the system volume on device 0.
	    -- Read block 0 from the volume
	    -- Empty the buffer in 12-bit mode (256 words) into 6120
		  storage starting at address 0200 in field 0.
	    -- Begin execution at address 0210.

	A special case is the "startup" volume.  This is marked  so  that
	it  can  be mounted by a MOUNT VOLUME command without knowing its
	name.  The DECmate II firmware mounts and bootstraps this  volume
	after  the firmware has been loaded during system initialization.
	Operating systems which have completed operation  and  have  been
	directed to "quit" should mount and bootstrap the startup volume.


			     <<< End of document >>>








	-----------------------------------------------------------------
	Programming the DECMATE II for the RD5lD Disk Subsystem
	Revision 1, 16-March-83					  Page A1
	----------------------------------------------------------------- 


	Changes to RD5lD Programming Specifications 		  Page B1
	_________________________________________________________________


	- - - - - - - 
	d i g i t a l				MEMORANDUM
	- - - - - - - 
						From: Bob Morse
	To: J. Elkins				Dept: Micro Systems Eng.
	D. Rice					Loc : MLO3-2/E41
	W. Keefe				DTN : 223-6720

	cc: Interested parties			Date: 16-Mar-83 (rev 2)

	Subject: Changes to RD51D Programming Specifications

	_________________________________________________________________


	This memo summarizes changes to  the  programming  specifications
	for  the  RD51D  hard  disk controller for the DECmate II.  These 
	alter  the  controller  commands  described  in  Programming  the							 ________________
	DECmate  II  for  the  RD51D  Disk Subsystem, revision 0, dated 7	____________________________________________
	January  1983,  and  are  incorporated  in  revision  1  of  that
	document.  The revised specifications are reflected in version 13 
	("D") and later of the 8751 controller ROM.

	   1.	The number of logical devices available to a  normal-mode
		user  has  been  reduced from 16 to 8.  Only devices 0..7
		should be used for normal program  and  operating  system
		functions.  Devices  8..15  may be used only when special
		mode is in effect.

	   2.	Devices 8 and 9 are automatically initialized  to  access
		the "master volume" (which maps the entire physical unit)
		for units 0 and 1, respectively.  These  devices  can  be
		used  only in master mode.  Their volumes should never be
		dismounted!

	   3.	The MOUNT MASTER VOLUME  command  (code  0006)  has  been
		deleted.

	   4.	The MOUNT STARTUP VOLUME command  (code  0010)  has  been
		deleted.  Its  function  is  now  performed  by the MOUNT 
		VOLUME command (see next item).

	   5	The MOUNT VOLUME command no longer checks  the  read  and
		write  passwords;  this  is now the responsibility of the
		operating system (error  code  0037  has  been  deleted).
		This  reduces the number of data words from 13 to 9:  one
		option byte followed by 8 bytes of volume name.

		This command no longer checks for duplicate mounting of a
		volume (error code 0036 has been deleted).  Such mounting
		poses no problems to the controller, but programs  should
		be  wary  of  mounting  the  same volume on more than one
		device if they then believe the two  devices  to  contain
		independent data!



	Changes to RD5lD Programming Specifications 		  Page B2
	_________________________________________________________________


		Bit 4 (or AC<7>) of the flag byte is  "0"  for  a  normal
		mount  by  name,  or "1" to mount the startup volume.  In
		the latter case, the name supplied with  the  command  is
		ignored. 

	   6.	The GET  VOLUME  PARAMETERS  and  READ  DISK  DIRECTORIES
		commands  no longer suppress the contents of the password
		fields.  This data is now returned to the caller, who  is
		now responsible for password checking.

	   7.	The GET CONTROLLER VERSION command (code 0031)  has  been
		eliminated.  Instead,  the  version number is returned as
		the fifth word of data returned by a GET  STATUS  command
		(code 0026).

	   8.	The READ STARTUP SECTOR  command  (code  0032)  has  been
		eliminated.  Instead,  read  block 0 of the master volume
		(which is pre-mounted on device 8) and do a normal 12-bit
		empty-buffer.

	   9.	The SET DRIVE, SET CYLINDER,  SET  HEAD  and  SET  SECTOR
		commands  (codes  0040,  0041,  0042  and 0043) have been
		replaced by a single command named SET  PHYSICAL  ADDRESS
		(code   0014)   which   sends  four  data  words  to  the
		controller.  These four words are identical to  the  four
		sent   separately  by  the  four  former  commands.  This
		command is for use only by  the  disk-formatting  utility				   ____
		and diagnostic exerciser programs.


	   10.	Command  codes  for  the  following  commands  have  been
		changed (to reduce the size of the command dispatch table
		in the controller):

		    Command		    Old code   New code		    _______		    ________   ________

		    SET NORMAL MODE	      0047 	 0020
		    SET FORMAT SEQUENCE	      0050 	 0015
		    RESTORE		      0045 	 0016
		    FORMAT		      0046	 0017

	   11.	The information returned by the GET  STATUS  command  has
		been  revised:  Bit  3  of  the  first byte (or AC<8>) no
		longer reflects the "error"  status;  its  value  is  now
		unspecified.  A  fifth  word  has  been  added; it is the
		controller program version number.

	   12.  The SET  SPECIAL  MODE  COMMAND  (code  0007)  no  longer
		requires a password and hence requires no data words.

	   13.	Electrical interface problems limit the  present  version
		of  the  firmware  to  one  unit  (unit 0); a second unit
		cannot  be  attached.  However,  the  controller  command
		structure  remains in place to handle two units in future 
		versions.



	Changes to RD51D Programming Specifications 		  Page B3
	_________________________________________________________________


	   14.	A new command named UPDATE VOLUME DATA (code 0006) allows
		any  of  the  data in a volume's directory entry, such as
		name, OS type, and "modified" flag, to be revised without
		disturbing  the  contents  of  the  volume.  The volume's
		physical position and size are protected from  alteration
		by this command.

	   15.	A new command named TEST ERROR (code 0021)  requests  the
		controller   to   set  its  ERROR  flag  (again)  if  the
		controller's error register  contains  a  non-zero  error
		code.

	   16.	The following error codes are no longer (or  never  were)
		generated by the controller: 
		    0003  Self test failed in unit 
		    0004  Self test failed in controller
		    0013  Data mark (in format) not found 
		    0036  Volume already mounted on another device 
		    0037  Incorrect read or write password

		Error code 0027 is  newly  defined.  Its  description  is
		"RAM failure in self test".

	In order  to  reduce  confusion  with  various  operating  system
	terminologies,  the  word "unit" has been substituted for "drive"
	to refer to the physical hard disk mechanism which  is  connected
	to one of the two electrical interfaces of the controller.

	For the convenience of various system maintenance  programs,  the
	64-block  area  at  the  beginning  of a unit (which contains its
	device control block, volume directory, and system firmware) will
	be  described  as  a  volume named FIRMWARE with a file structure
	code of 0.  This will be the first entry in the volume directory,
	and  is created by the FORMAT program which initializes the unit.
	The controller does not depend upon the presence of  this  entry,
 	but  utility  programs may use it instead of the master volume to
	reduce the chances of inadvertantly  damaging  data  outside  the
	first 64 blocks.

	The bootstrap block which is written in block  0  of  a  bootable
	volume  now  has a standard execution entry point of 0210 instead
	of 0200.  This leaves the first 16 bytes of  the  block  free  to
	contain the DEC standard boot block identification sequence.

	rfm