RTS8V2B.DOC





















    				  DISCLAIMER

		This document file was created by scanning  the 
		original  document and then editing the scanned 
		text.  As much as possible, the  original  text 
		format  was restored.  Some format changes were 
		made to insure this  document  would  print  on 
		current laser printers using 60 lines per page.
    		The  original  spelling  and  grammar  has been 
    		preserved.


		1-Jun-1996













				     RTS/8 
				 User's Manual
						
			  Order No. DEC-08-ORTMA-C-D






				  Version 2B




































	     digital equipment corporation - maynard, massachusetts




						First Printing, June 1974
						Revised: September 1975
						February 1977



     The information in this document is subject to change without notice
     and should not be construed as a commitment by Digital Equipment
     Corporation. Digital Equipment Corporation assumes no responsibility
     for any errors that may appear in this document.

     The software described in this document is furnished under a license
     and may be used or copied only in accordance with the terms of such
     license.

     Digital Equipment Corporation assumes no responsibility for the use
     or reliability of its software on equipment that is not supplied by
     DIGITAL.







     Copyright  1974, 1975, 1977 by Digital Equipment Corporation







     The postage prepaid READER'S COMMENTS form on the last page of this
     document requests the user's critical evaluation to assist us in pre-
     paring future documentation.


     The following are trademarks of Digital Equipment Corporation:


	       DIGITAL	         DECsystem-10	     MASSBUS
	       DEC	         DECtape	     OMNIBUS
	       PDP	         DIBOL	             OS/8
	       DECUS	         EDUSYSTEM	     PHA
	       UNIBUS	         FLIP CHIP	     RSTS
	       COMPUTER LABS	 FOCAL	             RSX
	       COMTEX	         INDAC	             TYPESET-8
	       DDT	         LAB-8	             TYPESET-10
	       DECCOMM	         DECsystem-20	     TYPESET-11
	       RTS/8

				   CONTENTS

								       Page

     PREFACE							       vii

     CHAPTER  1		INTRODUCTION				       1-1

	      1.1	RTS/8 DESCRIPTION			       1-1
	      1.2	REAL-TIME SYSTEM OPERATION		       1-2

     CHAPTER  2		USING TASKS UNDER RTS/8			       2-1

	      2.1	THE STRUCTURE OF RTS/8 TASKS		       2-1
	      2.2	CONCEPTS OF TASK COMMUNICATION		       2-1
	      2.2.1	  Task Synchronization Through the Use of
			  Event Flags				       2-2
	      2.2.2	  Intertask Messages			       2-3
	      2.3	EXECUTIVE INTERNAL TASK TABLES		       2-5

     CHAPTER  3		RTS/8 EXECUTIVE REQUESTS		       3-1

	      3.1	COMMUNICATION WITH THE RTS/8 EXECUTIVE	       3-1
	      3.2	ERs USED TO COMMUNICATE BETWEEN TASKS	       3-1
	      3.2.1	  SEND - Send Message			       3-2
	      3.2.2	  WAITE - Wait on Event Flag		       3-3
	      3.2.3	  SENDW - Send and Wait			       3-3
	      3.2.4	  RECEIVE - Receive Message		       3-4
	      3.2.5	  POST - Post Event Flag		       3-5
	      3.2.6	  Example of ERs for Message and Event Flags   3-5
	      3.3	ERs USED TO SET AND CLEAR TASK FLAGS	       3-7
	      3.3.1	  BLKARG - Block Task for Specified Reason     3-7
	      3.3.2	  UNBARG - Unblock Task for Specified Reason   3-8
	      3.3.3	  SUSPND - Suspend a Task's Execution	       3-8
	      3.3.4	  RUN - Run a Task			       3-9
	      3.4	USING INTERRUPTS IN RTS/8		       3-10
	      3.5	EXECUTIVE REQUEST WAIT STATES		       3-13

     CHAPTER  4		RTS/8 SYSTEM TASKS			       4-1

	      4.1	CLOCK HANDLER				       4-2
	      4.1.1	  Examples of Clock Handler Calls	       4-4
	      4.2	TERMINAL HANDLER			       4-5
	      4.2.1	  Additional Assembly Parameters Affecting
	 	          Terminal Handler Properties		       4-8
	      4.2.2	  Useful Equates in the Parameter File	       4-10
	      4.2.3	  Examples of Terminal Handler Messages	       4-11
	      4.3	LINE PRINTER HANDLER			       4-11
	      4.4	MASS STORAGE HANDLERS			       4-12
	      4.4.1	  Floppy Disk Handler		 	       4-14
	      4.4.2	  LINCtape Handler			       4-18
	      4.4.3	  Example of Mass Storage Handler Call	       4-20
	      4.5	POWER FAIL TASK				       4-20
	      4.6	OS/8 SUPPORT TASK			       4-21
	      4.6.1 	  Mapping of Fields with OS/8 Support Task     4-23




				      iii

				CONTENTS (Cont.)

								       Page

	      4.7	OS/8 - RTS/8 COMMUNICATION (OS8COM)	       4-23
	      4.7.1	  Using the OS8COM Task			       4-24
	      4.7.2	  Other Techniques			       4-25
	      4.8	OS/8 FILE SUPPORT TASK			       4-25
	      4.9	UNIVERSAL DIGITAL CONTROLLER/INDUSTRIAL
			CONTROLLER SUBSYSTEM (UDC/ICS) HANDLER	       4-27
	      4.9.1	  AO Analog Output			       4-29
	      4.9.2	  AI Analog Input			       4-29
 	      4.9.3	  DO Digital Output			       4-30
	      4.9.4	  DI Digital Input			       4-31
	      4.9.5	  GC Generic Code			       4-31
	      4.9.6	  EC Enable Counter			       4-31
	      4.9.7	  RC Read Counter			       4-33
	      4.9.8	  DC Disable Counter		  	       4-33
	      4.9.9	  ECT Enable Contacts			       4-33
	      4.9.10	  CS Change of State			       4-34
	      4.9.11	  DCT Disable Contacts			       4-34
	      4.9.12	  UDC/ICS Assembly Parameters		       4-34
	      4.9.13	  UDC/ICS Error Conditions		       4-35
	      4.10 	CASSETTE HANDLER			       4-36
	      4.10.1 	  Handler Function			       4-36
	      4.10.2 	  Utility Function			       4-38
	      4.11 	CASSETTE FILE SUPPORT HANDLER		       4-39
	      4.12	PDP-8A NULL TASK			       4-41
	      4.13	KL8-A SUPPORT				       4-41
	      4.13.1	  Executive KL8-A Support		       4-42
	      4.13.2	  TTY Task KL8-A Support		       4-42
	      4.13.3	  KL8-A Support for the OS/8 Support Task      4-43
	      4.13.4	  KL8-A Support for a User Task		       4-43
	      4.14 	EXIT TASK				       4-44

     CHAPTER  5		MONITOR CONSOLE ROUTINE			       5-1

	      5.1	MCR COMMAND ARGUMENTS			       5-1
	      5.2	MCR COMMANDS				       5-2
	      5.2.1	  DAte [mm/dd/yyyy [,Time-of-day]]	       5-2
	      5.2.2	  TIme [Time-of-day]			       5-2
	      5.2.3	  NAme Task-ID,Newname			       5-2
	      5.2.4	  REquest Task-ID [,(@Time-of-day ! Interval)
			  [,Interval]]				       5-3
	      5.2.5	  STop Task-ID				       5-4
	      5.2.6	  DIsable Task-ID			       5-4
	      5.2.7	  ENable Task-ID			       5-4
	      5.2.8	  CAncel Task-ID			       5-4
	      5.2.9	  SYstat [Task-ID]			       5-5
	      5.2.10	  OPen Address [,Count]			       5-6
	      5.2.11	  EXamine Address [,Count]		       5-6
	      5.2.12	  DEposit Address,Word [,Word] [,Word] 	       5-6
	      5.2.13 	  POst Address				       5-6
	      5.2.14	  EXIT					       5-7
	      5.3	MCR ERRORS				       5-7
	      5.4	NONRESIDENT MCR				       5-7



				      iv

			        CONTENTS (Cont.)

								       Page

     CHAPTER  6	ASSEMBLING AND LOADING TASKS FOR RTS/8		       6-1

	      6.1	PARAMETER FILE STRUCTURE		       6-1
	      6.1.1	Executive Specifications		       6-2
	      6.1.2	  Task Definitions			       6-2
	      6.1.3	  System Task Specifications		       6-3
	      6.1.4	  System Wide Definitions		       6-4
	      6.1.5	  Task Setup				       6-4
	      6.2	CREATING AN RTS/8 SYSTEM		       6-5
	      6.3	USING THE OS/8 BITMAP PROGRAM		       6-8
	      6.4	SAMPLE RTS/8 TASK PROGRAM		       6-8
	      6.5	USE OF CONTROL FILES UNDER RTS/8	       6-10
	      6.6	RTS/8 SYSTEM TASK PARAMETERS		       6-11
	      6.6.1	  Clock Handler Parameters		       6-11
	      6.6.2 	  Swapper Parameters			       6-12
	      6.6.3	  Terminal Handler Parameters		       6-12
	      6.6.4	  Monitor Console Routine Parameters	       6-14
	      6.6.5	  OS/8 Support Task Parameters		       6-14
	      6.6.6	  KL8-A Support Parameters		       6-15
	      6.6.7	  Line Printer Handler Parameters	       6-15
	      6.6.8	  DECtape Handler Parameters		       6-15
	      6.6.9	  EXIT Task				       6-16

     CHAPTER  7		NONRESIDENT TASKS			       7-1

	      7.1	OVERVIEW				       7-1
	      7.1.1	  Writeable Tasks			       7-3
	      7.1.2	  Checkpointable Tasks			       7-3
	      7.1.3	  Interaction Between Tasks		       7-3
	      7.2	MEMORY PARTITIONS			       7-3
	      7.2.1	  FREE Command				       7-4
	      7.3	NONRESIDENT TASK INITIALIZATION		       7-5
	      7.3.1	  Parameters for Nonresident Tasks	       7-6
	      7.3.2	  Assembling Nonresident Tasks		       7-7
	      7.3.3	  Creating the SAVE Image File		       7-7
	      7.4	PARAMETER INITIALIZATION FOR PARTITIONS	       7-8
	      7.4.1	  General Information			       7-8
	      7.5	NONRESIDENT TASK IMPLEMENTATION		       7-8

     CHAPTER  8		DEMONSTRATION PROGRAM			       8-1

	      8.1	MODIFIED PARAMETER FILE (PARAM.PA)	       8-1
	      8.2	NONRESIDENT TASK LISTINGS		       8-12
	      8.2.1	  Nonresident Task NR20			       8-12
	      8.2.2	  Nonresident Task NR22			       8-13
	      8.3	ASSEMBLY AND LOAD PROCEDURE		       8-14
	      8.4	NONRESIDENT TASK ASSIGNMENT AND EXECUTION      8-15

     CHAPTER  9		ADVANCED RTS/8 PROGRAMMING TECHNIQUES	       9-1

	      9.1	PERFORMING A RESCHEDULE			       9-1
	      9.1.1	  Writing Delicate Code			       9-1
	      9.1.2	  Inhibiting Task Switching		       9-2


				       v

				CONTENTS (Cont.)

								       Page

	      9.2	EXECUTIVE REQUESTS FOR ADVANCED APPLICATIONS   9-4
	      9.2.1	  WAITM - Waiting for Multiple Event Flags     9-4
	      9.2.2	  WAITX - Wait for Exactly This Event Flag     9-6
	      9.2.3	  DERAIL - Derail a Task's Execution	       9-6
	      9.2.3.1     Dangers of DERAIL			       9-7
	      9.2.3.2 	  Restrictions Using DERAIL		       9-7
	      9.3 	STARTING PARTITIONS AT AN ARBITRARY BOUNDARY   9-8
	      9.4 	DIRECT REFERENCES TO SYSTEM TABLES	       9-9


     APPENDIX A		RTS/8 DISTRIBUTED SOURCE FILES		       A-1

     APPENDIX B	RTS/8 COMPONENT SIZES				       B-1

     APPENDIX C	RTS/8 FLOWCHARTS				       C-1

     APPENDIX D	RTS/8 ASSEMBLY ERROR MESSAGES			       D-1

     APPENDIX E	EXECUTIVE INTERNAL TASK TABLES			       E-1

     GLOSSARY						        Glossary-1

     INDEX							   Index-1




				    FIGURES

     FIGURE   2-1	Message Format and Linking of Messages	       2-4
	      7-1	Nonresident Task Implementation		       7-2
	      B-1	RTS/8 System Memory Map (Default Memory
			Allocation)				       B-4
	      E-1	Executive Internal Task Table Structure	       E-5




				     TABLES

     TABLE    1-1	RTS/8 System Tasks			       1-2
	      2-1	Summary of Event Flag States		       2-3
	      3-1	Summary of Executive Requests		       3-2
	      3-2	Symbolic Names for Specifying WAITBITS	       3-9
	      3-3	Summary of Wait States Incurred by Executive
			Requests				       3-14
	      4-1	Summary of Terminal Handler Assembly Parameter
			Default Values				       4-10
	      9-1	Summary of Task Switching Flag (TSWFLG) States 9-4
	      B-1	RTS/8 Component Sizes			       B-1
	      B-2	MCR Component Size			       B-6




				      vi







				   PREFACE



     This manual describes the PDP-8 Real-Time  Operating  System  (RTS/8).
     Knowledge  of  PDP-8 assembly language programming (PAL8) is essential
     for a complete understanding of this manual.  In  addition,  the  user
     should  be  familiar  with  real-time  systems in general and with the
     operation and use of the development system for the PDP-8, OS/8.   The
     information  in  Chapter 9, "Advanced RTS/8 Programming Techniques" is
     for the experienced RTS/8 user.  It should be read after the user  has
     gained familiarity with RTS/8.

     This  version  of  the  manual  has  been  enlarged  and  expanded  to
     incorporate  several  new  RTS/8  features. The Major features include
     KL8-A  Support,  PDP-8/A  Null  Task,  the  EXIT  Task,  and  two  new
     Executive Requests.  Other features are the nonresident implementation
     of the MCR, UDC/ICS support, an OS8COM facility that allows  the  OS/8
     system to talk to an RTS/8 task, and control files that allow the user
     to efficiently make multiple task copies.  RTS/8 flowcharts have  been
     added to show system operation.

     The  following  PDP-8  handbooks  will  be  helpful  for  review   and
     reference:

	  INTRODUCTION TO PROGRAMMING (DEC-08-XINPA-A-D)
          SMALL COMPUTER HANDBOOK (90P45)
          OS/8 HANDBOOK (DEC-S8-OSHBA-A-D)
          UDC8 UNIVERSAL DIGITAL CONTROL SUBSYSTEM MAINTENANCE MANUAL 
	  (46H745)
          PDP-8A MINICOMPUTER HANDBOOK (EB0621976)
          ICS8 INDUSTRIAL CONTROL SUBSYSTEM MAINTENANCE MANUAL (EKOICS8MM)





















				      vii






				   CHAPTER 1

				  INTRODUCTION



     1.1  RTS/8 DESCRIPTION

     RTS/8 is a compact real-time system designed for the PDP-8  family  of 
     processors (except the PDP-8/S).  This system allows up to 63 tasks to
     run concurrently and compete for resources on a fixed priority  basis.
     It  can  be used for a wide range of applications in which a number of
     processes must be monitored and controlled.  As with  other  real-time
     systems, RTS/8 responds to physical or conceptual events to permit the
     timely execution and scheduling of tasks.

     The RTS/8 Executive  controls  execution  and  interaction  among  all
     tasks.   The  Executive  decides  which tasks should run (based on the
     priorities of the runnable tasks), and services the tasks by means  of
     Executive Requests (ERs).

     A task is the basic program unit within  RTS/8.   RTS/8  system  tasks
     (DEC-supplied)  and  their  file  names  are listed in Table 1-1.  The
     system supports both resident and nonresident tasks.  A resident  task
     resides  permanently in memory; a nonresident task is one in which the
     major portion of the task resides on a  mass  storage  device  and  is
     loaded  into  memory  only  when  that task becomes executable.  Using
     nonresident tasks permits portions of several tasks to share the  same
     areas of memory, providing economical use of memory.

     RTS/8 includes system tasks that control  most  standard  DIGITAL  I/O
     devices.  A full complement of peripherals is supported, including RK8
     and RK8-E moving-head disks, DF32  and  RF08  fixed-head  disks,  TC08
     DECtape,  RX8  floppy  disk,  LINCtape, DEC cassette, and LEO and LS8E
     line printers (RTS/8 does not  support  TD8E  DECtape).   The  Monitor
     Console  Routine  (MCR) task provides an interface between the user at
     the console terminal and the system.  The MCR provides the user with a
     series of commands to control, inspect, and, to some extent, debug the
     system.  The MCR commands are straightforward and easy to  use.   They
     allow  the  user to schedule and execute tasks at specified intervals,
     suspend task execution, and print system status reports.

     A system task also is provided that allows a single copy of  the  OS/8
     operating  system  to  run  in  the  background,  creating a real-time
     foreground-OS/8 background system.  With OS/8 in the  background,  the
     user  has the facilities for program assembly, debugging, and editing.
     The minimum RTS/8 hardware configuration  required  for  a  foreground
     only  system  is  a  PDP-8 family processor, 4K words of memory, and a
     console terminal capable of papertape  input.   A  system  capable  of
     running  a  real-time foreground and OS/8 in the background requires a
     PDP-8 family  processor  with  KM8-A,  KM8-E  or  TSS-8  Time  Sharing
     options,  a mass storage device (such as an RK8E cartridge disk or RX8
     floppy disk), and two terminals (one must be dedicated to OS/8  system
     execution).

     				      1-1

				 INTRODUCTION
    
 
     RTS/8 tasks are created by editing the RTS/8 master parameter file  to
     produce  a parameter file that describes the user's particular system.
     Task source files are then assembled with the  edited  parameter  file
     using the PAL8 assembler.  The assembler can run either under OS/8, or
     the OS/8 support system under RTS/8.  Then using  ABSLDR  under  OS/8,
     all task binaries are joined into a complete RTS/8 system.


				   Table 1-1
			       RTS/8 System Tasks

     ----------------------------------------------------------------------
     | Task Name    | File Name   |		  Task Function		  |
     ----------------------------------------------------------------------
     | -	    | PARAM.PA	  | System parameter file with		  |
     |		    |             | equates blank. Appropriate		  |
     |		    |		  | values should be inserted to	  |
     |		    |		  | create specific parameter files.	  |
     |		    | RTS8.PA	  | RTS/8 Executive			  |
     | MCR	    | MCR.PA      | Monitor Console Routine		  |
     | null task    | MCR.PA	  | Null task				  |
     | OS8	    | OS8SUP.PA	  | OS/8 Support Task			  |
     | OS8F	    | OS8SUP.PA	  | OS/8 File Support Task		  |
     | PWRF	    | PWRF.PA     | Power Fail Task			  |
     | CLOCK	    | CLOCK.PA	  | Clock Handler Task			  |
     | TTY	    | TTY.PA	  | Terminal Driver Task		  |
     | LPT	    | LPT.PA	  | Line Printer Driver Task		  |
     | DTA	    | DTA.PA	  | TC08 DECtape Driver Task		  |
     | RK8	    | RK8.PA	  | RK8 Disk Driver Task		  |
     | RK8	    | RK8E.PA	  | RK8E Disk Driver Task		  |
     | RF08/DF32    | RF08.PA     | RF08/DF32 Fixed-Head Disk Driver Task |
     | CSA	    | CSA.PA	  | Cassette Driver Task		  |
     | CSAF	    | CSAF.PA	  | Cassette File Support Task		  |
     | UDC/ICS	    | UDCICS.PA	  |Universal Digital Controller/Industrial|
     |		    |		  | Controller Subsystem Handler Task	  |
     | RX8A	    | RX01RT.PA	  | Floppy Disk Handler (1st controller)  |
     | RX8B	    | RX01RT.PA	  | Floppy Disk Handler (2nd controller)  |
     | RX8C	    | RX01RT.PA	  | Floppy Disk Handler (3rd controller)  |
     | RX8D	    | RX01RT.PA	  | Floppy Disk Handler (4th controller)  |
     | LTA	    | LTA.PA	  | LINCtape Driver Task		  |
     | SWAPPER	    | SWAP.PA	  | Nonresident Task swapper		  |
     | NULL8A	    | NULL8A.PA	  | Null Task for PDP-8A		  |
     | EXIT	    | EXIT.PA	  | Exit Task				  |
     |		    |		  |					  |
     ----------------------------------------------------------------------


     1.2  REAL-TIME SYSTEM OPERATION

     A  multiprogramming  system  is  a  software  framework  that   allows
     available resources (such as memory, CPU time, and peripheral devices)
     to be shared by several tasks.  Basically, a  task  is  a  portion  of
     machine  code  that performs a specific function; a task is defined by
     convention since it overlaps with the  definitions  of  "program"  and
     "subroutine."

     				      1-2

				 INTRODUCTION
    

     Multiprogramming allows many tasks to be in some  state  of  execution
     simultaneously.  If a task cannot use available central processor time
     because it is waiting for  completion  of  an  I/O  operation  (or  is
     blocked  by  some  other  condition),  the  central  processor  can be
     switched to another task to use the available  time,  thus  increasing
     system efficiency.
 
     Most real-time systems are required to serve a group of tasks that run
     at  varying  times  or frequencies and alternate between being compute
     bound or I/O bound.  If machine resources are to be efficiently  used,
     these  tasks  cannot be run in series since the central processor will
     be poorly utilized during the periods the tasks  are  I/O  bound.   In
     addition,  most  real-time  tasks  are  essentially  time-critical and
     should not wait for a slow, less important I/O or compute  bound  task
     to  finish  before  being  executed.   Thus,  multiprogramming  and  a
     priority scheme for scheduling the central processor  provide  maximum
     resource utilization.

     Thus, a real-time system is a multiprogramming system  that  must,  in
     addition to the multiprogramming features, respond quickly to critical
     internal or external events.  The  real-time  system  is  required  to
     suspend the operation of a less important task and start the task that
     deals with the critical event.

     A priority scheme establishes the relative importance of various tasks
     in the system.  This allows a less important task to be interrupted to
     permit execution of a critical real-time task.   For  RTS/8,  a  fixed
     priority  scheme  was  chosen  because  such  a  scheme  is simple and
     reliable, and requires low scheduling overhead.



























				      1-3






				   CHAPTER 2

			    USING TASKS UNDER RTS/8



     2.1  THE STRUCTURE OF RTS/8 TASKS
     
     The RTS/8 Executive is the controlling program  in  an  RTS/8  System.  
     The Executive decides which task should run based on the priorities of 
     the runnable tasks (those tasks not waiting for completion of any  I/O 
     or  other events).  It also provides services to the tasks by means of
     Executive Requests.  Executive Requests are discussed in Chapter 3. 
     
     The user assigns unique task numbers to each task in an RTS/8  System.
     He  can  assign up to 63 (77 octal) task numbers, and must account for
     system tasks within the total number of tasks.  A  task  number,  once
     assigned,  cannot  change  during  the execution of the program, since
     RTS/8 uses a fixed priority system.  Task numbers serve the  following
     purposes: 
     
	  1.  The task number is used by the RTS/8 Executive as an index to
     	      various  system  tables  which contain information about each 
	      task. 
     
          2.  The task number is used by  other  tasks  in  the  system  to 
	      reference a particular task when performing certain Executive 
	      Requests (such as sending a message). 
     
          3.  The task number determines the  task's  priority - the  lower 
	      the task number, the higher the priority of the task. 
     
     The Executive uses five internal tables to maintain information  about
     the tasks in the system.  A brief description of these tables is given
     in Section 2.3. 


     2.2  CONCEPTS OF TASK COMMUNICATION

     RTS/8 is event  driven,  i.e.,  the  highest  priority  runnable  task
     executes continuously until it is completed or some event or condition
     in the system causes it to be suspended.  Another change or  condition
     can  reactivate  the task.  Tasks can be self-starting if assembled to
     run at system startup, started by another task, or started by the user
     at  the  terminal console using the MCR task.  RTS/8 performs two main
     types of task communication, as follows: 

          1.  Task synchronization through the use of Event Flags

 	  2.  Intertask messages





				      2-1

			    USING TASKS UNDER RTS/8


     2.2.1  Task Synchronization Through the Use of Event Flags

     Whenever two processes occur independently, one process  may  need  to
     wait  until  the  execution  of  the  other  is finished.  This can be
     illustrated  by using the PDP-8 terminal interface as an example.  The
     PDP-8, when ready to generate the first character, alerts the terminal
     by  issuing  a Load Teleprinter Sequence (TLS) instruction.  The PDP-8
     must now wait in a TSF; JMP.-l loop if it wishes  to  do  further  I/O
     immediately.   It  cannot  proceed  with  the next character until the
     terminal raises its ready flag to signal that it is finished  printing
     the  first  character.   When the flag is raised, the PDP-8 then exits
     from the wait loop and proceeds to load the next character.

     Similarly, RTS/8 provides Event Flags as  a  signalling  mechanism  to
     synchronize  tasks  with  each  other.  An Event Flag is a user-chosen
     location that contains the status of an event.  The events are  either
     l)  physical  processes such as a clock ticking or a valve closing, or
     2) conceptual occurrences such as a certain string of characters typed
     by  the  operator  or  scheduling  a  task for execution.  Like device
     flags, an Event Flag can signify either a busy or a  completed  state,
     defined as PENDING (>0) and FINISHED (=0), respectively.  Thus, a task
     can direct another task via a message to perform a  specified  action,
     at which time it sets a mutually-agreed upon Event Flag to the PENDING
     value.  When the second task has completed  the  specified  action  it
     sets  the  Event  Flag to the FINISHED value; this is known as Posting
     the Event Flag.  As a simple example,  if  the  first  task  has  been
     waiting for the Event Flag with the instructions:

	  TAD Event Flag  /LOAD EVENT FLAG IN AC
	  SZA CLA 	  /IF EVENT FINISHED, SKIP
	  JMP .-2 	  /KEEP TRYING

     then the Posting of the Event Flag will cause the first task  to  exit
     from  its  loop, continuing on with the knowledge that the second task
     has completed its processing.

     Since this loop ties up the PDP-8 processor, Event Flags  under  RTS/8
     have an additional state, WAITING (<0).  Using the example just cited,
     the addition of the WAITING state now allows the first  task  to  tell
     the  RTS/8  Executive  that  it  wants  to  WAIT  until the Event Flag
     signifying the status of the second task  is  FINISHED.   The  monitor
     saves  the  contents  of the waiting task's PC and sets the Event Flag
     Wait bit in its Task Flags Table Word.  The Event Flag is set  to  the
     WAITING state.  The WAITING state for an Event Flag is octal 4000 plus
     the waiting task's Task Number.  When the Event Flag is POSTed via  an
     RTS/8 Executive Request call, the task WAITING for it is automatically
     taken out of Event Flag Wait by RTS/8.  (If no other blocking bits are
     set,  the  waiting  task  is again runnable, and will resume execution
     when higher priority tasks are blocked.) WAITE is the mnemonic for the
     RTS/8 Executive Request that Waits for an Event Flag.

     This code would look as follows:

	  CAL
	  WAITE
	  event flag
				      2-2

			    USING TASKS UNDER RTS/8


     All Executive Requests are described fully in Chapter 3.  A summary of
     Event Flag states is shown in Table 2-1.


				Table 2-1
			Summary of Event Flag States

	      -------------------------------------------------
	      |  Event Flag State     |		Value	      |
	      |-----------------------|-----------------------|
	      |			      |			      |
	      | FINISHED (posted)     |  0		      |
	      | PENDING		      |  >0		      |
	      | WAITING		      |  <0 (4000 + Task No.) |
	      |			      |			      |
	      -------------------------------------------------


     2.2.2  Intertask Messages

     Just as Event Flags under  RTS/8  are  analogous  to  hardware  device
     flags,   messages   are   analogous   to   data-sending  hardware  I/O
     instructions (for example, TLS).  That  is,  messages  start  a  task,
     providing  the  task  is  WAITING for a message, and at the same time,
     they pass information  to  the  task.   Messages  are  transmitted  by
     Executive Requests.
     
     An RTS/8 message consists of a three-word Message Header  followed  by
     any  number of contiguous words of information to be exchanged between
     two tasks.  The Message Header is  used  exclusively  by  RTS/8.   The
     first  word  of  the Message Header is the Event Flag for the message.
     When the message is sent, the RTS/8 Executive sets the Event  Flag  to
     the  PENDING state.  This signifies that the message has been sent but
     not yet completed.  No action occurs to the Event Flag upon receipt of
     the  message  by  the receiving task; however, RTS/8 requires that the
     receiver POSTs the  Event  Flag  when  it  has  performed  the  action
     specified  (or  implied)  by  the  message.   This  posting serves two
     purposes:
     
          1.  It informs the task which sent  the  message  (the  "sender")
     	      that the requested action has been completed, and
     
          2.  It allows the message to be sent again (see Item 2 below).
     
     If multiple messages are waiting to be received by a task, RTS/8  uses
     the  second  and  third  words  of  the  Message  Header to link these
     messages together (see Figure 2-1).  The second word is a CDF  (Change
     Data  Field)  instruction to the field of the next message.  The third
     word is the address of the next message.  A second word of 0 signifies
     that  this is the last message.  If the receiving task is not actively
     waiting for a message, the message is placed on the  receiving  task's
     Input  Message Queue.  Messages are then queued in order of decreasing
     priority of the sender (increasing task number).  Messages  sent  from
     the same task are queued in the order in which they were issued.

     
				      2-3

			    USING TASKS UNDER RTS/8


       RTS/8 
     EXECUTIVE
      MSGTBL	     MESSAGE 1	      MESSAGE 2	      MESSAGE 3
     ---------     ------------     ------------     ------------ <----
     |  CDF  |  /->|Event Flag|  /->|Event Flag|  /->|Event Flag|     |
     ---------  |  ------------  |  ------------  |  ------------     |
     |  PTR  |__|  |   CDF    |  |  |   CDF    |  |  |    0     |   Message
     ---------     ------------  |  ------------  |  ------------   Header
    		   |   PTR    |__|  |   PTR    |__|  |		|     |
		   ------------     ------------     |----------| <----
		   |          |     |          |     |          |     |
		   |          |     |          |     |          |     |
		   |          |     |          |     |          |   Message
		   |          |     |          |     |          |   Content
		   |          |     |          |     |          |     |
		   ------------     |	       |     |		|     |
				    |	       |     ------------ <----
				    |          |
				    |          |
				    ------------


	Figure 2-1 Message Format and Linking of Messages


     The rest of the message can contain any desired information.   Sending
     a  message  does  not  physically  move the message information to the
     receiving task, but provides the receiver with the field  and  address
     of the first data word of the message.
     
     It should be noted that the information in a  message  is  not  copied
     into the receiver's area.  This has the following implications:
     
	  1.  Data in a message should not be modified by the sender  while
	      the Event Flag for the message is PENDING.
     
	  2.  The same message cannot be sent  a  second  time  before  its
	      Event  Flag  is FINISHED the first time.  RTS/8 enforces this
	      by checking the message Event Flag on a  SEND  operation  and
	      putting  the  sender  into  Event Flag Wait if the message is
	      still PENDING.
     
	  3.  It is legal for the receiving task to  store  information  in
	      the  body  of  the  message.  In this way, an "answer" to the
	      message can be returned without the complications of  sending
	      a  return  message  back  to the sender.  For example, when a
	      task sends a message to the disk driver task requesting  I/O,
	      the driver places the error status of the completed operation
	      in a specific word in the  message  to  indicate  whether  an
	      error occurred.






				      2-4

			    USING TASKS UNDER RTS/8

 
     2.3  EXECUTIVE INTERNAL TASK TABLES
     
     The Executive uses five internal tables to maintain information  about
     the  tasks  in  the system.  A brief description of these tables is as
     follows:
     

	      Table				Description

     Task State Table (TSTABL)	   Contains   information   such   as   the
				   contents  of  the task's PC, Link and AC
				   at the time the task stopped running.

     Task Flags Table (TFTABL)	   Contains information about why the  task
				   is  not  running, i.e., it indicates for
				   what conditions (blocking or wait  bits)
				   the task is waiting.

     Task Input Message Queue	   Contains messages that  have  been  sent
     Header Table (MSGTBL)	   to  this task. This table is referred to
				   simply as the Message Table.

     Residency Table (RESTBL)	   Used for nonresident tasks,  this  table
				   specifies where the task is to reside in
				   memory, and where it resides on the swap
				   device.

     Partition Table (PARTBL)	   Used for nonresident tasks,  this  table
				   contains  information  about each memory
				   partition, such as length  and  location
				   of  the partition. Memory partitions are
				   shared by nonresident tasks.


     The user does not need to know the  format  of  these  tables  to  use
     RTS/8.   However,  a  detailed explanation of these tables is given in
     Appendix E.
     


















				      2-5






				   CHAPTER 3

			   RTS/8 EXECUTIVE REQUESTS



     3.1  COMMUNICATION WITH THE RTS/8 EXECUTIVE
     
     RTS/8  tasks  communicate  with  the  RTS/8  Executive  via  Executive
     Requests  (ERs).   RTS/8  uses  locations  20-27  in  every field as a
     communication region for ERs to facilitate Executive  Requests  across
     field  boundaries.  The Executive can be called in any field via a JMS
     20 instruction (designated symbolically as CAL).  The Data Field  (DF)
     does  not  have  to be any specific value when the CAL is given, since
     the code in location 20 sets the DF to  the  Instruction  Field  (IF),
     sets the IF to 0 and jumps to the RTS/8 Executive.
     
     A summary of Executive Requests is given in Table 3-1.   Most  of  the
     Executive  Requests  are  explained  in  detail  in this chapter.  The
     RESCHD, WAITX and DERAIL Executive Requests are described  in  Chapter
     9.
     
     The RTS/8 Executive will not honor any request to switch tasks arising
     from  an  interrupt if the interrupted task's Program Counter (PC) was
     less than 100(octal).  This protects the RTS/8 Executive's entry point
     (location  20 in each field) from being destroyed.  User tasks must be
     written so that instructions are  never  executed  below  100  in  any
     field.
     
     All ER's except DERAIL and SKPINS can relinquish processor control  to
     higher-priority tasks as a result of their action.

     
     3.2  ERs USED TO COMMUNICATE BETWEEN TASKS
     
     The five ERs associated with the  Intertask  Messages  and  the  Event
     Flags  are  SEND, WAITE, SENDW, RECEIVE and POST.  An example of their
     use is shown in Section 3.2.6.  In addition, a sixth ER  called  WAITX
     is  described  in  Chapter 9, Advanced Programming Techniques (Section
     9.2.2).















				      3-1

			   RTS/8 EXECUTIVE REQUESTS


				   Table 3-1
			 Summary of Executive Requests

     ----------------------------------------------------------------------
     |Code| Symbolic |	Description		        |Section Reference|
     |    |   Name   |					|		  |
     |----|----------|----------------------------------|-----------------|
     |    |	     |					|		  |
     | 0  | SEND     | Send a message to a task		|	3.2.1	  |
     |    |	     |					|		  |
     | 1  | RECEIVE  | Look for and/or receive a	|	3.2.4	  |
     |    |	     | message from a task		|		  |
     |    |	     |					|		  |
     | 2  | WAITE    | Wait for an Event Flag to be	|	3.2.2	  |
     |    |	     | posted				|		  |
     |    |	     |					|		  |
     | 3  |	     | RUN Run a task			|      	3.3.4	  |
     |    |	     |					|		  |
     | 4  | SUSPND   | Suspend execution of a task	|	3.3.3	  |
     |    |	     |					|		  |
     | 5  | POST     | Post an Event Flag		|	3.2.5	  |
     |    |	     |					|		  |
     | 6  | SKPINS   | Insert code into interrupt	|	3.4	  |
     |    |	     | skip chain			|		  |
     |    |	     |					|		  |
     | 7  | DERAIL   | Derail or force a task's		|	9.2.3	  |
     |    |	     | execution to a new address	|		  |
     |    |	     |					|		  |
     | 10 | BLKARG   | Block a task from running for	|	3.3.1	  |
     |    |	     | a specific reason		|		  |
     |    |	     |					|		  |
     | 11 | SENDW    | Send a message and wait for	|	3.2.3	  |
     |    |	     | it to be received		|		  |
     |    |	     |					|		  |
     | 12 | UNBARG   | Remove a reason that a task	|	3.3.2	  |
     |    |	     | is blocked from running		|		  |
     | 13 | RESCHD   | Force the RTS/8 Scheduler to run	|       9.1.2     |
     |    |	     |					|		  |
     | 14 | WAITX    | Wait for a particular Event	|	9.2.2	  |
     |    |	     | Flag to be posted		|		  |
     ----------------------------------------------------------------------


     3.2.1  SEND - Send Message
     
	  Format:  CAL
		   SEND
		   TSKNUM
		   MESSAG

     The SEND ER sends the message located at MESSAG in the  field  of  the
     CAL  instruction to the task whose number is TSKNUM.  If the receiving
     task has a higher priority  than  the  sender  and  is  waiting for  a
     message,  the  sender  is temporarily suspended and the receiver runs.
     In this case, the sender is not put  into  any  WAIT  state  once  the
     
				      3-2

			   RTS/8 EXECUTIVE REQUESTS


     message  is  sent.   However,  if the Event Flag in location MESSAG is
     PENDING (nonzero), meaning the message is still busy from  a  previous
     SEND,  the sender will be put into Event Flag Wait on location MESSAG,
     and only when the Event Flag becomes FINISHED (zero) will this SEND be
     performed.   Care should be taken that a message is sent from only one
     task as only the last request to send a busy  message  is  remembered;
     the first task can go to sleep in Event Wait permanently.
     

     3.2.2  WAITE - Wait on Event Flag

	  Format:  CAL
		   WAITE
		   EFLG

     The WAITE ER checks the status of location EFLG and if it is FINISHED,
     returns  control  to  the  caller.   If  EFLG is PENDING, its state is
     changed to WAITING and the calling task is put into Event  Flag  Wait.
     When location EFLG is POSTed by another task or interrupt routine, the
     calling  task  becomes  runnable  again.   The  Event  Flag  must   be
     initialized  (set  to 1) before use in most cases, particularly when a
     task is initiating an event to be  completed  by  another  task.   The
     waiting  task  must reset the Event Flag before using it again in that
     the Event Flag does not reset itself.
     

				     NOTE

		    In advanced applications, the  user  may
		    be waiting for multiple Event Flags (see
		    Section 9.2.1 for description of WAITM).
		    In  this case the task will run whenever
		    any one of the Event  Flags  is  posted,
		    and not necessarily the one specified in
		    the WAITE.  To insure that a  particular
		    Event  Flag  is posted, use the WAITX ER
		    described in Section 9.2.2.
     
     
     3.2.3  SENDW - Send and Wait

	  Format:  CAL
		   SENDW
		   TSKNUM
		   MESSAG

     The SENDW ER is exactly equivalent to the sequence:

		   CAL
		   SEND	     /SEND THE MESSAGE
		   TSKNUM
		   MESSAG
		   CAL
		   WAITE     /WAIT FOR RECEIVER TO ACKNOWLEDGE
		   MESSAG
     
				      3-3

			   RTS/8 EXECUTIVE REQUESTS
     

     3.2.4  RECEIVE - Receive Message

	  Format:  	      TAD TSKNUM	  /ONLY TO RESTRICT TO ONE
		     	      CAL		  /SENDING TASK
			      RECEIVE
		     MADDR,   0			  /MESSAGE ADDRESS STORED
						  /HERE; CDF TO MESSAGE
						  /FIELD IN AC ON RETURN

     If the AC is zero when the RECEIVE ER is issued,  the  calling  task's
     Input Message Queue is examined.  If there are messages in the calling
     task's Input Message Queue, the first (i.e., highest-priority) message
     is dequeued and the address of its first data word is placed in MADDR.
     A CDF to the field of the message is stored in the AC.

     If there are no messages, the task is placed  in  Message  Wait  until
     such  time  as  a  message  is sent to this task.  However, a task may
     first examine its Input Message Queue Header in field 0  to  determine
     the state of the Input Message Queue.

     If the AC is nonzero when the RECEIVE ER is issued, the calling task's
     Input  Message  Queue  is  searched  for a message whose sender's Task
     Number matches the contents of bits 1-11 of the AC.  If such a message
     is  found,  it  is  removed  from  the  queue as specified above; if a
     message is not found, the issuing task  is  placed  in  Message  Wait.
     This allows a message from only one given task to be received.
     

				     NOTE

		    The following information is  useful  to
		    the  advanced  user.   When a task is in
		    MSGWT, after just having done a RECEIVE,
		    its  PC  as  stored in the TSTABL points
		    back to the location containing the CAL.
		    Thus,  when a message comes in, the task
		    re-executes the RECEIVE ER  and  accepts
		    the message.  This mechanism is normally
		    transparent    to    the    user.    One
		    implication is that no harm is caused by
		    taking  a task out of MSGWT because once
		    the  task  starts  up  again,  it   will
		    re-execute  the  RECEIVE ER, and go back
		    into MSGWT.


     Normally, if there are no messages in the Input Message Queue  when  a
     task  performs a RECEIVE, the task is put into Message Wait.  However,
     a 1 in bit 0 of the AC (i.e., the AC is negative) when the RECEIVE  is
     issued  indicates that the task is not willing to wait.  Thus, with no
     messages in the  Input  Message  Queue  (or  none  sent  by  the  task
     specified  in bits 1-11 of the AC), the task will then continue to run
     (at CAL +3) with the AC equal to zero.  The zero AC provides the means
     for the RTS/8 Executive to inform the task that there were no messages
     (of the desired type) pending.

				      3-4

			   RTS/8 EXECUTIVE REQUESTS


     3.2.5  POST - Post Event Flag

     	  Format: 	      TAD EFPTR		  /POINTER TO EVENT FLAG
			      CAL
			      POST
			      CDF EFFLD		  /FIELD OF EVENT FLAG

     The Event Flag pointed to by the AC, in the  field  specified  by  the
     CDF, is  set  to the FINISHED (zero) state.  If its previous state was
     WAITING, the task that was waiting for it is cleared of its Event Flag
     Wait.   This  ER  never sets the calling task in a WAIT state.  If the
     task waiting for the Event Flag is  of  a  higher  priority  than  the
     calling  task,  the  calling  task  is temporarily suspended while the
     other is run.


     3.2.6  Example of ERs for Message and Event Flags

     The following example illustrates the RTS/8 ERs dealing with  Messages
     and  Event  Flags.  Since I/O and interrupts under RTS/8 have not been
     discussed yet, this example is elementary.  There is no  advantage  to
     keeping  the  functions  of  the  two  tasks  separate, and the entire
     send/receive structure is being used here as an  elaborate  subroutine
     call.  A description of the execution sequence follows the example.

				     Task A

     A1	       ALOOP,	      CAL
			      SEND	     /SEND TASK B MESSAGE 1
     			      B
     			      MES1
     A2			      CAL
     			      SEND	     /SEND TASK B MESSAGE 2
     			      B
     			      MES2
     A3			      CAL
     			      WAITE	     /WAIT FOR MESSAGE 1
     			      MES1
     A4			      JMP ALOOP      /LOOP
     	       MES1,	      ZBLOCK 3       /MESSAGE 1
     			      15	     /RANDOM NUMBERS
     			      37
     			      23

     	       MES2,	      ZBLOCK 3       /MESSAGE 2
     			      -1	     /RANDOM NUMBERS
     			      4









				      3-5

			   RTS/8 EXECUTIVE REQUESTS


     				     Task B

     B1	       BLOOP,	      CAL
     			      RECEIVE		  /GET A MESSAGE
	       MADDR,	      0
     B2			      DCA EFCDF		  /SAVE MESSAGE CDF FOR POST
     B3			      TAD EFCDF
     B4			      DCA .+1		  /PUT CDF INLINE
     B5			      HLT		  /CDF TO MESSAGE FIELD
     B6			      TAD I MADDR  	  /GET 1ST DATA WORD OF
     						  /MESSAGE (DO NOTHING WITH IT)
     B7			      CLA
     B8			      STA CLL RTL	  /-3 IN AC
     B9			      TAD MADDR		  /AC POINTS TO MESSAGE
     						  /EVENT FLAG
     B10		      CAL
     			      POST		  /DECLARE MESSAGE RECEIVED
     	       EFCDF,	      HLT		  /CDF TO MESSAGE FIELD HERE
     Bll		      JMP BLOOP		  /LOOP

     The flow of execution in this example depends  on  which  of  the  two
     tasks  has  higher  priority.  Assuming that at some time both A and B
     become runnable and task  A  has  higher  priority,  the  sequence  of
     execution is as follows:

     	  Sequence			   Reason For Execution
 
     	       A1 	      Task A has higher priority than task B.
     	       A2 	      Task A has higher priority than task B.
     	       A3 	      Task A has higher priority than task B.
     	       B1 	      Task A is now in Event Flag Wait  since  MES1
     			      was PENDING;  MES1 is now in WAITING state.

     	  Sequence			   Reason For Execution
    
	       B2-B10	      Task A is still waiting; the  RECEIVE  at  B1
     			      received MES1
	       A4	      The POST at B10 posted MES1 and "woke up"  A,
     			      which has higher priority than B.
	       A1	      A continues executing.
	       A2	      A tries to send MES2 again;  B  has  not  yet
     			      processed it; MES2 is PENDING.
	       Bll	      Therefore, A is put into Event Flag Wait  and
     			      B is resumed; MES2 is now WAITING.
	       Bl-B10	      B now RECEIVes and POSTs MES2.
	       A2	      This brings A out of  Event  Flag  Wait;  the
     			      RTS/8 Executive has modified task A's program
     			      counter  so  that  it  will  re-execute   the
     			      offending SEND.
	       A3	      A3 now waits for MES1 to be POSTed.

     If task B has higher priority, the sequence of execution is:



     
				      3-6

			   RTS/8 EXECUTIVE REQUESTS


     	  Sequence			   Reason For Execution

	       B1	      Task B has higher priority than task A.
	       A1	      Task B is placed in Message Wait since  there
     			      are  no  messages in its input queue.  Task A
     			      then sends MES1 to Task B.
	       B2-B10	      Task A's message brings task B out of Message
     			      Wait;  since  B  has  higher  priority,  A is
     			      stopped and B runs.
	       Bll	      The POST at B10 sets MES1 to FINISHED but has
     			      no other effect.
	       B1	      Now task B tries to get another message.
	       A2	      There are no other messages, so task B is put
     			      in Message Wait and A is run.
	       B2-Bll	      Task A sends  MES2  which  "wakes  up"  B;  B
     			      processes MES2 and
	       B1	      returns for more,
	       A3	      and is put in Message Wait.   Since  MES1  is
     			      FINISHED
	       A4	      the WAITE at A3 has no effect and task A
	       A1	      loops back to A1 and sends MES1 again.


     
     3.3  ERs USED TO SET AND CLEAR TASK FLAGS

     Several ERs allow a task to explicitly set and clear flags in the Task
     Flags  Table  entry of another task, and to set flags in its own table
     entry.  These ERs are BLKARG, UNBARG, SUSPND and RUN.


     
     3.3.1  BLKARG - Block Task for Specified Reason

	  Format:   TAD TASKNUM    /OR 0 IF SELF
		    CAL
		    BLKARG
		    WAITBITS

     TASKNUM contains the number of the task to be blocked  (that  is,  not
     allowed  to  run).   WAITBITS  specifies one or more bits to be set in
     that task's Task Flags word.  Assuming WAITBITS is nonzero, this  will
     cause  the specified task to become non-runnable.  If TASKNUM contains
     zero, the issuing task will be blocked on the specified wait bits.

     The TASKNUM=0 form of this ER is the only legal  way  to  specify  the
     issuing  task  as  the  task to be blocked; if TASKNUM is equal to the
     issuing task number, the action of this ER is undefined.

     Example:






				      3-7

			   RTS/8 EXECUTIVE REQUESTS


     Task 14 is placed into User Wait by executing the following code.

	  TAD (14
	  CAL
	  BLKARG
	  USERWT

     Symbolic names for specifying the condition for blocking or unblocking
     a task in the WAITBITS word is given in Table 3-2.
     

     3.3.2  UNBARG - Unblock Task for Specified Reason

	  Format: TAD TASKNUM
		  CAL
		  UNBARG
		  WAITBITS

     TASKNUM contains the number of  the  task  to  unblock,  and  WAITBITS
     specifies  one  or  more  bits to be cleared in that task's Task Flags
     word.  If the Task Flags  word  becomes  zero  as  a  result  of  this
     operation,  the specified task becomes runnable; if the specified task
     has higher priority than the issuing task and  becomes  runnable,  the
     issuing task  is  temporarily suspended while the higher-priority task
     runs.

     This ER is a no-op (no operation) if issued with TASKNUM equal to  the
     issuing task's number.

     Example:

     Task 14 is taken out of User Wait by executing the following code.

	  TAD (14
	  CAL
	  UNBARG
	  USERWT
     
     
     3.3.3  SUSPND - Suspend a Task's Execution

	  Format:   TAD TASKNUM /0 IF SELF
		    CAL
		    SUSPND

     This SUSPND ER is identical in action to the following instructions:

		    TAD TASKNUM
		    CAL
		    BLKARG
		    RUNWT





				      3-8

			   RTS/8 EXECUTIVE REQUESTS


     				   Table 3-2
		     Symbolic Names for Specifying WAITBITS
     
     -----------------------------------------------------------------------
     |Symbolic Name| Value |			  Meaning		   |
     |-------------|-------|-----------------------------------------------|
     |     	   |	   |						   |
     | NONRWT	   |  4000 | Nonresident  Wait - This   task   cannot   run|
     |    	   |	   | because it is not in memory.		   |
     |     	   |	   |						   |
     | EFWT	   |  2000 | Event Flag Wait - This task is waiting for  an|
     |		   |	   | Event  Flag  (which  contains  a WAITING value|
     |		   |	   | corresponding to this task) to be POSTed.	   |
     |     	   |	   |						   |
     | RUNWT	   |  1000 | Run Wait - This task is waiting for a  RUN  ER|
     |		   |	   | to  be  executed with its number in the AC, or|
     |     	   |	   | for the operator to  type  "REQUEST  task"  to|
     |	 	   |       | the Monitor Console Routine (see Chapter 5).  |
     |     	   |	   |						   |
     | SWPWT	   |  0400 | Swap Wait - This task cannot run because it is|
     |		   |	   | in the process of being brought into memory.  |
     |     	   |	   |						   |
     | EORMWT	   |  0200 | Event or Message Wait - This task  is  waiting|
     |             |	   | for an Event Flag to be posted or a message to|
     |     	   |	   | arrive, whichever happens first.		   |
     |     	   |	   |						   |
     | USERWT	   |  0100 | User Wait - This bit is reserved  for  use  by|
     |     	   |	   | user-written  tasks.   RTS/8 does not use this|
     |		   |       | bit.					   |
     |     	   |	   |						   |
     | ENABWT	   |  0040 | Enable  Wait - This  task  is  waiting  to  be|
     |     	   |	   | Enabled.  Use of this bit is restricted to the|
     |     	   |	   | Monitor Console Routine for the "ENABLE  task"|
     |     	   |	   | and "DISABLE task" commands (see Chapter 5).  |
     |     	   |	   |						   |
     | MSGWT	   |  0020 | Message Wait - This task is waiting to be sent|
     |     	   |	   | a message.					   |
     |     	   |	   |						   |
     | DNEWT	   |  0001 | Task does not exist.  This bit should never be|
     |		   |	   | set or cleared by a user task.		   |
     -----------------------------------------------------------------------

     
     3.3.4  RUN - Run a Task

		    Format: TAD TASKNUM
		    CAL
		    RUN

     This RUN ER is identical in action to the following instructions:

		    TAD TASKNUM
		    CAL
		    UNBARG
		    RUNWT

				      3-9

			   RTS/8 EXECUTIVE REQUESTS


     The SUSPND and RUN ERs exist because their function is performed often
     enough to warrant a shorthand version.  An example that shows how they
     can be used in a task follows.

     A data collection task is to print a report  every  1000  data  points
     without  interrupting  the  data  collection/reduction  process.  When
     executed, the Report Generation Task comes up running, so that the
     
     first report occurs on the first data.  In  this  simplified  example,
     the  data  operated  on  by  the  report program may have been already
     updated for the next cycle before  being  reported.   A  full  example
     would require a scheme such as double buffering to protect the data.

     			       Data Control Task

	       DLOOP,	 TAD (-1750	/1000 DECIMAL
			 DCA COUNT
	       DATALP,   CAL
			 WAITE
			 DATAEF		/WAIT FOR DATA READY
			 .		/CODE TO STORE DATA
			 .		/POINT IN BUFFER
			 .
			 .		/GET A DATA POINT
			 ISZ COUNT	/AND PROCESS IT
			 JMP DATALP	/COUNT OFF 1000 POINTS
			 TAD (REPORT
			 CAL		/RUN REPORT TASK
			 RUN
			 JMP DLOOP	/KEEP COLLECTING
	       COUNT, 0

				Report Generation Task

	       RLOOP,	 CAL 		/AC=0, SUSPEND
			 SUSPND 	/UNTIL NEEDED
			 JMS TITLE 	/HAS BEEN RUN
			 .
			 .		/PRINT REPORT
			 . 		/WITH TITLE
			 .     
     			 .
			 JMP RLOOP 	/REPORT OVER-GO
					/BACK AND WAIT

     To eliminate interference with the data collection, REPORT should have
     a lower priority than DATA.
     
     
     3.4  USING INTERRUPTS IN RTS/8

     The RTS/8 Executive contains code  to  receive  and  dismiss  hardware
     interrupts  and  to perform interrupt-initiated task switching, but it
     does not provide room for an interrupt skip chain.  Instead, the  skip
     chain  is  literally  a  chain  and  is built up dynamically at system
     
				      3-10

			   RTS/8 EXECUTIVE REQUESTS


     startup time via the SKPINS ER.  A description of the SKPINS ER is  as
     follows.

	  Format:   CAL
		    SKPINS
		    MODULE

     MODULE  is  the  address  (in  the  current  field)  of  an  interrupt
     processing module.
     
     An interrupt processing module has the following format:

	  MODULE, 0		      /THIS WORD GETS A POINTER
				      /TO THE NEXT MODULE
		  0		      /MODULE ENTERED HERE - CONTAINS
				      /CDF CIF TO NEXT MODULE FIELD
		  SKDR		      /SKIP ON DEVICE READY
		  (SKP)		      /(ONLY IF SKDR REALLY MEANS SKIP
				      /ON DEVICE NOT READY)
		  JMP I MODULE	      /NOT READY - GO TO NEXT MODULE IN
				      /CHAIN
		  CDF CIF CUR	      /THIS ONE IS MINE - SET DF AND IF
				      /CORRECTLY
		  .		      /INTERRUPT PROCESSING
		  .
		  .
		  CIF 0		      /DISMISS THE INTERRUPT, MAYBE POST
		  POSTDS	      /AN EVENT FLAG DEPENDING UPON
				      /CONTENTS OF AC

     See item 7 below for the definition of the POSTDS instruction.

     Whenever a task executes a SKPINS ER, the interrupt chain is broken at
     the  very  end  and  the user's interrupt module is inserted.  This is
     usually done  by  tasks  at  system  start-up  time  only.   The  last
     interrupt  module points to the interrupt dismiss routine as its "next
     module".  In this way, RTS/8 tries to  avoid  superfluous  interrupts.
     SKPINS always inserts at the end of the skip chain.  This implies that
     the skips in the skip chain are ordered roughly  by  priority  of  the
     task  which  inserted them, since any SKPINS ERs in a task are usually
     executed as once-only code at system start-up time.

     Once  an  interrupt  module  receives  control  (i.e.,  its  I/O  skip
     succeeds), there are several restrictions on its execution:

	  1.  The interrupt module must clear the interrupt request.

	  2.  The Data Field and Instruction Field are those  of  the  next
	      interrupt  module;   the  user must correct this as described
	      above before any indirect addressing or jumps are performed.

	  3.  An interrupt module may not issue any RTS/8 ERs.

	  4.  An interrupt  module  should  not  compute  excessively  when
	      interrupts  are  off.  Typical execution time should be under

				     3-11

			   RTS/8 EXECUTIVE REQUESTS


	      75us.  If considerably more computing than this is needed,  a
	      task  should  be  scheduled to perform it by POSTing an Event
	      Flaq.  A POSTDS instruction is used to wake up the task  from
	      Event Wait.

	  5.  Interrupt modules must not turn  interrupts  on  because  the
	      state  of  the interrupted task will be destroyed by a second
	      interrupt.

	  6.  On entry to the interrupt module, the  contents  of  the  AC,
	      Link,  and  Data  Field  have already been saved, but not the
	      contents  of  the  Multiplier  Quotient   (MQ).    Therefore,
	      interrupt modules requiring the use of the MQ should save it,
	      and then restore it before dismissing the interrupt.

	  7.  Interrupt modules must dismiss the interrupt by  setting  the
	      Instruction  Field  to  0  and  issuing a POSTDS instruction.
	      POSTDS is defined as a JMP I 24 instruction.  An  Event  Flag
	      may  be POSTed when the interrupt is dismissed by setting the
     
	      Data Field to the field of the Event  Flag  and  placing  the
	      location  of  the  Event  Flag in the AC prior to issuing the
	      POSTDS. For example:

		   CDF CUR 	    /DF = THIS FIELD
		   TAD (EVFLG 	    /EVFLG MAY NOT BE AT LOCATION 0
		   CIF 0
		   POSTDS 	    /DISMISS INTERRUPT AND POST EVFLG

	      If an Event Flag is not going to be posted by  the  interrupt
	      routine,  the  AC must be cleared prior to issuing the POSTDS
	      instruction.

     For example, an RTS/8 Paper Tape Punch handler task might contain  the
     following sections of code:

     In the initialization code (contained in a task that  is  runnable  at
     system start-up time):

	  START,  CAL		   /LINK THE PUNCH SKIP
		  SKPINS	   /INTO THE SKIP CHAIN
		  PTPINT
	  GETREQ, CAL
		  RECEIVE	   /WAIT FOR MESSAGE
		  .
		  .
		  .

     As a character punch subroutine used by the main body of the task:






     
				     3-12

			   RTS/8 EXECUTIVE REQUESTS


	  PUNCH,  0		   /ENTER WITH CHAR IN AC
		  DCA TEMP	   /SAVE CHAR
		  CAL		   /WAIT UNTIL PUNCH READY
		  WAITE
		  PTPEF		   /SET PUNCH EVENT FLAG
		  ISZ PTPEF	   /TO THE PENDING STATE
		  TAD TEMP
		  PLS		   /PUNCH CHAR
		  CLA
		  JMP I PUNCH	   /RETURN
		  .     
		  .     
		  .     

     Interrupt skip chain code:

	  PTPINT, ZBLOCK 2	   /USED TO CHAIN SKIPS
		  PSF		   /CHECK PUNCH FLAG
		  JMP I PTPINT	   /NOT READY
		  CDF CIF CUR	   /SET CORRECT DF, IF
		  PCF		   /CLEAR PUNCH FLAG
		  TAD (PTPEF
		  POSTDS	   /DISMISS INTERRUPT,
				   /POSTING PTPEF
		  .
		  .
		  .
	  PTPEF,  0		   /PUNCH INITIALLY READY
	  TEMP,   0

     RTS/8 does not provide a mechanism for removal  of  entries  from  the
     interrupt skip chain.
     

     3.5  EXECUTIVE REQUEST WAIT STATES

     A summary of wait states generated by Executive Requests is  shown  in
     Table 3-3.


















				     3-13

			   RTS/8 EXECUTIVE REQUESTS

     
				   Table 3-3
	     Summary of Wait States Incurred by Executive Requests
     
     ----------------------------------------------------------------------
     |   ER	 | Wait State	  | Condition		| PC Suspended At |
     |---------- |----------------|---------------------|-----------------|     
     | SEND	 |  none	  | EFWT for SEND if	|	_	  |
     |		 |		  | message busy at 	|		  |
     |		 |		  | 'CAL'		|		  |
     |		 |		  |			|		  |
     | RECEIVE	 |  MSGWT	  | If no messages	|      'CAL'	  |
     | (No wait  |		  | in Input Queue	|		  |
     |if AC=4000)|		  | and AC positive	|		  |
     |		 |		  |			|		  |
     | WAITE	 |  EFWT	  | If Event Flag	|     'CAL'+3	  |
     |(No wait if|		  | not FINISHED	|		  |
     | EF 'done')|		  |			|		  |
     |		 |		  |			|		  |
     | RUN	 |  none	  |	_		|	_	  |
     |		 |		  |			|		  |
     | SUSPND	 |  RUNWT	  | If task = self	|     'CAL'+2	  |
     |		 |		  |			|		  |
     | POST	 |  none	  |	_		|	_	  |
     |		 |		  |			|		  |
     | SKPINS	 |  none	  |	_		|	_	  |
     |		 |		  |			|		  |
     | DERAIL	 |  none	  |	_		|	_	  |
     |		 |		  |			|		  |
     |	BLKARG	 | any (given by  | If task = self	|     'CAL'+3	  |
     |		 | argument)	  |			|		  |
     |		 |		  |			|		  |
     | SENDW	 |  EFWT	  | If message free	|     'CAL'+3	  |
     |		 |		  | but Event Flag	|		  |
     |		 |		  | not FINISHED	|		  |
     |     	 |  EFWT	  | If message busy	|      'CAL'	  |
     |		 |		  |			|		  |
     | UNBARG	 |  none	  |	_		|	_	  |
     |		 |		  |			|		  |
     | RESCHD	 |  none	  |	_		|	_	  |
     |		 |		  |			|		  |
     | WAITX	 |  EORMWT	  | If specified Event	|	'CAL'	  |
     |		 |		  | Flag not FINISHED	|		  |
     |		 |		  |			|		  |
     | WAITM	 | any (given by  |	 _		|  'CAL'+3	  |
     |		 | argument)	  |			|		  |
     |		 |		  |			|		  |
     |--------------------------------------------------------------------|
     | NOTE:  (a)  'CAL' denotes the address of the CAL instruction in the|
     |		   Executive Request.					  |
     |	      (b)  A message is said to be busy if its Event Flag has not |
     |		   yet been POSTED by its previous user.		  |
     ----------------------------------------------------------------------
     
     
     
     
				     3-14






				   CHAPTER 4

			      RTS/8 SYSTEM TASKS


     The RTS/8 system includes  system  tasks  that  control  most  of  the
     standard  Digital  PDP-8  I/O devices.  Also included is one task that
     provides interactive system control  from  the  console  terminal  and
     allows  a  single  copy  of  the  OS/8  monitor  system  to run in the
     background.  Foreground tasks are  protected  from  background  tasks;
     however,  the  reverse is not true.  The complete list of system tasks
     available in the RTS/8 system is as follows:

          o   Clock  Handler -  accepts  requests  in  the  form  of  RTS/8
	      messages  to  perform  actions  after  a  specified  time has
	      elapsed.

	  o   Console and Non-console Terminal  Handlers - handle a  single
	      terminal in either line or character mode.

	  o   Line Printer Handler - supports an LS8, LS8E, LP8 or LV8 line
	      printer.

	  o   Mass Storage Handlers - Control the  passing  of  information
	      from  these devices to and from memory for the RK08 and RK8-E
	      moving-head disks, DF32 and RF08 fixed-head disks,  and  TC08
	      DECtape unit.  Data is read and written in the standard RTS/8
	      block format (400 octal contiguous words).

	  o   Floppy Disk Handler - provides support for the use of the RX8
	      floppy disk.

	  o   LINCtape  Handler - supports  both   OS/8   and   DIAL-format
	      LINCtapes.

	  o   OS/8 Files Support Task - allows the user to look up, create,
	      and  delete files in OS/8 directories from a foreground task.
	      This task, when used with the mass storage handlers, provides
	      the  capability  to  read or write OS/8 files on mass storage
	      devices.

	  o   OS/8  Support  Task - supports  the  execution  of  an   OS/8
	      operating system in the background.

	  o   UDC/ICS Handler - enables the user  to  control  the  various
	      types of UDC/ICS modules.

	  o   Cassette Handler - allows the user to read or write data on a
	      tape cassette.

	  o   Cassette File Support Handler - allows the user to  look  up,
	      enter, and delete files from a DECcassette in CAPS-8 format.



				      4-1

			      RTS/8 SYSTEM TASKS

	  o   Power Fail Task - when used  with  power  fail  hardware,  it
	      provides  for  an  orderly  shutdown  when  AC power is lost.
	      Also, it allows a programmed restart when power returns.

	  o   Exit Task - allows the user  to  perform  special  processing
	      before making an exit from RTS/8.

	  o   PDP-8A Null Task - allows the user to count in decimal on the
	      LED display of the PDP-8A.

     The sources of the system tasks are supplied with  the  RTS/8  system.
     The  tasks  referred  to  as "handlers" are completely message-driven,
     i.e., when idle they are in the Message Wait state.  Other tasks  send
     these  handlers  I/O request messages.  When the handler completes the
     I/O operation, it POSTs the Event Flag  associated  with  the  request
     message and issues another RECEIVE ER.


     4.1  CLOCK HANDLER

     The Clock Handler Task can be assembled to  handle  any  one  of  four
     hardware  clocks.   The  user selects the clocks by setting the symbol
     CLKTYP in the parameter file to 0 for KD8-EA/DK8-EC, to 1 for KW12, to
     2  for  PDP-8A,  or  to 3 for DK8-EP.  The Clock Handler accepts RTS/8
     messages and inserts the entries into an internal clock queue.  As the
     entries  become  due, they are removed from the queue, and the request
     is decoded and executed.  The user fixes the length of  the  queue  at
     assembly  time  by defining the symbol CLKQLN in the parameter file to
     the minimum number of entry slots.  The default value  for  CLKQLN  is
     20.

     The format of a clock message is:

	  CLKMSG,   ZBLOCK 3	       /3 WORDS RESERVED FOR RTS/8
		    COMMAND+TASKNO     /TASKNO=0 MEANS TASKNO=SENDING TASK
		    TIMEHI
		    TIMELO
		    EXTRA1
		    EXTRA2

     The words TIMEHI and TIMELO specify a time interval from  the  present
     time  in  terms  of  "system ticks".  The user specifies the number of
     system ticks in a second in the RTS/8 parameter file by  defining  the
     parameter  SHERTZ.   The  hardware  tick rate (in ticks per second) is
     specified by the parameter HERTZ.  CLKTYP  and  HERTZ  are  determined
     completely  by  the  user's hardware configuration.  SHERTZ equals the
     reciprocal of the software system clock resolution.  HERTZ must be  an
     exact   multiple  of  SHERTZ.   For  example,  the  parameters  for  a 
     line-frequency clock might be:

	  DECIMAL
	  HERTZ= 120
	  SHERTZ= 10

     indicating that there will be 10 "system ticks" per second based on  a
     60-cycle  clock.   Such  parameters  might be used if only 1/10 second

				      4-2

			      RTS/8 SYSTEM TASKS


     resolution is necessary in the Clock Handler.  Note that  the  maximum
     interval  that can be expressed in TIMEHI and TIMELO is (2**24)/SHERTZ
     seconds.  This is approximately three days if SHERTZ=60.

     Other RTS/8 system tasks use the symbol CLOCK when  referring  to  the
     Clock  Handler.   The  user  should  define  this  symbol in the RTS/8
     parameter file to be equal to the Clock Handler's task number.  It

     should be undefined if a Clock Handler is not to be  included  in  the
     system.  (See Chapter 6 for a description of the parameter file.)

     COMMAND is the type of request and has the following meanings:

     Octal	    Symbolic		       Description

     0000     MARKTIME		     POST the event flag CLKMSG  after  the
				     specified  interval  elapses.  TASKNO,
				     EXTRA1, and EXTRA2 are ignored.

     1000     SCHEDULE		     POST CLKMSG  immediately.   Execute  a
				     RUN ER on the task specified by TASKNO
			 	     after the specified interval  elapses.
				     EXTRA1 and EXTRA2 are ignored.

     2000     TIMOUT		     POST CLKMSG immediately.   DERAIL  the
				     task   specified   by  TASKNO  into  a
				     subroutine whose address is  specified
				     in EXTRA1 after the specified interval
				     elapses. EXTRA2 is ignored.

     3000     SCHEDULE PERIODICALLY  POST CLKMSG  immediately.   Execute  a
				     RUN ER on the task specified by TASKNO
			  	     after the specified interval  elapses,
				     and  re-queue  this  command  with the
				     parameters EXTRA1 and EXTRA2 in  place
				     of  TIMEHI  and  TIMELO.  This has the
				     effect of running the  specified  task
				     periodically  with  a period specified
				     by EXTRA1 and EXTRA2.

     7000     CANCEL		     Cancel all the clock requests for  the
				     task   specified  by  TASKNO.  TIMEHI,
				     TIMELO,   EXTRA1,   and   EXTRA2   are
				     ignored.    POST  CLKMSG  immediately.
				     Note  that  the   requests   are   not
				     actually  deleted  and that they still
				     occupy  space  in the queue until they
				     time out.








				      4-3

			      RTS/8 SYSTEM TASKS


			---------------------------------------------------
			| 0 | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10 | 11 |
			---------------------------------------------------
		 	\_________/	         \_______________________/
			      |				     |
	Command: _____________|				     |
					       Task number __|
	0  MARKTIME
	1  SCHEDULE
	2  TIMOUT
	3  SCHEDULE PERIODICALLY
	7  CANCEL


		      Command Word Format - Clock Handler


     The Clock Handler also maintains the current  time-of-day  (in  system
     ticks  until  midnight),  in  symbolic locations TODH (high-order) and
     TODL (low-order) in Page 0 of Field 0.  When this time-of-day  reaches
     zero  (i.e., at midnight), it is reset to the quantity -(SHERTZ*86400)
     (24 hours until midnight) and an OS/8-format  date  word  in  symbolic
     location DATE in Page 0 of Field 0 is incremented by one day.
     
     Note that in order for the quantity SHERTZ*86400 to be contained in 24
     bits,  SHERTZ must be less than 192.  If SHERTZ is larger, an assembly
     error will result while assembling the Clock Handler.


     4.1.1  Examples of Clock Handler Calls

		   CAL		       /WITH A 60HZ SYSTEM TICK RATE,
		   SENDW	       /THIS CAUSES THE CURRENT TASK
		   CLOCK	       /TO "GO TO SLEEP" FOR 2 SECONDS.
		   SLEEPM
		   .
		   .
	  SLEEPM,  ZBLOCK 3	       /MESSAGE HEADER
		   0		       /SET EVENT FLAG AFTER INTERVAL
		   0;170	       /INTERVAL IS 120 (DECIMAL) SYSTEM
				       /TICKS

     If the  user  changes  the  value  170  to  the  assembler  expression
     2^SHERTZ, the preceding sequence becomes configuration-independent.

		   CAL		       /RUN THE TASK REPORT ONCE
		   SEND		       /EVERY HOUR, INDEFINITELY,
		   CLOCK	       /ASSUMING A 60HZ SYSTEM TICK RATE
		   RUNMSG

	  RUNMSG,  ZBLOCK 3	       /MESSAGE HEADER
		   SCHEDULE REPORT PERIODICALLY
				       /RUN REPORT AFTER SPECIFIED
				       /INTERVAL AND PERIODICALLY
				       /THEREAFTER,

				      4-4

			      RTS/8 SYSTEM TASKS


		   0;1		       /FIRST RUN IS ALMOST IMMEDIATELY
				       /(1/60 SECOND)
		   64;5654	       /PERIOD BETWEEN RUNS IS 216000
				       /(DECIMAL) SYSTEM TICKS = 3600
				       /SECONDS = 1 HOUR.


     4.2  TERMINAL HANDLER

     The RTS/8 Terminal Handler handles a single terminal in either line or
     character mode.  Input in line mode is terminated by a carriage return
     or an ALTMODE character and may be edited  using  the  RUBOUT  and  ^U
     characters.   The  RUBOUT  character  deletes the last valid character
     typed and prints a backslash; the  ^U  character  deletes  the  entire
     line and returns the carriage.  Character mode input is not echoed and
     is terminated by overflow of a specified character count.

     If multiple terminals are to  be  handled,  multiple  copies  of  this
     Terminal  Handler  must be assembled.  Assembly parameters in the body
     of the handler specify which device codes  the  handler  will  use  to
     access  its  terminal.   These  parameters  also  specify  whether the
     handler is to be a "console" Terminal Handler, that is,  the  terminal
     on which the MCR program is going to be  run.   The  console  Terminal
     Handler  invokes  the  MCR  whenever  a  ^C  is typed on the keyboard;
     nonconsole terminal handlers treat ^C as any other character.  For the
     console handler, C wakes up MCR by POSTing an Event Flag.

     The parameters edited into the distributed  version  of  the  Terminal
     Handler assemble the handler to handle the PDP-8 console terminal as a
     "console" device.  Thus, when the MCR function is required,  both  the
     MCR  task and the Terminal Handler task must be assembled and included
     as part of the RTS/8 system.  Modification of the Terminal Handler  to
     support  a  VT50  terminal and other features are described in Section
     4.2.1. 

     The format of messages to the Terminal Handler can be  either  of  the
     following:

     ZBLOCK 3			   ZBLOCK 3
     command+length		   ASSGN+tsknum
     INBUF
     OUTTXT

     Description:		   Description:

     Types text specified by	   ASSGN=200
     OUTTXT and command, then	   Assigns Terminal Handler to task specified
     reads text into INBUF.	   Deassigns Terminal Handler if tsknum=0

     Legal Commands, which can be combined, are as follows:






				      4-5

			      RTS/8 SYSTEM TASKS


     Octal   Symbolic  Action if specified    Action if not specified

     4000    NOPACK    Output text is in      Output text is in
		       unpacked ASCII, one    packed 6-bit, two
		       character per word     characters per word
		       terminated by a 0000.  terminated by a 00.

     2000    NOCRLF    Do not type a CR/LF    Type a CR/LF after
		       after the message.     typing the message.

     1000    IND       OUTTXT points to the   OUTTXT is the first
		       first word of the      word of the output text.
		       output text.

     0400    NOLINE    Input is in character  Input is in line mode;
		       mode; terminated       terminated by a CR
		       after 'length' input   or ALTMODE (ESC). The
		       characters read.       length is still tested.

	  Length	      Is a  seven-bit  field  which  specifies  the
			      maximum  size of the input buffer if input is
			      in line mode, or the number of characters  to
			      input  if  input  is  in  character mode.  If
			      input is in line mode and there are  LENGTH-1
			      characters  in  the  input buffer, characters
			      other than carriage return,  ALTMODE,  RUBOUT
			      and  ^U  will  not  be accepted or echoed the
			      message Event Flag is Posted.

	  INBUF		      Is a pointer to the input buffer;  if  it  is
			      zero, no input is taken.  The input buffer is
			      filled with input characters packed  one  per
			      word  with  the parity bit (bit 4) forced on.
			      If input is in line mode, the last  character
			      of  the line is followed by a zero word (if a
			      carriage return terminated  the  line)  or  a
			      -1(7777)   word   (if  an  ALTMODE  character
 			      terminated the line).

	  OUTTXT	      Is either the first word of the  output  text
			      string  (if  IND=0) or a pointer to the first
			      word of the output string  (if  IND=1000)  in
			      the same field as the message.

	  ASSGN =200	      "Assigns"  the  Terminal   Handler   to   the
			      specified task.  This will cause the terminal
			      handler to  only  accept  messages  from  the
			      specified  task.   If  another  task tries to
			      SEND a message to the Terminal Handler  while
			      it is assigned, the message will be placed in
			      the Terminal Handler's  Message  Input  Queue
			      but will not be removed for processing by the
			      Terminal  Handler  until  the  assignment  is
			      released.   The  task  to  which the Terminal
			      Handler   is   assigned   can   release   the

				      4-6

			      RTS/8 SYSTEM TASKS


			      assignment by sending a message assigning the
			      Terminal Handler to task number  0.   No  I/O
			      operation   is  performed  by  an  assignment
			      message.

	  tsknum	      Is a 6-bit field used with the ASSGN  command
			      to  specify  the  task  number of the task to
			      which the terminal is  to  be  assigned.   If
			      this   field   is   zero,   the  terminal  is
			      deassigned  allowing  the  terminal  task  to
			      accept commands from any task.


			---------------------------------------------------
			| 0 | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10 | 11 |
			---------------------------------------------------
			  ^   ^	  ^   ^   ^  \___________________________/
     Command (bits 0-4)	  |   |   |   |   |__		   |
			  |   |   |   |____ |		   |
     0: Packed ASCII   \__|   |   |______ | |		   |
     1: Unpacked ASCII /      |________ | | |		   |
				      | | | |		   |
     0: CR/LF at end of message    \__| | | |		   |  
     1: No CR/LF at end of message /	| | |		   |
					| | |		   |
     0: OUTTXT is the first word    \___| | |		   |
     1: OUTTXT points to first word /	  | |		   |
					  | |		   |
     0: Input in line mode      \_________| |		   |
     1: Input in character mode /	    |		   |
					    |		   |
     Bit 4 must be a 0 _____________________|		   |
							   |
     Length (bits 5-11)					   |
							   |
     If bit 3=1, no. of characters to input   \____________|
     If bit 3=0, maximum size of input buffer /


	  Command and Length Word Format - Terminal Handler I/O Mode


			---------------------------------------------------
			| 0 | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10 | 11 |
			---------------------------------------------------
			 \_____________/  ^   ^  \_______________________/
				|	  |   |			    |	
	Unused _________________|	  |   |			    |
					  |   |			    |
	Bit 4 must be a 1 ________________|   |			    |
					      |			    |
	Unused _______________________________|	      Task number __|


	       Command Word Format - Terminal Handler ASSGN Mode

				      4-7

			      RTS/8 SYSTEM TASKS


     4.2.1  Additional  Assembly  Parameters  Affecting  Terminal   Handler
	    Properties

     Several assembly parameters are available to the user  as  an  aid  in
     using  the  TTY  task.   This  section  describes these parameters.  A
     summary of their default values is shown in Table 4-1.

	  VT50	  =0	      Do not treat CTRL/S  and  CTRL/Q  as  special
			      characters.

		  =1	      Support CTRL/S and CTRL/Q.  If  this  feature
			      is enabled, typing CTRL/S while data is being
			      printed/displayed on the terminal will  cause
			      data  to stop until the next CTRL/Q is typed.
			      This can be used on  fast  CRT  terminals  to
			      temporarily   "freeze"   the   screen.   This
			      parameter must be set  to  1  if  the  user's
			      terminal  is a model VT50 or VT52 since these
			      terminals     will     occasionally      send
			      synchronization   characters   to   the  host
			      computer of their own volition.

	  WIDTH   =n	      Where n is an octal number that sets the page
			      width   to   n   characters.   TTY  width  is
			      currently set to 120(octal) characters.   For
			      example, setting the parameter

				   WIDTH = 60

			      changes the TTY  page  width  to  80(decimal)
			      characters.   After  n characters are printed
			      on   the   terminal,   the    handler    will
			      automatically   type  out  a  carriage-return
			      line-feed.   Sometimes  it  is  desirable  to
			      suppress  this CR/LF (for example, when using
			      direct cursor  addressing).   In  this  case,
			      WIDTH should be set equal to 0.  

	  SCOPE		      This option is used to determine treatment of
			      the RUBOUT key as follows:

			      SCOPE=0 provides the normal  mode  of  RUBOUT
			      support (echo rubouts with a backslash).
		
			      SCOPE=1 causes RUBOUT to move the cursor left
			      one   position,   physically   removing   the
			      character from the screen.  If the cursor  is
			      in  column  1, RUBOUT still works, but has no
			      visible effect.

	  TAB		      This option is used to simulate tabs  by  the
			      proper    number    of   spaces.    This   is
			      accomplished via the assembly  parameter  TAB
			      as follows:


				      4-8

			      RTS/8 SYSTEM TASKS


			      TAB=0 specifies that the  hardware  does  not
			      support  tabs.   The  software simulates tabs
			      with spaces.

			      TAB=1  specifies  that  the   hardware   does
			      support tabs.

	  FILL		      Fill  characters  are   supported   via   the
			      assembly    parameter    FILL   as   follows:

			      FILL=0 provides no fill characters.

			      FILL=n  sends n fill characters (nulls) after
			      a line feed.  The number n  must  be  in  the
			      range  1-5.   FILL=4  is recommended for 2400
			      baud VT05s.

	  CONSOL	      CONSOL = 1  means  the   handler   is   being
			      assembled for the console terminal(default).

			      CONSOL = 0 means that this handler  will  not
			      wake up the MCR when a ^C is typed.

	  OLDTTY	      OLDTTY = 1  specifies  the  use  of  the  old
			      two-page  handler  which  was  supplied  with
			      RTS/8 version  1.   This  handler  has  fewer
			      features  than  the  new  handler but it is a
			      page shorter.  The  parameters  VT50,  WIDTH,
			      SCOPE,  TAB and FILL described herein have no
			      effect when using this handler.

			      OLDTTY = 0 specifies  the  use  of  the   new
			      3-page terminal handler.

	  LSBOT		      LSBOT = 1 specifies the listing of  both  the
			      old two-page and new three-page.

			      LSBOT = 0(default) causes  only  the  handler
			      selected   by  the  OLDTTY  parameter  to  be
			      listed.

	  TTFLD		      Specifies the field of the TTY Handler  task;
			      for example, 20 designates field 2.

	  TTLOC		      Specifies the starting location  of  the  TTY
			      Handler  task;   for example, 3000 designates
			      the starting location at 3000.









				      4-9

			      RTS/8 SYSTEM TASKS


				   Table 4-1
		Summary of Terminal Handler Assembly Parameter
				 Default Values

     ----------------------------------------------------------------------
     | Parameter | Default Value |		  Meaning		  |
     |-----------|---------------|----------------------------------------|
     | VT50	 |	1	 | Support ^S, ^Q			  |
     |		 |		 |					  |
     | WIDTH	 |	120	 | Page width of 80(decimal) characters   |
     |		 |		 |					  |
     | SCOPE	 |	0	 | Rubouts echo as \			  |
     |		 |		 |					  |
     | TAB	 |	0	 | Simulate tabs			  |
     |		 |		 |					  |
     | FILL	 |	0	 | No fill characters			  |
     |		 |		 |					  |
     | CONSOL	 |	1	 | ^C wakes up MCR			  |
     |		 |		 |					  |
     | OLDTTY	 |	0	 | Use 3-page TTY task			  |
     |		 |		 |					  |
     | LSBOT	 |	0	 | List only TTY task selected by OLDTTY  |
     |		 |		 |					  |
     | TTFLD	 |	10	 | Not a default value, but given as an   |
     |		 |		 | example to show that the given number  |
     | TTLOC	 |	5000	 | assignments for TTFLD and TTLOC load   |
     |		 |		 | the TTY Handler in field 1 starting at |
     |		 |		 | location 5000			  |
     ----------------------------------------------------------------------


     4.2.2  Useful Equates in the Parameter File

     Several useful equates (described in Section 4.2) are available  which
     can  be  used  when  sending messages to TTY or LPT tasks. They are as
     follows:

	  NOPACK = 4000	      Used if output message  is  not  6-bit  ASCII
			      format.

	  NOCRLF = 2000	      Used if output message should not be followed
			      by carriage return/line feed.

	  IND = 1000	      Used if OUTTXT points to the  first  word  of
			      the output text.

	  NOLINE = 400	      Used if input is in character mode.

	  ASSGN = 200	      Used to assign the  device  handler  for  use
			      only by this task.

	  KL8ALINE = 100      Used with KL8-A support (see Section 4.13.2).


    

				      4-10

			      RTS/8 SYSTEM TASKS


     4.2.3  Examples of Terminal Handler Messages

	  HIYA,    ZBLOCK 3 	       /MESSAGE HEADER
		   0 		       /PACKED TEXT, END WITH CR/LF,
		   0 		       /NO INPUT
		   TEXT /HELLO/        /TEXT TO BE OUTPUT

     Sending the above message to the Terminal Handler prints HELLO on  the
     terminal.

	  QUEST,   ZBLOCK 3	       /MESSAGE HEADER
		   NOCRLF+60	       /PACKED TEXT, NO CR/LF,
				       /48-CHARACTER INPUT LIMIT
		   ANSWER	       /POINTER TO INPUT BUFFER
		   TEXT /TYPE THE ANSWER:/

     Sending the above message to the  Terminal  Handler  prints  TYPE  THE
     ANSWER:   on  the  terminal and inputs a reply without first returning
     the carriage.  The answer obtained from the  above  message  could  be
     printed on the terminal by sending the following message:

	  TYPANS,  ZBLOCK 3	       /MESSAGE HEADER
		   NOPACK+IND	       /UNPACKED TEXT, INDIRECT, WITH CR/LF
		   0		       /NO INPUT
		   ANSWER	       /POINTER TO OUTPUT TEXT


     4.3  LINE PRINTER HANDLER

     The RTS/8 Line Printer Handler outputs to an LEO,  LS8E,  LP8  or  LV8
     line  printer.   The format of messages to the Line Printer Handler is
     identical to the format of messages to the terminal handler,  but  the
     INBUF word and the LINE bit are ignored (the INBUF word must, however,
     be present in the message).






















				      4-11

			      RTS/8 SYSTEM TASKS


			---------------------------------------------------
			| 0 | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10 | 11 |
			---------------------------------------------------
			  ^   ^	  ^   ^   ^  \___________________________/
     Command (bits 0-4)	  |   |   |   |   |__		   |
			  |   |   |   |____ |		   |
     0: Packed ASCII   \__|   |   |______ | |		   |
     1: Unpacked ASCII /      |________ | | |		   |
				      | | | |		   |
     0: CR/LF at end of message    \__| | | |		   |  
     1: No CR/LF at end of message /	| | |		   |
					| | |		   |
     0: OUTTXT is the first word    \___| | |		   |
     1: OUTTXT points to first word /	  | |		   |
					  | |		   |
     0: Input in line mode      \_________| |		   |
     1: Input in character mode /	    |		   |
					    |		   |
     Bit 4 must be a 0 _____________________|		   |
							   |
     Length (bits 5-11)					   |
							   |
     If bit 3=1, no. of characters to input   \____________|
     If bit 3=0, maximum size of input buffer /


	 Command and Length Word Format - Line Printer Handler I/O Mode



			---------------------------------------------------
			| 0 | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10 | 11 |
			---------------------------------------------------
			 \_____________/  ^   ^  \_______________________/
				|	  |   |			    |	
	Unused _________________|	  |   |			    |
					  |   |			    |
	Bit 4 must be a 1 ________________|   |			    |
					      |			    |
	Unused _______________________________|	      Task number __|


	     Command Word Format - Line Printer Handler ASSGN Mode


     4.4  MASS STORAGE HANDLERS

     Handlers are available for TC08  DECtape,  DF32  and  RF08  fixed-head
     disks, RK8 and RK8E moving-head disks, RX01 floppy disks and LINCtape.
     All mass storage handlers accept the same message format  to  read  or
     write  blocks  on  various  mass storage devices.  However, the Floppy
     Disk Handler and the LINCtape Handler  allow  the  use  of  additional
     parameters other than the ones described herein.  These parameters are
     described in Sections 4.4.1 and 4.4.2.


				      4-12

			      RTS/8 SYSTEM TASKS


     The format of messages to mass storage handlers is:

	  MSMESG,  ZBLOCK 3
		   UNIT
		   RW + PAGES + FIELD
		   BUFADD
		   BLOKNO
		   STATUS

     where:

	  UNIT	   Is the number of the logical unit on which the operation
		   is to be performed.  DF32 and RF08 disks consist of only
		   one  unit.   TC08  DECtape   has   logical   units   0-7
		   corresponding  to  its physical units 0-7.  LINCtape has
		   logical units 0-7 corresponding to  its  physical  units
		   0-7.   RK8  disk  has logical units 0-3 corresponding to
		   its physical units 0-3.  RK8E  disk  has  logical  units
		   0-7.   Units  0-3  correspond  to the outer (lower track
		   number) half  of  physical  units  0-3,  and  units  4-7
		   correspond  to  the  inner (higher track number) half of
	 	   physical units 0-3, respectively.  RX01 has units 0 or 1
		   which  corresponds  to  the  left   and   right   drive,
		   respectively.

	  RW	   Is 0 for a read operation, 4000 for a write operation.

	  PAGES    Specifies the number of  (128-word)  pages  to  transfer
		   (times  100  octal).   For example, PAGES=2000 specifies
		   the transfer of  20(octal)  pages  or  2048  words;   if
		   PAGES=0, 40(octal) pages or 4096 words are transferred.

	  FIELD    Is the PDP-8 field in which  the  transfer  takes  place
		   (times   10  octal).   For  example,  if  FIELD=30,  the
		   transfer takes place in field 3.

     The RW+PAGES+FIELD word is sometimes called the function word  of  the
     message.

			---------------------------------------------------
			| 0 | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10 | 11 |
			---------------------------------------------------
			 \_____________________________/ \_______________/
					|			 |
	    Reserved for task use ______| 			 |
								 |
	    Unit ________________________________________________|


		   Unit Word Format - Mass Storage Handlers






				      4-13

			      RTS/8 SYSTEM TASKS


			---------------------------------------------------
			| 0 | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10 | 11 |
			---------------------------------------------------
			  ^  \_________________/ \_________/ \___________/
			  |	      |		      |		   |
     0: Read operation  \_|	      |		      |		   |
     1: Write operation /	      |		      |		   |
				      |		      |		   |
     No. of pages to transfer ________|		      |		   |
						      |		   |
     0-7 Field of transfer ___________________________|		   |
								   |
     Reserved for task use ________________________________________|


	         Function Word Format - Mass Storage Handlers


	  BUFADD   Is the starting address of the buffer to be transferred.

	  BLOKNO   Is the  block  number  on  the  device  from  which  the
		   transfer  will  begin.   All devices are assumed to have
		   256-word blocks.  On DECtape, the  first  128  words  of
		   each of an even/odd pair of 129-word DECtape records are
		   considered to be a block.

	  STATUS   Is a word that the handler sets  on  completion  of  the
		   operation.   It  contains  a  zero  if  the operation is
		   successful, otherwise it will contain a nonzero quantity
		   which  is  the  contents  of the device status register.
		   Tasks which use the mass storage  handlers  should  test
		   this  word  after  the  I/O operation has been completed
		   (that is, after the  Event  Flag  has  been  POSTed)  to
		   determine  if  any  errors occurred during the transfer.
		   All RTS/8 mass storage handlers retry  operations  three
		   times  if  errors  are  encountered  before  setting the
		   STATUS word to a nonzero.

     Note that the middle three words  of  a  message  to  the  RTS/8  mass
     storage  handlers  are  identical  to the arguments to an OS/8 handler
     when the same operation is performed.


     4.4.1  Floppy Disk Handler

     Each copy of the Floppy Handler can control one single  or  dual  RX01
     drive;   for  more  than  one RX01, multiple copies of the handler are
     required.  The format of messages to the Floppy Disk Handler is:

	  ZBLOCK 3
	  CODE+DEL+MODE+UNIT
	  RW+PAGES+FIELD
	  BUFADD
	  BLOKNO
	  STATUS

				      4-14

			      RTS/8 SYSTEM TASKS


     where:

	  CODE    = 0    Regular condition.  BLOKNO is  interpreted  as  an
			 OS/8   logical  record  number.   Also,  PAGES  is
			 interpreted in the OS/8 sense to mean  the  number
			 of  pages  of  data  to  transfer.  The DEL bit is
			 ignored.

		  = 4000 Special  Physical  Sector  Condition.   PAGES   is
			 ignored.    One  sector  is  transferred.   It  is
			 specified by BLOKNO which is to be interpreted  as
			 TTTTTTTSSSSS.   That  is, the high order 7-bits of
			 BLOKNO represent the physical track number.   This
			 number  must  be  in the range 0-76 decimal (0-114
			 octal).  The low order 5 bits of BLOKNO  represent
			 the sector number on that track.  This number must
			 be in the range 1-26 decimal (1-32 octal).

	  DEL	  = 0	 Deleted data marks should not be considered.

		  = 2000 Handle  deleted  data  marks  (if  CODE=4000)   as
			 follows:   If writing a sector, write deleted data
			 indication.  Do not note this fact in STATUS word.
			 If reading a sector, set bit 5 of STATUS word to a
			 1 if read deleted  data  indication.   In  such  a
			 case,  the  STATUS word may be nonzero even though
			 no physical error has occurred.  Other STATUS bits
			 are relevant and STATUS negative means hard error.

	  MODE    = 0	 Specifies transfer in 12-bit mode.

		  = 100  Specifies transfer in 8-bit mode.

			 OS/8 format uses 12-bit mode.  In 12-bit mode, the
			 64  12-bit  words  that  comprise  an  OS/8 floppy
			 sector are packed into the first 96 bytes  of  the
			 sector, while the last 32 bytes contain random bit
			 patterns.  In 8-bit mode, an  8-bit  byte  on  the
			 floppy disk corresponds to the low order 8-bits of
			 a 12-bit word in memory.  Data in the high order 4
			 bits of a word in memory is not transferred to the
			 floppy disk.

			 In 12-bit mode, a  sector  contains  64  (decimal)
			 12-bit  words  of  data.   In 8-bit mode, a sector
			 contains 128 8-bit bytes of data.

	  UNIT	  =	 Specifies the drive unit number.  It may be  0  or
			 1.  The number 0 refers to the unit on the left of
			 a dual drive.

	  RW 	  = 0 	 Read data from floppy disk.

		  = 4000 Write data to floppy disk.


				      4-15

			      RTS/8 SYSTEM TASKS


	  PAGES   =	 Specifies the number of pages to  transfer  (times
			 100  octal).  Pages = 0 transfers 40 pages (a full
			 field).  This value takes the range 0-37  in  bits
			 1-5  of  this  word.   PAGES  is ignored if CODE =
			 4000.  In that case,  either  100  (octal)  12-bit
			 words  or  200  8-bit  bytes  (from 200 words) are
			 transferred depending on MODE.

	  FIELD   =	 Specifies the field of buffer  (times  10  octal).
			 Bits 6-8 of this word have the range 0-7.

	  BUFADD  =	 Specifies the address of the  first  word  of  the
			 buffer   containing  data.   Field  of  buffer  is
			 determined by FIELD.  Length of buffer depends  on
			 PAGES if CODE = 0 or on MODE if CODE = 4000.

	  BLOKNO  =	 Represents first logical OS/8 block to transfer if
			 CODE  = 0.  Each OS/8 block consists of 4 sectors.
			 Track 0 is ignored and a 2-to-1 interleave  scheme
			 is  employed.   If CODE = 4000, this word contains
			 physical track and sector numbers  in  the  format
			 TTTTTTTSSSSS.

	  STATUS  =	 Receives  the  status  of   the   operation   upon
			 completion.    If   negative,  a  hard  error  has
			 occurred.  If 0, no error has occurred.  This word
			 may be positive nonzero only if DEL = 2000.

			 The meaning of the STATUS bits is as follows:

			 Bit		Meaning if 1

			 0		Hard error
			 1-3		Not used by controller
			 4		Not used by RTS/8
			 5		Deleted data indication
			 6-7		Not used by controller
			 8		Reserved for future use by
					controller
			 9		INIT done (can occur after
					temporary power failure to
					controller)
			 10		Parity error
			 11		CRC error




				      NOTE
		    On power fail restart,  the  INIT  error
		    might  occur.   When  this error occurs,
		    the calling task  should  send  the  I/O
		    message again.



				      4-16

			      RTS/8 SYSTEM TASKS


			---------------------------------------------------
			| 0 | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10 | 11 |
			---------------------------------------------------
			  ^   ^	              ^                         ^
			  |   |		      |				|
     0: Regular condition\|   |_________      |				|
     1: Special physical /	       |      |				|
	sector condition/	       |      |				|
				       |      |				|
     0: Do not handle deleted marks \__|      |				|
     1: Handle deleted marks	    /	      |				|
					      |				|
     0: Transfer in 12-bit mode \_____________|				|
     1: Transfer- in 8-bit mode /					|
									|
     0: Left unit of dual drive  \______________________________________|
     1: Right unit of dual drive /


	CODE = 4000 (bit 0 set to 1) transfers one sector specified by
	BLOCKNO as follows:


			---------------------------------------------------
			| 0 | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10 | 11 |
			---------------------------------------------------
			 \_________________________/ \___________________/
				      |			       |
	Physical track no. \__________|			       |
	(0-114 octal)      /				       |
							       |
	Sector no. on track \__________________________________|
	(1-32 octal)        /


		    Unit Word Format - Floppy Disk Handler


			---------------------------------------------------
			| 0 | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10 | 11 |
			---------------------------------------------------
			  ^		      ^		      ^    ^    ^
			  |		      |		      |    |    |
	Hard error _______|		      |		      |    |    |
					      |		      |    |    |
	Deleted data _________________________|		      |    |    |
							      |    |    |
	INIT done ____________________________________________|    |    |
								   |	|
	Parity error ______________________________________________|	|
									|
	CRC error ______________________________________________________|


		   Status Word Format - Floppy Disk Handler

				      4-17

			      RTS/8 SYSTEM TASKS


     The largest legal OS/8 block number on a floppy disk is 755 octal.  If
     block  756  is  referenced, an error is generated. Use of larger block
     numbers may produce  unpredictable  results.   Specifying  an  illegal
     track or sector may produce an error with STATUS = 4000.

     The standard OS/8 Interleave Scheme is as follows:

     OS/8 Logical Block (octal) Floppy Sectors (track/sector in decimal)

	      0			1/1,	1/3,	1/5,	1/7
	      1			1/9,	1/11,	1/13,	1/15
	      2			1/17,	1/19,	1/21,	1/23
	      3			1/25,	1/2,	1/4,	1/6
	      4			1/8,	1/10,	1/12,	1/14
	      5			1/16,	1/18,	1/20,	1/22
	      6			1/24,	1/26,	2/1,	2/3
	      7			2/5,	2/7,	2/9,	2/11
	     10			2/13,	2/15,	2/17,	2/19
	     11			2/21,	2/23,	2/25,	2/2
	     12			2/4,	2/6,	2/8,	2/10
	     13			2/12,	2/14,	2/16,	2/18
	     14			2/20,	2/22,	2/24,	2/26
	     15			3/1,	3/3,	3/5,	3/7
	     .
	     .
	     .

     Track 0 is not used by OS/8, and cannot  be  accessed  in  the  12-bit
     mode.

     4.4.2  LINCtape Handler

     The LINCtape Handler supports both OS/8  and  DIAL  format  LINCtapes.
     The format of messages to the LINCtape Handler is:

	  ZBLOCK 3
	  MODE+UNIT
	  RW+PAGES+FIELD
	  BUFADD
	  BLOKNO
	  STATUS

    where:

	 UNIT=		 Specifies the LINCtape unit number in range  0  to
			 7.

	 MODE=0		 Specifies OS/8 Mode. A  LINCtape  is  presumed  to
			 contain  200  or  201  (octal)  words per physical
			 block.

	     =4000	 Specifies DIAL Mode.  A LINCtape  is  presumed  to
			 contain 400 (octal) words per physical block.



				      4-18

			      RTS/8 SYSTEM TASKS


			 Note: The LINCtape used is not checked to see if
			 it is properly formatted for the specified mode.
			 Use of a LINCtape with improper physical  format
			 will produce unpredictable results.

	 RW  =0		 Read data from LINCtape

	     =4000	 Write data to LINCtape

	 PAGES		 Specifies the number of 128-word pages to transfer
			 (times   100   octal).   For  example,  PAGES=2000
			 transfers  20  octal  pages  or  2048  words;   if
			 pages=0,   40   octal  pages  or  4096  words  are
			 transferred.

	 FIELD		 Specifies the PDP-8 field in  which  the  transfer
			 takes  place  (times  10  octal).   (For  example,
			 FIELD=30, the transfer takes place  in  field  3).

	 BUFADD		 Is the  starting  address  of  the  buffer  to  be
			 transferred.

	 BLOKNO		 Is the block number on the device from  which  the
			 transfer  will  begin.  All devices are assumed to
			 have 256-word  blocks.   On  OS/8  LINCtapes,  two
			 consecutive  physical  blocks  comprise  one  OS/8
			 logical block.  Only the first 128 words  in  each
			 physical block contain meaningful data.

			 When running in DIAL  mode,  BLOKNO  represents  a
			 physical  LINCtape  block  number.   In this case,
			 PAGES must be even because an even number of pages
			 is  transferred.   If  PAGES is (incorrectly) odd,
			 the  last  page  is  not  transferred,  except  if
			 PAGES=1  which  will result in one block (2 pages)
			 being transferred.

	 STATUS		 is the ones complement of tape  check  (checksum).
			 The value 0 means no error.  STATUS is always 0 on
			 a Write operation.   Three  software  retries  are
			 attempted on a checksum read error.  Note that the
			 hardware performs infinite retries on most  errors
			 (write-lock-out,  tape  not  mounted,  bad spot on
			 tape) and does not return control to  RTS/8  until
			 successful.

	
				    CAUTION

		    In the OS/8 mode, the word following the
	 	    end   of   the   buffer  is  temporarily
		    destroyed while a LINCtape operation  is
		    in   progress.   The  location  is  then
		    restored   upon   completion   of    the
		    operation.   However,  since  RTS/8 is a

				      4-19

			      RTS/8 SYSTEM TASKS


		    real-time system, code may be  executing
		    while the tape operation is in progress.
		    The user must make sure that  this  word
	 	    is  never  referenced while the LINCtape
		    is being used.  Under  no  circumstances
		    should the word following the end of the
		    buffer belong to another task.
	


			---------------------------------------------------
			| 0 | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10 | 11 |
			---------------------------------------------------
			  ^				     \___________/
	0: OS/8 mode  \___|					   |
	1: DIAL model /						   |
								   |
	Unit number _______________________________________________|

		      Unit Word Format - LINCtape Handler


     4.4.3  Example of Mass Storage Handler Call

		   CAL
		   SENDW
		   DTA			/SEND A MESSAGE TO THE DECTAPE
					/HANDLER
		   DTAMSG		/AND WAIT FOR COMPLETION
		   TAD STATUS		/CHECK THE STATUS OF THE OPERATION
		   SZA CLA
		   JMP ERR		/BAD - GO TO ERROR ROUTINE
					/OK - CONTINUE PROCESSING
		   .
		   .
		   .
	  DTAMSG,  ZBLOCK 3		/MESSAGE HEADER
		   4			/DECTAPE UNIT 4
		   4210			/WRITE 256 WORDS FROM FIELD 1
		   BUFFER		/ADDRESS OF BUFFER
		   55			/INTO BLOCK 55 (RECORDS 132 & 133)
	  STATUS,  0			/STATUS OF OPERATION STORED HERE


     4.5  POWER FAIL TASK

     The Power Fail  Task  provides  the  mechanism  by  which  the  system
     recovers  from power failure.  If the power-fail/auto-restart hardware
     option is present and if the system parameter PWRFAL was equated to  a
     nonzero  value, the SPL (Skip on Power Low) instruction is included in
     the interrupt skip chain.   If  a  power  low  condition  occurs,  the
     processor  state  is  saved  and  the processor is halted.  When power
     comes back, the processor state is  restored  and  an  Event  Flag  is
     POSTed  which  wakes  up  the  Power  Fail  Task.  The Power Fail Task
     restores the clock, console terminal, and OS/8 terminal  if  they  are

				      4-20

			      RTS/8 SYSTEM TASKS


     present, and also performs an action for each task in the system based
     on the contents of an internal table.  Each task has a one-word  entry
     in this table, which contains:

	  0	   If nothing should be done for this task (default value)

	  -1	   If the EFWT (Event Flag Wait) bit should be  cleared  in
		   the  Task  Flags  Table  entry for this task (i.e., this
		   task should be taken out of Event Flag Wait)

	  ADDR 	   If the task should be DERAILed to location ADDR  in  the
		   field  in  which  it  is executing as well as having its
		   EFWT bit cleared.

     Each task in the system may alter its entry in the Power  Fail  Task's
     table  by sending a message to the Power Fail Task.  The format of the
     message is:

	  PWRMSG,  ZBLOCK 3
		   WORD

     where:

	  WORD     is the new contents of the Power Fail Task's table entry
		   for the sending task.


     4.6  OS/8 SUPPORT TASK

     The OS/8 Support Task supports the execution  of  the  OS/8  operating
     system  as  a  task  under  RTS/8.  OS/8 is run in the top two or more
     memory  fields  under  control  of  the  KM8-E  memory  extension  and
     timeshare  option (standard on PDP-8/E, 8/F, or 8/M with 8K or more of
     core memory) or TSS-8 time sharing hardware option.


				      NOTE

		    A jumper on the KM8-E module is used  to
		    select   the  timeshare  function.   The
		    module is shipped with  this  jumper  in
		    place   (timeshare  function  disabled). 
		    The PDP-8A utilizes the memory extension
		    and  timeshare  option  provided  by the
		    KM8-A extended option board.   A  switch
		    on  the  KM8-A  module is used to enable
		    the timeshare function.


     The OS/8  Support  Task  is  configured  at  system  startup  time  to
     establish  a  correspondence  between  OS/8  devices and RTS/8 handler
     tasks.  Terminal input and  output  from  OS/8  are  ring-buffered  by
     several characters to minimize input loss due to the usurpation of the
     CPU by tasks of higher priority.   Because  of  the  large  number  of
     trapped CDF instructions in OS/8 and its Commonly Used System Programs

				      4-21

			      RTS/8 SYSTEM TASKS


     (CUSPs), response time is slower than a stand-alone  OS/8  system  but
     still  quite  reasonable.  The background OS/8 task must have the same
     system device that was used by the OS/8 system  to  load  RTS/8.   The
     OS/8 Support Task cannot run on a stand-alone PDP-8 without OS/8.

     Several parameters in the system parameter file control  the  assembly
     of  the  OS/8  Support Task.  The parameters and their meanings are as
     follows:

	  OSFLDS	 Defined as the number of fields to be dedicated to
			 OS/8.
			 Example: OSFLDS=2 specifies two fields  or  8K  of
			 memory for OS/8.

	  OSKBDV	 Set equal to the keyboard IOT  code  of  the  OS/8
			 terminal.
			 Example:   OSKBDV=03  specifies  the  use  of  the
		 	 console terminal keyboard of OS/8.
			 Note:  OS/8 requires its own dedicated terminal.

	  OSTTDV	 Set equal to the teleprinter IOT code of the  OS/8
			 terminal.
			 Example:   OSTTDV=04  specifies  the  use  of  the
			 console teleprinter for OS/8.

	  OSFILL	 Specifies how many null characters must  follow  a
			 line-feed  character  on  the OS/8 terminal.  This
			 allows high-speed VT05 terminals  to  be  used  as
			 OS/8   terminals.    For  standard  Teletypes  and
			 DECwriter  terminals,  this  parameter  should  be
			 set to zero.
			 Example:  OSFILL=4 allows the use of a  2400  baud
			 VT05.

	  OSSYSD	 Specifies the OS/8 system device driver task.
			 Example:  OSSYSD=DTA  specifies  DTA0  as  the OS/8
			 system device.


				      NOTE

		    The user does  not  need  to  include  a
		    terminal  driver  for  the OS/8 terminal
		    device (it is built into OS8SUP).


     The OS/8 system that runs under the OS/8 Support Task  runs  all  OS/8
     CUSPs  except  BUILD,  BOOT,  PIP10,  INDUSTRIAL  BASIC, and BASIC and
     FORTRAN LAB runtime functions.  All references  to  the  keyboard  and
     teleprinter   are   diverted   to  the  specified  OS/8  keyboard  and
     teleprinter.  References in OS/8 to the LEO, LS8E,  LP8  or  LV8  line
     printers  are diverted to the RTS/8 line printer handler if the system
     parameter LPT is defined; otherwise they are executed directly by  the
     Support  Task.   References to the following OS/8 device names will be
     diverted to the corresponding RTS/8 handler if one is defined:

				      4-22

			      RTS/8 SYSTEM TASKS


	  DTA0-DTA7
	  LTA0-LTA7
	  RKA0-RKA3
	  RKB0-RKB3
	  RXA0-RXA7

     If one is not defined, OS/8 will perform the I/O  directly  using  the
     standard OS/8 handler.

     In addition, the OS/8 handlers SYS and DSK are diverted to the handler
     specified  by the parameter OSSYSD.  Other references to I/O under the
     supported OS/8 system may cause the OS/8 support task  to  hang  in  a
     loop.  References to a handler called RTS8 are diverted to OS8COM (see
     Section 4.7).


     4.6.1  Mapping of Fields with OS/8 Support Task

     The parameter HGHFLD in the parameter file must  specify  the  highest
     field  available to the entire RTS/8-OS/8 system.  This is usually the
     highest field available in memory (e.g., 30 for a 16K  machine).   The
     OS8SUP  task  maps OS/8 fields into real fields as follows.  The field
     which OS/8 uses as field 0 is actually HGHFLD.  OS/8 fields 1,  2,  3,
     etc.    are  mapped  into  consecutive  fields  beginning  with  field
     HGHFLD-OSFLDS+1, proceeding upward.  If an OS/8 program  references  a
     field  greater than HGHFLD, unpredictable results will occur, as these
     fields are mapped over the lower OS/8 fields.  The software core  size
     is  correctly  set  to  OSFLDS  and should be used by multi-field OS/8
     programs.


     4.7  OS/8 - RTS/8 COMMUNICATION (OS8COM)

     The OS/8 Support Task contains a mechanism by which OS/8 can  talk  to
     an RTS/8 task.  To perform this communication, the OS/8 system must be
     configured with a handler called RTS8.  This handler can be  a  dummy;
     it  need  not  do  anything.  In fact, it can be some other handler to
     which the name RTS8 has been assigned.  The OS/8  Support  Task  traps
     all  calls to this handler.  The arguments that are passed to the RTS8
     handler by an OS/8 program will be  passed  to  an  RTS8  task  called
     OS8COM.   The  user  is  responsible  for  writing  this  OS8COM task.

     The OS8COM task performs an RTS/8  RECEIVE  ER.   The  task  can  then
     receive a message any time an OS/8 program reads or writes to the RTS8
     handler.  This message looks like any other message to a mass  storage
     device.   OS8SUP does make one change to the arguments. Bits 6 through
     8 of the function word originally contain the  field  of  the  buffer.
     This  is  the  field where OS/8 expects the buffer to be.  When OS8COM
     gets control, these bits identify the actual field that  contains  the
     buffer.    OS8COM   can  return  information  to  OS/8  through  these
     arguments.





				      4-23

			      RTS/8 SYSTEM TASKS


     4.7.1  Using the OS8COM Task

     An OS/8 program that runs an RTS/8 task as specified by the OS/8  user
     is shown in the following example.

     Example:
		     USR=7700	     /LOCATION OF OS/8 USER SERVICE ROUTINE
		     JMS PRINT	     /PRINT MESSAGE "WHAT TASK WOULD YOU
				     /LIKE TO RUN?" ON THE OS/8 TERMINAL
		     JMS READ	     /READS RESULT FROM OS/8 KEYBOARD
				     /RETURNS TASK NUMBER IN RANGE 1-77
				     / IN AC
		     DCA TASKNUM     /STORE IT AWAY
		     CIF 10
		     JMS I (USR      /CALL USR
		     1		     /TO DO A FETCH
		     DEVICE RTS8     /OF DEVICE 'RTS8'
     ENTRY,	     ADDR	     /DUMMY ADDRESS (HANDLER WILL ALREADY
				     /BE RESIDENT
		     HLT	     /ERROR (HANDLER NOT FOUND)
     /NOTE THAT THIS CODE IS NOT REUSABLE AND THAT LOCATION
     /' ENTRY ' IS SET TO THE ENTRY POINT FOR THIS HANDLER
		     CIF 0
		     JMS I ENTRY     /CALL HANDLER
		     0		     /DUMMY READ
     TASKNUM,	     0		     /TASK NUMBER
		     ZBLOCK 2	     /DUMMY
		     JMP I (7605     /RETURN TO OS/8

     It should be noted that TASKNUM is being passed as the second argument
     instead of the first because OS8SUP automatically modifies bits 6-8 of
     the first argument, presuming that a mapped field  number  is  located
     there.   OS8COM expects three arguments after the handler call plus an
     error return.  These must be specified by the user.

     Where the OS/8 portion of the program has  been  written,  the  OS8COM
     task that handles the RTS/8 side of the communication must be written.
     OS8COM  is  written  like any other RTS/8 user task, and an example of
     what it might look like is as follows:

		     TASK=OS8COM     /OS8COM IS ASSIGNED A PRIORITY IN THE
				     /PARAMETER FILE
		     INIWT=0	     /COMES UP RUNNING
		     CUR=40	     /SPECIFY FIELD HERE
		     FIELD CUR%10
		     *200	     /STARTING ADDRESS
     START,	     CAL
		     RECEIVE	     /IMMEDIATELY GO INTO RECEIVE WAIT
     MADDR,	     0		     /ADDRESS OF MESSAGE LEFT HERE
		     DCA MSGFLD	     /CDF TO MESSAGE FIELD LEFT IN AC
     MSGFLD,	     HLT
		     ISZ MADDR	     /POINT TO FUNCTION WORD
		     ISZ MADDR	     /POINT TO BUFFER ADDRESS
				     /(SECOND OS/8 ARGUMENT)


				      4-24

			      RTS/8 SYSTEM TASKS


		     TAD I MADDR     /GET TASK NUMBER
		     CAL
		     RUN	     /RUN THIS TASK
				     /OS8COM WANTS TO BE HIGHER
				     /PRIORITY THAN TASK IT IS RUNNING
		     TAD MSGFLD
		     DCA EFCDF
		     TAD (-5
		     TAD MADDR	     /GET ADDRESS OF EVENT FLAG
				     /FOR MESSAGE
		     CAL
		     POST	     /POST MESSAGE
     EFCDF,	     HLT
		     JMP START	     /GET ANOTHER MESSAGE

     In this example, the task number was put in the second argument of the
     OS/8  call.   However,  it  became the third word of the RTS/8 message
     because OS8SUP always adds a word to the mass  storage  call  argument
     list,  namely the unit number.  For a description of the OS/8 standard
     handler call format, see Section 4.1  of  the  OS/8  Software  Support
     Manual.   For  a  description  of the standard message format for mass
     storage devices, see Section 4.4 of this manual.


     4.7.2  Other Techniques

     Other techniques which can be employed by the user are as follows:

	  1.  If the RTS/8 handler STATUS word  (word  5)  of  the  message
	      posted  by OS8COM is nonzero, then return is taken to OS/8 at
	      the error return of the handler call.

	  2.  Arguments may be passed back to  OS/8  through  the  argument
	      list.

	  3.  If more than three words of data need to be passed to  OS8COM
	      from  OS/8,  the  user can pass a CDF and address of the area
	      where the data resides.  If  the  CDF  occurs  as  the  first
	      argument  to  the  handler  call,  it  automatically  will be
	      relocated before being passed to OS8COM.


     4.8  OS/8 FILE SUPPORT TASK

     The OS/8 File Support Task (OS8F)  allows  other  tasks  to  look  up,
     create,  and  delete files in OS/8 directories.  This task is included
     in the same source file as the OS/8 Support Task,  but  the  user  can
     assemble  it  independently of that task (depending on which tasks are
     defined in the system parameter file).  The format of messages to OS8F
     is:






				      4-25

			      RTS/8 SYSTEM TASKS


	  OSFMSG,  ZBLOCK 3
		   DEVHND^10+UNIT+FUNCT
		   FILPTR
		   STATUS
		   BLOKNO
		   LENGTH 

     where:

	  DEVHND	 Is the task number of the handler for the  desired
			 device.

	  UNIT		 Is the unit number on which the operation is to be
		 	 performed.

	  FUNCT		 Represents the function to be performed.   It  can
			 have the following values:

			 0     Looks up the specified filename and returns
			       its starting block number in BLOKNO, and its
			       length in LENGTH (as a two's complement
			       number).

			 2000  Enters the specified filename into the first
			       empty  space (on the device) whose length is
			       equal to or exceeds  the  value  in  LENGTH.
			       Returns the starting block number of the new
			       file in BLOKNO.  If a file of the same  name
			       previously  existed  on  the  device  it  is
			       deleted.  The value of LENGTH is unchanged.

			 4000  Deletes the specified filename.

	  FILPTR	 Is a pointer to a  4-word  filename  in  the  same
			 field as the message.  The PAL8 pseudo-op FILENAME
			 can be used to generate these filenames.

	  STATUS	 Describes the final status  of  the  operation  as
		  	 follows:

			 0     Operation successful.
			 1     File not found on Lookup or Delete.
			 2     No room for file on Enter.
			 >2    I/O error occurred. The value is the
			       hardware error status of the device.
			 -1    Invalid directory on device.










				      4-26

			      RTS/8 SYSTEM TASKS


			---------------------------------------------------
			| 0 | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10 | 11 |
			---------------------------------------------------
			 \_____/  ^  \_____________________/ \___________/
			    |     |		|		   |
	Function: __________|	  |		|		   |
	O Lookup		  |		|		   |
	1 Enter			  |		|		   |
	2 Delete		  |		|		   |
	3 Unused		  |		|		   |
				  |		|		   |
	Unused ___________________|		|		   |
						|		   |
	Task number ____________________________|		   |
							  	   |
	Unit ______________________________________________________|

			    OS8F Call Function Word


     If both OS8F and the OS/8 Support Task are present  in  a  system,  an
     interlock  is  set  up  to  prevent simultaneous updating of directory
     blocks by both systems.  Because OS/8 tends to leave directory  blocks
     in  memory  for  long  periods  of  time, this interlock scheme causes
     lengthy delays for the OS8F task.  Before a Delete or Enter  operation
     is performed, OS8F waits until OS/8 is in a state in which:

	  1.  There  is  no  active  temporary  file  on  the  OS/8  device
	      corresponding to DEVHND and UNIT.

	  2.  OS/8 has just loaded the Keyboard Monitor,  Command  Decoder,
	      or USR into core.

     Look up operations are not interlocked since they do  not  modify  the
     directory.


     4.9  UNIVERSAL  DIGITAL  CONTROLLER/INDUSTRIAL  CONTROLLER   SUBSYSTEM
	  (UDC/ICS) HANDLER

     The UDC/ICS handler gives the  user  the  capability  to  control  the
     various  types  of  UDC/ICS functional devices.  This handler performs
     two types of action:  immediate  and  associated.   Immediate  actions
     include  reading  and sending analog and digital values to appropriate
     UDC/ICS functional devices.   Associated  actions  can  be  linked  to
     specified  events  within  the UDC/ICS (counters overflowing, switches
     being thrown).  The associated actions can do the following:

	  1.  Run a specified task when the event occurs
	  2.  Set the Event Flag when the event occurs
	  3.  DERAIL a specified task when the event occurs

     The number of associated requests that can be  pending  simultaneously
     is  determined  by  the  size of the buffer, which is specified by the
     assembly parameter RINGBUF.

				      4-27

			      RTS/8 SYSTEM TASKS


     The UDC/ICS handler permits the following operations:

	  1.  Analog Output 	 - send a 10-bit value to an analog channel

	  2.  Analog Input 	 - accept input from analog subchannel

	  3.  Digital Output 	 - send a 12-bit value to a digital channel

	  4.  Digital Input 	 - read a digital channel

	  5.  Get Generic Code   - determine  the  generic   code   for   a
				   specified channel

	  6.  Enable Counter	 - permit interrupts from a counter channel

	  7.  Read Counter	 - read  current  value  of   the   counter
				   channel

	  8.  Disable Counter	 - disable  interrupts   from   a   counter
				   channel

	  9.  Enable Contacts	 - permit interrupts from a contact channel

	 10.  Change Of State	 - find the current COS value for a contact
		  		   channel

	 11.  Disable Contacts   - ignore interrupts from a contact channel

     Each operation is discussed in detail below, including the  format  of
     the  message  for specifying the operation.  The first three words are
     required for use by the Executive.  Word 4 specifies  one  of  the  11
     UDC/ICS  operations  which  are as follows: AO=0;  DO=1;  DI=2;  GC=3;
     EC=4;   RC=5;   DC=6;   ECT=7;   CS=10;   DCT=11;   AI=12.    Word   5
     designates  the channel being used for the indicated operation.  Words
     6 through 8 may be required to completely specify the  operation,  and
     the  number  used  is  dependent  upon  the  operation.  The word that
     follows the last word specifying the desired operation is used for the
     value  read  or  the  value returned.  Word 10 of all UDC/ICS messages
     contains the error state.

     The general format for a UDC/ICS message is:

	  ZBLOCK 3
	  OPERATION
	  CHANNEL
	  OPWORD1
	  OPWORD2
	  OPWORD3
	  VALUE
	  STATUS






				      4-28

			      RTS/8 SYSTEM TASKS


     4.9.1  AO   Analog Output

	  Format:    AO
		     channel number
		     subchannel & value

     Channel number is the analog output channel.  The subchannel and value
     word  is formed by the subchannel (0-3) in bits 0 and 1 and the 10-bit
     value in bits 2-11.  For example,  a  message  for  an  analog  output
     operation:

	   AOEX,   ZBLOCK 3
		   AO		       /ANALOG OUTPUT
		   23		       /CHANNEL 23
		   4614		       /SUBCHANNEL 2, VALUE 614
		   ZBLOCK 3
	   AOER,   0		       /ERROR INDICATOR


			---------------------------------------------------
			| 0 | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10 | 11 |
			---------------------------------------------------
			 \_____/ \_______________________________________/
			    ^			    ^
	Subchannel _________|			    |
						    |
	Value ______________________________________|


	      Subchannel and Value Word Format - UDC/ICS Handler


     4.9.2  AI   Analog Input

	  Format:   AI
		    channel
		    subchannel & gain
		    answer

     where channel is the analog input channel.  The  subchannel  and  gain
     word need only specify the gain in bits 1-3 and the subchannel in bits
     9-ll for UDC, and 5-11 for ICS.  The handler automatically sets bit  0
     (enable conversion) and read control register (UDC bit 8;  ICS bit 4).
     The ICS analog converters must have addresses which are less  than  20
     (octal)  since  all  converter modules must be located in the first 16
     slots of the ICS unit.   After  conversion,  the  digitized  value  is
     placed in the answer word.









				      4-29

			      RTS/8 SYSTEM TASKS


			---------------------------------------------------
			| 0 | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10 | 11 |
			---------------------------------------------------
			  ^  \_________/  ^  \___________________________/
			  |	  |	  |		  |
       Enable conversion _|	  |	  |		  |
				  |	  |		  |
       Gain ______________________|	  |		  |
					  |		  |
       ICS read control register; ________|		  |
       (for UDC, bit 8) 				  |
							  |
       ICS subchannel; ___________________________________|
       (for UDC, bits 9-11)


	       Subchannel and Gain Word Format - UDC/ICS Handler


     An example of a message for an analog input operation is as follows:

	  AIEX,    ZBLOCK 3
		   AI		       /ANALOG INPUT
		   17		       /CHANNEL 17
		   3		       /SUBCHANNEL 3, GAIN 1
	  AIANS,   0		       /RESULT HERE
		   ZBLOCK 2
	  AIERR,   0		       /ERROR INDICATOR

     The user should ensure that for each major channel there is sufficient
     time (approximately 250 microseconds for UDC;  5 milliseconds for ICS)
     for each subchannel conversion  to  be  completed  before  another  is
     indicated.  In general, it may be helpful if all A/D conversions for a
     major channel are initiated from the same task.


     4.9.3  DO   Digital Output

	  Format:   DO
		    channel
		    value

     Channel is a legal digital output channel and value is the  number  to
     be output.  For example:

	  DOEX,	   ZBLOCK 3
		   DO 		       /DIGITAL OUTPUT
		   20 		       /CHANNEL 20
		   7777 	       /VALUE = 7777
		   ZBLOCK 3
	  DOER,	   0 		       /ERROR INDICATOR





				      4-30

			      RTS/8 SYSTEM TASKS


     4.9.4  DI   Digital Input

	  Format:   DI
		    channel
		    result

     Channel is the appropriate  digital  input  channel  and  result  will
     contain the value of the channel when read.  For example:

	  DIEX,    ZBLOCK 3
		   DI 		       /DIGITAL INPUT
		   27 		       /CHANNEL 27
	  DIANS,   0		       /VALUE OF CHANNEL 27 WILL BE PUT
				       /HERE
	  	   ZBLOCK   3
	  DIER, 0		       /ERROR INDICATOR


     4.9.5  GC   Generic Code

	  Format:   GC
		    channel
		    result

     The generic code of the specified  channel  is  put  in  result.   For
     example:

	  GCEX,    ZBLOCK 3
		   GC		       /DETERMINES GENERIC CODE
		   27		       /CHANNEL 27
	  GCANS,   0		       /GENERIC CODE PUT HERE
		   ZBLOCK 3
	  GCER,    0		       /ERROR INDICATOR

     Generic  codes  are  as  follows:  0 - No  interrupt;   1 - Controller
     error;  2,3 - Contact Interrupt Modules;  4 - Counter Module;  7 - A/D
     converter.


     4.9.6  EC   Enable Counter

	  Format:   EC
	  	    channel
	  	    initial value
	  	    reload value
	  	    event action
	  	    address

     Channel is the counter channel to be enabled,  initial  value  is  the
     first  value  to  be loaded into that channel, and reload value is the
     value with which to reload the channel  after  every  event.   If  the
     reload  value is 0, the counter is not reloaded.  The event action and
     address words specify what happens when the counter interrupts.  There
     are  three  mutually exclusive possibilities, indicated by setting the
     appropriate bit in the event action word as follows:

				      4-31

			      RTS/8 SYSTEM TASKS


	  Bit 0 = 1  -    Set  Event  Wait  Flag  of  this  job;   continue
			  execution  of  this  job  when  the event occurs.
			  Address word not used.

	  Bit 1 = 1  -    Run a task  that  sent  the  message;   run  task
			  specified  by  bits  4-11  of  event action word.
			  Address word not used.

	  Bit 2 = 1  -    DERAIL the  task  that  sent  the  message;   the
			  address word is only used by the DERAIL operation
			  and  specifies  the   address   of   the   DERAIL
			  subroutine.   The  subroutine must be in the same
			  field as the calling task.

	  Bit 3 = 1  -    Do action just once.  If bit  3  =  0,  specified
			  action  is performed after each interrupt.  Bit 3
			  indicates whether action  is  to  occur  once  or
			  repeatedly.

     Several enable counter examples follow:

	  ECEX1,    ZBLOCK 3
		    EC		       /ENABLE COUNTER
		    4		       /CHANNEL 4
		    7700	       /INITIAL VALUE OF 7700
		    7710	       /RESET TO 7710 AFTER EACH EVENT
		    4000	       /POST EVENT FLAG ON EVENT EVERY TIME
				       /IT OCCURS
		    0		       /UNUSED
	  ECER1,    0		       /ERROR INDICATOR

	  ECEX2,    ZBLOCK 3
		    EC		       /ENABLE COUNTER
		    4		       /CHANNEL 4
		    1205	       /INITIAL VALUE OF 1205
		    0		       /DON'T RESET
		    2016	       /RUN TASK 16 ON EVENT EVERY TIME IT
				       /OCCURS
		    0		       /UNUSED
	  ECER2,    0		       /ERROR INDICATOR

	  ECEX3,    ZBLOCK 3
		    EC		       /ENABLE COUNTER
		    5		       /CHANNEL 5
		    10		       /INITIAL VALUE OF 10
		    7700	       /RESET TO 7700
		    1015	       /DERAIL TO TASK 15 EVERY TIME IT
				       /OCCURS
		    5620	       /AT LOCATION 5620
	  ECER3,    0		       /ERROR INDICATOR






				      4-32

			      RTS/8 SYSTEM TASKS


     4.9.7  RC   Read Counter

	  Format:   RC
		    channel
		    result

     where channel is the counter channel whose  current  value  is  to  be
     read.  That value is placed in result.  For example:

	  RCEX,    ZBLOCK 3
		   RC		       /READ COUNTER
		   6		       /CHANNEL 6
	  RCANS,   0		       /VALUE OF CHANNEL 6 PUT HERE
		   ZBLOCK 3
	  RCER,    0		       /ERROR INDICATOR


     4.9.8  DC   Disable Counter

	  Format:   DC
		    channel

     where channel is the counter channel from which interrupts are  to  be
     ignored.  For example:

	  DCEX,   ZBLOCK 3
		  DC		       /DISABLE COUNTER
		  6		       /CHANNEL 6
	  DCER,   ZBLOCK 4
		  0		       /ERROR INDICATOR


     4.9.9  ECT   Enable Contacts

	  Format:   ECT
		    bit & channel
		    event action
		    address

     where the bit & channel word specifies the bit on the contact  channel
     from  which  to  enable interrupts.  Channel is specified in bits 4-11
     and the contact bit is packed in bits 0-3 as a value from 0-13(octal).

     Event action and address are specified in the same manner  as  in  the
     enable counter function.  For example:

	  ECTEX1,   ZBLOCK 3
		    ECT		       /ENABLE CONTACTS
		    5401	       /FROM BIT 13(OCTAL) OF CHANNEL 1
		    2013	       /RUN TASK 13 AFTER AN EVENT OCCURS
		    ZBLOCK 3
	  ECTElR,   0		       /ERROR INDICATOR
	  ECTEX2,   ZBLOCK 3



				      4-33

			      RTS/8 SYSTEM TASKS


		    ECT		       /ENABLE CONTACT
		    1001	       /FROM BIT 2 OF CHANNEL 1
		    4000	       /ON 1ST OCCURRENCE OF EVENT, POST
				       /EVENT FLAG
		    ZBLOCK 3
	  ECTE2R,   0		       /ERROR INDICATOR

     Twelve messages are required to enable the entire channel.


     4.9.10  CS   Change of State

	  Format:   CS
		    channel
		    result

     where channel is the contact channel whose  current  change  of  state
     value is to be placed in result.  For example:

	  COSEX,   ZBLOCK 3
		   CS		       /READ COS
		   1		       /CHANNEL 1
	  COSANS,  0		       /RESULT HERE
		   ZBLOCK 3
	  COSER,   0		       /ERROR INDICATOR


     4.9.11  DCT   Disable Contacts

	  Format:   DCT
		    bit & channel

     where bit & channel is specified as in enable contact.  That is,  bits
     0-3  specify  the bit (0 - 13 octal) and bits 4-11 specify the channel
     to be disabled.  For example:

	  DCTEX,   ZBLOCK 3
	 	   DCT		       /DISABLE CONTACTS
		   5401		       /FROM CHANNEL 1, BIT
				       /13(OCTAL)
		   ZBLOCK 4
	  DCTANS,  0		       /ERROR INDICATOR


     4.9.12  UDC/ICS Assembly Parameters

     The UDC/ICS handler has several assembly parameters that the user must
     specify to indicate the UDC/ICS configuration.  The number and address
     is required only for those modules that perform interrupts.  They  are
     as follows:

	  RINGBF	 Number of interrupts that can  be  stored  in  the
			 ring buffer.

	  NCNTR		 Number of counter modules.

				      4-34

			      RTS/8 SYSTEM TASKS


	  NCNTC		 Number of contact modules.

	  NAD		 Number of analog input converter modules.

	  FCTR		 Address of the first counter module.  The  modules
			 must be at contiguous module addresses.

	  FCT		 Address of the  first  contact  interrupt  module.
			 Interrupt  modules  must  be  at contiguous module
			 addresses.

	  FAD		 Address of the first A/D converter module.  Analog
			 input modules must be at contiguous module
			 addresses.

	  NMPLX		 Number of multiplexer modules per analog converter
			 (ICS only).

     These parameters are used mainly  to  specify  the  sizes  of  several
     tables  in  the  UDC/ICS  handler,  allocated  as 30 (octal) words per
     contact module, 3(octal) words/counter module, and 16(octal) words per
     analog module.  The UDC/ICS handler currently assumes that the handler
     and all its tables are entirely within the same data  field  (although
     the user could easily reprogram this).

     The user must keep in mind when establishing RINGBF size that  if  the
     buffer is full, UDC/ICS interrupts are disabled until there is room in
     the buffer.  Also, each interrupt requires two entries in the  buffer; 
     that is, the actual buffer size is 2 * RINGBF.


     4.9.13  UDC/ICS Error Conditions

     To indicate error conditions, the UDC/ICS handler places  a  value  in
     the tenth word of the task's message.  The values and meanings are:

	  Value				       Meaning

	    1		 Illegal generic code  for  specified  channel  and
			 operation
	    2		 Channel or subchannel value not valid
	    3		 Illegal function code
	    5		 UDC/ICS  control  not  responding  (power  off  or
			 hardware error)


     The user should initialize and check  the  error  word.   A  no  error
     condition puts a 0 in this location.

     Only errors encountered at noninterrupt  time  are  returned  in  this
     manner,  thus  they  may  also  indicate  a  faulty  UDC/ICS  hardware
     functional device.  Generic codes of 0 or 1 encountered  at  interrupt
     time are ignored.



				      4-35

			      RTS/8 SYSTEM TASKS


     4.10  CASSETTE HANDLER

     The  Cassette  Handler  (CSA)  allows  the  user  to  read  and  write
     variable-length  records  on  DEC  cassettes,  as  well  as to perform
     various special functions (such as rewind and  write  end-file).   One
     copy of the Cassette Handler can operate eight units.

     There are two general categories of cassette operation:

	  1.  Handler functions - read and write

	  2.  Utility functions - rewind, backspace file  gap,  write  file
	      gap, backspace block gap, and skip to file gap

     The user should call these functions in a  meaningful  sequence.   The
     first  word  of  the  message defines the cassette unit and either the
     handler or utility call.

     4.10.1  Handler Function

     The format of a message to the Cassette Handler when using  a  handler
     call is:

	  ZBLOCK 3
	  CALL + UNIT
	  RW + FIELD + NONSTORE
	  BUFADD
	  SIZE
	  STATUS

     For a handler function, the words after the RTS/8 message  header  are
     defined as follows:

	  Word 1 bit  0 = 0	 Utility call
		      0 = 1	 Handler call
		 bits 9-11	 Cassette unit

	  Word 2 bit  0 = 0	 Read
		      0 = 1	 Write
		 bits 6-8	 Field of buffer
		 bit  11	 Do not store data (applicable to read
				 only)

	  Word 3		 Buffer address
	  Word 4		 Record size in bits 4-11
	  Word 5		 Status return










				      4-36

			      RTS/8 SYSTEM TASKS


			---------------------------------------------------
			| 0 | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10 | 11 |
			---------------------------------------------------
			  ^				     \___________/
			  |					   |
     0: Handler call \____|					   |
     1: Utility call /						   |
								   |
     Unit _________________________________________________________|


		      Unit Word Format - Cassette Handler


			---------------------------------------------------
			| 0 | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10 | 11 |
			---------------------------------------------------
			  ^			 \_________/		^
			  |			      |			|
     0: Read  \___________|			      |			|
     1: Write /		  			      |			|
						      |			|
     Field ___________________________________________|			|
									|
     0: Read into memory \______________________________________________|
     1: Check data 	 /


		      Function Word Format - Handler Call


     Cassette conventions specify a record size of 200 bytes, but the  user
     can  use  any  size  up  to  377 (8 bits are transferred).  The buffer
     specified by the message cannot cross field boundaries.   For  a  read
     operation,  the  buffer  is optional (although its word in the message
     must be included), according to  bit  ll  of  word  2.   The  nonstore
     capability  can  be  used  for  advancing through a long file.  Word 5
     contains the contents of status register B, which is  defined  by  the
     bit setting as follows:

	  Bit    Meaning

	   4  = CRC /block error
	   5  = Timing
	   6  = EOT/BOT
	   7  = EOF
	   8  = Drive empty
	   9  = Read/write
	  10  = Write lockout
	  ll  = Ready






				      4-37

			      RTS/8 SYSTEM TASKS


			---------------------------------------------------
			| 0 | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10 | 11 |
			---------------------------------------------------
					  ^   ^   ^   ^   ^   ^    ^    ^
	CRC/block error __________________|   |   |   |   |   |    |    |
					      |   |   |   |   |    |    |
	Timing _______________________________|   |   |   |   |    |    |
						  |   |   |   |    |    |
	EOT/BOT __________________________________|   |   |   |    |    |
						      |   |   |    |    |
	EOF __________________________________________|   |   |    |    |
							  |   |    |    |
	Drive empty ______________________________________|   |    |    |
							      |    |    |
	Read/write ___________________________________________|	   |    |
								   |	|
	Write lookout _____________________________________________|    |
									|
	Ready __________________________________________________________|


		 Status Return Word Format - Cassette Handler

     At the end of each cassette operation, the user should examine Word  5
     to check for errors encountered.

     An example of a cassette handler message to write  l00  bytes  from  a
     buffer starting at 21200 to cassette unit 3 is as follows:

	  MSG1,	   ZBLOCK 3
		   4003		       /HANDLER OPERATION ON UNIT 3
		   4020		       /WRITE FROM FIELD 2 THE
		   1200		       /BUFFER AT 1200 WHICH IS
		   0100		       /100 BYTES LONG
		   0000		       /STATUS RETURN

     To read and not store 200 bytes from unit 2, the message is:

	  MSG2,	   ZBLOCK 3
		   4002		       /HANDLER OPERATION ON UNIT 2
		   0001		       /READ AND DON'T STORE
		   0000		       /UNUSED
		   0200		       /200 BYTES
		   0000		       /STATUS RETURN


     4.10.2  Utility Function

     The format of a message to the Cassette Handler when using  a  utility
     call is:

	  ZBLOCK 3
	  CALL+UNIT
	  FUNCTION
	  STATUS

				      4-38

			      RTS/8 SYSTEM TASKS


     For a utility function, the words after the RTS/8 message header are
     defined as follows:

	  Word 1   bit 0 = 0 		  Utility call
		   bit 0 = 1 		  Handler call
		   bits 9-11 		  Cassette unit

	  Word 2  (function in bits 6-8): 10 = Rewind
					  30 = Backspace file gap
					  40 = Write file gap
					  50 = Backspace block gap
					  70 = Skip to file gap

	  Word 3  Status return


			---------------------------------------------------
			| 0 | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10 | 11 |
			---------------------------------------------------
						 \_________/
						      |
	Function: ____________________________________|
	1 Rewind
	3 Backspace file gap
	4 Write file gap
	5 Backspace block gap
	7 Skip to file gap


		      Function Word Format - Utility Call


     For example, to request a rewind on unit 1, the message is:

	  MSG3,    ZBLOCK 3
		   0001 	       /UTILITY OPERATION ON UNIT 1
		   0010 	       /REWIND
		   0000 	       /STATUS RETURN

     If an error is encountered, the operation is retried 3  times,  except
     when  a  write  lock  out  is  placed on a write operation or an error
     occurs while reading CRC.

     The CAPS-8 User's Manual (DEC-8E-OCASA-A-D) is suggested  reading  for	 ____________________
     users who are unsure of cassette conventions.


     4.11  CASSETTE FILE SUPPORT HANDLER

     The Cassette File Support Handler (CSAF)  supports  the  DEC  standard
     cassette format and allows the calling task to look up and enter files
     on cassettes in that  format.   This  handler  requires  the  cassette
     handler (CSA) to perform the actual I/O operations involved.

     The cassette operations ENTER, LOOKUP and CLOSE are performed  by  the

				      4-39

			      RTS/8 SYSTEM TASKS


     Cassette  File Support Handler (CSAF) which in turn calls the cassette
     handler (CSA).  ENTER and LOOKUP require the user to  put  appropriate
     information  in a record header area with which CSAF performs the file
     operations.  The header area must be at least 40(octal) words long and
     cannot cross field boundaries.

     Word definitions for a CSAF message are as follows:

	  Word 1 bit  0 = 1 - ENTER
		 bit  1 = 1 - LOOKUP
		 bit  2 = 1 - CLOSE
		 bits 9-11  - unit

	  Word 2	      Address of header for ENTER and LOOKUP;
			      status return for CLOSE

	  Word 3	      Field of header for ENTER and LOOKUP (bits
			      6-8)

	  Word 4	      Status return for ENTER and LOOKUP

     In all cases, the status return is the contents of Status Register B.

			---------------------------------------------------
			| 0 | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10 | 11 |
			---------------------------------------------------
			 \_________/			     \___________/
			      |					   |
	Function: ____________|					   |
	1 Close							   |
	2 Lookup						   |
	4 Enter							   |
								   |
	Unit ______________________________________________________|


	       Unit Word Format - Cassette File Support Handler


     For ENTER and LOOKUP, the format of the header area must conform  with
     cassette  standards  (and  therefore is compatible with CAPS-8).  This
     format is as follows:

		       Byte		     Use

		       0-5	       Filename

		       6-10	       Filename extension

		       11	       File type
					     1 = ASCII
					     0 = undefined

		       12-13	       File record length.
					Currently word 12 must be 0

				      4-40

			      RTS/8 SYSTEM TASKS


		       14-15	       Unused

		       16-23	       Date (ASCII) specified as
					ddmmyy

		       24-35	       Unused

		       Reference is to 8-bit bytes,  one  per  word,  right
		       justified

     For an ENTER operation, if a file  with  the  name  specified  in  the
     header area is found on the specified unit, it is deleted.

     For a LOOKUP operation, the record  size  of  the  specified  file  is
     returned in location header+l3 (byte 13).  If the file is not found or
     if an error occurs, this location contains 0.

     The CLOSE operation is automatically followed by a REWIND.

     Examples of messages follow.

	  MSG4,	   ZBLOCK 3
		   4000		       /ENTER ON UNIT 0
		   6400		       /INFORMATION IN HEADER STARTING AT
				       /6400
		   0010		       /OF FIELD 1
		   0000		       /STATUS RETURN

	  MSG5,    ZBLOCK 3
		   1003		       /CLOSE ON UNIT 3
		   0000		       /STATUS RETURN


     4.12  PDP-8A NULL TASK

     The PDP-8A Null Task counts from  1  to 9999  in  decimal  in  the  AC
     display.   It  also  counts from 1 to 7777 in octal in the MQ display.
     The source which is called NULL8A, takes up  a  page.   The  user  can
     configure  the  null  task  into  an  RTS/8 system by inclusion in the
     parameter file of its task name and the statement

	  NULL8A = NTASKS+1


     4.13  KL8-A SUPPORT

     The KL8-A is a 4-serial line asynchronous multiplexer for the  PDP-8/A
     that has three lines with partial modem control and one line with full
     modem control.  KL8-A support is available to the RTS/8 Executive, the
     TTY  task,  and the OS/8 Support Task.  To use KL8-A support, the user
     should perform the procedures that  are  described  in  the  following
     sections.




				      4-41

			      RTS/8 SYSTEM TASKS


     4.13.1  Executive KL8-A Support

     The symbol KL8A in the parameter file is set to a value equal  to  the
     number  of  KL8-A  units  being employed by the user.  If one KL8-A is
     being used, then KL8A=1 is specified.

     If the symbol 'KL8A' is set to 0 or undefined in the  parameter  file,
     no KL8-A support will be provided by RTS/8.

     KL8-A support is provided by the RTS/8  Executive.   The  source  file
     KL8ASR.PA must be assembled as follows:

     .PAL KL8ASR<PARAM,KL8ASR

     The parameters in the parameter file that relate to KL8-A service  are
     as follows:

	  KL8A = 0 or undefined    means that no KL8-A service is desired.

	       = n		   means support for n  physical  lines  is
				   desired.   Each  physical KL8-A provides
				   four lines.

	  KL8ADV =		   Device  code  for   the   first   KL8-A.
				   Default  is  40.   Each  KL8-A  uses two
				   consecutive device codes (e.g.,  40  and
				   41).  If multiple KL8-A's are used, they
				   should have consecutive device codes.

	  KL8ACT =		   Specifies  page  for  start   of   KL8-A
				   connect  routine.   Default  is 7400 (if
				   KL8A = 1).  The  KL8-A  connect  routine
				   must  be  located  in  field  0.   It is
				   1-page long for one KL8-A  and  grows  a
				   page  for every three additional KL8-A's
				   used (or  part  thereof).   The  default
				   value of this parameter is such that the
				   KL8-A support  routine  gets  jammed  up
				   against  the  end  of field 0, ending at
				   location 7577.


     4.13.2  TTY Task KL8-A Support

     KL8-A support in the TTY task is initiated by setting symbol  KL8A  in
     the  parameter  file  to  nonzero.   Then the KL8-A line to be used is
     specified in place of the terminal IOT  device  code  plus  100.   For
     example, if the TTY task is to control line 3 of a KL8-A,

	  TTDEV = KL8ALINE+3

     is specified in the parameter file.  (The symbol KL8ALINE  is  defined
     to  have  the value 100 in the parameter file.) If more than one KL8-A
     interface is used, the lines are numbered consecutively beginning with
     O and continuing across interfaces.  Thus, KL8-A logical line number 5

				      4-42

			      RTS/8 SYSTEM TASKS


     actually is physical line number 1  of  the  second  KL8-A  interface.
     Physical lines are numbered from 0 to 3.

     KL8-A support requires additional memory  in  field  O  for  Executive
     Support but does not increase the size of the TTY task.  KL8-A support
     is included in both the old (2-page) and new (3-page) TTY task.


     4.13.3  KL8-A Support for the OS/8 Support Task

     KL8-A support for OS/8 is similar to that described for the  TTY task.
     However,  the  following procedure is used.  First, the symbol KL8A is
     set to nonzero in the parameter file.  Then, the particular KL8-A line
     is  specified  by  using a number of the form lOO+line in place of the
     device code, where "line" is the line number of the KL8-A that is OS/8
     being  used.  The symbol KL8ALINE is conveniently defined as being 100
     in the parameter file.  For OS/8 support, the parameter

	  OSTTDV = KL8ALINE+2

     specifies that terminal output goes to line 2 of the KL8-A.  When more
     than  one  KL8-A is used, the lines should be numbered successively as
     described for the TTY task support in Section 4.13.2.


     4.13.4  KL8-A Support for a User Task

     The KL8-A support in the Executive allows a user to program the  KL8-A
     in a manner similar to the KL8-J.

     First, the user task must insert the KL8-A  into  the  interrupt  skip
     chain  and provide a keyboard and printer interrupt routine to service
     the line he wishes to use.  This is accomplished via the following
     code:

	  CDF CUR
	  CIF 0
	  IOF
	  TAD (LINE^4
	  JMS I (KL8ACT
	  KEYBD INTERRUPT ROUTINE
	  PRINTER INTERRUPT ROUTINE

     where LINE is the line  number  of  the  KL8-A  desired.   KL8-A  line
     numbers  are consecutive, begin at 0, and may span across KL8-As.  The
     KL8-A line number is actually of the form 4a+b where a is  the  number
     of  the  KL8-A  (0,1,2...)  and  b  is the physical line number of the
     specific KL8-A (0-3).

     Second, the user must define the instruction corresponding to the  TLS
     instruction  that  will  be  used  when  outputting to the KL8-A line.
     For example, if the device code for the KL8-A is  40,  then  the  user
     will probably want an instruction such as

	  TLSX=6404

				      4-43

			      RTS/8 SYSTEM TASKS


     in his task.
 
     Normally, a program would contain  the  following  code  to  output  a
     character:

	  TAD char
	  TLS

     When using a KL8-A, the task would first connect up the KL8-A  support
     by  calling  KL8ACT.   Then, to output a character, the following code
     would be used:

	  TAD line ^400
	  TAD char
	  TLSX

     The AC is not cleared by the TLSX.


     4.14  EXIT TASK

     The EXIT Task is not required for RTS/8 operation.  If  this  task  is
     included  in  a  system,  it is run by the MCR EXIT command.  The EXIT
     task performs the same functions as those performed by  the  MCR  EXIT
     command, that is, it waits for any pending operations to be completed,
     then turns off interrupts and returns to the  OS/8  operating  system.
     In  addition,  the  EXIT Task allows a user task to request additional
     special exit processing just prior to shutting down  RTS/8.   This  is
     done  by  having  the user task send a message to the EXIT Task.  This
     message contains a single word.  This word is the address of a routine
     (in  the same field as the message) that will be called (via a JMS) at
     the time of the exit.  When the  MCR  EXIT  command  is  typed,  these
     routines  will be called and executed in the order that they were sent
     to the EXIT Task.


				      NOTE

		    Any message sent to the EXIT Task will
		    not  get posted.  Also, do not use the
		    MCR REquest command to  run  the  EXIT
		    Task.














				      4-44






				   CHAPTER 5

			    MONITOR CONSOLE ROUTINE

     The Monitor Console Routine (MCR) provides functions that the user can
     request  from  the console terminal to control, inspect, and debug (to
     some extent) his system.

     The MCR indicates that it is active and ready to  accept  commands  by
     printing the prompting character > on the system console terminal.  An
     MCR command consists of a  command  word  followed  by  arguments  and
     terminated  by either a carriage return or an ALTMODE.  Only the first
     two characters of the command are  significant  except  for  the  EXIT
     command.   Commands  can  be  a  maximum  of 40 characters long.  If a
     carriage return terminates the command line, the MCR  returns  to  the
     terminal  for  another command when it finishes processing the current
     command.  If an ALTMODE terminates the  command  line,  the  MCR  puts
     itself  in  a wait state when it finishes processing the command.  The
     MCR is brought out of this wait state by typing  ^C  (CTRL C)  on  the
     console terminal.

     When the MCR prompts with its > and is waiting  for  input,  no  other
     RTS/8  task  can use the terminal.  Therefore, if the terminal is used
     for something other than an  exclusive  MCR  terminal  (for  instance,
     error  logging), type C, type the MCR command and terminate it with an
     ALTMODE character.  This procedure prevents the MCR from tying up  the
     terminal.


     5.1  MCR COMMAND ARGUMENTS

     Certain syntactic constructions are used as arguments to  several  MCR
     commands.  The definitions of these arguments follow.

			      A single comma or a single space may be  used
			      interchangeably  to separate arguments to MCR
			      commands.

	      Task-ID	      A Task-ID is either  an  octal  number  or  a
			      name.   If  it is a number, it represents the
			      internal RTS/8 Task Number.  This number also
			      designates  the priority of a task.  If it is
			      a name, the first 4 characters  of  the  name
			      are looked up in the MCR's Task Name table to
			      produce a Task Number.

	      Time-of-day     A time-of-day is of the form hh:mm, where  hh
			      represents   hours   past   midnight  and  mm
			      represents minutes past hh:00.

	      Address	      An Address is an octal number  from  1  to  5
			      digits that represents a PDP-8 memory



				      5-1  

			    MONITOR CONSOLE ROUTINE


			      address.  If the address is  less  than  five
			      digits  long  it  is  assumed  the high order
			      digits are 0.

	      Word	      A Word is an octal number from 1 to 4  digits
			      long.


     5.2  MCR COMMANDS

     In the MCR command descriptions that follow, the  significant  portion
     of  the  command word is capitalized.  Optional arguments are enclosed
     in square brackets ([])  and  choices  are  embedded  in  parentheses,
     separated  by  exclamation points (!).  Commands preceded by asterisks
     (*) are not present if the user did not define the symbol CLOCK in the
     RTS/8  parameter  file (indicating that a clock is not in the system),
     or if the symbol MCRCLK is set to 0 (in order to shorten the MCR  code
     length).
     
     
     5.2.1  * DAte [mm/dd/yyyy [,Time-of-day]]
     
     The date mm/dd/yyyy, if specified, becomes the system date.   For  the
     year  portion  of  the  date, only the last digit is significant;  the
     others are ignored since  197  assumed.   The  RTS/8  system  date  is
     automatically  incremented  at midnight, but all months are treated as
     being 31 days in length.  The second argument, if  specified,  is  set
     equal  to  the system time-of-day.  If no arguments are specified, the
     current system date is printed on the console  terminal  in  the  form
     mm/dd/yy.

	  >DATE 07/31/76
	  >DATE
	  07/31/76
     
     
     5.2.2  * TIme [Time-of-day]
     
     If  a  Time-of-day  command  is  specified,  it  becomes  the   system
     time-of-day.    If   no  argument  is  specified  the  current  system
     time-of-day is printed out on the console terminal in the form hh:mm.

	  >TIME 14:00
	  >TIME
	  14:00
     
     
     5.2.3  NAme Task-ID,Newname
     
     The character string Newname becomes the  new  name  of  the  task  if
     specified  by  this  command.   The  old name of that task (if any) is
     lost.  Newname can be any length, but only the first 4 characters  are
     stored.   Newname should not be the name of any other task or an error
     message results.


     				      5-2

			    MONITOR CONSOLE ROUTINE


     Examples:
     
	  >NAME 7 REPORT
     
     Task number 7 is given the name REPO.

	  >NAME REPORT,FOO

     Task number 7, which is known as REPO, is now known as FOO.


				     NOTE

		    The  system  initializes  the  MCR  name
		    table  at  assembly  time to contain the
		    names of any DEC-supplied tasks that are
		    listed  in  the parameter file (e.g., if
		    the  symbol  CLOCK  is  defined  in  the
		    parameter file as CLOCK=2, task number 2
		    gets the name  CLCK).   By  editing  the
		    file  MCR.PA after the label NMTBL, user
		    task names can be  permanently  included
		    by modifying the MCR name table.


     5.2.4  REquest Task-ID [,(@Time-of-day ! Interval)[,Interval]]

     The REquest Task-ID command requests a task  to  run  immediately  (if
     only  Task-ID  is  specified),  at  a given time-of-day, after a given
     interval, or at a given interval.

     Interval is of the form:

	       nH 	 n hours
	       nM 	 n minutes
	       nS 	 n seconds
	       nT 	 n system ticks

     Requesting a task clears the RUNWT bit in the Task Flags  Table  entry
     for  that  task.  The interval, given in the third argument, specifies
     the period at which the task is rerun.  If the parameter CLOCK in  the
     RTS/8 parameter file is not defined, the second and third arguments of
     this command are ignored and the given task runs immediately.  In  the
     examples given below, three different formats are used for the REquest
     command, but only the first two characters are significant except when
     using the EXIT command.
     
     Examples:
     
	  >REQUEST X
     
     runs task X immediately.
     
	  >RE FOO,@2:00


				      5-3

			    MONITOR CONSOLE ROUTINE


     runs task FOO at 2:00 am (if it is after 2 am, FOO will  run  tomorrow
     at 2 am).
     
	  >RE 5,10M,5M

     runs task number 5  ten  minutes  from  now  and  every  five  minutes
     thereafter.
     
	  >REQ HIPR,1T,6T

     On a machine with a 60 Hz clock,  this  command  runs  the  task  HIPR
     immediately  (that  is, .016 seconds from now, and 10 times per second
     thereafter).

				     NOTE
		    If, at the time the REquest  command  is
		    executed,  (which  may  be several hours
		    after it is typed in) the task specified
		    by  Task-ID  does not have the RUNWT bit
		    set in its Task Flags Table entry,  then
		    the  REquest  command  is  a  no-op  (no
		    operation), that is, the command has  no
		    effect.   Similarly,  the  task will not
		    run  upon  execution  of   the   REquest
		    command  if it had other bits set beside
		    RUNWT; the task will run only  when  the
		    other blocking bits are cleared.


     5.2.5  STop Task-ID

     The STop Task-ID command suspends execution of the task  specified  by
     Task-ID  by turning the RUNWT bit on in the Task Flags Table entry for
     that task.  A task that has been stopped can be restarted by using the
     REquest  MCR  command (in this instance it is easier to think of it as
     the REsume MCR command).


     5.2.6  DIsable Task-ID

     The DIsable Task-ID command disables future execution of the specified
     task  by  setting  the ENABWT bit on in the Task Flags Table entry for
     that task.


     5.2.7  ENable Task-ID

     The ENable Task-ID command clears the ENABWT bit  in  the  Task  Flags
     Table  entry  for the specified task, thus enabling it to run.  If the
     ENABWT bit was not set, the command is a no-op.


     5.2.8  * CAncel Task-ID

     The CAncel Task-ID command cancels any clock queue  entries  involving

				      5-4

			    MONITOR CONSOLE ROUTINE


     the  task  specified  by Task-ID.  This includes l)any entries made by
     the MCR (from previous timed Request  commands),  2)entries  involving
     the  specified  task  made  by  other tasks (e.g., a timed DERAIL) and
     3)entries made by the specified task involving itself (e.g.,  a  timed
     POST).   In  the  case of the timed POST, the event flag is not POSTed
     and the task may hang up forever waiting for it.


     5.2.9  SYstat [Task-ID]

     The SYstat command, depending on whether  an  argument  is  specified,
     prints  either  a  general  system status report or a status report in
     greater detail on a single task.  If no  argument  is  specified,  the
     SYstat command prints a system status report.  Each line of the report
     describes an existent task in the system.  For each  task  the  report
     prints  the  task number/priority, task name (if it has one), and what
     blocking bits are on in its Task Flags Table entry.  Each blocking bit
     is  printed as a one-letter code, preceded by a space.  The one letter
     codes and their meanings are:

	 E Waiting for event flag
	 M Waiting for a message
	 O Waiting for an event flag or a message
	 R Waiting to be REquested or RUN
	 S Waiting to be swapped in
	 D Disabled
	 U USERWT bit set
	 N Nonresident wait

     In addition, an asterisk printed at the end of the line means the task
     has messages waiting in its input queue.

     A more detailed  status  report  on  a  single  task  is  obtained  by
     specifying  the  Task-ID  of  that  task  as an argument to the SYstat
     command.  The detailed report contains  all  the  information  in  the
     general status report, followed by five octal words:

	  WORD 1  The location of the Task State Table
		  entry containing words 2-5; this
	          word is followed by a colon
	  WORD 2  Task Link in sign bit, IF in bits 6-8,
		  DF in bits 9-11 (PDP-8/E and 8/A Flags
		  Register)
	  WORD 3 Task PC
	  WORD 4 Task AC
	  WORD 5 Task MQ
     
     Examples:

     A general SYstat command might produce  the  following  sample  output
     line:

	  13 CARD E *

     This line means task number 13, named CARD, is in Event Flag Wait  and

				      5-5

			    MONITOR CONSOLE ROUTINE


     has input messages pending.  The command:

	  >SYSTAT CARD

     might produce the single line:

	  13 CARD E * 1320: 0022 1741 0000 2525

     This line indicates that CARD is stopped at location 21741 with its AC
     and Link zero and 2525 in its MQ.

     The user can leave the SYstat facility out  of  the  MCR  assembly  by
     setting  the system parameter MCRSYS to 0 in the RTS/8 parameter file.
     Leaving it out saves one page of code.


     5.2.10  OPen Address [,Count]

     The OPen  Address  command  displays  the  Count  locations  in  octal
     starting at Address on the console terminal in the form:

	  lllll/ cccc

     The range of locations displayed may cross a field boundary.  If Count
     is not specified, it is assumed to be 1.


     5.2.11  EXamine Address [,Count]

     The EXamine command is identical to the OPen command.


     5.2.12  DEposit Address,Word [,Word] [,Word]....

     The DEposit Address command deposits the second through nth  arquments
     into  core  at  consecutive  locations starting at Address.  As in the
     OPen Address command, field boundaries can be crossed.   For  example,
     
	  >DEPOSIT 26132 7700,7200,50
     
     deposits 7700 into location 26132, 7200 into location 26133, and  0050
     into  location  26134.   Note  that the command to the MCR can contain
     only 40 characters, and any characters beyond this limit are lost;  an
     error message is generated for commands larger than 40 characters, hut
     part of the deposit will have been done.
     
     
     5.2.13  POst Address
     
     The POst Address  command  POSTs  the  Event  Flag  at  the  specified
     address.   This  command is useful when the user debugs a system since
     it can simulate the effects of nonexistent tasks or devices.
     


     
				      5-6

			    MONITOR CONSOLE ROUTINE


     5.2.14  EXIT
     
     The EXIT command causes the MCR to terminate  RTS/8  execution  (after
     pausing  approximately  one  second  for  pending I/O to complete) and
     returns to the OS/8 monitor at location 07600.  The user must type out
     this  command completely or it will be regarded as an EXamine command.
     If the Exit Task is included in the system, this command runs the Exit
     Task before going to 7600.
     
     
     5.3  MCR ERRORS
     
     The MCR checks each command line for errors  and,  if  one  is  found,
     issues one of the following messages and reprompts on the terminal for
     a corrected command:
     
	  BAD CHAR Character was not expected where it occurred

	  BAD NUMBER Number is out of legal range or is missing

	  BAD DELIM No space or comma is where one was expected

	  BAD NAME Task name is not in name table or duplicate
     
     
     5.4  NONRESIDENT MCR
     
     The MCR has a resident portion and a nonresident  portion.   The  user
     can  make  the  MCR nonresident by defining the appropriate symbols in
     the parameter file.  If the symbols are undefined, the MCR runs  as  a
     completely-resident task.
     
     The MCR is made nonresident by  defining  the  symbol  MCRPRT  in  the
     parameter  file.   This  symbol  is set to the partition number of the
     partition into which it is desired to  swap  the  MCR.   For  example,
     
	  MCRPRT=2
     
     means that the MCR will swap into partition 2.

     The procedure for specifying this partition is  described  in  Section
     7.4.   The  partition  size  must be big enough to hold the entire MCR
     except for one page.  The length of the MCR varies depending on  other
     parameters  and  the  number  of  tasks.   The  size of the MCR can be
     determined  from  the  MCR  component  size  table  in   Appendix   B.
     Regardless  of the size of the MCR, the first page is always resident,
     while the remainder  is  the  nonresident  portion.   The  nonresident
     portion of the MCR must start at a location that is a multiple of 400.
     Therefore, the  MCR  resident  portion  must  start  at  an  odd-block
     boundary.   The MCR can be made writeable, but not checkpointable.  It
     frees its partition whenever it is using the terminal or while waiting
     for a CTRL/C.
     
     The symbol MCRORG is used to specify the starting location of the MCR.
     If this symbol is not defined in the parameter file, RTS/8 locates the

				      5-7

			    MONITOR CONSOLE ROUTINE


     MCR so that it fits up against the end of the field  in  which  it  is
     located.   If  MCRORG  is  defined,  it  specifies the initial loading
     address of the MCR.  For example,
     
	  MCRORG=2400
     
     means that the MCR begins loading at location 2400.
     
     The user can leave out the clock  functions  in  the  MCR  by  setting
     MCRCLK to 0.














































				      5-8






				   CHAPTER 6

		    ASSEMBLING AND LOADING TASKS FOR RTS/8

     The user assembles RTS/8 tasks with parameter files,  using  the  OS/8
     PAL8  assembler.   RTS/8  parameter files are all edited versions of a
     master parameter file (PARAM.PA) that is included in  the  distributed
     sources.  Appendix A lists the RTS/8 source files.  All definitions in
     the master file which are to be supplied by the user are left blank in
     the file.  For example, a sample line in the file is:

	  PDP8E= /1 IF PDP 8/E OR PDP 8/A, ELSE 0

     If this parameter is set to 1, the specified machine is a PDP-8/E or a
     PDP-8/A.  If either machine is not used, this parameter is set to 0.

     Thus, a unique parameter file is  created  for  the  particular  RTS/8
     environment,  where  environment  is  a  combination  of the available
     hardware and the set of tasks being run.

     The structure of the parameter file is discussed in the next  section.
     Other  sections  in  this  chapter describe 1) the OS/8 BITMAP program
     which allows the user to construct a map showing the memory  locations
     used  by  given  binary  files, 2) a sample RTS/8 program 3) a general
     procedure for creating an RTS/8 system, and 4) a listing of parameters
     and their functions that affect the individual RTS/8 system tasks.


     6.1  PARAMETER FILE STRUCTURE

     The parameter file contains the parameters that the user  must  define
     to  specify a particular RTS/8 system configuration.  A parameter file
     that has been modified for  the  demonstration  program  is  shown  in
     Section   8.1.  This  file  also  contains  user-defined  symbols  for
     DECNET/8.  For further information on  DECNET/8,  see  RTS/8  DECNET/8							    _______________
     Programmer's Guide and Reference Manual (DEC-08-LDPRA-A-D).     _______________________________________

     The parameter file is divided into the following five sections.  These
     sections are labeled as follows:

	  1.  Executive Specifications

	  2.  Task Definitions

	  3.  System Task Specifications

	  4.  System Wide Definitions

	  5.  Task Setup






				      6-1

		    ASSEMBLING AND LOADING TASKS FOR RTS/8


     6.1.1  Executive Specifications

     The parameters in the  Executive  Specification  section  control  the
     assembly  of  the  Executive, and therefore are essential to the RTS/8
     system.  The parameters in this  section  and  their  meaning  are  as
     follows:
     
	  Symbol			       Meaning
     
	  PDP8E		 Set to 1 if PDP-8/E, PDP-8F, PDP-8M or PDP-8/A  is
			 the  machine being used;  if not, this symbol must
			 be set to 0.

	  PDP12		 Set to 1 if PDP12 is the machine being used;  if 0
			 or undefined, the PDP-12 is not being used.

	  EAE		 Set to 1 if the system should save contents of the
			 MQ during an interrupt or task switching.

	  PWRFAL	 Set to 1 if power fail/restart is enabled  in  the
			 hardware.

	  KL8A		 Set to a nonzero if KL8-A support routines  should
			 be loaded into system.

	  HGHFLD	 Set to a value designating the highest field used;
			 for  example,  HGHFLD  = 30 specifies field 3 when
			 using a machine with 16K core memory.

	  NTASKS	 Set to an octal value  that  specifies  the  total
			 possible  number  of tasks in the system.  It also
			 represents the highest number that can be assigned
			 to  any task in the system.  Not all possible task
			 numbers need be assigned to  actual  tasks;   this
			 symbol merely sets the length of system tables.

	  CHECKP	 Set   to   1   if   any   nonresident   task    is
			 checkpointable.

	  PARTNS	 Set to the number of memory  partitions  allocated
			 in the system.  Set to zero if there are no memory
			 partitions defined in the  system.   For  example,
			 PARTNS  =  2  indicates  that there are two memory
			 partitions defined, that is,  partition  number  0
			 and partition number 1.


     6.1.2  Task Definitions

     The Task Definitions section defines symbolic names  for  the  various
     system  tasks.  The names of all system tasks which are to be included
     in the system are defined here.  Any system task not  included  should
     have  the  line  which  defines it deleted from this section.  Perform
     this deletion by inserting a slash (/) character at the  beginning  of
     the line, which makes the entire line a comment.  Symbolic definitions

				      6-2

		    ASSEMBLING AND LOADING TASKS FOR RTS/8


     of the user's own tasks can be added to this  section.   The  user  is
     reminded  that  the assignment of task numbers in octal indicates task
     priority, that is, the lower the number, the higher  the  priority  of
     the task.
     
     The Task Definitions section, as it initially appears to the user,  is
     shown below.

     /COMMON TASK NUMBERS - EDITED BY USER
     /IT IS ADVISABLE TO DEFINE ALL TASKS HERE.  NAMES GIVEN BELOW
     /ARE USED BY SOME SYSTEM TASKS AND SHOULD REMAIN COMMENTED OUT
     /IF THE CORRESPONDING TASK IS NOT INCLUDED IN THE SYSTEM

     /PWRF=	     /POWER FAIL HANDLING TASK
     /CLOCK=	     /CLOCK HANDLER - SHOULD BE HIGH PRIORITY
     /SWAPPER=	     /NONRESIDENT TASK SWAPPER TASK
     /TTY=	     /TELETYPE DRIVER TASK
     /LPT=	     /LINE PRINTER DRIVER TASK
     /MCR=	     /MONITOR CONSOLE ROUTINE
     /DTA=	     /DECTAPE DRIVER TASK
     /LTA=	     /LINCTAPE DRIVER TASK
     /RK8=	     /RK8 OR RK8E DISK DRIVER TASK
     /RF08=	     /RF08 DISK DRIVER TASK
     /DF32=	     /DF32 DISK DRIVER TASK
     /CSA=	     /CASSETTE DRIVER TASK
     /CSAF=	     /CASSETTE FILE SUPPORT TASK
     /UDC=	     /UNIVERSAL DIGITAL CONTROLLER TASK
     /RX8A=	     /FIRST FLOPPY CONTROLLER
     /RX8B=	     /SECOND FLOPPY CONTROLLER
     /RX8C=	     /THIRD FLOPPY CONTROLLER
     /RX8D=	     /FOURTH FLOPPY CONTROLLER
     /OS8=   NTASKS  /OS/8 SUPPORT - NORMALLY LOWEST PRIORITY
     /OS8F=	     /OS/8 FILE SUPPORT
     /DDCMP=	     /DDCMP TASK FOR DECNET
     /NSP=	     /NETWORK SERVICES PROTOCOL TASK
     /NIP=	     /NETWORK INFORMATION PROGRAM
     /TLK=	     /NETWORK TERMINAL COMMUNICATIONS TASK TRANSMITTER
     /LSN=	     /NETWORK TERMINAL COMMUNICATIONS TASK RECEIVER
     /NULL8A=	     /NULL JOB FOR PDP-8/A
     /EXIT=	     /EXIT TASK
     /DKC8A=	     /AUXILIARY DKC8A HANDLER

     This section of the parameter file is shown in Section  8.1  after  it
     has  been  modified  for the demonstration program.  It also shows the
     addition of the  two  nonresident  tasks  used  in  the  demonstration
     program.


     6.1.3  System Task Specifications

     The parameters in the System Task Specifications section  control  the
     assemblies  of  the various RTS/8 system tasks.  The set of parameters
     controlling a specific task are all grouped  to-tether  and  assembled
     conditionally   only  if  that  task  name  is  defined  in  the  Task
     Definitions section  of  the  parameter  file.   The  user  edits  the

				      6-3

		    ASSEMBLING AND LOADING TASKS FOR RTS/8
     
     
     parameters  in  this  section.   The parameters and their meanings are
     listed in Section 6.4.


     6.1.4  System Wide Definitions

     The System Wide Definitions section includes the  definitions  of  the
     symbols that RTS/8 uses to describe Executive Requests and Task Status
     Flag bits.  It also contains useful definitions  such  as  instruction
     equivalences,  monitor  call  values,  UDC/ICS  functional  values and
     system locations.  The user should not alter this section.
     

     6.1.5  Task Setup

     The Task Setup section uses five symbols that the user defines in  the
     body  of this task to initialize the RTS/8 table entries needed to put
     that task in the system.  These five  symbols  and  their  definitions
     are:

     	       TASK	 Defines the task number of the task by a statement
     			 of the form:

     			      TASK=symbol

     			 where "symbol" is the symbolic name for  the  task
     			 that  the  user has defined in the RTS/8 parameter
			 file.

	       CUR	 Defines the field of the task's  starting  address
			 in bits 6-8 (e.g., CUR=10).


						NOTE

			     The user must place  the  task's  starting
			     code  in the field specified by CUR.  This
			     is  done  by  using  the  PAL8   assembler
			     pseudo-op FIELD.

			     For  example,  FIELD  CUR%10  places   the
			     task's starting code in field 1.


	       START	 Defines   the   task's   starting   address   (not
			 necessarily the lowest address in the task)

	       INIWT	 Defines the initial wait bits in  the  Task  Flags
			 Table entry for this task.  For example, INIWT = 0
			 means the task is runnable when the system  starts
			 up;   INIWT  =  RUNWT  (1000 octal) specifies that
			 this task is not runnable initially and  is  in  a
			 Run  Wait  condition.   This task becomes runnable
			 when another task issues a  RUN  ER  or  when  the
			 operator  types  a Request command to the MCR.  If

				      6-4

		    ASSEMBLING AND LOADING TASKS FOR RTS/8


			 INIWT is  undefined,  the  task  starts  up  being
			 runnable.

	       VERS	 Defines the task's  version  number,  this  is  an
			 optional  parameter.   By  convention,  the task's
			 version  number  becomes  the  task's  initial  MQ
			 value.

     The  user  can  define  up  to  three  tasks  in  one  assembly.   The
     corresponding  symbols  for  the other tasks are TASK2 and TASK3, CUR2
     and CUR3, etc.  The task setup section places its data into the  RTS/8
     tables  by  origining into them;  no executable code is generated.  If
     desired, more than three tasks can  be  created  in  one  assembly  by
     adding  the  code  for any additional tasks at the end of the PARAM.PA
     file.  It should be noted  that  only  one  task  is  defined  in  the
     demonstration program in Chapter 8.
     
     
     6.2  CREATING AN RTS/8 SYSTEM

     An RTS/8 System can be created by using the general procedure that  is
     described in this section.  It is assumed that the user has physically
     mounted a copy of the distribution medium, and  has  bootstrapped  the
     development  system.   Although  nonresident tasks are treated in this
     procedure, greater detail on employing nonresident tasks is  given  in
     Chapter 7.

     The general procedure for creating an RTS/8 System is as follows:

	  1.  Layout on paper the system and user tasks  required  for  the
	      particular  RTS/8  configuration to be employed.  Utilize the
	      tables and memory map given in Appendix B that show the RTS/8
	      components,   their  sizes,  and  their  default  origins  to
	      determine where the tasks are to be loaded into memory.

	  2.  Assign task names and task priorities.  If nonresident  tasks
	      are  used, assign the Swapper Task a higher priority than any
	      of the nonresident tasks.  Remember that the lower the  value
	      assigned to a task, the higher its priority.

	  3.  When large programs are involved, a documentation file should
	      be  created  as a user convenience to maintain a directory of
	      the system configuration.  This file can contain  information
	      such  as  the  tasks employed in the system, task names, task
	      priorities, and control files.

          4.  Obtain a listing of the  master  parameter  file  (PARAM.PA).
	      Use the OS/8 command

		   .LIST PARAM.PA

	      to get a listing from a line printer, or
     
     		   .TYPE PARAM.PA


				      6-5

		    ASSEMBLING AND LOADING TASKS FOR RTS/8


	      to get a listing from a terminal.

	  5.  Use an editor (EDIT or TECO  under  OS/8)  to  establish  the
	      values  of  the  parameters in the parameter file (PARAM.PA).
	      The structure of the parameter file is described  in  Section
	      6.1, and the parameters affecting the individual RTS/8 system
	      tasks are described in Section 6.6.

	      PARAM.PA should be read in as an input file, edited, and then
	      renamed  as  an  output  file.   This procedure maintains the
	      integrity of DIGITAL-supplied sources.

	  6.  Create and edit any control files that are used (See  Section
	      6.5).

	  7.  Assemble the tasks with the  parameter  file  after  all  the
	      required parameters are defined.  This can be accomplished by
	      individually assembling each task with the parameter file  as
	      follows:

		   .PAL RTS8<PARAM,RTS8

	      or

		   .PAL PARAM-NB, RTS8
     
	      The CCL option -NB indicates that a binary file should not be
	      created.  Shown is the assembly of the RTS/8 Executive.  This
	      has to be done for every task that is included in the system.
	      Each  control file used must also be assembled.  Assemble the
	      control file with the parameter  file,  placing  the  control
	      file  between  the  parameter file and the required module as
	      follows:

		   .PAL TTYl<PARAM,TTYCFl,TTY

	      An alternate and more efficient method that can  be  employed
	      is  to  use  a  Batch  stream.   The  assembly, load and save
	      commands for the system are generated as a  Batch  job.   The
	      OS/8  SUBMIT command is then used to run BATCH which will use
	      the Batch job commands as  inputs  and  execute  them.   This
	      method can also be used for installing nonresident tasks into
	      the system.

	      The assembly of each task, preceded by the parameter file, is
	      required  because  there  is  no linking loader function with
	      RTS/8.  The assembly process creates binary  files  from  the
	      sources  that  are  ready  to  be loaded and run.  Each RTS/8
	      system task contains assembler code  that  assembles  it  for
	      loading  into  a  specific area of core memory.  The user can
	      assemble tasks to load into  areas  of  memory  not  used  by
	      system  tasks,  or  edit  the  system  tasks for loading into
	      specific areas.  Page 0  locations  and  autoindex  registers
	      used  by  system  tasks  can also be redefined by editing the
	      affected tasks.

				      6-6

		    ASSEMBLING AND LOADING TASKS FOR RTS/8


          8.  Obtain a bitmap of RTS/8 tasks to determine if  two  or  more
	      tasks are erroneously loaded into the same memory area or use
	      the same page 0 locations (See section 6.3).

	  9.  Load the system after all the required tasks  are  assembled.
	      All  required system tasks, user tasks, and control files can
	      be loaded at one time as follows:

		   .LOAD RTS8,CLOCK,TTY,MCR,UT1,UT2

	      The RTS/8 Executive Task always must be loaded first.   Also,
	      nonresident  tasks are included in this step in order to load
	      their resident portions and executive table entries.

	  10. Save the system after it is loaded  by  using  the  following
	      command:

	           .SAVE SYS filename

	      If the system is saved, the user does not have to rebuild  it
	      each time it is needed.

	  11. When using  nonresident  tasks,  create  a  SAVE  image  file
	      (nonresident  disk  image) for each nonresident task from its
	      binary file as follows:

		   .LOAD TASKX

	      Then save the nonresident portion of the  task  on  the  swap
	      device:

		   .SAVE DSK TASKX N1-N2

	      where DSK is the swap device, N1 is the lowest address in the
	      partition, and N2 is the highest address in the partition.

	  12. Start the system by using the following command:

		   .R filename

	      The following is applicable  when  using  nonresident  tasks.
	      When  the  system  starts, it calls the OS/8 command decoder,
	      which types an asterisk on the  console  terminal.   At  this
	      time,  initialize  the block address of each nonresident task
	      core image as follows:

		   *DSK:TASKX=N

	      In this command line, DSK is the swap device and TASKX is the
	      core image file containing the nonresident portion of task N.
	      Repeat this procedure for each nonresident task, one task per
	      line,  and  terminate  the  last  line with an ALTMODE.  This
	      procedure automatically initializes and starts the real  time
	      system.


				      6-7

		    ASSEMBLING AND LOADING TASKS FOR RTS/8


	      An RTS/8 system created with the procedure just described has
	      a  starting  address  of  00200.   If an RTS/8 system was not
	      specifically confiqured for a PDP-8/E  or  PDP-12,  it  halts
	      initially  to  allow  the  operator to clear any stray device
	      flags  by  operating  nonstandard  hardware  switches  or  by
	      pressing  START.  Press START to resume operation on a PDP-8,
	      8/I or 8/L.
     
     
     6.3  USING THE OS/8 BITMAP PROGRAM

     The OS/8 BITMAP program can be extremely useful in determining that no
     two  RTS/8 tasks are loading into the same area or using the same Page
     0 locations.  OS/8 BITMAP accepts a list of binary files as input  and
     produces  as  its  output a map of core memory.  Each location of core
     memory is represented in this map by a  single  digit  which  has  the
     following meaning:

	  0    Nothing has been loaded into this location

	  1    Information has been loaded into this location

	  2    Information has been loaded into this location twice

	  3    Information has been loaded into this location three or more
	       times

     There are certain places in core  memory  where  2's  are  allowed  to
     appear  in  the  bit  map.  These areas are the RTS/8 Executive Tables
     (starting at location 01200), the MCR name table in the MCR, the power
     fail  action table, and nonresident task partitions (which may contain
     2's and 3's).  Appearance of a 3 or a 2 in an area  other  than  these
     three  areas  just mentioned in the bit map indicates that two or more
     tasks are being loading into the same location.
     
     
     6.4  SAMPLE RTS/8 TASK PROGRAM

     The task that is used as an example in this section was  selected  for
     its  simplicity,  and  to  show the basic concepts of RTS/8 operation.
     The purpose of the task is simply to print "HELLO".  The user requires
     an RTS/8 system configuration that includes a console Terminal Handler
     (TTY) and the Monitor Console Routine (MCR).  It is assumed  that  the
     task  will  be running on a PDP-8 E/F/M/A with 8K of core memory and a
     standard console terminal.
     
     The program (SAMPLE.PA) listed below is complete, and  when  assembled
     with  the  parameter file, will run as task 5 in a properly-configured
     system.  The task is initially in the Run Wait state.  When  requested
     by  the  user  through  the  Monitor  Console Routine, the task prints
     "HELLO" on the console terminal, and then suspends itself.   If  again
     requested by the user, the same sequence will occur.




				      6-8

		    ASSEMBLING AND LOADING TASKS FOR RTS/8


	     /SAMPLE RTS/8 PROGRAM
		     TASK=5 	   /GIVEN A PRIORITY OF 5
		     CUR=0 	   /IN FIELD 0
		     INIWT=RUNWT   /SET TO RUN WAIT STATE
		     FIELD 0	   /PLACED IN FIELD 0
		     *3000	   /ANY AVAILABLE PAGE
	     START,  CAL
		     SENDW	   /MUST BE DEFINED AS "START"
		     TTY	   /SEND AND WAIT
		     MSG1	   /THE TERMINAL
		     CAL	   /THE MESSAGE BLOCK
		     SUSPND	   /SUSPEND THE TASK
		     JMP START	   /RESUMES HERE IF REQUESTED
	     MSG1,   ZBLOCK 3	   /RTS/8 LINKAGE
		     0;0	   /TERMINAL OPTIONS
		     TEXT /HELLO/  /TYPE HELLO
		     $

     An edited version of PARAM.PA now is required for this  configuration,
     and  it  is  named PARAMS.PA.  To produce PARAMS.PA from PARAM.PA, the
     following definitions are edited into the parameter file:

	  PDP8E=1
	  HGHFLD=10
	  NTASKS=10
	  TTY=4
	  MCR=3

     NTASKS is the largest task  number  used  with  this  system.   It  is
     assigned  any  number  greater  than  the  values for MCR, TTY and the
     sample task, and which is smaller than 100 octal.  The task values for
     SAMPLE,  MCR and TTY were arbitrarily chosen in the range greater than
     zero and less than NTASKS.

     The program is then assembled as follows:

	  .R PAL8

	  *SAMPLE.BN<PARAMS.PA,SAMPLE.PA

     The system for the sample task requires the Executive Task  RTS8  plus
     the  TTY  and  MCR Task to run.  This can be accomplished by using the
     following Batch stream:

	  $JOB
	  .PAL PARAMS-NB,RTS8
	  .PAL PARAMS-NB,MCR
	  .PAL PARAMS-NB,TTY
	  .PAL PARAMS-NB,SAMPLE
	  .LOAD RTS8,MCR,TTY,SAMPLE
	  .SAVE SYS:SAMP
	  $END
     
     Assembly and loading of the tasks, including saving  the  program,  is
     now  complete.   The  CCL option -NB indicates that PARAM is not to be

				      6-9

		    ASSEMBLING AND LOADING TASKS FOR RTS/8


     used as the name of the binary file being created.

     The system now can be run as follows (user input is underlined):

     	     .R SAMP		 /OS/8 RUN COMMAND	      ______
	     >RE 5($)		 /REQUEST SAMPLE FROM MCR	      _______
	     HELLO		 /TASK EXECUTES AND SAYS 'HELLO'
	     ^C			 /RETURNS CONTROL TO MCR	     __
	     >SYSTAT		 /SYSTEM STATUS COMMAND	      ______
	     03 MCR		 /MCR TASK
	     04 TTY		 /TERMINAL TASK
	     05        R	 /TASK 5 WAITING TO BE RUN
	     >RE 5($)		 /RUN TASK AGAIN	      _______
	     HELLO		 /TASK SAYS 'HELLO' AGAIN
	     ^C			 /RETURN CONTROL TO MCR	     __
	     >EXIT		 /RETURN TO OS/8	      ____
	     .			 /OS/8 MONITOR
     
     		
     			 	     NOTE

		   ($) is the ALTMODE character;  all other
		   input lines are terminated by a Carriage
		   Return.
     
     
     6.5  USE OF CONTROL FILES UNDER RTS/8

     There are times when a user may want to assemble a given source module
     in  more  than  one way and use the results under RTS/8.  For example,
     suppose there are three terminals that a user wants to  service  under
     RTS/8.   Each  terminal  has its own characteristics, and each copy of
     the TTY task needs to have its own set of parameters.  The  user  must
     load  three copies of the TTY task into memory at different locations,
     and  possibly  in  different  fields.   This  cannot  be  accomplished
     efficiently  when  using  a  single  parameter  file.   With  a single
     parameter file, three copies of the file TTY.PA must be made and  each
     one  edited  to  produce  three  individual tailored copies of the TTY
     task.  This procedure is not convenient or modular.

     A better way to do this is to use a control file that contains all the
     equates  necessary to define the parameters needed by a particular TTY
     task.  The control file then is assembled  together  with  and  placed
     between the parameter file and the TTY module.  For example,

	  .PAL TTY1 <PARAM,TTYCF1,TTY

     creates a binary file called TTY1 from TTY.PA  using  a  control  file
     called TTYCF1.

     To facilitate using this procedure, a skeleton  TTY  control  file  is
     supplied  with the RTS/8 task sources.  It contains all the parameters
     that the user normally defines in the parameter file.   Thus,  a  user
     who wants to use multiple terminals, instead of editing the parameters
     in the parameter file, can create a control  file  for  each  terminal

				      6-10

		    ASSEMBLING AND LOADING TASKS FOR RTS/8


     that  is  used, and then edit the control file to make multiple copies
     as necessary.

     An example of a TTY Control file after it has been edited by a user is
     shown below.
     
     	    TASK=TTY1
     			     /DEFAULT IS 'TTY'
     /	    TTDEV=	     /PRINTER DEVICE CODE - DEFAULT IS 04
     /	    KBDEV=	     /KEYBOARD DEVICE CODE - DEFAULT IS TTDEV-1
	    CONSOL=1
     /	    VT50=	     /1 ENABLES CTRL/S AND CTRL/Q
     	    SCOPE=1
     /	    FILL=	     /NUMBER OF FILL CHARACTERS, I.E. 4
     /	    WIDTH=	     /TTY LINE WIDTH (0 MEANS INFINITE), DEFAULT
     			     /120
     /	    TAB=	     /1 IF TTY HAS HARDWARE TABS
     	    OLDTTY=0
     /	    LSBOT=	     /1 LISTS BOTH HANDLERS (DEFAULT 0)
     	    TTFLD=20
	    TTLOC=3000

     This example shows a TTY control file that has been  edited  for  task
     TTY1.   This  terminal  handler task will be assembled for the console
     terminal.  Setting SCOPE=1 causes RUBOUT to move the cursor  left  one
     position,  physically removing the character from the screen.  The new
     three-page handler is specified.  It is placed in field 2, starting at
     location 3000.

     A skeleton control file is also supplied for the RX01  floppy.   Users
     can easily generate and use control files for other purposes.
     
     
     6.6  RTS/8 SYSTEM TASK PARAMETERS

     This section provides a convenient grouping of those parameters  which
     affect  the individual RTS/8 system tasks.  Given for each system task
     is the parameter, its function and where applicable, an example.   The
     section or chapter where a detailed description of the task appears in
     the text of this manual is noted after the task subhead.
     
     
     6.6.1  Clock Handler Parameters (Section 4.1)

     	  PARAMETER			       MEANING
     
	  CLKTYP	 Specifies selection of hardware clocks as follows:

		         0 = DK8-EA/DK8-EC
			 1 = KW12
			 2 = PDP-8/A
			 3 = DK8-EP

	  CLKQLN	Specifies minimum number  of  entry  slots  in  the
			clock queue (default is 20).

				      6-11

		    ASSEMBLING AND LOADING TASKS FOR RTS/8


	  HERTZ		Specifies number  of  hardware  ticks  per  second.
			HERTZ  and  SHERTZ  are decimal values in that they
			are  preceded  in  the  parameter   file   by   the
			pseudo-operator DECIMAL.

	  SHERTZ	Specifies the number of system  ticks  per  second.
			This  parameter  is followed by the pseudo-operator
			OCTAL, which  resets  the  radix  to  its  original
			octal base.


     6.6.2  Swapper Parameters (Section 7.4)

	  SYS 		 Specifies the  swap  driver  task;   for  example,
			 SYS = RK8 specifies the RK8 driver task.

	  SUNIT 	 Specifies the swap  device  physical  drive  unit;
			 SUNIT = 0 selects RKAO.
     
     
     6.6.3  Terminal Handler Parameters (Section 4.2)

	  PARAMETER			       MEANING
     
	  TTDEV		 Is set to the proper printer device code;  default
     			 value is 4.

	  KBDEV		 Is  set  to  the  proper  keyboard  device   code;
     			 default value is TTDEV-1.

     The following parameters are available to the user to facilitate the
     use of the TTY task.

	  VT50		 Is set to 1 (default) to enable CTRL/S and  CTRL/Q
			 functions.   When  set to 0, CTRL/S and CTRL/Q are
			 not treated as special characters.  Typing  CTRL/S
			 while  data  is  being  printed/displayed  on  the
			 screen stops the data presentation until the  next
			 CTRL/Q  is typed.  This parameter must be set to 1
			 if the user's terminal is a VT50  or  VT52.   Both
			 CTRL/S and CTRL/Q turn off the echo flag.

	  CONSOL	 Is set to 1 to specify that the handler  is  being
			 assembled for the console TTY (default).  Set to 0
			 to specify that this handler should  not  wake  up
			 the MCR when ^C is typed.

	  WIDTH		 Is set to an octal number that specifies  the  TTY
			 page  width.   TTY  width  is currently set to 120
			 (octal), that is,  a  page  width  of  80  decimal
			 characters.  WIDTH = 60 sets the TTY page width to
			 48 decimal characters.

	  SCOPE		 This option is used to determine the treatment  of
			 the RUBOUT key as follows:

				      6-12

		    ASSEMBLING AND LOADING TASKS FOR RTS/8



			 SCOPE=0 (default)  provides  the  normal  node  of
			 RUBOUT support.

			 SCOPE=1 causes RUBOUT to move the cursor left  one
			 position,  physically  removing the character from
			 the screen.  If the cursor is in column 1,  RUBOUT
			 still works, but has no visible effect.

	  TAB		 This option simulates tabs by the proper number of
			 spaces.   This  is  accomplished  via the assembly
			 parameter TAB as follows:

			 TAB=0 (default) specifies that the  hardware  does
			 not  support tabs.  The software simulates tabs by
			 spaces.

			 TAB=1 specifies that  the  hardware  does  support
			 tabs.

	  Fill 		 characters  are   supported   via   the   assembly
			 parameter FILL as follows:

			 FILL=0  (default)  does  not  provide   any   fill
			 characters.

			 FILL=n sends n fill  characters  (nulls)  after  a
			 line feed;  n must be in the range 1-5.  FILL=4 is
			 recommended for 2400 baud VT5's.

	  OLDTTY	 Is set to 1 to specify the use of the  old  2-page
			 TTY  handler.   Set  to  0  (default)  to  use the
			 standard 3-page  handler.   The  old  handler  has
			 fewer  features,  but  it  is a page shorter.  The
			 parameters VT50, WIDTH, SCOPE, TAB and  FILL  have
			 no effect when using the old handler.

	  LSBOT		 Is set to 1 to list both the old  2-page  and  new
			 3-page  handler.   Set to 0(default) when only the
			 handler selected by OLDTTY is to be listed.

	  TTFLD		 Is set to specify the  field  of  TTY  Task;   for
			 example, 20 specifies field 2.

	  TTLOC		 Is set to specify the location of TTY  Task;   for
			 example,  3000  specifies  a  starting location of
			 3000.

     Several equates are listed in the parameter file.  They are useful for
     sending messages to TTY or LPT Tasks.  These equates follow:

	  NOPACK=4000 	 Used if the output message is not 6-bit ASCII.

	  NOCRLF=2000 	 Used if the output message should not be  followed
			 by carriage return/line feed.

				      6-13

		    ASSEMBLING AND LOADING TASKS FOR RTS/8


	  IND=1000	 Used if OUTTXT points to the  first  word  of  the
			 output text.

	  NOLINE=400	 Used if the output is in character mode.

	  ASSGN=200	 Used to assign the device handler for use by  only
			 this task.

	  KL8ALINE=100	 Used with KL8-A support (see Section 4.13.2).


     6.6.4  Monitor Console Routine Parameters (Chapter 5)

	  PARAMETER			       MEANING

	  MCRSYS	 Is set to 1 if the SYSTAT facility is desired  for
			 printing  system status reports of existent system
			 tasks.


	  MCRCLK	 Is set to 0 if the clock functions are not  wanted
			 by the user.

	  MCRFLD	 Is set to the field in  which  it  is  desired  to
			 locate  MCR.   MCRFLD = 30 places the MCR in field
			 3.

	  MCRPRT	 Is set to the number of the partition  into  which
			 the   nonresident  portion  of  the  MCR  will  be
			 swapped.    This   parameter   makes    the    MCR
			 nonresident;   however,  the first page of the MCR
			 is always resident.

	  MCRORG	 Is set to specify the  starting  location  of  the
			 MCR.   Default  causes the MCR to load against the
			 end of the field.

	  MCRCDV	 Set to task name of task which is to  be  the  MCR
			 console device.  Default is TTY.


     6.6.5  OS/8 Support Task Parameters (Section 4.6)

	  PARAMETER			       MEANING

	  OSFLDS	 Is set to the number of fields allocated for OS/8.
			 0SFLDS = 2  specifies  two  fields or 8K of memory
			 for OS/8.

	  OSKBDV	 Is set to the device  code  that  selects  desired
			 OS/8 keyboard terminal.  0SKBDV = 03 specifies the
			 use of the console  terminal  keyboard  for  OS/8.
			 Note: OS/8 requires its own dedicated terminal.



				      6-14

		    ASSEMBLING AND LOADING TASKS FOR RTS/8


	  OSTTDV	 Is set to the device code  which  selects  desired
			 OS/8  teleprinter.   0STTDV = 04 specifies the use
			 of the console teleprinter for OS/8.

	  OSSYSD	 Is set to select the  OS/8  system  device  driver
			 task.   0SSYSD  =  DTA  specifies DTAO as the OS/8
			 system device.

	  OSFILL	 Is set to the number of null characters that  must
			 follow a line feed character on the OS/8 terminal.
			 0SFILL = 4 is specified  when  using  a  2400-baud
			 VT05  terminal.   Set  to  O  when  using standard
			 hard-copy terminals.

		 	 Note: A terminal device handler does not  have  to
			 be included for the OS/8 terminal device.


     6.6.6  KL8-A Support Parameters (Section 4.13)

	  PARAMETER			       MEANING

	  KL8ADV	 Specifies the device code  for  the  first  KL8-A.
			 Default is 40.  If multiple KL8-A's are used, they
			 should have consecutive device codes.

	  KL8ACT	 Specifies the page for the KL8-A connect  routine.
			 Default  is  7400  (if KL8A=1).  The KL8-A connect
			 routine must be located in field 0.


     6.6.7  Line Printer handler Parameters (Section 4.3)

	  PARAMETER 			       MEANING

	  LPTLOC 	 Specifies  the  starting  location  of  the   Line
			 Printer Handler Task.

	  LPTFLD 	 Specifies the field of the Line Printer Task.


     6.6.8  DECtape Handler Parameters (Section 4.4)

	  PARAMETER 			       MEANING

	  DTALOC 	 Specifies the starting  location  of  the  DECtape
			 Handler Task.

	  DTAFLD 	 Specifies the field of the DECtape Handler Task.







				      6-15

		    ASSEMBLING AND LOADING TASKS FOR RTS/8


     6.6.9  EXIT Task (Section 4.14)

	  PARAMETER 			       MEANING

	  EXITFLD 	 Specifies the field of the EXIT Task.

	  EXITLOC 	 Specifies the starting location of the EXIT Task.

















































				      6-16







				   CHAPTER 7

			       NONRESIDENT TASKS


     7.1  OVERVIEW

     A nonresident task is a task or a portion of a task that resides on  a
     mass  storage  device  during  the time the task is not runnable.  The
     mass storage device is called the swap device.  It  can  be  any  mass
     storage  medium  (e.g.,  an RK8 cartridge disk or an RX8 floppy disk).
     When a nonresident task becomes  executable,  the  Executive  posts  a
     residency  request.  The Executive then runs a special task called the
     Swapper to load the nonresident or portion  of  the  nonresident  task
     into  memory.   The loading process is called a swap.  The memory area
     into which or out of which the nonresident task is swapped is called a
     partition.   A  partition is a contiguous block of memory that is used
     for task execution;  it is readable in a  single  mass  storage  call.
     The  use of nonresident tasks per,nits several tasks to share the same
     areas of memory, optimizing the use of available memory.

     Tasks can be either totally or partially nonresident.  Very few  tasks
     are  totally  nonresident;   in  most  applications,  the  nonresident
     portion includes all, or nearly all, of the active locations.   Active
     locations  are those that contain executable instructions or data that
     are never accessed by other tasks.  The resident  portion  of  a  task
     includes  messages, event flags, buffers and similar passive registers
     that may be needed by other tasks.

























				      7-1

			       NONRESIDENT TASKS


		PDP-8 MEMORY
	------------------------------------		 SWAP DEVICE
     0K |				   |	  (Disk, DECcassette, etc.)
	|  REAL TIME PROGRAM AREA	   |
	|				   |
	|  Contains:			   |		   ..........
	|    1. Resident tasks		   |	  	 /  Contains  \
	|    2. Resident portions of	   | 		/ nonresident  \
	|	non resident tasks	   |		\ portion of a /
     pK |----------------------------------|		 \     task   /
	|				   |		   ..........
	|	PARTITION AREA		   |			|
	|				   |			|
	| 1. Contains non resident portion |			|
	|    of nonresident task when that |       ------------------------
	|    task is being executed.	   |	   |			  |
	|				   |	   |	 SWAPPER TASK	  |
	| 2  Allows multiple tasks of same |	   |	 (SWAP.PA)	  |
	|    relative size to run in the   |	   |			  |
	|    same memory area.		   |-------| 1. Loads nonresident |
	|				   |	   | portion of task into |
	| 3. The characteristic of a 	   |	   | memory.		  |
	|    partition is as follows:	   |	   | 2. Swaps out non-	  |
	|				   |	   | resident task onto	  |
	|    a) Has a starting address	   |	   | Swap Device.	  |
	|				   |	   | 3 Also loads and	  |
	|    b) Resides completely within  |	   | swaps writeable and  |
	|	a single memory field	   |	   | checkpointable tasks.|
	|				   |	   |			  |
	|    c) Length has to be an 	   |	   ------------------------
	|	integral number of pages   |
	|				   |
	|    d) Cannot overlap another 	   |
	|	partition		   |
	|				   |
     nK ------------------------------------

		  Figure 7-1 Nonresident Task Implementation


     The process that swaps the nonresident portion of a task  into  memory
     is  similar  to  the  overlay  capability found in OS/8 FORTRAN IV and
     related programs.   However,  swapping  is  much  more  powerful  than
     overlaying.   Every nonresident task has two properties that establish
     when and how  it  is  swapped  into  or  out  of  memory.   These  two
     properties are "writeability" and "checkpointability".

     A task is made "writeable" if its nonresident portion must be  written
     onto  the  swap  device  whenever  it  is swapped out to make room for
     another   task.    A   writeable   task   is   any   task   that    is
     self-modifying - i.e.,  the  task's  code  is  changeable  during task
     execution, and any task that must initialize before it can start.  The
     writeability feature guarantees that the nonresident portion of a task
     is always up to date by  refreshing  the  swap  device  image  of  the
     nonresident portion whenever the task is swapped out of memory.

				      7-2

			       NONRESIDENT TASKS


     A task is made "checkpointable" if it may be  swapped  out  of  memory
     automatically, without its consent, to make room for a higher priority
     task.  A task that was checkpointed  and  swapped  out  of  memory  is
     swapped  back  automatically as soon as all higher priority tasks have
     relinquished the necessary memory space.  Execution then continues  at
     the  point where it was interrupted, and the task is not aware that it
     was interrupted.

     Some  nonresident  tasks  have  both  writeable   and   checkpointable
     characteristics.  Writeable tasks are utilized when a task must modify 
     itself  (for  example,  it  includes  JMS  instructions  or  temporary 
     locations).   Tasks  suitable  for  checkpointing  are  those that are
     1) fairly long-running, and 2) are required only occasionally.


     7.1.1  Writeable Tasks

     A writeable task is one that includes code that is self-modifying,  or
     code  that  must  be  initialized  before execution.  Before execution
     begins, all nonresident tasks must reside as core image files  on  the
     swap  device.  The core images are created by loading each nonresident
     task separately, and executing an OS/8 monitor SAVE command; this  can
     be done under BATCH.  When a task is executed, its nonresident portion
     is read from this core image file  by  the  swapper.   If  a  task  is
     writeable,  its nonresident portion will be written into the same file
     when it is swapped from memory.  It is likely that a  task,  writeable
     at  execution  start-up, would flag itself not writeable at some later
     time when all initialization is completed.  The nonresident portion of
     a task is writeable if it must be saved on a mass storage device (swap
     device) before overwriting it in memory with another task.
     
     
     7.1.2  Checkpointable Tasks
     
     Checkpointing is ideally suited for long-running  tasks.   The  system
     can  run  short  tasks  in the same area, swap them out of memory, and
     swap the long running task back again.
     
     
     7.1.3  Interaction Between Tasks
     
     Resident  tasks  can  interact  with  the  resident  portion  of   any
     nonresident  task.   Two  nonresident  tasks  that  occupy overlapping
     memory regions can interact with each  other  through  their  resident
     partitions.  For example, if a nonresident task is executing, it sends
     a message  and  is  then  checkpointed.   The  message  recipient  can
     acknowledge the sender's message even though the sender is not totally
     resident.  However, the message sent must be resident.
     
     
     7.2 MEMORY PARTITIONS
     
     The swappable portion of  a  nonresident  task  resides  in  a  memory
     partition.   This  partition  is  simply  a contiguous block of memory
     locations that is readable in one mass storage call.  Every  partition

				      7-3

			       NONRESIDENT TASKS


     has the following characteristics:
     
	  o  It is wholly contained in one memory field.

	  o  It has a starting address.

	  o  It has a length (size) that must divide evenly by 200 (octal)
	     since OS/8 file structured devices read and write in one-half
	     block (one page) increments.

	  o  It normally begins at an address which is a multiple of 400.

     The user can set the parameters for establishing the partition  either
     in  the  parameter  file  or  the  source  of  the Swapper Task.  This
     procedure is described in Section 7.4.

     Partitions are  mutually  distinct,  that  is,  one  partition  cannot
     overlap  another.   Any  number  of  partitions can be defined.  The n
     partitions are numbered in any order, from 0 to  n-1,  with  partition
     number 0 being the first partition.  They need not be adjacent.

     Only one task can occupy a partition at any given time.  The occupying
     task  owns  the  partition  until  that task executes a "free" command
     (described in the next section), or (if the task is checkpointable) as
     long  as  higher  priority  tasks  that  share  the  partition  remain
     nonexecutable.

     It is most convenient if every partition begins on the first  location
     of even-numbered pages, that is, the starting address is a multiple of
     400 octal.
     

     7.2.1  FREE Command

     A free request can be appended to the function argument of  some  ER's
     (for example, SEND, RECEIVE, etc.) as follows:

	  CAL 		 /A CALL TO THE EXECUTIVE
	  COMMAND+FREE 	 /"COMMAND" IS ANY RTS/8 EXECUTIVE
		     	 /REQUEST.  THE
			 /ISSUING TASK IS TO BE SWAPPED OUT OF
			 /MEMORY IF SOME OTHER TASK
			 /BECOMES EXECUTABLE AND REQUIRES THE
			 /PARTITION BEFORE THE FREEING TASK
			 /CANCELS THE FREE REQUEST.

     A free request must be combined with some other executive request.  If
     the sequence:

	  CAL
	  FREE

     is issued, it will be interpreted as:



				      7-4

			       NONRESIDENT TASKS


	  CAL
	  SEND+FREE

     Only nonresident tasks may issue free requests;  other  free  requests
     are  ignored.   A  task  may  free  its  own  partition, but never the
     partition of another task.

     A task normally frees its partition  whenever  it  must  wait  for  an
     event.   If any other task has a pending request for the partition, it
     is swapped into the  free  partition  immediately.   If  there  is  no
     pending  request for the partition, the freeing task continues to wait
     in the free partition until some other  occupant  requests  residency.
     In  either  case,  once  the freeing task becomes executable again, it
     must compete  for  the  partition  along  with  any  other  executable
     occupants.   The  freeing  task may become executable before any other
     task requests residency in the partition.   In  this  case,  the  free
     command  is  cancelled, and the freeing task retains possession of the
     partition.  No read or write operation is  necessary  to  effect  this
     swap  in  this  case.  By freeing the partition whenever the occupying
     task (which may or may not be writeable) must wait for an  event,  the
     programmer  is  assured  that  the partition contains a running (i.e.,
     nonwaiting) task whenever possible.  If there are no  writeable  tasks
     in  the  partition,  no  swap  device  I/O  is involved in freeing the
     partition.
     
     
     7.3  NONRESIDENT TASK INITIALIZATION
     
     The following procedure is recommended to implement any  RTS/8  system
     containing nonresident tasks.

	  1.  Code and debug each nonresident  task  as  a  resident  task.
	      During  the  debugging, load the task being debugged and only
	      the tasks required for execution of the task to be  debugged.
	      Once  the  task  executes  correctly  while resident, make it
	      nonresident.  Making a task nonresident is described  in  the
	      sections that follow.

	  2.  On  a  listing,  mark  the  nonresident   portion   of   each
	      nonresident   task.    Determine  the  size  of  each  task's
	      nonresident portion.  Then design the partitioning scheme and
	      allocate  nonresident tasks to memory partitions by modifying
	      the parameter file as described in Section 7.4.

	  3.  Re-origin each  nonresident  task  so  that  its  nonresident
	      portion lies within its partition.  If necessary, ensure that
	      resident portions of nonresident tasks do  not  overlap  into
	      another  partition.   BITMAP,  an  OS/8  utility  program, is
	      useful for this since it allows the user to determine if  two
	      or  more  tasks  are  erroneously  being loaded into the same
	      memory section.  The use of BITMAP is  described  in  Section
	      6.3.  A  detailed description of BITMAP is given in Chapter 2
	      of the OS/8 Handbook.  Execute the task as  a  resident  task
	      once more to make sure it does not contain location dependent
	      code.   Also,  if  any  memory  partition  begins  on an  odd

				      7-5

			       NONRESIDENT TASKS


	      numbered page, temporarily relocate each task that resides in
	      that partition.  An example of starting a nonresident task at
	      an arbitrary boundary is given in Section 9.3.
     
     
     7.3.1  Parameters for Nonresident Tasks
     
     Several  assembly  parameters  must  be  initialized  when   employing
     nonresident  tasks.   Five  of  the  parameters  are  located  in  the
     parameter  file  (PARAM.PA)  and  three  must  be  included   in   the
     nonresident task itself.

     The  parameter  file  (PARAM.PA)  contains  five  parameters  (PARTNS,
     CHECKP,  SWAPPER,  SYS  and  SUNIT)  which  must  be  initialized when
     employing  nonresident  tasking.   These  parameters  are  defined  as
     follows:

	  PARTNS    is set to the  number  of  memory  partitions  defined.
		    PARTNS is set to zero in the parameter file to indicate
		    that no memory partitions are defined in the system.

	  CHECKP    is set to 1 if any nonresident task is checkpointable.

	  SWAPPER   is the nonresident  task  swapper  task;   it  must  be
		    assigned  a task number that is of higher priority than
		    the task it swaps, that is, a  number  lower  in  value
		    than that of any nonresident task in the system.
     
          SYS	    is set to designate the swap device driver  task;   for
     		    example, SYS = RK8 specifies the disk driver task.

     	  SUNIT	    is set to specify the swap device physical drive  unit;
		    for example, SUNIT = 0 specifies the disk cartridge
     		    drive.

     Every  nonresident  task  source  must  include  the  following  three
     parameters:

	  PARTNO= n, where n is the task's partition number (starting at 0)
	  CPABLE= 0, if the task is not checkpointable
		  1, if the task is checkpointable
	  WRITE=  0, if the task is not writeable
		  1, if the task is writeable

     Failure to initialize these parameters correctly causes the program to
     execute  unpredictably.  The presence of parameter PARTNO identifies a
     task as a nonresident task.  Hence, the variable  name  PARTNO  should
     not be used except in nonresident tasks.

     A nonresident task is not appreciably different from a resident  task.
     However, buffers should not be in nonresident portions of a task since
     the buffers will be  out  of  memory  when  that  task  is  not  being
     executed.   There are no special coding restrictions.  The nonresident
     portion is always present  in  memory  while  a  nonresident  task  is
     executing.   It  is  generally  safe  to  assume  that the nonresident

				      7-6

			       NONRESIDENT TASKS


     portion is never present when the task is not executing.  There  is  a
     slight  structural  difference between resident and nonresident tasks;
     nonresident  tasks  have  clearly  defined  resident  and  nonresident
     portions that cannot be intermixed.
     
     
     7.3.2  Assembling Nonresident Tasks
     
     Each nonresident task is assembled separately.  The  nonresident  task
     must  include  the  parameter TASK, but never the parameters TASK2 and
     TASK3 (see Section 6.1.5, Task Setup).

     The swap device file that contains  the  nonresident  portion  of  the
     nonresident  task  requires special treatment.  This file must contain
     the first word of the nonresident portion in  the  first  location  of
     relative  block  1,  the second word of the nonresident portion in the
     second location, and so on.  This file must be a core image;  however,
     the  OS/8  monitor  requires that the first location of any core image
     section load into a memory address that divides evenly by  400(octal).
     If  the  lowest  address  in  the  partition  also  divides  evenly by
     400(octal), this condition is met.  There is no problem because  every
     task can be assembled in the partition directly.

     Modify  the  parameter  file  (PARAM.PA)  to  establish  the   desired
     parameters.  Then assemble the nonresident task and the parameter file
     together.
     
     
     7.3.3  Creating the SAVE Image File
     
     Create a SAVE image file (nonresident  disk  image)  from  the  binary
     image file as follows:

	   .R ABSLDR
	   *TASKX.BN$
	   .SAVE DEV TASKX.SV N1-N2
     
     For each task, where DEV is the swap device, N1 is the lowest  address
     in the partition, and N2 is the highest address in the partition.  The
     resulting core images contain only the nonresident  portions  of  each
     task  and meet all the requirements previously outlined.  However, the
     first block of the core image (relative block 0) is the  core  control
     block,  which is not used by the swapper.  As stated previously, it is
     strongly recommended that the partitions begin at a location that is a
     multiple  of  400(octal)  since the OS/8 SAVE command only saves areas
     starting at 400(octal) boundaries.


				      NOTE
		    SAVE  image  files  can  be  constructed
		    under  OS/8  BATCH.   Also, the OS/8 CCL
		    command LOAD may be used to  create  the
		    SAVE image.
     


				      7-7

			       NONRESIDENT TASKS

     
     7.4  PARAMETER INITIALIZATION FOR PARTITIONS
     
     The user must initialize certain parameters to define the partitioning
     scheme.  They can be set in either PARAM.PA or SWAP.PA.  The following
     three variables are required for each of the partitions:

	  MFLDnn= MEMORY FIELD OF PARTITION N
	  ADDRnn= MEMORY ADDRESS OF PARTITION N
	  SIZEnn= SIZE OF PARTITION N, SPECIFIED IN PAGES

     The user can set up  the  parameter  file  to  accept  eight  sets  of
     partition  parameters.   When  more than eight partitions are defined,
     the  parameter  table  must  be  extended  according  to  instructions
     contained  in source.  Since adding extra partitions does not increase
     system overhead, it is best to have as many  partitions  as  possible.
     This  minimizes the number of tasks that must share a partition.  Each
     partition should have at least two occupants;  otherwise, there is  no
     reason  for  making the task nonresident.  The partitioning scheme can
     also be defined by initializing the  required  parameters  within  the
     swapper source.
     
     
     7.4.1  General Information
     
     The entire partition table appears on the swapper PAL or  CREF  output
     listing.   The  user  should  check  it  carefully  to ensure that all
     partition parameters (MFLDnn, ADDRnn and SIZEnn  for  each  partition)
     were  defined  correctly.   The parameter file generates the residency
     table entry for each nonresident task and it appears  on  the  PAL  or
     CREF  output listing for that task.  The user should examine word 1 of
     this entry to verify that  the  nonresident  task  parameters  PARTNO,
     CPABLE, and WRITE were initialized correctly.  Word 2 of the residency
     table entry will be zero because the task's block address on the  swap
     device  is  unknown at assembly time.  This location is initialized by
     the OS/8 command decoder shortly after program startup, and it can  be
     examined  anytime  thereafter.  In the usual case, where the file is a
     core image, this location should contain M+1, where  M  is  the  block
     address returned by the following command:

	  .DIR DEV:TASKX.SV/B
          
     TASKX.SV  is  the  core  image  on  the  swap  device  containing  the
     nonresident portion of the task.
     
     
     7.5  NONRESIDENT TASK IMPLEMENTATION
     
     Perform the following procedure to implement nonresident tasks.

	  1.  Assemble every task that will be included in the  program  as
	      described  in Section 7.3.2.  Obtain PAL or CREF listings and
	      bitmaps.  Finally, obtain a bitmap of the entire  system  and
	      verify that memory is allocated correctly.  On the bitmap, 3s
	      are legal only within partitions.


				      7-8

			       NONRESIDENT TASKS


	  2.  Create the SAVE image file as described in Section 7.3.3.

	  3.  Load the binaries of  the  RTS/8  executive  and  each  task,
	      including  nonresident  tasks.   Always  load  the  executive
	      first.  Nonresident tasks are included in this  operation  in
	      order  to  load  their  resident portions and Executive table
	      entries.  Either save the loaded program as a core image file
	      or start it from the keyboard.

	  4.  Start the real-time program  using  the  monitor  R  command.
	      This  calls the OS/8 command decoder, which types an asterisk
	      on the console terminal.  At this time, initialize the  block
	      address of each nonresident task core image as follows:

		   *DEV:TASKX.SV=N

	      In this command line, DEV is the swap device and TASKX.SV  is
 	      the  core  image  file  containing the nonresident portion of
	      task N.  Repeat this procedure for each nonresident task, one
	      task  per  line, and terminate the last line with an ALTMODE.
	      This  procedure  automatically  initializes  and  starts  the
	      real-time program.

	      This initialization procedure may be executed automatically
	      under OS/8 BATCH control.

	      Example:

		  $JOB SYSTEM
		  /RUN "SYSTEM" AND INSTALL
		  /NONRESIDENT TASKS.
		  .RUN SYS SYSTEM
		  *TASK1=35 /TASK 35 IS "TASK1" SAVE IMAGE
		  *TASK2=36$ /TASK 36 IS "TASK2" SAVE IMAGE
		  $END

	      Submitting SYSTEM.BI runs RTS/8 user system SYSTEM.SV,
	      installing its two nonresident tasks.

	  5.  Debug the entire program.   Accomplish  this  by  selectively
	      placing   HLT   instructions    (preceded  by  IOF,  NOP,  if
	      appropriate) and examining the memory once the HLT  has  been
	      executed.   Use the MCR and/or the console switch register to
	      place  and  remove  HLT  instructions  and  to   modify   all
	      permanently  resident  areas.   When using MCR, remember that
	      MCR  output  represents  a  snapshot  of   memory   at   some
	      undetermined  point in time that is long past by the time the
	      MCR has output to the terminal.
     
     
     
     


     
     
     				      7-9






				   CHAPTER 8

			     DEMONSTRATION PROGRAM

     This chapter contains a demonstration of RTS/8 with nonresident  tasks
     executing  in  the  foreground.  Included is a listing of the modified
     parameter file (PARAM.PA).   In  addition,  there  is  an  example  of
     nonresident  tasks  (Tasks  NR20  and  NP22) and the assembly and load
     instructions required for implementing the demonstration program.


     8.1  MODIFIED PARAMETER FILE (PARAM.PA)

     /2.6 PARAMETERS FOR RTS/8 TASKS V28+DECNET
	     LSTFLG=0	     /CHANGE 0 TO 1 TO PREVENT LISTING PARAM
	     XLIST LSTFLG
     /
     /
     /
     /
     /
     /
     /COPYRIGHT     (C)    1974,1975,1976 BY DIGITAL EQUIPMENT CORPORATION
     /
     /
     /
     /
     /
     /
     /THE INFORMATION IN THIS DOCUMENT IS SUBJECT TO CHANGE WITHOUT NOTICE
     /AND SHOULD NOT BE CONSTRUED AS A COMMITMENT BY DIGITAL EQUIPMENT
     /CORPORATION. DIGITAL EQUIPMENT CORPORATION ASSUMES NO RESPONSIBILITY
     /FOR ANY ERRORS THAT MAY APPEAR IN THIS DOCUMENT.
     /
     /THE SOFTWARE DESCRIBED IN THIS DOCUMENT IS FURNISHED TO THE PURCHASER
     /UNDER A LICENSE FOR USE ON A SINGLE COMPUTER SYSTEM AND CAN BE COPIED
     /(WITH INCLUSION OF DIGITAL'S COPYRIGHT NOTICE) ONLY FOR USE IN SUCH
     /SYSTEM, EXCEPT AS MAY OTHERWISE BE PROVIDED IN WRITING BY DIGITAL.
     /
     /DIGITAL EQUIPMENT CORPORATION ASSUMES NO RESPONSIBILITY FOR THE USE
     /OR RELIABILITY OF ITS SOFTWARE ON EQUIPMENT THAT IS NOT SUPPLIED BY
     /DIGITAL.
     /
     /
     /
     /
     /







				      8-1

			     DEMONSTRATION PROGRAM


     /RTS8 V2 EXEC PARAMETERS - EDITED BY USER
     PDP8E=1
     PDP12=0
     EAE=0
     PWRFAL=0
     KL8A=0	     /NUMBER OF KL8A'S IN USE
		     /I.E. 1 IF ONE KL8A (UP TO 4 LINES)
     HGHFLD=30
		IFDEF	CUR    <
		IFNZRO	HGHFLD-CUR&4000 <CURBIG,_ERROR_>>	
				/FLAG WARNING IF UNDEFINED FIELD SEEN
     NTASKS=23
     CHECKP=1
     PARTNS=1
		/COMMON PARTITIONS ARE NUMBERED FROM 0 TO N-l)

     /COMMON TASK NUMBERS - EDITED BY USER
     /IT IS ADVISABLE TO DEFINE ALL TASKS MERE, NAMES GIVEN BELOW
     /ARE USED BY SOME SYSTEM TASKS AND SHOULD REMAIN COMMENTED OUT
     /IF THE CORRESPONDING TASK IS NOT INCLUDED IN THE SYSTEM

     /PWRF=	      /POWER FAIL HANDLING TASK
     CLOCK=1
     SWAPPER=16
     TTY=2
     LPT=3
     MCR=4
     /DTA=		/DECTAPE DRIVER TASK
     /LTA=		/LINCTAPE DRIVER TASK
     RK8=7
     /RF08=		/RF08 DISK DRIVER TASK
     /DF32=		/DF32 DISK DRIVER TASK
     /CSA=		/CASSETTE DRIVER TASK
     /CSAF=		/CASSETTE FILE SUPPORT TASK
     /UDC=		/UNIVERSAL DIGITAL CONTROLLER TASK
     /RX8A=		/FIRST FLOPPY CONTROLLER
     /RX8B=		/SECOND FLOPPY CONTROLLER
     /RX8C=		/THIRD FLOPPY CONTROLLER
     /RX8D=		/FOURTH FLOPPY CONTROLLER
     OS8=NTASKS
     OS8F=15
     NR20=20
     NR22=22
     /DDCMP=		/DDCMP TASK FOR DECNET
     /NSP=		/NETWORK SERVICES PROTOCOL TASK
     /NIP=		/NETWORK INFORMATION PROGRAM
     /TLK=		/NETWORK TERMINAL COMMUNICATIONS TASK TRANSMITTER
     /LSN=		/NETWORK TERMINAL COMMUNICATIONS TASK RECEIVER
     /NULL8A=		/NULL JOB FOR PDP-8/A
     /EXIT=		/EXIT TASK
     /DKC8A=		/AUXILIARY DKC8A HANDLER

     /SOFTWARE PARAMETERS - EDITED BY USER



				      8-2

			     DEMONSTRATION PROGRAM


	     XLIST	1
	     IFDEF	OS8	<
	     XLIST	LSTFLG
     OSFLDS=2
     OSTTDV=31
     OSKBDV=30
		        /DEFAULT IS OSTTDV-I
     OSSYSD=RK8
     OSFILL=0
			/(EG 4 FOR 2400 BAUD VT05)
     /OS8ORG=		/ORIGIN (IN FIELD 0)
	     XLIST	1>
	     IFDEF	MCR   <
	     XLIST	LSTFLG
     /MCRCLK=		/0 IF MCR TOO FACILITIES TO BE OMITTED (DEFAULT =1)
     MCRSYS=1
			/1 IF DESIRED (DEFAULT)
     /MCRFLD=		/FIELD OF MCR
     /MCRPRT=		/PARTITION NUMBER OF MCR (IF NON-RESIDENT)
     /MCRCDV=		/CONSOLE TO BE USED BY MCR, E.G. TTY
			/DEFAULT IS TTY
	     XLIST 1>
	     IFDEF CLOCK   <
	     XLIST LSTFLG
     CLKTYP=0
     CLKQLN=20
		   /MAY BE CHANGED BY USER
     DECIMAL
     HERTZ=l000
     SHERTZ=1
	     IFNZRO	CLKTYP&1 <HERTZ=1750>	/FORCE DK8EP,KW12 TO 1 KHZ
     	     OCTAL
	     XLIST	1>
	     IFDEF	LPT	<
     /LPTLOC=
     /LPTFLD=
	     >
	     IFDEF	DTA	<
     /DTALOC=
     /DTAFLD=
     	     >
	     TBLLST= 0		/SET TO 'LSTFLG' IF YOU DON'T DESIRE
				/TO SEE TABLES WHEN PARAMETER FILE IS
				/NOT LISTED.

     /SYSTEM LOCATIONS:

     MSGTBL= 1200-2			/TASK MESSAGE TABLE
     TSTABL= NTASKS+2^2+MSGTBL-4	/TASK STATE TABLE - HOLDS
					/TASK LINK,UM,DF,IF,PC,AC,MQ
     TFTABL= NTASKS+2^4+TSTABL-1	/TASK FLAGS TABLE - HOLDS
					/TASK STATUS FLAGS
	     XLIST	1
	     IFDEF	SWAPPER
	     XLIST	LSTFLG

				      8-3

			     DEMONSTRATION PROGRAM
     SYS=RK8
     SUNIT=0
	     IFNDEF	SUNIT	<SUNIT= 0>  /DEFAULT SWAP UNIT IS 0

	     FIELD 0
     /
     /PARTITION TABLE (PARTBL) ENTRIES:
     /MUST BE INITIALIZED BY USER AS EXPLAINED IN THE COMMENTS
     /DON'T FORGET TO REMOVE LEADING "/" FROM LINES USED
     /
     RESTBL= TFTABL+NTASKS+2		     /RESIDENCY TABLE
     PARTBL= NTASKS-SWAPPER^2+RESTBL+3&7774  /PARTITION TABLE

             *PARTBL
	     XLIST	1
	     IFNZRO	PARTNS	<
	     XLIST	TBLLST
     MFLD00=1
     ADDR00=00
     SIZE00=1
	     SIZE00^10+MFLD00^10+4000
	     ADDR00
	     ZBLOCK	2
	     XLIST
	     IFNZRO	PARTNS-1	<
	     XLIST	TBLLST
     MFLD01=			/MEMORY FIELD OF PARTITION #1
     ADDR01=			/LOWEST ADDRESS IN PARTITION #1
     SIZE01=			/SIZE OF PARTITION #1 (CORE PAGES)
	     SIZE01^10+MFLD01^10+4000
	     ADDR01
	     ZBLOCK	2
	     XLIST
	     IFNZRO	PARTNS-2	<
	     XLIST	TBLLST
     MFLD02=			/MEMORY FIELD OF PARTITION #2
     ADDR02=			/LOWEST ADDRESS IN PARTITION #2
     SIZE02=			/SIZE OF PARTITION #2
	     SIZE02^10+MFLD02^10+4000
	     ADDR02
	     ZBLOCK	2
	     XLIST
	     IFNZRO	PARTNS-3	<
	     XLIST	TBLLST
     MFLD03=		/PARTITION #3
     ADDR03=
     SIZE03=
	     SIZE03^l0+MFLD03^10+4000
	     ADDR03
	     ZBLOCK	2
	     XLIST
	     IFNZRO	PARTNS-4	<
	     XLIST	TBLLST
     MFLD04=		/PARTITION #4
     ADDR04=
     SIZE04=
	     SIZE04^10+MFLD04^10+4000

				      8-4

			     DEMONSTRATION PROGRAM


	     ADDR04
	     ZBLOCK	2
	     XLIST
	     IFNZRO	PARTNS-5	<
	     XLIST	TBLLST
     MFLD05=		/PARTITION #5
     ADDR05=
     SIZE05=
	     SIZE05^l0+MFLD05^10+4000
	     ADDR05
	     ZBLOCK	2
	     XLIST
	     IFNZRO	PARTNS-6
	     XLIST	TBLLST
     MFLD06=		/PARTITION #6
     ADDR06=
     SIZE06=
	     SIZE06^10+MFLD06^10+4000
	     ADDR06
	     ZBLOCK	2
	     XLIST
	     IFNZRO	PARTNS-7
	     XLIST	TBLLST
     MFLD07=		/PARTITION #7
     ADDR07=
     SIZE07=
	     SIZE07^10+MFLD07^10+4000
	     ADDR07
	     ZBLOCK 	2
	     XLIST 1>>>>>>>>
     /
     /ADDITIONAL PARTITIONS MAY BE DEFINED BY THE USER AS SHOWN ABOVE
     /FURTHERMORE, THE PARTITION TABLE MAY RESIDE ANYWHERE IN FIELD ZERO
     /
	     PRTEND=.	     /NOTE END OF PARTITION TABLE
	     XLIST	1>
	     IFDEF	TTY	<
	     XLIST	LSTFLG
     /       TTDEV=		/PRINTER DEVICE CODE - DEFAULT IS 4
     /       KBDEV= 		/KEYBOARD DEVICE CODE - DEFAULT IS TTDEV-1
     /	     CONSOL=		/1 MEANS CONSOLE TTY (DEFAULT)
     /	     VT50=		/1 ENABLES CTRL/S AND CTRL/Q
     /	     SCOPE=		/1 MEANS TTY CAN DO A BACKSPACE
     /	     FILL=		/NUMBER OF FILL CHARACTERS, I.E. 4
     /	     WIDTH=		/TTY LINE WIDTH (0 MEANS INFINITE), 
				/ DEFAULT IS 120
     /	     TAB= 		/1 IF TTY HAS HARDWARE TABS
     /	     OLDTTY=		/1 TO USE OLD 2-PAGE TTY HANDLER
     /	     LSBOT=		/1 LISTS BOTH HANDLERS (DEFAULT 0)
     /	     TTFLD=		/FIELD OF TTY TASK (TIMES 10)
     /	     TTLOC=		/LOCATION OF TTY TASK

	     XLIST	1>
	     IFNZRO	KL8A	<
	     XLIST	LSTFLG

				      8-5

			     DEMONSTRATION PROGRAM


     /KL8ADV=			/KL8A DEVICE CODE - DEFAULT IS 40
     /KL8ACT=			/KL8A CONNECT ROUTINE PAGE - DEFAULT IS 7400
	     XLIST	1>
	     IFDEF	EXIT	<
	     XLIST	LSTFLG
     /EXITFLD=		/FIELD OF EXIT TASK (TIMES 10)
     /EXITLOC=		/LOCATION OF EXIT TASK
	     XLIST	1>
	     XLIST	LSTFLG

	     IFNDEF	PDP8E	<PDP8E=1>
	     IFNDEF	PDP12	<PDP12=0>
	     IFNDEF	EAE	<EAE=0>
	     IFNDEF	PWRFAL	<PWRFAL=0>
	     IFNDEF	KL8A	<KL8A=0>

	     XLIST	1
	     IFDEF	NSP	<
	     XLIST	LSTFLG
     MAXCCB=		/NUMBER OF LOGICAL CHANNELS (CCB'S) BEING USED
			/E.G. 3 FOR 3 CHANNELS
			/THESE ARE NUMBERED 1,2,3
     MAXNOD=		/NUMBER OF NODE NAMES IN NODE TABLE
     NSPFLD=		/FIELD OF NSP TASK AND MOST NETWORK TABLES (E.G. 30)
			/(TABLES INCLUDE CCBTAB, LNKTAB, NODTAB AND NETTAB)
     NSPLOC= 2600 	/ORIGIN OF NSF TASK, MUST BE .LE. 3200
			/THE DEFAULT IS CURRENTLY 3200
     NODNUM=		/NODE NUMBER OF THIS NODE

	     /IMPORTANT RELATIVE ORIGINS WITHIN NETWORKS TASKS

	     DRLXIT= NSPLOC+4400 	/ADDRESS OF AST DE-QUEUER
	     CCBTAB= DRLXIT+200 	/ADDRESS OF CCB TABLE
	     NODTAB= CCBTAB+100 	/ADDRESS OF NODE TABLE
	     NETTAB= NODTAB+50 		/ADDRESS OF NETWORK 'INFORMATION' 
					/ TABLE

     /THE DEFAULT NETWORKS TASKS USE CORE AS FOLLOWS:

     /DDCMP: PAGE 0, 0200-3577 		(l LINE, 2 PAGE NODE POOL)
     /NSP:   PAGE 0, 3200-7577


     /NETWORK TASKS USE PAGE 0 AS FOLLOWS:

     /DDCFLD: 	     10-12, 30-77
     /NSPFLD	     15-17, 77-177

     /NODE TABLE ENTRIES

     /EACH ENTRY HAS THE FORM
     /WORDS 1-3      NODE NAME (6-BlT, 0-PADDED)
     /WORD 4	     LINE NUMBER
     /WORD 5	     BIT 0=1 IF ADJACENT NODE
     /		     BITS 4-11 CONTAIN NODE NUMBER

				      8-6

			     DEMONSTRATION PROGRAM


	     IFDEF TASK <  IFZERO TASK-NSP <
	     FIELD NSPFLD%10
	     *NODTAB

     NODTAB, TEXT   /NAME/
	     0			/LINE NUMBER
	     0			/NODE NUMBER
	     *NETTAB+4
	     NODNUM		/OUR NODE NUMBER
	     TEXT   /NAME/ 	/OUR NODE NAME
	     FIELD 0
	     >>
	     >

	     XLIST   1
	     IFDEF   DDCMP
	     XLIST   LSTFLG
     MAXLIN=	     /NUMBER OF PHYSICAL LINES BEING USED
		     /E.G. 3 FOR 3 LINES
		     /THESE ARE NUMBERED 0,1,2
     MAXPKT= 24	     /SET TO NUMBER OF NODE POOL PACKETS TO ALLOW
		     /THE NODE POOL EXISTS AT THE END OF DDCMP
		     /JUST BEFORE THE LCB TABLE (SIMILAR TO THE CLOCK QUEUE)
		     /EACH PACKET REQUIRES 14 WORDS OCTAL, (ABOUT 10. PER 
		     /PAGE) (THE DEFAULT REQUIRES 2 PAGES CORE)
     /KG8E=	     /SET TO IOT SKELETON IF KG8E IS PRESENT (E.G. 6110)
     UDCFLD=	     /FIELD OF DDCMP TASK,LCBTAB AND 'NODE POOL' (E.G. 20)
		     /THIS FIELD MUST BE DIFFERENT FROM NSPFLD
     DDCLOC= 0200    /ORIGIN OF DDCMP TASK
		     /THE ABOVE MUST BE BELOW 5000-SIZE OF NODE POOL AND 
		     /LCBTAB. THE DEFAULT IS CURRENTLY 200

     LCBSIZ= 32	     /GLOBAL DEFINITION OF LCB SIZE (DO NOT ALTER)
     PKSIZE= 14      /GLOBAL DEFINITION OF PACKET SIZE (DO NOT ALTER)

	     DDCFNC= DDCLOC	  /ADDRESS OF DDCMP 'FUNCTION CALL' ROUTINE
	     HEADPK= DDCLOC+3020  /ADDRESS OF START OF PACKET FREELIST
	     LCBTAB= MAXPKT^PKSIZE+HEADPK  /ADDRESS OF LINE CONTROL BLOCK TABLE

	     /IMPORTANT NETWORKS PAGE 0 GLOBALS

	     DDCEF=  46	     /DDCMP I/O EVENT FLAG
	     FREHD=  47      /LOCATION OF I/O PACKET FREELIST HEAD
	     DDCTL=  50      /POINTS TO TAIL OF DDCMP INPUT QUEUE
	     DDCHD=  51	     /POINTS TO HEAD OF DDCMP INPUT QUEUE
	     ATNINP= 52	     /POINTS TO TRANSMIT COMPLETE RING BUFFER
	     OHDR=   55	     /LOCATION OF HEADER BUFFER FOR TRANSMITS
	     OCRCL=  63      /HEADER CRC FOR TRANSMITS
	     ODCRCL= 65      /DATA CRC FOR TRANSMITS
	     OUTCDF= 67	     /DATA DESCRIPTOR FOR TRANSMITS
	     DDCUSR= NSP     /DEFAULT USER OF DDCMP TASK
	     XLIST   1>




				      8-7

			     DEMONSTRATION PROGRAM


	     XLIST   1
	     IFDEF   NIP	<
	     XLIST   LSTFLG
     /NIPFLD=		     /FIELD OF NIP (TIMES 10)
     /NIPLOC=		     /LOCATION OF NIP
     /NIPART=		     /PARTITION FOR NIP
     /SKIMP=		     /SET TO 1 TO GET SHORT NIP


     /NIPLOG=		     /DEVICE NIP OUTPUTS TO
			     /DEFAULT IS LPT IF IT EXISTS (OTHERWISE TTY)
     /NIPRES=		     /LOCATION FOR RESIDENT PORTION OF NIP
			     /REQUIRED ONLY IF NIPART DEFINED
			     /DEFAULT IS NIPLOC-200
	     XLIST   1       >

	     IFDEF   TLK     <
	     XLIST   LSTFLG
     /TLKFLD=		     /FIELD OF TLK TASK
     /TLKLOC=		     /START Of TLK TASK
     TLKCHN=	     /CCB CHANNL TO ASSIGN TO TLK TASK
	     XLIST   1	     >
	     IFDEF   LSN     <
	     XLIST   LSTFLG
     /LSNFLD=		     /FIELD OF LSN TASK (TIMES 10)
     /LSNLOC=		     /START OF TLK TASK
     LSNCHN=	      /CCB CHANNL TO ASSIGN TO LSN TASK
	     XLIST    1	     >
	     XLIST    LSTFLG


     /EQUIVALENCES
     AC7776= CLL STA RAL
     AC7775= CLL STA RTL
     AC4000= CLA STL RAR
     AC3777= CLL STA RAR
     AC2000= CLA STL RTR
     AC0002= CLA STL RTL

     /MONITOR CALL VALUES:

     CAL=    JMS     20		/CALL THE EXECUTIVE
     POSTDS= JMP I   24		/DISMISS AN INTERRUPT
     WAITM=  JMS I   25		/WAIT FOR MULTIPLE EVENTS

		     /NOTE "**" MEANS CRITICAL VALUE MAY NOT
		     /BE CHANGED WITHOUT MODIFYING SYSTEM CODE!!
     SEND=   0	     /SEND MESSAGE
     RECEIV= 1       /RECEIVE MESSAGE
     WAITE=  2	     /WAIT FOR EVENT FLAG
     RUN=    3	     /CONTINUE TASK EXECUTION
     SUSPND= 4	     /SUSPEND TASK EXECUTION
     POST=   5	     /POST AN EVENT FLAG
     SKPINS= 6       /INSERT CODE INTO INTERRUPT SKIP CHAIN
     DERAIL= 7	     /INITIATE END-ACTION

				      8-8

			     DEMONSTRATION PROGRAM


     BLKARG= 10	     /BLOCK TASK FOR REASON SPECIFIED IN ARG
     SENDW=  11	     /SEND MESSAGE AND WAIT
     UNBARG= 12	     /UNBLOCK TASK FOR REASON SPECIFIED IN ARG
     RESCHD= 13	     /FORCE A RESCHEDULE
     WAITX=  14	     /WAIT FOR EXACTLY THIS EVENT FLAG
     FREE=   4000    /**FREE PARTITION

	     XLIST   1
	     IFDEF UDC    <
	     XLIST   LSTFLG
	     AO=0;DO=1;DI=2;GC=3;EC=4;RC=5
	     DC=6;ECT=7;CS=10;DCT=11;AI=12
	     XLIST   1>
	     XLIST   LSTFLG

     /TASK STATUS FLAGS:
     
     NONRWT= 4000    /**NONRESIDENT TASK WAIT
     EFWT=   2000    /EVENT FLAG WAIT
     RUNWT=  1000    /SCHEDULE WAIT
     SWPWT=  0400    /**SWAPPER WAIT
     EFRMWT= 0200    /EVENT FLAG OR MESSAGE WAIT
     USERWT= 0100    /USER SPECIFIED WAIT
     ENABWT= 0040    /ENABLE WAIT
     MSGWT=  0020    /MESSAGE WAIT
     NETWT=  0010    /NETWORK WAIT (RESERVED FOR POSSIBLE FUTURE USE)
     DNEWT=  0001    /**DOES NOT EXIST WAIT

     	     IFNZRO  KL8A    <IFNDEF KL8ACT  <
	     KLUD=   KL8A-l/3^200
	     KL8ACT= 7400-KLUD>>

     TSWFLG= 35	     /TASK SW INHIBIT FLAG    IN FIELD 0
     TODL=   36      /LOW ORDER TIME OF DAY   IN FIELD 0
     TODH=   37	     /HIGH ORDER TIME OF DAY  IN FIELD 0
     DATE=   40	     /DATE IN OS8 FORMAT      IN FIELD 0
     MCREF=  41	     /MCR START EVENT FLAG    IN FIELD 0

    /SOME USEFUL EQUATES FOR TTY AND LPT MESSAGES:

	     NOPACK=4000     /TEXT IS NOT PACKED IN 6-BIT
	     NOCRLF=2000     /OUTPUT SHOULD NOT BE FOLLOWED BY CR/LF
	     IND=1000	     /OUTTXT PTS TO FIRST WORD OF TEXT
	     NOLINE=400	     /INPUT IS IN CHARACTER MODE
	     ASSGN=200	     /ASSIGNS DEVICE
	     KL8ALINE=100    /USED TO SPECIFY A LINE OF A KL8A

	     XLIST   1
	     IFDEF   CLOCK   <
	     XLIST   LSTFLG
            /SOME USEFUL EQUATES FOR STANDARD CLOCK MESSAGES:





				      8-9

			     DEMONSTRATION PROGRAM


	     MARKTIME=       0	  /POST EVENT FLAG AFTER SPECIFIED INTERVAL
	     SCHEDULE=       1000 /RUN TASK AFTER SPECIFIED INTERVAL
	     TIMOUT=         2000 /DERAIL TASK AFTER SPECIFIED INTERVAL
	     PERIODICALLY=   2000 /USED AS MODIFIER TO 'SCHEDULE'
				  /RE-QUEUES RUN REQUEST AFTER SPECIFIED 
				  /INTERVAL E.G. 'SCHEDULE FOO PERIODICALLY'
	     CANCEL=	     7000 /DELETE ALL REQUESTS FROM SPECIFIED TASK 
				  /FROM QUEUE
	     XLIST   1>

	     XLIST   1 	     /FORCE LISTING OFF
	     IFDEF   TASK    <
	     XLIST

     /TASK TABLE SETUP - "TASK", "CUR","INIWT", AND "START"
     /MUST BE DEFINED BY TASK:

	     IFNDEF  INIWT   <INIWT=0>
	     IFNDEF  INIWT2  <INIWT2=0>
	     IFNDEF  INIWT3  <INIWT3=0>

	     *TASK^2+MSGTBL
	     ZBLOCK 2	     /MESSAGE BUFFER INITIALLY CLEAR
	     *TASK^4+TSTABL
	     CUR%l0+CUR      /INITIAL FLAGS
	     START
	     0		     /INITIAL AC 0
	     XLIST;   IFDEF  VERS <
	     XLIST
	     VERS	     /INITIAL MQ
	     XLIST    >
	     XLIST
	     *TASK+TFTABL
	     INIWT
	     XLIST
	     >

	     IFDEF TASK2     <
	     XLIST
	     *TASK2^2=MSGTBL
	     ZBLOCK 2	      /MESSAGE BUFFER INITIALLY CLEAR
	     *TASK2^4+TSTABL
	     CUR2%10+CUR2     /INITIAL FLAGS2
	     START2
	     0		      /INITIAL AC 0
	     XLIST;   IFDEF   VERS2   <
	     XLIST
	     VERS2	      /INITIAL MQ
	     XLIST    >
	     XLIST
	     *TASK2+TFTABL
	     INIWT2
	     XLIST
	     >


				      8-10

			     DEMONSTRATION PROGRAM


	     IFDEF   TASK3    <
	     XLIST
	     *TASK3^2+MSGTBL
	     ZBLOCK 2	       /MESSAGE BUFFER INITIALLY CLEAR
	     *TASK3^4+TSTABL
	     CUR3%10+CUR3      /INITIAL FLAGS3
	     START3
	     0		       /INITIAL AC 0
	     XLIST;  IFDEF     VERS3   <
	     XLIST
	     VERS3	       /INITIAL MQ
	     XLIST   >
	     XLIST
	     *TASK3+TFTABL
	     INIWT3
	     XLIST
	     >

	     IFDEF   TASK     <
	     IFDEF   PARTNO   <
	     XLIST

     /RESIDENCY TABLE (RESTBL) ENTRY:

     /INITIALIZED FOR NONRESIDENT TASKS ONLY

	     *TASK-SWAPPER-1^2+RESTBL
	     PARTNO^4+PARTBL+CPABLE+CPABLE+WRITE
	     XLIST
	     IFNDEF  SWAPPER <NOSWAP,_ERROR_>	/SWAPPER MISSING
	     IFNZRO TASK-SWAPPER&4000    <SWPRIO,_ERROR_>/NON-RESIDENT TASK
					  /HAS PRIORITY HIGHER THAN SWAPPER
	     >>

	     IFDEF   PARTNO  <
	     IFNDEF  TASK    <NOTASK,_ERROR_>	/PARTITION BUT NO TASK
	     IFNDEF  SWAPPER <NOSWAP,_ERROR_>	/PARTITION BUT NO SWAPPER
	     IFNDEF  PARTNO  <NOPART,_ERROR_>	/MISSING PARTITIONS
	     IFZERO  PARTNO-PARTNS&4000 <PRTERR,_ERROR_> /PARTNO.GE.PARTNS
	     >
	     XLIST  0















				      8-11

			     DEMONSTRATION PROGRAM


     8.2  NONRESIDENT TASK LISTINGS

     The following are listings of nonresident tasks (NR20 and NR22):


     8.2.1  Nonresident Task NR20

     TASK=20

	    0020  TASK=20
	    0020	  TASK=20
	    0400	  START=400
	    0001	  WRITE=1
	    0001	  CPABLE=1
	    0010	  CUR=10
	    5000	  INIWT=RUNWT+NONRWT
	    0000	  PARTNO=0
	    0001	  FIELD CUR%10
	    0400	  *400
     10400  4020	  CAL
     10401  4011	  SENDW+FREE
     10402  0001	  CLOCK
     10403  0600	  SLPMSG
     10404  4020	  CAL
     10405  4011	  SENDW+FREE
     10406  0003	  LPT
     10401  0606	  LPTMSG
     10410  5200	  JMP START
	    0600	  *600
     10600  0000	  SLPMSG, ZBLOCK 3
     10603  0000	  0
     10604  0000	  0;SHERTZ
     10605  0001
     10606  0000	  LPTMSG, ZBLOCK 3
     10611  0000 	  0
     10612  0000	  0
     10615  2401	  TEXT /TASK 20 RUNNING/
     10614  2313
     10615  4062
     10616  6040
     10617  2225
     10620  1616
     10621  1116
     10622  0700












				      8-12

			     DEMONSTRATION PROGRAM


     8.2.2  Nonresident Task NR22

     TASK=22

	    0022  TASK=22
	    0022	  TASK=22
	    0400	  START=400
	    0001	  WRITE=1
	    0001	  CPABLE=1
	    0010	  CUR=10
	    5000	  INIWT=RUNWT+NONRWT
	    0000	  PARTNO=0
	    0001	  FIELD CUR%10
	    0400	  *400
     10400  4020	  CAL
     10401  4011	  SENDW+FREE
     10402  0001	  CLOCK
     10403  0630	  SLPMSG
     10404  4020	  CAL
     10405  4011	  SENDW+FREE
     10406  0003	  LPT
     10407  0636	  LPTMSG
     10410  5200	  JMP START
	    0630	  *630
     10630  0000	  SLPMSG, ZBLOCK 3
     10633  0000	  0
     10634  0000	  0;SHERTZ
     10635  0001
     10636  0000	  LPTMSG, ZBLOCK 3
     10641  0000	  0
     10642  0000	  0
     10643  2401	  TEXT /TASK 22 RUNNING/
     10644  2313
     10645  4062
     10646  6240
     10641  2225
     10650  1616
     10651  1116
     10652  0700

















				      8-13

			     DEMONSTRATION PROGRAM


     8.3  ASSEMBLY AND LOAD PROCEDURE

     The assembly and load procedure for the demonstration  program  is  as
     follows:


     .PAL RTS8<PARAM,RTS8
     ERRORS DETECTED:  0
     LINKS GENERATED:  0 

     .PAL CLOCK<PARAM,CLOCK
     ERRORS DETECTED:  0
     LINKS GENERATED:  0 

     .PAL MCR<PARAM,MCR
     ERRORS DETECTED:  0
     LINKS GENERATED:  0 

     .PAL OS8SUP<PARAM,OS8SUP
     ERRORS DETECTED:  0
     LINKS GENERATED:  0 

     .PAL TTY<PARAM,TTY
     ERRORS DETECTED:  0
     LINKS GENERATED:  0 

     .PAL LPT<PARAM,LPT
     ERRORS DETECTED:  0
     LINKS GENERATED:  0 

     .PAL RK8E<PARAM,RK8E
     ERRORS DETECTED:  0
     LINKS GENERATED:  0 

     .PAL NR20<PARAM,NR20
     ERRORS DETECTED:  0
     LINKS GENERATED:  0 

     .PAL NR22<PARAM,NR22
     ERRORS DETECTED:  0
     LINKS GENERATED:  0 

     .PAL SWAP<PARAM,SWAP
     ERRORS DETECTED:  0
     LINKS GENERATED:  0 

     .R ABSLDR
     *NR20$
     .SA SYS NR20 10400-10577

     .R ABSLDR
     *NR22$
     .SA SYS NR22 10400-10577



				      8-14

			     DEMONSTRATION PROGRAM


     .R ABSLDR
     *RTS8,MCR,CLOCK,RK8E,TTY,LPT,OS8SUP
     *SWAP,NR20,NR22$
     .SA SYS RTS8V2

     This example shows the assembly of the parameter file and  the  source
     task  itself.   The  binaries of each nonresident task are then loaded
     into memory, and their nonresident portions saved on the swap  device.
     All  tasks  are  then loaded using the ABSLDR with the RTS/8 Executive
     being loaded first.  Finally, the core  image  of  all  the  tasks  in
     memory is saved using the OS/8 SAVE command.



     8.4  NONRESIDENT TASK ASSIGNMENT AND EXECUTION

     The following is the execution of  RTS/8  showing  the  assignment  of
     tasks NR20 and NR22 to the system.

     .R RTS8V2
     *NR20=20
     *NR22=22
     *$>SY
     01  CLCK O
     02  TTY  M
     03  LPT  M
     04  MCR
     07  RK8  M
     15  OS8F M
     16  SWAP R
     20	      R N
     22	      R N
     23  OS8  E
     >RE 20
     RE> 22
     >EXIT
     .

     In  the  above  example,  the  user  terminates  the  installation  of
     nonresident  tasks  with  an ALTMODE, and returns to the MCR. A SYstat
     command is executed which prints a system status report  (see  Section
     6.2.9).   The REquest command is then used to run tasks NR20 and NR22.
     Shown below is output from tasks NR20 and NR22 on the line printer.

     TASK 20 RUNNING
     TASK 20 RUNNING
     TASK 20 RUNNING
     TASK 20 RUNNING
     TASK 22 RUNNING
     TASK 20 RUNNING
     TASK 22 RUNNING
     TASK 20 RUNNING

     The EXIT command is typed to terminate RTS/8 execution and  return  to
     the OS/8 monitor.

				      8-15






				   CHAPTER 9

		     ADVANCED RTS/8 PROGRAMMING TECHNIQUES


     9.1  PERFORMING A RESCHEDULE
     

     9.1.1  Writing Delicate Code
     
     Frequently, a task needs to manipulate  data  in  another  task  or  a
     common  area.  Since tasks are running 'simultaneously', problems will
     arise if two tasks want to access the same  data  at  the  same  time.
     Consequently,  delicate  code  wants  to  run with interrupts disabled
     while accessing data in another task.
     

				     NOTE

		    Interrupts may be  disabled  temporarily
		    using  either  a  IOF/ION  pair  or,  on
		    machines with memory  extension,  a  CIF
		    instruction  which  inhibits  interrupts
		    until the execution of the next  JMP  or
		    JMS instruction.


     For example, suppose Task A increments location COUNT occasionally and
     Task  B  decrements  location  COUNT  from time to time during program
     execution.  The code might look like the following:

	  /TASK A
	  LOOPA,	 .
			 .
			 .
	  X,		 ISZ COUNT
			 .
			 .
			 .
			 JMP LOOPA
	  COUNT,	 0

	  /TASK B
	  LOOPB,	 .
			 .
			 .
			 STA
	  Y,		 TAD COUNT
	  Z,		 DCA COUNT






				      9-1

		     ADVANCED RTS/8 PROGRAMMING TECHNIQUES


			 .
			 .
			 JMP LOOPB

     If Task A increments COUNT the  same  number  of  times  that  Task  B
     decrements COUNT, it would be assumed that COUNT would be 0 at the end
     of the program.  However, this is not  necessarily  so  since  a  race
     condition can occur.

     Suppose that Task A has a higher priority than Task B, and Task  A  is
     waiting  for  an  event  to occur with COUNT currently containing a 6.
     Task B is ready to decrement  COUNT.   However,  an  interrupt  occurs
     after location Y has been executed.  The AC contains a 5 and Task B is
     ready to store a 5 back into COUNT.  The  interrupt  service  routine,
     noting  that  the  event Task A was waiting for has just occurred, now
     suspends Task B and resumes Task A.  Task A now bumps COUNT from 6  to
     7,  and  then  goes  back  to  sleep.  Task B then resumes with the AC
     containing a 5 and stores a 5 into COUNT which is incorrect for proper
     program execution.
     
     This situation is prevented from  happening  by  disabling  interrupts
     around  the  delicate code.  Either of the following two solutions can
     be employed:

	     Solution 1		      Solution 2

	  /TASK   B		   /TASK   B
	  LOOPB,  .		   LOOPB,  .
		  .			   .
	          .			   .
		  STA			   CIF CUR
		  IOF			   STA
	  Y,	  TAD COUNT	   Y,	   TAD COUNT
	  Z,	  DCA COUNT	   Z,	   DCA COUNT
		  ION
		  .			   .
		  .			   .
		  JMP LOOPB		   JMP LOOPB

     Solution 2 (only usable on machines with memory  extension)  uses  the
     CIF  instruction  since  it  temporarily inhibits interrupts until the
     next JMP or JMS instruction is executed.
     
     
     9.1.2  Inhibiting Task Switching
     
     Although the procedure in the previous section  can  be  used,  it  at
     times  can  be very inefficient.  If it is desired to perform a lot of
     manipulation on data which could be accessed by other tasks, it may be
     inappropriate  to turn off interrupts.  Inhibiting interrupts for long
     periods of time could affect other portions of the system where  timed
     events  are  very  important.   Also,  an  interrupt  can be lost (for
     example,  clock  interrupts)  if  interrupts  are  turned  off  for  a
     significant amount of time.


				      9-2

		     ADVANCED RTS/8 PROGRAMMING TECHNIQUES

     
     For this case, another solution is possible.  A task  can  inform  the
     RTS/8 Executive that it wants to continue to run, and that while it is
     executing a certain piece of code, no other task should run even if  a
     task  of  higher  priority becomes runnable.  This process is known as
     inhibiting task switching.

     Task switching should be inhibited only  under  unusual  circumstances
     and   performed   with  care.   While  task  switching  is  inhibited,
     interrupts may still occur and the interrupt service routine will  get
     control.   However,  if  task  switching  is  inhibited, the interrupt
     service routine will always return control  to  the  interrupted  task
     after  the  interrupt  has been serviced even if higher priority tasks
     are now runnable.
     

				     NOTE

		    If the user wishes  to  manipulate  data
		    which  is accessed by an interrupt-level
		    routine, interrupts  must  be  inhibited
		    since  inhibiting  task  switching alone
		    will not be sufficient in this case.

     There are two methods  of  inhibiting  task  switching  which  are  as
     follows:

     Method 1: Task switching is automatically inhibited whenever a  task's
     PC  is  less  than  100.   Thus,  delicate code could be placed in the
     bottom of page 0 of any field.

     Method 2: A task may inhibit task switching by zeroing location 35  in
     field  0.   This  location is symbolically referred to as TSWFLG (task
     switching flag) and is defined as such  in  the  parameter  file.   In
     either  case, after the task is through with its delicate code, it may
     not be sufficient for  the  task  to  reset  TSWFLG  to  its  original
     value(l).   This  is  due  to  the  fact  that there may be some other
     higher-priority task that is entitled to run but did not  run  because
     task  switching  was  inhibited.   The  user  can  find  this  out  by
     interrogating location TSWFLG.  If another task became runnable  while
     task  switching  was  inhibited,  the  RTS/8  executive  sets the task
     switching flag to -1.  When a task is ready to  allow  task  switching
     again,  it must examine this flag before resetting it to 1.  If it was
     -1, the  task  returns  control  to  the  RTS/8  scheduler.   This  is
     performed by using the RESCHD ER as follows:

	  CAL
	  RESCHD

     This ER causes RTS/8 to perform a reschedule that allows the  runnable
     task of highest priority to be executed.  If a user does not perform a
     RESCHD after re-enabling task switching, then a higher  priority  task
     which  is  entitled  to  run  might  not  run until the next interrupt
     occurs.  The interrupt may never occur, or if it does, it may  be  too
     late for proper program execution.


				      9-3

		     ADVANCED RTS/8 PROGRAMMING TECHNIQUES


     The preferred code for inhibiting task switching for Task B which  was
     described previously is shown below:

	  /TASK   B
	  LOOPB,  .
		  .
		  .
		  CDF 0
		  DCA I (TSWFLG   /INHIBIT TASK SWITCHING
		  STA
	  Y,	  TAD COUNT
	  Z,	  DCA COUNT
		  ISZ I (TSWFLG   /ALLOW TASK SWITCHING
		  JMP .+3	  /SHOULD WE RESCHEDULE?
		  CAL		  /YES
		  RESCHD
		  CDF CUR	  /NO
		  .
		  .
		  .
		  JMP LOOPB


				     NOTE

		    Interrupt level routines should not look
		    at or set the TSWFLG.


     A summary of TSWFLG states is shown in Table 9-1.


				   Table 9-1
		Summary of Task Switching Flag (TSWFLG) States

	 --------------------------------------------------------
	 |	  TSWFLG State		  |	   Value	|
	 |--------------------------------|---------------------|
	 | Task switching allowed	  |	      1		|
	 | Task switching inhibited	  |	      0		|
	 | Task switching inhibited;	  |			|
	 | reschedule as soon as possible |	     -1		|
	 --------------------------------------------------------


     9.2  EXECUTIVE REQUESTS FOR ADVANCED APPLICATIONS


     9.2.1  WAITM - Waiting for Multiple Event Flags

     Sometimes it is desirable to wait for a logical  combination  (AND  or
     OR) of Event Flags.  Waiting for the logical AND of two Event Flags is
     quite simple.  The sequence:



				      9-4

		     ADVANCED RTS/8 PROGRAMMING TECHNIQUES


	  CAL
	  WAITE
	  A			   /WAIT FOR EVENT FLAG A
	  CAL
	  WAITE
	  B			   /AND THEN WAIT FOR EVENT FLAG B

     waits until both A and B have been POSTed.

     Waiting for the logical OR of several event flags  is  more  difficult
     since there is a possible race condition between the various tests and
     the interrupts  (or  task  executions)  which  POST  the  Event  Flags
     involved.   The  key  to  waiting  for  an  OR  of several Event Flags
     successfully is not to allow  any  interrupts  to  occur  between  the
     testing  of the first Event Flag and the placing of the task in a Wait
     state if none of the flags were POSTed.

     This is accomplished by using a special sequence of instructions and a
     special  RTS/8  call  named  WAITM.  WAITM is defined as JMS I 25.  It
     must be executed with interrupts off, the Instruction Field set  to  0
     and  the  Data Field set to the current field, and it must be followed
     by a word containing the blocking bit(s) to be set in the  Task  Flags
     Table.   The  action of WAITM is equivalent to the action of the RTS/8
     BLKARG ER except that a fast path through the RTS/8 Executive is taken
     and  interrupts  remain off until the blocking bits are on in the Task
     Flags Table.

     For an example of the use of WAITM, assume that a task "TASK" wants to
     test  two  Event  Flags A and B.  If A is POSTed, control should go to
     location ADONE; if B is POSTed control should go  to  location  BDONE.
     If  neither is POSTed, the task must wait until one of them is POSTed.
     The code to perform this function is:

	  TESTAB, IOF			/INTERRUPTS OFF - DELICATE CODE
		  TAD A
		  SNA CLA
		  JMP ADONE		/ADONE MUST TURN INTERRUPTS ON
		  TAD (4000+TASK	/SET A TO "WAITING" STATE
					/INDICATING
		  DCA A			/THAT THIS TASK IS WAITING ON IT
		  TAD B
		  SNA CLA
		  JMP BDONE		/BDONE MUST TORN INTERRUPTS ON
		  TAD (4000+TASK	/SET B TO "WAITING" STATE
					/INDICATING
		  DCA B			/THAT THIS TASK IS WAITING ON IT
		  CIF 0
		  CDF CUR
		  WAITM
		  EFWT			/BLOCK TASK ON EVENT FLAG WAIT
		  JMP TESTAB		/WE'RE BACK - ONE OF THE TWO
					/EVEMT FLAGS HAS BEEN POSTED.
					/GO BACK TO FIND OUT WHICH ONE



				      9-5

		     ADVANCED RTS/8 PROGRAMMING TECHNIQUES


     9.2.2  WAITX - Wait for Exactly This Event Flag
     
     The WAITX ER is similar to the WAITE ER.  The exception is that if the
     Event  Flag  is  not  FINISHED,  the task goes into EORMWT (instead of
     EFWT), and the task's PC in the TSTABL points  back  to  the  location
     containing the CAL of this ER.  Thus, when the task resumes execution,
     it will re-execute the WAITX.  If the EORMWT bit was cleared for  some
     reason  other than the Posting of the Event Flag in question, the task
     will immediately go back into EORMWT.

     Consequently, control will never flow past this ER  unless  the  Event
     Flag  specified  is actually posted (see discussion of DERAIL, Section
     9.2.3).  If a WAITE had been used and  if  the  task  was  waiting  on
     multiple  Event  Flags  (which  can  happen using WAITM), then control
     conceivably could start up after the WAITE ER because some other Event
     Flag,  and  one  that  is  no  longer  cared  about, was posted.  This
     situation can not occur with a WAITX.


     9.2.3  DERAIL - Derail a Task's Execution

     The DERAIL ER modifies the execution of a specified task and transfers
     control   to  a  special  subroutine  of  the  task  to  process  some
     exceptional condition.  It does not cause any wait bits to get set  or
     cleared.

	   Format:  TAD TASKNUM
		    CAL
		    DERAIL
		    ADDR

     This ER simulates a "JMS ADDR" for the task whose number is  contained
     in  TASKNUM  (the "derailed" task).  ADDR is assumed to be in the same
     field in which the derailed task is executing.  The derailed task's PC
     (from  its  Task State Table entry) is stored in ADDR; the PC entry in
     its Task State Table entry is then  set  to  ADDR-~1.   Two  important
     points concerning the operation of the DERAIL ER are as follows:

	  1.  The derailed task's AC, Link, and Data Field settings are not
	      saved  by  the  DERAIL  ER;  therefore they must be saved and
     	      restored by the derail subroutine.  In this sense,  a  derail
	      subroutine is very much like an interrupt at the task level.

	  2.  The contents of the derailed task's Task Flags word  are  not
	      affected  by  the  DERAIL  ER.   If  the derailed task is not
	      runnable, the derail subroutine will not  be  executed  until
	      the task becomes runnable.

     The DERAIL ER is generally used by a high priority task to  signal  an
     emergency  condition  to  lower priority tasks.  An example would be a
     process-control environment where it is sometimes necessary  to  abort
     all  operations  if  the room temperature exceeds some critical value.
     This can be checked by a task which measures room temperature every 10
     seconds.   It is inefficient and unmodular to include shutdown code in
     this "watchdog task" for all machinery  being  controlled.   A  better

				      9-6

		     ADVANCED RTS/8 PROGRAMMING TECHNIQUES


     solution  is to provide a location to which each equipment-controlling
     task can be DERAILED in order to shut down its own piece of equipment.
     The  RTS/8  Power-Fail  task  uses  the DERAIL ER to provide a similar
     facility on power-fail recovery (see Section 4.5), which can  be  used
     to reinitialize a task.

     Example:

     An example of a DERAIL routine is as follows:

	  DENTRY,	  0		  /DERAIL ROUTINE ENTRY POINT
			  DCA SAVAC	  /SAVE AC
			  RAR
			  DCA SAVLNK	  /SAVE LINK
			  RDF
			  TAD (CDF
			  DCA DFRESET	  /SAVE DATA FIELD
			  CDF CUR
			  .		  /HANDLE EMERGENCY CONDITION
			  .
			  .
					  /BRANCH TO 'RESUME' IF YOU WANT
					  /TO RESUME WHERE YOU LEFT OFF
					  /BRANCH TO 'NORESUME' IF NOT
			  .
	  RESUME,	  TAD SAVLNK	  /RESTORE LINK
			  CLL RAL
			  TAD SAVAC	  /RESTORE AC
	  DFRESET,	  HLT		  /RESTORE DF
			  JMP I DENTRY	  /RESUME (SAME FIELD)
	  NORESUME,	  CLA CLL
			  CDF CUR
			  JMP RESTART	  /RESTART TASK
	  SAVAC,	  0
	  SAVLNK, 	  0


     9.2.3.1  Dangers of DERAIL - A task can get into  serious  trouble  if
     it  is  derailed  while already in a derail routine.  If this happens,
     the original PC, AC, link, etc., will be lost.   There  is  no  simple
     solution.   Turning  off  interrupts  in the derail routine may be too
     late to prevent this - the second derail could have  already  occurred
     before the derail routine was even entered the first time.

     Consequently, a user doing a DERAIL should make  sure  that  not  more
     than  one  DERAIL is  done  at  a time.  Alternatively, before doing a
     DERAIL, a task can check an interlock flag (which it must maintain) to
     see  whether  the  target task has been derailed or not.  The test and
     set of such a flag should be performed with interrupts inhibited.
     

     9.2.3.2  Restrictions Using DERAIL -  If a  task  is   not   runnable,
     derailing  it will not make it runnable.  If the task is in Event Flag
     Wait, it will remain in Event Flag Wait until the event occurs.   When
     the  Event  Flag  is POSTed, the task will wake up and begin to run in

				      9-7

		     ADVANCED RTS/8 PROGRAMMING TECHNIQUES


     its  derail  routine  rather  than in  the  mainline  routine.   Thus,
     derailing  a  task to get it to perform some important job immediately
     may not always work.  The task might be in one of the Wait states  and
     may  not  be able to run for some time.  For example, if the task were
     in Receive Wait at the time, the derail routine would not run until  a
     message came in for that task.

     A partial solution around this restriction is to code the task  to  be
     derailed  so  that  it  always  waits on events using WAITX instead of
     WAITE.  Then, if the user wants to derail this task, the task is first
     taken out of MSGWT or EORMWT and then derailed.

     An example of the code for this situation is as follows:

	  TAD TASKNUM
	  CAL
	  UNBARG		   /UNBLOCK THE TASK
	  MSGWT!EORMWT		   /FROM MESSAGE-RELATED WAITS
	  TAD TASKNUM
	  CAL
	  DERAIL
	  DENTRY

     This will work because  both  the  RECEIVE  and  the  WAITX  Executive
     Requests  bump  the PC back to the CAL before going into a Wait state.
     Thus, no harm is done if the task is taken out of that wait state  for
     an  incorrect reason.  When the task resumes running at that point, it
     will re-execute the CAL (RECEIVE or WAITX) and go back into  the  Wait
     state as necessary.  This method will not work if the task was in EFWT
     due to a WAITE ER because the task would resume running  thinking  the
     Event  Flag  had  been  posted  when  in  fact  it  had not.  A way to
     circumvent this (other than WAITX) is for the task to do WAITM instead
     of a WAITE, and poll the Event Flag upon waking up.


     9.3  STARTING PARTITIONS AT AN ARBITRARY BOUNDARY

     The advanced user can start a partition at an  arbitrary  boundary  by
     using the following assembly and loading procedure.  The example given
     assumes that the partition in which the user  writes  the  nonresident
     portion  of  the  task  to run is three pages long (11200-11777).  The
     PAL8 pseudo-operators FIELD and  RELOC  are  used,  and  described  in
     detail in the OS/8 handbook.

	  /TASKX
	  FIELD 1	     /SET FIELD
	  *1000		     /LOAD THIS CODE AT 11000-11577
	  RELOC 1200	     /BUT ASSEMBLE IT TO RUN AT 11200-11777
	  .
	  .
	  <CODE>
	  .
	  .
	  PAGE
	  .

				      9-8

		     ADVANCED RTS/8 PROGRAMMING TECHNIQUES

	  .
	  <CODE>
	  .
	  .
	  RELOC

     The assembly, load and save procedures for the code are:

	  .R PAL8
	  *TASKX<PARAM.PA,TASKX.PA	   (ASSEMBLY OF TASK)
	  .R ABSLDR
	  *TASKX$			   (LOADING OF TASK INTO 11000)
	  .SAVE DEV TASKX 11000-11577	   (SAVING OF TASK-THREE PAGES OF
					   CODE)

     The swapper, upon loading this task, places it into the  partition  at
     11200, which is where it was assembled to run.


     9.4  DIRECT REFERENCES TO SYSTEM TABLES

     A task may directly  interrogate  locations  in  the  RTS/8  Executive
     tables  to  obtain information about itself or any other task, as long
     as the following two restrictions are observed:

	  1.  Due to the interrupt-driven nature of the system, these table
	  entries  may  change  at  any  time; therefore, interrupts should
	  be inhibited between  the  time  these  entries  are  tested  and
	  the  time  that  processing  which  depends  on  the  testing  is
	  completed.  For example, testing the  Message  Queue  Header  for
	  a  task  may  show  no  messages,  but an I/O interrupt occurring
	  immediately after the test might allow  a  higher  priority  task
	  to  run.   This  task  might  send  a  message,  invalidating the
	  result of the  test.   To  prevent  this,  interrupts  should  be
	  turned off during and after the test.

	  2.  System table  entries  may  be  changed  only  through  RTS/8
	      Executive Requests.

     Symbols have been defined in the system parameter  table  that  permit
     symbolic  references  to  be made into these tables symbolically.  The
     symbolic expressions which yield  the  address  of  the  system  table
     entries for task N are:

	  N+TFTABL			   Task Flags Table entry for  task
					   N; if zero, task N is runnable.

	  N^2+MSGTBL			   Input Message Queue  Header  for
					   task  N;  if zero, task N has no
					   messages in its queue.

	  N^4+TSTABL			   First word of Task  State  Table
					   Entry for task N.

	  N^2+RESTBL			   First word  of  Residency  Table
					   entry for nonresident task N.

				      9-9

		     ADVANCED RTS/8 PROGRAMMING TECHNIQUES


     For example, for a task to determine whether it had  messages  in  its
     input queue without issuing a RECEIVE request, the code would be:

	  CDF 0				/EXEC TABLES IN FIELD 0
	  IOF				/TURN INTERRUPTS OFF
	  TAD I (TASK^2+MSGTBL
	  SNA CLA			/ANY MESSAGES?
	  JMP NONE			/NO
	  ION				/YES

     The code at NONE must eventually turn interrupts back on.













































				      9-10







				  APPENDIX A

			RTS/8 DISTRIBUTED SOURCE FILES



     The RTS/8 source files included on the distributed tape are:

     File Name   Task Name	      Task Function

     PARAM.PA		    System parameter file with all  equates  blank.
			    Appropriate values should be inserted to create
			    specific parameter files.
     RTS8.PA		    RTS/8 Executive
     MCR.PA	 MCR 	    Monitor Console Routine
     MCR.PA	 null task  Null task
     OS8SUP.PA   OS8	    OS/8 Support Task
     OS8SUP.PA   OS8F	    OS/8 File Support Task
     PWRF.PA	 PWRF 	    Power Fail Task
     CLOCK.PA	 CLOCK 	    Clock Handler Task
     TTY.PA	 TTY 	    Terminal Driver Task
     LPT.PA	 LPT 	    Line Printer Driver Task
     DTA.PA	 DTA 	    TC08 DECtape Driver Task
     RK8.PA	 RK8 	    RK8 Disk Driver Task
     RK8E.PA	 RK8 	    RK8E Disk Driver Task
     RF08.PA	 RF08/DF32  RF08/DF32 Fixed-Head Disk Driver
			    Task
     CSA.PA	 CSA 	    Cassette Driver Task
     CSAF.PA	 CSAF 	    Cassette File Support Task
     UDCICS.PA   UDC/ICS    Universal Digital Controller/
			    Industrial Controller Subsystem
			    Handler Task
     RXOlRT.PA   RX8A	    Floppy Disk Handler (1st controller)
     RXOlRT.PA   RX8B	    Floppy Disk Handler (2nd controller)
     RXOlRT.PA   RX8C	    Floppy Disk Handler (3rd controller)
     RXOlRT.PA   RX8D	    Floppy Disk Handler (4th controller)
     LTA.PA 	 LTA	    LINCtape Driver Task
     SWAP.PA     SWAPPER    Nonresident Task Swapper
     NULL8A.PA   NULL8A	    Null Task for PDP-8A
     EXIT.PA     EXIT	    Exit Task














				      A-1






				  APPENDIX B

			     RTS/8 COMPONENT SIZES

     The following table gives the approximate size and default origins  of
     each  component  of  the  RTS/8  system.   An RTS/8 memory map showing
     default memory allocation is shown in Figure B-1.  The modules may  be
     placed  anywhere  in  memory at the user's discretion except for RTS8,
     CLOCK and SWAP.  Also, certain modules must be placed in field 0 where
     indicated in the tables.

     The following parameters, which are used in Table B-1, are defined  as
     follows:

	  NTASKS = Number of tasks in system
	  CLKQLN = Number of entries in clock queue
	  MCRSYS = 1 if MCR SYSTAT function desired, else 0
	  MCRCLK = 1 if MCR CLOCK functions desired, else 0
	  KLINES = Number of physical KL8-A lines

     Any fractions from divides should be dropped.


				   Table B-1
			     RTS/8 Component Sizes

     ----------------------------------------------------------------------
     |		   |		    | Number of Pages |			  |
     | Software	   | Default	    | Required (1 page|			  |
     | Component   | Origin	    | =128 words)     |      Comments	  |
     |-------------|----------------|-----------------|-------------------|
     |		   |		    |		      |			  |
     | RTS/8	   | 00200	    | 5+NTASKS/18     |	Must	be     in |
     | Executive   |		    |		      | locations  00200- |
     |		   |		    |		      | 01200.  Uses page |
     |		   |		    |		      |	0  locations  0-3 |
     |		   |		    |		      |	and   20-47   and |
     |		   |		    |		      |	auto-index	  |
     |		   |		    |		      |	register 17.	  |
     |		   |		    |		      |			  |
     | Clock Module| 1st page	    | 3+CLKQLN/22     |	Must be in  field |
     |		   | after end of   |		      | 0. Uses		  |
     |		   | RTS/8 Executive|		      | auto-index	  |
     |		   | (or SWAPPER)   |		      |	register 10.	  |
     |		   |		    |		      |			  |
     | New	   | 03400	    | 3		      |			  |
     | Terminal    |		    |		      |			  |
     | Module, V2  |		    |		      |			  |
     |		   |		    |		      |			  |
     ----------------------------------------------------------------------
						   (Continued on next page)




				      B-1

			     RTS/8 COMPONENT SIZES


			       Table B-1 (Cont.)
			     RTS/8 Component Sizes

     ----------------------------------------------------------------------
     |		   |		    | Number of Pages |			  |
     | Software	   | Default	    | Required (1 page|			  |
     | Component   | Origin	    | =128 words)     |      Comments	  |
     |-------------|----------------|-----------------|-------------------|
     |		   |		    |		      |			  |
     | Old	   | 03400	    | 2		      |			  |
     | Terminal    |		    |		      |			  |
     | Module, V1  |		    |		      |			  |
     |		   |		    |		      |			  |
     | Line Printer| 14400	    | 1		      |			  |
     | Module	   |		    |		      |			  |
     |		   |		    |		      |			  |
     | TC08 DECtape| 14600	    | 2		      |			  |
     | Module	   |		    |		      |			  |
     |		   |		    |		      |			  |
     | RK8E Disk   | 04200	    | 2		      |			  |
     | Module	   |		    |		      |			  |
     |		   |		    |		      |			  |
     | DF32/RF08   | 04400	    | 1		      |			  |
     | Module	   |		    |		      |			  |
     |		   |		    |		      |			  |
     | LINCtape	   | 15000	    | 2		      |			  |
     |		   |		    |		      |			  |
     | RK8 Disk    | 04200	    | 1		      |			  |
     | Module	   |		    |		      |			  |
     |		   |		    |		      |			  |
     | Power Fail  | 10200	    | 1+NTASKS/32     |			  |
     | Module	   |		    |		      |			  |
     |		   |		    |		      |			  |
     | UDC Module  | 10600	    | 7-11 depending  | Uses page 0	  |
     |		   |		    | on table space  |	locations 130-144 |
     |		   |		    | desired.	      |			  |
     |		   |		    |		      |			  |
     | Cassette	   | 13600	    | 3		      |			  |
     | Module	   |		    |		      |			  |
     |		   |		    |		      |			  |
     | Cassette    |13000	    | 3		      | Requires cassette |
     |Label Support|   		    |		      |	handler.	  |
     | Module	   |		    |		      |			  |
     |		   |		    |		      |			  |
     | OS/8 File   | 04600 if OS/8  | 6		      | Requires a mass   |
     | Support 	   |support present,|		      |	storage handler.  |
     | Module 	   | otherwise 	    |		      |	Must run in field |
     |		   | 06200*	    |		      | 0.		  |
     |		   |		    |		      |			  |
     ----------------------------------------------------------------------
     * Moves down by length of KL8A support code if KL8A support present.

						   (Continued on next page)



				      B-2

			     RTS/8 COMPONENT SIZES


			       Table B-1 (Cont.)
			     RTS/8 Component Sizes

     ----------------------------------------------------------------------
     |		   |		    | Number of Pages |			  |
     | Software	   | Default	    | Required (1 page|			  |
     | Component   | Origin	    | =128 words)     |      Comments	  |
     |-------------|----------------|-----------------|-------------------|
     |		   |		    |		      |			  |
     | OS/8 Support| 06200* 	    | 6		      | Must run in field |
     | Task	   |		    |		      | 0 - requires   8K |
     |	   	   |		    |		      |	for OS/8 plus a   |
     |	   	   |		    |		      |	mass     storage  |
     |	   	   |		    |		      |	handler.   Uses	  |
     |	   	   |		    |		      |	page 0  locations |
     |	   	   |		    |		      |	164-177.	  |
     |		   |		    |		      |			  |
     | Monitor     | 17600 minus    |	5+3xMCRCLK+   |	Requires "console"|
     | Console	   | length (15200  | MCRSYS +	      |	terminal handler  |
     |Routine Task | with all 	    |(NTASKS+40)/64.  | and page 0	  |
     |		   | options and    | 		      | locations 100-117.|
     |		   |no KL8A support)|		      | See Table B-2 for |
     |		   |		    |		      | more details.	  |
     |		   |		    |		      |			  |
     | RX01	   | 13200	    | 2		      |			  |
     |		   |		    |		      |			  |
     | SWAPPER	   | 1st page after | 2		      | Must   be   in    |
     |		   | end of RTS/8   |		      |	field 0		  |
     |		   | executive      |		      |			  |
     |		   |		    |		      |			  |
     | EXIT	   | 15000	    | 1/2	      | May relocate	  |
     |		   |		    |		      | within a page	  |
     |		   |		    |		      |			  |
     | NULL8A	   | 13600	    | 1		      |			  |
     |		   |		    |		      |			  |
     | KL8A Support| 17600 minus    | l+KLINES+1      | Must be		  |
     |		   | length	    | 3		      |	in field 0.	  |
     |		   |		    |		      |			  |
     ----------------------------------------------------------------------
     * Moves down by length of KL8A support code if KL8A support present.
















				      B-3

			     RTS/8 COMPONENT SIZES


	      RTS/8 SYSTEM MEMORY MAP (Default Memory Allocation)

     ----------------------------------------------------------------------
     | PAGES   |			FIELD 0  			  |
     |---------|----------------------------------------------------------|
     | 0       |							  |
     |	   200 |-    -							  |
     |	   400 |-    |							  |
     |     600 |-    | RTS/8						  |
     |---------|     | (20 tasks)					  |
     | 1000    |     |							  |
     |     200 |-    |							  |
     |	   400 |-    |							  |
     |     600 |-    V							  |
     |---------|     *							  |
     | 2000    |     | SWAP						  |
     |     200 |-    V							  |
     |	   400 |-    ^							  |
     |     600 |-    | CLOCK						  |
     |---------|     |							  |
     | 3000    |     V							  |
     |     200 |-							  |
     |	   400 |-    -            -					  |
     |     600 |-    |            | TTY,V1				  |
     |---------|     | TTY,V2     _					  |
     | 4000    |     |							  |
     |     200 |-    -   -         -					  |
     |	   400 |-        | RK8E    - RK8    -				  |
     |     600 |-        -                  - RK08			  |
     |---------|                                       ^		  |
     | 5000    |                                       |		  |
     |     200 |-                                      | OS8F		  |
     |	   400 |-                                      |		  |
     |     600 |-                                      |		  |
     |---------|                                       |		  |
     | 6000    |                                       *		  |
     |     200 |-           ^						  |
     |	   400 |-           |						  |
     |     600 |-           | OS8SUP					  |
     |---------|            |						  |
     | 7000    |            |						  |
     |     200 |-           |              ^				  |
     |	   400 |-           *              - KL8ASR			  |
     |     600 |-							  |
     ----------------------------------------------------------------------
							See key below


        Figure B-1  RTS/8 System Memory Map (Default Memory Allocation)







				      B-4

			     RTS/8 COMPONENT SIZES


	      RTS/8 SYSTEM MEMORY MAP (Default Memory Allocation)

     ----------------------------------------------------------------------
     | PAGES   |			FIELD 1  			  |
     |---------|----------------------------------------------------------|
     | 0       |	  						  |
     |	   200 |-  -	  						  |
     |	   400 |-  | PWRF  						  |
     |     600 |-  V      -  						  |
     |---------|          |  						  |
     | 1000    |          |    						  | 
     |     200 |-         |    						  |
     |	   400 |-         | UDCICS    					  |
     |     600 |-         |  						  |    
     |---------|          |  						  |    
     | 2000    |          |  						  |    
     |     200 |-         |  						  |
     |	   400 |-         V  						  |
     |     600 |-  							  |
     |---------|                               -			  |
     | 3000    |                               | CSAF			  |
     |     200 |-          -                   |			  |
     |	   400 |-          | RX01RT            -        -		  |
     |     600 |-          -         -                  |		  |
     |---------|                     - NULL8A           | CSA             |
     | 4000    |                                        |		  |
     |     200 |-  -                                    |		  |
     |	   400 |-  - LPT                                -		  |
     |     600 |-         -						  |
     |---------|          - DTA      -               -			  |
     | 5000    |                     | CTA           - EXIT		  |
     |     200 |-		     -             -			  |
     |	   400 |-                                  |			  |
     |     600 |-                                  |			  |
     |---------|                                   |			  |
     | 6000    |                                   | Large		  |
     |     200 |-                                  | MCR		  |
     |	   400 |-           ^                      |			  |
     |     600 |-           |                      |			  |
     |---------|            | Small                |			  |
     | 7000    |            | MCR                  |			  |
     |     200 |-           |                      |			  |
     |	   400 |-           |                      |			  |
     |     600 |-           -                      -			  |
     ----------------------------------------------------------------------
							See key below


     Figure B-1  RTS/8 System Memory Map (Default Memory Allocation)(cont.)







				      B-5

			     RTS/8 COMPONENT SIZES


     ----------------------------------------------------------------------
     |									  |
     | KEY:								  |
     |									  |
     | RTS/8 modules may vary in size and placement in memory depending   |
     | upon the chosen system configuration.  The following symbology has |
     | been chosen to show component default allocation in memory.	  |
     |									  |
     |	     -	          ^		   ^		    ^		  |
     |	     |		  |		   |		    |		  |
     |	     |		  |		   |		    |		  |
     |	     -		  -		   *		    V		  |
     |									  |
     |     Fixed      Expandable      Relocatable      Relocatable	  |
     |						      and Expandable	  |
     |									  |
     ----------------------------------------------------------------------




				   Table B-2
			      MCR Component Size
 
     ----------------------------------------------------------------------
     |        	 | If less than 34(octal) 	| If 34(octal) or more    |
     |		 | tasks 			| tasks			  |
     |--------------------------------------------------------------------|
     |		 |				|			  |
     | NO SYSTAT | LENGTH:	5 pages		| LENGTH:	6 pages	  |
     | NO CLOCK  | DEF ORIG:	6400		| ORIG:		6200	  |
     |		 | IF NONRS:	6200		| IF NONRS:	6200	  |
     |		 | PART:	6400-7377	| PART:		6400-7577 |
     |		 |				|			  |
     | SYSTAT	 | LENGTH:	6 pages		| LENGTH:	7 pages	  |
     | NO CLOCK  | ORIG:	6200		| ORIG:		6000	  |
     |		 | IF NONRS:	6200		| IF NONRS:	5600	  |
     |		 | PART:	6400-7577	| PART:		6000-7377 |
     |		 |				|			  |
     | CLOCK	 | LENGTH:	10 pages	| LENGTH:	11 pages  |
     | NO SYSTAT | ORIG:	5600		| ORIG:		5400	  |
     |		 | IF NONRS:	5600		| IF NONRS:	5200	  |
     |		 | PART:	6000-7577	| PART:		5400-7377 |
     |		 |				|			  |
     | SYSTAT	 | LENGTH:	11 pages	| LENGTH:	12 pages  |
     | CLOCK	 | ORIG:	5400		| DEF ORIG:	5200	  |
     |		 | IF NONRS:	5200		| IF NONRS:	5200	  |
     |		 | PART:	5400-7377	| PART:		5400-7577 |
     |		 |				|			  |
     ----------------------------------------------------------------------






				      B-6







				  APPENDIX C


			       RTS/8 FLOWCHARTS



     This appendix contains RTS/8 flowcharts that  graphically  show  RTS/8
     system operation.













































				      C-1

			        RTS/8 FLOWCHARTS


		 ***
	       *      *
	      *	 EXEC  *			Calling Sequence:
	       *      *
	         ***				p-1	TAD VAL
		  |				p	CAL
		  |				p+1	FUNCTION CODE
	          V				p+2	ARG1
	   ----------------			p+3	AGR2 (or return)
  	   |  SAVE AC IN  |			p+4	RETURN
	   |    ACARG     |
	   ----------------			CAL = JMS 20
		  |				Thru Current Field:
		  |				20	0
		  |				21	CDF CUR
		  V				22	CIF 0
	       ////\\\\				23	CMP CALIOF (field 0)
	      /	       \ 			24	DSPOST
	     /	 TASK 	\  TSWFLG = -1		25	XWAITM
	 ---/  SWITCHING \----  No:
	 |  \   ALLOWED  /   |  Rescan
       0 |   \	   ?    /    |  ASAP
      No |    \        /     |
         |     \\\\//// 1    |
	 |	  |    Yes   |
	 -------->|    	     |
		  V	     |	
	 ------------------  |
	 |  INHIBIT TASK  |  |
	 |  SWITCHING.	  |  |
	 |  CLEAR RESCAN  |  |
	 |  FLAG	  |  |
 	 ------------------  |
		  |	     |
		  |<----------	
		  V	
	 ------------------
	 |      ION	  |
	 ------------------
		  |
		  V	
	 ------------------
	 |  SAVE CALLING  |
	 |	FIELD	  |
	 ------------------
		  |
		  V
	 ------------------
	 |  SAVE RETURN   |
	 |   ADDRESS	  |
	 ------------------		
		  |	
		  V
	     To page C-3


				      C-2

			        RTS/8 FLOWCHARTS

	    From page C-2
		  |
	 ------------------	
	 |  GET FUNCTION  |	
	 |	CODE	  |
	 ------------------	
		  |		
		  V			SW designates an operation that
	 ------------------		is performed only when using
	 |      SAVE	  |		nonresident operations.
	 |    COMMAND	  |
	 ------------------		EAE designates an operation that 
	 SW	  |			is performed only when the Extended 
		  |			Arithmetic Element is used.
		  ---------		
		  	  |		
		  	  V
		 ------------------
	 	 |  EXECUTE	  |
		 |  DISPATCH JUMP |	
		 |  THRU COMMAND  |
		 |  TABLE. IGNORE |
		 |  FREE BIT	  |
	 	 ------------------
		          |
        Function          |
        Code	          V				     ****
	    |	 ------------------			   *      *
	    V	 | JMP I .+FUNC+1 |<----------------------* CMDJMP *
		 ------------------			   *      *
	    0	 |     XSEND	  |    Pg. C-5		     ****
		 ------------------
	    1	 |     XRECEIV	  |    Pg. C-17
		 ------------------
	    2	 |     XWAITE	  |    Pg. C-10
		 ------------------
	    3	 |     XRUN	  |    Pg. C-28
		 ------------------
	    4	 |     XSUSPND	  |    Pg. C-28
		 ------------------
	    5	 |     XPOST	  |    Pg. C-20
		 ------------------
	    6	 |     XSKPINS	  |    Pg. C-21
		 ------------------
	    7	 |     XDERAL	  |    Pg. C-22
		 ------------------
	    10	 |     XBLKARG	  |    Pg. C-19
		 ------------------
	    11	 |     XSENDW	  |    Pg. C-5
		 ------------------
	    12	 |     XUNBARG	  |    Pg. C-18
		 ------------------
	    13	 |     XTSTOP	  |    Pg. C-13
		 ------------------
	    14	 |     XWAITX	  |    Pg. C-10
		 ------------------
		  
				      C-3

			        RTS/8 FLOWCHARTS





				     *****
				   *       *
				  *  EXRET  *
				   *       *
				     *****
				       |
				       |
				       V
			       -----------------
			       |     SET UP    |
			       |  RETURN FIELD |
			       -----------------
				       |
				       |
				       |
				       |
				       V
				 ////// \\\\\\	TSWFLG = -1 ---------------
		  TSWFLG=1 	/	      \   Yes	    |  KEEP TASK  |
     ------------   	       / TASKSWITCHING \	    |  SWITCHING  |
     |	Cannot	|<-------------\  NEEDS RESCAN /----------->|  INHIBITED  |
     |  Happen  |		\      ?      /		    ---------------
     ------------		 \\\\\\ //////			    |
				       |			    V
				       | TSWFLG = 0		  *****
				       | No			*       *
				       |		       *  TSTOP  *
				       V			*	*
			       -----------------		  *****
			       |  ALLOW TASK-  |	        (Pg. C-13)
			       |  SWITCHING    |
			       |  JMP I 20     |
			       |  RETURN TO    |
			       |  CALLING TASK |
			       -----------------


















				      C-4

			        RTS/8 FLOWCHARTS

   ---------							  ---------
   | SEND  |							  | SEND  |
   | SENDW |							  | SENDW |
   ---------							  ---------


	     ****		  ***
	   *      *		*     *
	  * XSENDW *	       * XSEND *
	   *      *		*     *
	     ****		  ***
	       |		   |
	       V		   V
	---------------     ---------------	Calling Sequence
	|     SET     |     |    CLEAR    |	p+1  SEND (W)
	|  WAIT FLAG  |	    |  WAIT FLAG  |	p+2  TASK # (Sending to)
	---------------	    ---------------	p+3  MSGADR
	       |		   |		P+4  RETURN
	       ---------------------
			 |
			 |
			 V
	 	 -----------------
		 |  GET TASK     |
		 |  NUMBER TO    |
		 |  SEND MSG TO  |
		 -----------------
			 |
			 |			
			 V
		 -----------------
		 |  GET MESSAGE  |
		 |  ADDRFSS	 |
		 -----------------
			 |
			 |
			 V
		   To page C-6





			Initial Values   |  Becomes
		-------------------------|--------------------
		| p   |	 MSGADR,  0000	 |  Sending Task #   |
		-------------------------|--------------------
		| p+1 |		  0000   |  CDF to next      |
		|     |			 |  msg, if any      |
		-------------------------|--------------------
		| p+2 |		  0000   |  Addr of next     |
		|     |		 	 |  msg (0 if none)  |
		-------------------------|--------------------
		| p+3 |          Start of Message	     |
		----------------------------------------------


				      C-5

			        RTS/8 FLOWCHARTS


				             From page C-5
			       			    |
			       			    V
				           //////////\\\\\\\\\\
					  /		       \
				         /      MESSAGE         \
			          Yes   /   ALREADY IN QUEUE     \
			 ---------------\ (FIRST WORD OF MESSAGE /
			 |	         \	 =0)  ?	        /
			 |		  \		       /
			 |                 \\\\\\\\\\//////////
			 |			    |
			 |			    | No
			 V	        	    |		   ****
	 	-------------------		    |	 	 *	*
		|  BACKUP RETURN  |		    |<----------* MSGFRE *
		|  TO CAL	  |		    |		 *      *
		|  ADDRESS	  |		    |	   	   ****
		-------------------		    V
			 |		   -------------------
	****		 |		   |  BUMP RETURN    |
      *      *		 |		   |  	  TO  	     |
     * MSEFWT *--------->|		   |      CAL+4	     |
      *      *		 |		   -------------------
        ****		 |			    |
			 V			    |
        	-------------------		    V
		|     AC=	  |	   -------------------
		|     MESSAGE	  |	   |  FIND RECEIVING |
		|     ADDRESS	  |	   |  TASK #'s	     |
		-------------------	   |  ENTRY IN	     |
			 |		   |  MSGTBL	     |
			 |		   -------------------
			 V		 	    |
		        ***			    |
		      *	    *			    V
		     * WAITS *		   -------------------
		      *     *		   |    GET DATA     |
			***		   |    FIELD OF     |
		     (Pg. C-10)		   |    MESSAGE	     |
					   -------------------
						    |
						    |
						    V
					           ****
					         *	*
					        * ADDTOQ *
					         *      *
					           ****
					         (Pg. C-7)
			





 				      C-6

			        RTS/8 FLOWCHARTS


				     ****
				   *      *
				  * ADDTOQ *
				   *      *
				     ****
				      |
				      |
				      V
			      ------------------
		 	      |  GET FIRST     |
			      |  QUEUE WORD    |
			      |  (CDF TO NEXT) |
			      ------------------
				      |
				      |
				   ////\\\\
			  Yes	  /	   \
	  -----------------------/  EMPTY   \
	  |			 \  (=0) ?  /
	  |			  \	   /
	  |			   \\\\////
	  |			      |
	  |			      | No
	  |			      V
	  |		      ------------------
	  |	 	      |    CDF INTO    |
	  |		      |    NEXT	       |
	  |		      |    MESSAGE     |
	  |		      ------------------
	  |			      |
	  |			      |
	  |			      V
	  |		      /////////\\\\\\\\\\
	  |		     /                   \
	  |		    /	      IS          \
	  |		   /	 SENDING TASK      \  No    ---------------
	  |		  /  NUMBER LESS THAN TASK  \------>|  FIND NEXT  |
	  |		  \	NUMBER IN THIS      /	    |  MESSAGE IN |
	  |		   \	  QUEUE MSG        /	    |  QUEUE      |
	  |		    \	      ?           /	    ---------------
	  |		     \			 /		   |
	****		      \\\\\\\\\//////////		   |
      *      * 			      |				   V
     * ENDOFQ *---------------------->| Yes			  ****
      *	     *			      |				*      *
	****			      |			       * ADDTOQ *
				      |				*      *
				      V				  ****
				To Page C-8			(Pg. C-7)







				      C-7

			        RTS/8 FLOWCHARTS

		
				From Page C-7
				       |
				       V
			       ------------------
			       |  PUT CDF TO    |
			       |  MSG AND PC OF |
			       |  MSG INTO      |
			       |  QUEUE WORDS   |
			       ------------------
				       |
				       |
				       V
			       ------------------
			       |      IOF	|
			       ------------------
				       |
				       |
				       V
			       ------------------
			       |   GET TASK #	|
			       |   TO SEND	|
			       |   MESSAGE TO 	|
			       ------------------
				       |
				       |
				       V
			       ------------------
			       |  FREE MSG WAIT |
			       |  AND/OR EVENT	|   Via call to FREEJ
			       |  WAIT BITS IN	|
			       |  STATUS TABLE 	|
			       ------------------
				       |
				       |
				       V
			      --------------------
			      |  L=1 IF REVEIV-  |
			      |  ING TASK IS     |   This will be tested if
			      |  RUNNABLE & OF   |   this CAL was a SEND 
			      |  HIGHER PRIORITY |   and not a SENDW.
			      |  THAN SENDER;	 |
			      |  L=0 IF NOT	 |
			      --------------------
				       |
				       |
				       V
				 To Page C-9



				





				      C-8

			        RTS/8 FLOWCHARTS


				From Page C-8
				       |
     D		    ****	       |
     O		  *      *	       |
		 * MSGCDF *----------->|
     N		  *      *	       |
     O              ****	       V
     T			      -------------------
			      |  STORE SENDING  |
     T			      |  TASK NUMBER    |
     O			      |  IN MSG HEADER  |
     U			      -------------------
     C				       |
     H    Link indicates 	       |
	  whether a new		       V
     L    task should be      -------------------
     I    run or not.	      |  STORE CDF TO	|
     N			      |  NEXT MSG IN	|   =0 if none
     K    The link status     |  MSGHDR		|
	  will be checked     -------------------
     I    later on in		       |
     N    POSTEX.		       |
				       V
     T			      -------------------
     H			      |   STORE PC OF   |
     I			      |   NEXT MSG IN   |   =0 if none
     S			      |	  MSGHDR	|
			      -------------------	  Message is now
     C				       |		  linked into the 
     O				       |		  message queue
     D				       |
     E				       V
     				   ////\\\\		   ****
     !				  /        \  No	 *	*
     !				 /  CAL WAS \---------->* POSTEX *
     !				 \  SENDW   /		 *	*
     !				  \   ?    /		   ****
     !				   \\\\////		 (Pg. C-18)
				      |
				      |  Yes
				      V
				    ****
				  *      *
				 * MSEFWT *
				  *      *
				    ****
				  (Pg. C-6)









				      C-9

			        RTS/8 FLOWCHARTS

   ---------							  ---------
   | WAITE |							  | WAITE |
   | WAITX |							  | WAITX |
   ---------							  ---------


                ****		      ****
	      *      *		    *      *
	     * XWAITE *		   * XWAITX *
	      *      *		    *      *
		****		      ****
		  |		       |
		  |		       |
		  V		       V	   Calling Sequence:
	    -------------	---------------
	    |   CLEAR   |	|  SET ACARG  |    p   CAL
	    |   ACARG   |	|    TO -1    |    p+1 WAITE
	    -------------	---------------    p+2 EVENT FLAG ADDR
		  |		       |	   p+3 RETURN
		  -------------------->|
			               |
			               V
			      -------------------
       Enter Here From	      |   GET ADDRESS   |
       SEND or SENDW          |  OF EVENT FLAG  |
       (Pg. C-6)	      -------------------
           ****	              	       |
	 *      *	               |
	* WAITS  *-------------------->|
	 *      *	               |
	   ****			       V
			      -------------------
       ACARG /= -1	      |  SAVE ADDRESS   |
			      |  OF EVENT FLAG  |
			      -------------------
			               |
			               |
			               V
			      -------------------
			      |       IOF	|
			      -------------------
			               |
			               |
			               V
				    ////\\\\		    ****
				   /	    \  Yes	  *      *
				  /  EVENT   \---------->* EXRET  *
				  \ FLAG = 0 /		  *      *
				   \	    /		    ****
				    \\\\////
			               |    No		Restart caller if
				       |		TASKSW allows
				       V		(Pg. C-4)
				  To Page C-11



				      C-10

			        RTS/8 FLOWCHARTS


				From Page C-10
			               |
				       V
			      -------------------
			      |     EVTFLG =    |   Give it waiting
			      |  4000 + TASK #  |   status
			      -------------------
			               |
			               V
				    ////\\\\
			     Yes   /	    \
		------------------/ WAS THIS \
		|		  \ A WAITX  /
		|		   \    ?   /
		|		    \\\\////
		V	               |    No
	-----------------              |
	|  PUSH PC BACK |              V
	|  TO POINT TO  |	   ---------------   Store Event Flag
	|      CAL	|	   |  AC = EFWT  |   Wait in Flag Table
	-----------------	   ---------------
		|			  |
		|			  |
		V			  V
	-----------------		 ****	     Jump with link clear
	|  AC = EORMWT  |	       *      *	     (tested at TSTOP)
	-----------------	      * TSWAIT *     (Pg. C-12)
		|		       *      *
		|		 	 ****
		V
	      ****
	    *	   *
	   * TSWAIT *
	    *	   *
	      ****
	    (Pg. C-12)




















				      C-11

			        RTS/8 FLOWCHARTS


				  (Pg. C-17)
				     ****
				   *	  *         Wait for mesasge.
				  * WAITM3 *        Enter here from RECEIVE.
				   *	  *
				     ****
				       | 
				       | 
				       V
			    -----------------------
			    |  BACKUP CALLING PC  |
			    |  TO DO CALX AGAIN   |
			    -----------------------
				       |
				       V
			      -------------------
			      |     SET LINK	|   Message Wait Status
			      |    AC = MSGWT	|
			      -------------------
	   ****			       |
	 *      *		       |
	* TSWAIT *-------------------->|
	 *      *		       |
	   ****			       V
			      -------------------
			      | SAVE AC IN MASK |
	(Pg. C-19)	      -------------------
	   ****			       |
	 *      *		       |
	* TSWATX *-------------------->|
	 *      *		       |
	   ****			       V
			    -----------------------
			    |  STORE IN TASK #'s  |
			    |  FLAG TABLE ENTRY   |
			    -----------------------
				       |
				       V
			      -------------------   Interrupts were off
			      |       ION	|   here if we came from
			      -------------------   XWAITE.
				       |
				       V
				  To Page C-13












				      C-12

			        RTS/8 FLOWCHARTS


				From Page C-12
				       |
				       V
				     ///\\\
				    /	   \   Yes
				   /  LINK  \------------
				   \  SET ? /		|
				    \	   /		|
				     \\\///		|
			               |   No		|
				       V		|
			      -------------------	|
			      |  CLEAR TASK AC  |	|
			      -------------------	|
	   ****			       |		|
	 *      *		       |		|
	* TSTOP	 *-------------------->|		|
	 *      *		       |		|
	   ****			       V		|
			    ----------------------	|
			    |  SAVE AC IN ACARG  |	|
			    ----------------------	|
				       |		|
				       |<----------------
				       V		
			 -----------------------------
			 |  GET TASK NUMBER'S ENTRY  |
			 |      IN STATUS TABLE      |
			 -----------------------------
				       |
				       V
			      -------------------
			      |   SAVE RESTART  |
			      |  FLAGS, PC, AC  |
			      -------------------
				       |
				       V
			      -------------------
			      |     SAVE MQ	|
			      -------------------
			      EAE      |
				       V
			  ---------------------------
			  |  FREE PARTITION IF FREE |
			  |  BIT WAS SET IN COMMAND |
			  ---------------------------
			      SW       |		    ****
				       |		  *	 *
				       |<----------------* FINDJ  *
				       |		  *	 *
				       |		    ****
				       V		 RTS/8 Scheduler
				 To Page C-14            (Pg. C-30)



				      C-13

			        RTS/8 FLOWCHARTS


				From Page C-13
				       |
				       V
     Schedule next	      -------------------
     runnable task	      |    TASK # = 1   |
     (start scan 	      -------------------
     from top)			       |
				       V
			      -------------------
			      |      ENABLE 	|
			      |  TASKSWITCHING  |
			      -------------------
				       |
				       V
			   -------------------------
			   |  SET 'MACHINE STATUS  |
			   |  UNIMPORTANT' FLAG    |
			   -------------------------
	   ****			       |
	 *      *		       |
	* FINDJL *-------------------->|
	 *      *  ^		       |
	   ****	   |		       V
		   |	    -----------------------
		   |	    |  GET TASK #'s ENTRY |
		   |	    |    IN FLAG TABLE    |
		   |	    -----------------------
		   |		       |
		   |		       |	    Interrupts temporarily
		   |		       |	    inhibited here.
		   |		       |
		   |		       V
		   |		   /////\\\\\		    ****
		   |		  /	     \  Yes	  *      *
		   |		 / FLAGS = 0  \--------->* STARTJ *
		   |		 \ (RUNNABLE) /		  *      *
		   |		  \     ?    /		    ****
		   |		   \\\\\/////		 (Pg. C-15)
		   |	               |    No
		   |		       |
		   |		       |	    Note no end of table
		   |		       |	    check - there must be
		   |		       |	    a runnable task. 
		   |		       |	    (Null task is always
		   |		       |	    runnable.)
		   |		       V
		   |	     ----------------------
		   |	     |  BUMP TASK NUMBER  |
		   |	     ----------------------
		   |		       |
		   |		       |
		   ---------------------




				      C-14

			        RTS/8 FLOWCHARTS


				     ****
				   *	  *	    Here from FINDJ
				  * STARTJ *	    (Scheduler) 
				   *	  *	    Found a runnable task
				     ****
			               |
			               V
			      -------------------
			      |       ION	|
			      -------------------
				       |
			               V
			    -----------------------
			    |  GET TASK #'s ENTRY |
			    |   IN STATUS TABLE   |
			    -----------------------
				       |
			               V
			      -------------------
			      |       IOF	|
			      -------------------
				       |
			               V
			    -----------------------
			    |  SAVE OLD STATUS IN |
			    |    TEMP LOCS OF	  |
			    |  INTERRUPT ROUTINE  |
			    -----------------------
				       |
     Interrupt			       |
     Dismiss code		       |
				       |
			    	       |
	   ****			       |
	 *      *		       |
	* DISMIS *-------------------->|
	 *      *		       |
	   ****			       |
				       V
				   /////\\\\\		    ****
				  /	     \  Yes	  *      *
     This is tested on		 /  PENDING   \--------->* USERSK *
     an 8/E or 8/a only		 \ INTERRUPTS /		  *      *
				  \     ?    /		    ****
		   		   \\\\\/////		 (Pg. C-23)
		   	               |    No
		   		       V
			  ---------------------------
			  |  SWEEP OLD STATUS INTO  |
			  |  DF, IF, AC, PC, ETC.   |
			  ---------------------------
				       |
				       V
				  To Page C-16


				      C-15

			        RTS/8 FLOWCHARTS


				From Page C-15
				       |
				       V
			      -------------------
			      |    RESTORE MQ	|
			      -------------------
			      EAE      |
				       V
			      -------------------
			      |       ION	|
			      -------------------
				       |
				       V
			  ---------------------------
			  |  	    JMP I 0	    |
			  |  RETURN FROM INTERRUPT  |
			  ---------------------------







































				      C-16

			        RTS/8 FLOWCHARTS


   ----------							 ----------
   | RECEIV |							 | RECEIV |
   ----------							 ----------


				     *****	    Calling Sequence:
				   *	   *
				  * XRECEIV *	    p-1  TAD ARG
				   *	   *	    p    CAL
				     *****	    p+1  RECEIV
			               |	    p+2  MADDR, 0
				       |	    p+3  RETURN
				       V
			      -------------------
			      |   GET ENTRY IN	|
			      |  MESSAGE QUEUE	|
			      -------------------
				       |
				       V
			      -------------------
			      |  GET FIRST WORD |
			      |  OF QUEUE ENTRY |
			      -------------------
				       |
				       V
				   /////\\\\\		    ****
				  /	     \  Yes	  *      *
     	     ------------------->/   EMPTY    \--------->* WAITM3 *
     	     |			 \ (NO MSGS)  /		  *      *
	     |			  \    ?     /		    ****
	     |	   		   \\\\\/////		 (Pg. C-12)
	     |	   	               |    No
	     |	   		       V
	     |			   /////\\\\\		 -----------------
	     |			  /	     \  No	 |  UNLINK THIS	 |
     	     |			 /  ARG = 0   \--------->|  MESSAGE FROM |
     	     |			 \     ?      /	    ^	 |   THE QUEUE 	 |
	     |			  \          /	    |	 -----------------
	     |	   		   \\\\\/////	    |		 V 
	     |	   	               |    Yes	    |	 -----------------
	     |	   		       V	    |	 |  STORE ADDR   |
	     |			   /////\\\\\	    |	 |  OF MESSAGE   |
     -----------------	  	  /	     \      |    |   IN CAL+2	 |
     |  ADVANCE TO   |	     No	 /  SENDING   \ Yes |    ----------------- 
     |  NEXT MESSAGE |<---------/ TASK OF MSG  \----|		 V
     |  ON THE QUEUE |		\    = ARG     /	 -----------------
     -----------------		 \	      /		 |  AC = CDF TO  |
				  \     ?    /		 |    MESSAGE	 |
				   \\\\\/////		 -----------------
						   	         V
				      		   	        ****
				     			      *      *
				      		     	     * EXRET  *
							      *      *
								****
				      			     (Pg. C-4)
				      C-17

			        RTS/8 FLOWCHARTS


   ----------							 ----------
   | UNBARG |							 | UNBARG |
   ----------							 ----------


				     *****
				   *	   *
				  * XUNBARG *
				   *	   *
				     *****
			               |
				       V
			      -------------------
			      |  GET BIT MASK	|
			      |  FROM ARG LIST  |
			      -------------------
				       |		     ****
				       |		   *	  *
				       |<-----------------* UNBLOK *
	 			       |		   *	  *
	   			       V		     ****
			      -------------------
			      |	      IOF	|
			      -------------------
				       |	    Call FREEJ
				       V	  
			     ---------------------  L=1 if clearing mask
			     |  CLEAR MASK BITS  |  bits makes task
			     |   IN FLAG TABLE   |  runnable and it is
			     ---------------------  higher priority; 
				       |	    L=0 otherwise.
				       V	  
			      -------------------
			      |	      ION	|
	(Pg. C-9)	      -------------------
	   ****			       |
	 *      *		       |
	* POSTEX *-------------------->|
	 *      *		       |
	   ****			       V
				   /////\\\\\		    ****
				  /	     \  No	  *      *
     				 /  RUN NEW   \--------->* EXRET  *
     				 \    TASK    /	 L = 0	  *      *
				  \     ?    /		    ****
		   		   \\\\\/////		 (Pg. C-4)
		   	               |    Yes
		   		L = 1  |
				       V
				      ****
				    *	   *
				   * TSTOP  *
				    *	   *
				      ****
				   (Pg. C-13)

				      C-18

			        RTS/8 FLOWCHARTS


   ----------							 ----------
   | BLKARG |							 | BLKARG |
   ----------							 ----------


				     *****	    Calling Sequence:
				   *	   *
				  * XBLKARG *	    p-1  TAD TASK #
				   *	   *	    p    CAL
				     *****	    p+1  BLKARG
			               |	    p+2  WAITBITS
			               |	    p+3  RETURN
				       V
			      -------------------
			      |  GET WAIT BITS  |
			      |  FROM ARG. LIST |
	(Pg. C-28)	      -------------------
	   ****			       |
	 *      *		       |
	*  BLOK  *-------------------->|
	 *      *		       |
	   ****			       V
				   /////\\\\\
				  /	     \		    ****
				 /  CALLING   \  Yes	  *      *
     				/  TASK TO BE  \-------->* TSWATX *
     				\    BLOCKED   /	  *      *
				 \ (TASK# = 0)/		    ****
				  \    ?     /		 (Pg. C-12)
		   		   \\\\\/////
		   	               |    No
		   		       V
			    -----------------------
			    |  SET MASK BITS IN   |
			    |  FLAG TABLE ENTRY   |
			    |  OF SPECIFIED TASK  |
			    -----------------------
				       |
				       V
				     *****
				   *	   *
				  *  EXRET  *
				   *	   *
				     *****
				  (Pg. C-4)











				      C-19

			        RTS/8 FLOWCHARTS


   ----------							 ----------
   |  POST  |							 |  POST  |
   ----------							 ----------


				     *****
				   *	   *
				  *  XPOST  *
				   *	   *
				     *****
			               |	    Calling Sequence:
				       V
			      -------------------   p-1  TAD EFPTR
			      |  SAVE ORIGINAL  |   p    CAL
			      |   EVENT FLAG    |   p+1  POST
			      -------------------   p+2  ECDF, CDF EFFLD
				       |	    p+3	 RETURN
				       V
			     ----------------------
			     |  CLEAR EVENT FLAG  |
			     ----------------------
				       |
				       V
			       /////////\\\\\\\\\
			      /			 \		    ****
			     /    WAS SOMEONE     \  No		  *	 *
			    /  WAITING FOR THIS TO \------------>* EXRET  *
			    \	HAPPEN (OLD FLAG   / 	  	  *	 *
			     \	    NEGATIVE)     /  L=0	    ****
			      \	       ?         /	 	 (Pg. C-4)
		   	       \\\\\\\\\/////////
		   	          L=1  |    Yes
		   		       V
			   -------------------------
			   |  GET WAITING TASK'S #  |
			   |  FROM LOW ORDER BITS   |
			   |  OF THE OLD FLAG       |
			   --------------------------
				       |
				       V
			  ---------------------------
			  |  CLEAR BOTH EVENT FLAG  |
			  |    WAIT AND EVENT OR    |
			  |         MESG WAIT	    |
			  ---------------------------
				       |
				       V
				     *****
				   *	   *
				  * UNBLOK  *
				   *	   *
				     *****
				  (Pg. C-18)



				      C-20

			        RTS/8 FLOWCHARTS


   ----------							 ----------
   | SKPINS |							 | SKPINS |
   ----------							 ----------


				     *****	    Calling Sequence:
				   *	   *
				  * XSKPINS *	    p    CAL
				   *	   *	    p+1  SKPINS
				     *****	    p+2  MODULE ADDR
			               |	    p+3  RETURN
			               |
				       V
			      -------------------
			      |    GET FIRST    |
			      |   MODULE NAME   |
			      -------------------
				       |
				       V
				   /////\\\\\
				  /	     \  No      -------------------
    				 /  IS IT 0   \-------->|  ALREADY IN THE |
     				 \ 	?     /		|  SKIP CHAIN !!! |
				  \          /		-------------------
		   		   \\\\\/////			  |
		   	               |    Yes			  V
		   		       V			*****
			    -----------------------	      *	      *
			    |  PUT DISMIS ROUTINE |	     *  EXRET  *
			    |   ADDR IN 1st WORD  |	      *	      *
			    -----------------------		*****
				       |		     (Pg. C-4)
				       V
			    --- -------------------
			    |   PUT CDF, CIF OF   |
			    |  DISMIS IN 2nd WORD |
			    -----------------------
				       |
				       V
			   -------------------------
			   |  PUT MODULE ADDRESS   |
			   |  AND CDF, CIF IN LAST |
			   |  MODULE OF INTERRUPT  |
			   |      SKIP CHAIN       |
			   -------------------------
				       |
				       V
				     *****
				   *	   *
				  *  EXRET  *
				   *	   *
				     *****
				  (Pg. C-4)



				      C-21

			        RTS/8 FLOWCHARTS


   ----------							 ----------
   | DERAIL |							 | DERAIL |
   ----------							 ----------


				     ****
				   *	  *
				  * XDERAL *
				   *	  *
				     ****
			               |
				       V
			      -------------------   Calling Sequence:
			      |   GET TASK #'s  |
			      |   STATUS TABLE  |   p-1  TAD TASK #
			      |     POINTER     |   p    CAL
			      -------------------   p+1  DERAIL
				       |            p+2  SUBROUTINE
				       V	    p+3  RETURN
			      -------------------
			      |  STORE RESTART  |
			      |   PC IN SUBR    |
			      -------------------
				       |
				       V
			      -------------------
			      |  STORE SUBR+1   |
			      |  IN RESTART PC  |
			      -------------------
				       |
				       V
				     *****
				   *	   *
				  *  EXRET  *
				   *	   *
				     *****
				  (Pg. C-4)



















				      C-22

			        RTS/8 FLOWCHARTS


				   *********
				 *	     *
				*  INTERRUPT  *
				*   ROUTINE   *
				 *           *
				   *********
				       |
				       |
				       V
				   /////\\\\\
				  /	     \		    *******
     				 /    TIME    \  Yes	  *  GO TO  *
				/    SHARING   \--------->*   OS/8    *
				\   INTERRUPT  /          * SUPPORT *
     				 \      ?     /		    *******
				  \          /		  if present
		   		   \\\\\/////
		   	               |    No
				       |
		   		       V
			      -------------------
			      |     SAVE THE    |
			      |  MACHINE STATUS |
	(Pg. C-15)	      -------------------
	   ****			       |
	 *      *		       |
	* USERSK *-------------------->|
	 *      *		       |
	   ****			       V
			     ---------------------
			     |   USER-INSERTED   |
			     |   SKIPS FOR ANY   |
			     |  CRUCIAL DEVICES  |
			     ---------------------
				       |
				       |
				       V
	     *****		   /////\\\\\
	  *	    *		  /	     \ 
	*    GO TO    *	    Yes	 /    KL8A    \
	* APPROPRIATE *<---------\  INTERRUPT /
	*  INTERRUPT  *		  \     ?    /
	  * MODULE  *  		   \\\\\/////
	     *****	               |    No
				       |
		   		       V
				 To Page C-24









				      C-23

			        RTS/8 FLOWCHARTS


				From Page C-23
				       |
		   		       V
				   /////\\\\\	        -------------------
				  /	     \  Yes     |  SET UP LOC 0   |
     				 /   POWER    \-------->|  FOR POWER FAIL |
     				 \  FAILURE   /		|     RESTART     |
				  \     ?    /		-------------------
		   		   \\\\\/////			 |
		   	               |    No			 V
		   		       V		     ********
				   /////\\\\\ 		    *	     *
	   *******		  /	     \		    *  HALT  *
	 *  GO TO  *	    Yes	 /   CLOCK    \		    *	     *
	*   CLOCK   *<-----------\ 	      /		     ********
	 * HANDLER *		  \     ?    /
	   *******	   	   \\\\\/////		 as CPU restarts
        if present	               |    No		   ************
		   		       V		  * 	       *
				    *********		  *  POWER-UP  *
				 *             *	  *  RESTART   *
				*  GO TO FIRST  *	  * 	       *
				*  USER INTER-  *	   ************
				*  RUPT MODULE  *		 |
				 *             *		 V
				    *********		-------------------
							|  AC = POWER-UP  |
							|   EVENT FLAG    |
							|     ADDRESS     |
							-------------------
								 |
								 V
							       ****
							     *	    *
							    * DSPOST *
							     *	    *
							       ****
							    (Pg. C-25)


















				      C-24

			        RTS/8 FLOWCHARTS


   ----------							 ----------
   | POSTDS |							 | POSTDS |
   ----------							 ----------


				  (Pg. C-24)
				     *****
				   *	   *
				  *  DSPOST *
				   *	   *
				     *****
				       |	      Come here from user
				       V	      issusing POSTDS
				   /////\\\\\
	   ****			  /	     \ 	      p-3  CDF EFFLD
	 *      *	    Yes	 /   AC = 0   \	      p-2  TAD EFPTR
	* DISMIS *<--------------\ 	?     /	      p-1  COF 0
	 *      *		  \          /	      p    POSTDS
	   ****	   		   \\\\\/////
	(Pg. C-15)	               |    No
		   		       V
			     ----------------------
			     |    SAVE THE OLD    |
			     |  EVENT FLAG VALUE  |
			     ----------------------
				       |
				       V
			      ---------------------
			      |  ZERO EVENT FLAG  |
			      ---------------------
				       |
				       V
				////////\\\\\\\\
			       /                \		    ****
			      /       WAS A      \  Yes	          *      *
			     /    TASK WAITING    \------------->* DISMIS *
			     \ ON THIS FLAG? (OLD /	          *	 *
			      \ VALUE NEGATIVE)  /		    ****
			       \       ?        /	         (Pg. C-15)
				\\\\\\\\////////
		   	               |    No
		   		       V
			   --------------------------
			   |  CLEAR EVENT FLAG AND  |
			   |    EVENT OR MESSAGE    |   Call FREEJ
			   |   WAIT BITS IN TABLE   |
			   |   ENTRY OF WAIT TASK   |
			   --------------------------
				       |
				       V
				 To Page C-26





				      C-25

			        RTS/8 FLOWCHARTS

			
				From Page C-25
				       |
				       V
				   /////\\\\\
     Run the waiting task if	  /	     \		     ****  
     its flag word is now 	 /    RUN     \  No	   *      *
     zero and it is higher	/   WAITING    \--------->* DISMIS *
     priority than the 		\    TASK      /	   *      *
     current user.		 \     ?      /		     ****
				  \          /		  (Pg. C-15)	
		   		   \\\\\/////
		   	               |    Yes
		   		       V
				   /////\\\\\
				  /	     \  	  -----------------
				 /    TASK    \  Yes      |  SET RESCAN   |
     				/   SWITCHING  \--------->|     FLAG      |
				\   INHIBITED  /  	  |  CTSFWLG = -1 |
     				 \  	?     /		  -----------------
				  \          /			  |
		   		   \\\\\/////			  V
		   	               |    No			****
		   		       V		      *	     *
				   /////\\\\\		     * DISMIS *
				  /	     \ 		      *	     *
     			     No	 /  IS SAVE   \			****
     		-----------------\ STATE FLAG /		     (Pg. C-15)
		|		  \   -1     /
		|   		   \\\\\/////
		|   	               |    Yes
		|   		       V
		|	    ------------------------
		|	    |  SAVE CURRENT TASK'S |
		|	    |     PC, AC IN ITS    |
		|	    |  STATUS TABLE ENTRY  |
		|	    ------------------------
		|		       |
		|		       V
		|	      -------------------
		|	      |  SAVE TASK'S MQ |
		|	      -------------------
		|	      EAE      |
		|--------------------->|
				       V
			      -------------------
			      |       ION	|
			      -------------------
				       |
				       V
				 To Page C-27






				      C-26

			        RTS/8 FLOWCHARTS


				From Page C-27
				       |
				       V
			      -------------------
			      |    PREPARE TO   |
			      |  START NEW TASK |
			      -------------------
				       |
				       V
				   /////\\\\\			    ****
				  /	     \  No		  *      *
     				 /   IS IT    \----------------->*  FINDJ *
     				 \  RESIDENT  /			  *      *
				  \     ?    /			    ****
		   	      SW   \\\\\/////			 (Pg. C-30)
		   	               |    Yes
		   		       V
				     ****
				   *	  *
				  * STARTJ *
				   *	  *
				     ****
				  (Pg. C-15)
			
































				      C-27

			        RTS/8 FLOWCHARTS


   ---------							  ---------
   |  RUN  |							  |  RUN  |
   ---------							  ---------


				     *****
				   *	   *
				  *  XRUN   *
				   *	   *
				     *****
				       |		Calling Sequence:
				       V
			      -------------------	p-1  TAD TASK #
			      |   AC = RUNWT    |	p    CAL
			      -------------------	P+1  RUN
				       | Run Wait	p+2  RETURN
				       V
				     *****
				   *	   *
				  * UNBLOK  *		Go and set the 
				   *	   *		flag bits.
				     *****
				  (Pg. C-18)





   ----------							 ----------
   | SUSPND |							 | SUSPND |
   ----------							 ----------


				     *****
				   *	   *
				  * XSUSPND *
				   *	   *
				     *****
				       |		Calling Sequence:
				       V
			      -------------------	p-1  TAD TASK #
			      |   AC = RUNWT	|	p    CAL
			      -------------------	p+1  SUSPND
				       |		p+2  RETURN
				       V
				     *****
				   *	   *
				  *  BLOK   *
				   *	   *
				     *****
				  (Pg. C-19)





				      C-28

			        RTS/8 FLOWCHARTS


   ---------							  ---------
   | WAITM |							  | WAITM |
   ---------							  ---------


				     *****
				   *	   *
				  *  XWAITM  *
				   *	   *
				     *****
				       |
				       V
			      -------------------
			      |    SAVE AC IN   |
			      |    'COMMAND'  	|
			      -------------------
			      SW       |
				       V
			      -------------------
			      |   CLEAR AC, L   |
			      -------------------
				       |
				       V
			      -------------------
			      |   FAKE A CAL	|
			      -------------------
				       |
				       V
			      -------------------
			      |  DISABLE TASK   |
			      |   SWITCHING	|
			      -------------------
				       |
				       V
			      -------------------
			      |     PUT WAIT	|
			      |    BITS IN AC	|
			      -------------------
				       |
				       V
				     *****
				   *	   *
				  *  TSWAIT *
				   *	   *
				     *****
				  (Pg. C-12)










				      C-29

			        RTS/8 FLOWCHARTS


				     *****
				   *	   *		RTS/8 SCHEDULER
				  *  FINDJ  *		FIND A TASK TO RUN
				   *	   *
				     *****
				       |
				       V
			      -------------------
			      |   ENABLE TASK	|
			      |    SWITCHING	|
			      -------------------
				       |
				       V
			    -----------------------
			    |      GET SET TO     |
			    |  EXAMINE FIRST TASK |
			    -----------------------
				       |
				       V
			      -------------------
			      |    ZERO SAVE	|
			      |    STATE FLAG	|
			      -------------------
				       |
		---------------------->|
		|		       V
		|	      -------------------
		|	      |       ION	|
		|	      -------------------
		|		       |
		|		       V
		|	      -------------------
		|	      |     BUMP TO 	|
		|	      |     NEXT TASK	|
		|	      -------------------
		|		       |
		|		       V
		|	      -------------------
		|	      |       IOF	|
		|	      -------------------
		|		       |
		|		       V
		|	      -------------------
		|	      |  GET TASK FLAGS |
		|	      -------------------
		|		       |
		^		       V
	From Page C-31		  To Page C-31








				      C-30

			        RTS/8 FLOWCHARTS


	   To Page C-30		 From Page C-30
		^		       |
		|		       V
		|		  //////\\\\\\
		|		 /            \
		|		/     ANY      \
	 	|	  Yes  /    BLOCKING    \
	 	|--------------\BITS OTHER THAN /
				\     NRWT     /
				 \     ?      /
				  \\\\\\//////
				       |     No
				       V
				   /////\\\\\			    ****
				  /	     \  Yes		  *      *
     				 /  IS TASK   \----------------->* STARTS *
     				 \  RESIDENT  /			  *      *
				  \     ?    /			    ****
		   		   \\\\\/////			 Start task
		   	          SW   |    No			 (Pg. C-15)
		   		       V
			      -------------------
			      |    PUT TASK	|
			      |    INTO SWPWT	|
			      -------------------
			      SW       |
				       V
			      -------------------
			      |   TAKE SWAPPER	|
			      |   OUT OF RUNWT	|
			      -------------------
			      SW       |
				       V
				     *****
				   *	   *
				  *  FINDJ  *
				   *	   *
				     *****
				  (Pg. C-30)

















				      C-31






				  APPENDIX D

			 RTS/8 ASSEMBLY ERROR MESSAGES


     Certain user  errors  are  caught  at  assembly  time.   They  produce
     standard PAL8 error diagnostics on the terminal of the form

	  IC
	  US tag
	  IC

     where the tag specified indicates  the  type  of  error  as  described
     below.

      Tag	    Module			Possible Error

     MCRBLK	    MCR.PA	   MCR  was  declared  nonresident  (MCRPRT
				   defined)  and MCR origin was incorrectly
				   a multiple of 400.  Nonresident  portion
				   of  MCR  is second page which must start
				   on a block boundary.

				   Fix:  Redefine MCRORG.

     SYSERR	    several	   System error; should  not  occur  unless
				   user modified RTS/8 sources.

				   Fix:  See  comments   on   source   line
					 which generated the error.

     TBLERR	    RTS8.PA	   Internal Executive tables were generated
				   incorrectly.  See source.

     CURBIG	    PARAM.PA	   User task  specified  a  value  for  CUR
				   which was larger than HGHFLD.

				   Fix:  Redefine CUR.

     RATERR	    CLOCK.PA	   HERTZ is not a multiple of SHERTZ.

				   Fix:  Redefine  HERTZ   or   SHERTZ   in
					 parameter file.

     TODERR	    CLOCK.PA	   SHERTZ is  too  large.  SHERTZ  must  be
				   less than 192 (decimal).

				   Fix:  Redefine SHERTZ in
					 parameter file.






				      D-1

			 RTS/8 ASSEMBLY ERROR MESSAGES


      Tag	    Module			Possible Error

     NOKL8A	    KL8ASR.PA	   The symbol KL8A was not defined  in  the
				   parameter file.

				   Fix:  Set symbol KL8A in parameter file
					 equal to number of physical
					 KL8-A's present.

     KLOERR.	    KL8ASR.PA	   The symbol KL8A was set equal to  0  yet
				   the file KL8ASR.PA was assembled.

				   Fix:  Do not assemble KL8ASR.PA if KL8-A
					 support is not desired or redefine
					 KL8A in the parameter file.

     HITMON.	    KL8ASR.PA	   The KL8-A service overlaid location 7600
				   in field 0.  Ignore this error if you do
				   not want to preserve OS/8 resident code.

				   Fix:  Redefine KL8ACT in parameter file.

     NOSWAP	    PARAM.PA	   A nonresident task was  assembled  in  a
				   system with no swapper.

				   Fix:  Define SWAPPER in  parameter  file
					 or undefine PARTNO in user task.

     SWPRIO	    PARAM.PA	   A  nonresident  task  was  given  higher
				   priority than the swapper.

				   Fix:  Change priority of swapper or user
					 task.
     FLDERR	    PARAM.PA	   Some  parameter  representing  a   field
				   number  times  10 was not in the correct
				   form (e.g. HGHFLD, MCRFLD, etc.)

				   Fix:  Correct value of parameter in
					 parameter file.

     CURERR	    PARAM.PA	   One of the symbols CUR,  CUR2,  or  CUR3
				   was not of the proper form.

				   Fix:  Correct value in user task  to  10
					 times field of task.











				      D-2






				  APPENDIX E

			 EXECUTIVE INTERNAL TASK TABLES


     The Executive uses five internal tables to maintain information  about
     the  tasks in the system.  Each task's task number is used as an index
     into the first four tables to retrieve and update information for that
     task.  The internal tables are as follows:

          1.  The  Task  State  Table  (TSTABL) - contains  4-word  entries
	      holding  the  most  recent contents of CPU registers for each
	      task as follows:

		   Word 1 - contains the link (bit 0)
				     the Greater Than Flag (bit 1) -if flag
				     exists on machine being used
				     the User Mode Flag (bit 5) -if flag
				     exists on machine being used
				     the Instruction Field (bits 6-8)
				     the Data Field (bits 9-11)

		   Word 2 - contains the contents of the Program Counter
			    (PC)

		   Word 3 - contains the contents of the Accumulator (AC)

		   Word 4 - contains the contents of the Multiplier
			    Quotient (MQ) register if the system has been
			    assembled to save the MQ.

	      Whenever the system executes a task, it loads the contents of
	      the  task's  Task  State Table entries into the corresponding
	      CPU registers.  Whenever a task  stops  executing,  its  Task
	      State  Table  entries  are  set  to the new contents of these
	      registers.  The Task State Table is located after the Message
	      Table, that is, at location NTASKS+2^2+MSGTBL-4 in field 0.

	      Example:

	      Consider the following TSTABL entries for a task.

		   4012
		   3376
		   1234
		   0211

	      The task is interrupted just as it is about  to  execute  the
	      instruction  at  location 3376 (entry 2) of field 1 (bits 6-8
	      of entry 1).  At this  point,  the  contents   of   the   CPU
	      registers for this task are entered in the TSTABL.  The AC is
	      1234 (entry 3), and the MQ is 0211 (entry 4).   The  link  is
	      set (bit O of entry 1), and the data field is 2 (bits 9-11 of
	      entry 1).
    
 				      E-1

			EXECUTIVE INTERNAL TASK TABLES
    
 
	  2.  The  Task  Flags  Table  (TFTABL) - contains  1-word  entries
	      holding  various  flags  (bits)  for  each  task to determine
	      whether the task is runnable.  A task is runnable only if its
	      Task  Flags Table entry contains zero.  Each flag (bit) which
	      is set in a nonzero word indicates  a  reason  why  the  task
	      cannot  run.   The currently defined flags, if set, and their
	      meanings are as follows:
     

          Octal	    Symbolic			 Meaning
     
          4000	    NONRWT    Nonresident  Wait - This  task   cannot   run
     			      because it is not in memory.

	  2000	    EFWT      Event Flag Wait - This task is waiting for an
     			      Event  Flag  (which  contains a WAITING value
     			      corresponding to this task) to be POSTed.

          1000	    RUNWT     Run Wait - This task is waiting for a RUN  ER
     			      to  be executed with its number in the AC, or
     			      for the operator to type  "Request  task"  to
     			      the Monitor Console Routine (see Chapter 6).

   	  0400	    SWPWT     Swap Wait - This task cannot run  because  it
     			      is  in  the  process  of  being  brought into
     			      memory.

	  0200	    EORMWT    Event or Message Wait - This task is  waiting
     			      for  an  Event Flag to be set or a message to
     			      arrive, whichever happens first.

	  0100	    USERWT    User Wait - This bit is reserved for  use  by
     			      user-written  tasks.  RTS/8 does not use this
     			      bit.

	  0040	    ENABWT    Enable Wait - This  task  is  waiting  to  be
     			      Enabled.   Use  of  this bit is restricted to
     			      the Monitor Console Routine for  the  "ENable
     			      task"  and  "DIsable  task"  commands.   (See
     			      Chapter 6).

	  0020	    MSGWT     Message Wait - This task  is  waiting  to  be
     			      sent a message.

	  0010	    NETWT     Reserved for future use.

	  0001	    DNEWT     Does Not Exist Wait - This  task  cannot  run
     			      because it is nonexistent.

	  0000	    -	      Task is runnable.

	      The Task Flags Table is located after the Task  State  Table,
	      that is, at location NTASKS+2^4+TSTABL-1 in field 0.

	      Examples:

				      E-2

			EXECUTIVE INTERNAL TASK TABLES


	      1.  If the TFTABL entry for a task is

		       1000

		  the task is waiting to run.
     
	      2.  If the TFTABL entry for a task is

		       0440

	          the task was disabled from running by the operator at the
	          MCR  terminal  while  the nonresident portion of the task
	          was waiting to be swapped in.

	      3. If the TFTABL for a task is

		      0000

	         the task is runnable.  However, this task may not  run  if
	         a task of higher priority has precedence.

	  3.  The Task Input Message Queue Header Table (MSGTBL) - contains
	      2-word entries that represent the "head" (start) of the input
	      message queue for each task:

		   Word 1 - if zero, there are no messages  in  the  queue;
			    if  non-zero, the word is a CDF to the field of
			    the first message in the queue.

	           Word 2 - if word 1 was not zero, this word is a  pointer
			    to  the  address  of  the  first message in the
			    queue.

	      The Message Table is located at the end of the RTS/8
	      Executive in field 0.

	      Example:

	      Consider the following MSGTBL entries for a task.

		   6211
		   2044

	      Since the first entry is a nonzero, there are messages in the
	      input queue waiting for this task to receive them.  The first
	      entry is a CDF instruction to field 1.  The second entry is a
	      pointer indicating that the first message begins at location
	      2044 in field 1.

	  4.  The Residency Table (RESTBL) - contains  2-word  entries  for
	      each nonresident task.

	 	  Word 1 - contains  a  pointer  to  the  task's  Partition
			   Table  entry in bits O through 9.  Bit 10 is set
			   a task is checkpointable,  and  bit  11  is  set

				      E-3

			EXECUTIVE INTERNAL TASK TABLES


			   if  a  task  is  writeable.   Checkpointable and
			   writeable tasks are defined in Section 5.1.

		  Word 2 - contains the absolute block address (plus  1  to
			   allow  for the core control block) of the task's
			   core image on the swap device.

	      The Residency Table is located after the  Task  Flags  Table,
	      that is, at location TFTABL+NTASKS+2 in field 0.
     
	      Example:

	      Consider the following RESTBL entries for a task.

		   1611
		   0124

	      This task has a nonresident portion.   The  4-word  partition
	       table  entry used by this task begins at location 1610.  The
	      task is not checkpointable (bit 10 of entry 1 is a 0), but it
	      is writeable (bit 11 of entry 1 is a 1).

	      The disk-resident portion of this task begins at block 124 on
	      the swap device.  (The save image begins at block 123.)

	  5.  The Partition Table (PARTBL) - contains a  4-word  entry  for
	      each partition.  It is indexed into via a partition number.

		   Word 1 - contains the length  (size)  in  bits  1-5  and
			    field  (bits  6-8) argument of the mass storage
			    device driver call that reads an occupant  into
			    the partition with the "WRITE" bit set.  Bit 11
			    of this word is the partition busy flag.

		   Word 2 - contains the memory address of the partition.

		   Word 3 - contains a pointer to word 1 of the  occupant's
			    RESTBL entry.

		   Word 4 - unused

	      The Partition Table must  begin  at  an  address  that  is  a
	      multiple  of  four.  It is located after the Residency Table,
	      i.e., at location NTASKS-SWAPPER^2+RESTBL+3&7774 in field 0.

	      Example:

	      Consider  the  following  PARTBL  entries  for  a  particular
	      partition.

		   5421
		   1400
		   1553
		   0000


				      E-4

			EXECUTIVE INTERNAL TASK TABLES


	      This partition is currently in use (bit 11 of entry 1 is a 1)
	      by  a  task whose 2-word RESTBL entry begins at location 1553
	      (entry 3).  The partition begins at location 1400  (entry  2)
	      of  field  2  (bits  6-8  of  entry  1).  The partition is 14
	      (octal) pages long (bits 1-5 of entry 1).

     Figure E-1  summarizes  the  internal  task  table  structure  of  the
     Executive.   The  Residency  Table and Partition Table are optional in
     that they are used only when  nonresident  tasks  are  employed.   The
     exact  location  of  these  tables  in memory depends on the number of
     tasks and other parameters in the parameter file.  They can  be  found
     for a particular assembly under the "System Locations:" heading at the
     end of the parameter file assembly listing.
     
     

		   TASK STATE			     TASK FLAGS	
		  TABLE (TSTABL)		   TABLE (TFTABL)	
	    ---------------------------     -----------------------------
     Word 1 | Instruction       Data  |	    | Bits determine if task is |
	    |	 Field	        Field |	    | runnable			|
	    |			      |	    |				|
	    | Link GT UM (IF)	 (DF) |	    |				|
	    |   0   1  5  6-8	 9-11 |     |				|
	    |-------------------------|     -----------------------------
     Word 2 | Contents of Program     |
	    |	Counter (PC)	      |	    Task runnable if entry	
	    |-------------------------|     contains zero
     Word 3 | Contents of Accumulator |
	    | (AC)		      |
	    |-------------------------|
     Word 4 | Contents of Multiplier  |
	    | Quotient (MQ)	      |
	    ---------------------------

	    Upon task execution, TSTABL
	    loaded into corresponding 
	    CPU registers		

	    Upon task interruption, TSTABL
	    entry set to new contents of 
	    CPU registers


	      Figure E-1 Executive Internal Task Table Structure











				      E-5

			EXECUTIVE INTERNAL TASK TABLES


		TASK INPUT MESSAGE		     RESIDENCY
	       QUEUE HEADER (MSGTBL)		   TABLE (RESTBL)
	    ---------------------------     -----------------------------
     Word 1 | If zero, no messages in |	    | Contains pointer to task  |
	    | queue. If nonzero, word |	    | PARTBL entry in bits 0-9; |
	    | is CDF to the field of  |	    | bit 10 - ckeckpointable;  |
	    | first message	      |	    | bit 11 - writeable	|
	    |-------------------------|     -----------------------------
     Word 2 | If nonzero, this word   |     | Block address plus 1 of 	|
	    | is pointer to the first |	    | the task's core image on  |
	    | message in the queue    |     | swap device		|
	    ---------------------------     -----------------------------

	    Represents the "head" of        bit 10 of word 1 is set if
	    the input message queue 	    task checkpointable
	    for each task	    
					    bit 11 of word 1 is set if
					    task writeable




			  PARTITION
			TABLE (PARTBL)
	    --------------------------------------
     Word 1 | Contains the length (size) and     |
	    | Field argument (bits 1-8) of the   |
	    | mass storage device driver call    |
	    | that reads occupant into partition |
	    | with 'write' bit set (bit 0).      |
	    |------------------------------------|
     Word 2 | Contains starting address of the	 |
	    | partition			         |
	    |------------------------------------|
     Word 3 | Contains pointer to word 1 of the  |
	    | occupant's RESTBL entry		 |
	    |------------------------------------|
     Word 4 | Unused				 |
	    | 				      	 |
	    --------------------------------------

	    Bit 0 is always set (write)

	    Bit 11 of word 1 is the partition
	    memory flag


	   Figure E-1 Executive Internal Task Table Structure (cont.)








				      E-6






				   GLOSSARY

     Accumulator	      The  register  in   which   the   arithmetic
			      operations are performed (abbreviated AC).

     Analog		      Representation of information by  continuous
			      variables.

     Analog Channel	      An UDC/ICS functional device.

     Argument		      A variable or constant which is given in  the
			      call of a subroutine as information to it;  a
			      variable upon whose  value  the  value  of  a
			      function  depends; the known reference factor
			      necessary to find an item in a table or array
			      (i.e. the index).

     Assembler		      A program which translates symbolic  op-codes
			      into  machine  language  and  assigns  memory
			      locations for variables and constants.

     Auto-index register      Whenever one of the absolute locations  from,
			      0010  through  0017  in  any  memory field is
			      addressed indirectly, the  contents  of  that
			      location  is incremented by one, rewritten in
			      the same location, and used as the  effective
			      address of the current instruction.

     Auto-restart	      The ability to start the CPU automatically on
			      power-up.

     Baud		      A unit of measure of data flow (one  bit  per
			      second).

     Bit		      A binary digit (each PDP-8  word  is  compose
			      of 12 bits).

     Bit Map		      A method of keeping track of used and  unused
			      entities  by  assigning one bit in a table to
			      each entity.

     Block		      A   set   of   consecutive   machine    words
			      characters   or  digits  handled  as  a  unit
			      particularly  with  reference  to  input   an
			      output;    an   OS/8   block   is  400  octal
			      contiguous words;  also to inhibit a  process
			      from continuing.

     Block Gap		      The blank space between blocks on a recording
			      medium.

     Blocking Bits	      Bits in an RTS/8 Monitor Table which  specify
			      why a given task is blocked.


				  Glossary-1




     Byte		      A group of  binary  digits  usually  operated
			      upon as a unit.

     Cassette		      A magnetic tape device  used  for  program  a
			      data storage.

     Central Processing Unit  The unit of a computing system that  includes
			      the  circuits  controlling the interpretation
			      and execution  of  instructions  (abbreviated
			      CPU).

     Checkpointable Task      A task is checkpointable if it may be swapped
			      out  of  memory  automatically,  without  its
			      consent, to make  room  for  higher  priority
			      tasks.

     Clear		      To erase the contents of a  storage  location
			      by  replacing  the  contents,  normally  with
			      zeros.

     Clock		      A time keeping or measuring device within the
			      computer     system;     provides    periodic
			      interrupts.

     Communication Region     Locations  20-27  of  every  field,  used  to
			      simplify  passing  executive  request  across
			      field boundaries.

     Compute Bound	      Requiring extensive (or total) use of the CPU
			      relative  to other hardware elements (such as
			      I/O devices).

     Configuration	      The number and types of hardware present on a
			      system.

     Contact Channel	      A UDC/ICS functional device.

     Contiguous		      Code  which  resides  in  memory  immediately
			      adjacent to other sections of code.

     Controller		      The circuitry that controls a device.

     Core Image File	      A  file  in  core  image  format   (i.e.,   a
			      'picture' of core); also known as SAVE file.

     Core Storage	      The main high-speed storage of a computer  in
			      which  binary  data  is  represented  by  the
			      switching polarity of magnetic cores.

     Counter Channel	      A UDC/ICS functional device.

     CPU Registers	      High-speed   circuitry    used    to    store
			      information  affecting  the  operation of the
			      CPU (e.g., PC, IF, DF).



				  Glossary-2




     Data		      A general term used  to  denote  any  or  all
			      facts,  numbers,  letters  and  symbols.   It
			      connotes basic elements of information  which
			      can be processed or produced by computer.

     Data Field		      A 3-bit register which determines the  memory
			      field   from   which operands  are  taken  in
			      indirectly       addressed       instructions
			      (abbreviated DF).

     Debug		      To detect, locate and correct mistakes  in  a
			      program.

     Deferred Actions	      Actions which are considered low-priority and
			      are   not   performed  until  higher-priority
			      actions are serviced.

     Deferred Requests	      Requests which  are  considered  low-priority
			      and    are   serviced   after   high-priority
			      requests.

     Derail		      To  transfer  control  or  execution   of   a
			      specified task to a subroutine.

     Device Codes	      Numbers  assigned  to  each  device  in   the
			      system.

     Device Status Register   A register which contains the current  status
			      of a device.

     Digital		      Representation  of  information  by  discrete
			      units.

     Digital Channel	      A UDC/ICS functional device.

     Driver		      See Handler.

     Dynamic		      Pertaining to a quantity that is affected  by
			      some   condition   (such   as  time)  and  is
			      therefore relative to  the  condition;   also
			      refers to features at system run-time.

     Entry Point	      The location in a routine  to  which  control
			      can be transferred and execution begun.

     Event Flag		      The location which contains the status of  an
			      event  (event  being  either a result of some
			      operation, or a physical occurrence).

     Executive		      The program which controls the  execution  of
			      other programs or routines.

     Executive Requests	      Means of communication between tasks and  the
			      RTS/8 Executive.



				  Glossary-3




     Field		      A division of  memory  on  a  PDP-8  computer
			      referring to a 4K section of memory.

     File Gap		      A fixed length of blank tape separating files
			      on  a  recording  medium;  generally  several
			      times the size of a block gap.

     Functional Devices	      The  devices  available  for  use  under  the
			      UDC/ICS handler.

     Gain		      An increase in signal power.

     Generic Codes	      Codes used to identify which type of  UDC/ICS
			      functional  device caused an interrupt and to
			      direct program control to service routines.

     Handler		      A routine which is designed  to  control  the
			      operation of a device.

     I/O Bound		      A condition in which a process is  performing
			      much I/O but using very little CPU time.

     Indirect Address	      An address in a  computer  instruction  which
			      indicates a location where the address of the
			      referenced operand is to be found.

     Initialization Code      Code  which  sets  counters,  switches,   and
			      addresses to zero or other starting values at
			      the beginning of or at prescribed points in a
			      computer routine.

     Input Buffer	      A section of memory used for storage of input
			      data.

     Instruction Field	      A   register   which   holds   the   contents
			      determining from which field the operand of a
			      directly  addressed  instruction  should   be
			      taken (abbreviated IF).

     Interactive	      Highly responsive to real-world inputs.

     Interface		      The common hardware and/or software boundary
			      between two devices or systems.

     Interlock Scheme	      Arranging the  control  of  devices  so  that
			      their operation is interdependent.

     Interrupt		      A break in execution caused by some  external
			      event;   execution  is  usually  resumed at a
			      later time.

     Interrupt Processing Module   
			      A routine which acts upon the external  event
			      which caused an interrupt.



				  Glossary-4




     Interval Queue	      A  list   of   actions   to   perform,   each
			      accompanied  by the interval of time which is
			      to elapse from the  previous  action  to  the
			      current one.

     Line-frequency Clock     A clock whose ticking occurs at a multiple of
			      the power line frequency.

     Link		      A one-bit register in the PDP-8;  an  address
			      pointer  generated  automatically by the PAL8
			      assembler to indirectly address  an  off-page
			      symbol.

     Logical OR		      A logical function  of  two  or  more  inputs
			      which is true whenever either input is true.

     Loop		      A sequence of instructions that  is  executed
			      repeatedly   until   a   terminal   condition
			      prevails.

     Mass Storage Device      A device such as disk or DECtape which stores
			      large  amounts  of data readily accessible to
			      the central processing unit.

     Master Parameter File    A file included in the distributed sources of
			      RTS/8  which  the  user  can edit to indicate
			      parameters    specific    to    his    system
			      configuration.

     Memory Address	      A register which holds the address  specified
			      by a memory reference instruction.

     Message		      A contiguous area of  memory  which  contains
			      information about execution of tasks.

     Message-driven	      An RTS/8 task is called message-driven if  it
			      only   executes   in   response  to  messages
			      received from other tasks.

     Mnemonic		      Alphabetic representation of  a  function  or
			      octal machine instruction.

     Module		      A  routine   which   handles   a   particular
			      function.

     Monitor Console Routine  The Monitor routine which provides  the  user
			      with  functions  which  allow him to control,
			      inspect, and debug his system.

     Multiplier Quotient      A 12-bit register used  in  conjunction  with
			      the   accumulator   to  perform  mathematical
			      operations (abbreviated MQ).





				  Glossary-5




     Multi-programming	      Two or more programs (tasks) in memory at the
			      same time which execute alternately depending
			      on the current state of the system.

     Nonresident Task	      A nonresident task is a task or a portion  of
			      a  task  that  is swapped into memory when it
			      becomes executable.

     No-op		      No operation occurs; control proceeds to  the
			      next instruction in sequence.

     Null Characters	      Characters with ASCII code 000.

     Overflow		      A condition that occurs when  a  mathematical
			      operation  yields a result whose magnitude is
			      greater than the data presentation is capable
			      of storing.

     Pack		      To conserve memory by combining information.

     Page		      A 128-word (decimal) section  of  PDP-8  core
			      memory  beginning  at  an  address which is a
			      multiple of 200(octal).

     Parameter file	      A file used to record arguments which may  be
			      assigned different values.

     Parity Bit		      A  bit  which  indicates  whether  the  total
			      number of binary one digits in a word is even
			      or odd.

     Pointer		      A word containing the address of another word
			      in memory.

     Post		      To post an Event Flag means to set  it  to  a
			      FINISHED   state   via   an  RTS/8  Executive
			      Request.

     Posted		      One  of  the  states  of   an   event   flag,
			      indicating  that  the event is complete; same
			      as "FINISHED".

     Power-fail		      An interruption of power to the computer.

     Priority Scheme	      A scheme by which certain operations  or  the
			      execution  of  a set of instructions is given
			      preference over other operations.

     Program Counter	      A register which contains the address of  the
			      next  instruction to be executed (abbreviated
			      PC).

     Promptinq Character      A  character  which  prints  on  the  console
			      terminal  and  cues  the user to perform some
			      action.


				  Glossary-6




     Queue		      A waiting list (e.g.,  a  queue  of  programs
			      waiting for processing time).

     Ready Flag		      A bit which a device controller sets when  it
			      is ready to accept commands from the CPU.

     Real-time System	      A system in which  computation  is  performed
			      while a related physical process is occurring
			      so that the results of the computation can be
			      used  in  guiding  or  measuring the physical
			      process.

     Receiver		      The task which has received  a  message  from
			      another task (sender).

     Record		      A collection of related items of data treated
			      as a unit.

     Record Header Area	      An area of at least 40(octal) words in length
			      which   contains   information  necessary  to
			      perform cassette operations.

     Ring-buffer	      A  storage  area  for  data  accessed  on   a
			      first-in,  first-out basis. Similar to Queue,
			      but usually  involves  storage  of  character
			      codes.

     Scheduling		      The  operation  of  sharing  resources  among
			      computing tasks.

     Sender		      The task which has sent a message to  another
			      task (receiver).

     Sign Bit		      The bit which contains the sign of a number.

     Simulate		      To represent the function of a device, system
			      or  program  with  another  device, system or
			      program.

     Skip Chain		      An instruction sequence which determines  the
			      source  of  an  interrupt request on a PDP-8;
			      contains one or more tests for each  possible
			      (hardware) interrupt condition.

     State		      A complete description of the condition of  a
			      piece of hardware or of a task.

     Status		      That portion of the state which other devices
			      or tasks might be interested in.

     Subchannel		      One of the 4 channels  of  a  UDC/ICS  analog
			      functional device.

     Suspend		      To temporarily halt execution of a task while
			      another task of higher priority runs.


				  Glossary-7




     Symbols		      Names which can be assigned values  or  which
			      can be used to indicate specific locations in
			      a program.

     Synchronization	      A means of coordinating tasks (through  event
			      flags) so that one task executes while others
			      wait.

     System Ticks	      An RTS/8 convention designed to  obviate  the
			      tasks   in   the   system  from  knowing  the
			      frequency of the clock.

     Task		      A task is a routine which performs a specific
			      function.    A  task  may  be  "resident"  or
			      "nonresident".    A    resident    task    is
			      permanently located in memory.  A nonresident
			      task is loaded into memory as  it  is  needed
			      and can be overlaid after its completion.

     Task Flags Table	      A  table  of  1-word  entries  in  the  RTS/8
			      Executive whose contents determine whether or
			      not a task is runnable.

     Task Input Message Queue
     Header Table	      A table of 2-word entries which represent the
			      head  of  the  input  message  queue for each
			      task.

     Task Number	      A unique number between 1  and  63  (decimal)
			      assigned to each task in an RTS/8 system.

     Task State Table	      A table of 4-word entries which contains  the
			      most  recent  contents  of  CPU registers for
			      each task.

     Task Switching	      The act of stopping execution of one task and
			      continuing  execution  of  another  from  the
			      point that it was last stopped.

     Terminal		      A peripheral device in a system through which
			      data can enter or leave the computer.

     Utilities		      Routines  to  perform   non-Monitor   related
			      functions.

     Word		      In the PDP-8, a 12-bit unit of data which may
			      be stored in one addressable location.










				  Glossary-8





				     INDEX


     ALTMODE, 4-5, 5-1                    DECtape handler system parameters,
     Analog input UDC/ICS operation,          6-15
         4-29                             Demonstration program, 8-1
     Analog output UDC/ICS operation,     DEposit command, 5-6
         4-29                             DERAIL ER, 9-6
     Arbitrary boundaries, 9-8            Digital input UDC/ICS operation,
     Assembling nonresident tasks,            4-31
         7-7                              Digital output UDC/ICS operation,
     Assembling tasks, 6-5, 8-14              4-30
     Assembly,                            DIsable command, 5-4
     nonresident tasks, 7-8               Disable contacts UDC/ICS operation,
     Assembly error messages, D-1             4-34
     Assembly parameters, UDC/ICS,        Disable counter UDC/ICS operation,
         4-34                                 4-33
                                          Distributed source files, A-1

     Batch control,
       nonresident tasks, 7-9             Editing parameter file, 6-6, 6-9
     Batch stream, 6-6, 6-9               ENable command, 5-4
     BLKARG ER, 3-7                       Enable contacts UDC/ICS operation,
     Buffers, 7-6                             4-33
                                          Enable counter UDC/ICS operation,
                                              4-31
     CAL instruction, 3-1                 Error conditions,
     CAncel command, 5-4                  UDC/ICS, 4-35
     Cassette file support handler,       Event flag states summary, 2-3
         4-39                             Event flags, 2-2
     Cassette file support system         EXamine command, 5-6
         tasks, 4-40                      Executive internal task tables,
     Cassette handler, 4-36                   2-5, E-1
     Change of state UDC/ICS opera-       Executive KL8-A support, 4-42
         tion, 4-34                       Executive request wait states,
     Character mode, 4-5                      3-14
     Checkpointable tasks, 7-3            Executive requests,
     Clock handler, 4-2                     BLKARG, 3-7
     Clock handler system parameters,       DERAIL, 9-6
         6-11                               POST, 3-5
     CTRL/C, 4-5, 5-1                       RECEIVE, 3-4
     Communication region, 3-1              RUN, 3-9
     Component sizes, B-1                   SEND, 3-2
     Control files,                         SENDW, 3-3
       use of, 6-10                          SKPINS, 3-11
     Core image, 7-7, 7-8                   SUSPND, 3-8
     Creating an RTS/8 system, 6-5          UNBARG, 3-8
     Creating SAVE image file, 6-7,         WAITE, 3-3
         7-7                                WAITX, 9-6
                                          EXIT command, 5-7
                                          EXIT task, 4-44
     DAte command, 5-2                    EXIT task system parameters, 6-16
     Debugging,
       nonresident task, 7-9


				    Index-1

				 INDEX (CONT.)



     Field mapping, 4-23                  MCR Commands (cont.)
     FINISHED state, 2-2                    ENable, 5-4
     Floppy disk control file, 6-11         EXamine address, 5-6
     Floppy disk handler, 4-14              EXIT, 5-7
     Flowcharts, C-1                        NAme, 5-2
     FREE command, 7-4                      OPen address, 5-6
                                            POst address, 5-6
                                            REquest, 5-3
     Generic code UDC/ICS operation,        STop, 5-4
	 4-31                               SYstat, 5-5
                                            TIme, 5-2
                                          MCR component size, B-6
     Inhibiting task switching, 9-2       MCR error messages, 5-7
     Instructions,                        MCR system parameters, 6-14
       CAL, 3-1                           Memory partitions, 7-3
       POSTDS, 3-11                       Message header, 2-3
     Instructions (cont.),                Message table, E-3
       WAITM, 9-4
     Interrupt module restrictions,
         3-11                             NAme command, 5-2
     Interrupt skip chain, 3-10            Nonresident MCR, 5-7
     Intertask messages, 2-3              Nonresident task debugging, 7-9
                                          Nonresident task implementation,
                                              7-8
     KL8-A support system parameters,     Nonresident task initialization,
         6-15                                 7-5
       OS/8 support task, 4-43            Nonresident task parameters, 7-6
       TTY task, 4-42                     Nonresident tasks, 7-1
       User task, 4-43                    Nonresident tasks,
                                            assembly, 7-8
                                            batch control, 7-9
     LINCtape handler, 4-18                 loading, 7-9
     Line mode, 4-5                         SAVE image file, 7-9
     Line printer handler, 4-11             starting, 7-9
     Line printer system parameters,
         6-15
     Loading,                             Obtaining listings, 6-5
       nonresident tasks, 7-9             OPen command, 5-6
     Loading tasks, 6-7, 8-14             OS/8 file support task, 4-25
                                          OS/8 operating system, 4-21
                                          OS/8 support task, 4-21
     Mass storage handlers, 4-12          OS/8 support task system param-
     MCR command arguments,                   eters, 6-14
       address, 5-1                       OS/8-RTS/8 communication, 4-23
       comma, 5-1
       sinqle space, 5-1
       task-ID, 5-1                       Parameter file,
       time-of-day, 5-1                     task definitions, 6-2
       word, 5-2                            task setup, 6-4
     MCR commands,                          task specifications, 6-3
       CAncel, 5-4                        Parameter fide structure, 6-1
       DAte, 5-2                          Partition parameter initializa-
       DEposit address, 5-6                   tion, 7-8
       DIsable, 5-4                       Partition table, E-4

				    Index-2

				 INDEX (CONT.)


     PDP-8A null task, 4-41               System tasks (cont.)
     PENDING state, 2-2                     EXIT, 4-44
     Performing a reschedule, 9-1           floppy disk handler, 4-14
     POst address command, 5-6              LINCtape handler, 4-18
     POST ER, 3-5                           Line printer handler, 4-11
     POSTDS instruction, 3-11               mass storage handler, 4-12
     Power fail task, 4-20                  OS/8 file support, 4-25
                                            OS/8 support, 4-21
                                            PDP-8A null, 4-41
     Read counter UDC/ICS operation,        power fail, 4-20
         4-33                               terminal handler, 4-5
     Real-time system operation, 1-2        UDC/ICS handler, 4-27
     RECEIVE ER, 3-4
     REquest command, 5-3
     Residency table, E-3                 Task communication, 2-1
     RTS/8 description, 1-1               Task flags table, E-2
     RTS/8 task. structure, 2-1           Task number, 2-1
     RUBOUT, 4-5                          Task state table, E-1
     RUN ER, 3-9                          Task status report, 5-5
                                          Task synchronization, 2-2
                                          Terminal handler, 4-5
     Sample task program, 6-8             Terminal handler system param-
     SAVE image file,                         eters, 6-12
       creating, 6-7, 7-7                 Terminal parameter default values,
       nonresident tasks, 7-9                 4-10
     Saving the system, 6-7, 8-14         TIme command, 5-2
     SEND ER, 3-2                         Timeshare function disabled, 4-21
     SENDW ER, 3-3                        TTY control file, 6-10
     SKPINS ER, 3-11                      TTY task KL8-A support, 4-42
     Starting,
       nonresident tasks, 7-9
     STop command, 5-4                    UDC/ICS assembly parameters, 4-35
     SUSPND ER, 3-8                       UDC/ICS error conditions, 4-35
     Swap device, 7-1, 7-6                UDC/ICS handler, 4-27
     Swapper system parameters, 6-12      UDC/ICS handler system tasks, 4-27
     Syntaetic constructions, 5-1         UDC/ICS operation,
     SYstat command, 5-5                    analog input, 4-29
     System parameters,                     analog output, 4-29
       clock handler, 6-11                  change of state, 4-34
       DECtape handler, 6-15                digital input, 4-31
       EXIT task, 6-16                      digital output, 4-30
       KL8-A support, 6-15                  disable contacts, 4-34
       line printer, 6-15                   disable counter, 4-33
       MCR, 6-14                            enable contacts, 4-33
       OS/8 support task, 6-14              enable counter, 4-31
       swapper, 6-12                        generic code, 4-31
       terminal handler, 6-12               read counter, 4-33
     System status report code, 5-5       UNBARG ER, 3-8
     System tables direct references,     Use of control files, 6-10
         9-9                              User task KL8-A support, 4-43
     System task summary, 4-1             Using BITMAP program, 6-8, 7-5
     System tasks,                        Using interrupts, 3-10
       cassette file support, 4-39
       cassette handler, 4-36
       clock handler, 4-2                 WAITBITS symbolic names, 3-9

				    Index-3

				 INDEX (CONT.)


     WAITE ER, 3-3
     WAITING state, 2-2
     WAITM instruction, 9-4
     WAITX ER, 9-5
     Writeable tasks, 7-3
     Writing delicate code, 9-1


















































				    Index-4