SYSGEN.DOC





















				  DISCLAIMER

		This document file was created by scanning  the
		original  document and then editing the scanned
		text.  As much as possible, the  original  text
		format  was restored.  Some format changes were
		made to insure this  document  would  print  on
		current laser printers using 60 lines per page.
		The  original  spelling  and  grammar  has been
		preserved.


		1-Sep-1996



							    RTS/8
						   System Generation Manual
						     Order No. AA-D943A-TA




				 February 1979












				   ABSTRACT

     This manual describes the procedure by which a user generates an RTS/8
     realtime operating system. After answering System Generation
     questions, the program can automatically build, using OS/8 BATCH and
     MACREL/LINK, an RTS/8 system with little or no user intervention.

     The System Generation procedure is a flexible one that presents the
     user with the minimum number of questions needed to build a system. As
     user systems may vary significantly, the RTS/8 System Generation
     permits modifications in its interactive dialogue so that the System
     Generation is unique to a user's needs.






		SUPERSESSION INFORMATION: This is a new manual.
		VERSION: V01









	 ------------------------------------------------------------
	 | To order additional copies of this document, contact the |
	 |      Software Distribution Center, Digital Equipment     |
	 |	  Corporation, Maynard, Massachusetts 01754	    |
	 ------------------------------------------------------------

	    digital equipment corporation - maynard. massachusetts


					      First Printing, February 1979


     The information in this document is subject to change without notice
     (and should not be construed as a commitment by Digital Equipment
     Corporation.  Digital Equipment Corporation assumes no responsibility
     for any errors that may appear in this document.

     The software described in this document is furnished under a license
     and may only be used or copied in accordance with the terms of such
     license.

     No responsibility is assumed for the use or reliability of software on
     equipment that is not supplied by DIGITAL or its affiliated companies.










	     Copyright  (c)  1979 by Digital Equipment Corporation










     The postage-prepaid READER'S COMMENTS form on the last page of this
     document requests the user's critical evaluation to assist us in
     preparing future documentation.


     The following are trademarks of Digital Equipment Corporation:


	      DIGITAL		  DECsystem-10	      MASSBUS
	      DEC		  DECtape	      OMNIBUS
	      PDP		  DIBOL		      OS/8
	      DECUS		  EDUSYSTEM	      PHA
	      UNIBUS		  FLIP CHIP	      RSTS
	      COMPUTER LABS	  FOCAL		      RSX
	      COMTEX		  INDAC		      TYPESET-8
	      DDT		  LAB-8		      TYPESET-11
	      DECCOMM		  DECSYSTEM-20	      TMS-11
	      ASSIST-11		  RTS-8		      ITPS-10
	      VAX		  VMS		      SBI
	      DECnet		  IAS		      PDT
	      DATATRIEVE	  TRAX






				    CONTENTS

								   Page

     PREFACE							   v

     CHAPTER  1	INTRODUCTION					   1-1

     CHAPTER  2	THE SYSGEN DIALOGUE				   2-1

	      2.1   OVERVIEW					   2-1
	      2.2   THE DIALOGUE				   2-2
	      2.3   PASS 2 AND BATCH				   2-46
	      2.4   RTS/8 SYSGEN DOCUMENT NUMBERS		   2-51

     CHAPTER  3 TWO EXAMPLE SYSGENS				   3-1

	      3.1   OVERVIEW					   3-1
	      3.2   A DEFAULT SYSGEN				   3-1
	      3.3   A NORMAL SYSGEN				   3-4

     CHAPTER  4 MODIFYING THE SYSGEN				   4-1

	      4.1   OVERVIEW					   4-1
	      4.2   THE STRUCTURE OF SCRIPT.MA			   4-1
	      4.2.1   Record Directory				   4-2
	      4.2.2   Script Records				   4-3
	      4.2.3   Parameter Records				   4-10
	      4.2.4   Skeleton Records				   4-12
	      4.2.5   Error Message Records			   4-12
	      4.2.6   LINK and MACREL BATCH Records		   4-12
	      4.2.7   Limit Records				   4-12
	      4.3   EXAMPLES					   4-13
	      4.3.1   Deleting Questions			   4-13
	      4.3.2   Adding Questions				   4-17
	      4.3.3   Changing the Default			   4-31
	      4.3.4   Multiple TTY Systems			   4-34

     APPENDIX A	    RTS/8 SYSTEM GENERATION SOURCE FILES	   A-1

     APPENDIX B     DEC/X8 SPECIFICATION SHEET			   B-1

     APPENDIX C     SYSGEN CHECK LIST				   C-1

     APPENDIX D	    RTS/8 PARAMETER LISTING			   D-1

     APPENDIX E	    ERROR MESSAGES				   E-1

     INDEX						       Index-1




				      iii






				    PREFACE



     This manual describes the RTS/8 system generation  procedure.   System
     generation,  or  SYSGEN,  is  an  interactive  procedure  you use when
     building RTS/8 operating systems from source  modules.   These  source
     modules are tasks that DIGITAL supplies and tasks that you create.  In
     addition,  the  design  of  the RTS/8 SYSGEN script allows you to make
     changes in the interactive  dialogue  so  that  the  SYSGEN  procedure
     itself more precisely meets your needs.

     The manner in which you program an RTS/8 operating system after it  is
     running  is  described  in  the  RTS/8 User's Manual, V3.  This SYSGEN
     manual assumes that you are familiar with the  DIGITAL-supplied  tasks
     as  they  are  described in the User's Manual.  For example, the RTS/8
     Monitor Console Routine is not described.  You are  expected  to  have
     read the sections of the User's Manual which describe it.

     The RTS/8 SYSGEN, among other functions,  allows  you  to  incorporate
     various  device handlers into your RTS/8 system.  However, this manual
     does not attempt to describe the devices themselves.  It  assumes  you
     know  which  devices  are  in  your  system  and are familiar with the
     information contained in the hardware manual that  you  received  when
     you purchased the device.  For example, no attempt is made to describe
     an RLO1 disk.

     The first three chapters of this  manual  introduce  and  explain  the
     SYSGEN.   Chapter 1 is an overview of the SYSGEN process.  The portion
     of the SYSGEN that is most  visible  to  a  user  is  the  interactive
     dialogue.   Chapter 2 discusses this dialogue.  Any SYSGEN you perform
     uses portions of this dialogue.  As Chapter 2 presents the dialogue in
     its entirety, you may find it difficult to see the continuity and flow
     inherent in the information the SYSGEN prints.  Consequently,  Chapter
     3 is a listing of two example SYSGENs.

     The advanced user may wish to  change  the  SYSGEN  so  that  it  more
     precisely  conforms  to  the kinds of systems that will be built.  The
     final chapter details how you may tailor the SYSGEN procedure to  your
     needs.













				       v







				   CHAPTER 1

				 INTRODUCTION


     RTS/8 SYSGEN is the procedure you use to build a  real-time  operating
     system.   Unless you decide to reconfigure the SYSGEN (see Chapter 4),
     most of the operations that the SYSGEN performs are invisible to  you;
     that  is, the operations the SYSGEN performs are not seen and, in most
     cases, are not important to what you are doing.

     The minimum memory size that you will need to run the SYSGEN  is  12K.
     Also,  the  SYSGEN  program,  SYSGEN.SV,  must  reside  on SYS and the
     dialogue must reside on a mass storage device.  If you chain to BATCH,
     you  will need a 16K system.  In addition, you conceivably may require
     more memory than 16K if you are creating a large RTS/8 system.

     The SYSGEN program produces three batch files that OS/8 BATCH uses  to
     create  the  RTS/8  system.  The SYSGEN may also create TTY and floppy
     disk control files.  These files contain information that is  specific
     to  a  particular  TTY  or floppy device.  When MACREL creates the .RB
     (Relocatable Binary) file, it uses the equates in these control  files
     to create a task that is specific to your configuration.

     The SYSGEN is an interactive dialogue;  that is, it asks you questions
     and  you  supply  answers.  After you answer the questions, the SYSGEN
     builds a real-time operating system that consists of an Executive (the
     routines  that  control  task execution) and other tasks.  These other
     tasks are either DIGITAL-supplied tasks or those that you create.

     You may also build an  RTS/8  system  that  consists  of  a  real-time
     operating system foreground and an OS/8 background.  In such a system,
     the real-time tasks have primary control of the computer.  When  these
     tasks  do  not  need to use the computer, OS/8 can run;  that is, OS/8
     runs in the "background" of the RTS/8 operating system.

     You begin executing the SYSGEN, called SYSGEN.SV on  its  distribution
     medium, by typing

     R SYSGEN

     in response to the OS/8 prompt.  (The SYSGEN runs only under OS/8  and
     SYSGEN.SV must be on SYS.) If SYSGEN.SV is not on SYS, you must use an
     OS/8 COPY command to bring it to SYS.  The program then asks you which
     device  contains  the  interactive  dialogue.   The  dialogue,  called
     SCRIPT.SV on the distribution medium, can either reside on SYS  or  on
     any  other  file-structured  device  that  OS/8  recognizes.   If  the
     dialogue is on SYS, you type a carriage return.  Otherwise,  type  the
     OS/8 device name.




				      1-1

				 INTRODUCTION


     After you respond to this question, the SYSGEN  dialogue  begins.   In
     general,  each  question is composed of three parts.  The first is the
     question itself.  The second is a string within  square  brackets  [].
     This string indicates the type of response you must type;  for example
     [D] means decimal, [Y/N] means YES/NO and so on.  The  third  portion,
     within parentheses, indicates the default answer.  For example:

     DO YOU WANT ASSEMBLY LISTINGS [Y/N] (N):

     In this question, N (meaning no) is the default answer that you select
     by typing a carriage return.

     Many of the questions pertain to DIGITAL supplied tasks.  For some  of
     the  DIGITAL  tasks, you need only state that you wish to include that
     task in the RTS/8 system.  Other DIGITAL tasks may require  more  than
     one  response.   For example, if you include the RTS/8 Monitor Console
     Routine, the SYSGEN eventually asks if you wish to include the  SYSTAT
     command.

     The first series of SYSGEN questions ask  you  to  supply  information
     about  the  computer  on which you will run RTS/8.  A second series of
     questions ask where the SYSGEN should  store  output  files,  what  it
     should  do  with the output files, and other similar information.  For
     example, you may  create  an  RTS/8  system  that  provides  you  with
     assembly listings, linker load maps, and comes up running.

     The SYSGEN then asks which DIGITAL tasks you wish to  include  in  the
     system.   It  then  asks  questions about these tasks (if applicable).
     The last questions of the dialogue ask if you  wish  to  include  user
     tasks  and in which partitions you wish them to reside (if the task is
     nonresident), if you wish  to  change  task  priorities,  and  if  the
     partition allocation is correct.

     During any one session, the SYSGEN does not print all the questions it
     is capable of asking because questions may be mutually exclusive.  For
     example, if you state that the computer upon which RTS/8 will  execute
     does  not include EAE hardware, the SYSGEN does not ask if you wish to
     save the contents of the EAE registers. Consequently, you see only the
     questions that are necessary to build the system.

     While typing answers, you may edit your response by using  the  delete
     key  or  erase the entire answer with a CTRL/U.  If, however, you type
     an incorrect response, the SYSGEN prints an  error  message  and  then
     reprints  the  question.  A list of error messages appears in Appendix
     E.

     In general, you must provide four types of information to the SYSGEN.

	  o  You must tell the SYSGEN what actions it is to perform when it
	     completes  the  interactive  dialogue.   These actions include
	     writing output files, creating listings, and chaining  to  the
	     RTS/8 system.



				      1-2

				 INTRODUCTION


	  o  You must provide  information  that  tells  the  SYSGEN  which
	     machine  you are creating an RTS/8 system for and the kinds of
	     hardware (not peripherals) that exist in the configuration.

	  o  You must specify which of the DIGITAL tasks you  will  include
	     in  the  system.   The  DIGITAL  tasks, for the most part, are
	     handlers for peripheral devices.  Other DIGITAL tasks are  the
	     Monitor  Console Routine and the Power Fail Task.  For some of
	     the  DIGITAL  tasks,  you  must  provide   specific   hardware
	     information such as the peripheral's device code.

	  o  You can place tasks that you write into the RTS/8 system.  You
	     may  also  make  any user task nonresident and place it into a
	     partition.

     When you begin a SYSGEN, you should have all the information you  will
     need  with  you  at the terminal.  Appendix C is a checklist of SYSGEN
     questions.  Using a copy of this form, you can fill in your  responses
     before you sit down at the terminal.  In addition, this form documents
     the systems that you create.

     The RTS/8 SYSGEN also allows you to create a unique  SYSGEN  procedure
     as  well  as  a  unique  operating  system.  By customizing the SYSGEN
     procedure, you create an interactive dialogue  and  presentation  that
     best  fits  your needs.  For example, the SYSGEN contains questions on
     RF02 and DF32 fixed head disks and LINCtapes.  If your system does not
     contain these devices, you may make a simple change in SCRIPT.MA  (the
     source  program  for  SCRIPT.SV) using any text editor.  These changes
     prevent the SYSGEN from asking these questions.

     The following two chapters  present  the  SYSGEN  dialogue.   For  the
     novice  user  of  the SYSGEN, these are the only chapters that need be
     read as they discuss the SYSGEN that DIGITAL distributes.

     The user who wishes to  make  modifications  in  the  SYSGEN  dialogue
     should  read  Chapter 4, which discusses how you can delete questions,
     add questions, and change the default system.


















				      1-3







				   CHAPTER 2

			      THE SYSGEN DIALOGUE


     2.1  OVERVIEW

     This chapter  describes  RTS/8  SYSGEN  questions,  expected  answers,
     SYSGEN  remarks, and SYSGEN run paths.  Because the SYSGEN chooses the
     questions it prints (basing its choices on the  answers  you  give  to
     other  questions), some of the questions in this chapter may appear to
     be out of order.  In addition, other questions were purposely  printed
     here  in  a  different order so that you may more fully understand the
     material that the SYSGEN offers.

     Chapter 3 is closely related to  this  chapter  in  that  it  consists
     entirely  of  two  example  dialogues.   (These  examples  present the
     dialogue in the order they would appear on your terminal.)

     The following section contains four types of information.

	  o  The first is the question  that  the  SYSGEN  prints.   SYSGEN
	     questions  appear  in  capital  letters  and begin at the left
	     margin.

	  o  The second is the remark, also  printed  in  capital  letters,
	     that  the  SYSGEN  prints  if  you ask it to.  The remarks are
	     indented from the left margin.  (The SYSGEN  does  not  indent
	     these remarks when it prints them.)

	  o  The third type of  information  is  remarks  that  the  SYSGEN
	     always  prints.   These  remarks appear in capital letters and
	     also begin at the left margin.  To distinguish  these  remarks
	     from  questions,  each  line  of the remark is followed by the
	     word "remark" in this chapter.

	  o  The fourth kind of information is a further explanation of the
	     question.   This  explanation (in upper and lower case) is not
	     part of the SYSGEN.

     Some of the upper and lower case explanations state that  if  you  are
     unsure  if  something exists in your system or if you do not have some
     information, such as a device code, you should check with your  system
     manager  or  your  sales  representative.  You can also check the form
     that DIGITAL provided when you  purchased  your  system.   This  form,
     reproduced  as  Appendix  B,  lists the device codes.  In this sample,
     note that the devices you purchased are listed in  column  1  and  the
     device codes in column 2.





				      2-1

			      THE SYSGEN DIALOGUE


     2.2  THE DIALOGUE

     Before running the SYSGEN, you should type an OS/8


     SET TTY NO PAUSE


     command because page pauses are  unnecessary  (and  distracting)  when
     running the SYSGEN program.

     The machine you use to create the RTS/8 system  must  contain  12K  of
     memory.   If  you will chain to BATCH, as will be discussed below, you
     must  have  sufficient  memory  to  assemble  and  link   the   system
     (ordinarily, 16K).

     You begin the SYSGEN by running the SYSGEN.SV program.   This  program
     runs only under OS/8.  If SYSGEN is not on the system device, you must
     copy it to SYS.  After the OS/8 monitor prompt, type


     R SYSGEN


     After the SYSGEN is running, it prints the question:


     ON WHAT DEVICE IS SCRIPT.SV LOCATED ? :


     SCRIPT.SV is the file that  contains  the  interactive  dialogue.   If
     SCRIPT.SV is on SYS, type a carriage return.  Otherwise, type the OS/8
     name of the device upon which the file SCRIPT.SV resides.  The  SYSGEN
     program then begins printing the interactive dialogue.


     RTS/8 V03 SYSTEM BUILDER PROGRAM V01.			     remark
								     remark
     THIS PROGRAM IS A CONVERSATIONAL				     remark
     QUESTION AND ANSWER SYSTEM FOR				     remark
     BUILDING RTS/8 REAL TIME SYSTEMS.				     remark
								     remark
     THE QUESTIONS AND EXPLANATIONS IN THIS			     remark
     DIALOGUE ARE BRIEF. CHAPTER 2 IN THE			     remark
     SYSTEM GENERATION MANUAL INCLUDES AD-			     remark
     DITIONAL INFORMATION.					     remark

     DO YOU WANT PROGRAM OPERATION
     INFORMATION? (YOU MAY TYPE Y FOR YES OR N
     FOR NO FOLLOWED BY A CARRIAGE RETURN):


     If you answer "Y" to this question, you receive an explanation of  how
     you  interact with the SYSGEN dialogue.  If you are using this program

				      2-2

			      THE SYSGEN DIALOGUE


     for the first time, you  should  read  these  instructions  carefully.
     (The following paragraphs also explain how to use the SYSGEN program.)

     The standard SYSGEN question has the following format


	  NUMBER    QUESTION    ANSWER-TYPE    DEFAULT


     Each of these elements is discussed in the following  paragraphs.   An
     example of a question that the SYSGEN prints is


	  003 DO YOU WISH TO BUILD AN RTS/8 SYSTEM WITHOUT
	  SPECIFYING PARAMETERS? [Y/N] (N):


     The SYSGEN discussion begins with a description  of  the  answer-types
     that SYSGEN expects to a question.


	  YES OR NO ANSWERS ARE INDICATED
	  BY A [Y/N] NOTATION. TYPE A 'Y' FOR YES
	  OR AN 'N' FOR NO, FOLLOWED BY A CARRIAGE
	  RETURN, TO ANSWER THE QUESTION.


     Answer a YES/NO question with a Y or N or with a YES or NO.  Note that
     the  SYSGEN does not record your response to a question until you type
     a carriage return.


	  QUESTIONS REQUIRING A NUMERICAL RESPONSE
	  ARE INDICATED BY A [D] FOR DECIMAL OR AN [O]
	  FOR OCTAL.  ENTER THE NUMBER FOLLOWED BY
	  A CARRIAGE RETURN.  (ALWAYS INTEGER)


     If your response to a question is a number, type the number  and  then
     type  a  carriage  return.  The SYSGEN checks to ensure that numerical
     responses do not contain non-numeric characters.  SYSGEN always checks
     to  determine  if numerical answers are within acceptable limits.  For
     example, if your answer to a question was 100 (octal) and the  largest
     answer SYSGEN allows for the question is 77 (octal), the SYSGEN prints
     an error message.  Also, if your answer is  greater  than  six  digits
     long, SYSGEN prints an error message.  (Some teletype questions accept
     only five character or digit answers.) If the expected response is  an
     octal  number,  SYSGEN  rejects any number that contains an 8 or 9 and
     prints an error message.

     Chapter 4 discusses how SYSGEN evaluates numerical answers and how you
     may change the limits.



				      2-3

			      THE SYSGEN DIALOGUE


     ARE YOU READY TO CONTINUE? [Y/N] (Y):


     When you finish reading the above instructions, type a response to the
     ARE YOU READY question.  You may type a Y or, because Y is the default
     answer, a carriage return.  (See below for an explanation  of  default
     answers.)  If  you  type  an  N, the SYSGEN repeats the question.  Any
     other response produces an error message.

     This question exists  so  that  the  SYSGEN  does  not  print  further
     instructions  until  you  tell  it  that  you  are ready.  (If you are
     displaying the information on a hard copy terminal, you  may  wish  to
     remove this question.  See Chapter 4.)

     After you answer this question, SYSGEN types additional information.


	  QUESTIONS REQUIRING AN ALPHANUMERIC
	  ANSWER ARE INDICATED BY [A].  RESPOND
	  BY TYPING THE ALPHANUMERIC DATA FOLLOWED
	  BY A CARRIAGE RETURN.


     The error-checking that the SYSGEN performs  on  alphanumeric  answers
     determines  if you type too many characters and if the answer contains
     characters other than the upper case  letters  A  through  Z  and  the
     numbers  0  through 9.  Because many alphanumeric responses are device
     specifications, you must be especially careful that  you  enter  these
     responses correctly.  If you do not, OS/8 BATCH or the generated RTS/8
     system cannot execute.


	  IF YOU WOULD LIKE AN EXPLANATION
	  OF A QUESTION, TYPE A ? FOLLOWED BY A CARRIAGE
	  RETURN.  THE PROGRAM THEN PRINTS AN EXPLANA
	  TION AND ALSO REPRINTS THE QUESTION.


     Most questions have explanations.  The purpose of  these  explanations
     is  to  jog  your  memory about what the question is asking.  For more
     information, you should read this  manual,  the  appropriate  hardware
     manual, or the RTS/8 User's Manual.		    ___________________


	  ON THE LINE FOLLOWING MOST REMARKS IS A
	  DOCUMENTATION NUMBER OF THE FORM
	  (DOC. NO NNN). YOU USE THIS NUMBER TO LOCATE
	  ADDITIONAL INFORMATION IN THE SYSTEM GENERATION
	  MANUAL.


     The documentation number gives you a means to find information in this
     chapter while you are generating a system.


				      2-4

			      THE SYSGEN DIALOGUE


     The last page of this chapter is a table that lists all  the  document
     numbers  that  the SYSGEN references.  Across from the document number
     is the page in this manual where you can find additional  information.
     (These  numbers are the same as the MACREL tag that the SYSGEN uses to
     locate the remark.)


	  EACH QUESTION HAS A NUMBER ASSOCIATED
	  WITH IT.  IF YOU NOTICE A MISTAKE DURING AN
	  RTS/8 QUESTION SESSION, TYPING #NNN
	  CAUSES QUESTION NUMBER NNN TO BE REPEATED.

	  YOU CAN THEN CHANGE THE ANSWER TO NNN.
	  THE PROGRAM THEN RESUMES AT THIS NEW
	  QUESTION. IT ALSO RENUMBERS QUESTIONS
	  BEGINNING AT THIS NUMBER.  (NOTE THAT
	  AFTER A TASK PRIORITY CHANGE, THIS FEATURE IS NOT
	  SERVICED.)


     For example, if you are on question 47 and you  wish  to  change  your
     answer  to  question  44, you type #44;  the SYSGEN then reprints that
     question.

     You may only branch backwards.  When the SYSGEN branches,  it  removes
     the  answers  to  questions  it  branches  over.   Therefore, you must
     reanswer questions that the SYSGEN branches over.

     Because the SYSGEN dynamically numbers questions, it is possible  that
     the  question  you  branched  from will have a different number if you
     reencounter that question.  In  the  above  example,  if  question  44
     branches  in  a different manner than it previously did, then the next
     time question 47 appears, it will have a different number.   Moreover,
     if  your  answer  to  question  44 means that question 47 is no longer
     relevant, the SYSGEN does not repeat it.

     After you add your own tasks to the system in  response  to  a  SYSGEN
     question (this occurs near the end of the SYSGEN), it asks if you wish
     to change the priority of any of the tasks in the system.  After  this
     question,  you  cannot  use  the  # branching feature to jump to other
     questions.  See DOC. NO 312 for information on task priority changes.


	  IF YOU TYPE AN INVALID ANSWER, THE PROGRAM
	  PRINTS AN ERROR MESSAGE, AND THEN REPRINTS
	  THE QUESTION.


     Appendix E lists the error messages and explains  the  responses  that
     cause  the  SYSGEN  to print a message.  For all non-fatal errors, the
     SYSGEN retypes the question to which you gave an  incorrect  response.
     If  the  error  was fatal, control returns to the OS/8 monitor.  Fatal
     errors occur only if


				      2-5

			      THE SYSGEN DIALOGUE


	  1.  BATCH, TTY, and other similar utilities do not exist  in  the
	      system upon which you are generating the RTS/8 system.

	  2.  You enter an incorrect device specification  and  the  SYSGEN
	      cannot locate the devices.

	  3.  You make errors in modifying  the  SYSGEN  (as  described  in
	      Chapter 4).

	  4.  The device to which you send SYSGEN output files do not  have
	      sufficient space to contain the files.

     All other errors are non-fatal.


	  CONTROL/C RETURNS YOU TO THE OS/8 KEY-
	  BOARD MONITOR AND ABORTS THE CURRENT SYSGEN.


     If you type a CONTROL/C, all the information you enter is lost and the
     SYSGEN  does  not  create  output  files.  There is no recovery if you
     accidently type CONTROL/C.


	  FOR FILE STORAGE SPECIFICATIONS SUCH
	  AS DTA0, THE PROGRAM EXPECTS STANDARD DEVICE
	  NAMES.  NOTE THAT YOU DO NOT APPEND A COLON
	  TO THE DEVICE NAME.


     The SYSGEN accepts any string you type that  contains  the  upper-case
     letters  A  through  Z and the numbers 0 through 9.  Consequently, you
     must make sure that the file specification is a character string  that
     OS/8  recognizes.   You  may, of course, use an OS/8 ASSIGN command to
     equate a user file specification with a system file specification.


	  NEXT TO THE BRACKETS [] INDICATING THE
	  EXPECTED RESPONSE ARE PARENTHESES () WHICH
	  INDICATE THE DEFAULT ANSWER.  YOU SELECT THE
	  DEFAULT ANSWER BY JUST TYPING A CARRIAGE RETURN.


     A default answer is a predetermined answer that satisfies the majority
     of  the  users  of RTS/8.  However, it may not be appropriate for your
     particular system.

     See Chapter 4 for information on changing defaults.

     If a question does not have  a  default,  the  parentheses  contain  a
     question mark, that is, (?).




				      2-6

			      THE SYSGEN DIALOGUE


     The following questions ask you to state which computer of  the  PDP/8
     family  you wish to install the RTS/8 system on. If the processor does
     not match the  machine  type,  it  represents  a  special  case.   For
     example,  the  8/A  620 series has an 8/E processor in an 8/A cabinet.
     In such a case, you use the processor designation to specify the clock
     task  and  the  powerfail  task.   Here, the target machine has an 8/A
     clock and 8/E powerfail hardware.  For example, if you do not  have  a
     clock  or  powerfail  hardware,  you may state that you have an 8/A or
     8/E.  If the target machine has a clock, call it an 8/A.   If  it  has
     powerfail  hardware,  call it an 8/E.  If it has both, call it an 8/E;
     when you answer the clock question, specify a non-standard 8/A clock.


     IS THE TARGET MACHINE FOR WHICH YOU ARE
     BUILDING THE RTS/8 SYSTEM A PDP 8/A? [Y/N] (Y):

	  THE TARGET MACHINE IS THE MACHINE FOR
	  WHICH THE RTS/8 SYSTEM IS BEING BUILT.  THE
	  MACHINE RUNNING THIS PROGRAM AND THE TARGET MACHINE
	  DO NOT HAVE TO BE THE SAME.
	  (DOC. NO 042)


     For example, you may build a system for a PDP 8/A that  contains  128K
     of  memory  and many I/O peripherals while running the SYSGEN on a PDP
     12 with 12K of memory whose only peripheral is a LINCtape drive.


     IS THE TARGET MACHINE A PDP 8/E? [Y/N] (N):

	  THE TARGET MACHINE IS THE MACHINE FOR
	  WHICH THE RTS/8 SYSTEM IS BEING BUILT.  THE
	  MACHINE RUNNING THIS PROGRAM AND THE TARGET MACHINE
	  DO NOT HAVE TO BE THE SAME.
	  (DOC. NO 042)

     IS THE TARGET MACHINE A PDP-12? [Y/N] (N):

	  THE TARGET MACHINE IS THE MACHINE FOR
	  WHICH THE RTS/8 SYSTEM IS BEING BUILT.  THE
	  MACHINE RUNNING THIS PROGRAM AND THE TARGET MACHINE
	  DO NOT HAVE TO BE THE SAME.
	  (DOC. NO 042)

     IS THE TARGET MACHINE A VT78 SYSTEM? [Y/N] (N):

	  THE TARGET MACHINE IS THE MACHINE FOR
	  WHICH THE RTS/8 SYSTEM IS BEING BUILT.  THE
	  MACHINE RUNNING THIS PROGRAM AND THE TARGET MACHINE
	  DO NOT HAVE TO BE THE SAME.
	  (DOC. NO 042)




				      2-7

			      THE SYSGEN DIALOGUE


     If your answers were "no" to the questions asking which machine  RTS/8
     will run on, the SYSGEN assumes it is a PDP 8/L, a PDP-8, or a LINC-8.


     THE TARGET MACHINE MUST BE A PDP 8/I,			     remark
     A PDP 8/L, A PDP-8, OR A LINC-8 BECAUSE IT IS		     remark
     NOT ONE OF THE ABOVE.					     remark
     (DOC. NO 046)


     The SYSGEN requires you to specify the actions it  will  perform  upon
     completion  of  this  dialogue.   Depending  upon  your answer, it can
     return to the monitor, chain to OS/8 BATCH to  execute  the  files  it
     creates,  and/or  continue  through  the  BATCH procedure to the RTS/8
     system.

     The SYSGEN also requires you to specify  where  it  is  to  write  its
     output  files,  what  it  should  name  them,  and  other such similar
     information.


     TO WHICH DEVICE SHOULD SYSGEN WRITE THE OUTPUT
     FILES? [A] (SYS):

	  THIS PROGRAM PRODUCES THREE MAJOR OUTPUT
	  FILES:  (1) A PARAMETER FILE, (2) A MACREL BATCH
	  FILE, AND (3) A LINKER BATCH FILE.  OS/8 BATCH
	  MUST KNOW THE DEVICE UPON WHICH THESE FILES
	  RESIDE IN ORDER TO GENERATE AN RTS/8 SYSTEM.
	  (DOC. NO 022)


     The device that you specify must be active in the system that you  are
     using to create the RTS/8 system.  If you specify a device that is not
     in the system, the  SYSGEN  produces  an  error  message  and  returns
     execution  control  to the OS/8 Keyboard Monitor, and all your answers
     are lost.

     The parameter file is a series of statements  that  MACREL  uses  when
     assembling  source  files.   These statements are equates that, if the
     SYSGEN defines them, MACREL  uses  when  assembling  another  program.
     (See Chapter 4 for a discussion of the parameter file.  Also, Appendix
     D is an abbreviated listing of the parameter file.)

     The MACREL batch  file  is  the  list  of  source  files  that  MACREL
     assembles  to  create  the  .RB files that the LINK program uses.  The
     SYSGEN enters the source file name for each task you indicate  in  the
     SYSGEN.   (The task name must be the name of the source file.) It also
     appends switches depending on answers you give to  questions  in  this
     section.

     The LINK batch file contains the file specifications that  LINK  needs
     to create the .SV image of the RTS/8 system.


				      2-8

			      THE SYSGEN DIALOGUE


     The MACREL and LINK batch files must reside on SYS  (or  a  coresident
     device  such as RKB0 or RL0B) when BATCH executes.  If they are not on
     SYS or a coresident device, BATCH cannot execute.  (This  is  an  OS/8
     restriction.)

     The SYSGEN appends switches to the  MACREL  and  LINK  batch  file  in
     response to your answers to questions.

     For further information on MACREL and LINK, see the MACREL/LINK User's							 __________________
     Manual.     ______

     DO YOU WANT TO CHAIN IMMEDIATELY TO THE
     RTS/8 SYSTEM WHICH BATCH CAN PRODUCE? [Y/N] (Y):

	  THIS PROGRAM CAN INSERT A REQUEST TO RUN THE
	  RTS/8 SYSTEM IT PRODUCES WHEN BATCH FINISHES
	  RUNNING.  NOTE THAT INPUT SOURCE FILES MUST BE
	  ON ONE MEDIUM TO PROVIDE FOR THIS FEATURE TO
	  WORK CORRECTLY.
	  (DOC. NO 024)


     If you wish the RTS/8 system to begin running  after  BATCH  generates
     the  RTS/8  system,  answer yes to this question.  When BATCH finishes
     executing, it chains to RTS/8 automatically if the RTS/8 save image is
     on  SYS.   (If  the  save  image  is not on SYS, BATCH still chains to
     RTS/8. However, the save image is not executable.)


     WHAT FIVE CHARACTER NAME WOULD YOU LIKE
     TO CALL THE FILES PRODUCED? [A] (DEFLT):

	  THE RTS/8 SYSGEN PROGRAM NAMES THE OUTPUT FILES.
	  EXAMPLE:  MDEFLT.BI IS THE INPUT SOURCE BATCH
	  FILE FOR THE MACREL ASSEMBLIES; LDEFLT.BI IS
	  THE INPUT SOURCE BATCH FILE FOR THE LINKER;
	  PDEFLT.MA IS THE PARAMETER FILE PRODUCED.
	  (DOC. NO 026)


     The name you select for the output  file  can  be  from  one  to  five
     characters  long.   If  your answer is six characters long, the SYSGEN
     truncates it to five characters.  (If it is more than  six  characters
     long, the SYSGEN prints an error message.)

     The above remark assumes you chose the default  file  name  of  DEFLT.
     However,  if  you  chose  the name MYOWN, the SYSGEN creates the files
     MMYOWN.BI, LMYOWN.BI, and PMYOWN.MA.







				      2-9

			      THE SYSGEN DIALOGUE


     The first character of the three major output files* are always M  for
     MACREL,  L  for  LINK,  and  P  for  parameter.   See  Chapter 4 for a
     discussion of these files.  See also DOC. NO  022  for  a  summary  of
     these files.


     DO YOU WANT THE SYSGEN PROGRAM TO REQUEST
     BATCH TO RUN BEFORE TERMINATING? [Y/N] (Y):

	  THE RTS/8 SYSGEN PROGRAM CAN CHAIN TO BATCH
	  AFTER COMPLETING THIS QUESTION AND ANSWER SESSION.
	  THE PROGRAM BUILDS A BATCH FILE BASED ON
	  THE DEVICE SPECIFICATIONS YOU PROVIDE IN YOUR
	  ANSWERS.  BATCH ALSO RESUBMITS ITSELF IF ALL
	  SOURCE FILES ARE NOT ON THE SAME MEDIUM.
	  BATCH THEN CREATES THE RTS/8 SAVE IMAGE.
	  (DOC. NO 030)


     Answering yes to this question instructs the SYSGEN to chain to BATCH.
     BATCH then executes the MACREL and LINK batch files.

     If all of the source MACREL files for the RTS/8 tasks are not  on  the
     same  medium, which you will indicate in another question (see DOC. NO
     340), the SYSGEN inserts instructions that  allow  you  to  mount  the
     media  when  BATCH  needs  them.   If  the sources are not on the same
     medium, then the MACREL batch file does not automatically chain to the
     LINK  batch  file.  After BATCH causes MACREL to assemble all sources,
     you must interrupt BATCH using a C, then submit the LINK batch file.

     If you also answered yes to a previous question (DOC. NO  024),  RTS/8
     also comes up running after the conclusion of the SYSGEN.


     ON WHICH INPUT DEVICE DO THE SOURCE
     FILES RESIDE? [A] (SYS):

	  FOR EXAMPLE, THE DEVICE COULD BE RXA0 OR DTA0.
	  (NOTE THAT A ':' IS NOT A LEGAL CHARACTER).
	  THE SOURCE FILES MUST RESIDE ON ONE TYPE OF
	  MEDIA AND THE .RB FILES MUST ALL RESIDE ON ONE
	  MEDIUM. IF RTS/8 IS TO RUN AUTOMATICALLY, BATCH
	  MUST WRITE THE .SV FILE ONTO SYS.
	  (DOC. NO 033)


     The source files this question references are the source files for any
     tasks that you include in the system and the source files that DIGITAL
     provides.


     --------------
     *  The SYSGEN may also create control files for the  TTY  drivers  and
     floppy controllers.

				     2-10

			      THE SYSGEN DIALOGUE


     Note that the colon terminating this  question  is  not  part  of  the
     device name;  it is part of the SYSGEN question.

     Although the sources must be on one type of device, they do  not  have
     to  be  on the same physical device.  For example, some of the sources
     could be on one floppy and the remainder on another.  However, you can
     not have some of the sources on one medium such as a floppy and others
     on another medium such as a DECtape.

     If, for example, the source files are on two floppies, you  answer  no
     to  this  question.   When BATCH submits the MACREL batch file, MACREL
     assembles all the source files on the first floppy.  BATCH then prints
     a  message  that  tells  you to insert the next floppy into the drive.
     After you  signal  that  you  have  performed  this  action,  assembly
     continues.   This  process continues until MACREL assembles all source
     files.  You must then type a C to abort  BATCH  because  BATCH  cannot
     determine when MACREL has assembled all of the files.  (BATCH keeps on
     displaying the message to insert the new medium.)  You  then  manually
     submit the LINK batch file.


     ON WHICH DEVICE SHOULD BATCH STORE THE .RB
     FILES? [A] (SYS):

	  FOR EXAMPLE, THE DEVICE COULD BE RXA0 OR DTA0.
	  (NOTE THAT A ': ' IS NOT A LEGAL CHARACTER).
	  THE SOURCE FILES MUST RESIDE ON THE TYPE OF
	  MEDIA AND THE .RB FILES MUST ALL RESIDE ON ONE
	  MEDIUM. IF RTS/8 IS TO RUN AUTOMATICALLY, BATCH
	  MUST WRITE THE .SV FILE ONTO SYS.
	  (DOC. NO 033)


     The SYSGEN uses this remark, DOC. NO 033, for several questions.

     The .RB files are the assembled source files  that  are  ready  to  be
     linked.

     The device referenced in this question must  be  in  the  system  when
     BATCH  executes  the MACREL batch file.  If there is insufficient room
     on the device for storing the  .RB  files,  BATCH  displays  an  error
     message.  If this occurs, you must either delete files from the medium
     or place another device in that drive (if possible) and then  resubmit
     the MACREL batch file.


     ON WHICH OUTPUT DEVICE SHOULD BATCH STORE
     THE .SV FILE? [A] (SYS):

	  FOR EXAMPLE, THE DEVICE COULD BE RXA0 OR DTA0.
	  (NOTE THAT A ': ' IS NOT A LEGAL CHARACTER).
	  THE SOURCE FILES MUST RESIDE ON ONE TYPE OF
	  MEDIA AND THE .RB FILES MUST ALL RESIDE ON ONE
	  MEDIUM. IF RTS/8 IS TO RUN AUTOMATICALLY, BATCH

				     2-11

			      THE SYSGEN DIALOGUE


	  MUST WRITE THE .SV FILE ONTO SYS.
	  (DOC. NO 033)


     You may write the .SV image to any device in the system.  However,  if
     this  device  is  not  SYS,  BATCH cannot chain to an executable RTS/8
     system.  If you wish to write the .SV image to  a  non-system  device,
     you  must copy the RTS/8 save file onto SYS before executing the RTS/8
     image.


     DO YOU WANT ASSEMBLY LISTINGS? [Y/N] (N):

	  YOU MAY ELECT TO OBTAIN ASSEMBLY LISTINGS
	  OF SYSTEM AND USER TASKS AS MACREL ASSEMBLES
	  THEM DURING THE BATCH STREAM.
	  (DOC. NO 334)


     If you wish assembly listings, you receive them for all tasks  in  the
     RTS/8  system.   Obtaining  assembly listings is useful if you will be
     changing the sources.  For the  form,  organization,  and  content  of
     assembly listings, see the MACREL/LINK User's Manual.				_________________________

     TO WHICH OUTPUT DEVICE SHOULD BATCH
     WRITE THE ASSEMBLY LISTINGS? [A] (LPT):

	  FOR EXAMPLE, THE DEVICE COULD BE RXA0 OR DTA0.
	  (NOTE THAT A ':' IS NOT A LEGAL CHARACTER).
	  THE SOURCE FILES MUST RESIDE ON ONE TYPE OF
	  MEDIA AND THE .RB FILES MUST ALL RESIDE ON ONE
	  MEDIUM. IF RTS/8 IS TO RUN AUTOMATICALLY, BATCH
	  MUST WRITE THE .SV FILE ONTO SYS.
	  (DOC. NO 033)


     Normally, the SYSGEN directs MACREL to print the assembly listings  on
     the  line  printer.   You may, however, instruct MACREL to write these
     listings to files on any device.  If MACREL  writes  the  listings  to
     device  files,  you must make sure that the device has sufficient room
     to contain them.

     If the SYSGEN writes the assembly listings to a mass  storage  device,
     the   listings   have   an   .LS   extension   and  the  corresponding
     cross-reference listing extension will be .LT.


     DO YOU WANT LINKER LOAD MAP LISTINGS?
     [Y/N] (N):

	  THE LINKER LOAD MAP DESCRIBES THE MEMORY LAYOUT
	  OF THE RTS/8 SYSTEM.
	  (DOC. NO 341)


				     2-12

			      THE SYSGEN DIALOGUE


     You request a load map if you must know the locations in memory  where
     tasks reside.  See the MACREL/LINK User's Manual for an explanation of			    _________________________
     the form and contents of the load map.


     ON WHICH OUTPUT DEVICE SHOULD BATCH
     WRITE THE MEMORY MAP LISTINGS? [A] (LPT):

	  FOR EXAMPLE, THE DEVICE COULD BE RXA0 OR DTA0.
	  (NOTE THAT A :  IS NOT A LEGAL CHARACTER).
	  THE SOURCE FILES MUST RESIDE ON ONE TYPE OF
	  MEDIA AND THE .RB FILES MUST ALL RESIDE ON ONE
	  MEDIUM. IF RTS/8 IS TO RUN AUTOMATICALLY, BATCH
	  MUST WRITE THE .SV FILE ONTO SYS.
	  (DOC. NO 033)


     Normally, the SYSGEN directs LINK to print the memory maps on the line
     printer.   A  non-default answer tells LINK which device to write this
     file to.

     The following question asks if you want to  build  a  default  system.
     This system is a small RTS/8 system and includes only the tasks listed
     in DOC. NO 017.  A default system does not include user tasks.


     DO YOU WISH TO GENERATE AN RTS/8 SYSTEM WITHOUT
     SPECIFYING PARAMETERS? [Y/N] (N):

	  IF YOU ANSWER YES TO THIS QUESTION, THE
	  RTS/8 SYSGEN PROGRAM GOES TO PASS 2 AND
	  GENERATES A SYSTEM WHICH INCLUDES A TTY TASK,
	  A MONITOR CONSOLE ROUTINE, A TEST ROUTINE,
	  A NULL ROUTINE, A CLOCK ROUTINE, AND AN EXIT
	  TASK.
	  (DOC. NO 017)


     For an explanation of the function and purpose of these tasks, see the
     RTS/8 User's Manual.  However, the Test Routine is explained below.     ___________________

     If you answer yes to this question, the  SYSGEN  immediately  goes  to
     Pass  2.   Pass  2  is  the  part of SYSGEN that builds the Parameter,
     MACREL, and LINK batch files.  (Section 2.3 explains Pass 2 actions.)


     ARE ALL SOURCE FILES ON THE SAME MEDIUM? [Y/N] (Y):

	  IF, FOR EXAMPLE, THE SOURCE FILES EXIST ON
	  SEVERAL FLOPPIES, THEN THE BATCH FILE WILL BE
	  CONSTRUCTED TO RESUBMIT ITSELF.  ON EACH
	  PASS, THE SOURCES FROM ANOTHER
	  FLOPPY CAN BE ASSEMBLED.
	  (DOC. NO 340)

				     2-13

			      THE SYSGEN DIALOGUE


     If all of the sources are not on the same medium,  OS/8  BATCH  pauses
     and  prints  a  message  that  allows you to place the medium into the
     drive unit.  (If they are not on the same medium, the SYSGEN inserts a
     BATCH  /E  switch.   This switch specifies that when BATCH cannot find
     the file on the medium, it should  not  abort.   This  gives  you  the
     opportunity to place the medium with the file into the device drive.)

     Note that you cannot have sources on two different kinds  of  devices,
     for example, DECtape and floppies.

     The SYSGEN now asks you to enter information on  the  target  system's
     hardware.   (The SYSGEN does not ask these and the following questions
     if you select the default system;  see DOC. NO 017.)


     DOES THE TARGET SYSTEM HAVE EAE HARDWARE? [Y/N] (N):

	  EAE HARDWARE IS AN OPTION WHICH MAY BE
	  PRESENT IN THE TARGET CONFIGURATION.  EAE
	  HARDWARE ALLOWS OPERATIONS SUCH AS MULTIPLY AND
	  DIVIDE TO BE PERFORMED IN THE HARDWARE.
	  (DOC. NO 050)


     The EAE (Extended Arithmetic Element) allows the central processor  to
     perform  arithmetic  operations  at high speed.  Most users employ the
     EAE with a 23-bit Floating-Point Processor to provide  fast  floating-
     point  arithmetic, mathematical and trigonometric function evaluation,
     and formatted floating-point I/O.

     Check with the system manager or your sales representative if  you  do
     not know if the system has EAE hardware.


     DO YOU WISH TO SAVE THE CONTENTS OF THE EAE
     REGISTERS WHEN TASK SWITCHING OCCURS? [Y/N] (Y):

	  IF MORE THAN ONE TASK USES THE EAE
	  REGISTERS, YOU SHOULD SAVE ITS CONTENTS
	  TO AVOID LOSING DATA WHEN TASK SWITCHING OCCURS.
	  ASSUME THAT BOTH TASK A AND TASK B
	  USE THE EAE.  IF TASK B STARTS EXECUTING
	  BEFORE TASK A FINISHES, THEN THE CONTENTS OF THE
	  EAE MAY BE DIFFERENT WHEN TASK A RESUMES BECAUSE
	  OF TASK B'S USE OF THE EAE.
	  (DOC. NO 052)


     Although it is usually desirable to  save  the  contents  of  the  EAE
     registers,  you  do  not  have  to  save  them.   Considerably greater
     processor overhead is needed if you save the  registers;   you  should
     save  them  only if the tasks that you add to the system use them.  If
     you save the EAE registers, the RTS/8 Executive includes an additional
     location  for  each  task;   for example, if you save the EAE and your

				     2-14

			      THE SYSGEN DIALOGUE


     system has 30  tasks,  then  the  RTS/8  Executive  contains  30  more
     locations than it would if you did not save the EAE registers.


     DOES THE TARGET SYSTEM HAVE A HARDWARE
     MQ REGISTER? [Y/N] (Y):

	  SOME TARGET SYSTEMS MAY NOT.
	  THE MQ REGISTER IS OPTIONAL ON THE PDP 8/I,
	  8/L, LINC 8, AND THE 8.
	  (DOC. NO 054)


     The MQ (Multiplier Quotient Register) is a 12-bit bidirectional  shift
     register  that acts as an extension of the accumulator during extended
     arithmetic operations.  You may also use this register as a  temporary
     storage location.

     If you indicate that RTS/8 should save the EAE, then it also saves the
     MQ register contents.  However, if you indicate that the target system
     does not contain an EAE or that you do not wish to save the  EAE,  you
     still may wish to save the MQ.


     DO YOU WANT TO SAVE THE CONTENTS OF THE
     MQ REGISTER WHEN TASK SWITCHING OCCURS? [Y/N] (Y):

	  IF MORE THAN ONE TASK USES THE MQ
	  REGISTER, YOU SHOULD SAVE ITS CONTENTS
	  TO AVOID LOSING DATA WHEN TASK SWITCHING OCCURS.
	  ASSUME THAT BOTH TASK A AND TASK B
	  USE THE MQ.  IF TASK B STARTS EXECUTING
	  BEFORE TASK A FINISHES, THEN THE CONTENTS OF THE
	  MQ MAY BE DIFFERENT WHEN TASK A RESUMES
	  BECAUSE OF TASK B'S USE OF THE EAE.
	  (DOC. NO 056)


     You should save the contents of the MQ only if the tasks  you  install
     in  the  RTS/8  system  use  the  MQ.   Saving the MQ requires greater
     processor overhead.


     IN WHICH FIELD DOES RTS8 RESIDE? [D] (0):

	  UNLESS YOU ARE REALLY SURE, RTS8 SHOULD
	  RESIDE IN FIELD 0.
	  (DOC. NO 353)


     The answer to this question must be from 0 to 31 (decimal).




				     2-15

			      THE SYSGEN DIALOGUE


     DIGITAL strongly recommends that you always place RTS/8  in  field  0.
     (You  might  wish  to  place  RTS/8  in  a  different field if you are
     generating a symbiont system.)

     For example, if the target machine contains 16K of memory and you wish
     to  place  RTS/8 in the highest possible memory locations, answer 4 to
     the number of fields and then place RTS/8 in field 3.

     If you place RTS/8 in a field other than 0, then you must control LINK
     to  ensure  that  other RTS/8 tasks do not execute in fields below the
     RTS/8 field.


     HOW MANY FIELDS OF MEMORY EXIST IN THE
     TARGET MACHINE? [D] (4):

	  IF YOU HAVE 16K OF MEMORY, THE ANSWER
	  IS 4.  ENTER THE NUMBER IN DECIMAL.
	  (DOC. NO 060)


     Your answer to this question must be between 2 and 32 (decimal).

     Consider carefully your answer  to  this  question.   If  you  do  not
     specify  sufficient memory, there may not be enough room for the RTS/8
     save image to execute  properly.   Consequently,  unless  you  have  a
     reason  for  limiting  memory,  your answer should specify the maximum
     amount of memory available in the target system.  (The minimum  amount
     of  memory is determined by the amount of storage LINK needs to create
     the system.)

     If you are unsure how much memory the target system  has,  check  with
     the system manager or your sales representative.  If the target system
     has OS/8, you may also determine the number of fields  by  typing  the
     OS/8  Keyboard  Monitor  MEMORY  command.   See  the OS/8 Handbook for								  _____________
     further information.


     DOES YOUR TARGET SYSTEM HAVE POWER FAIL HARDWARE? [Y/N] (N):

	  POWER FAIL HARDWARE IS AN OPTION
	  AVAILABLE ON ALL MACHINES (EXCEPT THE VT-78)
	  WHICH HAVE CORE MEMORY.
	  (DOC. NO 062)


     Power fail hardware causes an interrupt to occur when the power  falls
     below  a  predetermined  threshold.  When power returns, this hardware
     causes the computer to restart.

     The power fail hardware is useful only with machines  that  have  core
     memory (which is non-volatile) If the target machine has semiconductor
     memory, it ordinarily does not possess power fail hardware.


				     2-16

			      THE SYSGEN DIALOGUE


     If you do not know if the system has this hardware,  check  with  your
     system manager or your sales representative.


     DO YOU WANT THE POWER FAIL HANDLER? [Y/N] (N):

	  EACH DEC TASK WILL BE LISTED ONE AT A
	  TIME.  IF YOU WISH TO INCLUDE THE TASK IN YOUR
	  SYSTEM, TYPE Y.  IF NOT, TYPE N.  IF THE
	  SYSGEN PROGRAM REQUIRES MORE INFORMATION
	  ABOUT A TASK, IT WILL ASK THE QUESTIONS
	  IN ANOTHER SECTION.
	  (DOC. NO 073)


     Answer yes to this question if you wish  to  provide  for  an  orderly
     shutdown  of  the  computer  when it loses power.  This task saves the
     contents of all volatile registers.  When sufficient power exists, the
     task  restores  the  contents  of  the  volatile registers and returns
     control to RTS/8.  If you answered no to the question  that  asked  if
     you  have power fail hardware (DOC. NO 062), the SYSGEN does not print
     this question.


		 ----------------- CAUTION ------------------
		 | If  you  erroneously  answer  that   the |
		 | target  system  has  power fail hardware |
		 | and you state that you wish to have  the |
		 | power  fail  task,  then  the  resulting |
		 | RTS/8 system  will  execute  improperly. |
		 | This  is an error that the SYSGEN cannot |
		 | check for because the target machine and |
		 | the   machine   upon   which   you   are |
		 | generating the RTS/8 system may  not  be |
		 | the same.				    |
		 --------------------------------------------

     DOES THE TARGET SYSTEM HAVE KL8-A
     HARDWARE? [Y/N] (N):

	  THE KL8-A IS A 4-CHANNEL ASYNCHRONOUS
	  INTERFACE FOR THE PDP-8 FAMILY.  IT PROVIDES
	  FULL MODEM CONTROL ON 1 CHANNEL AND PARTIAL MODEM
	  CONTROL ON THE OTHER THREE CHANNELS.  IF
	  YOU HAVE ANY KL8-A'S IN YOUR TARGET SYSTEM,
	  ANSWER YES TO THE QUESTION.
	  (DOC. NO 064)

     HOW MANY KL8-A'S ARE IN THE TARGET SYSTEM? [D] (1):

	  THERE ARE 4 CHANNELS PER KL8-A.  IF, FOR
	  EXAMPLE, YOU HAVE 8 CHANNELS THE ANSWER IS 2.
	  (DOC. NO 066)


				     2-17

			      THE SYSGEN DIALOGUE


     Your answer must be between 1 and 3.

     If you do not know if the target system has a KL8-A or you do not know
     how  many  KL8-As  exist  in  the  target  system, consult your system
     manager or your sales representative.


     THIS SECTION PRESENTS THE PARAMETERS			     remark
     REQUIRED TO SPECIFY THE KL8-A TASK WHICH			     remark
     YOU HAVE SELECTED.						     remark
     (DOC. NO 274)						     remark


     If you select the KL8-A, the SYSGEN prints the above remark  after  it
     presents all DIGITAL tasks.


     WHAT IS THE DEVICE CODE FOR THE FIRST KL8-A
     DEVICE? [O] (40):

	  MULTIPLE KL8-A HARDWARE MUST HAVE
	  CONSECUTIVE DEVICE CODES.  THE ANSWER TO THIS
	  QUESTION IS THE DEVICE CODE FOR THE FIRST KL8-A.
	  (DOC. NO 276)


     Your answer must be between 1 and 77 (octal).

     If you do not know the device code, check with the system  manager  or
     your sales representative.


     DO YOU HAVE KT8A HARDWARE IN THE TARGET
     SYSTEM? [Y/N] (N):

	  THE KT8A IS A MEMORY MANAGEMENT OPTION
	  WHICH ALLOWS YOU TO HAVE UP TO 128K OF
	  MEMORY ON SEVERAL MACHINES OF THE PDP-8 FAMILY.
	  (DOC. NO 070)


     If the target machine has more than 32K of  memory,  it  has  a  KT8A.
     (However,  a  machine  with  less  than  32K  may  also  possess  KT8A
     hardware.) You can determine if you have more than 32K  of  memory  by
     using  the  OS/8  Keyboard Monitor MEMORY command (provided the target
     system has OS/8). If you are unsure if the target  system  contains  a
     KT8A, check with your system manager.


     DO YOU WANT ANY OF THE DEC- PROVIDED
     SYSTEM TASKS IN YOUR RTS/8 SYSTEM? [Y/N] (Y):

	  SEVERAL TASKS ARE PROVIDED BY DEC IN
	  SOURCE FORM WHICH YOU CAN INCLUDE IN YOUR

				     2-18

			      THE SYSGEN DIALOGUE


	  RTS/8 SYSTEM (FOR EXAMPLE, THE TTY TASK).
	  (DOC. NO 072)

     If you answer yes  to  the  above  question,  the  SYSGEN  prints  the
     following remark.


     EACH DEC TASK WILL BE LISTED ONE AT A			     remark
     TIME.  IF YOU WISH TO INCLUDE THE TASK IN YOUR		     remark
     SYSTEM, TYPE Y.  IF NOT, TYPE N.  IF THE			     remark
     SYSGEN PROGRAM REQUIRES MORE INFORMATION			     remark
     ABOUT A TASK, IT WILL ASK THE QUESTIONS			     remark
     IN ANOTHER SECTION.					     remark
     (DOC. NO 073)						     remark


     This remark is also the  response  you  receive  when  you  type  a  ?
     response  to  many  of  the  SYSGEN  questions that ask if you wish to
     include a DIGITAL-supplied task.  For more information on any of these
     questions,  see  the  appropriate  hardware manual or the RTS/8 User's							       ____________
     Manual.     ______

     If a task you select requires more than a yes/no response, the  SYSGEN
     asks  these  questions  after  it asks all questions that allow you to
     select DIGITAL tasks.  However, here they  are  grouped  together  for
     your convenience.


     CLOCK HANDLER? [Y/N] (N):

	  EACH DEC TASK WILL BE LISTED ONE AT A
	  TIME.  IF YOU WISH TO INCLUDE THE TASK IN YOUR
	  SYSTEM, TYPE Y.  IF NOT, TYPE N.  IF THE
	  SYSGEN PROGRAM REQUIRES MORE INFORMATION
	  ABOUT A TASK, IT WILL ASK THE QUESTIONS
	  IN ANOTHER SECTION.
	  (DOC. NO 073)


     Answer yes to this question only if the target  system  has  a  clock.
     (If the target system does not have a clock and you answer yes to this
     question, RTS/8  ignores  the  clock  handler  task  that  the  SYSGEN
     installs.) If you are unsure if the target system has a clock, consult
     the system manager or your sales representative.


     THIS SECTION PRESENTS THE PARAMETERS			     remark
     REQUIRED TO SPECIFY THE CLOCK TASK WHICH			     remark
     YOU HAVE SELECTED.						     remark
     (DOC. NO 216)						     remark


     If you state that the target system has a clock, the SYSGEN prints the


				     2-19

			      THE SYSGEN DIALOGUE


     above remark and the following questions after it presents all DIGITAL
     tasks.


     DOES YOUR TARGET SYSTEM HAVE A
     STANDARD CLOCK? [Y/N] (Y):

	  STANDARD CLOCKS:
	  CPU	 CLOCK
	  ---	      -----
	  PDP 8/A     PDP8A
	  PDP 8/E     DK8EA/DK8EC
	  PDP-12      KW12
	  VT-78       PDP8A
	  OTHER       DK8EA/DK8E

	  IF YOUR TARGET SYSTEM HAS A CLOCK OTHER
	  THAN THOSE INDICATED IN THE TABLE,
	  ANSWER 'N' TO THIS QUESTION.
	  (DOC. NO 220)


     If the target system contains the clock that DIGITAL normally provides
     with  your  PDP  8  system,  answer  yes to this question.  If you are
     unsure if you have a standard clock, consult  the  system  manager  or
     your sales representative.

     If the processor does not match the  machine  type,  it  represents  a
     special case.  For example, the 8/A 620 series has an 8/E processor in
     an 8/A cabinet.  For  information  on  answering  this  and  the  next
     question, see the paragraph preceding DOC. NO 42.


     WHAT IS THE DEC DESIGNATION FOR THE NON-
     STANDARD CLOCK? [A] (?):

	  THE NON-STANDARD CLOCKS SUPPORTED ARE THE
	  DK8EP AND ALL THOSE WITH INSTRUCTION SETS
	  COMPATIBLE WITH ONE OF THE ABOVE.
	  (DOC. NO 222)


     If you have a non-standard clock, you must check its  instruction  set
     against those that this handler supports.

     If the clock is incompatible with those listed above, you must provide
     your own clock handler.

     Note that this answer does not have a default.


     HOW MANY ENTRY SLOTS IN THE CLOCK QUEUE
     DO YOU WANT? [D] (16):


				     2-20

			      THE SYSGEN DIALOGUE


	  THE LEGAL RANGE IS 16-256.  EACH SLOT REQUIRES
	  6 MEMORY LOCATIONS.  (DOC. NO 224)


     The clock handler uses 6 locations in memory to store a clock request.
     (The  six  contiguous  locations  are  called an entry slot.) You must
     ensure that the clock queue has sufficient slots to store requests; if
     you specify an insufficient number, your system may malfunction.


     HOW MANY SOFTWARE TICKS PER SECOND? [D] (10):

	  RTS8 ALLOWS THE HARDWARE CLOCK INTERRUPT RATE
	  TO BE SUBDIVIDED SO THAT THE SOFTWARE SEES ONLY
	  EVERY NTH INTERRUPT.  THE SOFTWARE INTERRUPT RATE
	  SHERTZ MUST DIVIDE EVENLY INTO THE HARDWARE RATE
	  HERTZ.  IF NOT, ASSEMBLY ERRORS RESULT.
	  (DOC. NO 347)


     Your answer must be in the range 1 through 192 (decimal).

     To answer this question, you must know the hardware tick  rate.   This
     tick  rate  is usually 50 or 60 times a second.  If, for example, your
     hardware clock can produce an interrupt every 1/60 of a  second,  then
     you  could  answer,  among  other  answers,  1,  6,  12,  20,  and 30.
     Respectively, the RTS/8 software receives interrupts every 1/60, 1/10,
     1/5, 1/3, and 1/2 seconds.


     DO YOU WANT THE SPECIAL CLOCK INTERRUPT LINKAGE? [Y/N] (N):

	  THIS FEATURE, TO BE USED WITH EXTREME CARE,
	  ALLOWS A USER-SUPPLIED SUBROUTINE TO BE CALLED
	  FROM CLOCK INTERRUPT LEVEL.
	  (DOC. NO 351)


     In some cases, a task may require an action to be taken at a  time  as
     soon  as  possible  after  the clock hardware interrupt.  This linkage
     provides this close timing.  (Note that it is normally  sufficient  to
     have  the clock schedule a task to carry out an action rather than use
     this linkage.)

     For more information, see Section 4.4  of  the  RTS/8  User's  Manual.						     _____________________
     DIGITAL  recommends  that you incorporate the linkage into your system
     only if a task  must  respond  immediately  after  a  clock  interrupt
     occurs.


     UNIVERSAL DIGITAL CONTROLLER TASK? [Y/N] (N):

	  EACH DEC TASK WILL BE LISTED ONE AT A
	  TIME.  IF YOU WISH TO INCLUDE THE TASK IN YOUR

				     2-21

			      THE SYSGEN DIALOGUE


	  SYSTEM, TYPE Y.  IF NOT, TYPE N.  IF THE
	  SYSGEN PROGRAM REQUIRES MORE INFORMATION
	  ABOUT A TASK, IT WILL ASK THE QUESTIONS
	  IN ANOTHER SECTION.
	  (DOC. NO 073)


     The UDC/ICS is an analog and  digital  I/O  device  that  permits  the
     computer   to  interrogate  external  devices  in  a  process  control
     environment.  This handler is the means by which a  task  communicates
     with  the  UDC/ICS  functional devices.  See Section 4.15 of the RTS/8								      _____
     User's Manual for a description of this handler.     _____________


     THIS SECTION PRESENTS THOSE PARAMETERS			     remark
     WHICH RTS/8 REQUIRES TO SPECIFY THE UDC			     remark
     TASK WHICH YOU HAVE SELECTED.				     remark
     (DOC. NO 225)						     remark


     If you state that the target system contains a UDC, the SYSGEN  prints
     the above remark after it presents all DIGITAL tasks.


     HOW MANY INTERRUPTS CAN BE STORED AT
     ONE TIME? [O] (12):

	  YOU SET THE NUMBER OF SLOTS RESERVED FOR
	  INTERRUPTS PENDING SERVICE BY THIS QUESTION
	  (DOC. NO 227)


     Your answer must be in the range 1 through 50 (octal).

     This number represents the  maximum  number  of  interrupts  that  the
     handler  can store.  The handler stores interrupts so that it does not
     have to interrupt other processing until it  can  service  the  latest
     interrupt.   If  you do not specify sufficient slots, the RTS/8 system
     may either not receive an interrupt or it may stop executing.


     HOW MANY COUNTER MODULES IN THE TARGET
     SYSTEM'S UDC? [O] (1):

	  ENTER THE NUMBER OF MODULE BOARDS WHICH
	  WILL BE IN THE UDC OF THE TARGET SYSTEM.
	  (DOC. NO 231)


     Your answer must be in the range 1-20 (octal).

     Consult the system manager to determine how many counter modules exist
     in the target system.


				     2-22

			      THE SYSGEN DIALOGUE


     HOW MANY CONTACT MODULES IN THE UDC? [O] (2):

	  ENTER THE NUMBER OF MODULE BOARDS WHICH
	  WILL BE IN THE UDC OF THE TARGET SYSTEM.
	  (DOC. NO 231)


     Your answer must be in the range 1-20 (octal).

     Consult the system manager to determine how many contact modules exist
     in the target system.


     HOW MANY ANALOG INPUT CONVERTER MODULES? [O] (2):

	  ENTER THE NUMBER OF MODULE BOARDS WHICH
	  WILL BE IN THE UDC OF THE TARGET SYSTEM.
	  (DOC. NO 231)


     Your answer must be in the range 1-20 (octal).

     Consult  the  system  manager  to  determine  how  many  analog  input
     converter modules exist in the target system.


     WHAT IS THE ADDRESS OF THE FIRST COUNTER
     MODULE? [O] (?):

	  ENTER THE ADDRESS OF THE FIRST MODULE.
	  THE ADDRESSES MUST BE CONTIGUOUS.
	  (DOC. NO 235)


     Your answer must be  in  the  range  0  through  3777  (octal).   This
     question has no default answer.

     Consult the system manager  to  determine  the  first  counter  module
     address.


     WHAT IS THE ADDRESS OF THE FIRST CONTACT
     INTERRUPT MODULE? [O] (?):

	  ENTER THE ADDRESS OF THE FIRST MODULE.
	  THE ADDRESSES MUST BE CONTIGUOUS.
	  (DOC. NO 235)


     Your answer must be in the range 0 through 3777  (octal).   Note  that
     there is no default answer to this question.

     Consult the system manager  to  determine  the  first  contact  module
     address.

				     2-23

			      THE SYSGEN DIALOGUE


     WHAT IS THE ADDRESS OF THE FIRST A/D
     CONVERTER MODULE? [O] (?):

	  ENTER THE ADDRESS OF THE FIRST MODULE.
	  THE ADDRESSES MUST BE CONTIGUOUS.
	  (DOC. NO 235)


     Your answer must be from 0 to  3777  (octal).   There  is  no  default
     answer to this question.

     Consult the system manager to determine the first  analog  to  digital
     converter address.


     RF08 DISK DRIVER? [Y/N] (N):

	  EACH DEC TASK WILL BE LISTED ONE AT A
	  TIME.  IF YOU WISH TO INCLUDE THE TASK IN YOUR
	  SYSTEM, TYPE Y.  IF NOT, TYPE N.  IF THE
	  SYSGEN PROGRAM REQUIRES MORE INFORMATION
	  ABOUT A TASK, IT WILL ASK THE QUESTIONS
	  IN ANOTHER SECTION.
	  (DOC. NO 073)


     Answer yes to this question only if the  target  system  has  an  RF08
     fixed head disk drive and you wish to perform I/O using that device.

     If you will be supplying your own handler or driver, answer no to this
     question.


     DF32 DISK DRIVER? [Y/N] (N):

	  EACH DEC TASK WILL BE LISTED ONE AT A
	  TIME.  IF YOU WISH TO INCLUDE THE TASK IN YOUR
	  SYSTEM, TYPE Y.  IF NOT, TYPE N.  IF THE
	  SYSGEN PROGRAM REQUIRES MORE INFORMATION
	  ABOUT A TASK, IT WILL ASK THE QUESTIONS
	  IN ANOTHER SECTION.
	  (DOC. NO 073)


     Answer yes to this question if the target system has a DF32 fixed head
     disk drive and you wish to perform I/O operations using the device.


     RK8E DISK DRIVER? [Y/N] (N):

	  EACH DEC TASK WILL BE LISTED ONE AT A
	  TIME.  IF YOU WISH TO INCLUDE THE TASK IN YOUR
	  SYSTEM, TYPE Y.  IF NOT, TYPE N.  IF THE
	  SYSGEN PROGRAM REQUIRES MORE INFORMATION

				     2-24

			      THE SYSGEN DIALOGUE


	  ABOUT A TASK, IT WILL ASK THE QUESTIONS
	  IN ANOTHER SECTION.
	  (DOC. NO 073)


     Answer yes to this question if the target system has an RK8E cartridge
     disk drive and you will use it for I/O.


     RK8 DISK DRIVER? [Y/N] (N):

	  EACH DEC TASK WILL BE LISTED ONE AT A
	  TIME.  IF YOU WISH TO INCLUDE THE TASK IN YOUR
	  SYSTEM, TYPE Y.  IF NOT, TYPE N.  IF THE
	  SYSGEN PROGRAM REQUIRES MORE INFORMATION
	  ABOUT A TASK, IT WILL ASK THE QUESTIONS
	  IN ANOTHER SECTION.
	  (DOC. NO 073)

     Answer yes to this question if the target system has an RK8  cartridge
     disk drive.


     RL01 DISK DRIVER? [Y/N] (N):

	  EACH DEC TASK WILL BE LISTED ONE AT A
	  TIME.  IF YOU WISH TO INCLUDE THE TASK IN YOUR
	  SYSTEM, TYPE Y.  IF NOT, TYPE N.  IF THE
	  SYSGEN PROGRAM REQUIRES MORE INFORMATION
	  ABOUT A TASK, IT WILL ASK THE QUESTIONS
	  IN ANOTHER SECTION.
	  (DOC. NO 073)


     Answer yes to this question if the target  system  has  an  RL01  mass
     storage disk drive.


     DECTAPE DRIVER? [Y/N] (N):

	  EACH DEC TASK WILL BE LISTED ONE AT A
	  TIME.  IF YOU WISH TO INCLUDE THE TASK IN YOUR
	  SYSTEM, TYPE Y.  IF NOT, TYPE N.  IF THE
	  SYSGEN PROGRAM REQUIRES MORE INFORMATION
	  ABOUT A TASK, IT WILL ASK THE QUESTIONS
	  IN ANOTHER SECTION.
	  (DOC. NO 073)


     Answer yes to this question if the  system  contains  a  TC08  DECtape
     drive.  Note that RTS/8 does not support TD8E DECtape drives.




				     2-25

			      THE SYSGEN DIALOGUE


     LINCTAPE DRIVER? [Y/N] (N):

	  EACH DEC TASK WILL BE LISTED ONE AT A
	  TIME.  IF YOU WISH TO INCLUDE THE TASK IN YOUR
	  SYSTEM, TYPE Y.  IF NOT, TYPE N.  IF THE
	  SYSGEN PROGRAM REQUIRES MORE INFORMATION
	  ABOUT A TASK, IT WILL ASK THE QUESTIONS
	  IN ANOTHER SECTION.
	  (DOC. NO 073)


     The SYSGEN asks you this question only  if  you  previously  specified
     that the target machine is a PDP 12.  If you wish to use the LINCtape,
     answer yes to this question.

     The SYSGEN now asks if you want floppy disk controllers and  how  many
     you wish to have.


     FIRST FLOPPY CONTROLLER? [Y/N] (N):

	  EACH DEC TASK WILL BE LISTED ONE AT A
	  TIME.  IF YOU WISH TO INCLUDE THE TASK IN YOUR
	  SYSTEM, TYPE Y.  IF NOT, TYPE N.  IF THE
	  SYSGEN PROGRAM REQUIRES MORE INFORMATION
	  ABOUT A TASK, IT WILL ASK THE QUESTIONS
	  IN ANOTHER SECTION.
	  (DOC. NO 073)

     SECOND FLOPPY CONTROLLER? [Y/N] (N):

	  EACH DEC TASK WILL BE LISTED ONE AT A
	  TIME.  IF YOU WISH TO INCLUDE THE TASK IN YOUR
	  SYSTEM, TYPE Y.  IF NOT, TYPE N.  IF THE
	  SYSGEN PROGRAM REQUIRES MORE INFORMATION
	  ABOUT A TASK, IT WILL ASK THE QUESTIONS
	  IN ANOTHER SECTION.
	  (DOC. NO 073)

     THIRD FLOPPY CONTROLLER? [Y/N] (N):

	  EACH DEC TASK WILL BE LISTED ONE AT A
	  TIME.  IF YOU WISH TO INCLUDE THE TASK IN YOUR
	  SYSTEM, TYPE Y.  IF NOT, TYPE N.  IF THE
	  SYSGEN PROGRAM REQUIRES MORE INFORMATION
	  ABOUT A TASK, IT WILL ASK THE QUESTIONS
	  IN ANOTHER SECTION.
	  (DOC. NO 073)

     FOURTH FLOPPY CONTROLLER? [Y/N] (N):

	  EACH DEC TASK WILL BE LISTED ONE AT A
	  TIME.  IF YOU WISH TO INCLUDE THE TASK IN YOUR
	  SYSTEM, TYPE Y.  IF NOT, TYPE N.  IF THE

				     2-26

			      THE SYSGEN DIALOGUE


	  SYSGEN PROGRAM REQUIRES MORE INFORMATION
	  ABOUT A TASK, IT WILL ASK THE QUESTIONS
	  IN ANOTHER SECTION.
	  (DOC. NO 073)


     Each floppy controller performs I/O upon two floppies;  that  is,  one
     floppy  unit  contains two drives.  Thus, if your system allows you to
     use six floppies simultaneously, you include three floppy  controllers
     in the RTS/8 system.

     Answer yes to these questions if the  target  system  contains  either
     single  or  double  density floppies.  Since the floppy controller can
     distinguish between single and double  density  floppies,  the  SYSGEN
     does not ask which kind the target system contains.

     The SYSGEN allows you to include up to four floppy controllers  in  an
     RTS/8  system.  (The SYSGEN also builds a control file for each floppy
     controller you wish to include in the system.  A  control  file  is  a
     file  that  MACREL combines with a source file.  This allows SYSGEN to
     use a single source file to create more than one task.)

     The SYSGEN asks if you want a second controller only  if  you  respond
     affirmatively  to its question asking if you want a floppy controller.
     Likewise, it asks if you want a third controller only if you said  you
     wanted a second controller, and so on.


     THIS SECTION PRESENTS THE HARDWARE DEVICE			     remark
     CODE SPECIFICATION(S) FOR THE FLOPPY CONTROLLER(S)		     remark
     WHICH YOU HAVE SELECTED.					     remark
     (DOC. NO 335)


     If you state that the target system contains floppy drives, the SYSGEN
     prints the above remark after it finishes asking which tasks it should
     include in the system.


     WHAT IS THE DEVICE NUMBER FOR THE FIRST
     DEVICE CONTROLLER? [O] (75):

	  THE RTS/8 SYSGEN PROGRAM PRODUCES A
	  PARAMETER CONTROL FILE FOR EACH FLOPPY
	  CONTROLLER YOU SPECIFY.  ENTER THE ANSWER IN
	  OCTAL.
	  (DOC. NO 136)

     WHAT IS THE DEVICE NUMBER FOR THE SECOND
     DEVICE CONTROLLER? [O] (70):





				     2-27

			      THE SYSGEN DIALOGUE


	  THE RTS/8 SYSGEN PROGRAM PRODUCES A
	  PARAMETER CONTROL FILE FOR EACH FLOPPY
	  CONTROLLER YOU SPECIFY.  ENTER THE ANSWER IN
	  OCTAL.
	  (DOC. NO 136)

     WHAT IS THE DEVICE NUMBER FOR THE THIRD
     DEVICE CONTROLLER? [O] (71):

	  THE RTS/8 SYSGEN PROGRAM PRODUCES A
	  PARAMETER CONTROL FILE FOR EACH FLOPPY
	  CONTROLLER YOU SPECIFY.  ENTER THE ANSWER IN
	  OCTAL.
	  (DOC. NO 136)

     WHAT IS THE DEVICE NUMBER FOR THE FOURTH
     DEVICE CONTROLLER? [O] (72):

	  THE RTS/8 SYSGEN PROGRAM PRODUCES A
	  PARAMETER CONTROL FILE FOR EACH FLOPPY
	  CONTROLLER YOU SPECIFY.  ENTER THE ANSWER IN
	  OCTAL.
	  (DOC. NO 136)

     Your answers to these questions must be between 1 and 77 (octal).

     If you do not know the device codes  for  the  floppies,  consult  the
     system  manager or your sales representative.  DIGITAL also provides a
     specification sheet that lists the devices codes.  See Appendix B  for
     a sample sheet.


     LINE PRINTER DRIVER? [Y/N] (N):

	  EACH DEC TASK WILL BE LISTED ONE AT A
	  TIME.  IF YOU WISH TO INCLUDE THE TASK IN YOUR
	  SYSTEM, TYPE Y.  IF NOT, TYPE N.  IF THE
	  SYSGEN PROGRAM REQUIRES MORE INFORMATION
	  ABOUT A TASK, IT WILL ASK THE QUESTIONS
	  IN ANOTHER SECTION.
	  (DOC. NO 073)


     Answer yes to this question if you wish to include  the  line  printer
     handler.


     EMERGENCY BREAKTHROUGH TASK? [Y/N] (N):

	  THE EMERGENCY BREAKTHROUGH TASK ALLOWS A TASK
	  TO BREAK THROUGH TO A TTY (SELECTED LATER) FOR URGENT
	  MESSAGES.
	  (DOC. NO 325)


				     2-28

			      THE SYSGEN DIALOGUE


     The emergency breakthrough task interrupts a task  that  controls  the
     terminal  so  that  an  emergency message can be sent to the terminal.
     (Using the standard RTS/8 message format, you can  send  an  emergency
     message  from  one  task to this task;  the emergency task then prints
     the message on the terminal.)  This  procedure  is  necessary  because
     other  tasks  cannot  print messages while another task has control of
     the terminal.  For more information, see Chapter 4 of the RTS/8 User's							       ____________
     Manual.     ______


     WHAT IS THE TASK NAME OF THE DEVICE HANDLER TO BE
     USED FOR EMERGENCY BREAKTHROUGH MESSAGES? [A] (TTY):

	  YOU HAVE SELECTED THE EMERGENCY BREAKTHROUGH TASK.
	  SELECT WHICH TTY TASK IS TO BE PRE-EMPTED FOR
	  EMERGENCY MESSAGES.
	  (DOC. NO 331)


     If you select the emergency breakthrough task,  state  which  terminal
     receives emergency messages.

     If you select the default answer, you must answer YES to the following
     question.


     TERMINAL DRIVER? [Y/N] (Y):

	  EACH DEC TASK WILL BE LISTED ONE AT A
	  TIME.  IF YOU WISH TO INCLUDE THE TASK IN YOUR
	  SYSTEM, TYPE Y.  IF NOT, TYPE N.  IF THE
	  SYSGEN PROGRAM REQUIRES MORE INFORMATION
	  ABOUT A TASK, IT WILL ASK THE QUESTIONS
	  IN ANOTHER SECTION.
	  (DOC. NO 073)


     Answer yes to this question if your target system includes  terminals.
     If  the  target  system  uses the MCR task or the OS/8 background task
     (and they both share the same terminal), you must include  this  task.
     You  may, of course, provide your own TTY handler provided you name it
     TTY.MA.


     HOW MANY TTY TASKS WILL BE IN THE
     TARGET SYSTEM? [D] (1):

	  THE RTS/8 SYSGEN PROCEDURE AUTOMATICALLY
	  GENERATES UP TO FIVE TTY TASKS FOR YOUR
	  RTS/8 TARGET SYSTEM; 1 FOR EACH OF UP
	  TO FIVE TTY PERIPHERALS.  A CONTROL FILE WILL
	  BE BUILT FOR ANY IN EXCESS OF 1 TTY TASK,
	  NOT EXCEEDING A TOTAL OF FIVE.
	  (DOC. NO 317)

				     2-29

			      THE SYSGEN DIALOGUE


     The SYSGEN program allows you to include up to five TTY tasks  in  the
     target system.  If your system requires more than five, see Chapter 4.

     For each TTY task other than the first, the SYSGEN creates  a  control
     file  that contains equates necessary to generate the TTY .RB image or
     images.  (A control file is a file that MACREL combines with a  source
     file.   This  allows SYSGEN to use a single source file to create more
     than one task.) The last line of each control file is an .INCLUDE that
     tells  MACREL  to  use the principal TTY task with the equates for the
     specific TTY task you generate.

     The following TTY questions differ from other SYSGEN questions in that
     the answer you type must be five or fewer characters.


     IN THE FOLLOWING QUESTIONS, YOU CAN ENTER			     remark
     UP TO FIVE ANSWERS, SEPARATED BY COMMAS.			     remark
     THE ANSWERS INDICATE YOUR CHOICE FOR THE GIVEN		     remark
     PARAMETER FOR EACH OF THE TTY TASKS THAT YOU HAVE		     remark
     SELECTED.  EXAMPLE:					     remark
     IF YOU TYPE TO THE DEVICE CODE QUESTION:			     remark
     04,31,33,35,37 (CARRIAGE RETURN) YOU SELECT		     remark
     DEVICE CODE CODE 04 FOR TTY TASK, 31 FOR TTY1		     remark
     ETC.							     remark
     (DOC. NO 252)						     remark


     For the next eight questions, you  must  specify  either  the  default
     answer  or  you  must specify the answer for each TTY task.  (When you
     are running the SYSGEN, it prints a message that tells you that  there
     are  no  more  questions  that  require more than one answer.) If, for
     example, the target system contains five TTY tasks, you must supply an
     answer for each.  You cannot type two answers and then have the SYSGEN
     supply the default answer for the remaining three.


     WHAT IS THE KEYBOARD DEVICE CODE FOR THE
     TTY TASK? [O] (03):

	  THE DEVICE CODE FOR THE TTY TASK HAS A
	  DEFAULT OF 4 BUT YOU MAY CHANGE IT TO
	  MATCH THE TARGET SYSTEM'S HARDWARE CONFIGURATION.
	  THE KEYBOARD DEFAULT IS (03).
	  (DOC. NO 254)


     The keyboard device code specifies the part of the terminal from which
     the  computer  receives  information.   If  you do not know the device
     code, check with your system manager  or  your  sales  representative.
     The  default  shown  for  this  question is valid if the target system
     contains only one TTY and it is correct for your system.

     If your terminal is connected to a KL8-A, the device code is 100  plus


				     2-30

			      THE SYSGEN DIALOGUE


     the  line  number for the keyboard (KB) and the teleprinter (TT).  For
     additional information, see DOC. NO 174.


     WHAT IS THE TTY DEVICE CODE FOR THE
     TTY TASK? [O] (04):

	  THE DEVICE CODE FOR THE TTY TASK HAS A
	  DEFAULT OF 4 BUT YOU MAY CHANGE IT TO
	  MATCH THE TARGET SYSTEM'S HARDWARE CONFIGURATION.
	  THE KEYBOARD DEFAULT IS (03).
	  (DOC. NO 254)


     This device code specification is the code the computer uses to signal
     the  terminal  that  it is to receive information.  If you do not know
     the device  code,  check  with  your  system  manager  or  your  sales
     representative.   The default for this question is valid if the target
     system contains one TTY and  the  device  code  is  correct  for  your
     system.


     DO YOU WANT CNTRL/S AND CNTRL/Q FEATURES
     FOR YOUR TTY TASK? [Y/N] (Y):

	  WHEN YOU SET THIS PARAMETER, CNTRL/S STOPS
	  TTY PRINTOUT AND CNTRL/Q RESUMES THE PRINTOUT.
	  (DOC. NO 257)

     DO YOU WANT RUBOUT SUPPORT FOR THE TTY
     SCREEN? [Y/N] (Y):

	  IF YOU SET THIS PARAMETER, TYPING RUBOUT
	  CAUSES THE CURSOR TO MOVE LEFT 1 POSITION AND
	  REMOVE THE LAST CHARACTER YOU TYPE FROM SCREEN.
	  (DOC. NO 261)


     You normally include these features if you have a CRT.  However, it is
     not  necessary for you to include these features.  (On many terminals,
     the RUBOUT key is labeled DELETE.)


     HOW MANY NULLS AFTER A LINE FEED FOR THE TTY
     DEVICE? [O] (0):

	  NULLS ALLOW A LINE FEED TO TAKE PLACE
	  BEFORE THE NEXT CHARACTER IS TRANSMITTED.
	  (DOC. NO 263)


     Some terminals require the transmission of null  characters  in  order
     that  the TTY device can complete the carriage return/line feed action
     before it prints another character.

				     2-31

			      THE SYSGEN DIALOGUE


     HOW MANY CHARACTERS DO YOU WANT ON A LINE
     FOR THE TTY DEVICE? [D] (80):

	  THIS QUESTION ASKS HOW MANY CHARACTERS FIT
	  ON A LINE.  0 MEANS THAT NO POSITION COMPUTATIONS
	  ARE DONE AT ALL.  NOTE THAT THE WIDTH MUST BE A
	  MULTIPLE OF 8.
	  (DOC. NO 265)


     The maximum on most CRT screens is 80.  The maximum on most  hard-copy
     terminals  is 128.  (A 132-character line requires that you answer 128
     to this question, because 128 is the largest number that is  divisible
     by 8.) If your answer is not a multiple of 8, the teletype handler may
     execute improperly.


     DOES THE HARDWARE SUPPORT TABS ON THE
     TTY DEVICE? [Y/N] (Y):

	  IF YOU ANSWER NO, THE SOFTWARE
	  SIMULATES TABS BY INSERTING SPACES.
	  (DOC. NO 273)


     If you are unsure if a terminal supports  hardware  tabs,  check  with
     your system manager.


     HOW MANY SECONDS BEFORE A TTY READ TIMEOUT? [D] (0):

	  A ZERO ANSWER MEANS NO TIMEOUT EXISTS.
	  TIMEOUT MEANS THAT IF THE TASK HAS A PENDING
	  REQUEST AND YOU DO NOT TYPE A RESPONSE WITHIN THE
	  TIMEOUT PERIOD, THE TTY HANDLER ABORTS THE
	  CURRENT REQUEST.
	  (DOC. NO 267)


     The TTY read timeout function tells RTS/8 to abort a read  request  if
     the  receiving  task  does  not receive a prompt reply.  This function
     allows the  terminal  to  be  freed  without  resorting  to  emergency
     messages.


     SWAPPER TASK? [Y/N] (N):

	  THE SWAPPER TASK SWAPS NONRESIDENT TASKS
	  INTO AND OUT OF MEMORY.  YOU MUST INCLUDE THIS
	  TASK IF THE RTS/8 SYSTEM WILL HAVE ANY NON-
	  RESIDENT TASKS.
	  (DOC. NO 342)



				     2-32

			      THE SYSGEN DIALOGUE


     Answer yes  to  this  question  if  the  target  system  will  contain
     nonresident  tasks.   If  you answer 'no' to this question, the SYSGEN
     does not ask any questions about nonresident tasks  or  allow  you  to
     change partitions at a later time.

     You may wish to include the swapper  even  if  no  task  is  initially
     non-resident.   Specifically, if you are debugging a nonresident task,
     DIGITAL recommends that  you  debug  it  when  it  is  resident.   For
     additional information, see Chapter 6 of the RTS/8 User's Manual.						  ___________________


     THIS SECTION PRESENTS THOSE PARAMETERS			     remark
     REQUIRED TO SPECIFY THE SWAPPER TASK WHICH			     remark
     YOU HAVE SELECTED.						     remark
     (DOC. NO 240)						     remark


     If you stated that the target system contains the  swapper  task,  the
     SYSGEN prints this remark after it presents all DIGITAL tasks.


     WHICH RTS/8 DEVICE TASK WILL THE SWAPPER TASK
     USE TO MAKE TRANSFERS? [A] (RK8E):

	  SWAPPING MUST OCCUR FROM THE DEVICE THAT WAS
	  SYS WHEN THE RTS/8 SYSTEM WAS ORIGINALLY RUN FROM OS/8.
	  TYPE THE RTS/8 DEVICE HANDLER FOR THAT DEVICE.
	  (DOC. NO 246)


     This question asks you to type the name of the device  that  the  SWAP
     task uses when it reads and writes task object code.  This device must
     be the OS/8 system from which RTS/8 was run.


     WHICH PHYSICAL UNIT WILL THE SWAPPER USE
     FOR MAKING TRANSFERS? [A] (0):

	  TYPE THE DEVICE NUMBER OF THE DEVICE
	  CORRESPONDING TO SYS. TYPE 0 FOR RKA0.
	  (DOC. NO 250)


     As some mass storage devices have more than one physical  device,  you
     must  also specify which unit of the device swapper makes transfers to
     or from.  Typically, this is unit 0;  however it can be other units.


     CASSETTE DRIVER? [Y/N] (N):

	  EACH DEC TASK WILL BE LISTED ONE AT A
	  TIME.  IF YOU WISH TO INCLUDE THE TASK IN YOUR
	  SYSTEM, TYPE Y.  IF NOT, TYPE N.  IF THE
	  SYSGEN PROGRAM REQUIRES MORE INFORMATION

				     2-33

			      THE SYSGEN DIALOGUE


	  ABOUT A TASK, IT WILL ASK THE QUESTIONS
	  IN ANOTHER SECTION.
	  (DOC. NO 073)


     Answer yes to this question if the target system  performs  I/O  on  a
     tape cassette.


     DO YOU WANT THE CASSETTE FILE SUPPORT
     TASK? [Y/N] (N):

	  EACH DEC TASK WILL BE LISTED ONE AT A
	  TIME.  IF YOU WISH TO INCLUDE THE TASK IN YOUR
	  SYSTEM, TYPE Y.  IF NOT, TYPE N.  IF THE
	  SYSGEN PROGRAM REQUIRES MORE INFORMATION
	  ABOUT A TASK, IT WILL ASK THE QUESTIONS
	  IN ANOTHER SECTION.
	  (DOC. NO 073)


     This task performs auxiliary operations such as rewind,  backspace  to
     file gap, write file gap, backspace to a block gap, and skip a file on
     a CAPS-8 formatted cassette.


     OS/8 FILE SUPPORT TASK? [Y/N] (N):

	  THE OS/8 FILE SUPPORT TASK ALLOWS OTHER
	  TASKS TO LOOKUP, CREATE, AND DELETE FILES IN
	  OS/8 DIRECTORIES.  A SYSTEM MAY HAVE THIS TASK
	  WITHOUT HAVING OS/8 IN THE SYSTEM.
	  (DOC. NO 153)


     The file support task allows foreground jobs to  manipulate  files  on
     file-structured media.


     MONITOR CONSOLE ROUTINE? [Y/N] (Y):

	  EACH DEC TASK WILL BE LISTED ONE AT A
	  TIME.  IF YOU WISH TO INCLUDE THE TASK IN YOUR
	  SYSTEM, TYPE Y.  IF NOT, TYPE N.  IF THE
	  SYSGEN PROGRAM REQUIRES MORE INFORMATION
	  ABOUT A TASK, IT WILL ASK THE QUESTIONS
	  IN ANOTHER SECTION.
	  (DOC. NO 073)


     The MCR accepts a series of interactive commands  that  allow  you  to
     control,  inspect,  and,  to  some extent, debug the RTS/8 system.  It
     also allows you to schedule and execute tasks at specified  intervals,
     suspend task execution, and print system status information.

				     2-34

			      THE SYSGEN DIALOGUE


     THIS SECTION PRESENTS THE PARAMETERS			     remark
     REQUIRED TO SPECIFY THE MCR TASK				     remark
     WHICH YOU HAVE SELECTED.					     remark
     (DOC. NO 205)						     remark


     The SYSGEN prints this remark and the following questions if you  have
     indicated  that  the  target  system  contains an MCR.  For additional
     information, see Chapter 5 of the RTS/8 User's Manual.				       ___________________


     DO YOU WANT TIME-OF-DAY FACILITY IN
     YOUR MCR TASK? [Y/N] (Y):

	  THE MCR TIME COMMAND ALLOWS MCR
	  TO PRINT OR CHANGE THE TIME-OF-DAY.
	  DOC. NO 207)


     The SYSGEN prints this question  if  you  specified  that  the  target
     system contains a clock.  If you include this facility, you may either
     change or display the system time of day.


     DO YOU WANT THE MCR SYSTEM STATUS
     REPORT CAPABILITY? [Y/N] (Y):

	  THE SYSTAT COMMAND OF THE MCR TASK
	  PRINTS THE STATUS OF A SINGLE TASK OR OF THE
	  ENTIRE SYSTEM.  INDICATED ARE FLAGS/MESSAGES, RUN
	  STATUS, AND SOME CURRENT REGISTER CONTENTS.
	  (DOC. NO 211)


     See Section 5.3.13 of the RTS/8 User's Manual for a description of the					       ___________________
     SYSTAT facility.


     WHICH TERMINAL WILL THE MCR TASK
     USE? [A] (TTY):

	  ENTER THE TASK NAME OF THE TASK WHICH
	  RTS/8 WILL USE AS THE MCR CONSOLE DEVICE.
	  (DOC. NO 215)


     If you specify the default answer, you must include at least  one  TTY
     task in the system (see DOC. NO 317).  If you do not, the RTS/8 system
     you are creating will execute improperly.  (You may  also  select  the
     default answer if you include your own TTY task provided that you name
     this task TTY.MA.)




				     2-35

			      THE SYSGEN DIALOGUE


     RTS/8 TEST TASK? [Y/N] (N):

	  EACH DEC TASK WILL BE LISTED ONE AT A
	  TIME.  IF YOU WISH TO INCLUDE THE TASK IN YOUR
	  SYSTEM, TYPE Y.  IF NOT, TYPE N.  IF THE
	  SYSGEN PROGRAM REQUIRES MORE INFORMATION
	  ABOUT A TASK, IT WILL ASK THE QUESTIONS
	  IN ANOTHER SECTION.
	  (DOC. NO 073)


     The Test Task is a demonstration program that prints a string on  your
     terminal.   As DIGITAL distributes it, the task is in a run state when
     the RTS/8 system begins executing.   If  the  target  system  has  the
     Monitor  Console Routine, it releases control of the terminal, and the
     test task sends a message that it wishes to print  a   string  on  the
     terminal.  This string consists of the characters you type in response
     to the Test Task prompt.  After you type the  string,  the  Test  Task
     prints it.

     If you type an ESCAPE to terminate the string, the Test Task  suspends
     itself.  You may reactivate the Test Task by requesting it to run from
     the MCR.

     The MACREL source code for the test task shows the use  of  the  .TASK
     and .NONRES macros.  Thus, you can make the Test Task nonresident.


     EXIT TASK? [Y/N] (N):

	  EACH DEC TASK WILL BE LISTED ONE AT A
	  TIME.  IF YOU WISH TO INCLUDE THE TASK IN YOUR
	  SYSTEM, TYPE Y.  IF NOT, TYPE N.  IF THE
	  SYSGEN PROGRAM REQUIRES MORE INFORMATION
	  ABOUT A TASK, IT WILL ASK THE QUESTIONS
	  IN ANOTHER SECTION.
	  (DOC. NO 073)


     You include this task so that the target system  can  perform  special
     processing  before  the  RTS/8  system  returns  control  to  the OS/8
     Monitor. See Section 4.6 of the RTS/8 User's Manual.				     ___________________


     OS/8 SUPPORT TASK? [Y/N] (N):

	  EACH DEC TASK WILL BE LISTED ONE AT A
	  TIME.  IF YOU WISH TO INCLUDE THE TASK IN YOUR
	  SYSTEM, TYPE Y.  IF NOT, TYPE N.  IF THE
	  SYSGEN PROGRAM REQUIRES MORE INFORMATION
	  ABOUT A TASK, IT WILL ASK THE QUESTIONS
	  IN ANOTHER SECTION.
	  (DOC. NO 073)


				     2-36

			      THE SYSGEN DIALOGUE


     This task allows the RTS/8 system to support the execution of an  OS/8
     operating system in the background of a foreground/background system.


     OS/8 SHARED BACKGROUND TERMINAL SUPPORT TASK? [Y/N] (Y):

	  THE OS/8 BACKGROUND TERMINAL SUPPORT TASK
	  ALLOWS A TERMINAL TO BE SHARED BY FOREGROUND
	  TASKS AND AN OS/8 BACKGROUND.
	  (DOC. NO 323)


     Answer yes to this question if the OS/8 terminal  background  terminal
     is the same as the RTS/8 foreground.


     THIS SECTION PRESENTS THE QUESTIONS			     remark
     WHICH REQUIRE MULTIPLE PARAMETERS TO SPECIFY		     remark
     THE OS/8 BACKGROUND TASK WHICH YOU HAVE SELECTED.		     remark
     (DOC. NO 166)						     remark


     If you selected the OS/8 task, the SYSGEN prints the above remark.


     HOW MANY FIELDS DO YOU WISH TO ALLOCATE
     FOR THE OS/8 BACKGROUND? [D] (2):

	  OS/8 REQUIRES A MINIMUM OF 2 FIELDS (8K).
	  IF YOU WISH TO USE BATCH, YOU NEED A
	  MINIMUM OF 3 FIELDS (12K).
	  (DOC. NO 170)


     OS/8 requires a minimum of two memory fields to operate.  If you  will
     use  the  OS/8  BATCH  utility  when RTS/8 is running, OS/8 requires a
     minimum of three fields.  You may, however, specify up to 8 fields  of
     memory if the target system has a KT8A.


     WHAT IS THE OS/8 KEYBOARD DEVICE
     CODE? [O] (03):

	  TYPE THE DEVICE CODE FOR THE KEY-
	  BOARD DEVICE YOU HAVE SELECTED FOR THE
	  OS/8 TASK.
	  (DOC. NO 174)


     Your answer must be between 1 and 113.

     The keyboard device code is the code for the terminal keyboard  (which
     is  different  than  the  teleprinter described in the next question).
     See also DOC. NO 254.

				     2-37

			      THE SYSGEN DIALOGUE


     SYSGEN uses device codes in the range 100 to 113 to indicate that  the
     terminal  is  attached  to  a  KL8-A.   Note  that  the  keyboard  and
     teleprinter codes are the same for a KL8-A  terminal.   Thus,  100-103
     are  the  four lines on the first KL8-A;  104-107 for the second;  and
     110-113 for the third.


     WHAT IS THE OS/8 TELEPRINTER DEVICE
     CODE? [O] (04):

	  TYPE THE DEVICE CODE FOR THE
	  TERMINAL YOU HAVE SELECTED FOR THE OS/8 TASK.
	  (DOC. NO 172)


     Your answer must be in the range 1 through 113.

     The teleprinter device code is the code  for  the  logical  unit  that
     prints  information  from  the  PDP/8.   If you do not know the device
     code,  check  with  the  system  manager   or   your   DIGITAL   sales
     representative.


     WHAT IS THE RTS/8 HANDLER TASK FOR OS/8? [A] (RK8E):

	  YOU SPECIFY THE SYSTEM DEVICE FOR THE OS/8
	  TASK HERE.  TO ANSWER THIS QUESTION, TYPE THE SYSTEM
	  DRIVER TASK (UP TO 6 CHARACTERS).  THIS DEVICE
	  MUST BE 'SYS' AT THE TIME YOU RUN THE TARGET
	  SYSTEM.
	  (DOC. NO 176)


     This question asks you  to  enter  the  device  name  upon  which  SYS
     resides.  This device is also that which the swap task uses.


     DO YOU WANT THE OS/8 BACKGROUND TASK TO RUN IN
     THE HIGHEST AVAILABLE FIELDS? [Y/N] (Y):

	  THE OS/8 SUPPORT TASK RUNS THE OS/8 BACKGROUND
	  IN CONTIGUOUS FIELDS (TYPICALLY THE HIGHEST FIELDS
	  OF THE TARGET MACHINE). THE KT8A ALLOWS THE OS/8
	  BACKGROUND FIELDS TO BE LOCATED IN CONTIGUOUS FIELDS
	  OTHER THAN THE HIGHEST FIELDS. ENTER THE DECIMAL
	  NUMBER OF THE LOWEST FIELD IN WHICH OS/8 WILL RUN.
	  FIELD 0 IS RESERVED FOR RTS/8.
	  (DOC. NO 202)


     If the target system possesses KT8A memory  management  hardware,  the
     OS/8 support task can reside wherever it is most convenient for you to
     place it.  (If you do not have the KT8A, the SYSGEN does not ask  this


				     2-38

			      THE SYSGEN DIALOGUE


     question.  Instead, it automatically places OS/8 in the highest memory
     fields.)

     You must make sure that OS/8 does not reside in the same  field  where
     RTS/8  resides  (see  DOC. NO 353).  Normally you would place RTS/8 in
     field 0 and OS/8 in the upper memory  fields.   If  you  inadvertently
     place the two in the same field of memory, RTS/8 does not assemble.


     WHAT IS THE LOWEST FIELD WHICH RTS/8 WILL
     USE FOR THE OS/8 TASK? [D] (?):

	  THE OS/8 SUPPORT TASK RUNS THE OS/8 BACKGROUND
	  IN CONTIGUOUS FIELDS (TYPICALLY THE HIGHEST FIELDS
	  OF THE TARGET MACHINE). THE KT8A ALLOWS THE OS/8
	  BACKGROUND FIELDS TO BE LOCATED IN CONTIGUOUS FIELDS
	  OTHER THAN THE HIGHEST FIELDS.  ENTER THE DECIMAL
	  NUMBER OF THE LOWEST FIELD IN WHICH OS/8 WILL RUN.
	  FIELD 0 IS RESERVED FOR RTS/8.
	  (DOC. NO 202)


     Your answer must be in the range 1 through 30 (decimal).

     Only if you answer no to the previous question does the  SYSGEN  print
     this  question.   If you do not wish OS/8 to run in the highest fields
     of memory, enter the lowest field in which it will run.  (See also the
     comment for DOC. NO 202 above.)


     HOW MANY NULL CHARACTERS ARE REQUIRED
     AFTER A LINE FEED UNDER OS/8? [D] (0):

	  TO ALLOW AN I/O DEVICE TIME TO COMPLETE
	  A LINE FEED BEFORE TRANSMITTING THE NEXT
	  CHARACTER, ZERO CHARACTERS (NULLS) ARE
	  PADDED INTO THE TRANSMISSION FOLLOWING THE
	  LINE FEED CHARACTER.  YOU MUST DETERMINE
	  FROM THE CONFIGURATION OF THE TARGET SYSTEM
	  HOW MANY ARE REQUIRED.  (EXAMPLE: A 2400
	  BAUD VT-50 REQUIRES 4).
	  (DOC. NO 204)


     Your answer must be in the range 0 through 10 (decimal).

     Some terminals require null characters as fill  to  allow  a  carriage
     return/line feed to complete its mechanical motion before transmitting
     additional characters.  If you  are  unsure,  check  with  the  system
     manager or your sales representative.

     If  you  have  a  KL8-JA  interface,  it  automatically  provides  pad
     characters.


				     2-39

			      THE SYSGEN DIALOGUE


     WHAT IS THE TASK NAME FOR THE OS/8 BACKGROUND
     TERMINAL SUPPORT TASK? [A] (TTY):

	  TYPE THE TASK NAME OF THE TERMINAL HANDLER
	  WHICH THE FOREGROUND WILL SHARE WITH THE OS/8
	  SUPPORT TASK.
	  (DOC. NO 327)


     If you select the default to  this  question,  you  must  have  stated
     previously  that  the target system has at least one TTY task.  If you
     do not include a TTY task, the RTS/8 system you create cannot  execute
     correctly unless you include an alternate task.


     NULL JOB? [Y/N] (N):

	  EACH DEC TASK WILL BE LISTED ONE AT A
	  TIME.  IF YOU WISH TO INCLUDE THE TASK IN YOUR
	  SYSTEM, TYPE Y.  IF NOT, TYPE N.  IF THE
	  SYSGEN PROGRAM REQUIRES MORE INFORMATION
	  ABOUT A TASK, IT WILL ASK THE QUESTIONS
	  IN ANOTHER SECTION.
	  (DOC. NO 073)


     SYSGEN prints this question only if you have a PDP 8/A.  The  function
     of  this  task is to display a sequential series of numbers on the LED
     accumulator.  If you answer no to this question or if you do not  have
     a  PDP  8/A,  the  Executive  uses a null task that is part of the MCR
     task.

     If your system does not have an MCR, the RTS/8 Executive uses a  small
     null routine included within its code.


     DO YOU WANT TO INCLUDE ANY USER TASKS
     IN THIS RTS/8 SYSTEM? [Y/N] (N):

	  YOU MAY SPECIFY USER TASKS DURING THIS
	  PORTION OF THE QUESTION AND ANSWER PROGRAM.
	  ANSWER YES IF YOU HAVE ANY TASKS TO INCLUDE
	  OTHER THAN THE SYSTEM TASKS SELECTED ABOVE.
	  (DOC. NO 300)


     A user task is a task that you write which is to be part of the  RTS/8
     system.   If  you  answer  yes to this question, the SYSGEN prints the
     following remark.






				     2-40

			      THE SYSGEN DIALOGUE


     ENTER THE NAMES OF YOUR TASKS FOLLOWED BY			     remark
     A CARRIAGE RETURN.  EXAMPLE:				     remark
								     remark
     TASK 1:  NAME-1,M						     remark
     TASK 2:  NAME-2,M						     remark
		 .						     remark
		 .						     remark
		 .						     remark
     TASK N:  NAME-N,M						     remark
								     remark
     M IS THE PARTITION WHERE THE TASK WILL RESIDE		     remark
     (ENTER ZERO OR NO ENTRY FOR THE MAIN LEVEL).		     remark
     YOU SHOULD ENTER THE TASK IN THE ORDER OF			     remark
     DECREASING PRIORITY (THE FIRST ENTERED HAS THE HIGH-	     remark
     EST PRIORITY).  TERMINATE ENTRY BY TYPING A CARRIAGE	     remark
     RETURN (ONLY).						     remark
     (DOC. NO 301)						     remark

     TASK 001 ?:


     An RTS/8 system may contain up to 127 tasks.  However, the  number  of
     tasks that you may include at this point is dependent on the number of
     DIGITAL tasks you specify;  that is, the total number of tasks is 127,
     not the number of user tasks.

     The task name must be the name of the source file;  for example,  task
     MYOWN must have the source file MYOWN.MA.

     You should enter the tasks in order of decreasing priority.   You  may
     not enter an extension to any user task as the task name that you type
     must have an .MA extension.  (Note that the period you type before  an
     extension  is  an  illegal  character  in  the  SYSGEN.) If you make a
     mistake in assigning priorities (or partitions), the SYSGEN gives  you
     an  opportunity  to  make  corrections in the following two questions.
     However, if you enter a task name incorrectly, you  must  repeat  this
     question  beginning  at  task  1.  You repeat the question by typing a
     carriage return to leave the question, then type a # followed  by  the
     question number of this question.

     If you attempt to enter more than 127  tasks,  the  SYSGEN  prints  an
     error  message  and then prints the following question.  This question
     is also the next question when you type a carriage return in  response
     to the TASK prompt.


     DO YOU WANT TO CHANGE ANY OF THE TASK'S
     PRIORITIES? [Y/N] (N):

	  YOU MAY CHANGE THE PRIORITY OF ANY OF THE
	  TASKS HERE.  DIGITAL RECOMMENDS THAT YOU LEAVE
	  THE PRIORITY OF THE SYSTEM TASKS AS IS.  FOR
	  YOUR CONVENIENCE, THE NAMES OF SYSTEM AND


				     2-41

			      THE SYSGEN DIALOGUE


	  USER TASKS WHICH YOU HAVE SPECIFIED CAN BE
	  LISTED HERE.
	  (DOC. NO 307)


     If you answer YES to this question, the SYSGEN  prints  the  following
     instructions.


     THE WAY IN WHICH YOU CHANGE DEVICE PRIORITIES		     remark
     IS TO NAME THAT TASK WHICH WILL BE HIGHER IN		     remark
     PRIORITY THAN THE NEXT NAMED TASK, TAKEN A PAIR AT A	     remark
     TIME, AND DELIMITED BY A COMMA.				     remark
								     remark
     EXAMPLE:							     remark
								     remark
     PRIORITY CHANGE:  TASK-3, TASK-1				     remark
     PLACES TASK-3 HIGHER IN PRIORITY THAN			     remark
     TASK-1.  THE TASK ORDER WILL NOW BE TASK-3,		     remark
     TASK-1, TASK-2.  WHEN YOU FINISH CHANGING			     remark
     PRIORITIES, A CARRIAGE RETURN (ONLY) TERMINATES THE ENTRY.      remark
								     remark
     TYPE ? AND A CARRIAGE RETURN TO OBTAIN A LIST-		     remark
     ING OF THE CURRENT TASK PRIORITIES AFTER ANY		     remark
     PRIORITY PROMPT DURING THE RESPONSE TO THIS QUESTION	     remark
     (DOC. NO 312)

     PRIORITY CHANGE:

     The above line is the system prompt for you to begin.


     If you are unsure of the task priority order, type a question mark  in
     response  to  the  PRIORITY  CHANGE prompt.  The SYSGEN then lists all
     tasks in the system and their priority in octal.  The following  is  a
     sample worksheet.


	  RTS8 BUILD PROGRAM
	  TASK PRIORITY ASSIGNMENT

	  TASK    PRIORITY
	  PWRF   = 001
	  CLOCK  = 002
	  RL01   = 003
	  RX8A   = 004
	  RX8B   = 005
	  LPT    = 006
	  TTY    = 007
	  MCR    = 010
	  0S8    = 011




				     2-42

			      THE SYSGEN DIALOGUE


     If, in response to PRIORITY CHANGE prompts, you type


	  RX8A,RL01
	  RX8B,RL01


     and then type a question mark, you receive the following worksheet.


	  RTS8 BUILD PROGRAM
	  TASK PRIORITY ASSIGNMENT

	  TASK    PRIORITY
	  PWRF   = 001
	  CLOCK  = 002
	  RX8A   = 003
	  RX8B   = 004
	  RL01   = 005
	  LPT    = 006
	  TTY    = 007
	  MCR    = 010
	  0S8    = 011

     In this second listing, the two floppy controller  tasks  now  have  a
     higher  priority  than the RL01 task.  The remainder of the listing is
     the same.

     If your system does not have a line printer, the SYSGEN  automatically
     displays  the  information  on  your terminal.  If you wish to display
     this information on your terminal and you have a line printer, use  an
     OS/8 ASSIGN command to assign the line printer to TTY before beginning
     the SYSGEN.  If you assign the line printer to your terminal  and  you
     state  in  other questions that the assembler and map listings will go
     to the LPT, then you must

	  o  Not chain to BATCH,

	  o  Use the OS/8 DEASSIGN command, and

	  o  Execute the Pass 2 output files by running BATCH.

     If your system includes nonresident tasks, the SWAP task must  have  a
     higher priority than any nonresident user task.

     After answering this question,  you  may  not  branch  to  a  previous
     question using the # feature.


     DO YOU WANT TO CHANGE ANY TASK'S PARTITION
     ASSIGNMENT? [Y/N] (N):




				     2-43

			      THE SYSGEN DIALOGUE


	  IF YOU WISH TO CHANGE THE PARTITION
	  ASSIGNMENT OF ANY TASK (SYSTEM OR USER), ANSWER
	  YES TO THE QUESTION. MOST SYSTEM TASKS MUST BE
	  MEMORY RESIDENT, AND SHOULD NOT BE ASSIGNED TO A
	  PARTITION. NO TASK WITH A PRIORITY HIGHER THAN
	  THE SWAP TASK MAY BE SWAPPED.
	  (DOC. NO 242)


     If you answer YES to this question, the SYSGEN  prints  the  following
     instructions.


     AT THIS POINT, YOU SPECIFY THE NAMES OF THE		     remark
     TASKS WHICH YOU WISH TO PLACE IN DIFFERENT			     remark
     PARTITIONS.  EXAMPLE:					     remark
								     remark
     PARTITION :  TASK-1,M					     remark
     CAUSES TASK-1 TO BE PLACED IN PARTITION M.			     remark
     TYPE A ? AND A CARRIAGE RETURN TO OBTAIN A CURRENT		     remark
     LISTING OF PARTITION ALLOCATION.				     remark
     A CARRIAGE RETURN (ONLY) TERMINATES THE ENTRY.		     remark
     (DOC. NO 314)

     PARTITION :


     This question changes only the partition assignments.

     If  you  wish  to  obtain  a  worksheet  of  the   present   partition
     assignments, type a question mark in response to the PARTITION prompt.
     A worksheet for a small system might look as follows.


	  RTS8 BUILD PROGRAM
	  TASK PARTITION ALLOCATION

	  TASK    PARTITION
	  PWRF     0
	  CLOCK    0
	  RL01     0
	  RX8A     0
	  RX8B     0
	  LPT      0
	  TTY      0
	  MCR      0
	  OS8      0
	  SWAP     0
	  A	   1
	  B	   1
	  C	   2
	  D	   3
	  E	   4


				     2-44

			      THE SYSGEN DIALOGUE


     The following responses to PARTITION prompts


	  MCR,6
	  B,5


     cause the following worksheet to appear  in  response  to  a  question
     mark.


	  RTS8 BUILD PROGRAM
	  TASK PARTITION ALLOCATION

	  TASK    PARTITION
	  PWRF     0
	  CLOCK    0
	  RL01     0
	  RX8A     0
	  RX8B     0
	  LPT      0
	  TTY      0
	  OS8      0
	  SWAP     0
	  A	   1
	  C	   2
	  D	   3
	  E	   4
	  B	   5
	  MCR      6


     This second worksheet differs from the first in  that  it  shows  that
     task  B  now executes in partition 5 and the MCR executes in partition
     6.


		  ------------------- NOTE -------------------
		  | MCR is the  only  DIGITAL-supplied  task |
		  | that    you    can   successfully   make |
		  | nonresident.  However, the  SYSGEN  does |
		  | not  know  that  a  task  cannot be made |
		  | nonresident.  Thus, you  can  place  any |
		  | task  into  any  partition.   To prevent |
		  | DIGITAL tasks from becoming nonresident, |
		  | each  task  except the MCR has code that |
		  | overrides your input and does not  allow |
		  | LINK to place the task into a partition. |
		  --------------------------------------------

     If you do not have a line  printer  to  display  the  partitions,  the
     SYSGEN  displays the information on your terminal.  If you have a line
     printer and wish to display the information on your terminal,  use  an


				     2-45

			      THE SYSGEN DIALOGUE


     OS/8  ASSIGN command before beginning the SYSGEN.  (See the comment to
     DOC. NO 301 for additional information.)

     The above question is the last question of the SYSGEN.

     If you took the default path, the SYSGEN prints


     THE QUESTION AND ANSWER SESSION IS				     remark
     COMPLETED.  A DEFAULT SYSTEM IS NOW BEING			     remark
     PRODUCED.							     remark


     If you do not take the default path, the SYSGEN prints


     THE QUESTION AND ANSWER SESSION IS COMPLETED.		     remark
     THE PROGRAM WILL CONTINUE ON TO				     remark
     PASS 2 (FILE BUILDING).					     remark


     For both default and non-default, the SYSGEN prints the  following  if
     you do not chain to BATCH.


     PASS 2 COMPLETED.  RETURNING TO MONITOR


     If you chain to BATCH, the BATCH program prints


     PASS 2 COMPLETED.  CHAINING TO BATCH AS REQUESTED


     $JOB-MACREL TASK ASSEMBLY

     $MSG MOUNT TASK SOURCES ON SYS: AND STRIKE ANY KEY TO CONTINUE



     2.3  PASS 2 AND BATCH

     As stated in the previous section, the output of the SYSGEN is

	  1.  A Parameter file

	  2.  A MACREL batch file

	  3.  A LINK batch file

	  4.  From 0 to 4 TTY control files (The source  file  TTY.MA  does
	      not  need  an  external  control  file.  Instead, the control
	      information for this file is part of the parameter file.)


				     2-46

			      THE SYSGEN DIALOGUE


	  5.  From 0 to 4 floppy control files

     The function of Pass 2 is to create these files and write them to  the
     device  you  specify.   The Pass 2 actions always occur and the SYSGEN
     always writes these files.

     Chapter 3 presents these files for a major RTS/8 system.   Ordinarily,
     you  do  not  need  to  understand  the information contained in these
     files.  You may, of course, use OS/8  to  list  these  files  on  your
     terminal or line printer.

     The parameter file that the SYSGEN creates consists  of  a  series  of
     equates.  These equates define symbols that the RTS/8 task sources use
     when they assemble.  The equates may  define  task  priority,  set  up
     conditional  assemblies,  and  provide  other  such  information.  See
     Chapter 4 for additional information on the Parameter File.

     The switches that appear  in  the  MACREL  and  LINK  batch  file  are
     dependent upon the answers you give to SYSGEN questions.

     The MACREL batch file is a series of commands, one for  each  task  in
     the  RTS/8  system,  that  instruct  MACREL  to assemble the tasks.  A
     sample statement is:


     .MAC SYS: TTY<SYS: PMYOWN,SYS: TTY/B/C/Z


     This statement tells MACREL to assemble the DIGITAL-supplied TTY task,
     using  the  equates  contained in the parameter file PMYOWN.MA.  (This
     sample line assumes that you choose to give  the  name  MYOWN  to  the
     output  files.)  The  /B option tells MACREL to print a header, the /C
     option tells MACREL to create a cross-reference listing and  /Z  tells
     MACREL  to  swap  BATCH  out of memory.  (The /C is a no-op unless you
     request listings.)


		  ------------------- NOTE -------------------
		  | These option switches appear only if you |
		  | require listings.			     |
		  --------------------------------------------

     The last line of the MACREL batch file is an instruction  that  either
     tells  BATCH  to  submit  the  LINK batch file and/or resubmit itself.
     Note that BATCH prints a log on the OS/8 terminal.

     The LINK batch file contains  the  file  specifications  necessary  to
     generate the .SV image of the RTS/8 system.  The switches in this file
     are:

	  /K set virtual core
	  /M load the top page of fields
	  /C close current overlay and open next overlay


				     2-47

			      THE SYSGEN DIALOGUE


	  /O close current overlay level and open next level
	  /X tells LINK that this is an RTS/8 system generation

     If you have specified that BATCH should chain to RTS/8, the last  line
     of  this file is a RUN dev: Sname command.  This command tells OS/8 to
     begin executing RTS/8.

     When BATCH executes, the MACREL and LINK files must reside on  SYS  or
     on  a  device  coresident  with SYS such as RKB0 or RL01.  If they are
     not, BATCH cannot execute.

     The SYSGEN gives you four ways to create an RTS/8 system.

	  1.  Automatic--SYSGEN chains to BATCH and  BATCH  chains  to  the
	      RTS/8  system.   The  automatic  path  requires  the  minimum
	      intervention.  If the source files are all on one device, you
	      answer yes to questions that:

		  o  tell SYSGEN to chain to BATCH

		  o  tell BATCH to  execute  the  MACREL  batch  file  that
		     assembles  the RTS/8 sources and submit the LINK batch
		     file that creates the RTS/8 system

		  o  chain from BATCH to the RTS/8 system

	      Because RTS/8 executes within a batch  file,  you  return  to
	      BATCH  when  you  leave RTS/8.  However, since the command to
	      execute the RTS/8 system was  the  last  instruction  in  the
	      batch file, control immediately passes to the OS/8 Monitor.

	      If your sources are on the same kind of device but are not on
	      the  same  physical device, BATCH prints a message that tells
	      you to insert the physical  device  into  the  device  drive.
	      (You must then resubmit the batch file.)

	  2.  Semi-automatic--SYSGEN chains to BATCH  and  creates  a  save
	      image  of  the RTS/8 system.  You may then run this system by
	      using an OS/8 R command when you need to execute  RTS/8.   If
	      the  RTS/8  system  is not on SYS, you must either copy it to
	      SYS or, if the device where the save image of  RTS/8  resides
	      is a system device, boot the RTS/8 save image device.

	      This differs from the Automatic only in the last step:  BATCH
	      does not chain to the RTS/8 system.

	  3.  Manual--SYSGEN returns to the OS/8  Keyboard  Monitor.   When
	      you  wish  to create the RTS/8 system, you execute OS/8 BATCH
	      as follows

		   .R BATCH
		   *MNAME/T

	      or

				     2-48

			      THE SYSGEN DIALOGUE


		   .SUBMIT MNAME/T

	      where MNAME is the name of the MACREL batch file.

	      If the source files are not on the same medium, then you must
	      also  use  the /E option so that BATCH does not abort when it
	      does not find a file.  If the files are not all on  the  same
	      medium,  the  BATCH  file does not automatically chain to the
	      LINK BATCH file.  Instead, you must type a  ^C  and  manually
	      submit the LINK BATCH file.

	      You use the /T option so that the BATCH log  prints  on  your
	      terminal rather than the line printer.

	      After BATCH processes this file, it automatically submits the
	      LINK  file.   When  BATCH concludes, you have a save image of
	      RTS/8.  (You may then run the system as specified in 2.)

	  4.  Chained Manual--the same as  the  Manual  except  that  BATCH
	      chains to the RTS/8 system it creates.



































				     2-49

			      THE SYSGEN DIALOGUE


     The following block diagram illustrates the four paths.

	  Automatic      Semi-automatic       Manual       Chained-Manual

	  ----------       ----------       ----------       ----------
	  |	   |       |	    |       |	     |       |	      |
	  |  OS/8  |       |  OS/8  |       |  OS/8  |       | OS/8   |
	  |	   |       |	    |       |	     |       |	      |
	  ----------       ----------       ----------       ----------
	      |		       |		|		 |
	      v		       v		v		 v
	  ----------       ----------       ----------       ----------
	  |	   |       |	    |       |	     |       |	      |
	  | SYSGEN |       | SYSGEN |       | SYSGEN |       | SYSGEN |
	  |	   |       |	    |       |	     |       |	      |
	  ----------       ----------       ----------       ----------
	      |		       |		|		 |
	      v		       v		v		 v
	  ----------       ----------       ----------       ----------
	  |	   |       |	    |       |	     |       |	      |
	  |  BATCH |       |  BATCH |       |  OS/8  |       |  OS/8  |
	  |	   |       |	    |       |	     |       |	      |
	  ----------       ----------       ----------       ----------
	      |		       |		|		 |
	      v		       v		v		 v
	  ----------       ----------       ----------       ----------
	  |	   |       |	    |       |	     |       |	      |
	  |  RTS/8 |       |  OS/8  |       |  BATCH |       |  BATCH |
	  |	   |       |	    |       |	     |       |	      |
	  ----------       ----------       ----------       ----------
			       |		|		 |
			       v		v		 v
			   ----------       ----------       ----------
			   |	    |       |	     |       |	      |
			   |  RTS/8 |       |  OS/8  |       |  RTS/8 |
			   |	    |       |	     |       |	      |
			   ----------       ----------       ----------
						|
						v
					    ----------
					    |	     |
					    |  RTS/8 |
					    |	     |
					    ----------


     The intervening OS/8 steps in this diagram  allow  you  to  switch  to
     different machines or defer executing the RTS/8 system.

     The RTS/8 system that BATCH creates has the name of the form  SNAME.SV
     (where  NAME  is  the  character string you specified in response to a
     SYSGEN question).  You execute  this  program  by  typing  an  OS/8  R
     command (if you do not chain to RTS/8).  For more information, see the
     RTS/8 User's Manual.     ___________________

				     2-50

			      THE SYSGEN DIALOGUE


     The MACREL and LINK batch files are always run as one unit.   This  is
     intentional.   The  SYSGEN assembles each source file with a parameter
     file.  Changes in the parameter file due to different SYSGEN paths can
     cause  great  differences in parameter file equates.  Consequently, if
     the MACREL and LINK files are not run together, the RTS/8  system  may
     assemble  incorrectly.   Although  it  is  tempting  to  use .RB files
     created in other SYSGENS, you should not use this procedure unless the
     parameter  files  each  .RB  file  was assembled with are identical or
     differences will not affect the system.


     2.4  RTS/8 SYSGEN DOCUMENT NUMBERS

     The following table specifies the page number of  this  chapter  where
     you may find additional information for RTS/8 questions.

	      DOC NO		PAGE	    DOC NO	       PAGE
	      ______		____	    ______	       ____

	       17 . . . . . . . 2-12	     225 . . . . . . . 2-19
	       22 . . . . . . . 2-7	     227 . . . . . . . 2-19
	       24 . . . . . . . 2-8	     231 . . . . . . . 2-19
	       26 . . . . . . . 2-8	     235 . . . . . . . 2-20
	       30 . . . . . . . 2-9	     240 . . . . . . . 2-28
	       33 . . . . . . . 2-9	     242 . . . . . . . 2-38
	       42 . . . . . . . 2-6	     246 . . . . . . . 2-29
	       46 . . . . . . . 2-7	     250 . . . . . . . 2-29
	       50 . . . . . . . 2-12	     252 . . . . . . . 2-26
	       52 . . . . . . . 2-13	     254 . . . . . . . 2-26
	       54 . . . . . . . 2-13	     257 . . . . . . . 2-27
	       56 . . . . . . . 2-13	     261 . . . . . . . 2-27
	       60 . . . . . . . 2-14	     263 . . . . . . . 2-27
	       62 . . . . . . . 2-14	     265 . . . . . . . 2-27
	       64 . . . . . . . 2-15	     267 . . . . . . . 2-28
	       66 . . . . . . . 2-15	     273 . . . . . . . 2-28
	       70 . . . . . . . 2-16	     274 . . . . . . . 2-16
	       72 . . . . . . . 2-16	     276 . . . . . . . 2-16
	       73 . . . . . . . 2-16	     300 . . . . . . . 2-35
	      136 . . . . . . . 2-24	     301 . . . . . . . 2-35
	      153 . . . . . . . 2-30	     307 . . . . . . . 2-36
	      166 . . . . . . . 2-32	     312 . . . . . . . 2-36
	      170 . . . . . . . 2-32	     314 . . . . . . . 2-38
	      172 . . . . . . . 2-33	     317 . . . . . . . 2-26
	      174 . . . . . . . 2-32	     323 . . . . . . . 2-32
	      176 . . . . . . . 2-33	     325 . . . . . . . 2-25
	      202 . . . . . . . 2-33	     327 . . . . . . . 2-34
	      204 . . . . . . . 2-34	     331 . . . . . . . 2-25
	      205 . . . . . . . 2-30	     334 . . . . . . . 2-10
	      207 . . . . . . . 2-30	     335 . . . . . . . 2-24
	      211 . . . . . . . 2-30	     340 . . . . . . . 2-12
	      215 . . . . . . . 2-31	     341 . . . . . . . 2-11
	      216 . . . . . . . 2-17	     342 . . . . . . . 2-28
	      220 . . . . . . . 2-17	     347 . . . . . . . 2-18
	      222 . . . . . . . 2-18	     351 . . . . . . . 2-18
	      224 . . . . . . . 2-18	     353 . . . . . . . 2-14

				     2-51







				   CHAPTER 3

			      TWO EXAMPLE SYSGENS


     3.1  OVERVIEW

     This chapter is a listing of two example SYSGENS.  The  first  example
     is the terminal dialogue you receive when you create a default system.
     This example (which shows the dialogue, the execution  of  the  MACREL
     and  LINK  batch files, and a segment of MCR prompts from an executing
     RTS/8 system) does not attempt to show many of  the  features  of  the
     SYSGEN.

     The second example is the creation of a  larger  RTS/8  system.   This
     example  shows  many of the SYSGEN features and the majority of SYSGEN
     questions.  Some error messages were included within this  example  so
     that  you may see how they print.  This example also lists portions of
     the output files which the SYSGEN creates.

     As the previous chapter discussed all elements of the SYSGEN dialogue,
     the   examples  in  this  chapter  are  presented  without  additional
     explanatory comment.  where necessary, comments explain which file  is
     produced and other similar information.



     3.2  A DEFAULT SYSGEN

     .R SYSGEN
     ON WHAT DEVICE IS SCRIPT.SV LOCATED ? :


     RTS/8 V03 SYSTEM BUILDER PROGRAM V01.

     THIS PROGRAM IS A CONVERSATIONAL
     QUESTION AND ANSWER SYSTEM FOR
     BUILDING AN RTS/8 REAL TIME SYSTEMS.

     THE QUESTIONS AND EXPLANATIONS IN THIS
     DIALOGUE ARE BRIEF.  CHAPTER 2 IN THE
     SYSTEM GENERATION MANUAL INCLUDES AD-
     DITIONAL INFORMATION.

     001 DO YOU WANT PROGRAM OPERATION
     INFORMATION? (YOU MAY TYPE Y FOR YES OR N
     FOR NO FOLLOWED BY A CARRIAGE RETURN):N


     002 IS THE TARGET MACHINE FOR WHICH YOU ARE
     BUILDING THE RTS/8 SYSTEM A PDP 8/A? [Y/N] (Y):N


				      3-1

			      TWO EXAMPLE SYSGENS


     003 IS THE TARGET MACHINE A PDP 8/E? [Y/N] (N):Y


     004 TO WHICH DEVICE SHOULD SYSGEN WRITE THE OUTPUT
     FILES? [A] (SYS):


     005 DO YOU WANT TO CHAIN IMMEDIATELY TO THE
     RTS/8 SYSTEM WHICH BATCH CAN PRODUCE? [Y/N] (Y):


     006 WHAT FIVE CHARACTER NAME WOULD YOU LIKE
     TO CALL THE FILES PRODUCED? [A] (DEFLT):

     007 DO YOU WANT THE SYSGEN PROGRAM TO REQUEST
     BATCH TO RUN BEFORE TERMINATING [Y/N] (Y):


     008 ON WHICH INPUT DEVICE DO THE SOURCE
     FILES RESIDE? [A] (SYS):RKB0


     009 ON WHICH DEVICE SHOULD BATCH STORE
     THE .RB FILES? [A] (SYS):


     010 ON WHICH OUTPUT DEVICE SHOULD BATCH STORE
     THE .SV FILE?  [A] (SYS):


     011 DO YOU WANT ASSEMBLY LISTINGS? [Y/N] (N):


     012 DO YOU WANT LINKER LOAD MAP LISTINGS? [Y/N] (N):


     013 DO YOU WISH TO BUILD AN RTS/8 SYSTEM WITHOUT
     SPECIFYING ANY PARAMETERS?  [Y/N] (N):Y

      THE QUESTION AND ANSWER SESSION IS
     COMPLETED.  A DEFAULT SYSTEM IS NOW BEING
     PRODUCED.

       PASS2 COMPLETED.  CHAINING TO BATCH AS REQUESTED.


     The following is a listing of the batch log for the  creation  of  the
     default  system created in the dialogue.  This is immediately followed
     by statements from the RTS/8 MCR.






				      3-2

			      TWO EXAMPLE SYSGENS


     $JOB-MACREL TASK ASSEMBLY

     $MSG MOUNT TASK SOURCES ON RKB0:AND STRIKE ANY KEY TO CONTINUE
     .MAC SYS:RTS8  <SYS:PDEFLT,RKB0:RTS8
     NO ERRORS
     .MAC SYS:TTY   <SYS:PDEFLT,RKB0:TTY
     NO ERRORS
     .MAC SYS:MCR   <SYS:PDEFLT,RKB0:MCR
     NO ERRORS
     .MAC SYS:CLOCK <SYS:PDEFLT,RKB0:CLOCK
     NO ERRORS
     .MAC SYS:EXIT  <SYS:PDEFLT,RKB0:EXIT
     NO ERRORS
     .SU SYS:LDEFLT.BI/T


     $JOB RTS8 MODULE LINKAGE


     .R LINK
     *SYS:SDEFLT</K=01/M/X
     *SYS:RTS8
     *SYS:TTY
     *SYS:MCR
     *SYS:EXIT
     *SYS:CLOCK
     *$
     .RU SYS:SDEFLT
     >SY
     01  CLOCK  O
     02  TTY    M
     03  MCR
     04  EXIT   R
     >SYSTAT TTY
     02  TTY    M   0051: 0000  2224  0000  0062
     >DATE  27-NOV-78
     >DATE
     27-NOV-78
     >TIME
     00:00:35
     >TIME 15:04
     >TIME
     15:04:01
     >EXIT
     $END

     $END BATCH

     .






				      3-3

			      TWO EXAMPLE SYSGENS


     3.3  A NORMAL SYSGEN

     .R SYSGEN
     ON WHAT DEVICE IS SCRIPT.SV LOCATED ? :  SYS


     RTS/8 V03 SYSTEM BUILDER PROGRAM V01.

     THIS PROGRAM IS A CONVERSATIONAL
     QUESTION AND ANSWER SYSTEM FOR
     BUILDING AN RTS/8 REAL TIME SYSTEMS.

     THE QUESTIONS AND EXPLANATIONS IN THIS
     DIALOGUE ARE BRIEF.  CHAPTER 2 IN THE
     SYSTEM GENERATION MANUAL INCLUDES AD-
     DITIONAL INFORMATION.


     001 DO YOU WANT PROGRAM OPERATION
     INFORMATION? (YOU MAY TYPE Y FOR YES OR N
     FOR NO FOLLOWED BY A CARRIAGE RETURN):

      YES OR NO ANSWERS ARE INDICATED
     BY A [Y/N] NOTATION.  TYPE A 'Y' FOR YES
     OR AN 'N' FOR NO FOLLOWED BY A CARRIAGE
     RETURN TO ANSWER THE QUESTION.

      QUESTIONS REQUIRING A NUMERICAL RESPONSE
     ARE INDICATED BY A [D] FOR DECIMAL OR AN [O]
     FOR OCTAL.  ENTER THE NUMBER FOLLOWED BY
     A CARRIAGE RETURN.  (ALWAYS INTEGER)

      QUESTIONS REQUIRING AN ALPHANUMERIC
     ANSWER ARE INDICATED BY [A].  RESPOND
     BY TYPING THE ALPHANUMERIC DATA FOLLOWED
     BY A CARRIAGE RETURN.

     002 ARE YOU READY TO CONTINUE? [Y/N](Y):


      IF YOU WOULD LIKE AN EXPLANATION
     OF A QUESTION, TYPE A ? FOLLOWED BY A CARRIAGE
     RETURN.  THE PROGRAM THEN PRINTS AN EXPLANA-
     TION AND ALSO REPRINTS THE QUESTION.

      ON THE LINE FOLLOWING MOST REMARKS IS A
     DOCUMENTATION NUMBER OF THE FORM
     (DOC. NO NNN). YOU USE THIS NUMBER TO LOCATE
     ADDITIONAL INFORMATION IN THE SYSTEM GENERATION
     MANUAL.





				      3-4

			      TWO EXAMPLE SYSGENS


      EACH QUESTION HAS A NUMBER ASSOCIATED
     WITH IT.  IF YOU NOTICE A MISTAKE DURING AN
     RTS/8 QUESTION SESSION, TYPING #NNN
     CAUSES QUESTION NUMBER NNN TO BE REPEATED.

      YOU CAN THEN CHANGE THE ANSWER TO NNN.
     THE PROGRAM THEN RESUMES AT THIS NEW
     QUESTION.  IT ALSO RENUMBERS QUESTIONS
     BEGINNING AT THIS NUMBER.  (NOTE THAT
     AFTER A TASK PRIORITY CHANGE, THIS FEATURE IS NOT
     SERVICED.)

     003 ARE YOU READY TO CONTINUE? [Y/N](Y):

      IF YOU TYPE AN INVALID ANSWER, THE PROGRAM
     PRINTS AN ERROR MESSAGE, AND THEN REPRINTS
     THE QUESTION.

      CONTROL C RETURNS YOU TO THE OS/8 KEY-
     BOARD MONITOR AND ABORTS THE CURRENT SYSGEN.

      FOR FILE STORAGE SPECIFICATIONS SUCH
     AS DTA0, THE PROGRAM EXPECTS STANDARD DEVICE
     NAMES.  NOTE THAT YOU DO NOT APPEND A COLON
     TO THE DEVICE NAME.

      NEXT TO THE BRACKETS [] INDICATING THE
     EXPECTED RESPONSE ARE PARENTHESES () WHICH
     INDICATE THE DEFAULT ANSWER.  YOU SELECT THE
     DEFAULT ANSWER BY JUST TYPING A CARRIAGE RETURN.

     004 IS THE TARGET MACHINE FOR WHICH YOU ARE
     BUILDING THE RTS/8 SYSTEM A PDP 8/A? [Y/N] (Y):NO


     005 IS THE TARGET MACHINE A PDP 8/E? [Y/N] (N):MAYBE


     ERROR 021 NOT A YES OR NO ANSWER OR BAD DEFAULT FOR Y/N RECORD

     005 IS THE TARGET MACHINE A PDP 8/E? [Y/N] (N):


     006 IS THE TARGET MACHINE A PDP-12? [Y/N] (N):


     007 IS THE TARGET MACHINE A VT78 SYSTEM? [Y/N] (N):


      THE TARGET MACHINE MUST BE A PDP 8/I,
     A PDP 8/L, A PDP-8, OR A LINC-8 BECAUSE IT IS
     NOT ONE OF THE ABOVE.
     (DOC.  NO 046)


				      3-5

			      TWO EXAMPLE SYSGENS


     008 TO WHICH DEVICE SHOULD SYSGEN WRITE THE OUTPUT
     FILES? [A] (SYS):RXA0


     009 DO YOU WANT TO CHAIN IMMEDIATELY TO THE
     RTS/8 SYSTEM WHICH BATCH CAN PRODUCE?  [Y/N] (Y):#8


     008 TO WHICH DEVICE SHOULD SYSGEN WRITE THE OUTPUT
     FILES? [A] (SYS):


     009 DO YOU WANT TO CHAIN IMMEDIATELY TO THE
     RTS/8 SYSTEM WHICH BATCH CAN PRODUCE?  [Y/N:] (Y):NO


     010 WHAT FIVE CHARACTER NAME  WOULD YOU LIKE
     TO CALL THE  FILES PRODUCED?  [A] (DEFLT):MY^U
     MINE

     011 DO YOU WANT THE SYSGEN PROGRAM TO REQUEST
     BATCH TO RUN BEFORE TERMINATING [Y/N] (Y):


     012 ON WHICH INPUT DEVICE DO THE SOURCE
     FILES RESIDE?  [A] (SYS):RKB0


     013 ON WHICH DEVICE SHOULD BATCH STORE THE .RB
     FILES? [A] (SYS):RKA0


     014 ON WHICH OUTPUT DEVICE SHOULD BATCH STORE
     THE .SV FILE?  [A] (SYS):RXA0


     015 DO YOU WANT ASSEMBLY LISTINGS? [Y/N] (N):Y


     016 TO WHICH OUTPUT DEVICE SHOULD BATCH
     WRITE THE ASSEMBLY LISTINGS?  [A] (LPT):


     017 DO YOU WANT LINKER LOAD MAP LISTINGS?
     [Y/N] (N):Y


     018 ON WHICH OUTPUT DEVICE SHOULD BATCH
     WRITE THE MEMORY MAP LISTINGS?  [A] (LPT):


     019 DO YOU WISH TO BUILD AN RTS/8 SYSTEM WITHOUT
     SPECIFYING ANY PARAMETERS? [Y/N] (N):


				      3-6

			      TWO EXAMPLE SYSGENS


     020 ARE ALL SOURCE FILES ON THE SAME MEDIUM?  [Y/N] (Y):Y


     021 DOES THE TARGET SYSTEM HAVE EAE HARDWARE?[Y/N] (N):?


      EAE HARDWARE IS AN OPTION WHICH MAY BE
     PRESENT IN THE TARGET CONFIGURATION.  EAE
     HARDWARE ALLOWS OPERATIONS SUCH AS MULTIPLY AND
     DIVIDE TO BE PERFORMED IN THE HARDWARE.
     (DOC. NO 050)

     021 DOES THE TARGET SYSTEM HAVE EAE HARDWARE?[Y/N] (N):Y


     022 DO YOU WISH TO SAVE THE CONTENTS OF THE EAE
     REGISTERS WHEN TASK SWITCHING OCCURS? [Y/N] (Y):


     023 HOW MANY FIELDS OF MEMORY EXIST IN THE
     TARGET MACHINE? [D] (4):#21


     021 DOES THE TARGET SYSTEM HAVE EAE HARDWARE?[Y/N] (N):


     022 DOES THE TARGET SYSTEM HAVE A HARDWARE
     MQ REGISTER?  [Y/N] (Y):

     023 DO YOU WANT TO SAVE THE CONTENTS OF THE
     MQ REGISTER WHEN TASK SWITCHING OCCURS? [Y/N] (Y):


     024 HOW MANY FIELDS OF MEMORY EXIST IN THE
     TARGET MACHINE? [D] (4):32


     025 IN WHICH FIELD DOES RTS8 RESIDE?  [D] (0):32


     ERROR 202 NUMERICAL ANSWER NOT WITHIN SPECIFIED LIMITS

     025 IN WHICH FIELD DOES RTS8 RESIDE?  [D] (0):29


     026 DOES YOUR TARGET SYSTEM HAVE POWER FAIL
     HARDWARE?  [Y/N] (N):Y


     027 DOES THE TARGET SYSTEM HAVE KL8A
     HARDWARE?  [Y/N] (N):Y


     028 HOW MANY KL8A'S ARE IN THE TARGET SYSTEM? [D] (1):3

				      3-7

			      TWO EXAMPLE SYSGENS


     029 DO YOU HAVE KT8A HARDWARE IN THE TARGET
     SYSTEM?  [Y/N] (N):Y

     030 DO YOU WANT ANY OF THE DEC- PROVIDED
     SYSTEM TASKS IN YOUR RTS/8 SYSTEM? [Y/N] (Y):


      EACH DEC TASK WILL BE LISTED ONE AT A
     TIME.  IF YOU WISH TO INCLUDE THE TASK IN YOUR
     SYSTEM, TYPE Y.  IF NOT, TYPE N.  IF THE
     SYSGEN PROGRAM REQUIRES MORE INFORMATION
     ABOUT A TASK, IT WILL ASK THE QUESTIONS
     IN ANOTHER SECTION .
     (DOC. NO 073)

     031 DO YOU WANT THE POWER FAIL HANDLER?  [Y/N] (N) :Y


     032 CLOCK HANDLER?  [Y/N] (N):Y


     033 UNIVERSAL DIGITAL CONTROLLER TASK?  [Y/N] (N):Y


     034 RF08 DISK DRIVER?  [Y/N] (N):Y


     035 DF32 DISK DRIVER?  [Y/N] (N):Y


     036 RK8E DISK DRIVER?  [Y/N] (N):Y


     037 RK8 DISK DRIVER?  [Y/N] (N):Y


     038 RL01 DISK DRIVER?  [Y/N] (N):Y


     039 DECTAFE DRIVER?  [Y/N] (N):Y


     040 FIRST FLOPPY CONTROLLER?  [Y/N] (N):Y


     041 SECOND FLOPPY CONTROLLER?  [Y/N] (N):Y


     042 THIRD FLOPPY CONTROLLER?  [Y/N] (N):Y


     043 FOURTH FLOPPY CONTROLLER?  [Y/N] (N):Y



				      3-8

			      TWO EXAMPLE SYSGENS


     044 LINE PRINTER DRIVER?  [Y/N] (N):Y


     045 TELETYPE DRIVER?  [Y/N] (Y):Y


     046 EMERGENCY BREAKTHROUGH TASK?  [Y/N] (N):Y


     047 SWAPPER TASK?  [Y/N] (N):Y


     048 CASSETTE DRIVER?  [Y/N] (N):Y


     049 DO YOU WANT THE CASSETTE FILE SUPPORT
     TASK?  [Y/N] (N):Y


     050 OS/8 FILE SUPPORT TASK?  [Y/N] (N):Y


     051 MONITOR CONSOLE ROUTINE?  [Y/N] (Y):


     052 RTS/8 TEST TASK?  [Y/N] (N):N


     053 EXIT TASK?  [Y/N] (N):Y


     054 OS/8 SUPPORT TASK?  [Y/N] (N):Y


     055 OS/8 BACKGROUND TERMINAL SUPPORT TASK? [Y/N] (Y):Y


      THIS SECTION PRESENTS THE QUESTIONS WHICH REQUIRE
     MULTIPLE PARAMETERS TO SPECIFY
     THE OS/8 TASK WHICH YOU HAVE SELECTED.
     (DOC. NO 166)

     056 HOW MANY FIELDS DO YOU  WISH TO ALLOCATE
     FOR THE OS/8 BACKGROUND?  [D] (2):?


      OS/8 REQUIRES A MINIMUM OF 2 FIELDS (8K).
     IF YOU WISH TO USE BATCH. YOU NEED A
     MINIMUM OF 3 FIELDS (12K).
     (DOC. NO 170)

     056 HOW MANY FIELDS DO YOU WISH TO ALLOCATE
     FOR THE OS/8 BACKGROUND?  [D] (2):3


				      3-9

			      TWO EXAMPLE SYSGENS


     057 WHAT IS THE OS/8 KEYBOARD DEVICE
     CODE?  [O] (03):9


     ERROR 030 RESPONSE NOT OCTAL/DECIMAL AS EXPECTED

     057 WHAT IS THE OS/8 KEYBOARD DEVICE
     CODE?  [O] (03):


     058 WHAT IS THE OS/8 TELEPRINTER DEVICE
     CODE?  [O] (04):


     059 WHAT IS THE RTS/8 HANDLER TASK FOR
     OS/8?  [A] (RK8E):


     060 HOW MANY NULL CHARACTERS ARE REQUIRED
     AFTER A LINE FEED UNDER OS/8?  [D] (O):


     061 DO YOU WANT THE OS/8 BACKGROUND TASK TO RUN IN
     THE HIGHEST AVAILABLE FIELDS? [Y/N] (Y):?


      THE OS/8 SUPPORT TASK RUNS THE OS/8 BACKGROUND
     IN CONTIGUOUS FIELDS (TYPICALLY THE HIGHEST FIELDS
     OF THE TARGET MACHINE). THE KT8A ALLOWS THE OS/8
     BACKGROUND FIELDS TO BE LOCATED IN CONTIGUOUS FIELDS
     OTHER THAN THE HIGHEST FIELDS. ENTER THE DECIMAL
     NUMBER OF THE LOWEST FIELD IN WHICH OS/8 WILL RUN.
     FIELD 0 IS RESERVED FOR RTS/8.
     (DOC. NO 202)

     061 DO YOU WANT THE OS/8 BACKGROUND TASK TO RUN IN
     THE HIGHEST AVAILABLE FIELDS? [Y/N] (Y):30


     ERROR 021 NOT A YES OR NO ANSWER OR BAD DEFAULT FOR Y/N RECORD


     061 DO YOU WANT THE OS/8 BACKGROUND TASK TO RUN IN
     THE HIGHEST AVAILABLE FIELDS? [Y/N] (Y):N


     062 WHAT IS THE LOWEST FIELD WHICH RTS/8 WILL
     USE FOR THE OS/8 TASK? [D] (?):30


      THIS SECTION PRESENTS THE PARAMETERS
     REQUIRED TO SPECIFY THE MCR TASK
     WHICH YOU HAVE SELECTED.
     (DOC. NO 205)

				     3-10

			      TWO EXAMPLE SYSGENS


     063 DO YOU WANT TIME-OF-DAY FACILITY IN
     YOUR MCR TASK?  [Y/N] (Y):

     064 DO YOU WANT THE MCR SYSTEM STATUS
     REPORT CAPABILITY?  [Y/N] (Y):


     065 WHICH TERMINAL WILL THE MCR TASK
     USE?   [A] (TTY):


      THIS SECTION PRESENTS THE PARAMETERS
     REQUIRED TO SPECIFY THE CLOCK TASK WHICH
     YOU HAVE SELECTED.
     (DOC. NO 216)

     066 DOES YOUR TARGET SYSTEM HAVE A
     STANDARD CLOCK?  [Y/N] (Y):


     067 HOW MANY SOFTWARE TICKS PER SECOND?  [D] (10):#66


     066 DOES YOUR TARGET SYSTEM HAVE A
     STANDARD CLOCK?  [Y/N] (Y):?


      STANDARD CLOCKS:
     CPU	 CLOCK
     ---	 -----
     PDP 8/A     PDP8A
     PDP 8/E     DK8EA/DK8EC
     PDP-12      KW12
     VT-78       PDP8A
     OTHER       DK8EA/DK8E

     IF YOUR TARGET SYSTEM HAS A CLOCK OTHER
     THOSE INDICATED IN THE TABLE,
     ANSWER 'N' TO THIS QUESTION
     (DOC. NO 20)

     066 DOES YOUR TARGET SYSTEM HAVE A
     STANDARD CLOCK?  [Y/N] (Y):N


     067 WHAT IS THE DEC DESIGNATION FOR THE NON-
     STANDARD CLOCK?  [A] (?):PDP8A


     068 HOW MANY SOFTWARE TICKS PER SECOND?  [D] (10):30


     069 HOW MANY ENTRY SLOTS IN THE CLOCK QUEUE
     DO YOU WANT?  [D] (16):128

				     3-11

			      TWO EXAMPLE SYSGENS


     070 DO YOU WANT THE SPECIAL CLOCK INTERRUPT LINKAGE?  [Y/N] (N):Y


      THIS SECTION PRESENTS THOSE PARAMETERS
     WHICH RTS/8 REQUIRES TO SPECIFY THE UDC
     TASK WHICH YOU HAVE SELECTED.
     (DOC. NO 225)

     071 HOW MANY INTERRUPTS CAN BE STORED AT
     ONE TIME?  [O] (12):


     072 HOW MANY COUNTER MODULES IN THE TARGET
     SYSTEM UDC?  [O] (1):


     073 HOW MANY CONTACT MODULES IN THE UDC? [O] (2):


     074 HOW MANY ANALOG INPUT CONVERTER MODULES? [O] (2):


     075 WHAT IS THE ADDRESS OF THE FIRST COUNTER
     MODULE?  [O] (?):


     ERROR 23 NO DEFAULT ALLOWED FOR THIS QUESTION

     075 WHAT IS THE ADDRESS OF THE FIRST COUNTER
     MODULE?  [O] (?):1000


     076 WHAT IS THE ADDRESS OF THE FIRST CONTACT
     INTERRUPT MODULE?  [0] (O):1040


     077 WHAT IS THE ADDRESS OF THE FIRST A/D
     CONVERTER MODULE?  [O] (?):1100


      THIS SECTION PRESENTS THOSE PARAMETERS
     REQUIRED TO SPECIFY THE SWAPPER TASK WHICH
     YOU HAVE SELECTED
     (DOC. NO 240)

     078 WHICH RTS/8 DEVICE TASK WILL THE SWAPPER TASK
     USE TO MAKE TRANSFERS? [A] (RKBE):


     079 WHICH PHYSICAL UNIT WILL THE SWAPPER USE
     FOR MAKING TRANSFERS? [A] (0).




				     3-12

			      TWO EXAMPLE SYSGENS


     080 HOW MANY TTY TASKS WILL BE IN THE TARGET
     SYSTEM? [D] (1):


     081 WHAT IS THE KEYBOARD DEVICE CODE FOR THE
     TTY TASK?  [O] (03):


     082 WHAT IS THE TELEPRINTER DEVICE CODE FOR THE
     TTY TASK?  [O] (04):


     083 DO YOU WANT CNTRL/S AND CNTRL/Q FEATURES FOR
     YOUR TTY TASK?  [Y/N] (Y):


     084 DO YOU WANT RUBOUT SUPPORT FOR THE TTY
     SCREEN? [Y/N] (Y):#80


     080 HOW MANY TTY TASKS WILL BE IN THE
     TARGET SYSTEM?  [D] (1):5


      IN THE FOLLOWING QUESTIONS.  YOU CAN ENTER
     UP TO FIVE ANSWERS, SEPARATED BY COMMAS.
     THE ANSWERS INDICATE YOUR CHOICE FOR THE GIVEN
     PARAMETER FOR EACH OF THE TTY TASKS THAT YOU HAVE
     SELECTED.  EXAMPLE:
     IF YOU TYPE TO THE DEVICE CODE QUESTION:
     04,31,33,35,37 (CARRIAGE RETURN) YOU SELECT
     DEVICE CODE CODE 04 FOR TTY TASK, 31 FOR TTY1
     ETC.

     081 WHAT IS THE KEYBOARD DEVICE CODE FOR THE
     TTY TASK?  [O] (03):3,5,7,11


     ERROR 100 DEVICE CODE MUST BE SPECIFIED FOR EACH TTY TASK

     081 WHAT IS THE KEYBOARD DEVICE CODE FOR THE
     TTY TASK?  [O] (03):3,5,7,11,13


     082 WHAT IS THE TELEPRINTER DEVICE CODE FOR THE
     TTY TASK?  [O] (04):4,6,10,12,14


     083 DO YOU WANT CNTRL/S AND CNTRL/Q FEATURES
     FOR YOUR TTY TASK?  [Y/N] (Y):Y,N,Y,N,A


     ERROR 021 NOT A YES OR NO ANSWER  OR BAD DEFAULT FOR Y/N RECORD


				     3-13

			      TWO EXAMPLE SYSGENS


     083 DO YOU WANT CNTRL/S AND CNTRL/Q FEATURES
     FOR YOUR TTY TASK?  [Y/N] (Y):Y,N,Y,N,Y


     084 DO YOU WANT RUBOUT SUPPORT FOR THE
     TTY SCREEN? [Y/N] (Y):Y,N,Y,N,Y


     085 HOW MANY NULLS AFTER A LINE FEED FOR THE TTY
     DEVICE?  [O] (0):0,10,0,10,0


     086 HOW MANY CHARACTERS DO YOU WANT ON A LINE
     FOR THE TTY DEVICE?  [D] (8O):80,128,80,128,80


     087 DOES THE HARDWARE SUPPORT TABS ON THE
     TTY DEVICE?  [Y/N] (Y):Y,N,Y,N,Y


     088 HOW MANY SECONDS BEFORE A TTY READ TIMEOUT? [D] (0):10,0,0,10,0


      END OF MULTIPLE ANSWER SECTION.  THE FOLLOWING
     QUESTIONS REQUIRE SINGLE ANSWERS.
     (DOC. NO 270)

     089 WHAT IS THE TASK NAME FOR THE OS/8 BACKGROUND
     TERMINAL SUPPORT TASK? [A] (TTY):


     090 WHAT IS THE TASK NAME OF THE DEVICE HANDLER TO BE
     USED FOR EMERGENCY BREAKTHROUGH MESSAGES? [A] (TTY):


      THIS SECTION PRESENTS THE PARAMETERS
     REQUIRED TO SPECIFY THE KL8A TASK WHICH
     YOU HAVE SELECTED.
     (DOC. NO 274)

     091 WHAT IS THE DEVICE CODE FOR THE FIRST KL8A
     DEVICE?  [O] (40):


      THIS SECTION PRESENTS THE HARDWARE DEVICE
     CODE SPECIFICATION(S) FOR THE FLOPPY CONTROLLER(S)
     WHICH YOU HAVE SELECTED
     (DOC. NO 335)


     092 WHAT IS THE DEVICE NUMBER FOR THE FIRST
     DEVICE CONTROLLER? [O] (75):



				     3-14

			      TWO EXAMPLE SYSGENS


     093 WHAT IS THE DEVICE NUMBER FOR THE SECOND
     DEVICE CONTROLLER? [O] (70):


     094 WHAT IS THE DEVICE NUMBER FOR THE THIRD
     DEVICE CONTROLLER? [O] (71):


     095 WHAT IS THE DEVICE NUMBER FOR THE FOURTH
     DEVICE CONTROLLER? [0] (72):


     096 DO YOU WANT TO INCLUDE ANY USER TASKS IN THIS
     RTS/8 SYSTEM?  [Y/N] (N):Y

      ENTER THE NAMES OF YOUR TASKS FOLLOWED BY A
     CARRIAGE RETURN.  EXAMPLE:

     TASK 1:  NAME-1,M
     TASK 2:  NAME-2,M
	 .
	 .
	 .
     TASK N:  NAME-N,M

      M IS THE PARTITION WHERE THE TASK WILL RESIDE
     (ENTER ZERO OR NO ENTRY FOR THE MAIN LEVEL).
     YOU SHOULD ENTER THE TASKS TN THE ORDER OF
     DECREASING PRIORITY (THE FIRST ENTERED HAS THE HIGH-
     EST PRIORITY).  TERMINATE ENTRY BY TYPING A CARRIAGE
     RETURN (ONLY).
     (DOC. NO 301)

     TASK 001 ?:A,1


     TASK 002 ?:B,1


     TASK 003 ?:C,1


     TASK 004 ?:D,1


     TASK 005 ?:E,1


     TASK 006 ?:F,1
	 .
	 .
	 .
     TASK 099 ?:LH,5


				     3-15

			      TWO EXAMPLE SYSGENS


     TASK 100 ?:LI,6


     ERROR 120 SUM OF SYSTEM PLUS USER TASKS ALREADY 127 DECIMAL

     097 DO YOU WANT TO CHANGE ANY OF THE TASK'S
     PRIORITIES?  [Y/N] (N):Y

      THE WAY IN WHICH YOU CHANGE DEVICE PRIORITIES
     IS TO NAME THAT TASK WHICH WILL BE HIGHER IN
     PRIORITY THAN THE NEXT NAMED TASK, TAKEN A PAIR AT A
     TIME, AND DELIMITED BY A COMMA.


     EXAMPLE:

      PRIORITY CHANGE:  TASK-3, TASK-1
     PLACES TASK-3 HIGHER IN PRIORITY THAN
     TASK-1.  THE TASK ORDER WILL NOW BE TASK-3,
     TASK-1, TASK-2.  WHEN YOU FINISH CHANGING
     PRIORITIES, A CARRIAGE RETURN (ONLY) TERMINATES THE ENTRY.
     (DOC. NO 312)


      TYPE ? AND A CARRIAGE RETURN TO OBTAIN A LIST-
     ING OF THE CURRENT TASK PRIORITIES AFTER ANY
     PRIORITY PROMPT DURING THE RESPONSE TO THIS QUESTION
     (DOC. NO 244)

      PRIORITY CHANGE:?


     The following is a segment of the task priority list that was  printed
     on a line printer in response to a question mark.

     RTS8 BUILD PROGRAM
     TASK PRIORITY ASSIGNMENT

     TASK     PRIORITY
     PWRF    = 001
     CLOCK   = 002
     DTA     = 003
     CSA     = 004
     UDC     = 005
     RL01    = 006
     RF08    = 007
     DF32    = 010
     RK8     = 011
     RK8E    = 012
     RX8A    = 013
     RX8B    = 014
     RX8C    = 015
     RX8D    = 016
     LPT     = 017

				     3-16

			      TWO EXAMPLE SYSGENS


     EMT     = 020
     TTY     = 021
     TTY1    = 022
     TTY2    = 023
     TTY3    = 024
     TTY4    = 025
     SWAP    = 026
     CSAF    = 027
     OS8F    = 030
     MCR     = 031
     A       = 032
     B       = 033
     C       = 034
	  .
	  .
	  .
     SD      = 164
     LA      = 165
     LB      = 166
     LC      = 167
     LD      = 170
     LE      = 171
     LF      = 172
     LG      = 173
     LH      = 174
     EXIT    = 175
     BKT     = 176
     OS8     = 177


     PRIORITY CHANGE:AA,TTY


     PRIORITY CHANGE:AB,TTY


     PRIORITY CHANGE:AC,TTY


     PRIORITY CHANGE:AD,TTY


     PRIORITY CHANGE:LA,TTY


     PRIORITY CHANGE:?


     PRIORITY CHANGE:


     After several changes were made, another worksheet  was  obtained.   A
     segment of this listing is:


				     3-17

			      TWO EXAMPLE SYSGENS


     LPT     = 017
     EMT     = 020
     AA      = 021
     AB      = 022
     AC      = 023
     AD      = 024
     LA      = 025
     TTY     = 026
     TTY1    = 027


     098 DO YOU WANT TO CHANGE ANY TASK'S PARTITION
     ASSIGNMENT? [Y/N] (N):Y

      AT THIS POINT, YOU SPECIFY THE NAMES OF THE
     TASKS WHICH YOU WISH TO PLACE IN DIFFERENT
     PARTITIONS.  EXAMPLE:

     PARTITION :  TASK-1,M
     CAUSES TASK-1 TO BE PLACED IN PARTITION M.
     TYPE A ? AND A CARRIAGE RETURN TO OBTAIN A CURRENT
     LISTING OF PARTITION ALLOCATION
     A CARRIAGE RETURN (ONLY) TERMINATES THE ENTRY.
     (DO. NO 314)

     PARTITION :?


     In response to a question mark, the SYSGEN printed a  listing  of  the
     partitions  in which tasks reside.  The following is a segment of that
     list.


     RTS8 BUILD PROGRAM
     TASK PARTITION ALLOCATION

     TASK     PARTITION
     PWRF      0
     CLOCK     0
     DTA       0
     CSA       0
     UDC       0
     RL01      0
     RF08      0
     DF32      0
     RK8       0
     RK8E      0
     RX8A      0
     RX8B      0
     RX8C      0
     RX8D      0
     LPT       0
     EMT       0
     TTY       0

				     3-18

			      TWO EXAMPLE SYSGENS


     TTY1      0
     TTY2      0
     TTY3      0
     TTY4      0
     SWAP      0
     CSAF      0
     OS8F      0
     MCR       0
     Q	       0
     R	       0
     S	       0
     EXIT      0
     BKT       0
     OS8       0
     A	       1
     B	       1
     C	       1
     D	       1
	 .
	 .
	 .
     PC	       7
     PD	       7
     PE	       7
     PF	       7
     PG	       7
     PH	       7
     PI	       7


     PARTITION :MCR,6

     PARTITION :AA,3


     ERROR 203 NON-RESIDENT TASKS MAY NOT HAVE PRIORITY
     HIGHER THAN THE SWAP TASK.

      PARTITION :A,3


      PARTITION :B,4


      PARTITION :C,5


      PARTITION :D,6


      PARTITION :E,7


     ERROR 206 NO MORE THAN 16 ENTRIES PER PARTITION.

				     3-19

			      TWO EXAMPLE SYSGENS


      PARTITION :E,6


      PARTITION :


      THE QUESTION AND ANSWER SESSION IS COMPLETED.
     THE PROGRAM WILL CONTINUE ON TO
     PASS 2 (FILE BUILDING).

       PASS2 COMPLETED.  CHAINING TO BATCH AS REQUESTED.


      $JOB-MACREL TASK ASSEMBLY


     $MSG MOUNT TASK SOURCES ON RKB0:AND STRIKE ANY KEY TO CONTINUE

     The following is a partial listing of the parameter file  that  SYSGEN
     produces.

     PWRF=001
     CLOCK=002
     DTA=003
     CSA=004
     UDC=005
     RL01=00
     RF08=007
     DF32=010
     RK8=011
     RK8E=012
     RX8A=013
     RX8B=014
     RX8C=015
     RX8D=016
     LPT=017
     EMT=020
     AA=021
     AB=022
     AC=023
     AD=024
     LA=025
     TTY=026
     TTY1=027
     TTY2=030
     TTY3=031
     TTY4=032
     SWAP=033
     CSAF=034
     OS8F=035
     MCR=036
     A=037
     B=040
	 .

				     3-20

			      TWO EXAMPLE SYSGENS


	 .
	 .
     LB=166
     LC=167
     LD=170
     LE=171
     LF=172
     LG=173
     LH=174
     EXIT=175
     BKT=176
     OS8=177
     NTASKS=177
     MQ=1
     MQSV=1
     NFLDS=32.
     RTFLD=29.
     PWRFAL=1
     KL8A=3.
     KT8A=1
     OSFLDS=3.
     OSTTDV=04
     OSKBDV=03
     OSSYSD=RKBE
     OSFILL=0.
     OSBASE=30.
     BKTCDV=TTY
     MCRCLK=1
     MCRSYS=1
     MCRCDV=TTY
     CLKTYP=PDP8A
     SHERTZ=30.
     CLKQLN=128.
     CLKLRM=1
     RINGBF=12
     NCNTR=1
     NCNTC=2
     NAD=2
     FCTR=1000
     FCT=1040
     FAD=1100
     SYS=RK8E
     KBDEV=3
     TTDEV=4
     VT50=1
     SCOPE=1
     FILL=0
     WIDTH=80.
     TAB=1
     EMTCDV=TTY
     TTTIM=10.
     KL8ADV=40
     AC7776= CLL STA RAL
     AC7775= CLL STA RTL

				     3-21

			      TWO EXAMPLE SYSGENS


     AC4000= CLA STL RAR
     AC3777= CLL STA RAR
     AC2000= CLA STL RTR
     AC0002= CLA STL RTL
     AC5777= CLL STA RTR
     CAL=    JMS 20
     POSTDS=JMP I 24
     WAITM=  JMS l 25
     SEND=   0
     RECEIV=l
     WAITE=  2
     RUN=    3
     SUSPND=4
     POST=   5
     SKPINS=6
     DERAIL=7
     BLKARG=10
     SENDW=  11
     UNBARG=12
     RESCHD=13
     WAITX=  14
     FREE= 4000
     lFDEF UDC  <
     AO=0
     DO=0
     DI=2
     GC=3
     EC=4
     RC=5
     DC=6
     ECT=7
     CS=l0
     DCT=11
     AI=12>
     NONRWT=4000
     EFWT=   2000
     RUNWT=  1000
     SWPWT=  0400
     EORMWT=0200
     USERWT=0100
     ENABWT=0040
     MSGWT=  0020
     NETWT=  0010
     DNEWT=  0001
     NOPACK=4000
     NOCRLF=2000
     IND=1000
     NOLINE=400
     ASSGN=200
     KL8ALINE=100
     IFDEF CLOCK <
     MARKTIME=0
     SCHEDULE=1000
     TIMOUT=2000

				     3-22

			      TWO EXAMPLE SYSGENS


     PERIODICALLY=2000
     CANCEL=7000>
     IFNDEF OS8 <
     SLASHK=NFLDS-1>
     IFDEF OS8 <
     IFNDEF OSBASE <OSBASE=NFLDS-OSFLDS>
     IFZERO NFLDS-OSBASE-OSFLDS <SLASHK=NFLDS-OSFLDS>>
     IFNDEF BKTCDV <BKTCDV=0>
     IFNDEF  SUNIT <SUNIT= 0>
     HGHFLD=NFLDS-1
     HGHFLD=<<HGHFLD&7[10>+<HGHFLD&10%2>+<HGHFLD&20[4>>
     IFNDEF  PDP8E   <PDP8E=0>
     IFNDEF PDP8A    <PDP8A=0>
     IFNDEF  PDP12   <PDP12=0>
     IFNDEF VT78     <VT78=0>
     OMNI=PDP8E+PDP8A+VT78
     IFNDEF  EAESV   <EAESV=0>
     IFNDEF  EAE     <EAE=0>
     IFNDEF  MQSV    <MQSV=0>
     IFNDEF  MQ      <MQ=0>
     IFNDEF  PWRFAL  <PWRFAL=0>
     IFNDEF  KL8A    <KL8A=0>
     IFNDEF KT8A     <KT8A=0>
     IFNZRO EAESV    <MQSV=1>
     IFNZRO EAE      <MQ=1>
     IFZERO EAE      <EAESV=0>
     IFZERO MQ       <MQSV=0>
     IFDEF CLOCK     <
     IFNDEF CLKQLN   <CLKQLN=20>
     IFNDEF SHERTZ   <SHERTZ=12>
     IFNDEF CLKLRM   <CLKLRM=0>
     IFNDEF CLKTYP   <
     CLKTYP=3
     IFNZRO PDP8A    <CLKTYP=2>
     IFNZRO PDP12    <CLKTYP=0>
     IFNZRO PDP8E    <CLKTYP=0>
     >
     IFNZRO CLKTYP&1 <HERTZ=1750>
     IFZERO CLKTYP   <HERTZ=170>
     IFZERO CLKTYP-2 <HERTZ=144>
     IFNZRO HERTZ%SHERTZ[SHERTZ-HERTZ <_ERROR>
     IFZERO SHERTZ-301&4000 <_ERROR_>
     >
     IFNDEF RTFLD    <RTFLD=0>
     IFNZRO KT8A     <
     KTFLDS=40
     RACA=6175
     RACB=6176
     RACC=6177
     >
     EJECT




				     3-23

			      TWO EXAMPLE SYSGENS


     The SYSGEN also produced  four  floppy  control  files  and  four  TTY
     control files.


     TASK=RX8A
     RXDVCD=75
     .INCLUDE RKB0:RX.MA


     TASK=RX8B
     RXDVCD=70
     .INCLUDE RKB0:RX.MA


     TASK=RX8C
     RXDVCD=71
     .INCLUDE RKB0:RX.MA


     TASK=RX8D
     RXDVCD=72
     .INCLUDE RKB0:RX.MA


     TASK=TTY1
     TTDEV=6
     KBDEV=5
     FILL=10
     WIDTH=126.
     TTTIM=O.
     .INCLUDE RKB0:TTY.MA


     TASK=TTY2
     TTDEV=10
     KBDEV=7
     VT50=1
     SCOPE=1
     FILL=0
     WIDTH=80
     TAB= 1
     TTTIM=O.
     .INCLUDE RKB0:TTY.MA


     TASK=TTY3
     TTDEV=12
     KBDEV=11
     FILL=10
     WIDTH=128.
     TTTIM=10.
     .INCLUDE RKB0:TTY.MA



				     3-24

			      TWO EXAMPLE SYSGENS


     TASK=TTY4
     TTDEV=14
     KBDEV=13
     VT50=1
     SCOPE=1
     FILL=0
     WIDTH=80.
     TAB=1
     TTTIM=O.
     .INCLUDE RKB0:TTY.MA


     The following are excerpts from the MACREL and LINK batch  files.   In
     the  LINK  batch  file,  note the placement of the /O switches.  It is
     these switches that actually cause the  tasks  to  be  placed  into  a
     partition.   Note that the parameter file does not contain information
     on partition allocation.  This information exists only in this file.


     $JOB-MACREL TASK ASSEMBLY
     $MSG MOUNT TASK SOURCES ON RKB0:AND STRIKE ANY KEY TO CONTINUE
     .MAC RKA0:RTS8  ,LPT:RTS8 <SYS:PMINE,RKB0:RTS8  /B/C
     .MAC RKA0:PWRF,LPT:PWRF<SYS:PMINE,RKB0:PWRF/B/C
     .MAC RKA0:CLOCK,LPT:CLOCK<SYS:PMINE,RKB0:CLOCK/B/C
     .MAC RKA0:DTA,LPT:DTA<SYS:PMINE,RKB0:DTA/B/C
     .MAC RKA0:CSA,LPT:CSA<SYS:PMINE,RKB0:CSA/B/C
     .MAC RKA0:UDC,LPT:UDC<SYS:PMINE,RKB0:UDC/B/C
     .MAC RKA0:RL01,LPT:RL01<SYS:PMINE,RKB0:RL01/B/C
     .MAC RKA0:RF08,LPT:RF08<SYS:PMINE,RKB0:RF08/B/C
     .MAC RKA0:DF32,LPT:DF32<SYS:PMINE,RKB0:DF32/B/C
     .MAC RKA0:RK8,LPT:RK8<SYS:PMINE,RKB0:RK8/B/C
     .MAC RKA0:RK8E,LPT:RK8E<SYS:PMINE,RKB0:RK8E/B/C
     .MAC RKA0:RX8A,LPT:RX8A<SYS:PMINE,RKB0:RX8A/B/C
	 .
	 .
	 .
     .MAC RKA0:LE,LPT:LE<SYS:PMINE,RKB0:LE/B/C
     .MAC RKA0:LF,LPT:LF<SYS:PMINE,RKB0:LF/B/C
     .MAC RKA0:LG,LPT:LG<SYS:PMINE,RKB0:LG/B/C
     .MAC RKA0:LH,LPT:LH<SYS:PMINE,RKB0:LH/B/C
     .MAC RKA0:EXIT,LPT:EXIT<SYS:PMINE,RKB0:EXIT/B/C
     .MAC RKA0:OS8,LPT:OS8<SYS:PMINE,RKB0:OS8/B/C
     .SU SYS:LMINE.BI/T
     $END




     $JOB RTS8 MODULE LINKAGE
     .R LINK
     *RXA0:SMINE,LPT:SMINE</K=37/M/X
     *RKA0:RTS8
     *RKA0:PWRF
     *RKA0:CLOCK

				     3-25

			      TWO EXAMPLE SYSGENS


     *RKA0:DTA
     *RKA0:CSA
     *RKA0:UDC
     *RKA0:RL01
     *RKA0:RF08
     *RKA0:DF32
     *RKA0:RK8
     *RKA0:RK8E
     *RKA0:RX8A
     *RKA0:RX8B
     *RKA0:RX8C
     *RKA0:RX8D
     *RKA0:LPT
     *RKA0:TTY
     *RKA0:TTY1
     *RKA0:TTY2
     *RKA0:TTY3
     *RKA0:TTY4
     *RKA0:SWAP
     *RKA0:CSAF
     *RKA0:OS8F
     *RKA0:Q
     *RKA0:R
     *RKA0:S
     *RKA0:EXIT
     *RKA0:OS8
     */O
     *RKA0:F/C
     *RKA0:G/C
     *RKA0:H/C
     *RKA0:I/C
     *RKA0:J/C
     *RKA0:K/C
     *RKA0:L/C
     *RKA0:M/C
     *RKA0:N/C
     *RKA0:O/C
     *RKA0:P/C
     */O
     *RKA0:AA/C
     *RKA0:T/C
	 .
	 .
	 .
     *RKA0:ZB/C
     *RKA0:LE/C
     */O
     *RKA0:Y/C
     *RKA0:AF/C
     *RKA0:AM/C
     *RKA0:KF/C
     *RKA0:BE/C
     *RKA0:BF/C
     *RKA0:BG/C

				     3-26

			      TWO EXAMPLE SYSGENS


     *RKA0:PA/C
     *RKA0:PB/C
     *RKA0:PC/C
     *RKA0:PD/C
     *RKA0:PE/C
     *RKA0:PF/C
     *RKA0:PG/C
     *RKA0:PH/C
     *RKA0:PL/C
     *$
     $END












































				     3-27







				   CHAPTER 4

			     MODIFYING THE SYSGEN


     4.1  OVERVIEW

     This chapter describes how you make changes to the SYSGEN so  that  it
     can  more  precisely  meet  your  needs.   Although you may change the
     sources to the SYSGEN.SV program, DIGITAL does not recommend that  you
     proceed  in  that  manner.   Instead, DIGITAL recommends that you make
     changes in SCRIPT.MA.   (SCRIPT.MA  is  the  MACREL  source  file  for
     SCRIPT.SV, the file upon which SYSGEN operates.)

     The reason you modify the script is to reduce the potential for errors
     that can occur when a person unfamiliar with  the  SYSGEN  creates  an
     RTS/8 system.



     4.2  THE STRUCTURE OF SCRIPT.MA

     SCRIPT.MA contains the following sections.

	  1.  DATA FORMAT INFORMATION--comments that describe the SCRIPT.MA
	      record format.

	  2.  RECORD DIRECTORY--a table  that  SYSGEN  uses  when  locating
	      records.

	  3.  SCRIPT RECORDS--the script that  you  see  when  creating  an
	      RTS/8  system  as  well as conditional statements that SYSGEN
	      uses when branching over questions.

	  4.  PARAMETER RECORDS--the equates from which the SYSGEN  creates
	      the Parameter file.

	  5.  DEFAULT PARAMETERS--the  parameters  necessary  to  create  a
	      default RTS/8 system.

	  6.  SYSTEM PARAMETERS--a list of RTS/8 system equates  and  other
	      related information.

	  7.  TTY SKELETON CONTROL FILES--the framework  that  SYSGEN  uses
	      when creating TTY tasks.

	  8.  FLOPPY CONTROL SKELETON FILES--the framework that SYSGEN uses
	      when creating FLOPPY tasks.

	  9.  ERROR RECORDS--the records SYSGEN references when it  outputs
	      an error message.


				      4-1

			     MODIFYING THE SYSGEN


	 10.  PASS2  MESSAGES--the  messages  SYSGEN  prints  when  it   is
	      creating the output files.

	 11.  PASS2 MACREL BATCH RECORDS--the skeletal forms of the  MACREL
	      BATCH file.

	 12.  PASS2 LINKER BATCH MESSAGES--the skeletal forms of the LINKER
	      BATCH file.

	 13.  LIMIT CHECKING RECORDS--the numbers  that  the  SYSGEN  limit
	      checking  routine  uses  when  verifying  numerical  entries.
	      The following sections discuss these SCRIPT.MA elements.



     4.2.1  Record Directory

     This section describes the entry format for incorporating records into
     the  SCRIPT.MA  record  directory.   (Most of the records in SCRIPT.MA
     have a three-statement entry in the record directory.)

     ----------------------------------------------------------------------
     | The format of a record directory entry is:			  |
     |									  |
     |      N								  |
     |      MN								  |
     |      EDF     MN							  |
     |									  |
     | where:								  |
     |       N       is the record number.				  |
     |       MN      is the corresponding message number.		  |
     ----------------------------------------------------------------------

     The order of the entries in the record directory  corresponds  to  the
     order  in  which the SYSGEN asks questions or accesses records.  It is
     also the order in which SYSGEN accesses records when  it  creates  the
     PASS2  output  files.   (This order does not necessarily correspond to
     the order in which records exist in the script section of SCRIPT.MA.)

     Each record in SCRIPT.MA has a unique, fixed tag.  This  tag,  besides
     identifying  the  record and allowing SYSGEN to access the record, has
     the following meanings to the SYSGEN program.

     RECORD NUMBER	= script record
     RECORD NUMBER + 2000 = parameter   record   (corresponding   to    the
			    question)
     RECORD NUMBER + 3000 = limit record (limits on answers to questions if
			    any)

     The reason this relationship  exists  between  record  numbers  is  to
     facilitate  the  addition of new entries.  For example, if you were to
     add a question with the number 521,  you  would  add  the  appropriate
     parameter  at  2521,  and  the  limit  record  at  3521.  Because this


				      4-2

			     MODIFYING THE SYSGEN


     relationship exists, the SYSGEN requires  that every  record  you  add
     follow this scheme.

     The above record numbers  are  the  ones  you  use  when  manipulating
     SCRIPT.MA.   Other  record  numbers  also  have meaning to the system.
     However, the  relationship  between  the  script  question  and  other
     records are not as distinct.  Ordinarily, you should not add or delete
     information that has the following numbers.


     1000 = error messages and special tags
     4000 = reserved for future use
     5000 = PASS2 messages and control file records
     6000 = LINKER parameter (used for building LINKER batch file)
     7000 = MACREL parameter (used for building MACREL batch file)


     The SYSGEN generally uses Records n777 where  n  equals  1,2,...,7  to
     delimit  the  different script sections and you should not use them as
     record numbers.



     4.2.2  Script Records

     The Script Records section contains  all  questions  that  the  SYSGEN
     prints.   These questions are in approximately the order in which they
     appear during a SYSGEN.  However, it is not important where you  place
     them  within  this section because the SYSGEN references them by their
     tag.

     ----------------------------------------------------------------------
     | The general format of a script question is:			  |
     |									  |
     | MN,     TEXT    "WYYY SCRIPT [X] (z)"				  |
     |									  |
     | where:								  |
     |       N      is the record number.				  |
     |       MN     is the corresponding message number			  |
     |       W      is the record type and may be			  |
     |			 A:  ASCII response				  |
     |			 D:  a decimal response				  |
     |			 N:  a null record (ignored)			  |
     |			 O:  an octal response				  |
     |			 Y:  a Yes/No response				  |
     |       YYY    is a user question number (initially equal to N;      |
     |		    overwritten by a dynamically generated number when    |
     |		    printed on a terminal).				  |
     |       X      is the expected answer type.			  |
     |       Z      is the default answer.				  |
     |       SCRIPT is the text of the question.			  |
     ----------------------------------------------------------------------



				      4-3

			     MODIFYING THE SYSGEN


     The above general format is for one line questions.  If  the  question
     requires more than one line, the format is

     MN,     TEXT    "WYYY SCRIPT"<215><212>
	     TEXT    "SCRIPT"<215><212>
	     .
	     .
	     TEXT    "SCRIPT [X] (z)"

     In this format, the <215><212> string tells MACREL to print a carriage
     return/line  feed  when  it  prints a line of text.  If you omit these
     characters, SYSGEN will not print any lines of  the  record  following
     the  omission.   Also,  if  the  last  line  of  a  record  contains a
     <215><212>, the SYSGEN cannot find the  end  of  the  text.   If  this
     occurs,  the  next  record  becomes  part  of  the text of the current
     record.

     The maximum length of any script record text is 384 characters.

     When you are creating a record, you only have to use the  record  type
     indicator  to tell the SYSGEN which of its internal routines it should
     use when processing an answer.  For example, if you  create  a  record
     that begins


     M521,   TEXT    "0521...


     The SYSGEN uses its octal routines.  Likewise


     M521,   TEXT    "A521...


     tells the SYSGEN to process an ASCII answer.

     You must be careful that the number YYY that you select is  unique  in
     the  system.   You select this number, which must be in the range 0 to
     577, from a cross-reference listing of the  assembled  SCRIPT.MA.   If
     the  number is not in the cross-reference listing, it is available for
     your use. (This number is the octal tag that MACREL references when it
     assembles  SCRIPT.   It is also the means by which the SYSGEN accesses
     individual records.) Generally,  the  numbers  from  360  to  577  are
     available.   (Other  record numbers can become available if you delete
     existing script records.   See  Section  4.3.1  for  a  discussion  of
     deleting records.)

     In addition to the record types described above, several other  record
     types also exist.  A second major record type is the remark or R type.
     A remark is the text that the SYSGEN prints when you type  a  question
     mark as the answer to a question.

     The SYSGEN requires that the record following a question be a  remark.
     (Following  means  that it is the next record pointed to in the record

				      4-4

			     MODIFYING THE SYSGEN


     directory.  It does not mean the next sequential record in the  script
     section.) The SYSGEN automatically skips over the record unless a user
     types a question mark in response to a SYSGEN question.  When the user
     types a question mark, the SYSGEN accesses this record.

     ----------------------------------------------------------------------
     | The format of an R record is:					  |
     |									  |
     | MN,   TEXT    "RYYY SCRIPT"<215><212>				  |
     |       TEXT    "SCRIPT"<215><212>					  |
     |       .								  |
     |       .								  |
     |       .								  |
     |       TEXT    "SCRIPT"						  |
     |									  |
     | where:								  |
     |       R      indicates that the record is a remark.		  |
     |       SCRIPT is the text of the remark.				  |
     ----------------------------------------------------------------------

     A remark can contain up to 384 (decimal) characters.  Note that  every
     line  except  the  last  in  a  record  contains  the character string
     <215><212>.  This string tells MACREL to type a  carriage  return/line
     feed  at that point.  If you omit this string on an intermediate line,
     the SYSGEN does not print all lines past the omission.  If you include
     a <215><212> on the last line of a record's script, the SYSGEN assumes
     (erroneously) that the next record is also part of the text.

     For example, if you add a question that asks if the SYSGEN user wishes
     to  include  a  task  named  MYOWN, you might add the following to the
     script:


     M400, TEXT "Y400 DO YOU WANT TASK 'MYOWN'? [Y/N] (Y):"


     As  stated  above,  SYSGEN  requires  that  all   questions   have   a
     corresponding remark.  The remark to this question might be:

     M401,   TEXT    "R401 DO NOT INCLUDE THIS TASK IN THE"<215><212>
		     "SYSTEM UNLESS YOU USE DECTAPES."


     If the SYSGEN should print this question before the question that asks
     if  the user wants the LINCtape driver, you should physically enter it
     there.  (Entering questions and remarks in the  order  in  which  they
     appear  is  good  programming practice as it aids debugging.  However,
     the SYSGEN does not require you to  enter  questions  and  remarks  in
     order.)  You  then  enter the record number into the record directory.
     The segment of the record directory would look as follows:





				      4-5

			     MODIFYING THE SYSGEN


	     400	     /ADDED QUESTION
	     M400
	     EDF    M400

	     401	     /ADDED REMARK
	     M401
	     EDF    M401

	     133	     /LINCTAPE QUESTION
	     M133
	     EDF    M133

     (See the discussion of the Parameter File  for  information  regarding
     how the SYSGEN records the answer to a question.)

     The only complication that can occur when adding questions is that the
     SYSGEN  branches  over  questions.   This  means  that if you insert a
     question in a section of SCRIPT that the SYSGEN branches over, it  may
     not  print  the  questions  you  add to the script.  (See below, for a
     discussion of conditional records.) Section 4.3.2 presents  the  exact
     procedure that you should follow in inserting questions.

     Always include the default answer, enclosed within parentheses,  in  a
     script  question.   Omitting  the  default  answer is a fatal run-time
     error.

     When  you  select  the  default  answer,  the  SYSGEN   examines   the
     information  between  the  parentheses.  It then uses that information
     as the answer to the question.  If you wish to change the  default  of
     any  question,  you  need  to  change only the information between the
     parentheses.  For example, if, when  creating  an  RTS/8  system,  you
     normally want assembly listings, you would change the question


     M333,   TEXT    "Y333 DO YOU WANT ASSEMBLY LISTINGS? [Y/N] (N):"
								 |
								 |
     to								 |
								 |
								 v
     M333,   TEXT    "Y333 DO YOU WANT ASSEMBLY LISTINGS? [Y/N] (Y):"


     You do not have to include the SYSGEN answer  type  prompts  that  are
     enclosed  within  square  brackets.  However, it is good documentation
     practice to include them.

     When you are entering questions, you may find it desirable  to  branch
     around  questions  that  are  irrelevant because of a previous answer.
     Thus, you may include  conditional  records  that  operate  upon  your
     previous  answers  to  A, O, D, or Y (alphanumeric, octal, decimal, or
     yes/no, respectively) records.



				      4-6

			     MODIFYING THE SYSGEN


     ----------------------------------------------------------------------
     | The format for conditionals is:					  |
     |									  |
     | MN,   TEXT    "IA,N1,N2,ARG"					  |
     |									  |
     | where:								  |
     |       I      designates the record as a conditional		  |
     |       A      is the type of conditional such that		  |
     |			 Z:  answer equals zero				  |
     |			 P:  answer not equal to zero			  |
     |			 E:  answer equals ARG				  |
     |			 N:  answer not equal to ARG			  |
     |			 G:  answer greater than ARG			  |
     |			 L:  answer less than ARG			  |
     |			 S:  answer true,  set  no  source  (there  is  a |
     |			     priority assignment but no source code)      |
     |       N1     is the record whose answer is being tested		  |
     |       N2     is the record number to which the program will branch |
     |		    if the conditional test is true.			  |
     |       ARG    is any octal number (from  0-7777)  and  is  required |
     |		    after E, N, G, and L				  |
     ----------------------------------------------------------------------

     In this format, I is the record type and A is the subtype.

     If N1 equals N2 the program branches to the  previous  record  (normal
     branching is toward the end of the script table).

     A yes/no answer has a value of 1 and 0 respectively.

     The SYSGEN allows you to  use  record  numbers  600  through  776  for
     conditionals  and  remarks  because  these  record  types do not write
     entries into SYSGEN tables.  (Note that the examples in  this  chapter
     do  not  follow  this convention.  This is because the SYSGEN does not
     require you to use  the  600  through  776  numbers  for  remarks  and
     conditionals.)

     If you enter a question with a 600  through  677  record  number,  the
     SYSGEN  executes  the  question  correctly.  However, DIGITAL reserves
     these numbers for future expansion;  if you use them, future  releases
     of the SYSGEN may require you to redo your script.

     Record numbers 700 through 777 are reserved for listing  switches  and
     control  file  entries.   The  SYSGEN uses these numbers to store your
     answers to TTY and floppy questions.  If you enter questions which use
     these  numbers  and  your target system uses more than one terminal or
     has floppies, you will be using the same  numbers  for  two  different
     entries.   If  this  occurs,  the  RTS/8  system  you  create executes
     improperly.

     Conditionals and remarks can use these numbers  because  they  do  not
     store answers.



				      4-7

			     MODIFYING THE SYSGEN


     In the example presented above, the remark suggested  that  you  would
     not  include  the  task  MYOWN  in  the  system  if you did not have a
     DECtape.  By using a conditional, you could direct the SYSGEN to  skip
     this  question  if  you  answered  NO  to  the  DECtape question.  The
     conditional you would add, after checking the cross-reference  listing
     for an available number, might be


     I402,   TEXT    "IZ133,134"     /133 IS DECTAPE, 134 IS LINCTAPE


     It is also  permissible  to  branch  to  a  second  conditional.   For
     example,  if you also did not want to ask the LINCtape question if the
     target machine was not a PDP 12 (as is done in the script)  you  could
     instead enter:


     I402,   TEXT    "IZ133,345"


     Statement 345 is


     I345,   TEXT    "IZ044,134"     /044 REFERS TO PDP-12 WHICH IS
				     /THE MACHINE THAT USES LINCTAPE


     The following is how  the  record  directory  would  look  after  this
     change.


	     132	     /THIS IS THE DECTAPE QUESTION
	     M132
	     EDF     M132

	     073	     /THIS IS THE DECTAPE REMARK
	     M073
	     EDF     M073

	     402	     /THIS IS CONDITIONAL BRANCH
	     I402	     /OVER ADDED QUESTION
	     EDF     I402

	     400	     /THIS IS ADDED TASK QUESTION
	     M400
	     EDF     M400

	     401	     /THIS IS ADDED TASK REMARK
	     M401
	     EDF     M401

	     345	     /THIS IS CONDITIONAL AROUND
	     I345	     /LINCTAPE QUESTION
	     EDF     I345

				      4-8

			     MODIFYING THE SYSGEN


     You must place a three-word entry into the record directory  for  each
     record you incorporate into SCRIPT.MA.

     Because the SYSGEN can branch over records, you must insure  that  you
     do  not  place  your  questions where the SYSGEN will access them only
     when a user specifies a certain task or  combination  of  tasks.   The
     following are three places where this problem does not arise:

	  o  Before all DIGITAL single statement task questions

	  o  After all DIGITAL single statement task questions

	  o  Before the question asking if you wish to include user tasks

     If you place records at other positions, you may inadvertently  branch
     over your question unless you change branch targets.


		  ------------------- NOTE -------------------
		  |					     |
		  | One  other  record   type   exists:    T |
		  | records.   These T records direct SYSGEN |
		  | to  execute   special   DIGITAL-supplied |
		  | processing  subroutines  at  that point. |
		  --------------------------------------------

     Removing questions that  you  do  not  need  is  simpler  than  adding
     questions.   Because the SYSGEN uses only records listed in the record
     directory,  you  can  comment  out  the  question's  record  directory
     entries.  (You comment out a line by placing a slash before the line.)
     There is no need even to remove the question or comment it out in  the
     script.   If  a record is not in the record directory, the SYSGEN will
     not print it.  (DIGITAL recommends that you  leave  questions  in  the
     script  rather  than remove them in case your requirements change.) In
     addition, if you remove a question, you must also  remove  the  remark
     associated with the question.

     You must perform one other action when you delete  questions.   It  is
     possible  that  a conditional record uses the record you are deleting.
     To locate these conditional records, use a  text  editor  with  search
     capabilities (such as TECO or EDIT) to look for other instances of the
     record number.  The conditional record can use a record number in  two
     ways.

	  1.  If the record number indicates an answer that the SYSGEN must
	      compare to the branch type, you should remove the conditional
	      from the system.  In most cases,  if  the  conditional  skips
	      over a record, you probably do not need the record or records
	      being skipped over.

	  2.  If the record indicates the target of a  conditional  branch,
	      you  must  change the target.  Normally, the target should be
	      the next sequential record in the record directory (excluding
	      remarks).

				      4-9

			     MODIFYING THE SYSGEN



     4.2.3  Parameter Records

     The configuration, system tasks,  multiple  parameters  for  a  single
     task, and symbol table equates reside in the Parameter Records section
     of SCRIPT.MA.

     ----------------------------------------------------------------------
     | Each statement in this section is of the form:			  |
     |									  |
     | M2N,  TEXT    "EQUATE"						  |
     |									  |
     | where:								  |
     |       N      is the message number.				  |
     |       EQUATE is the symbol that MACREL uses  when  assembling  the |
     |		    RTS/8 system.					  |
     ----------------------------------------------------------------------

     This section of SCRIPT.MA contains the following subsections.

	  1.  Hardware configuration parameters

	  2.  System tasks in priority order

	  3.  Multiple parameter equates

	  4.  Default parameters

	  5.  System parameters

	  6.  Task and nonresident macros

     The numbers in this section and the numbers  you  use  in  the  script
     section  correspond  directly;   that  is,  the message number in this
     section is the message number in the script + 2000.  For example,  the
     task  equate  you  would add for the question in the previous examples
     would be


     M2400,  TEXT    "MYOWN="


     (You would place this equate into Section 2 of  the  parameter  file.)
     When the SYSGEN processes Section 2 of the parameter file, it sets the
     equates and writes it to the output file.  If the equate  is  not  set
     (that  is,  the answer is false), the SYSGEN ignores the record.  This
     number is the task's priority.

     The order in which you enter a task's equate in this  section  of  the
     parameter  file  helps  determine  a  task's  priority.   (The  SYSGEN
     determines a system task's priority by its initial  placement  in  the
     parameter file.)



				     4-10

			     MODIFYING THE SYSGEN


     If you change the task's priority (in response to a SYSGEN  question),
     the placement of this equate is in the task order and not the order in
     which you place it in the parameter file.

     When you add a question such as the one described above to the SYSGEN,
     the  task  is  now a system task.  In other words, the SYSGEN formally
     differentiates user tasks and system tasks.  That is, a user task is a
     task  that becomes part of the RTS/8 system because of a user response
     to the question that asks which additional tasks you wish  to  include
     in  the  system.   A system task, on the other hand, is a task that is
     part of the configuration of the system and the SYSGEN asks  questions
     about the particular task.

     When you receive the SYSGEN, it included only  DIGITAL  system  tasks.
     However,  when  you add questions that ask about other tasks, you have
     added system tasks.

     In  the  case  of  the  configuration  parameters  and  the   multiple
     parameters,  the  SYSGEN writes an equate to the output parameter file
     only if it places information after the equals sign.  If it  does  not
     place information after the equals sign, it ignores the equate.

     Section 5 of the parameter  list  consists  of  general  RTS/8  system
     equates.   These equates become part of every RTS/8 system unless they
     are within a conditional assembly.  For example, the  RTS/8  Executive
     Request  mnemonics  are always part of the RTS/8 system.  However, the
     SYSGEN includes the UDC equates only if a user selects the UDC.

     You do not need to include record numbers for equates you add in  this
     section  because  the SYSGEN automatically uses all records from label
     P1001 through label D1001.

     The examples in the previous sections illustrated how you add a single
     task  to  the  system.   In these examples, you only needed to add the
     equate MYOWN= to  the  parameter  file  task  section  and  place  the
     equate's  tag in the record directory.  In some cases, you may wish to
     add equates that direct MACREL to  assemble  portions  of  the  source
     code.    Section  4.3.2  illustrates  how  you  add  such  equates  to
     SCRIPT.MA.

     Section 4 of the parameter list is a  conditional  assembly  that  the
     SYSGEN  uses  for  a  default  system.   You  may make changes in this
     section to alter the default system.  Specifically, you may delete the
     tasks listed here and/or add DIGITAL and user tasks.  If the tasks you
     create have multiple  equates,  you  may  also  add  them  within  the
     conditional  assembly.   You  do not need to include record numbers in
     this section because the SYSGEN automatically includes everything from
     label M1000 to label P1001.

     If you change the default, you must also alter the default MACREL  and
     LINKER BATCH files so that the SYSGEN properly creates the new default
     system.  The default MACREL file begins at record 7004.   The  default
     LINKER  file  begins  at  record 6006.  Section 4.3.3 is an example of
     changing this default.

				     4-11

			     MODIFYING THE SYSGEN


     The last part of this section consists of the sources for the TASK and
     NONRES  macros  that all tasks use.  You should not alter these macros
     in any way.



     4.2.4  Skeleton Records

     The next two sections consists of  the  skeleton  files  for  the  TTY
     drivers  and floppy controllers.  You should not make modifications to
     these files.  If you do, the MACREL assembler will create  tasks  that
     execute improperly.



     4.2.5  Error Message Records

     The SYSGEN references all error messages by their record number.   The
     record  number  preceding  the  error  message is not coordinated with
     specific questions.  Instead, SYSGEN routines return the error message
     record number.  Other SYSGEN routines then locate the record number in
     the error directory.  Unless you incorporate your  own  error-handling
     routines, you should not make alterations in this section.



     4.2.6  LINK and MACREL BATCH Records

     These sections are each divided  into  two  parts.   The  first  is  a
     skeleton  for  default  systems.   If you change the default, you must
     change the default LINK and MACREL BATCH  records.   You  change  this
     section  only to explicitly name tasks that you wish to include in the
     default or delete a task that you no longer wish to  be  part  of  the
     default.  See Section 4.3.3 for more information.

     The second is a more generalized  skeleton  for  non-default  systems.
     You must not make modifications in these records because the number of
     characters in each record is important.  The SYSGEN creates the  BATCH
     file  by  substituting characters into the skeletons.  It also assumes
     that certain characters exist in certain places in the  skeleton.   If
     you  change  the  displacement into the skeleton, SYSGEN creates BATCH
     files that execute indeterminately.

     The only user modification that is normally feasible in these sections
     is  adding  additional  switches.  If you add switches, you must place
     them at the end of the record.



     4.2.7  Limit Records

     Every question the SYSGEN asks that requires a numerical  answer  must
     have  a limit record.  The SYSGEN checks this record to insure that an
     answer is neither less than nor greater than certain values.

				     4-12

			     MODIFYING THE SYSGEN


     ----------------------------------------------------------------------
     |									  |
     | The format for a limit record is:				  |
     |									  |
     | M3N,  TEXT    "L3N LOW,HIGH"					  |
     |									  |
     | where:								  |
     |       M3N    is the record tag.					  |
     |       N      is the record number.				  |
     |       L      is the designator for a limit record.		  |
     |       LOW    is the lowest value that the  question's  answer  can |
     |		    be.							  |
     |       HIGH   is the highest value that the question's  answer  can |
     |		    be.							  |
     ----------------------------------------------------------------------

     In the limit records, you type the limits in  the  same  base  as  the
     answer.   For  example, a decimal question has the limits expressed in
     decimal and an octal question in octal.  The SYSGEN automatically uses
     an  octal  or  decimal  processing  routine;  the record type (D or O)
     tells SYSGEN which routines to use.

     You must include the limit record's  record  number  into  the  record
     directory.

     If you wish to change  the  limits  on  any  question  for  a  DIGITAL
     supplied task, you can alter the number in this section.

     See Section 4.3.2 for examples of incorporating limit records.



     4.3  EXAMPLES

     This section demonstrates four possible changes you may wish  to  make
     in the SYSGEN.  The changes are:

	  o  Deleting questions

	  o  Adding questions

	  o  Changing the default

	  o  Adding additional TTY handlers



     4.3.1  Deleting Questions

     Because DIGITAL must provide a system  generation  procedure  that  is
     useful  to a wide range of users, the SYSGEN asks questions concerning
     a large number of devices.  This  example  shows  how  to  change  the
     SYSGEN  so  that  it does not ask questions about the following tasks:
     power fail, clock, UDC, RF08 disk,  DF32  disk,  RK8  disk,  LINCtape,

				     4-13

			     MODIFYING THE SYSGEN


     DECtape,  and  cassettes.   It  also shows how to eliminate the PDP 12
     question.

     To eliminate these questions, look up the record number in the  script
     portion  of  the  directory.   The  following list presents the record
     numbers and the associated system remark.


			     Question	      Remark
			      Number	      Number			      ______	      ______

	     Power Fail		074		073
	     Clock		075		073
	     UDC		125		073
	     RF08		126		073
	     DF32		127		073
	     RK8		130		073
	     DECtape		132		073
	     LINCtape		133		073
	     Cassette		150		073
	     Cass. File Sup.	151		073
	     Test		160		073
	     Exit		161		073

	     PDP 12		044		042


     The first action you take is to  comment  out  these  records  in  the
     record  directory.  The second step is to use the question number in a
     TECO or EDIT search either to eliminate or  change  conditionals  that
     may  use  the  answers  to  these  deleted  questions.   The following
     conditionals were found.

	  604
	  705
	  713
	  720
	  727
	  736
	  740
	  741
	  742
	  772

     Because this system does not include the Power Fail Task, it  is  also
     no  longer  necessary  to  ask  if  the  target  system has power fail
     hardware. The power fail question is number  061  and  its  remark  is
     062.   When  searching  through  the script for related numbers, it is
     noted that you must remove all clock and UDC questions.  These records
     are





				     4-14

			     MODIFYING THE SYSGEN


	     Clock	     216
			     217     220
			     221     222
			     346     347
			     223     224
			     350     351

	     UDC	     225
			     226     227
			     230     231
			     232     231
			     233     231
			     234     235
			     236     235
			     237     235

     Other records to omit are

	     MCR	     206     207

	     PDP 12	     343

     When these changes were made in SCRIPT.MA, these record  numbers  were
     commented  out in the record directory.  The questions themselves were
     left in the script.

     The following is an example of  portions  of  the  dialogue  that  the
     SYSGEN now prints.


     023 DO YOU WANT ANY OF THE DEC- PROVIDED
     SYSTEM TASKS IN YOUR RTS/8 SYSTEM? [Y/N] (Y):


      EACH DEC TASK WILL BE:  LISTED ONE AT A
     TIME.  IF YOU WISH TO INCLUDE THE TASK IN YOUR
     SYSTEM, TYPE Y.  IF NOT, TYPE N.  IF THE
     SYSTEM PROGRAM REQUIRES MORE INFORMATION
     ABOUT A TASK, IT WILL ASK THE QUESTIONS
     IN ANOTHER SECTION.
     (DOC NO 073)

     024 RK8E DISK DRIVER? [Y/N] (N):


     025  RL01 DISK DRIVER? [Y/N] (N):


     026 FIRST FLOPPY CONTROLLER?  [Y/N] (N):Y


     027 SECOND FLOPPY CONTROLLER?  [Y/N] (N):



				     4-15

			     MODIFYING THE SYSGEN


     028 LINE PRINTER DRIVER?  [Y/N] (N):


     029 TELETYPE DRIVER?  [Y/N] (Y):


     030 EMERGENCY BREAKTHROUGH TASK? [Y/N] (N):


     031 SWAPPER TASK? [Y/N]  (N):


     032 OS/8 FILE SUPPORT TASK?  [Y/N] (N):


     033 MONITOR CONSOLE ROUTINE?  [Y/N] (Y):


     034 OS/8 SUPPORT TASK?  [Y/N] (N):


      THIS SECTION PRESENTS THE PARAMETERS
     REQUIRED TO SPECIFY THE MCR TASK
     WHICH YOU HAVE SELECTED.
     (DOC NO 205)

     035 DO YOU WANT THE MCR SYSTEM STATUS
     REPORT CAPABILITY?  [Y/N] (Y):


     036 WHICH TERMINAL WILL THE MCR TASK
     USE?  [A] (TTY):


     This example shows a partial listing of a system generation.  In  this
     listing,  you  should  compare  the  tasks that the SYSGEN prints with
     those that the SYSGEN prints if you  had  not  removed  the  question.
     (See Chapter 3 for a listing of the order in which the SYSGEN normally
     prints questions.)

     When deciding whether or not to remove questions, you must  weigh  the
     convenience  of  leaving  the SYSGEN as DIGITAL distributes it against
     the possible errors that can occur if a user inadvertently includes a
     task that should not be part of the RTS/8 system.

     In general, the SYSGEN dialogue is sufficiently fast that the  time  a
     user  saves  by  seeing fewer questions should not be a factor in your
     decision.  The only factor should be a potential for fewer errors when
     creating systems.






				     4-16

			     MODIFYING THE SYSGEN


     4.3.2  Adding Questions

     The preceding example demonstrated how you delete  questions.   Before
     you  add  questions, you should ask yourself a similar question;  that
     is, do you believe that adding  questions  to  incorporate  new  tasks
     improves  the  SYSGEN  process? It is usually simpler to supply a task
     name in response to a SYSGEN question than to add questions   so  that
     the SYSGEN explicitly asks whether a user wishes to include a task.

     When adding questions you must do the following:

	  1.  Write the question and the associated remark.

	  2.  Consult a cross-reference listing of SCRIPT.MA  to  determine
	      which record numbers are available.

	  3.  Assign the record numbers to specific records.

	  4.  Write the conditional records (if any) that the  question  or
	      questions require.

	  5.  Write  the  task  equates  and  task  parameters  that   your
	      insertion requires.  The record number you use is the same as
	      you used in 3) except you preface it with a 2.

	  6.  Write the limit records.  The record number is  the  same  as
	      you  used in 3) except that you add 1000 to the number.  Note
	      that only octal and decimal records have limit records.

	  7.  Determine where the question or questions  should  appear  in
	      the SYSGEN.

	  8.  Examine the record directory at the point where you  wish  to
	      insert   the   records.    Carefully   check to  insure  that
	      conditional records, prefaced with  the  letter  "I"  in  the
	      directory,  do  not  branch  over  the  question.  (Using the
	      letter "I"  is  a  convention  that  allows  you  to  quickly
	      identify  branch  records.   It  is  not mandatory to do so.)
	      Because the SYSGEN branches over questions it does  not  need
	      to  ask,  you  must  be careful that you do not branch over a
	      question you add because of an answer to a question  that  is
	      unimportant to your system.

	  9.  Insert the record numbers  in the  record  directory.   These
	      insertions  occur in three places:  where the question should
	      be asked, where the parameter file record exists,  and  where
	      the  limit  record section exists.  If you omit the parameter
	      or limit records, the SYSGEN may detect a fatal error.  If it
	      does,  it  prints  an  error  message and returns to the OS/8
	      Monitor.

	 10.  Type the records themselves.  It is usually wisest  to  place
	      them where they logically belong due to normal question flow.
	      However, the SYSGEN only requires that you place them in  the

				     4-17

			     MODIFYING THE SYSGEN


	      proper  section of SCRIPT because it references them by their
	      tag, not their physical placement.

	 11.  Use MACREL to create the .RB image.

	 12.  Use LINK to create the .SV image.  The name you give to  this
	      file must be SCRIPT.SV.  Your command string should be of the
	      form

		    .R LINK
		    *SCRIPT[,filespec]<SCRIPT/M/K=37$

	      where:

		     filespec is an optional listing device or file.

	      Carefully examine the load map against a  load  map  for  the
	      most recent version of SCRIPT.  Make sure that your questions
	      do not  cause  an  overflow  in  one  of  the  DSECTS.   (The
	      following  example  includes  a  listing  of the load map for
	      SCRIPT.SV as DIGITAL distributes it and  a  second  load  map
	      for the version of SCRIPT created for the following example.)

	 13.  You may now run using the new script in place of the old.

	 14.  Examine the Parameter, MACREL, and LINK files  built  by  the
	      new SYSGEN to make sure that they are correct.

     The following example illustrates  the  insertion  of  a  sequence  of
     questions.   For  the  purposes of this example, it was assumed that a
     user created a transaction processing task.  The function of this task
     is to receive messages from terminals in the system, process them in a
     way that is not material to this example, and add the information to a
     data base.  Optional parts of the task specify where information is to
     be written in case of overflow, how often  the  data  base  should  be
     backed up, and other similar information.

     A script was written and appropriate branch records included.

     After looking in a cross-reference listing, it was found that all  400
     record numbers were available.


	    .DSECT SCRT05
	    FIELD 5

     M400,  TEXT   "Y400 DO YOU WANT THE TRANSACTION PROCESSING"<215><212>
	    TEXT   "TASK? [Y/N] (Y):"

     M401,  TEXT   "R401 YOU INCLUDE THIS TASK IF YOU WANT REAL-"<2l5><2l2>
	    TEXT   "TIME UPDATING OF YOUR DATA BASE."


     I402,  TEXT   "IZ400,735"	     /GO TO MCR IF NO TO M400

				     4-18

			     MODIFYING THE SYSGEN


     M403,  TEXT   "D403 HOW MANY TERMINALS WILL BE USING THE"<215><212>
	    TEXT   "TRANSACTION TASK? [D] (2):"

     M404,  TEXT   "R404 THE ANSWER YOU SPECIFY HERE SHOULD BE"<215><212>
	    TEXT   "LESS THAN OR EQUAL TO THE NUMBER OF TERMINALS"<215><212>
	    TEXT   "YOU SPECIFY IN THE TELETYPE DRIVER QUESTION."

     M405,  TEXT   "A405 WHAT IS THE I/O DEVICE WHICH THE TRANS-"<215><212>
	    TEXT   "ACTION TASK USES? [A] (RL0B):"

     M406,  TEXT   "R406 THIS DEVICE SHOULD HAVE A LARGE AMOUNT OF"
			<215><212>
	    TEXT   "STORAGE.  IN MOST CASES, A FLOPPY IS UNACCEP-"<215><212>
	    TEXT   "TABLE AND YOU SHOULD USE AN RK8E OR RL01."

     M407,  TEXT   "Y407 IS THERE AN OVERFLOW DEVICE? [Y/N] (N):"

     M410,  TEXT   "R410 IF THE SYSTEM WILL PROCESS MORE THAN 300"<215><212>
	    TEXT   "TRANSACTIONS AN HOUR, YOU SHOULD PROVIDE A "<215><212>
	    TEXT   "DEVICE SO THAT TRANSACTIONS ARE NOT LOST."

     I411,  TEXT   "IZ407,414"	           /SKIP OVERFLOW DEV OUES

     M412,  TEXT   "A412 WHAT IS THE OVERFLOW DEVICE? [A] (RL0C):"

     M413,  TEXT   "R413 THE SPACE FOR OVERFLOW CAN BE MUCH SMALLER"
			<215><2l2>
	    TEXT   "THAT THE PRIMARY DEVICE, YOU MAY USE A FLOPPY"<215><212>
	    TEXT   "FOR THE OVERFLOW."

     M414,  TEXT   "Y414 DO YOU WANT TO BACKUP THE TRANSACTION STORAGE"
			<215><212>
	    TEXT   "DEVICE? [Y/N] (Y):"

     M415,  TEXT   "R415 YOU BACK UP THE DEVICE SO THAT IF THERE IS A"
			<215><212>
	    TEXT   "SYSTEM FAILURE, YOU HAVE THE MAJORITY OF RECENT"
			<2l5><212>
	    TEXT   "TRANSACTIONS ON FILE."

     I416,  TEXT   "IZ414,735"	     /IF NO, GO TO MCR OUES

     M417,  TEXT   "A417 WHAT IS THE BACKUP STORAGE DEVICE [A] (RL1A):"

     M420,  TEXT   "R420 THIS DEVICE SHOULD HAVE THE SAME STORAGE"<215><212>
	    TEXT   "CAPACITY AS THE DEVICE UPON WHICH YOU STORE THE"
			<215><212>
	    TEXT   "TRANSACTION FILE."

     I421,  TEXT   "I7407,427"	           /IF NO OVERFLOW, GO TO HOW
					   /OFTEN DO YOU BACKUP
     M422,  TEXT   "Y422 DO YOU WANT OVERFLOW STORAGE FOR THE BACKUP"
			<215><212>
	    TEXT   "DEVICE? [Y/N] (Y):"

				     4-19

			     MODIFYING THE SYSGEN


     M423,  TEXT   "R423 YOU SHOULD PROVIDE OVERFLOW STORAGE IF THE"
			<215><2l2>
	    TEXT   "TRANSACTION DEVICE HAS OVERFLOW."

     I424,  TEXT   "IZ422,427"	           /IF NO, GO TO HOW OFTEN BACK UP
					   /DO YOU BACKUP

     M425,  TEXT   "A425 WHAT IS THE BACK UP OVERFLOW DEVICE? [A] (RL1C):"

     M426,  TEXT   "R426 YOU SHOULD INCLUDE BACKUP STORAGE THAT HAS"
			<2l5><212
	    TEXT   "CAPACTITY AS THE TRANSACTION BACKUP DEVICE."

     M427,  TEXT   "Y427 DO YOU WANT TO BACK UP THE TRANSACTION DEVICE"
			<215><212
	    TEXT   "AFTER A FIXED NUMBER OF TRANSACTIONS? [Y/N] (Y):"

     M430,  TEXT   "R430 IF YOU BACK UP THE DEVICE AFTER A FIXED NUMBER"
			<215><212>
	    TEXT   "OF TRANSACTIONS, THIS IS THE MAXIMUM NUMBER OF TRANS "
			<215><212
	    TEXT   "THAT CAN BE LOST IF THERE IS A SYSTEM FAILURE."

     I431,  TEXT   "IZ427,435"	           /GO TO BACK UP BY TIME

     M432,  TEXT   "D432 AFTER HOW MANY TRANSACTIONS SHOULD THE BACKUP"
			<215><212>
	    TEXT   "ROUTINE BEGIN WRITING THE INFORMATION ON THE TRANS-"
			<215><212>
	    TEXT   "ACTION DEVICE TO AUXILLIARY STORAGE? [D] (50):"

     M433,  TEXT   "R433 THE RANGE FOR THIS ANSWER IS 16 THROUGH 1023."

     I434,  TEXT   "IZ427,440"	           /SKIP NEXT IF ANSWER TO PREVIOUS


     M435,  TEXT   "R435 SINCE YOU DID NOT WANT BACKUP TO PROCEED AFTER"
			<215><212>
	    TEXT   "FIXED NUMBER OF TRANSACTIONS, YOU MUST SPECIFY THE"
			<215><2l2>
	    TEXT   "INTERVAL AT WHICH BACK UP WILL OCCUR."

     M436,  TEXT   "D436 THE INTERVAL IS? [D] (600):"

     M437,  TEXT   "R377 THE LIMITS ON YOUR ANSWER ARE 32 TO 1023,"
			 <215><212>
	    TEXT   "WHEN YOU CHOSE THIS OPTION, YOU ARE USUALLY"<215~<212>
	    TEXT   "ASKING FOR BACKUP TO OCCUR MORE OFTEN THAN IT"<215><212>
	    TEXT   "OCCURS BY THE NUMBER OF TRANSACTIONS."
     M440,  TEXT   "Y440 DO YOU WANT TO STORE TRANSACTIONS THAT"<215><212>
	    TEXT   "OCCUR WHILE BACKING UP IS GOING ON? [Y/N] (N):"




				     4-20

			     MODIFYING THE SYSGEN


     M441,  TEXT   "R441 THIS OPTION PROVIDES FOR MAXIMUM RECOVERY"
			<215><212>
	    TEXT   "IF THERE IS A SYSTEM FAILURE.  HOWEVER, THIS"<215><212>
	    TEXT   "PROCEDURE WILL STEAL TIME AND THUS SLOW DOWN"<215><212>
	    TEXT   "RESPONSE TIME AT USER TERMINALS."

     I442,  TEXT   "IZ440,735"

     M443,  TEXT   "A443 WHAT IS THE DEVICE TO WHICH THESE TRANSACTIONS"
			<215><212>
	    TEXT   "SHOULD BE WRITTEN? [A] (RL1B):"

     M444,  TEXT   "R444 THIS SHOULD BE A VERY FAST I/O DEVICE TO MIN-"
			<215><212>
	    TEXT   "THE TIME NECESSARY TO STORE THE INFORMATION."




     The task and other equates were written.  The equates were:

	     M2403,  TEXT    "BACKUP="      /TASK EQUATES
	     M2405,  TEXT    "TRANS="

	     M2412,  TEXT    "TRNTTY="      /PARAMETERS TO
	     M2417,  TEXT    "TRNDEV="      /PASS TO SOURCE
	     M2425,  TEXT    "BKDEV="       /FILES
	     M2432,  TEXT    "BKTRNS="
	     M2436,  TEXT    "BKTIME="
	     M2443,  TEXT    "BKINTR="

     The following limit records were written.

	     M3412,  TEXT    "L3412 001,005"
	     M3432,  TEXT    "L3432 016,1023"
	     M3436,  TEXT    "L3436 032,1023"


     The point where this task was to be located was immediately before the
     multiple MCR questions.

     After  examining  SCRIPT.MA,  it  was   found   that   the   following
     conditionals had to be changed.


	     I733,   TEXT    "IZ162,735"
	     I755,   TEXT    "IZ321,735"


     The text was typed.

     SCRIPT.MA was assembled and linked.  The following is the load map for
     the DIGITAL-supplied SCRIPT.MA.


				     4-21

			     MODIFYING THE SYSGEN


      OS/8   LINKER V 2A   LOAD MAP      16-OCT-78

     SECTION  ADDR    SIZE  ENTRY    ADDR    ENTRY    ADDR

     SCRT01   10000   3106
     SCRT02   20000   7350
     SCRT03   30000   7312
     SCRT04   40000   6320
     SCRT05   50000   4706
     SCRT06   60000   7464
     SCRT07   70000   5770
     SCRT10  100000   2244
     SCRT11  110000   0170
     SCRT12  120000   0662
     SCRT13  130000   0246
     SCRT14  140000   0442

     PROGRAM ENTRY:   00200
     JOB STATUS WORD: 0000



     The following is the new load map.  (Note that DSECT 5 was split  into
     two parts, DSECT 5 and DSECT 15.)


     .R LINK
     *SCRIPT,TTY:<SCRP2/M/K=37
     *$

      OS/8   LINKER V 2A   LOAD MAP      16-OCT-78

     SECTION  ADDR    SIZE  ENTRY    ADDR    ENTRY    ADDR

     SCRT01   10000   3334
     SCRT02   20000   7350
     SCRT03   30000   7312
     SCRT04   40000   6310
     SCRT05   50000   3720
     SCRT06   60000   7464
     SCRT07   70000   6064
     SCRT10  100000   2244
     SCRT11  110000   0170
     SCRT12  120000   0662
     SCRT13  130000   0246
     SCRT14  140000   0500
     SCRT15  150000   4716

     PROGRAM ENTRY:   00200
     JOB STATUS WORD: 0000





				     4-22

			     MODIFYING THE SYSGEN


     The SYSGEN was run.  The following text shows these questions as typed
     on  a  terminal.   Note  the two displays.  The first checks out every
     branch that the SYSGEN can take in a question.  Note  also  that  each
     remark  is  printed.  DIGITAL recommends that when you add changes you
     do them a segment at a time so that you can expeditiously verify  that
     the modified script is working.

     The second version is one pass through the dialogue  to  determine  if
     that works as hoped for.



     042 OS/8 SUPPORT TASK? [Y/N] (N):


     043 NULL JOB? [Y/N] (N):


     044 DO YOU WANT THE TRANSACTION PROCESSING
     TASK? [Y/N] (Y):


     045 HOW MANY TERMINALS WILL BE USING THE
     TRANSACTION TASK? [D] (2):51


     ERROR 202 NUMERICAL ANSWER NOT WITHIN SPECIFIED LIMITS

     045 HOW MANY TERMINALS WILL BE USING THE
     TRANSACTION TASK? [D] (2):?


      THE ANSWER YOU SPECIFY HERE SHOULD BE
     LESS THAN OR EQUAL TO THE NUMBER OF TERMINALS
     YOU SPECIFY IN THE TELETYPE DRIVER QUESTION.

     045 HOW MANY TERMINALS WILL BE USING THE
     TRANSACTION TASK? [D] (2):#44


     044 DO YOU WANT THE TRANSACTION PROCESSING
     TASK? [Y/N] (Y):N


      THIS SECTION PRESENTS THE PARAMETERS
     REQUIRED TO SPECIFY THE MCR TASK
     WHICH YOU HAVE SELECTED.
     (DOC. NO 205)


     045 DO YOU WANT THE MCR SYSTEM STATUS
     REPORT CAPABILITY? [Y/N] (Y):#44



				     4-23

			     MODIFYING THE SYSGEN


     044 DO YOU WANT THE TRANSACTION PROCESSING
     TASK? [Y/N] (Y):?


      YOU INCLUDE THIS TASK IF YOU WANT REAL-
     TIME UPDATING OF YOUR DATA BASE.

     044 DO YOU WANT THE TRANSACTION PROCESSING
     TASK? [Y/N] (Y):


     045 HOW MANY TERMINALS WILL BE USING THE
     TRANSACTION TASK? [D] (2):4


      THE ANSWER YOU SPECIFY HERE SHOULD BE
     LESS THAN OR EQUAL TO THE NUMBER OF TERMINALS
     YOU SPECIFY IN THE TELETYPE DRIVER QUESTION.

     045 HOW MANY TERMINALS WILL BE USING THE
     TRANSACTION TASK? [D] (2):4


     046 WHAT IS THE I/O DEVICE WHICH THE TRANS-
     ACTION TASK USES? [A] (RL0B):?


      THIS DEVICE SHOULD HAVE A LARGE AMOUNT OF
     STORAGE.  IN MOST CASES, A FLOPPY IS UNACCEP-
     TABLE AND YOU SHOULD USE AN RK8E OR RL01.

     046 WHAT IS THE I/0 DEVICE WHICH THE TRANS-
     ACTION TASK USES? [A] (RL0B):


     047 IS THERE AN OVERFLOW DEVICE? [Y/N] (N):N


     048 DO YOU WANT TO BACKUP THE TRANSACTION STORAGE
     DEVICE? [Y/N] (Y):#47


     047 IS THERE AN OVERFLOW DEVICE? [Y/N] (N):?


      IF THE SYSTEM WILL PROCESS MORE THAN 300
     TRANSACTIONS AN HOUR, YOU SHOULD PROVIDE AN
     DEVICE SO THAT TRANSACTIONS ARE NOT LOST.

     047 IS THERE AN OVERFLOW DEVICE? [Y/N] (N):Y


     048 WHAT IS THE OVERFLOW DEVICE? [A] (RL0C):?


				     4-24

			     MODIFYING THE SYSGEN


      THE SPACE FOR OVERFLOW CAN BE MUCH SMALLER
     THAN THE PRIMARY DEVICE.  YOU MAY USE A FLOPPY
     FOR THE OVERFLOW.

     048 WHAT IS THE OVERFLOW DEVICE? [A] (RL0C):


     049 DO YOU WANT TO BACKUP THE TRANSACTION STORAGE
     DEVICE? [Y/N] (Y):?


      YOU BACK UP THE DEVICE SO THAT IF THERE IS A
     SYSTEM FAILURE, YOU HAVE THE MAJORITY OF RECENT
     TRANSACTIONS ON FILE.

     049 DO YOU WANT TO BACKUP THE TRANSACTION STORAGE
     DEVICE? [Y/N] (Y):N


      THIS SECTION PRESENTS THE PARAMETERS
     REQUIRED TO SPECIFY THE MCR TASK
     WHICH YOU HAVE SPECIFIED.
     (DOC. NO 205)


     050 DO YOU WANT THE MCR SYSTEM STATUS
     REPORT CAPABILITY? [Y/N] (Y):#49


     049 DO YOU WANT TO BACKUP THE TRANSACTION STORAGE
     DEVICE? [Y/N] (Y):N


     050 WHAT IS THE BACKUP STORAGE DEVICE [A] (RL1A):?


      THIS DEVICE SHOULD HAVE THE SAME STORAGE
     CAPACITY AS THE DEVICE UPON WHICH YOU STORE THE
     TRANSACTION FILE.

     050 WHAT IS THE BACKUP STORAGE DEVICE [A] (RL1A):


     051 DO YOU WANT OVERFLOW STORAGE FOR THE BACKUP
     DEVICE? [Y/N] (Y):?


      YOU SHOULD PROVIDE OVERFLOW STORAGE IF THE
     TRANSACTION DEVICE HAS OVERFLOW.

     051 DO YOU WANT OVERFLOW STORAGE FOR THE BACKUP
     DEVICE? [Y/N] (Y):N



				     4-25

			     MODIFYING THE SYSGEN


     052 DO YOU WANT TO BACKUP THE TRANSACTION DEVICE
     AFTER A FIXED NUMBER OF TRANSACTIONS? [Y/N] (Y):#51


     051 DO YOU WANT OVERFLOW STORAGE FOR THE BACKUP
     DEVICE? [Y/N] (Y):


     052 WHAT IS THE BACKUP OVERFLOW DEVICE? [A] (RL1C):?


      YOU SHOULD INCLUDE BACKUP STORAGE THAT HAS
     CAPACTITY AS THE TRANSACTION BACKUP DEVICE.

     052 WHAT IS THE BACKUP OVERFLOW DEVICE? [A] (RL1C):


     053 DO YOU WANT TO BACKUP THE TRANSACTION DEVICE
     AFTER A FIXED NUMBER OF TRANSACTIONS? [Y/N] (Y):?


      IF YOU BACKUP THE DEVICE AFTER A FIXED NUMBER
     OF TRANSACTIONS, THIS IS THE MAXIMUM NUMBER OF TRANS-
     THAT CAN BE LOST IF THERE IS A SYSTEM FAILURE.

     053 DO YOU WANT TO BACKUP THE TRANSACTION DEVICE
     AFTER A FIXED NUMBER OF TRANSACTIONS? [Y/N] (Y):


     054 AFTER HOW MANY TRANSACTIONS SHOULD THE BACKUP
     ROUTINE BEGIN WRITING THE INFORMATION ON THE TRANS-
     ACTION DEVICE TO AUXILLIARY STORAGE? [D] (50):?


     THE RANGE FOR THIS ANSWER IS 16 THROUGH 1023.

     054 AFTER HOW MANY TRANSACTIONS SHOULD THE BACKUP
     ROUTINE BEGIN WRITING THE INFORMATION ON THE TRANS-
     ACTION DEVICE TO AUXILLIARY STORAGE? [D] (50):300


     055 DO YOU WANT TO STORE TRANSACTIONS THAT
     OCCUR WHILE BACKING UP IS GOING ON? [Y/N] (N):#53

     053 DO YOU WANT TO BACKUP THE TRANSACTION DEVICE AFTER
     FIXED NUMBER OF TRANSACTIONS? [Y/N] (Y):N


      SINCE YOU DID NOT WANT BACKUP TO PROCEED AFTER
     FIXED NUMBER OF TRANSACTIONS, YOU MUST SPECIFY THE
     INTERVAL AT WHICH BACKUP WILL  OCCUR.

     054 THE INTERVAL IS? [D] (600):?


				     4-26

			     MODIFYING THE SYSGEN


      THE LIMIT ON YOUR ANSWER ARE 32 TO 1023.
     WHEN YOU CHOSE THIS OPTION, YOU ARE USUALLY
     ASKING FOR BACKUP TO OCCUR MORE OFTEN THAN IT
     OCCURS BY THE NUMBER OF TRANSACTIONS.

     054 THE INTERVAL IS? [D] (600):1000


     055 DO YOU WANT TO STORE TRANSACTIONS THAT
     OCCUR WHILE BACKING UP IS GOING ON? [Y/N] (N):?


      THIS OPTION PROVIDES FOR MAXIMUM RECOVERY
     IF THERE IS A SYSTEM FAILURE.  HOWEVER, THIS
     PROCEDURE WILL STEAL TIME AND THUS SLOW DOWN
     RESPONSE TIME AT USER TERMINALS.

     055 DO YOU WANT TO STORE TRANSACTIONS THAT
     OCCUR WHILE BACKING UP IS GOING ON? [Y/N] (N):N


      THIS SECTION PRESENTS THE PARAMETERS
     REQUIRED TO SPECIFY THE MCR TASK
     WHICH YOU HAVE SELECTED
     (DOC. NO 205)

     056 DO YOU WANT THE MCR SYSTEM STATUS
     REPORT CAPABILITY?  [Y/N] (Y):#55

     054 DO YOU WANT THE OS/8 BACKGROUND TASK TO RUN IN
     THE HIGHEST AVAILABLE FIELDS? [Y/N] (Y):


     055 DO YOU WANT THE TRANSACTION PROCESSING
     TASK? [Y/N] (Y):


     056 HOW MANY TERMINALS WILL BE USING THE
     TRANSACTION TASK? [D] (2):


     057 WHAT IS THE I/O DEVICE WHICH THE
     TRANSACTION TASK USES? [A] (RL0B):


     058 IS THERE AN OVERFLOW DEVICE? [Y/N] (N):


     059 DO YOU WANT TO BACKUP THE TRANSACTION STORAGE
     DEVICE? [Y/N] (Y):


     060 WHAT IS THE BACKUP STORAGE DEVICE [A] (RL1A):


				     4-27

			     MODIFYING THE SYSGEN


     061 DO YOU WANT TO BACKUP THE TRANSACTION DEVICE
     AFTER A FIXED NUMBER OF TRANSACTIONS? [Y/N] (Y):N


      SINCE YOU DID NOT WANT BACKUP TO PROCEED AFTER
     FIXED NUMBER OF TRANSACTIONS,  YOU MUST SPECIFY THE
     INTERVAL AT WHICH BACKUP WILL OCCUR.

     062 THE INTERVAL IS? [D] (600):1000


     063 DO YOU WANT TO STORE TRANSACTIONS THAT
     OCCUR WHILE BACKING UP IS GOING ON? [Y/N] (N):Y


     064 WHAT IS THE DEVICE TO WHICH THESE TRANSACTIONS
     SHOULD BE WRITTEN? [A] (RL1B):


      THIS SECTION PRESENTS THE PARAMETERS
     REQUIRED TO SPECIFY THE MCR TASK
     WHICH YOU HAVE SELECTED.
     (DOC. NO 205)

     065 DO YOU WANT TIME-OF-DAY FACILITY IN
     YOUR MCR TASK? [Y/N] (Y):



     The last verification step is to check the parameter, MACREL, and LINK
     files to insure that the sysgen is recording information properly.


		  ------------------- NOTE -------------------
		  |					     |
		  | Because this transaction task  does  not |
		  | really exist, no attempt was made to run |
		  | the MACREL  and  LINK  files  so  as  to |
		  | actually create an RTS/8 system.	     |
		  --------------------------------------------

     PWRF=001
     CLOCK=002
     DTA=003
     CSA=004
     UDC=005
     BACKUP=006
     TRANS=007
     RL01=010
     RF08=011
     DF32=012
     RK8=013
     RK8E=014
     RX8A=015

				     4-28

			     MODIFYING THE SYSGEN


     RX8B=016
     RX8C=017
     RX8D=020
     LPT=021
     EMT=022
     TTY=023
     TTY1=024
     TTY2=025
     TTY3=026
     SWAP=027
     CSAF=030
     OS8F=031
     MCR=032
     TEST=033
     EXIT=034
     BKT=035
     OS8=036
     NULL8A=037
     NTASKS=037
     PDP8A=1
     EAE=1
     EAESV=1
     NFLDS=4.
     RTFLD=0.
     PWRFAL=1
     KL8A=2.
     KT8A=1
     OSFLDS=2.
     OSTTDV=04
     OSKBDV=03
     OSSYSD=RK8E
     OSFILL=0.
     BKTCDV=TTY
     MCRCLK=1
     MCRSYS=1
     MCRCDV=TTY
     SHERTZ=10.
     CLKQLN=16.
     RINGBF=12
     NCNTR=1
     NCNTC=2
     NAD=2
     FCTR=1
     FCT=1
     FAD=1
     SYS=RK8E
     KBDEV=3
     TTDEV=4
     VT50=1
     SCOPE=1
     FILL=0
     WIDTH=80.
     TAB=1


				     4-29

			     MODIFYING THE SYSGEN


     EMTCDV=TTY
     TTTIM=0.
     TRNTTY=4.
     TRNDEV=RL0B
     BKDEV=RL1A
     BKTIME=1000.
     BKINTR=RL1B
     KL8ADV=40

     $JOB-MACREL TASK ASSEMBLY
     $MSG MOUNT TASK SOURCES ON SYS:AND STRIKE ANY KEY TO CONTINUE
     .MAC SYS:RTS8 <SYS:PDEFLT,SYS:RTS8
     .MAC SYS:PWRF<SYS:PDEFLT,SYS:PWRF
     .MAC SYS:CLOCK<SYS:PDEFLT,SYS:CLOCK
     .MAC SYS:DTA<SYS:PDEFLT,SYS:DTA
     .MAC SYS:CSA<SYS:PDEFLT,SYS:CSA
     .MAC SYS:UDC<SYS:PDEFLT,SYS:UDC
     .MAC SYS:BACKUP<SYS:PDEFLT,SYS:BACKUP
     .MAC SYS:TRANS<SYS:PDEFLT,SYS:TRANS
     .MAC SYS:RL01<SYS:PDEFLT,SYS:RL01
     .MAC SYS:RF08<SYS:PDEFLT,SYS:RF08
     .MAC SYS:DF32<SYS:PDEFLT,SYS:DF32
     .MAC SYS:RK8<SYS:PDEFLT,SYS:RK8
     .MAC SYS:RK8E<SYS:PDEFLT,SYS:RK8E
     .MAC SYS:RX8A<SYS:PDEFLT,SYS:RX8A
     .MAC SYS:RX8B<SYS:PDEFLT,SYS:RX8B
     .MAC SYS:RX8C<SYS:PDEFLT,SYS:RX8C
     .MAC SYS:RX8D<SYS:PDEFLT,SYS:RX8D
     .MAC SYS:LPT<SYS:PDEFLT,SYS:LPT
     .MAC SYS:TTY<SYS:PDEFLT,SYS:TTY
     .MAC SYS:TTYl<SYS:PDEFLT,SYS:TTY1
     .MAC SYS:TTY2<SYS:PDEFLT,SYS:TTY2
     .MAC SYS:TTY3<SYS:PDEFLT,SYS:TTY3
     .MAC SYS:SWAP<SYS:PDEFLT,SYS:SWAP
     .MAC SYS:CSAF<SYS:PDEFLT,SYS:CSAF
     .MAC SYS:OS8F<SYS:PDEFLT,SYS:OS8F
     .MAC SYS:MCR<SYS:PDEFLT,SYS:MCR
     .MAC SYS:TEST<SYS:PDEFLT,SYS:TEST
     .MAC SYS:EXIT<SYS:PDEFLT,SYS:EXIT
     .MAC SYS:OS8<SYS:PDEFLT,SYS:OS8
     .MAC SYS:NULL8A<SYS:PDEFLT,SYS:NULL8A
     .SU SYS:LDEFLT.BI/T
     $END

     $JOB RTS8 MODULE LINKAGE
     .R LINK
     $SYS:SDEFLT</K=02/M/X
     *SYS:RTS8
     *SYS:PWRF
     *SYS:CLOCK
     *SYS:DTA
     *SYS:CSA
     *SYS:UDC
     *SYS:BACKUP

				     4-30

			     MODIFYING THE SYSGEN


     *SYS:TRANS
     *SYS:RL01
     *SYS:RF08
     *SYS:DF32
     *SYS:RK8
     *SYS:RK8E
     *SYS:RX8A
     *SYS:RX8B
     *SYS:RX8C
     *SYS:RX8D
     *SYS:LPT
     *SYS:TTY
     *SYS:TTYl
     *SYS:TTY2
     *SYS:TTY3
     *SYS:SWAP
     *SYS:CSAF
     *SYS:OS8F
     *SYS:MCR
     *SYS:TEST
     *SYS:EXIT
     *SYS:OS8
     *SYS:NULL8A
     */O
     */O
     */O
     */O
     */O
     */O
     */O
     *$
     .RU SYS:SDEFLT
     $END


     You may achieve  many  of  the  same  results  more  simply  by  using
     conditional  assembly  statements.   For example, you could ask if the
     system will include the transaction task.  If the system will  include
     this  task,  your  next  question could be for the user to specify the
     kind of transaction task.  The answer could be a number that specifies
     the  equates necessary for the transaction task.  By using conditional
     assembly statements, you could check for each numerical value.   Using
     this  procedure,  you could create the above transaction task with two
     questions rather than the number used here.



     4.3.3  Changing the Default

     The RTS/8 default procedure allows a user to create a system with  the
     minimum  amount   of effort.  When creating a default system, the user
     has only to specify where the SYSGEN is to write files,  where  source
     files  reside,  and  other similar information.  For a default system,


				     4-31

			     MODIFYING THE SYSGEN


     the SYSGEN uses prespecified  equates  and  explicitly  listed  output
     files.

     The procedure for creating a new default system is as follows

	  1.  Change the default equate  listing  in  the  parameter  file.
	      This  listing  begins  at  record  number M1000.  The records
	      following this number do not have record  numbers.   Instead,
	      the  SYSGEN  writes  all  information  within the conditional
	      assembly statement to the output parameter  file.   You  may,
	      therefore, insert any equate you wish within the conditional.
	      Then, if a user selects the default, the  SYSGEN  writes  the
	      entire conditional to the output file.

	      Note that the equate NTASK (meaning "number  of  tasks")  has
	      been  set  to  10 (octal).  This means that you may insert an
	      additional two tasks before you change this number.   If  you
	      insert  more than two, you must make this number greater than
	      or equal to the number of tasks in the system.  Also, you may
	      need  to  increase  the NFLD (number of fields) equate if the
	      default is a large system.

	      You may, of course, delete any  of  the  equates  that  exist
	      within the conditional in the DIGITAL-supplied SCRIPT.MA.

	  2.  If the system has tasks  other  than  those  in  the  DIGITAL
	      default,  you must explicitly name these files for the MACREL
	      batch file.  Beginning at record number M7004 is  a  list  of
	      the tasks that are part of the default.

	      The records you add must have the same  physical  spacing  as
	      the  records  in  the  DIGITAL  default.   The "X" characters
	      represent null characters that the SYSGEN replaces with  your
	      answer  to  a  question.   (Each "X" represents one character
	      position that SYSGEN assumes  will  exist.)  Also,  you  must
	      enter  a  six-character task name.  A shorter name is a fatal
	      error.  If your task name contains less than six  characters,
	      you  must  pad  it with trailing spaces so that the task name
	      occupies six characters.  Each task name occurs  three  times
	      on each line.

	      If you add a new record to the default, you must include  the
	      record number in the record directory.

	  3.  You must create a LINK batch file in much the same way as the
	      MACREL batch file.  The records for this file begin at record
	      M6006.  All records you enter must have the same form as that
	      of  the  DIGITAL  default  (including  the  leading "X" place
	      holder for the device specification.) For these records,  the
	      name need not be six characters long.

	      If you add new records, you must include the record number in
	      the record directory.


				     4-32

			     MODIFYING THE SYSGEN


     After you make the changes discussed in the preceding list, reassemble
     and  relink SCRIPT.MA.  The file that LINK produces must have the name
     SCRIPT.SV or the SYSGEN cannot run.

     The following example is a small modification of the  DIGITAL  default
     to  incorporate  the  transaction  task  that  was  the example in the
     previous section.

     The changes that were made to SCRIPT.MA are

	  1.  Remark number M017 was updated to reflect  the  new  default.
	      This  change  is not necessary but should be made so that the
	      remark best reflects the current SYSGEN.

	  2.  The TEST task was deleted from the default and TRANS (for the
	      transaction  task)  was  added.   (The  task  priority number
	      immediately following the task name  was  not  changed.   You
	      may,  of  course,  make any changes you like to this priority
	      number.)

	  3.  The equate TRNDEV (for the transaction device) was included.

	  4.  The TEST task was removed from the MACREL batch file and  the
	      transaction task substituted.

	  5.  The TEST task was removed from the LINK batch  file  and  the
	      transaction task substituted.

     The following listings show a segment of the new SYSGEN dialogue  that
     incorporates  the  changed  dialogue,  the  section  of  the SCRIPT.MA
     parameter file that shows the new default conditional, the new  MACREL
     batch file, and the new LINK batch file.

     012 DO YOU WISH TO BUILD AN RTS/8 SYSTEM WITHOUT
     SPECIFYING ANY PARAMETERS? [Y/N] (N):?

      IF YOU ANSWER YES TO THIS QUESTION THE
     RTS/8 BUILD PROGRAM GOES TO PASS 2 AND
     CREATES A SYSTEM THAT INCLUDES A TTY TASK,
     MONITOR CONSOLE ROUTINE, TRANSACTION,
     TASK, A CLOCK ROUTINE, AND AN EXIT
     TASK.
     (DOC. NO 017)

     012 DO YOU WISH TO BUILD AN RTS/S SYSTEM WITHOUT
     SPECIFYING ANY PARAMETERS? [Y/N] (N):Y


      THE QUESTION AND ANSWER SESSION IS
     COMPLETED.  A DEFAULT SYSTEM IS NOW BEING
     PRODUCED.

       PASS2 COMPLETED.  CHAINING TO BATCH AS REQUESTED.


				     4-33

			     MODIFYING THE SYSGEN


     DFLT=1
     IFDEF   DFLT<
     TTY=2
     MCR=3
     TRANS=4
     EXIT=6
     CLOCK=1
     NTASKS=10
     KL8A=0
     NFLDS=2
     TRNDEV=RL1B
     MQ=0
     MQSV=0>
     PDP8A=1
     AC7776= CLL STA RAL
     AC7775= CLL STA RTL


     $JOB-MACREL TASK ASSEMBLY
     $MSG MOUNT TASK SOURCES ON SYS:AND STRIKE ANY KEY TO CONTINUE
     .MAC SYS:RTS8  <SYS:PDEFLT,SYS:RTS8
     .MAC SYS:TTY   <SYS:PDEFLT,SYS:TTY
     .MAC SYS:MCR   <SYS:PDEFLT,SYS:MCR
     .MAC SYS:TRANS <SYS:PDEFLT,SYS:TRANS
     .MAC SYS:CLOCK <SYS:PDEFLT,SYS:CLOCK
     .MAC SYS:EXIT  <SYS:PDEFLT,SYS:EXIT
     .SU SYS:LDEFLT.BI/T
     $END


     $JOB RTS8 MODULE LINKAGE
     .R LINK
     *SYS:SDEFLT</K=0l/M/X
     *SYS:RTS8
     *SYS:TTY
     $SYS:MCR
     *SYS:TRANS
     *SYS:EXIT
     *SYS:CLOCK
     *$
     .RU SYS:SDEFLT
     $END



     4.3.4  Multiple TTY Systems

     As DIGITAL distributes the SYSGEN, you can create only five TTY tasks.
     If  your  system  requires  more  than five, you can use the following
     procedure to include as many TTY tasks as your memory can contain.

     When you request the SYSGEN to create  more  than  one  TTY  task,  it
     writes a control file for each task other than the first.  The control
     file skeleton is as follows:

				     4-34

			     MODIFYING THE SYSGEN


	     TASK=TTYn       /WHERE n REPRESENTS THE TTY FILE NAME
	     TTDEV=	     /PRINTER DEVICE CODE
	     KBDEV=	     /KEYBOARD DEVICE CODE
	     VT50=	     /1 ENABLE CTRL/S AND CTRL/Q
	     SCOPE=	     /1 MEANS TTY CAN DO A BACKSPACE
	     FILL=	     /NUMBER OF FILL CHARACTERS
	     WIDTH	     /TTY LINE WIDTH
	     TAB=	     /1 IF TTY HAS HARDWARE TABS
	     TTIM=	     /TTY READ TIMEOUT PARAMETER
	     .INCLUDE dev:TTY.MA
			     /dev: IS WHERE TTY.MA RESIDES


     In this skeleton,

	     TASK=TTYn

     relates a specific task name to the parameter file.  Consequently, you
     may  include  as  many  of  these files as are necessary on the device
     where source files reside.  Then, when you  are  running  the  SYSGEN,
     include these files as user tasks.

     You can create these files in two ways.  The  first  procedure  is  to
     create  them  using  a text editor.  Add the appropriate values to the
     right side of each equate, delete equates that  are  not  relevant  to
     your  system,  and  enter  the  device name where TTY.MA resides.  You
     would then give this file a name such as  TTY6.MA.   By  passing  this
     file through a text editor, you may create as many TTY source files as
     your system requires.  When you  create  the  files  in  this  manner,
     however,  the  contents of the TTY control files are static;  that is,
     they are not created during the SYSGEN process.

     The second procedure is to create the TTY  control  files  during  the
     SYSGEN.   This  procedure  requires  that  you run the SYSGEN at least
     twice. The first times that you run the SYSGEN, you  create  an  RTS/8
     system that uses only TTY tasks.  In this way, you can create four TTY
     control files each time you pass through the SYSGEN.  For example,  if
     your  target  system uses twelve terminals, you would pass through the
     SYSGEN three times.  The first pass creates  four  files,  the  second
     three, and the third five.

     After each SYSGEN pass, run each TTY task through a text editor.   For
     example,  if  your target system uses six terminals, you would run the
     SYSGEN, creating two TTY tasks (the first is TTY.MA and  is  the  same
     for  each  pass).   If your text editor were TECO, you would issue the
     following instructions


	     TECO outdev:TTY5.MA<indev:TTYl.MA
	     *FSTTY1$TTY5$		     !REPLACE TTY1 WITH TTY5!
	     EX$$			     !RETURN TO MONITOR!




				     4-35

			     MODIFYING THE SYSGEN


     You then run the SYSGEN creating the RTS/8 system.   When  the  SYSGEN
     asks if you wish to include any user tasks, you include TTY6.

     If you ask for a task priority listing in the next question  that  the
     SYSGEN  prints,  you  will  find that it prints the five TTY tasks you
     entered, possibly followed by several DIGITAL tasks.  These tasks  can
     be  SWAP,  CSAF,  OS8F,  and the MCR.  Following the MCR are your user
     tasks. Consequently, you may wish to change the priority  of  TTY5  so
     that it follows TTY4.

     The following example illustrates adding four TTY tasks  to  an  RTS/8
     system.   The  first  path through the SYSGEN created four TTY control
     files, named TTY1.MA, TTY2.MA, TTY3.MA, and  TTY4.MA.   Using  a  text
     editor,  as  discussed above, the appropriate changes were made.  When
     TECO wrote the  output  files,  their  names  were  TTY5.MA,  TTY6.MA,
     TTY7.MA, and TTY8.MA.

     The following example shows

	  1.  The dialogue  for  adding  files  that  will  become  TTY.MA,
	      TTY1.MA, TTY2.MA, TTY3.MA, and TTY4.MA to the system.

	  2.  The dialogue for entering the additional TTY tasks  into  the
	      system.

	  3.  Changing the priorities so that the TTY tasks are adjacent to
	      one another in the priority listing.

	  4.  A listing from the executing RTS/8 system.


     044 HOW MANY TTY TASKS WILL BE IN THE
     TARGET SYSTEM? [D] (1):5


      IN THE FOLLOWING QUESTIONS, YOU CAN ENTER
     UP TO FIVE ANSWERS, SEPARATED BY COMMAS.
     THE ANSWERS INDICATE YOUR CHOICE FOR THE GIVEN
     PARAMETER FOR EACH OF THE TTY TASKS THAT YOU HAVE
     SELECTED.  EXAMPLE:
     IF YOU TYPE TO THE DEVICE CODE QUESTION:
     04,31,33,35,37 (CARRIAGE RETURN) YOU SELECT
     DEVICE CODE CODE 04 FOR TTY TASK, 31 FOR TTY1
     ETC.

     045 WHAT IS THE KEYBOARD, DEVICE CODE FOR THE
     TTY TASK? [O] (03):3,41,43,45,47


     046 WHAT IS THE TELEPRINTER DEVICE CODE FOR THE
     TTY TASK? [O] (04):4,42,44,46,50




				     4-36

			     MODIFYING THE SYSGEN


     047 DO YOU WANT CNTRL/S AND CNTRL/Q FEATURES
     FOR YOUR TTY TASK? [Y/N] (Y):


     048 DO YOU WANT RUBOUT SUPPORT FOR THE TTY
     SCREEN'? [Y/N] (Y):


     049 HOW MANY NULLS AFTER A LINE FEED FOR THE TTY
     DEVICE? [O] (0):


     050 HOW MANY CHARACTERS DO YOU WANT ON A LINE
     FOR THE TTY DEVICE? [D] (80):


     051 DOES THE HARDWARE SUPPORT TABS ON THE
     TTY DEVICE [Y/N] (Y):


     052 HOW MANY SECONDS BEFORE A TTY READ TIMEOUT? [D] (0):


      END OF MULTIPLE ANSWER SECTION. THE FOLLOWING
     QUESTIONS REQUIRE SINGLE ANSWERS.
     (DOC. NO 270)

     053 DO YOU WANT TO INCLUDE ANY USER TASKS
     IN THIS RTS/8 SYSTEM?  [Y/N] (N):Y


      ENTER THE NAMES OF YOUR TASKS FOLLOWED BY
     A CARRIAGE RETURN. EXAMPLE:

     TASK 1:  NAME-1,M
     TASK 2:  NAME-2,M
	 .
	 .
	 .
     TASK N:  NAME-N,M


      M IS THE PARTITION WHERE THE TASK WILL RESIDE
     (ENTER ZERO OR NO ENTRY FOR THE MAIN LEVEL).
     YOU SHOULD ENTER THE TASKS IN THE ORDER OF
     DECREASING PRIORITY (THE FIRST ENTERED HAS THE HIGH-
     EST PRIORITY).  TERMINATE ENTRY BY TYPING A CARRIAGE
     RETURN (ONLY).
     (DOC. NO 301)

     TASK 001 ?:TTY5


     TASK 002 ?:TTY6

				     4-37

			     MODIFYING THE SYSGEN


     TASK 003 ?:TTY7


     TASK 004 ?:TTY8


     TASK 005 ?:


     054 DO YOU WANT TO CHANGE ANY OF THE TASK'S
     PRIORITIES? [Y/N] (N):Y


      THE WAY IN WHICH YOU CHANGE DEVICE PRIORITIES
     IS TO NAME THAT TASK WHICH WILL BE HIGHER IN
     PRIORITY THAN THE NEXT NAMED TASK, TAKEN A PAIR AT A
     TIME, AND DELIMINTED BY A COMMA.

     EXAMPLE:

      PRIORITY CHANGE:  TASK-3, TASK-1
     PLACES TASK-3 HIGHER IN PRIORITY THAN
     TASK-1.  THE TASK ORDER WILL NOW BE TASK-3,
     TASK-1, TASK-2.  WHEN YOU FINISH CHANGING
     PRIORITIES, A CARRIAGE RETURN (ONLY) TERMINATES THE ENTRY.
     (DOC. NO 312)

      TYPE ? AND A CARRIAGE RETURN TO OBTAIN A LIST-
     ING OF THE CURRENT TASK PRIORITIES AFTER ANY
     PRIORITY PROMPT DURING THE  RESPONSE TO THIS QUESTION
     (DOC. NO 244)

     PRIORITY CHANGE:?


     PRIORITY CHANGE:TTY5,MCR


     PRIORITY CHANGE:TTY6,MCR


     PRIORITY CHANGE:TTY7,MCR


     PRIORITY CHANGE:TTY8, MCR


     PRIORITY CHANGE:


      THE QUESTION AND ANSWER SESSION IS COMPLETED.
     THE PROGRAM WILL CONTINUE ON TO
     PASS 2 (FILE BUILDING).


				     4-38

			     MODIFYING THE SYSGEN


       PASS2 COMPLETED.  CHAINING TO BATCH AS REQUESTED.



     RTS8 BUILD PROGRAM
     TASK PRIORITY ASSIGNMENT

     TASK     PRIORITY
     CLOCK   = 001
     RL01    = 002
     RK8E    = 003
     LPT     = 004
     EMT     = 005
     TTY     = 006
     TTY1    = 007
     TTY2    = 010
     TTY3    = 011
     TTY4    = 012
     MCR     = 013
     TTY5    = 014
     TTY6    = 015
     TTY7    = 016
     TTY8    = 017
     EXIT    = 020
     BKT     = 021
     OS8     = 022


     RTS8 BUILD PROGRAM
     TASK PRIORITY ASSIGNMENT

     TASK     PRIORITY
     CLOCK   = 001
     RL01    = 002
     RK8E    = 003
     LPT     = 004
     EMT     = 005
     TTY     = 006
     TTY1    = 007
     TTY2    = 010
     TTY3    = 011
     TTY4    = 012
     TTY5    = 013
     TTY6    = 014
     TTY7    = 015
     TTY8    = 016
     MCR     = 017
     EXIT    = 020
     BKT     = 021
     OS8     = 022





				     4-39

			     MODIFYING THE SYSGEN


     .RU SYS:S9TTY
     >SYSAT
     01 CLOCK   O
     02 RL01    M
     03 RK8E    M
     04 LPT     M
     05 EMT     M
     06 TTY     M
     07 TTTASK  M
     10 TTTASK  M
     11 TTTASK  M
     12 TTTASK  M
     13 TTTASK  M
     14 TTTASK  M
     15 TTTASK  M
     16 TTTASK  M
     17 MCR
     20 EXIT    R *
     21 BKT     O
     22 OS8     E
     >TIME
     00:00:20



     >DATE 16-OCT-78
     >DATE
     16-OCT-78
     >TIME
     00:00:46
     >SYSTAT CLOCK
     01  CLOCK  O  2600: 0000  3403  0000  0026
     >$
     ^B

     .DIR/F=6/M


     <EMPTY>    <EMPTY>    <EMPTY>    <EMPTY>

     1083 FREE: BLOCKS














				     4-40







				  APPENDIX A

		     RTS/8 SYSTEM GENERATION SOURCE FILES



				 TASK SOURCES

     ----------------------------------------------------------------------
     |	Task Name    File Name			 Task Function		  |
     |--------------------------------------------------------------------|
     |									  |
     |	-	     RTS8.MA	   RTS/8 Executive			  |
     |	CLOCK	     CLOCK.MA	   Clock Handler Task			  |
     |	CSA	     CSA.MA	   Cassette Driver Task			  |
     |	CSAF	     CSAF.MA	   Cassette File Support Task		  |
     |	DTA	     DTA.MA	   TC08 DECtape Driver Task		  |
     |	EXIT	     EXIT.MA	   Exit Task				  |
     |	LPT	     LPT.MA	   Line Printer Driver Task		  |
     |	LTA	     LTA.MA	   LINCtape Driver Task			  |
     |	MCR	     MCR.MA	   Monitor Console Routine		  |
     |	NULL8A	     NULL8A.MA	   Null Task for PDP-8A			  |
     |	OS8	     OS8.MA	   OS/8 Support Task			  |
     |	OS8F	     OS8F.MA	   OS/8 File Support Task		  |
     |	PWRF	     PWRF.MA	   Power Fail Task			  |
     |	RF08/DF32    RF08.MA	   RF08/DF32 Fixed-Head Driver Task	  |
     |	RK8	     RK8.MA	   RK8 Disk Driver Task			  |
     |	RK8E	     RK8E.MA	   RK8E Disk Driver Task		  |
     |	RL01	     RL01.MA	   RL01 Disk Driver Task		  |
     |	RX8A	     RX.MA	   Floppy Disk Handler (1st Controller)   |
     |	RX8B	     RX.MA	   Floppy Disk Handler (2nd Controller)	  |
     |	RX8C	     RX.MA	   Floppy Disk Handler (3rd Controller)	  |
     |	RX8D	     RX.MA	   Floppy Disk Handler (4th Controller)	  |
     |	SWAP	     SWAP.MA	   Nonresident Task Swapper		  |
     |	TTY	     TTY.MA	   Terminal Driver Task			  |
     |	TTY1	     TTY.MA	   Terminal Driver Task			  |
     |	TTY2	     TTY.MA	   Terminal Driver Task			  |
     |	TTY3	     TTY.MA	   Terminal Driver Task			  |
     |	TTY4	     TTY.MA	   Terminal Driver Task			  |
     |	UDC/ICS	     UDCICS.MA	   Universal Digital Controller/	  |
     |				   Industrial Controller Subsystem	  |
     |				   Handler task				  |
     |	SYSGEN	     SYSGEN.SV	   The SYSGEN save image		  |
     |	SCRIPT	     SCRIPT.SV	   The SYSGEN script, assembled		  |
     |	SCRIPT	     SCRIPT.MA	   The SYSGEN MACREL source file	  |
     ----------------------------------------------------------------------







				      A-1







				  APPENDIX B

			  DEC/X8 SPECIFICATION SHEET


     Date_________ Manufacturing Facility__________________________________

     Customer_______________ DEC#____________ System Serial #______________

     Processor PDP-8______ Memory__________K    EAE?_________yes_______no

     Power Fail?__yes__no   Memory Parity?__yes__no   Time Share?__yes__no

     If DEC/X8 builder Input other than paper tape, specify device

     If DEC/X8 builder Output other than paper tape, specify device

						Filename______________.SV

     List devices in system with information as indicated below:
     ----------------------------------------------------------------------
		|		|    IF INCLUDED IN	| IF NOT INCLUDED	
		|		|   CUSTOM EXERCISER    | IN CUSTOM EXER-
		|		| DEC/X8		| CISER (REASON):
		|    DEVICE	| MODULE  DEC/X8   JOB  | MEMORY  NO DEC/X8
      DEVICE	|    CODE(S)	|  NAME  PRIORITY  SLOT |  LIMIT   MODULE
     ----------------------------------------------------------------------
		|		|	|        |	|	 |
		|		|	|        |	|	 |
		|		|	|        |	|	 |
		|		|	|        |	|	 |
		|		|	|        |	|	 |
		|		|	|        |	|	 |
		|		|	|        |	|	 |
		|		|	|        |	|	 |
		|		|	|        |	|	 |
		|		|	|        |	|	 |
		|		|	|        |	|	 |
		|		|	|        |	|	 |
		|		|	|        |	|	 |
		|		|	|        |	|	 |
		|		|	|        |	|	 |
		|		|	|        |	|	 |
		|		|	|        |	|	 |
		|		|	|        |	|	 |
		|		|	|        |	|	 |
		|		|	|        |	|	 |
		|		|	|        |	|	 |
		|		|	|        |	|	 |
		|		|	|        |	|	 |
		|		|	|        |	|	 |
     ----------------------------------------------------------------------

				      B-1







				  APPENDIX C

			       SYSGEN CHECK LIST



     This worksheet list overviews the questions that the SYSGEN  asks.  In
     the worksheet's spaces you can specify the answers you wish to give to
     questions before you sit at the terminal. For some of  the  questions,
     you  may  refer  to  the  Chapter 2 comments by their document numbers
     (listed in Section 2.4).










































				      C-1

			       SYSGEN CHECK LIST


     ----------------------------------------------------------------------
     |	QUESTION		   | ANSWER | DEFLT |	COMMENT    | DOC. |
     |				   |	    |	    |		   | NO.  |
     |====================================================================|
     |	PDP 8/A			   | y    n | Y	    |		   | 042  |
     |--------------------------------------------------------------------|
     |	PDP 8/E			   | Y 	  n | N	    |		   | 042  |
     |--------------------------------------------------------------------|
     |	PDP-12			   | y	  n | N	    |		   | 042  |
     |--------------------------------------------------------------------|
     |	VT78			   | y	  n | N	    |		   | 042  |
     |--------------------------------------------------------------------|
     |	EAE HARDWARE		   | y 	  n | N	    |		   | 050  |
     |				   |--------|-------|		   |      |
     |	  Save EAE		   | y	  n | Y	    |		   | 052  |
     |--------------------------------------------------------------------|
     |	MQ HARDWARE		   | y	  n | Y	    |		   | 054  |
     |				   |--------|-------|		   |	  |
     |	  Save MQ		   | y	  n | Y	    |		   | 056  |
     |--------------------------------------------------------------------|
     |	MEMORY FIELDS		   |	    | 4     | 1-32 decimal | 060  |
     |--------------------------------------------------------------------|
     |	RTS/8 FIELD		   |	    | 0     | 0-32 decimal | 353  |
     |--------------------------------------------------------------------|
     |	POWER FAIL HARDWARE	   | y	  n | N	    |		   | 062  |
     |--------------------------------------------------------------------|
     |	KL8A HARDWARE		   | y	  n | N	    |		   | 064  |
     |				   |--------|-------|		   |      |
     |	  How many in system	   |	    | 1     | 1-8 decimal  | 066  |
     |				   |--------|-------|		   |	  |
     |	  Device Code		   |	    | 40    | 1-77 octal   | 276  |
     |--------------------------------------------------------------------|
     |	KT8A HARDWARE		   | y	  n | N	    |		   | 070  |
     |--------------------------------------------------------------------|
     |	SYSGEN OUTPUT TO	   |	    | SYS   | device name  | 022  |
     |--------------------------------------------------------------------|
     |	CHAIN TO RTS/8 FROM BATCH  | y	  n |	    |		   | 024  |
     |--------------------------------------------------------------------|
     |	OUTPUT FILES NAME	   |        | DEFLT | 1 to 5 char. | 026  |
     |--------------------------------------------------------------------|
     |	CHAIN FROM SYSGEN TO BATCH | y    n | Y     |		   | 030  |
     |--------------------------------------------------------------------|
     |	WHERE ARE SOURCES	   |	    | SYS   | device name  | 340  |
     |--------------------------------------------------------------------|
     |	WHERE TO STORE .RB FILES   |	    | SYS   | device name  |	  |
     |--------------------------------------------------------------------|
     |	ASSEMBLY LISTINGS	   | y	  n | N	    |		   | 334  |
     |				   |--------|-------|		   |	  |
     |	Listing Device		   |	    | LPT   | device name  |	  |
     |--------------------------------------------------------------------|
     |	LINKER LOAD MAPS	   | y	  n | N	    |		   | 341  |
     |				   |--------|-------|		   |	  |
     |	Listing Device		   |	    | LPT   | device name  |	  |
     ----------------------------------------------------------------------

				      C-2

			       SYSGEN CHECK LIST


     ----------------------------------------------------------------------
     |	QUESTION		   | ANSWER | DEFLT |	COMMENT    | DOC. |
     |				   |	    |	    |		   | NO.  |
     |====================================================================|
     |	ARE SOURCES ON SAME MEDIA  | y 	  n |	    |		   | 340  |
     |--------------------------------------------------------------------|
     |	DEFAULT SYSTEM		   | y	  n | N	    |		   | 017  |
     |--------------------------------------------------------------------|
     |	POWER FAIL HANDLER	   | y	  n | N	    |		   |	  |
     |--------------------------------------------------------------------|
     |	CLOCK HANDLER		   | y	  n | N	    |		   |	  |
     |				   |--------|-------|		   |	  |
     |	  Standard Clock	   | y	  n |	    |		   | 220  |
     |				   |--------|-------|		   |	  |
     |	    Designation		   |	    | ?	    |		   | 222  |
     |				   |--------|-------|		   |	  |
     |	  Software Ticks	   |	    | 10    | 1-192 decimal| 347  |
     |				   |--------|-------|		   |	  |
     |	  # of Entry Slots	   |	    | 16    |16-256 decimal| 224  |
     |				   |--------|-------|		   |	  |
     |	  Interrupt Linkage	   | y	  n | N	    |		   | 351  |
     |--------------------------------------------------------------------|
     |	UDC			   | y	  n | N	    |		   |	  |
     |				   |--------|-------|		   |	  |
     |	  Interrupts Stored	   |	    | 12    | 1-50 octal   | 227  |
     |				   |--------|-------|		   |	  |
     |	  # of Counter Modules	   |	    | 1	    | 1-20 octal   | 231  |
     |				   |--------|-------|		   |	  |
     |	  # of Contact Modules	   |	    | 2	    | 1-20 octal   | 231  |
     |				   |--------|-------|		   |	  |
     |	  # of Analog Inputs	   |	    | 2	    | 1-20 octal   | 231  |
     |				   |--------|-------|		   |	  |
     |	  Address of Counter	   |	    | ?	    | 0-3777 octal | 235  |
     |				   |--------|-------|		   |	  |
     |	  Address of Analog	   |	    | ?	    | 0-3777 octal | 235  |
     |--------------------------------------------------------------------|
     |	RF08 DISK		   | y	  n | N	    |		   |	  |
     |--------------------------------------------------------------------|
     |	DF32 DISK		   | y	  n | N	    |		   |	  |
     |--------------------------------------------------------------------|
     |	RK8E DISK		   | y	  n | N	    |		   |	  |
     |--------------------------------------------------------------------|
     |	RL01 DISK		   | y	  n | N	    |		   |	  |
     |--------------------------------------------------------------------|
     |	DECTAPE			   | y	  n | N	    |		   |	  |
     |--------------------------------------------------------------------|
     |	LINCTAPE		   | y	  n | N	    |		   |	  |
     ----------------------------------------------------------------------







				      C-3

			       SYSGEN CHECK LIST


     ----------------------------------------------------------------------
     |	QUESTION		   | ANSWER | DEFLT |	COMMENT    | DOC. |
     |				   |	    |	    |		   | NO.  |
     |====================================================================|
     |	FIRST FLOPPY		   | y	  n | N	    |		   |	  |
     |				   |--------|-------|		   |	  |
     |	Device Number		   |	    | 75    | 1-77 octal   | 136  |
     |--------------------------------------------------------------------|
     |	SECOND FLOPPY		   | y	  n | N	    |		   |	  |
     |				   |--------|-------|		   |	  |
     |	Device Number		   |	    | 70    | 1-77 octal   | 136  |
     |--------------------------------------------------------------------|
     |	THIRD FLOPPY		   | y	  n | N	    |		   |	  |
     |				   |--------|-------|		   |	  |
     |	Device Number		   | 	    | 71    | 1-77 octal   | 136  |
     |--------------------------------------------------------------------|
     |	FOURTH FLOPPY		   | y	  n | N	    |		   |	  | 
     |				   |--------|-------|		   |	  |
     |	Device Number		   |	    | N	    | 1-77 octal   | 136  |
     |--------------------------------------------------------------------|
     |	LINE PRINTER		   | y	  n | N	    |		   |	  |
     |--------------------------------------------------------------------|
     |	TERMINAL		   | y	  n | Y	    |		   |	  |
     |				   |--------|-------|		   |	  |
     |	  # of TTYs in sys.	   |	    | 1     | 1-5	   | 317  |
     |				   |--------|-------|		   |	  |
     |	  Keyboard Dev. Code	   |	    | 03    | 1-113 octal  | 254  |
     |				   |--------|-------|		   |	  |
     |	  Teleprinter Dev. Code    |	    | 04    | 1-113 octal  | 254  |
     |				   |--------|-------|		   |	  |
     |	  CTRL/S, CTRL/Q	   | y	  n | Y	    |		   | 257  |
     |				   |--------|-------|		   |	  |
     |	  Rubout		   | y	  n | Y	    |		   | 261  |
     |				   |--------|-------|		   |	  |
     |	  Nulls after <LF>	   |	    | 0     | 0-10 octal   | 263  |
     |				   |--------|-------|		   |	  |
     |	  Characters on line	   |	    | 80    | multiple of 8| 265  |
     |				   |--------|-------|		   |	  |
     |	  Tab Support		   | y	  n | Y	    |		   | 273  |
     |				   |--------|-------|		   |	  |
     |	  Timeout		   |	    | 0	    | 0-10 decimal | 267  |
     |--------------------------------------------------------------------|
     |	EMERGENCY BREAKTHROUGH	   | y	  n | N	    |		   | 325  |
     |				   |--------|-------|		   |	  |
     |	  Device to Use	TTY	   |	    | TTY   | name	   | 331  |
     |--------------------------------------------------------------------|
     |	SWAPPER			   | y	  n | N	    |		   | 342  |
     |				   |--------|-------|		   |	  |
     |	  Swap Device		   |	    | RK8E  | device name  | 246  |
     |				   |--------|-------|		   |	  |
     |	  Physical Unit		   |	    | 0	    | alphanumeric | 250  |
     |--------------------------------------------------------------------|
     |	CASSETTE		   | y	  n | N     |		   |	  |
     ----------------------------------------------------------------------

				      C-4

			       SYSGEN CHECK LIST


     ----------------------------------------------------------------------
     |	QUESTION		   | ANSWER | DEFLT |	COMMENT    | DOC. |
     |				   |	    |	    |		   | NO.  |
     |====================================================================|
     |	CASSETTE FILE SUPPORT	   | y	  n | N     |		   |	  |
     |--------------------------------------------------------------------|
     |	OS/8 FILE SUPPORT	   | y	  n | N	    |		   | 153  |
     |--------------------------------------------------------------------|
     |	MCR			   | y	  n | Y	    |		   |	  |
     |				   |--------|-------|		   |	  |
     |	  Time of Day		   | y	  n | Y	    |		   | 207  |
     |				   |--------|-------|		   |	  |
     |	  Systat		   | y	  n | Y	    |		   | 211  |
     |				   |--------|-------|		   |	  |
     |	  MCR terminal		   | 	    | TTY   | TTY name 	   | 215  |
     |--------------------------------------------------------------------|
     |	TEST TASK		   | y	  n | N     |		   |	  |
     |--------------------------------------------------------------------|
     |	EXIT TASK		   | y	  n | N     |		   |	  |
     |--------------------------------------------------------------------|
     |	OS/8 SUPPORT		   | y    n | N	    |		   |	  |
     |				   |--------|-------|		   |	  |
     |	  # of fields for OS/8	   |	    | 2	    | 1-7 decimal  | 170  |
     |				   |--------|-------|		   |	  |
     |	  OS/8 Keyboard Device	   |	    | 03    | device code  | 174  |
     |				   |--------|-------|		   |	  |
     |	  OS/8 Teleprinter Dev.    |	    | 04    | device code  | 172  |
     |				   |--------|-------|		   |	  |
     |	  RTS/8 Handler for OS/8   |	    | RK8E  | device name  | 176  |
     |				   |--------|-------|		   |	  |
     |	  OS/8 in top fields	   | y	  n | Y     |		   | 202  |
     |				   |--------|-------|		   |	  |
     |	    Which Field then	   |	    | ?     | 2-30 decimal | 202  |
     |				   |--------|-------|		   |	  |
     |	  Nulls after line feed    |	    | 0	    | 0-10 decimal | 204  |
     |--------------------------------------------------------------------|
     |	OS/8 BACKGROUND		   | y	  n | Y	    |		   | 323  |
     |				   |--------|-------|		   |	  |
     |	  Background Terminal	   |	    | TTY   | TTY name 	   | 327  |
     |--------------------------------------------------------------------|
     |	NULL TASK		   | y	  n | N	    | PDP 8/A only |	  |
     |--------------------------------------------------------------------|
     |	ENTER USER TASKS	   | y	  n | N	    |		   | 300  |
     ----------------------------------------------------------------------











				      C-5

			       SYSGEN CHECK LIST


		 ---------------------------------------------
		 |	     TASK ENTRY WORKSHEET	     |
	         |===========================================|
		 |					     |
		 |   Task Name________________  Part._____   |
		 |					     |
		 |   Task Name________________  Part._____   |
		 |					     |
		 |   Task Name________________  Part._____   |
		 |					     |
		 |   Task Name________________  Part._____   |
		 |					     |
		 |   Task Name________________  Part._____   |
		 |					     |
		 |   Task Name________________  Part._____   |
		 |					     |
		 |   Task Name________________  Part._____   |
		 |					     |
		 |   Task Name________________  Part._____   |
		 |					     |
		 |   Task Name________________  Part._____   |
		 |					     |
		 |   Task Name________________  Part._____   |
		 |					     |
		 |   Task Name________________  Part._____   |
		 |					     |
		 |   Task Name________________  Part._____   |
		 |					     |
		 |   Task Name________________  Part._____   |
		 |					     |
		 |   Task Name________________  Part._____   |
		 |					     |
		 |   Task Name________________  Part._____   |
		 |					     |
		 |   Task Name________________  Part._____   |
		 |					     |
		 |   Task Name________________  Part._____   |
		 |					     |
		 |   Task Name________________  Part._____   |
		 |					     |
		 |   Task Name________________  Part._____   |
		 |					     |
		 |   Task Name________________  Part._____   |
		 |					     |
		 |   Task Name________________  Part._____   |
		 |					     |
		 |   Task Name________________  Part._____   |
		 |					     |
		 |   Task Name________________  Part._____   |
		 |					     |
		 |   Task Name________________  Part._____   |
		 ---------------------------------------------



				      C-6







				  APPENDIX D

			    RTS/8 PARAMETER LISTING



     This appendix is an abbreviated listing of the RTS/8  Parameter  file.
     It  differs  from  the parameter file in SCRIPT.MA in that information
     that is redundant or useful only to the SYSGEN is not included.  Also,
     where necessary, additional comments have been added.


	      .SBTTL PARAMETER RECORDS

     /2.9 PARAMETERS FOR RTS/8 TASKS 	     V3
     /
     /
     /COPYRIGHT  (C)  1974,1975,1976,1977,1978,1979
     /		      BY DIGITAL EQUIPMENT CORPORATION

     /THE INFORMATION IN THIS DOCUMENT IS SUBJECT TO CHANGE WITHOUT NOTICE
     /AND SHOULD NOT BE CONSTRUED AS A COMMITMENT BY DIGITAL EQUIPMENT
     /CORPORATION. DIGITAL EQUIPMENT CORPORATION ASSUMES NO RESPONSIBILITY
     /FOR ANY ERRORS THAT MAY APPEAR IN THIS DOCUMENT.
     /
     /THE SOFTWARE DESCRIBED IN THIS DOCUMENT IS FURNISHED TO THE PURCHASER
     /UNDER A LICENSE FOR USE ON A SINGLE COMPUTER SYSTEM AND CAN BE COPIED
     /(WITH INCLUSION OF DIGITAL'S COPYRIGHT NOTICE) ONLY FOR USE IN SUCH
     /SYSTEM, EXCEPT AS MAY OTHERWISE BE PROVIDED IN WRITING BY DIGITAL.
     /
     /DIGITAL EQUIPMENT CORPORATION ASSUMES NO RESPONSIBILITY FOR THE USE
     /OR RELIABILITY OF ITS SOFTWARE ON EQUIPMENT THAT IS NOT SUPPLIED BY
     /DIGITAL.


     /RTS/8 V3 - PARAMETER FILE


     /INDEX:
     /SECTION 1-CONFIGURATION PARAMETERS
     /SECTION 2-SYSTEM TASK TABLE
     /SECTION 3-MULTIPLE PARAMETER TASK LISTS
     /SECTION 4-DEFAULT PARAMETERS (NORMALLY FIXED)
     /SECTION 5-SYSTEM PARAMETERS (NORMALLY FIXED)
     /SECTION 6-TTY SKELETON CONTROL FILES
     /SECTION 7-RX FLOPPY SKELETON CONTROL FILES







				      D-1

			    RTS/8 PARAMETER LISTING


     /SECTION 1-CONFIGURATION PARAMETERS


     M1777,  TEXT    "IFNDEF RTS8    <XLIST>"

     M2016,  TEXT    "DFLT="	     /1 IF USER SPECIFIES DEFAULT SYSTEM
     				     /   DURING SYSGEN
     M2041,  TEXT    "PDP8A="	     /1 IF PDP 8/A, ELSE 0
     M2043,  TEXT    "PDP8E="	     /1 IF PDP 8/E, ELSE 0
     M2044,  TEXT    "PDP12="	     /1 IF PDP-12, 0 OR UNDEFINED
     				     /   IF NOT PDP-12

     M2047,  TEXT    "EAE="	     /1 IF SYSTEM HAS EAE HARDWARE
     M2051,  TEXT    "EAESV="	     /1 IF CONTENTS OF EAE REGISTERS SAVED
     				     /   WHEN CONTEXT SWITCHING OCCURS
     M2053,  TEXT    "MQ="	     /1 IF SYSTEM HAS HARDWARE MQ REGISTER
     M2055,  TEXT    "MQSV="	     /1 IF CONTENTS OF MQ REGISTER SAVED
     				     /   WHEN CONTEXT SWITCHING OCCURS

     M2057,  TEXT    "NFLDS="	     /NUMBER OF FIELDS, RIGHT JUSTIFIED

     M2352,  TEXT    "RTFLD="	     /FIELD IN WHICH RTS8 RESIDES

     M2061,  TEXT    "PWRFAL="	     /1 IF POWER FAIL/RESTART ENABLED IN

     M2065,  TEXT    "KL8A="	     /   HARDWARE NUMBER OF KL8A'S IN USE
     				     /I.E. 1 IF ONE KL8A (UP TO 4 LINES)

     M2067,  TEXT    "KT8A="	     /1 IF SYSTEM HAS EXTENDED MEMORY
     				     /   HARDWARE

     M2045,  TEXT    "VT78="	     /1 IF SYSTEM IS A VT78 SYSTEM


     /SECTION 2 - SYSTEM TASK TABLE


     /COMMON TASKS--THE SYSGEN ONLY PLACES THE TASKS YOU SELECT
     /IN THE OUTPUT PARAMETER FILE

     /TASKS ARE LISTED IN DECREASING ORDER OF PRIORITY (DEFAULT-TASK
     /NOT SELECTED, AND PRIORITY NOT SPECIFIED)

     M2074,  TEXT    "PWRF="	     /POWER FAIL HANDLING TASK

     M2075,  TEXT    "CLOCK="	     /CLOCK HANDLER - SHOULD BE HIGH
     				     /   PRIORITY. MULTIPLE PARAMETER
     				     /   TASK-SEE LISTING BELOW

     M2132,  TEXT    "DTA="	     /DECTAPE DRIVER TASK

     M2150,  TEXT    "CSA="	     /CASSETTE DRIVER TASK



				      D-2

			    RTS/8 PARAMETER LISTING


     M2125,  TEXT    "UDC="	     /UNIVERSAL DIGITAL CONTROLLER TASK
     				     /MULTIPLE PARAMETER TASK-SEE
     				     /   LISTING BELOW

     M2336,  TEXT    "RL01="	     /RL01 DISK DRIVER TASK

     M2126,  TEXT    "RF08="	     /RF08 DISK DRIVER TASK

     M2127,  TEXT    "DF32="	     /DF32 DISK DRIVER TASK

     M2130,  TEXT    "RK8="	     /RK8 OR RK8E DISK DRIVER TASK

     M2131,  TEXT    "RK8E="	     /RK8E DISK DRIVER TASK

     M2133,  TEXT    "LTA="	     /LINCTAPE DRIVER TASK

     M2134,  TEXT    "RX8A="	     /FIRST FLOPPY CONTROLLER

     M2137,  TEXT    "RX8B="	     /SECOND FLOPPY CONTROLLER

     M2141,  TEXT    "RX8C="	     /THIRD FLOPPY CONTROLLER

     M2143,  TEXT    "RX8D="	     /FOURTH FLOPPY CONTROLLER

     M2145,  TEXT    "LPT="	     /LINE PRINTER DRIVER TASK

     M2324,  TEXT    "EMT="	     /EMERGENCY BREAKTHROUGH MESSAGE TASK

     M2146,  TEXT    "TTY="          /TELETYPE DRIVER TASK
	     			     /MULTIPLE PARAMETER TASK - SEE
     				     /   LISTING BELOW
     M2701,  TEXT    "TTY1="	     /FIRST TTY CONTROL FILE TASK
     M2716,  TEXT    "TTY2="	     /SECOND
     M2731,  TEXT    "TTY3="	     /THIRD
     M2746,  TEXT    "TTY4="	     /FOURTH

     M2147,  TEXT    "SWAP="	     /NONRESIDENT TASK SWAPPER TASK
     				     /    MULTIPLE PARAMETER TASK-SEE
     				     /    LISTING BELOW

     M2151,  TEXT    "CSAF="	     /CASSETTE FILE SUPPORT TASK

     M2152,  TEXT    "OS8F="	     /OS/8 FILE SUPPORT

     M2156,  TEXT    "MCR="	     /MONITOR CONSOLE ROUTINE
     				     /MULTIPLE PARAMETER TASK-SEE
     				     /   LISTING BELOW

     		     /SYSGEN INSERTS USER TASKS HERE

     M2160,  TEXT    "TEST="	     /RTS/8 TEST TASK; COMES UP RUNNING
     				     /WHEN DEFAULT SYSTEM IS SPECIFIED

     M2161,  TEXT    "EXIT="	     /EXIT TASK

				      D-3

			    RTS/8 PARAMETER LISTING


     M2322,  TEXT    "BKT="	     /OS/8 TERMINAL SUPPORT TASK

     M2162,  TEXT    "OS8="	     /OS/8 SUPPORT - NORMALLY LOWEST
     				     /   PRIORITY MULTIPLE PARAMETER
     				     /   TASK-SEE LISTING BELOW

     M2163,  TEXT    "NULL8A="	     /NULL JOB FOR PDP-8/A

     M1776,  TEXT    "NTASKS="	     /NUMBER OF TASKS IN SYSTEM
	     			     /   (SYSTEM+USER TASKS)


     /SECTION 3 - MULTIPLE PARAMETER TASK LISTS


     		     /INCLUDE WHEN OS-8 TASK IS SPECIFIED


     M2167,  TEXT    "OSFLDS="	     /NUMBER OF FIELDS TO ALLOCATE TO
     				     /   OS/8 (KG 2)
     M2171,  TEXT    "OSTTDV="	     /OS/8 TELEPRINTER DEVICE CODE (KG 04)
     M2173,  TEXT    "OSKBDV="	     /OS/8 KEYBOARD DEVICE CODE (KG 03 IS
     				     /   CONSOLE)
     M2175,  TEXT    "OSSYSD="	     /OS/8 SYSTEM DEVICE DRIVER TASK
     				     /   (EG RK8E)
     M2203,  TEXT    "OSFILL="	     /FILLS NEEDED AFTER LINE FEED
     				     /   (EG 4 FOR 2400 BAUD VT05)
     M2201,  TEXT    "OSBASE="	     /IF KT8A HARDWARE PRESENT; LOWEST
     				     /   FIELD IN WHICH OS/8 TASK RUNS
     M2326,  TEXT    "BKTCDV="	     /TASK NAME OF TTY DEVICE TO SHARE
     				     /   WITH OS/8


     	     /INCLUDE WHEN MCR TASK IS SPECIFIED


     M2206,  TEXT    "MCRCLK="	     /0 IF MCR TIME OF DAY FACILITIES TO
     				     /   BE OMITTED (DEFAULT IS 1)
     M2210,  TEXT    "MCRSYS="	     /0 IF MCR SYSTAT FACILITY NOT DESIRED
     				     /1 IF DESIRED (DEFAULT)
     M2214,  TEXT    "MCRCDV="	     /CONSOLE TO BE USED BY MCR, E.G. TTY
     				     /DEFAULT IS TTY


	     /INCLUDE WHEN CLOCK TASK IS SPECIFIED


     M2221,  TEXT    "CLKTYP="	     /0 (DK8EA/DK8EC) OR l(KW12) OR 2
     				     /   (PDP8/A) OR 3 (DK8EP)
     M2346,  TEXT    "SHERTZ="	     /SOFTWARE CLOCK TICK RATE (DEFAULT
     				     /   IS 16 (DECIMAL)
     M2223,  TEXT    "CLKQLN="	     /MINIMUM NUMBER OF ENTRY SLOTS IN
     				     /   THE CLOCK QUEUE
     				     /MAY BE CHANGED BY USER

				      D-4

			    RTS/8 PARAMETER LISTING


     M2350,  TEXT    "CLKLRM="	     /ENABLE INTERRUPT LINKAGE FEATURE
     				     /   1 IS ENABLE, 0 IS DEFAULT


     /INCLUDE WHEN UDC TASK IS SPECIFIED


     M2226,  TEXT    "RINGBF="	     /NUMBER OF INTERRUPTS THAT CAN BE
     				     /   STORED
     M2230,  TEXT    "NCNTR="	     /NUMBER OF COUNTER MODULES
     M2232,  TEXT    "NCNTC="	     /NUMBER OF CONTACT MODULES
     M2233,  TEXT    "NAD="	     /NUMBER OF ANALOG INPUT CONVERTER
     				     /   MODULES
     M2234,  TEXT    "FCTR="	     /ADDRESS OF THE FIRST COUNTER MODULE
     M2236,  TEXT    "FCT="	     /ADDRESS OF THE FIRST CONTACT
     				     /   INTERRUPT MODULE
     M2237,  TEXT    "FAD="	     /ADDRESS OF THE FIRST A/D CONVERTER
     				     /   MODULE


     /INCLUDE WHEN SWAPPER TASK IS SPECIFIED


     M2245,  TEXT    "SYS="	     /SWAP DEVICE DRIVER TASK (KG RK8E)
     M2250,  TEXT    "SUNIT=" 	     /SWAP DEVICE PHYSICAL DRIVE UNIT
				     /   (EG 0 FOR RKA0)

		     /INCLUDE IF TTY TASK IS SPECIFIED
		     /THIS IS ALSO THE STRUCTURE FOR TTY
		     /CONTROL FILES

     M2253,  TEXT    "KBDEV="	     /KEYBOARD DEVICE CODE - DEFAULT IS 3
     M2255,  TEXT    "TTDEV="	     /PRINTER DEVICE CODE - DEFAULT IS 4
     M2256,  TEXT    "VT50="	     /1 ENABLES CTRL/S AND CTRL/Q
     M2260,  TEXT    "SCOPE="	     /1 MEANS TTY CAN DO A BACKSPACE
     M2262,  TEXT    "FILL="	     /NUMBER OF FILL CHARACTERS, I.E. 4
     M2264,  TEXT    "WIDTH="	     /TTY LINE WIDTH (0 MEANS INFINITE),
     				     /   DEFAULT IS 120
     M2272,  TEXT    "TAB="	     /1 IF TTY HAS HARDWARE TABS
     M2330,  TEXT    "EMTCDV="	     /NAME OF TTY DEVICE FOR EMERGENCY
     				     /   MESSAGE BREAKTHROUGH
     M2266,  TEXT    "TTTIM="	     /TTY READ TIMEOUT PARAMETER.


		     /INCLUDE IF KL8A TASK IS SPECIFIED


     M2275,  TEXT    "KL8ADV="       /KL8A DEVICE CODE - DEFAULT IS 40







				      D-5

			    RTS/8 PARAMETER LISTING


	     .SBTTL DEFAULT PARAMETERS


     /SECTION 4 - DEFAULT PARAMETERS (NORMALLY FIXED)

		     /CONFIGURATION DEFAULTS (DEFAULT TASKS INCLUDED)


     M1000,  TEXT    "IFDEF DFLT<"
	     TEXT    "TTY=2"	     /DEFAULT TASK ASSIGNMENT
	     TEXT    "MCR=3"
	     TEXT    "TEST=4"
	     TEXT    "EXIT=6"
	     TEXT    "CLOCK=1"	     /END;DEFAULT ASSIGNMENT
	     TEXT    "NTASKS=10"     /DEFAULT TOTAL NUMBER OF TASKS
	     TEXT    "KL8A=0"
	     TEXT    "NFLDS=2"
	     TEXT    "MQ=0"
	     TEXT    "MQSV=0>"

	     .SBTTL SYSTEM PARAMETERS

     /SECTION 5 - SYSTEM PARAMETERS (NORMALLY FIXED)


     /EQUIVALENCES:

     P1001,  TEXT    "AC7776=	     CLL STA RAL"
	     TEXT    "AC7775=	     CLL STA RTL"
	     TEXT    "AC4000=	     CLA STL RAR"
	     TEXT    "AC3777=	     CLL STA RAR"
	     TEXT    "AC2000=	     CLA STL RTR"
	     TEXT    "AC0002=	     CLA STL RTL"
	     TEXT    "AC5777=	     CLL STA RTR"


     /MONITOR CALL VALUES:

	     TEXT    "CAL= JMS 20"          /CALL THE EXECUTIVE

	     TEXT    "POSTDS=JMP I 24"      /DISMISS AN INTERRUPT

	     TEXT    "WAITM= JMS I 25"	    /WAIT FOR MULTIPLE EVENTS

		     /NOTE: "**" MEANS CRITICAL VALUE MAY NOT
		     /BE CHANGED WITHOUT MODIFYING SYSTEM CODE!!

	     TEXT    "SEND= 0"	     /SEND MESSAGE
	     TEXT    "RECEIV=1"	     /RECEIVE MESSAGE
	     TEXT    "WAITE= 2"	     /WAIT FOR EVENT FLAG
	     TEXT    "RUN= 3"	     /CONTINUE TASK EXECUTION
	     TEXT    "SUSPND=4"	     /SUSPEND TASK EXECUTION
	     TEXT    "POST= 5"	     /POST AN EVENT FLAG


				      D-6

			    RTS/8 PARAMETER LISTING


	     TEXT    "SKPINS=6"	     /INSERT CODE INTO INTERRUPT
     				     /    SKIP CHAIN
	     TEXT    "DERAIL=7"	     /INITIATE SOFTWARE INTERRUPT
	     TEXT    "BLKARG=10"     /BLOCK TASK FOR REASON SPECIFIED
	     			     /   IN ARG
	     TEXT    "UNBARG=12"     /UNBLOCK TASK FOR REASON SPECIFIED
	     			     /   IN ARG
	     TEXT    "RESCHD=13"     /FORCE A RESCHEDULE
	     TEXT    "WAITX= 14"     /WAIT FOR EXACTLY THIS EVENT FLAG
	     TEXT    "FREE= 4000"    /**FREE PARTITION

     /TASK STATUS FLAGS:

	     TEXT    "IFDEF UDC	<"
	     TEXT    "AO=0"
	     TEXT    "DO=0"
	     TEXT    "DI=2"
	     TEXT    "GC=3"
	     TEXT    "EC=4"
	     TEXT    "RC=5"
	     TEXT    "DC=6"
	     TEXT    "ECT=7"
	     TEXT    "CS=10"
	     TEXT    "DCT=11"
	     TEXT    "AI=12>"

	     TEXT    "NONRWT=4000"	    /**NONRESIDENT TASK WAIT

	     TEXT    "EFWT= 2000"	    /EVENT FLAG WAIT

	     TEXT    "RUNWT= 1000"	    /SCHEDULE WAIT

	     TEXT    "SWPWT= 0400"	    /**SWAPPER WAIT

	     TEXT    "EORMWT=0200"	    /EVENT FLAG OR MESSAGE WAIT

	     TEXT    "USERWT=0100"	    /USER SPECIFIED WAIT

	     TEXT    "ENABWT=0040"	    /ENABLE WAIT

	     TEXT    "MSGWT= 0020"	    /MESSAGE WAIT

	     TEXT    "NETWT= 0010"	    /NETWORK WAIT
     					    /   (RESERVED FOR FUTURE USE)

	     TEXT    "DNEWT= 0001"	    /**DOES NOT EXIST WAIT

	     /SOME USEFUL EQUATES FOR TTY AND LPT MESSAGES:

	     TEXT    "NOPACK=4000"   /TEXT IS NOT PACKED IN 6-BIT

	     TEXT    "NOCRLF=2000"   /OUTPUT SHOULD NOT BE FOLLOWED
				     /   BY CR/LF


				      D-7

			    RTS/8 PARAMETER LISTING


	     TEXT    "IND=1000"      /OUTTXT PTS TO FIRST WORD OF TEXT

	     TEXT    "NOLINE=400"    /INPUT IS IN CHARACTER MODE

	     TEXT    "ASSGN=200"     /ASSIGNS DEVICE

	     TEXT    "KL8ALINE=100"  /USED TO SPECIFY A LINE OF A KL8A

	     /SOME USEFUL EQUATES FOR STANDARD CLOCK MESSAGES:

	     TEXT    "IFDEF CLOCK    <"
	     TEXT    "MARKTIME=0"    /POST EVENT FLAG AFTER SPECIFIED
     				     /   INTERVAL
	     TEXT    "SCHEDULE=1000" /RUN TASK AFTER SPECIFIED INTERVAL
	     TEXT    "TIMOUT=2000"   /DERAIL TASK AFTER SPECIFIED INTERVAL
	     TEXT    "PERIODICALLY=3000"
				     /USED AS MODIFIER TO 'SCHEDULE'
				     /   RE-QUEUES RUN REQUREST AFTER
				     /   SPECIFIED INTERVAL, E.G.,
				     /   'SCHEDULE FOO PERIODICALLY'
	     TEXT    "REMOTE=4000" /POST CLOCK MESSAGE IMMEDIATELY.
				     /   AFTER SPECIFIED INTERVAL REPOST
	     TEXT    "CANCEL=7000>" /DELETE ALL REQUESTS FROM SPECIFIED
				     /   TASK FROM QUEUE

	     TEXT    "IFNDEF OS8     <"
	     TEXT    "SLASHK=NFLDS-1>"
				     /SLASHK CONTROLS GENERATION OF EXEC
				     /   LINKAGE, 20-26 EACH FIELD

	     TEXT    "IFDEF OS8      <"
	     TEXT    "IFNDEF OSBASE  <OSBASE=NFLDS-OSFLDS>"
	     TEXT    "IFZERO NFLDS-OSBASE-OSFLDS <SLASHK=NFLDS-OSFLDS>>"

	     TEXT    "IFNDEF BKTCDV  <BKTCDV=0>"

	     TEXT    "IFNDEF SUNIT   <SUNIT= 0>"
			     		     /DEFAULT SWAP UNIT IS 0

	     TEXT    "HGHFLD=NFLDS-1" 	     /FOR HISTORICAL REASONS
					     /   CALCULATES CDF TO
					     / HIGHEST LEGAL FIELD
	     TEXT    "HGHFLD=<<HGHFLD&710>+<HGHFLD&10%2>+<HGHFLD&204>>"

	     TEXT    "IFNDEF PDP8E   <PDP8E=0>"	    /FORCE UNDEFINED TO
	     TEXT    "IFNDEF PDP8A   <PDP8A=0>"	    / EQUAL ZERO
	     TEXT    "IFNDEF PDP12   <PDP12=0>"
	     TEXT    "IFNDEF VT78    <VT78=0>"

	     TEXT    "OMNI=PDP8E+PDP8A+VT78"	    /OMNI BUS FOR TTY
						    /   SETUP
						    /BSW



				      D-8

			    RTS/8 PARAMETER LISTING


	     TEXT    "IFNDEF EAESV   <EAESV=0>"	    /MORE UNDEFINED
	     TEXT    "IFNDEF EAE     <EAE=0>"	    /   EQUATES SET TO
	     TEXT    "IFNDEF MQSV    <MQSV=0>"	    /   ZERO
	     TEXT    "IFNDEF MQ      <MQ=0>"
	     TEXT    "IFNDEF PWRFAL  <PWRFAL=0>"
	     TEXT    "IFNDEF KL8A    <KL8A=0>"
	     TEXT    "IFNDEF KT8A    <KT8A=0>"


	     TEXT    "IFNZRO EAESV   <MQSV=1>"	    /IF EAE SAVED, MQ IS
						    /   ALSO SAVED
	     TEXT    "IFNZRO EAE     <MQ=1>" 	    /IF THERE IS EAE,
						    /   SYSTEM
						    /   ALSO HAS MQ
	     TEXT    "IFZERO EAE     <EAESV=0>"     /CAN'T SAVE IF THERE
	     TEXT    "IFZERO MQ	     <MQSV=0>"      /   ISN'T ONE


	     TEXT    "IFDEF CLOCK    <"
	     TEXT    "IFNDEF CLKQLN  <CLKQLN=20"    /DEFAULT
	     TEXT    "IFNDEF SHERTZ  <SHERTZ=12>"   /CLOCK
	     TEXT    "IFNDEF CLKLRM  <CLKLRM=0>"    /SETTINGS
	     TEXT    "IFNDEF CLKTYP  <"
	     TEXT    "CLKTYP=3"
	     TEXT    "IFNZRO PDP8A   <CLKTYP=2>"    /DEFAULT CLOCK FOR
	     TEXT    "IFNZRO PDP12   <CLKTYP=1>"    /   EACH KIND OF
	     TEXT    "IFNZRO PDP8E   <CLKTYP=0>"    /   MACHINE
	     TEXT    ">"
	     TEXT    "IFNZRO CLKTYP&1 <HERTZ=1750>" /DEFAULT TICK RATE
	     TEXT    "IFZERO CLKTYP  <HERTZ=170>"   /   FOR EACH KIND
	     TEXT    "IFZERO CLKTYP-2 <HERTZ=144>"  /      OF CLOCK
	     TEXT    "IFNZRO HERTZ%SHERTZ SHERTZ-HERTZ <ERROR>"
						    /IS HERTZ A MULTIPLE
						    /   OF SHERTZ?
	     TEXT    "IFZERO SHERTZ-301&4000 <ERROR>"
	     TEXT    ">"

	     TEXT    "IFNDEF RTFLD   <RTFLD=0>"	    /EXECUTIVE DEFAULT

	     TEXT    "IFNZRO KT8A    <" 	    /   IS FIELD ZERO
	     TEXT    "KTFLDS=40	     " 		    /KT, IF ON, FOR 128K
	     TEXT    "RACA=6175	     " 		    /KT8A
	     TEXT    "RACB=6176	     " 		    /BIT
	     TEXT    "RACC=6177	     "  	    /INSTRUCTIONS
	     TEXT    ">"


     /SECTION 6 - RX FLOPPY SKELETON CONTROL FILES

     /RX CONTROL FILE

     M1770,  TEXT    "TASK=RX8A"     /SPECIFY RX8A, FIRST FLOPPY
     				     /   CONTROL FILE
     A1770,  TEXT    "RXDVCD="	     /DEVICE CODE

     				      D-9

			    RTS/8 PARAMETER LISTING


     	     .SBTTL PASS2 MESSAGES

     /THESE MESSAGES INDICATE THE STATUS OF PASS3 TO THE USER.
     /ALSO INCLUDE RECORDS FOR CONTROL FILES ARE ENTERED HERE.

     M5700,  TEXT    "R  PASS2 COMPLETED.  RETURNING TO MONITOR"

     M5701,  TEXT    "R  PASS2 COMPLETED.  CHAINING TO BATCH AS REQUESTED."

     M5702,  TEXT    ".INCLUDE XXXXXX:TTY.MA"

     M5703,  TEXT    ".INCLUDE XXXXXX:RX.MA"

     M5777,  TEXT    "DONE MARKER"

	     .SBTTL PASS2 MACREL BATCH RECORDS

     /THIS SECTION OF THE SCRIPT CONTAINS THOSE RECORDS
     /REQUIRED TO CREATE THE MACREL BATCH FILE USED TO
     /ASSEMBLE USER SPECIFIED SYSTEM AND USER TASKS.

     / 	     For this listing, the following section has been
     /       split into two lines. It does not appear this
     /       way in the parameter file

     M7004, TEXT ".MAC XXXXXX:RTS8  ,XXXXXX:RTS8  <
			     XXXXXX:XXXXXX,XXXXXX:RTS8  /B/C"

     M7001, TEXT ".MAC XXXXXX: TTY  ,XXXXXX:TTY   <
			     XXXXXX:XXXXXX,XXXXXX:TTY   /B/C"

     M7002, TEXT ".MAC XXXXXX:MCR   ,XXXXXX:MCR   <
			     XXXXXX:XXXXXX,XXXXXX:MCR   /B/C"

     M7003, TEXT ".MAC XXXXXX:TEST  ,XXXXXX:TEST  <
			     XXXXXX:XXXXXX,XXXXXX:TEST /B/C"

     M7006, TEXT ".MAC XXXXXX:EXIT  ,XXXXXX: EXIT <
			     XXXXXX:XXXXXX,XXXXXX:EXIT  /B/C"

     M7005, TEXT ".MAC XXXXXX:CLOCK ,XXXXXX: CLOCK <
			     XXXXXX:XXXXXX,XXXXXX:CLOCK /B/C"


     /RECORD   NUMBERS M7001 THROUGH M7050 ARE RESERVED FOR THE DEFAULT
     /TASK SECTION, DELIMITED BY RECORD 7776.  DO NOT INSERT OTHER THAN
     /DEFAULT TASK EQUATES BEFORE RECORD 7776.

     M7776,  TEXT    "DONE DEFAULT TASK MARKER"






     				     D-10

			    RTS/8 PARAMETER LISTING


     /FOLLOWING MESSAGES ARE USED BY MBLD, A SERVICE ROUTINE UNDER
     /MAIN3, TO BUILD THE MACREL BATCH FILE.  USE CAUTION TO AVOID
     /DIFFICULTY IN THAT THESE RECORDS ARE PARSED ON A DISPLACEMENT
     /BASIS TO INSERT THE VARIABLE DATA.

     M7110,  TEXT    "$JOB-MACREL TASK ASSEMBLY"

     M7111,  TEXT    "$END"

     M7112,  TEXT    "$MSG MOUNT TASK SOURCES ON XXXXXX:
				     AND STRIKE ANY KEY TO CONTINUE:'

     M7114,  TEXT    ".MAC XXXXXX:XXXXXX,XXXXXX:XXXXXX<
				     XXXXXX:XXXXXX,XXXXXX:XXXXXX/B/C"

     M7116,  TEXT    ".SU XXXXXX:XXXXXX.BI/E/T"

     M7117,  TEXT    ".SU XXXXXX:XXXXXX.BI/T"

     M7777,  TEXT    "DONE MARKER"

     .SBTTL PASS2 LINKER BATCH MESSAGES


     /THESE SCRIPT MESSAGES ARE USED TO BUILD THE LINKER BATCH FILE.
     /THEY ARE OPERATED UPON BY PASS2 ROUTINE LBLD.MA. CAUTION SHOULD
     /BE EXERCISED IN MODIFYING THEM, SINCE THEY ARE DISPLACEMENT
     /SENSITIVE.
     /
     /
     /DEFAULT SECTION:

     M6006,  TEXT    "*XXXXXX:RTS8"

     M6001,  TEXT    "*XXXXXX:TTY"

     M6002,  TEXT    "*XXXXXX:MCR"

     M6003,  TEXT    "*XXXXXX:TEST"

     M6004,  TEXT    "*XXXXXX:EXIT"

     M6005,  TEXT    "*XXXXXX:CLOCK"

     M6776,  TEXT    "DONEMARKER"

     /END OF DEFAULT TASKS

     M6100,  TEXT    ".R LINK"

     M6101,  TEXT    "*XXXXXX:XXXXXX,XXXXXX:XXXXXX</K=01/M/X"




     				     D-11

			    RTS/8 PARAMETER LISTING


     /MORE OPTIONS MAY BE ADDED TO END OF M6101 WITHOUT DISRUPTING
     /PROGRAM OPERATION.

     M6102,  TEXT    "*XXXXXX:XXXXXX"

     M6103,  TEXT    "*XXXXXX:XXXXXX/C"

     M6104,  TEXT    "*/O"

     M6105,  TEXT    "*$"

     /DELIMITS LINKER COMMAND STRING

     M6107,  TEXT    ".RU XXXXXX:SXXXXX"

     /CHAIN TO RTS8 AFTER BUILD IF USER SELECTS

     M6110,  TEXT    "$END"

     M6111,  TEXT    "$JOB RTS8 MODULE LINKAGE"

     M6777,  TEXT    "DONE MARKER"

     .SBTTL LIMIT CHECKING RECORDS

     /FOR EACH OCTAL/DECIMAL QUESTION IN THE INTERACTIVE SCRIPT RECORDS,
     /AN ENTRY IS MADE IN THIS LIST OF THE LOWER,UPPER VALUES WHICH THE
     /CORRESPONDING ANSWER MAY ASSUME. EACH PASS THROUGH OCTDEC THE
     /LIMIT CHECKING ROUTINE IS CALLED TO VERIFY THE ENTRY.

     M3057,  TEXT    "L3057 002,032"

     M3352,  TEXT    "L3352 000,031"

     M3065,  TEXT    "L3065 001,003"

     M3167,  TEXT    "L3167 002,008"

     M3171,  TEXT    "L3171 001,113"

     M3173,  TEXT    "L3173 001,113"

     M3201,  TEXT    "L3201 002,030"

     M3203,  TEXT    "L3203 000,010"

     M3346,  TEXT    "L3346 001,192"

     M3223,  TEXT    "L3223 016,256"

     M3226,  TEXT    "L3226 001,050"

     M3230,  TEXT    "L3230 001,020"


     				     D-12

			    RTS/8 PARAMETER LISTING


     M3232,  TEXT    "L3232 001,020"

     M3233,  TEXT    "L3233 001,020"

     M3234,  TEXT    "L3234 000,3777"

     M3236,  TEXT    "L3236 000,3777"

     M3135,  TEXT    "L3135 001,077"

     M3140,  TEXT    "L3140 001,077"

     M3142,  TEXT    "L3142 001,077"

     M3144,  TEXT    "L3144 001,077"

     M3237,  TEXT    "L3237 000,3777"

     M3243,  TEXT    "L3243 001,007"

     M3251,  TEXT    "L3251 001,005"

     M3253,  TEXT    "L3253 001,113"

     M3255,  TEXT    "L3255 001,113"

     M3262,  TEXT    "L3262 000,010"

     M3264,  TEXT    "L3264 000,160"

     M3266,  TEXT    "L3266 000,3001"

     M3275,  TEXT    "L3275 001,007"






















     				     D-13







				  APPENDIX E

				ERROR MESSAGES


     This appendix  lists  all  of  the  RTS/8  System  Generation  Errors.
     Immediately  following  each  error  message  are two paragraphs.  The
     first paragraph  further  explains  the  error  message.   The  second
     describes the action the SYSGEN takes when it encounters the error and
     what you should do to prevent the reoccurrence of the error.


     ERROR 005 BAD RECORD DIRECTORY READ FROM MASS STORAGE (FATAL)

	  The SYSGEN was unable to access a record in SCRIPT.SV.

	  You may have a  bad  image  of  SCRIPT.SV  or  a  faulty  device.
	  Execution  control returns to the OS/8 Monitor.  You should check
	  your device and/or relink SCRIPT.SV.


     ERROR 012 BAD SCRIPT RECORD READ (FATAL)

	  The SYSGEN was unable to locate a record.

	  This usually  indicates  a  problem  with  the  device  on  which
	  SCRIPT.SV resides but it may indicate a bad SCRIPT.SV image.  You
	  should check the device upon which SCRIPT resides  and/or  relink
	  SCRIPT.SV.  Execution control returns to the OS/8 Monitor.


     ERROR 013 FEATURE INCORRECTLY USED (NUMBER NOT FOUND)

	  You attempted to branch forward.   The  SYSGEN  can  only  branch
	  backwards.   This  error  may also indicate that you have typed a
	  non-numeric character after the # symbol.

	  The SYSGEN reprints the question that it printed before you  made
	  the bad branch.  You can now branch to a question already printed
	  or answer the question.


     ERROR 016 SUBSEQUENT RECORD DIRECTORY READS UNSUCCESSFUL (FATAL)

	  The SYSGEN was unable to locate a record in SCRIPT.SV.

	  This error indicates that you are having device problems  or  you
	  have  a  bad SCRIPT.SV image.  You should examine the device upon
	  which SCRIPT.SV resides and/or relink SCRIPT.SV.  Control returns
	  to the OS/8 Monitor.



				      E-1

				ERROR MESSAGES


     ERROR 017 RESPONSE IS TOO LARGE

	  You typed more than  six  characters  (five  characters  for  TTY
	  questions) in an answer.

	  After the SYSGEN reprints the question, type the correct  answer.
	  This  error  normally  occurs  when  typing an answer to a device
	  specification question.  The longest character string  that  OS/8
	  recognizes is six characters.


     ERROR 021 NOT A YES OR NO ANSWER OR BAD DEFAULT FOR Y/N RECORD

	  A Yes/No question requires an answer that begins with the  letter
	  'Y'  or  letter  'N'.   This  error can indicate that the default
	  listed within parentheses is not a Y or N.  (This may occur if  a
	  user   made   a   typographical  error  when  making  changes  in
	  SCRIPT.MA.)

	  After the SYSGEN reprints the question, type a Y or  N.   If  the
	  problem  was  that  the default was not a Y or N, you must type a
	  ^C,  use  a  text  editor  to  change  the  default,   reassemble
	  SCRIPT.MA, and then redo the system generation.


     ERROR 022 SCRIPT RECORD WITH NO DEFAULT (FATAL)

	  The question does not have a default answer  within  parentheses.
	  This  occurs  only  when  a  user changes the text and forgets to
	  include a default in the question.

	  Control returns to the OS/8 Monitor.  You must use a text  editor
	  to enter a default answer and then reassemble the question.


     ERROR 023 NO DEFAULT ALLOWED FOR THIS QUESTION

	  Some SYSGEN questions have a question mark as their default.  For
	  these  answers  you  must  explicitly enter an answer rather than
	  type a carriage return.

	  After the SYSGEN reprints the question, type the answer.


     ERROR 030 RESPONSE NOT OCTAL/DECIMAL AS EXPECTED

	  Your answer contained characters other than the numbers 0 through
	  9 (or 0 through 7 for octal answers).

	  After the SYSGEN reprints the question, retype the answer.





				      E-2

				ERROR MESSAGES


     ERROR 050 ILLEGAL BRANCH RECORD (FATAL)

	  A branch record could not find its target.  This  message  occurs
	  when  an  error  was  made in modifying the script.  The cause is
	  that a record was deleted from SCRIPT and a branch left in or, in
	  the  case  of  adding  records, a branch was added and the branch
	  target does not exist.

	  Control returns to the OS/8 Monitor.  You must  now  examine  the
	  portion  of  the record directory following the last question you
	  answered to locate the branch record  that  caused  the  problem.
	  After  you  find the branch record, either change it or eliminate
	  it.  After the correction is made, reassemble SCRIPT.MA.


     ERROR 055 ASCII ANSWER CONTAINS NON ALPHANUMERIC DATA

	  Your answer  contained  characters  other  than  the  upper  case
	  letters A through Z and the numbers 0 through 9.

	  After the SYSGEN reprints the question, retype the answer.


     ERROR 060 T SUBROUTINE REQUESTED DOES NOT EXIST (FATAL)

	  The SYSGEN could not find a T  subroutine.   (These  are  special
	  processing  subroutines  included in the SYSGEN.  A user may also
	  write his own.)

	  If the T subroutine exists, no modification was made to the RTS/8
	  system  program  TYPET.MA.  If the subroutine does not exist, the
	  SYSGEN was linked improperly.


     ERROR 070 MORE THAN FIVE TTY TASKS SPECIFIED

	  Your answer was greater than five.

	  After the SYSGEN reprints the question, type a number from  1  to
	  5.


     ERROR 100 DEVICE CODE MUST BE SPECIFIED FOR EACH TTY TASK

	  You typed a carriage return or typed fewer device codes than  the
	  number of terminals in the target system.

	  After the SYSGEN reprints the question, type a  device  code  for
	  each device.






				      E-3

				ERROR MESSAGES


     ERROR 110 INCORRECT NUMBER OF ENTRIES FOR NUMBER OF TTY TASKS
	       SPECIFIED

	  You typed a carriage return  or  typed  fewer  entries  than  the
	  number of terminals in the system.

	  After the SYSGEN reprints the question, type an  entry  for  each
	  device.


     ERROR 120 SUM OF SYSTEM PLUS USER TASKS ALREADY 127 DECIMAL

	  The SYSGEN prints this error message when you  attempt  to  enter
	  the 128th task into the system.

	  The SYSGEN prints the next question (which asks if  you  wish  to
	  change  the priorities of any tasks).  If you wish to include the
	  128th task, you must branch back to the question  asking  if  you
	  want  to include any user tasks.  You then reenter all the tasks,
	  eliminating one of the tasks you previously entered.  If you wish
	  to  retain  all  the  user tasks, you must type a ^C and redo the
	  SYSGEN eliminating  one  of  the  DIGITAL  tasks  you  previously
	  specified.    Note  that  127 tasks is the maximum number you can
	  have in an RTS/8 system.


     ERROR 132 CANNOT OPEN, CLOSE, OR WRITE TO OUTPUT FILE (FATAL)

	  The device is write locked  or  some  other  similar  problem  is
	  preventing  the  SYSGEN  from writing information to the file you
	  specified in other questions.

	  Control returns to the OS/8 Monitor.  You must redo  the  SYSGEN,
	  making sure that the output device is working properly and is not
	  write locked.  (This message does not indicate that the device is
	  not configured in OS/8.)


     ERROR 134 INSUFFICIENT ROOM FOR OUTPUT FILE (FATAL)

	  The output device does not have enough free blocks for the SYSGEN
	  output files.

	  Control returns to the OS/8 Monitor.  You must delete blocks from
	  the output device, place another device in that drive, or specify
	  another output device in response to SYSGEN questions.









				      E-4

				ERROR MESSAGES


     ERROR 135 INCORRECT DEVICE SPEC.  FOR BUILD OUTPUT FILES (FATAL)

	  The device specification you gave for the SYSGEN  output  is  not
	  active in the OS/8 operating system.

	  Execution control returns to the  OS/8  Monitor.   Use  the  OS/8
	  RESORC  command  to  determine if the device is active.  If it is
	  active, you entered the device name incorrectly.  If it  is  not,
	  use  the BUILD program to install the device.  You must then redo
	  the SYSGEN.


     ERROR 137 DEVICE SPEC FOR OUTPUT FILES NOT MASS STORAGE (FATAL)

	  The output device for  SYSGEN  files  is  not  a  file-structured
	  device (such as a disk or a DECtape).  You accidently specified a
	  device such as a line printer or paper tape punch.

	  Execution control returns to the OS/8 Monitor.  You must redo the
	  SYSGEN,  this  time  making  sure  you  specify a file-structured
	  device.


     ERROR 141 BATCH.SV NOT FOUND (FATAL)

	  The BATCH.SV OS/8 utility program is not on your  system  device.
	  The SYSGEN program cannot automatically create an RTS/8 system if
	  you do not have the BATCH program.

	  After copying BATCH to SYS, you must resubmit  the  MACREL  BATCH
	  file.


     ERROR 144 I/O ERROR ON TASK LISTING DEVICE

	  The I/O device is inoperative.  (If your system does not  have  a
	  line printer, the SYSGEN automatically prints information on your
	  terminal display.)

	  If the task listing device (a line printer)  is  active  in  your
	  OS/8 system, check to see if it is turned on.  If it is turned on
	  and its name is LPT (or another name attributed to it by an  OS/8
	  ASSIGN  command),  you are having problems with your line printer
	  handler.  The quickest solution is assign LPT to TTY so that  the
	  listing appears on your terminal.  However, you should attempt to
	  rebuild and/or reboot your OS/8 system.


     ERROR 145 I/O ERROR ON TASK LISTING DEVICE

	  The I/O device is inactive.

	  See the comment to ERROR 144.


				      E-5

				ERROR MESSAGES


     ERROR 150 INCORRECT FORMAT FOR TASK PRIORITY CHANGE

	  Your answer to a task priority change prompt was incorrect.

	  After the SYSGEN reprints the prompt, retype your response.   The
	  format  for  specifying  a  change  is  to  type  two  task names
	  separated by commas.  The first task is  the  task  you  wish  to
	  move;   the  second  is  the  task  which   the first task should
	  immediatly precede.


     ERROR 160 PRIORITY TASK AS SPECIFIED NOT FOUND

	  The task you specified has not yet been entered in the system or,
	  if it was entered, you made a typographical error.

	  If your response contained a typographical error, you can  retype
	  the  task name.  If the task name you typed was correct, obtain a
	  listing of tasks in the system by typing a question  mark  and  a
	  carriage return.  This listing will tell you the tasks entered in
	  the system.  If you made a typographical error in entering a task
	  name, type a ^C and redo the SYSGEN.


     ERROR 200 ENCOUNTERED NON-EXISTENT RECORD TYPE (FATAL)

	  When the SYSGEN encountered a record, its first  letter  was  not
	  one  of those it recognizes.  The types the SYSGEN recognizes are
	  A, D, I, L, N, R, O, T, and Y.

	  Control returns to  the  OS/8  Monitor.   You  should  examine  a
	  listing  of  SCRIPT to determine where the error occurred.  After
	  you locate the error, make the correction with a text editor  and
	  reassemble script.  You must also redo the entire SYSGEN.


     ERROR 201 # FEATURE USAGE NOT OK AFTER PRIORITY CHANGES

	  After the question that asks if you wish to  change  any  of  the
	  task's  priorities,  the SYSGEN disables the function that allows
	  it to branch back to a previous question.

	  The SYSGEN reprints the question to which you gave a #  response.
	  If  there was an error to a previous question, you must type a ^C
	  and redo the SYSGEN.  Otherwise, you may continue forward.










				      E-6

				ERROR MESSAGES


     ERROR 202 NUMERICAL ANSWER NOT WITHIN SPECIFIED LIMITS

	  The answer you specified was either greater than or less than the
	  answer that is allowed for a question.

	  After the SYSGEN retypes the question,  type  a  number  that  is
	  within  the  question's  limits.  You may determine the limits by
	  examining the limit records in a listing of SCRIPT.MA or  looking
	  in the parameter file listing in Appendix D.


     ERROR 203 NON-RESIDENT TASKS MAY NOT HAVE PRIORITY HIGHER THAN THE
	       SWAP TASK

	  When making changes in task priorities, you attempted to  give  a
	  higher  priority to a nonresident task than the priority that the
	  SWAP task has.

	  After the SYSGEN reprompts, change the priority of  the  task  to
	  one  that  is  lower  than the swap task.  If you do not know the
	  task priorities, type a question mark and a carriage return.  The
	  SYSGEN then prints a task priority listing.


     ERROR 204 PARTITION ENTRY LIMITED FROM 0 (MAIN) TO 7

	  You attempted to place a nonresident task in  a  partition  other
	  than  those  in  the  range  0  through 7.  This message also may
	  indicate a typographical error in entering the partition number.

	  After the SYSGEN retypes the prompt, retype  the  entry  using  a
	  partition number in the range 0 through 7.


     ERROR 205 INCORRECT FORMAT FOR PARTITION CHANGE

	  The SYSGEN requires that you type the task name, a comma, and the
	  partition  into  which  you  wish  to place the task.  This error
	  indicates that the text you typed was not in this format.

	  After the SYSGEN reprompts,  retype  the  entry  in  the  correct
	  format.


     ERROR 206 NO MORE THAN 16 ENTRIES PER PARTITION

	  You attempted to place  a  seventeenth  task  into  partitions  1
	  through  7.   (You may place as many as you like into "partition"
	  0.)

	  If you receive this message  while  entering  tasks,  you  should
	  place the task that caused this message into another partition.



				      E-7

				ERROR MESSAGES


     ERROR 207 TASK HAS DUPLICATE NAME

	  The task whose name you just entered has already been entered.

	  After the SYSGEN reprompts, continue entering tasks.


















































				      E-8







				     INDEX


     Alphanumeric questions, 2-4	  Decimal questions, 2-3             
	 see also SCRIPT.MA record	      see also SCRIPT.MA record      
	   type indicator		        type indicator               
     Analog to digital converter,	  DECtape driver, 2-25               
	 see UDC			  Default answers, 2-4               
     Answers, maximum length, 2-3	    changing, 4-6                    
     Assembly listings, 2-12		  Default systems, 2-13              
       device, 2-12			    adding tasks to, 4-31, 4-32      
					      example, 4-32                  
					    creating, 4-11                   
					      example, 4-32                  
     Background operation,		  Default systems (Cont.),           
	 see OS/8 support task		    example, 3-1                     
     BATCH, 2-9, 2-11, 2-12	            LINK batch file, 4-11, 4-32      
     Branching, 2-4			      changing, 4-32                 
       renumbering, 2-5			      listing, D-11                  
					    MACREL batch file, 4-11, 4-32    
					      changing, 4-32                 
					      listing, D-10                  
     Cassette driver, 2-33		    parameter record listing, D-6    
     Cassette file support task, 2-34     Deleting questions, example,       
     Chaining,                                4-13                           
       to BATCH, 2-10, 2-48               DF32 disk driver, 2-24             
       to RTS/8, 2-9, 2-48		  Diskette,                          
     Changing limits,			      see Floppy disk controller     
	 see Limit records		  DOC. NO,                           
     Clock handler, 2-19		      see Document numbers           
       HERTZ (hardware tick rate),	  Document numbers, 2-4              
	 2-21				    listing, 2-51                    
       interrupt linkage, 2-21		  Drivers,                           
       nonstandard clocks, 2-20		      see under Device name          
       queue entry slots, 2-20		                                     
       SHERTZ, 2-21			                                     
       standard clocks, 2-20		                                     
       tick rate, 2-21			  EAE, 2-14                          
     Conditionals, 4-6			    saving registers of, 2-14        
       format, 4-7			  Emergency breakthrough task,       
       record numbers (preferred),	      2-28                           
	 4-7				    terminal name, 2-29              
       type, 4-7			  EMT,                               
     Controllers,			      see Emergency breakthrough     
	 see under Device name                  task                         
     Control files, 2-10, 2-27, 2-30      Equates, 2-47, 4-11                
					  Error message records, 4-12
                                          Error messages, 2-5        





				    INDEX-1

				 INDEX (Cont.)


     Errors, 2-5			  LINK load map, 2-12, 4-18        
       fatal, 2-5                           device, 2-13                   
       SYSGEN responses, 2-6                example, 4-22                  
     Example SYSGENs, 3-1, 3-4              listing, 2-12                  
     Execution,                           Load map,                        
         see SYSGEN                           see LINK load map            
     Exit task, 2-36                                                       
                                                                           
                                                                           
                                          MACREL batch file, 2-8, 2-47,    
     File specifications, 2-6                 4-12, 4-32                   
     Floppy disk controller, 2-26           default system, 4-11           
       control files, 2-27, 3-24              listing, 3-25, D-10          
       device numbers, 2-27               MACREL source files, 2-10, A-1   
       number in system, 2-27               assembly listings, 2-12        
     Foreground operation, 1-1, 2-37          device, 2-12                 
                                            multiple media, 2-10           
                                            .RB output files, 2-10, 2-11   
                                            source devices, 2-13           
     Handlers,                              source media, 2-10             
         see under Device name            MCR, 2-30                        
     HERTZ,                                 system status report, 2-30     
         see Clock handler                  terminal, 2-35                 
                                            time-of-day command, 2-30      
                                          Memory fields,                   
                                            KT8-A, 2-18                    
     Immediate response clock		    number in system, 2-16         
	 subroutine,			    OS/8, 2-37                     
	 see Clock handler		      placement in, 2-38           
     Interrupt clock linkage,               RTS/8, 2-16                    
	 see Clock handler                Minimum configuration, 1-1       
					  Monitor Console Routine,         
                                              see MCR                      
					  MQ, 2-15                         
     KL8-A, 2-17			    saving registers, 2-15         
       device codes, 2-18		
       number in system, 2-17		
     KT8-A, 2-18, 2-38			
					Nonresident tasks, 2-32, 2-42,
                                            2-44                      
					Null task, 2-40               
     Limit records, 4-12		                              
       changing, 4-13			                              
       format, 4-13			                              
       listing, D-12		        Octal questions, 2-3          
     LINC-8, 2-8			    see also SCRIPT.MA record 
     LINCtape driver, 2-26		      type indicators         
     Line printer driver, 2-28		Operating information, 2-2    
     LINK batch file, 2-8, 2-47,	OS/8 file support task, 2-30  
	 4-12, 4-32			OS/8 support task, 2-36        
       default system, 4-11		  background operation, 2-37   
	 listing, 3-25, D-11              keyboard device code, 2-37   
     LINK, 2-11, 2-47                     line feed, nulls after, 2-39 


				    INDEX-2

				 INDEX (Cont.)


     OS/8 support task, (Cont.)           .RB files, 2-10                     
       memory fields, 2-37                Record directory,                  
         placement in, 2-38                   see SCRIPT.MA                  
       RTS/8 handler task, 2-38           Remarks, 2-4, 4-4                  
       teleprinter device code, 2-38          see also SCRIPT.MA record      
       terminal driver, 2-40                    type indicator               
     Output files,                          adding, 4-5                      
         see MACREL batch file;               example, 4-5, 4-17             
         LINK batch file; Parameter       RF08 disk driver, 2-24             
         file; Control files              RK8 disk driver, 2-25              
                                          RK8E disk driver, 2-24             
                                          RLO1 disk driver, 2-25             
                                          RTS/8 field, 2-16                  
     Parameter file, 2-8, 2-47,           RTS/8 .SV image, 2-11, 2-47        
         3-20, 4-10                       RTS/8 system equates, 4-11         
         see also Parameter records         listing, D-2                     
     Parameter records, 4-10              RTS/8 tasks, number permitted,     
       default system listing, D-6            2-41                           
       format, 4-10                                                          
       listing, D-1                                                          
       records, 4-10                                                         
       system task listing, D-2           Save image file storage,           
     Partitions,                              see RTS/8 .SV image            
         see Task partitions              Script records,                    
     PDP 8, 2-7                               see SCRIPT.MA                  
     PDP 8/A, 2-7                         SCRIPT.MA, 4-1                     
       null task, 2-40                      accessing records, 4-2           
     PDP 8/E, 2-7                           cross-reference listing, 4-17    
     PDP 8/I, 2-7                           delimiting tags, 4-3             
     PDP 8/L, 2-7                           parameter records,               
     PDP-12, 2-7                              see Parameter records          
     Power fail handler, 2-17               questions,                       
     Power fail hardware, 2-16                adding, 4-5                    
     Priority,                                deleting, 4-9                  
         see Task priority                      restrictions, 4-9            
                                              example, 4-17                  
                                            record directory, 4-2            
                                              format, 4-2                    
     Questions,                             record length, 4-4, 4-5          
       adding, 4-5                          record numbers, 4-2              
         alternate procedure, 4-32          record tags, 4-2                 
         example, 4-17                      record type indicators, 4-3,     
         guidelines for, 4-17                 4-4                            
       automatic numbering, 2-5             remark records, 4-4              
       branching, 2-5                         adding, 4-5                    
       default answers, 2-4                 script records, 4-3              
       deleting, 4-9                          format, 4-3                    
         example, 4-14                        type indicator, 4-3            
                                          SCRIPT.SV, 1-1                     
                                            devices, 2-2                     
                                          SHERTZ,                            
                                              see Clock handler              



				    INDEX-3

				 INDEX (Cont.)


     Source files,			  Terminal driver, (Cont.)
	 see MACREL source files	    multiple terminal system, 4-34    
     .SV file,				      example, 4-36                   
	 see RTS/8 .SV image                number in system, 2-30            
     Swap task, 2-32                        OS/8, 2-39                        
       swapping device, 2-33                  keyboard device code, 2-37      
     SYSGEN,				      line feed, nulls after, 2-39    
       defined, 1-1			      teleprinter device code, 2-38   
       error responses, 2-5		    RUBOUT, 2-31                      
     SYSGEN (Cont.),                        tabs (hardware), 2-32             
       examples, 3-1, 3-4                   teleprinter device code, 2-31     
       minimum configuration for, 1-1       timeout, 2-32                     
       operating information, 2-2         Test task, 2-36                     
       output files, 2-8                                                      
       overview, 1-1, 1-2, 2-1                                                
       running, 1-1, 2-2                                                      
     SYSGEN.SV, 1-1                       UDC/ICS, 2-21                       
     System equates, 4-11                   analog input converter, 2-23      
       listing, D-6                           address, 2-24                   
     System generation,                   UDC/ICS (Cont.),             
       see SYSGEN                           contact module, 2-23       
     System tasks, 4-11                       address, 2-23            
       initial priority, 4-11               counter module, 2-22       
       parameter record listing, D-2          address, 2-23            
       source files, A-1                    interrupts stored, 2-22    
                                          User responses,              
                                            information required, 1-2  
                                            to questions, 1-2          
     Target computer,                     User tasks, 2-40, 4-11       
         see Target machine                   see also Task partitions;
     Target machine, 2-7                        Task priorities        
     Task partitions, 2-41, 2-44            names, 2-41                
       changing, 2-44                       number permitted, 2-41     
       listing, 2-44                     
     Task priority, 2-41                 
       changing, 2-41                     
       listing, 2-42                      VT78, 2-7
     Tasks, number permitted, 2-41       
     Terminal driver, 2-29               
       character deletion, 2-31           
       characters per line, 2-32          Yes/no questions, 2-3        
       control files, 2-30, 3-24              see also SCRIPT.MA record
       CTRL/Q, 2-31                             type indicators        
       CTRL/S, 2-31                      
       emergency breakthrough task,      
         see Emergency breakthrough      
         task                            
       keyboard device code, 2-30        
       line feed, nulls after, 2-31      
         OS/8, 2-39                      
       line length, 2-32                 
       MCR terminal, 2-35                



				    INDEX-4



							     RTS/8
							     User's Manual
							     AA-0724D-TA


			       READER'S COMMENTS


     NOTE:  This form is for document comments only. DIGITAL will
	    use comments submitted on this form at the company's
	    discretion. If you require a written reply and are
	    eligible to receive one under Software Performance
	    Report (SPR) service, submit your comments on an SPR
	    form.


     Did you find this manual understandable, usable, and well-organized?
     Please make suggestions for improvement.

     ----------------------------------------------------------------------

     ----------------------------------------------------------------------

     ----------------------------------------------------------------------

     Did you find errors in this manual? If so, specify the error and
     the page number.

     ----------------------------------------------------------------------

     ----------------------------------------------------------------------

     ----------------------------------------------------------------------

     Please indicate the type of reader that you most nearly represent.

	     o Assembly language programmer
	     o Higher-level language programmer
	     o Occasional programmer (experienced)
	     o User with little programming experience
	     o Student programmer
	     o Other (please specify)


     Name_______________________________________ Date______________________

     Organization__________________________________________________________

     Street _______________________________________________________________

     City_____________________________ State________ Zip Code _____________
						      or
						     Country



















     -------------------------------Fold Here------------------------------

















     -----------------Do Not Tear - Fold Here and Staple-------------------

							  +---------------+
							  |  FIRST CLASS  |
							  | PERMlT NO. 33 |
							  | MAYNARD. MASS.|
							  +---------------+
	BUSINESS REPLY MAIL					   ========
	NO POSTAGE STAMP NECESSARY IF MAILED IN THE UNITED STATES  ========
     ======================================================================
	Postage will be paid by:				   ========
								   ========
			  +-+-+-+-+-+-+-+			   ========
			  |d|i|g|i|t|a|l|			   ========
			  +-+-+-+-+-+-+-+			   ========
								   ========
		      Software Communications                      ========
		      146 Main Street  ML5-5/E39		   ========
		      Maynard, Massachusetts  01754		   ========